APPENDIX F

PESTICIDE MANAGEMENT OPERATIONS

1.  PURPOSE.  To outline procedures for handling pesticides and operating pest control equipment, and to establish safety precautions associated with pest control operations.

2.  GENERAL

a.  Pesticides generally used on ORARNG camps, armories, and facilities include insecticides, herbicides and rodenticides.

b.  Handling concentrated pesticides during shipment or storage, preparation of dilute formulations and application of dilute formulations is hazardous in that personal contamination

can result in skin damage, extreme illness, or death.

c.  Pesticides shall be procured under the supervision and approval of the Facility Manager for Camp Rilea or Camp Withycombe, or AGI-O for other facilities.

d.  Areas used for pesticide storage and mixing shall be marked to designate pesticide operations.

3.  PROCEDURES

a.  Training and Certification

(1)  Restricted use pesticides must be applied by a certified Pest Controller.  When pest control requirements necessitate the assistance of uncertified personnel, training of these personnel in the handling, mixing and application of pesticides shall be done by a certified Pest Controller.  In addition, applications by non-certified personnel must be supervised by a certified Pest Controller except products listed as self-help materials, which may be applied by anyone if approval to use the materials has been obtained.

(2)  Training of ORARNG personnel in operating pest control equipment shall be conducted by certified pest control personnel and other competent personnel assigned to assist.

(3)  All ORARNG personnel who perform pest management activities at least 25 percent of their on-duty time and/or apply restricted-use, state licensed or controlled pesticides will be state-certified.  The Facility Manager, Pest Control POC, and others who evaluate the quality of work of pest control contracts (Quality Assurance Evaluator-QAE) must also be certified.  To minimize costs, the Pest Controller can also be the QAE.

(4)  Training and certification will be conducted by the State of Oregon at ORARNG expense.  Certified pest control personnel shall be recertified IAW state requirements.

(5)  Personnel will be certified, as appropriate, in the following categories:

- Ornamental and turf pest control (EPA category 3).

(b)  Right-of-way Pest Control (EPA category 6)

(c)  Industrial, institutional, structural and health-related pest control

(EPA category 7).

(d)  Public health pest control (EPA category 8).

b.  Pest Control Equipment

(1)  Only authorized, trained personnel shall operate pest control equipment.

(2)  Cleaning and storage of pest control equipment will be done by authorized, trained personnel only, IAW manufacturer's instruction manuals for the specific equipment item.

(3)  Maintenance and adjustment of pest control equipment shall be performed IAW manufacturer's instructions for the specific equipment item.

(4)  All equipment used in pest control activities shall be marked "Contaminated with Pesticides".

c.  Protective Clothing and Equipment

(1)  The following personal protective clothing and equipment will be provided when recommended by the MSDS:

(a)  Chemical resistant gloves, aprons and boots.

(b)  Full face shield.

(c)  Splash goggles.

(d)  Full-Face respirators approved for use with pesticides.

(e)  Coveralls.

(2)  Coveralls will be worn when handling or applying pesticides.  External personal clothing shall not be worn during pesticide operations.

(3)  Coveralls contaminated with pesticides through spillage or during normal use shall be returned to designated work areas for replacement and laundering.  Laundering shall be done at ORARNG expense; contaminated clothing shall not be taken home to be laundered.

(4)  Splash goggles, face shields and pesticide respirators shall be cleaned and sanitized as necessary.

(5)  All chemical resistant protective equipment, such as aprons, gloves and boots, shall be washed at the end of each day of use and properly stored in lockers or other areas free of

contamination.

(6)  Respirators shall be worn during pest control operations as required by the MSDS.

(7)  All locations using respirators must have an approved respirator protection program that addresses the use, maintenance, and storage of respirators.

(8)  AGP should be contacted for additional guidance/information on the maintenance and care of respirators for state employees.

d.  Pesticide Storage

(1)  All pesticides shall be stored in buildings, or rooms within buildings, designated for this purpose.  The pesticides shall be stored in their original containers.  The

buildings/rooms shall be kept locked when not in use.

(2)  All pesticides shall be segregated as to kind of pesticide during storage.  Labels on all containers shall be visible at all times.  Pesticides that are classed as moderately

or highly toxic must be stored in facilities that meet the criteria described in 40 CFR 165.10 (Reference 4f).

(3)  The local Fire Department shall be furnished with an inventory of the kinds and amounts of pesticides present at each storage or mixing location.  This inventory shall be updated at least annually, at the end of each calendar year by the Pest Control POC.

e.  Pesticide Transportation

(1)  Only authorized operators shall transport pesticides upon approval by a state certified individual or the Facility Manager or Facility Maintenance Supervisor.

(2)  When transporting pesticides, operators shall have protective clothing and equipment with them.

(3)  Pesticides will not be transported in the cabs or passenger compartments of vehicles.  Pesticides will not be left unattended or unsecured in the vehicle.

f.  Pesticide Mixing

(1)   Self-help pesticides may be handled and mixed by uncertified personnel; however, pesticide label directions will be followed.  All other pesticides will be handled and mixed by authorized, certified personnel only.

(2)  Concentrate dispensing and liquid pesticide mixing shall be done on a nonporous surface (cement, asphalt, etc.).

(3)  Any pesticide contamination on the skin shall immediately be washed off with soap and water.  Contamination of the eyes shall be flushed generously with water.  After washing, the individual will secure immediate medical attention.

(4)  Pesticide containers shall be returned to their storage locations upon completion of mixing.

(5)  All pesticides shall be applied in accordance with the label directions.

(6)  When mixing liquid pesticides, the spray tank shall be filled 1/3 to 1/2 full with the diluent, the pesticide shall be added, and the spray tank shall then be filled with diluent.  All pesticide mixtures shall be agitated.

g.  Pesticide Application

(1)  Uncertified personnel may apply non-restricted pesticides.

(2)  Only authorized, certified personnel will apply restricted use, state-licensed or controlled pesticides. Part-time personnel shall be trained by a State certified individual prior to any pesticide application.  Pesticide application shall be carried out in accordance with the label directions of the pesticide used, the manufacturer's operating instructions for the equipment used, and as directed by a state-certified individual.

(3)  Pesticide application operations shall be conducted as follows:

(a)  Dry, granular pesticide application shall be conducted when the wind speed is less than 10 miles per hour to prevent drift.  An approved respirator shall be worn whenever

required by the label or deemed necessary by a state certified individual or the Pest Control POC.  The operator shall wear a respirator when pesticide dust is a hazard.

(b)  Outdoor liquid pesticide application shall be conducted when wind speed is less than 10 mph to prevent drift.  Approved respirators shall be worn when required by pesticide labels or deemed necessary by state-certified personnel or the Pest Control POC.

h.  Pesticide Spill Cleanup Kit

(1)  A pesticide spill cleanup kit, appropriate to the type and amount of pesticide used or stored, should be located in each building where pesticides are stored.  Contents of this kit are listed in Appendix G of this plan (latest revision).  In addition, adsorptive material to contain minor amounts of spilled liquid pesticides will be kept in each pesticide storage room.

(2)  The pesticide spill cleanup kit shall be used in accordance with Appendix F (latest revision).  All items in the kit that have been used shall be replaced as soon as possible.

i.  Pesticide Container Disposal

(1)  Liquid pesticide containers shall be triple rinsed, with the rinsate placed in the spray tank and used as a diluent.  Empty containers shall be crushed and placed in solid waste dumpsters.  Pesticide containers shall not be used for any purpose except for holding pesticide shown on the label.

(2)  Dry, granular pesticide containers (bags and/or sacks) shall be emptied thoroughly and placed in the garbage dumpster.  Pesticide bags or sacks shall not be burned or stored near heat or open flame.

4.  REFERENCES

a.  AR 200-5, 29 Oct 99, Pest Management.

b.  TM 5-632, Dec 1973, Military Entomology Operational Handbook.

c.  Equipment Manufacturer's Handbooks and Manuals.

d.  Pesticide Labels and Manufacturer's Literature.

e.  Title 40, Code of Federal Regulations, 1988 rev, Section 165.10, Recommended Procedures and Criteria for Storage of  Pesticides and Pesticide Containers.

(This page intentionally left blank.)