# Chapter 11

# SPILL CONTINGENCY PLANNING AND EMERGENCY RESPONSE

11-1.  REFERENCES

a.  AR 200-1, Chapter 3

b.  40 CFR parts 110-112, 300, 302, and 355

c.  Oregon Revised Statutes (ORS) 466.605- 466.680 and 468B.300-335/340-425

d.  Oregon Administrative Rules (OAR) 340-122

e.  ORARNGR 210-6, Installation Spill Contingency Planning, dated 1 Jul 98

11-2.  SCOPE

- Facilities that store, use or have the potential to discharge POL or other hazardous materials to the environment must have plans in place to respond to spills or other releases of those materials.  Different requirements apply to facilities with larger amounts of storage.  However, all ORARNG units and facilities have the potential for spills, so all facilities and units must comply with some requirements of this chapter.

11-3.  BACKGROUND INFORMATION

- Federal law requires each facility storing regulated materials above-ground in tanks greater than 660 gallons in size, or storing an accumulated amount greater than 1,320 gallons (regardless of the size of the containers), to implement a Spill Prevention, Control and Countermeasure Plan (SPCCP).  An SPCCP must be prepared IAW the provisions of 40 CFR 112, be reviewed and signed by a registered Professional Engineer, and be available to address preventive measures used to reduce the potential for spills at the site in question.  Current NGB guidance requires review of an SPCCP every three years by facilities personnel and AGI-ENV.  If new construction or modifications are made to the facility that impact spill potential on-site, the SPCCP must be reviewed and signed by a registered Professional Engineer no later than six months of completion of the construction or modification.

- Facilities with the potential to release regulated materials must plan for emergencies and unauthorized releases of these materials.  Facilities with the potential to release a regulated material in a “reportable quantity” (defined by law, but varies with type of material) must have implemented an Installation Spill Contingency Plan (ISCP).  An ISCP identifies the potential for releases and the responsibilities, procedures, and resources available to respond to spills.

- EPA allows SPCCP requirements to be covered in an "Integrated Contingency Plan" (ICP) as long as it is prepared IAW applicable regulatory guidance.  Since development of an ICP reduces considerable redundancy required for separate emergency response plans for a single site, ORARNG will prepare an ICP for each facility meeting the criteria for an SPCCP.

- ANY spill of POL, regulated material or hazardous waste must be cleaned up and reported immediately.  Reporting is critical to environmental compliance and successful cleanup.  Cleanup actions must be approached with caution, and requirements will be based on the type and amount of the spill and the characteristics of the affected environment.

- ORARNG personnel will not make major efforts or risk personnel safety to clean up spills.  Safety is always the first priority.   National Guard Bureau (NGB) policy limits ARNG personnel to “responses to incidental releases of hazardous substances where the substance can be absorbed, neutralized, or otherwise controlled at the time of release by employees in the immediate release area, or by maintenance personnel”.  ORARNG has adopted this policy, and AGI-ENV will maintain trained personnel and manage spill cleanup beyond these guidelines.

- Spill response plans must be current and cleanup materials must be available to ensure successful cleanup of small spills.

- Personnel tasked to respond to spills must be trained annually with classroom instruction and practical exercises to ensure personal protection and individual knowledge of responsibilities.  Personal protective equipment (PPE) will be provided, as appropriate to assigned duties and potential hazard, by SAO-S.

- Spills must be reported as quickly as possible in the most expedient means available in order to comply with the law and minimize damage to the environment.  Required reports, including notification to emergency response personnel and written reports which must be filed after initial response has been completed, are defined in detail in ORARNGR 210-6, which must be used to meet all requirements.  Initial spill response information must be documented on AGO Form 200-1-9, which is included at the end of this chapter.

- ORARNGR 210-6 addresses spill response requirements that apply to all ORARNG facilities, training activities, and convoy operations.  Managers of facilities with the potential to generate a spill of a "reportable quantity" must adopt an SOP or other guidance to supplement these requirements.  The SOP must be filed at Annex Q to Chapter 20 of this pamphlet.

- ORARNG units must maintain the ability to respond to spills when using training areas and facilities owned by other agencies or components.  Commanders must comply with spill response requirements at those locations.  If guidance is not provided during in-briefings, personnel should request such guidance.  Failure to respond will violate the law and create problems directly reflecting on the Commander, the unit, and the ORARNG.  Guidance for setting up convoy refueling operations or refueling operations in a tactical environment is provided on AGO Form 200-1-10, provided at the end of this chapter.

  - ENVIRONMENTAL COMPLIANCE STATEMENT

- All facilities meeting the criteria of 40 CFR 112 must be covered by a Spill Prevention Control and Countermeasure Plan or an equivalent Integrated Contingency Plan.  Facilities currently meeting those requirements are identified in Annex Q to Chapter 20 of this pamphlet.

- Spills of regulated materials and POL must be reported immediately and cleaned up, if possible.  Notice will be documented on AGO Form 200-1-9, Spill Incident Report.  Assistance in responding to spills beyond the unit/facility capability should be obtained through command channels from AGI-ENV.  State law also allows the first public service provider trained in spill response to take command of the incident when arriving at the scene.

- A Facility Spill Response SOP will be prepared IAW ORARNGR 210-6 for sites not covered by an SPCCP or ICP.  A copy of this plan will be maintained at the facility and at each functional area or tenant at the facility.  A copy will also be provided to AGI-ENV.

- All ORARNG units will maintain a Spill Response SOP to be used in responding to spills during transportation, convoy refueling operations, and military training.  AGO Form 200-1-10 is provided to meet this requirement, and can be supplemented as necessary to ensure personnel understand requirements and responsibilities.

11-5.  RESPONSIBILITIES

a.  AGI-ENV will:

- Coordinate with Facility EPOCs to develop and maintain ICPs at facilities required by federal law.  These plans will normally be prepared by contract, comply with the requirements of 40 CFR 112 and AR 200-1, and contain the signature of a registered Professional Engineer.

- Monitor regulatory requirements and operational changes at ORARNG facilities.   When regulatory requirements become applicable to other facilities, or as circumstances change at existing facilities, AGI-ENV will notify the Facility EPOC and arrange for the preparation of required plans.  Facilities currently required to have an approved ICP are identified at Annex Q to Chapter 20 of this pamphlet.

- Maintain ORARNGR 210-6, as required and applicable to all ORARNG facilities.

- Assist ORARNG personnel in meeting spill response requirements, including completion of Facility Spill Response Plans, as required.

- Incorporate appropriate spill planning training requirements into the Environmental Training Program, as described in Chapter 19 of this pamphlet.

- Manage spill response and cleanup actions beyond the capability of the unit or facility, and coordinate regulatory requirements with applicable federal, state, or local agencies.

- Facility EPOC , as described in Appendix B, ORARNGR 210-6, will:

- As required, assist AGI-ENV and cooperate with contractors in completing an ICP.

- File the site-specific ICP at Annex Q of this pamphlet.  If the ICP is too large to conveniently fit in the ECN, it may be kept in a separate location.  However, a Memorandum for Record must be inserted at Annex Q, defining the location of all copies of the ICP at the facility.

- Maintain a Facility Spill Response SOP if an ICP is not required.

- Prepare plans IAW the provisions of Appendix B, ORARNGR 210-6.

- Tailor the plan to the site by adding information from Appendix I of ORARNGR 210-6, including resources of units and activities located at the site.  Coordination is required and may involve sharing resources.  A single plan will be prepared for the entire facility, but all units and/or tenants will have some implementation responsibilities.

- Update site-specific information at all times to keep the response plan current.

- Forward a copy of the Facility Spill Response SOP through command channels to AGI-ENV for review.

- Update the Facility Spill Response SOP when significant changes affecting the plan have been made to the installation.

- File the Facility Spill Response SOP at Annex Q to Chapter 20 of this pamphlet.

- Provide training to personnel who use, store, or dispose of oil and hazardous substances, or are responsible to respond to spills of regulated substances.

- Implement spill response requirements, as necessary.

- Request guidance on spill response and reporting when entering training sites under the jurisdiction of other agencies.

- In order to assist in responding to spill incidents away from the facility, ensure a copy of AGO Form SRG-1/SRG-2 (ORARNG Spill Response Guide) / On-Scene Coordinator Responsibilities) and a copy of AGO Form 200-1-10 are filed in the logbook of each ORARNG vehicle assigned to the facility.

- Immediately respond to spills or other incidents IAW requirements noted above or detailed in ORARNGR 210-6.  Response includes required notification, security of the site, cleanup (if possible), disposal of contaminated materials, and submission of appropriate reports.

c.  Unit EPOC will:

- Cooperate with the Facility EPOC, AGI-ENV, and designated contractors, as required, to prepare and maintain site-specific Integrated Contingency Plans.

- Assist the Facility EPOC in maintaining the Facility Spill Response SOP, as applicable.

- Prepare a Unit Spill Response SOP or comply with all of ORARNGR 210-6.

- In order to assist in responding to spill incidents away from the facility, ensure a copy of AGO Form SRG-1/SRG-2 (ORARNG Spill Response Guide) / On-Scene Coordinator Responsibilities) and a copy of AGO Form 200-1-10 are filed in the logbook of each ORARNG vehicle assigned to the unit.

- Immediately respond to spills or other incidents IAW requirements noted above or detailed in ORARNGR 210-6.  Response includes required notification, security of the site, cleanup (if possible), disposal of contaminated materials, and submission of appropriate reports.

d.  State Maintenance Worker will:

- (1) Cooperate with the Facility EPOC, AGI-ENV, and designated contractors, as required, to prepare and maintain site-specific Integrated Contingency Plans.

- (2) Assist the Facility EPOC in maintaining the Facility Spill Response SOP, as applicable.

- (3) Prepare a separate Spill Response SOP for maintenance operations, or comply with the Facility Spill Response SOP and all applicable provisions of ORARNGR 210-6.

- (4) In order to assist in responding to spill incidents away from the facility, ensure a copy of AGO Form SRG-1/SRG-2 (ORARNG Spill Response Guide) / On-Scene Coordinator Responsibilities) and a copy of AGO Form 200-1-10 are filed in the logbook of each ORARNG vehicle assigned to facilities maintenance personnel.

- (5) Immediately respond to spills or other incidents IAW requirements noted above or detailed in ORARNGR 210-6.  Response includes required notification, security of the site, cleanup (if possible), disposal of contaminated materials, and submission of appropriate reports.

11-6.  KEY QUESTIONS	YES	NO	N/A

a.  Is a site-specific ICP required for the facility?	___	___	___

b.  If so, has an ICP been provided by AGI-ENV, signed by a

Professional Engineer, current (w/in 3 yrs), and on file in Annex Q?	___	___	___

c.  Who is the primary POC?  ______________________________

d.  Has a Facility Spill Response Plan been prepared for the facility?	___	___	___

e.  Is the FSRP current (w/in one year or personnel changes made)?  	___	___	___

f.  Have persons tasked to respond to spills received awareness						training on their duties and understand requirements?	___	___	___

g.  Are unit personnel familiar with spill response and reporting

requirements, particularly during training, convoy and

refueling operations?   	___	___	___

h.  Is a copy of AGO Form SRG-1/SRG-2 and AGO Form 200-1-10					       filed in the logbook of each vehicle under control of the unit?	___	___	___

i.  Do unit personnel request information on spill response

requirements at training sites used by the unit?	___	___	___

j.  Are cleanup materials and equipment available for quick

response to spills at sites where spills are likely to occur?	___	___	___

k.  Is there a spill response kit in all unit vehicles that transport

and distribute fuels?	___	___	___

l.  Upon inspection of the facility grounds, are there noticeable

spots of POL or other chemicals on the ground?	___	___	___

  - ENVIRONMENTAL COMPLIANCE NOTEBOOK

Personnel identified in the appropriate Annexes below should maintain copies of the following documentation:

a.  An ICP prepared and distributed by AGI-ENV, if applicable (Annex Q).  If an ICP is too large to conveniently fit in the ECN, it may be kept in a separate location.  However, a Memo for Record must be inserted at Annex Q, defining the location of all copies of the ICP at the facility.

b.  Approved Facility Spill Response SOP, if applicable, for the facility (Annex Q).

c.  Unit Spill SOP, as applicable (Annex Q).

- d.  Copies of any Spill Incident Reports completed and submitted IAW Appendix A, ORARNGR 210-6, within the previous three years (Annex Q).

- e.  Environmental Training Attendance Rosters (AGO Form 200-1-13), documenting personnel spill response training for the past two years (Annex X).

  - TECHNICAL ASSISTANCE.  Technical assistance on spill prevention and contingency plans and actions required to meet requirements can be obtained from the Spill Response POC in the Environmental Office (AGI-ENV) at 503-584-3866.