| Requirement | Threshold (minimum) | Objective |
| --- | --- | --- |
| Physical |  |  |
| Camera size | <= 1PL | <= 1VN |
| Resolution | 1000 X 1000 pixels | 2000 X 2000 pixels |
| Environment (including vibration and shock) | All applications currently used by film cameras |  |
| Camera Mounting | Compatible with existing Winters mounts |  |
| Internal battery | 2 hr | 4 hr swappable |
| Power | 28V DC trigger | Recharge battery while triggered (compatible with existing battery packs) |
| Data storage | Video stored on non-volatile memory | Removable media |
| Camera Lens | C-Mount |  |
| Operation |  |  |
| Maximum run speed | 200 fps | 400 fps |
| Minimum run speed | 30 fps | 1 fps |
| Record time per run 200 fps | 8 s | 16s |
| Record time per run 10 fps | 3 min | 1 hr |
| Total record time 200 fps | 40 s | 2 min |
| Total record time 10 fps | 15 min | 3 hr |
| Camera trigger | Record while triggered not predetermined record length | Start X sec after trigger record until trigger removed |
|  | Pre, Post, Mid trigger | Delayed Pre trigger |
|  |  | Wireless trigger |
| Video Blooming/White out | Blooming limited to single line/row | Auto exposure |
| Data transfer from volatile memory to nonvolatile memory | 10 min | 1 min |
| Video downlink | Real time preview | On command playback of any recoded sequence with variable speed control |
| Video download (non removable media) /media removal | 15 min | 3 min |
| Video conversion | Export to MPG or AVI and print Time and Event on each frame | Export to MPG, AVI, and uncompressed unproprietary format with Time and Event on each frame |
| Accreditation | Unclassified | Unclassified / Classified swappable |
| Data Marking |  |  |
| IRIG | IRIG 106 capable | IRIG 106 TM receiver |
| Event marker | Event marker recorded | Event marker on frame |