## Slide 1
LECTURE #7
HYDROLOGIC PROCESSES,
PARAMETERS, AND CALIBRATION

## Slide 2
THE HYDROLOGIC CYCLE

## Slide 3
HYDROLOGY - HYDROLOGIC COMPONENTS
Hydrologic Components:
  Rainfall or Snow
  Interception
  Depression storage
  Evapotranspiration
  Infiltration
  Surface storage
  Runoff
  Interflow
  Groundwater flow
adapted from EPA BASINS workshop
Evapotranspiration
Interception
Depression
storage
Ground surface
Capillary
rise
Precipitation
Infiltration
Soil moisture
Percolation
Groundwater
storage
Underground flow into or out of the area
Ground water flow
Streamflow
Interflow
Surface runoff
Channel pptn.

## Slide 4
HYDROLOGY - WATER BALANCE
Water balance equation 
  R = P - ET - IG - S
  where: P = Precipitation
  R = Runoff
  ET = Evapotranspiration
  IG = Deep/inactive groundwater
  S = Change in soil storage
Inter-relationships between components
Variation of components with time
  consideration of soil condition, cover, antecedent conditions, land practices
adapted from EPA BASINS workshop

## Slide 5
STANFORD WATERSHED MODEL
To Stream
Actual ET
Potential ET
Precipitation
Temperature
Radiation
Wind,Dewpoint
Snowmelt
Interception
Storage
Lower Zone
Storage
Groundwater
Storage
Interflow
Upper Zone
Storage
Overland Flow
Deep or Inactive
Groundwater
CEPSC*
BASETP*
AGWETP*
DEEPFR*
LZSN*
INFILT*
INTFW*
UZSN*
AGWRC*
NSUR*
SLSUR*
LSUR*
IRC*
Delayed Infiltration
Direct
Infiltration
PERC
1
ET
2
ET
3
ET
4
ET
5
ET
LZETP*
* Parameters
Output
Process
Input
Storage
ET
-
Evapotranspiration
n
Order taken to
meet ET demand
Decision

## Slide 6
PWATER STRUCTURE CHART
PWATER
Simulate water budget
for pervious land
segment
EVAPT
Simulate
interception
ICEPT
Simulate
interflow
INTFLW
Simulate
upper zone
behavior
UZONE
Simulate the
lower zone
behavior
LZONE
Simulate
groundwater
behavior
GWATER
Subsidiary
upper zone
subroutine
UZONES
Simulate
evapotrans-
piration (ET)
Subsidiary
upper zone
subroutine
ETUZS
ET from
lower zone
ETLZON
ET from
baseflow
ETBASE
Evaporate
from
interception
EVICEP
ET from
upper zone
ETUZON
ET from
active
ground
water
ETAGW
Dispose of
moisture
supply
Distribute
the water
available for
infiltration
and runoff
Determine
surface
runoff
Compute
inflow to
upper zone
DIVISN
DISPOS
SURFAC
PROUTE
UZINF1/2
Divide
moisture
supply

## Slide 7
INTERCEPTION FUNCTION
Precipitation
CEPSC
Throughfall
Evaporation

## Slide 8
INFILTRATION DIAGRAM
line I - (Infiltration capacity)
line II - (Interflow +
Infiltration capacity)

## Slide 9
INFILTRATION FUNCTION IN HSPF
% AREA
I = INFILT * INFFAC
(LZS / LZSN) INFEXP
IMAX = I * INFILD
IMAX
Potential
Runoff
Supply Rate
Infiltration
I
0
100
50
0
I
LZS / LZSN
Infiltration Rate (in/hr)
II
Inter-
flow
II = I * INTFW (2.0** (LZS / LZSN))

## Slide 10
STANFORD WATERSHED MODEL
To Stream
Actual ET
Potential ET
Precipitation
Temperature
Radiation
Wind,Dewpoint
Snowmelt
Interception
Storage
Lower Zone
Storage
Groundwater
Storage
Interflow
Upper Zone
Storage
Overland Flow
Deep or Inactive
Groundwater
CEPSC*
BASETP*
AGWETP*
DEEPFR*
LZSN*
INFILT*
INTFW*
UZSN*
AGWRC*
NSUR*
SLSUR*
LSUR*
IRC*
Delayed Infiltration
Direct
Infiltration
PERC
1
ET
2
ET
3
ET
4
ET
5
ET
LZETP*
* Parameters
Output
Process
Input
Storage
ET
-
Evapotranspiration
n
Order taken to
meet ET demand
Decision

## Slide 11
UPPER ZONE STORAGE FUNCTION

## Slide 12
SOIL PROFILE DRAINAGE PROCESSES AND FUNCTIONS
LZS / LZSN
PERC = 0.1 * INFILT * INFFAC * UZSN * UZS - LZS 3
UZSN LZSN
From UZS
To lower zone or groundwater
1.0
0.0
0.5
Fraction to LZS
0.0
1.0
2.0
To Groundwater
To Lower Zone

## Slide 13
STANFORD WATERSHED MODEL
To Stream
Actual ET
Potential ET
Precipitation
Temperature
Radiation
Wind,Dewpoint
Snowmelt
Interception
Storage
Lower Zone
Storage
Groundwater
Storage
Interflow
Upper Zone
Storage
Overland Flow
Deep or Inactive
Groundwater
CEPSC*
BASETP*
AGWETP*
DEEPFR*
LZSN*
INFILT*
INTFW*
UZSN*
AGWRC*
NSUR*
SLSUR*
LSUR*
IRC*
Delayed Infiltration
Direct
Infiltration
PERC
1
ET
2
ET
3
ET
4
ET
5
ET
LZETP*
* Parameters
Output
Process
Input
Storage
ET
-
Evapotranspiration
n
Order taken to
meet ET demand
Decision

## Slide 14
OVERLAND FLOW FUNCTION

## Slide 15
SUB-SURFACE FLOW FUNCTIONS
Interflow
IFWO = K2 * IFWS + K1 * INFLO
IFWS = interflow storage at start of time step
INFLO = addition to interflow storage during time- step
K2 = 1.0 - e-K
K1 = 1.0 - K2/K
K = - ln(IRC)dt/24
IRC = Interflow recession parameter
Baseflow
AGWO = KGW * AGWS * (1.0 + KVARY * GWVS)
AGWS = active groundwater storage
GWVS = antecedent index increased by drainage
to AGWS, decreased 3% each day
KVARY = input parameter
KGW = 1.0 - (AGWRC)dt/24
AGWRC = Groundwater recession parameter

## Slide 16
STANFORD WATERSHED MODEL
To Stream
Actual ET
Potential ET
Precipitation
Temperature
Radiation
Wind,Dewpoint
Snowmelt
Interception
Storage
Lower Zone
Storage
Groundwater
Storage
Interflow
Upper Zone
Storage
Overland Flow
Deep or Inactive
Groundwater
CEPSC*
BASETP*
AGWETP*
DEEPFR*
LZSN*
INFILT*
INTFW*
UZSN*
AGWRC*
NSUR*
SLSUR*
LSUR*
IRC*
Delayed Infiltration
Direct
Infiltration
PERC
1
ET
2
ET
3
ET
4
ET
5
ET
LZETP*
* Parameters
Output
Process
Input
Storage
ET
-
Evapotranspiration
n
Order taken to
meet ET demand
Decision

## Slide 17
EVAPOTRANSPIRATION FUNCTIONS
AND HIERARCHY
1st from baseflow (BASETP)
2nd from interception
3rd from UZS @ potential if UZS / UZSN > 2.0; else prorated for effective area
4th from active groundwater (AGWETP)
5th from LZS
% AREA Less Than
inch / DT
100%
ET Potential
Actual ET
0%
50%
ET Opportunity
MAX
0.25 LZS DT_
1 - LZETP LZSN 24
*
*
MAX =

## Slide 18
STANFORD WATERSHED MODEL
To Stream
Actual ET
Potential ET
Precipitation
Temperature
Radiation
Wind,Dewpoint
Snowmelt
Interception
Storage
Lower Zone
Storage
Groundwater
Storage
Interflow
Upper Zone
Storage
Overland Flow
Deep or Inactive
Groundwater
CEPSC*
BASETP*
AGWETP*
DEEPFR*
LZSN*
INFILT*
INTFW*
UZSN*
AGWRC*
NSUR*
SLSUR*
LSUR*
IRC*
Delayed Infiltration
Direct
Infiltration
PERC
1
ET
2
ET
3
ET
4
ET
5
ET
LZETP*
* Parameters
Output
Process
Input
Storage
ET
-
Evapotranspiration
n
Order taken to
meet ET demand
Decision

## Slide 19
PWATER PARAMETERS:
PWAT-PARM2
FOREST - Fraction of the PLS covered by forest
LZSN - Lower zone nominal soil moisture storage
INFILT - Index to the infiltration capacity of the soil
LSUR - Length of the assumed overland flow plane
SLSUR - Slope of the assumed overland flow plane
KVARY - Variable groundwater recession parameter
AGWRC - Basic groundwater recession rate
(when KVARY is zero)

## Slide 20
PWATER PARAMETERS:
PWAT-PARM3
PETMAX - Air temperature below which ET will be reduced below the
input value (used when CSNOFG = 1)
PETMIN - Air temperature below which ET will be zero regardless of
the input value (used when CSNOFG = 1)
INFEXP - Exponent in the infiltration equation
INFILD - Ratio between the max and mean infiltration capacities over the PLS
DEEPFR - Fraction of groundwater inflow which will enter deep (inactive) groundwater
BASETP - Fraction of remaining potential ET which can be satisfied from baseflow
AGWETP - Fraction of remaining potential ET which can be satisfied from active groundwater storage

## Slide 21
PWATER PARAMETERS:
PWAT-PARM4
CEPSC - Interception storage capacity
UZSN - Upper zone nominal soil moisture storage
NSUR - Manning’s N for the assumed overland flow plane
INTFW - Interflow inflow parameter
IRC - Interflow recession parameter, i.e., the ratio of interflow
outflow rate today / rate yesterday
LZETP - Lower zone ET parameter; an index to the density of
deep-rooted vegetation

## Slide 22
Models are approximations of reality; they can not precisely represent natural systems
There is no single, accepted statistic or test that determines whether or not a model is valid
Both graphical comparisons and statistical tests are required in model calibration and validation
Models cannot be expected to be more accurate than the errors (confidence intervals) in the input and observed data
A ‘weight-of-evidence’ approach is becoming the preferred practice for model calibration and validation
CALIBRATION ISSUES
‘Basic Truths’ in modeling natural systems

## Slide 23
Mean runoff volume for simulation period (inches)
Annual and monthly runoff volume (inches)
Daily flow timeseries (cfs)
  observed and simulated daily flow
  scatter plots
Flow frequency (flow duration) curves (cfs)
Storm hydrographs, hourly or less, (cfs)
CALIBRATION/VALIDATION COMPARISONS
“Weight-of-Evidence” Approach

## Slide 24
Precipitation
Total Runoff (sum of following components)
  Overland flow
  Interflow
  Baseflow
Total Actual Evapotranspiration (ET) (sum of following components)
  Interception ET
  Upper Zone ET
  Lower Zone ET
  Baseflow ET
  Active Groundwater ET
Deep Groundwater Recharge/Losses
CALIBRATION/VALIDATION COMPARISONS
Water Balance Components

## Slide 25
Graphical Comparisons:
Timeseries plots of observed and simulated values for fluxes (e.g., flow) or state variables (e.g., stage, sediment concentration, biomass concentration)
Observed and simulated scatter plots, with 45o linear regression line displayed, for fluxes or state variables
Cumulative frequency distributions of observed and simulated fluxes or state variable (e.g., flow duration curves)
Statistical Tests:
Error statistics, e.g., mean error, absolute mean error, relative error, relative bias, standard error of estimate, etc.
Correlation tests, e.g., correlation coefficient, coefficient of model-fit efficiency, etc.
Cumulative Distribution tests, e.g., Kolmogorov-Smirnov (KS) test
CALIBRATION/VALIDATION COMPARISONS
Graphical/Statistical Procedures & Tests

## Slide 26: R & R2 VALUE RANGES FOR MODEL PERFORMANCE
Criteria
0.6
0.7
0.8
0.9
Poor
Fair
Good
Very Good
Poor
Fair
Good
Very Good
0.75
0.80
0.85
0.90
0.95
R
2
Daily Flows
Monthly Flows
R

## Slide 27
HYDROLOGIC (PWATER) CALIBRATION
Annual Water Balance -
  Runoff = Prec. - Actual ET - Deep Perc. - D Storage
  Key Parameters: Repre. Precipitation (MFACT)
  LZSN
  LZETP
  INFILT
  DEEPFR
Groundwater (Baseflow) Volume and Recession -
  Runoff = Surface Runoff + Interflow + Baseflow
  Key Parameters: INFILT
  AGWRC/KVARY
  DEEPFR
  BASETP/AGWETP
Surface Runoff + Interflow (Hydrograph Shape) -
  Key Parameters: UZSN
  INTFW
  IRC
  LSUR, NSUR, SLSUR

## Slide 28
COMPONENTS OF HYDROGRAPH
Surface runoff - overland flow
Interflow - flow through surficial layers of soil
Baseflow
Runoff
Interflow
Baseflow - groundwater seepage from springs and
aquifers directly to the stream channel
adapted from EPA BASINS workshop

## Slide 29
HYDROGRAPH SENSITIVITY TO INFILT

## Slide 30
HYDROGRAPH SENSITIVITY TO INTFW

## Slide 31
HSPF PWATER PARAMETERS AND
TYPICAL/POSSIBLE VALUE RANGES (#1)

## Slide 32
HSPF PWATER PARAMETERS AND
TYPICAL/POSSIBLE VALUE RANGES (#2)

## Slide 33
HSPF PWATER PARAMETERS AND
TYPICAL/POSSIBLE VALUE RANGES (#3)

## Slide 34
IWATER STRUCTURE CHART
RETN
EVRETN
IROUTE
IWATER
Simulate
water budget
for impervious
land segment
Simulate
moisture
retention
Determine how
much of the
moisture supply
runs off
Evaporate from
retention
storage

## Slide 35
IWATER CALIBRATION
Impervious
area process
IWATER
parameter
Interception RETSC
Overland flow LSUR, NSUR, SLSUR
Evaporation (no parameter, occurs at PET)