## Slide 1: LECTURE #7b PWATER REFINEMENTS FOR WETLANDS HYDROLOGY
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2
‘NORMAL’ PWATER HYDROLOGIC
ASSUMPTIONS
'Normal' gravitational-driven watershed hydrology exists
Surface runoff is driven by ground surface slope; evaporation from surface detention is not significant
Groundwater level is deep; it does not interact with surface runoff, infiltration, or the unsaturated zone
Entire active groundwater storage provides baseflow; deep inactive groundwater is not represented
Unsaturated zone is modeled with two storages - upper zone, lower zone - with 'nominal' capacities but no maximum limits
Interflow represents a subsurface path to the stream; interflow storage has no maximum

## Slide 3
OBJECTIVES OF PWATER REFINEMENTS FOR WETLANDS HYDROLOGY
Track dynamic variation in groundwater level (i.e., rising/falling water table)
Model interaction between groundwater storage, soil (unsaturated zone) storages, and infiltration/runoff processes
Accommodate ponded conditions on the land surface
Allow evaporation from ponded surface storage and surface runoff
Allow additional options for surface runoff when not gravity driven, i.e. function of surface storage, water level differences, etc.
Perform refinements with minimal changes to existing PWATER routines
Allow for smooth transition between 'normal' hydrologic conditions and 'water table influence' effects

## Slide 4
FIELD CAPACITY, WILTING POINT AND
AVAILABLE WATER
Soil texture and available water holding capacity of soils.

## Slide 5
SOIL POROSITY CONCEPTS
Bulk density and pore space for Miami loam with A, E, Bt and C horizons.

## Slide 6
Pore Space
SOIL PROFILE CONCEPTS FOR HIGH WATER
TABLE VERSION OF PWATER
Land Surface
Pcw
Pgravw
UZS
LZS
GWS
AGWS
Minimum Channel Elevation
Datum
Lower Zone
Influence Depth
CohesionWater
Available Porosity
Gravitational
Water
Soil
Groundwater Level
Upper Zone
Influence Depth

## Slide 7
SOIL MOISTURE STORAGE CONCEPTS AND
MODEL ALGORITHIMS

## Slide 8
SOIL MOISTURE STORAGE CONCEPTS AND MODEL ALGORITHIMS
PGW
IFWS
LZS
Soil
UZS
PCW
UPGW
PCW
REGION
1
REGION
3
REGION
2
SURS
Soil
1.0
GW Datum
BELV
(base elevation)
LELV
(lower influence elevation)
UELV
(upper influence elevation)
SELV
(surface elevation)
GWEL
(groundwater elevation)
AGWS
BGWS

## Slide 9
INFLUENCE LEVELS
Lower Influence level -Water surface elevation above which groundwater affects lower zone behavior and processes
LELV = SELV - (2.5*LZSN)/PCW
where: LELV = lower zone influence level [in]
SELV = mean surface elevation (relative to some datum) [in]
LZSN = lower zone nominal storage [in]
PCW = porosity in micropores
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
Upper influence level - Water surface elevation above which groundwater affects upper zone behavior and processes
UELV = SELV - (4*UZSN + IFWSC)/UPGW
where: UELV = upper zone and interflow influence level [in]
SELV = mean surface elevation [in]
UZSN = upper zone nominal storage [in].
IFWSC = interflow storage capacity [in]
UPGW = porosity in macropores in upper soil layer [-]

## Slide 10
GROUNDWATER STORAGES AND ELEVATIONS
Region 1: GWEL < LELV
TGWS = AGWS +BGWS
GWEL = TGWS/(PCW + PGW)
Region 2: UELV > GWEL > LELV
LLGWS = LELV*(PCW + PGW)
GWEL = LELV + (TGWS-LLGWS)/PGW
Region 3: SELV > GWEL > UELV
ULGWS = LLGWS + (UELV - LELV)*PGW
GWEL = UELV + (UZS + IFWS + (TGWS - ULGWS))/PGW
Above Region 3: Surface Ponding
Water Surface Elevation = GWEL + SURS

## Slide 11
GROUNDWATER EVAPOTRANSPIRATION
Region 1: GWEL < LELV
'Normal' operation of ET algorithms, except ET at potential rate from Surface Detention Storage (SURS)
Region 2: UELV > GWEL > LELV
AGWET = REMPET*[AGWETP + (1.0 – AGWETP)*(GWEL- LELV)/(SELV-LELV)]
where: AGWET = evapotranspiration from groundwater [in]
REMPET = remaining potential evapotranspiration [in]
AGWETP = fraction of REMPET from active groundwater, input parameter [-]
GWEL = groundwater elevation [in]
SELV = surface elevation [in]
AGWET cannot exceed the groundwater storage above LELV:
AGWET = MIN[AGWET, (TGWS-LLGWS)]
Region 3: SELV > GWEL > UELV
ET at potential rate from UZS (normal operation) and added to AGWET
Above Region 3: Surface Ponding
ET at potential rate from SURS

## Slide 12
SURFACE RUNOFF OPTIONS
RTOPFG = 1:
'Normal' gravity and slope driven overland flow routing
RTOPFG = 2: Power function of Surface Storage
SURO = (1-SRRC*DELT60)*SURS**SREXP
where: SURO = Surface Outflow [in/interval]
SURS = Surface Detention Storage [in]
SRRC = Hourly recession constant
DELT60 = Hours per interval
SREXP = Exponent in surface runoff equation
RTOPFG = 3: General FTABLE Option
FTABLE 1
ROWS COLS ***
5 2
Depth Outflow ***
(in) (/hr) ***
---- ------- ***
0.0 0.00
2.0 0.01
4.0 0.02
6.0 0.03
8.0 0.04
END FTABLE 1

## Slide 13
NEW PWATER VARIABLES, PARAMETERS, AND
CONSTANTS (#1)
NAME TYPE EXPLANATION COMMENTS
GWEL Variable Groundwater elevation (in) Elevation of the groundwater calculated in each time
step.
GWDATM Parameter Datum for GWEL (ft) (typically Total groundwater storage is the storage between
mean sea level in coastal areas) GWDATM and the groundwater elevation.
SELV Constant Mean surface elevation (in) The mean elevation is representative for flat areas.
=MELEV*12-GWDATM
(MELEV is a parameter)
UELV Constant Upper Influence Elevation (in) Elevation above which the groundwater affects upper
= SELV-(4*UZSN+IFWSC)/UPGW zone and interflow storage behavior.
LELV Constant Lower Influence Elevation (in) Elevation above which the groundwater affects lower
= SELV-(2.5*LZSN)/PCW zone behavior and may affect interflow.
BELV Parameter Base elevation for AGWO (in) Groundwater elevation above which there is outflow
(corresponds to the bottom into the channels. Groundwater below BELV is
elevation of nearby channels) inactive.
ULGWS Constant Total Groundwater storage when Groundwater storage above which groundwater
the groundwater level is at affects upper zone and interflow behavior.
UELV (in)
LLGWS Constant Total Groundwater storage when Groundwater storage above which groundwater
the groundwater level is at affects lower zone and may affect interflow behavior.
LELV (in)

## Slide 14
NEW PWATER VARIABLES, PARAMETERS, AND
CONSTANTS (#2)
NAME TYPE EXPLANATION COMMENTS
BGWS Constant Total Groundwater storage when Groundwater storage above which there is
groundwater level is BELV (in) groundwater outflow.
PCW Parameter Cohesion water porosity (-) Soil pore space in micropores
PGW Parameter Gravitational water porosity (-) Soil pore space in macropores.
UPGW Parameter Upper gravitational water Pore space in macropores in the upper layers of the
porosity (-) soil column.
IFWSC Parameter Maximum interflow storage (in) Maximum interflow storage if GWEL>UELV
SRRC Parameter Surface Runoff Recession Used to calculate surface runoff as a function of
Constant (-) surface storage only.
SREXP Parameter Surface Runoff Exponent (-) Used to calculate surface runoff as a function of
surface storage only.
DELTA Constant / Tolerance level to determine Used to smooth out jumps in gw elevation due to
Parameter transition between regions (in) changes in soil region.
LELFAC Parameter Factor in equation describing Typical value is 2.5.
lower zone influence level
UELFAC Parameter Factor in equation describing Typical value is 4.0.
the upper influence level

## Slide 15
EXAMPLE GW ELEVATION SIMULATION RESULTS FOR St. LUCIE WATERSHED, FL (#1)
Groundwater elevations at Indiantown Well (1979-1994).

## Slide 16
EXAMPLE GW ELEVATION SIMULATION RESULTS FOR St. LUCIE WATERSHED, FL (#2)
Groundwater elevations at Indiantown Well (1988).

## Slide 17
CONCLUSIONS
    High water table/wetlands code changes have been successfully implemented into PWATER
    Preliminary testing with prototype model and generic data for South Florida has been successful; model simulates range and variability of groundwater levels
    Preliminary testing with a subset of St. Lucie data shows reasonable reproduction of groundwater levels and variability
    Complete testing within the integrated HSPF/FEQ system on St. Lucie is needed; issues of irrigation applications, pumping, and canal water levels must be addressed

## Slide 18
COMPONENTS OF WETLANDS WATER
BUDGETS
P + SWI + GWI = ET + SWO + GWO +S
P = precipitation
SWI = surface-
water inflow
SWO = surface-
water outflow
GWI = ground-
water inflow
GWO = ground-
water outflow
ET = evapotrans-
piration
S = change in
storage
National Water Survey - Wetland Resources

## Slide 19
WATER BUDGETS FOR SELECTED WETLAND TYPES
Components are expressed in percentages.
National Water Survey - Wetland Resources

## Slide 20
WATER BUDGETS FOR SELECTED WETLAND TYPES
National Water Survey - Wetland Resources
Components are expressed in percentages.

## Slide 21
WATER BUDGETS FOR SELECTED WETLAND TYPES
National Water Survey - Wetland Resources
Components are expressed in percentages.