EPA420-R-00-002

February 2000

# ANALYSIS OF COMMERCIAL MARINE VESSELS

# EMISSIONS AND FUEL CONSUMPTION DATA

# Final Report

Work Assignment 1-10

EPA Contract No. 68-C7-0051

Prepared for:

U.S. ENVIRONMENTAL PROTECTION AGENCY

OFFICE OF MOBILE SOURCES

Ann Arbor, MI

Under subcontract to:

## SIERRA RESEARCH

# Sacramento, CA

Prepared by:

ENERGY AND ENVIRONMENTAL ANALYSIS, INC.

1655 North Fort Myer Drive, Suite 600

Arlington, VA  22209

# TABLE OF CONTENTS

Page

1.	INTRODUCTION 		1-1

2.	REVIEW OF RELEVANT DATA 		2-1

2.1	Introduction 		2-1

2.2	Findings on Reports Providing Emissions Data 		2-1

2.3	Summary of Reports Analyzing Emissions Data 		2-3

2.4	Recommendations for Analysis 		2-6

3.	EMISSION FACTOR DEVELOPMENT 		3-1

3.1	Introduction 		3-1

3.2	Lloyd’s Emission Test Data 		3-2

3.3	U.S. Coast Guard Emission Test Data 		3-6

3.4	Emissions Data Analysis 		3-13

3.5	Emission Factor Development 		3-21

4.	MARINE VESSEL CLASSIFICATIONS AND POWER RATINGS 		4-1

4.1	Classifications Employed in Literature 		4-1

4.2	Operating Mode Classifications in Literature 		4-4

4.3	Analysis of Ship Type and Weight Categories 		4-6

5.	EMISSION FACTOR SUMMARY 		5-1

6.	REFERENCES 		6-1

APPENDIX A	EMISSION FACTOR REGRESSION SUMMARIES 		A-1

APPENDIX B	SUMMARY OF REPORTS REVIEWED 		B-1

APPENDIX C	ACUREX CLASSIFICATION OF SHIPTYPES 		C-1

LIST OF TABLES

Page

Table 2-1.	Summary of Emissions Data 		2-4

Table 3-1.	Overview of the Lloyd’s Emission Test Database 		3-3

Table 3-2.	Lloyd’s NO to NOx Ratio for Marine Engines 		3-5

Table 3-3.	Overview of the USCG Emission Test Database 		3-8

Table 3-4.	Lloyd’s Marine Engine Fuel Specifications 		3-10

Table 3-5.	Marine Engine Emission Factor Algorithms 		3-44

Table 3-6.	Marine Gas Turbine Emission Rate Data 		3-52

Table 4-1.	Booz-Allen Classification of Vessels 		4-2

Table 4-2.	Engine Loads by Ship Type for Each Operating Mode 		4-7

Table 4-3.	Results of Regressions between Horsepower and Deadweight Tonnage 		4-9

Table 4-4.	Regressions of Horsepower vs. Deadweight and Cruise Speed 		4-10

Table 4-5.	Recommended Ship Types and Regressions of Horsepower
		to Deadweight 		4-11

Table 4-6.	Suggested Loads by Mode 		4-13

Table 5-1.	Marine Engine Emission Factor and Fuel Consumption Algorithms 		5-3

Table 5-2.	Suggested Load Factors 		5-6

LIST OF FIGURES

Page

Figure 3-1.	Derivation of USCG Fuel H to C Ratio 		3-9

Figure 3-2.	Implied A/F Ratio 		3-14

Figure 3-3.	A/F Ratio Comparison - Detailed Carbon Balance 		3-17

Figure 3-4.	A/F Ratio Comparison - Detailed Oxygen Balance 		3-18

Figure 3-5.	A/F Ratio Comparison – Excess Air Balance 		3-19

Figure 3-6.	CO2/O2 Relationship 		3-20

Figure 3-7.	Consistency of A/F Ratio Estimates 		3-22

Figure 3-8.	Test Data Load Coverage 		3-23

Figure 3-9.	Measured CO2 		3-25

Figure 3-10.	Measured O2 		3-26

Figure 3-11.	Measured NO 		3-27

Figure 3-12.	Measured CO 		3-28

Figure 3-13.	Measured HC 		3-29

Figure 3-14.	Measured SO2 		3-30

Figure 3-15.	Measured PM 		3-31

Figure 3-16.	Fuel Consumption Data by Absolute Load 		3-32

Figure 3-17.	Fuel Consumption Data by Fractional Load 		3-33

Figure 3-18.	PM Emission Rate Data 		3-35

Figure 3-19.	NO Emission Rate Data 		3-36

LIST OF FIGURES

(Continued)

Page

Figure 3-20.	NOx Emission Rate Data 		3-37

Figure 3-21.	NO2 Equivalent NOx Emission Rate Data 		3-38

Figure 3-22.	SO2 Emission Rate Data 		3-39

Figure 3-23.	CO Emission Rate Data 		3-40

Figure 3-24.	CO2 Emission Rate Data 		3-41

Figure 3-25.	O2 Emission Rate Data 		3-42

Figure 3-26.	HC Emission Rate Data 		3-43

Figure 3-27.	NO Emission Rate Data by Fuel Type 		3-49

Figure 3-28.	NOx Emission Rate Data by Fuel Type 		3-50

Figure 3-29.	NO2 Emission Rate Data by Fuel Type 		3-51

Figure 3-30.	Gas Turbine Emission Rates 		3-53

Figure A-1.	PM Emission Rate Data by Engine Type 		A-17

Figure A-2.	NO Emission Rate Data by Engine Type 		A-18

Figure A-3.	NOx Emission Rate Data by Engine Type 		A-19

Figure A-4.	NO2 Emission Rate Data by Engine Type 		A-20

Figure A-5.	CO Emission Rate Data by Engine Type 		A-21

Figure A-6.	CO2 Emission Rate Data by Engine Type 		A-22

Figure A-7.	O2 Emission Rate Data by Engine Type 		A-23

Figure A-8.	HC Emission Rate Data by Engine Type 		A-24

LIST OF FIGURES

(Continued)

Page

Figure A-9.	Dry Exhaust Emission Rate Data by Engine Type 		A-25

Figure A-10.	H2O Emissions Rate Data by Engine Type 		A-26

Figure A-11.	Wet Exhaust Emission Rate Data by Engine Type 		A-27

Figure A-12.	NO Emission Rate Data by Fuel Type 		A-28

Figure A-13.	NOx Emission Rate Data by Fuel Type 		A-29

Figure A-14.	NO2 Emission Rate Data by Fuel Type 		A-30

Figure A-15.	CO Emission Rate Data by Fuel Type 		A-31

Figure A-16.	CO2 Emission Rate Data by Fuel Type 		A-32

Figure A-17.	O2 Emission Rate Data by Fuel Type 		A-33

Figure A-18.	HC Emission Rate Data by Fuel Type 		A-34

Figure A-19.	Dry Exhaust Emission Rate Data by Fuel Type 		A-35

Figure A-20.	H2O Emission Rate Data by Fuel Type 		A-36

Figure A-21.	Wet Exhaust Emission Rate Data by Fuel Type 		A-37

1.  INTRODUCTION

The EPA is initiating a review of its guidance on developing emission inventories for ocean-going and harbor vessels operating at port areas.  The current methodology, as defined in AP-42, is based on a three step calculation.  The first step apportions the time spent by a vessel in a port area to different operating modes.  The second calculates fuel consumption in each operating mode.  The third step calculates emissions using fuel consumption specific emission factors, which is how marine engine emission factors have been historically specified.  All of these calculations are by vessel type and class, with the type specifying whether the vessel is a tanker, passenger liner, etc, and the class specifying either the weight or horsepower range.

The time-in-mode is a function of the particular port area geography and is not considered in this report.  The other factors used in the computation are examined, with particular focus on the emission factor, for all pollutants of concern.  One reason for a detailed reconsideration of the emission factor is that a number of large marine diesels have been tested for emissions and their tests result have become available in the last few years.  In addition, both the EPA and ARB have recently sponsored studies to calculate marine vessel emissions in the South Coast Air Basin and in some areas of Region IX, so that there is a body of new research available to update emission factors.  Hence, the use of a larger and newer database on marine vessel emission is expected to substantially improve the quality of the derived emission factors.

In this work assignment, the EPA did not require a literature review, but instead provided with nine reports as the basis for this review.  Due to the fact that data on emissions from gas turbines were restricted to two engines, most of the analysis presented in this report pertains only to diesel powered marine vessels and only an average emission rate for the gas turbines is presented.  Section 2 of this report presents the findings of our literature review of the nine reports provided by EPA.  Section 3 details our analysis of emissions data contained in reports, and the resultant derivation of emission factors.  Section 4 provides an analysis of vessel classifications and horsepower to vessel weight relationships.  Section 5 summarizes the resultant emission factors by vessel type, and operating mode.

2.  REVIEW OF RELEVANT DATA

2.1	INTRODUCTION

As noted, the U.S. EPA had identified nine reports in its work assignment for review.  All of these were obtained by EEA from EPA and reviewed to assess the usefulness for this study.  The reports can be classified into two groups of four reports.  One group provides detailed tables on actual emissions data.  The second group of four reports are studies that utilize one or more of the reports in the first group to estimate emission factors, and to estimate emission inventories for marine vessels operating in a specific region, like the South Coast Air Basin.  One report simply provided data on gas turbines emissions and is not reviewed in this section, but the data is presented in Section 3.

The reports were reviewed to estimate the applicability of the data or the analysis to the EPA requirements to calculate emission factors by ship class, type and operating mode.  EPA has also proposed rules for controlling marine engine emissions by defining three engine categories.  The EPA categories are based on individual cylinder displacement and the categories are:

- less than five liters;

- five to 20 liters; and

- greater than 20 liters.

These categories approximately correspond to engines in the high speed, medium speed and slow speed categories used by IMO and Lloyds in previous analyses.  However, the correspondence may or may not hold true for some specific engine designs.

2.2	FINDINGs ON REPORTS PROVIDING EMISSIONS DATA

The four reports that provide emissions data includes one from British Columbia Ferry Corporation, one from Environment Canada, one from Lloyd’s (in three sections), and one from the U.S. Coast Guard.  Each report is summarized in Appendix B.

The Lloyd’s data1,2,3 is the most detailed although there are some inconsistencies in the data.  For example, the text and table do not agree on the actual number of engines tested, or the type.  Data on engine tests are reported in Appendices, but engine make and displacement are not reported.  In addition, the Lloyd’s data also indicated large inconsistencies in the measured output at full load versus actual engine ratings.  Ostensibly, all engines were tested at idle, 25, 50, 75, and 100 percent of full power; yet in a majority of cases, the 100 percent rated power as measured on the emissions test differs from the engine rated power by as much as (50 percent.  While reductions in power associated with a service derating is possible and production variations of (10 percent may be reasonable, such large differences are cause for concern, especially as they are unexplained in the text.

However, it should be noted that for most engines, full output corresponded to 83 (17% of rated power, while about ten engines have measured power either below 66 percent of rated or over 101 percent of rated power.  Results indicate generally well behaved CO emission factors as a function of percent of rated power but HC and NOx emissions dependence on load varies both in magnitude and direction across engines as a function of load.  In general, absolute emission rates can vary across engines but the emissions profile for diesel engines as a function of load do not vary greatly.  The variations as plotted in the Lloyds report are so large across engines that it raises questions on the data and test procedure.

The BC Ferry Test Program report5 appears incomplete and has several inconsistencies that make the data difficult to use.  The main issue is that the test procedure was conducted at two different, undefined conditions labeled “normal cruise” and “docking operation”.  Data on eight engines are presented, (the tables show nine engine tested at normal cruise), but the test conditions relative to the engine rated power are very inconsistent across engines.  Engine data is inadequate to determine what EPA category they may fall into.  Data presented indicates that five were medium speed diesels, while three are high speed engines (but the data on one high speed engine shows an improbably high RPM figure for a 4500 kW diesel).  Only fuel specific emission rates are reported for the engines.

The Environment Canada report6 provides data on 11 engines tested on three modes:  maneuvering, low speed cruise and high speed cruise.  The report does not describe how these modes are defined and whether the relative load on the engine (or load factor) was similar across the 11 engines.  Only fuel specific emission indices are reported, and there are very large variations across engines in a similar category.  Not enough data is provided to determine how these engines fit into the EPA categories.  EEA attempted to obtain more detailed data on the test procedure and measured emissions from Environment Canada, but could not do so in the time available.

The tests conducted by the Coast Guard4 were on six ships with two engines each (one ship also had two gas turbine engines in addition to the diesels).  The test procedure was ostensibly conducted at idle, 25, 50, 75, and 100 percent of maximum power, although here again, there appear to be large differences in some instances between reported maximum power and engine ratings.  In one instance, the observed power is 85 percent higher than the engine rating provided.  Fuel specifications and engine type information (two-stroke/four-stroke) was not provided.

Across all of the four reports, emissions data is available on 20 slow speed engine, 51 medium speed engines and eight high speed engines, plus an additional ten auxiliary engines whose characteristics are not listed.  It is not clear if these have been any QA/QC on the data, since the data appear to have certain inconsistencies.

Table 2-1 summarizes the data available and the test procedure used, to the extent it is documented.

2.3	SUMMARY OF REPORTS ANALYZING EMISSIONS DATA

Of the four reports in this category, three were reports that developed marine emissions, inventories for specific regions.  The earliest (1991) report is by Booz-Allen and Hamilton9 for the ARB that developed inventories for Los Angeles/Long Beach and San Francisco.  The report computed emissions from Ocean-going, harbor, and fishing vessels.  Ocean-going and harbor

TABLE 2-1

SUMMARY OF EMISSIONS DATA

| Reference | BC Ferries | Environment Canada | Lloyds Register | Coast Guard |
| --- | --- | --- | --- | --- |
| Vessels | 8 | 13 | 40 | 6 |
| Engines |  |  |  |  |
| - Slow speed | 0 | 9 | 11 | 0 |
| - Medium speed | 6 | 1 | 36 | 8 |
| - High speed | 3 (?) | 1 | 0 | 4 |
| - Auxiliary | 3 | 5 | 2 | 0 |
| Test Cycle | Normal cruise Docking Full Power for Auxiliary | Maneuvering Low Speed Normal Cruise Hoteling for Auxiliary engines | 100% load 75% load 50% load 25% load Idle | 100% load 75% load 50% load 25% load Idle |
| Data Reported | All except THC in kg/ton of fuel | All in Kg/ton of fuel | All except PM, as raw data | All in mass per kW-hr and per ton of fuel |
| Potential Problems | Test points undefined and varies by engine | Test points undefined. All engines not tested at all loads | Measured output at 100% load unrelated to rated power | Measured and rated power do not match for some engines. |

vessels were further divided into four types and five weight or HP classes.  Fishing vessels were subdivided into four HP categories. The operating profile in each port for the three vessel classes was obtained by surveys.  Emissions were calculated using the DOT Port Vessel Emission Model, that calculates fuel consumption and resulting emissions using existing AP-42 emission factors.  The methodology is relatively simplistic in that emissions are purely a function of fuel consumption, not load.

A very similar approach was used by Lloyds8 to determine emissions from ferries operated in Vancouver by the British Columbia Ferry Corporation.  The main difference appears to be the use of engine specific emission factors derived from the Lloyds’s test program referenced in the previous section.  The report is not clear how fuel consumption was translated to emissions, i.e., by mode or based on aggregate fuel consumption rates.

The two other reports, by Arcadis (previously Acurex), calculate emission inventories for marine vessels in the South Coast Air Basin.  The 1996 report for the South Coast AQMD10 differed from the 1991 Booz-Allen Report by including Navy and Coast Guard operations.  The Acurex report also used actual data on the HP ratings and fuel consumption (obtained from Lloyds) and improved the characterization of operations in the South Coast.  The Acurex report includes a very detailed classification of eight ship types, with each ship type subdivided into eight to ten weight categories.  However emissions characterization again appear to be based on calculated fuel consumption, with the use of emission factors on a unit of fuel consumed as derived by Lloyds.  These emissions appear to have been derived to represent a power setting of about 85 percent of maximum continuous rating (MCR), but there is no documentation of the methodology used.

The more recent (1999) report by Arcadis (Acurex) for EPA Region IX8 provides an analysis of marine NOx emissions for the South Coast.  The characterization of ship types is quite detailed as in the 1996 report.  This is the only report where emissions in units of work (g/kW-hr) were derived as a function of percent of MCR.  The emission factors on this basis were constructed from the ‘raw’ data provided by Lloyds.  Surprisingly, the report does not mention the large discrepancy between rated and measured power and it is not obvious how the percent of MCR was derived.  Regression analysis of individual data points was utilized to relate NOx emissions to engine load factor (% of MCR).  The regression analysis, however, suggested that NOx emissions either decline slightly or are independent of MCR.  If these results are correct, it would suggest little or no difference if NOx was treated as a constant or as a function of load.  Nevertheless, the methodology is conceptually superior to using aggregate fuel consumption data that is multiplied by an emission factor in units of fuel consumption.

2.4	RECOMMENDATIONS FOR ANALYSIS

The review of the emission data available indicated significant inconsistencies in engine power ratings versus measured power output that are too large to ascribe to engine-to-engine variability, or a ‘service’ derating.  Moreover, the test procedures used by different organizations are inconsistent, while the reported results are incompatible with the results from a recommended IMO standard test cycles.  In most cases, engine displacement is not available, so that the relationship to EPA engine categories cannot be exactly determined (but could be approximated). In addition, some reported changes in engine emissions with load are directionally inconsistent across engines.  Hence, the data analysis focused on data cleaning techniques to identify and correct or reject data that are determined to be in error.

Reports by Booz-Allen, Acurex and Arcadis employ consistent classifications by ship type, but the Acurex and Arcadis reports have developed more detailed breakouts of each ship type by weight category.  The use of Lloyd’s data to determine the engine and auxiliary HP by these detailed type and weight categories is an improvement over earlier techniques.  If engine power is linearly related to ship characteristics, it is not clear that models require the use of weight categories for ship types.  A linear regression connecting horsepower to ship weight is preferable relative to analysis by weight categories.

The computation of emissions using fuel consumption as a surrogate load indicator appears to be both unnecessary and to introduce errors.  Indeed, the 1999 Arcadis report has utilized emissions as a function of engine load factor to directly compute emission at every operating mode that is represented in the operating profile.  This direct method is preferable to linking emissions to fuel consumption since the computation of fuel consumption and the translations to emissions introduce multiplicative errors in emission estimations.  EEA suggest a future marine emission model with four specified modes of operation (e.g., docking, low speed cruise, etc.) where each type of operation is associated with a single load factor.  On the other hand, if emissions in g/kW-hr are approximately constant with load factors, (as indicated for NOx in the Arcadis report) different approaches may not lead to significantly different answers.

In addition, time constraints did not allow us to resolve many of the data issues raised.  In the future, EEA recommends that EPA focus on resolving some of the data issues and in expanding the database.

3.  EMISSION FACTOR DEVELOPMENT

3.1	INTRODUCTION

Ostensibly, six of the reports provided to EEA for review present the results of marine engine emissions testing.1-6  However, three of these reports do not present the described emissions test data in sufficient detail to support the fundamental analysis required for the development of marine engine emission factors.3,5,6  These reports essentially present the results of the author’s emission factor analysis, but not the underlying data that went into the analysis.  Without this underlying data, the utility of these reports is limited for several reasons.  First, the presented emission factors are expressed in units of emission mass per fuel mass consumed, a metric that for real-world application requires either knowledge or estimation of fuel consumption rates.  However, fuel consumption rates are not usually measured, but rather estimated from engine design and loading data, where engine loading itself can usually only be estimated.  It seems inappropriate to introduce additional uncertainty into the emissions estimation process through the use of fuel mass-based emission factors in lieu of emission factors expressed in more fundamental units of mass per unit engine work.  Second, the presented emission factors represent the aggregation of an unknown number of individual emission tests, such that the statistical significance of the reported emission factors can be determined.  Third, as demonstrated below, considerable caution must be exercised in converting measured emission concentrations into valid emission rates.  Without access to the underlying test data, it is not possible to either ensure that adequate caution has been exercised or that the generated emission rates are comparable to those developed from other test programs.

Attempts were made to contact the authors of the three reports that do not present underlying emission test data, but these attempts were not successful in the timeframe available to EEA for analysis.  As a result, the emission factors described below were developed through the statistical analysis of fundamental test data presented in only three of the emission testing reports.1,2,4  Two of these reports were prepared by Lloyd’s Register of Shipping and consider a wide range of commercial engine sizes and configurations.  The third report was prepared for the U.S. Coast Guard (USCG) and considers a number of engines that are representative of marine engines in use in the USCG fleet.  As described below, all three datasets required considerable quality assurance efforts to ensure that emission factors developed from the reported test data were both reasonable and accurate.

3.2	LLOYD’S EMISSION TEST DATA

Lloyd’s Register of Shipping produced two reports that present the results of individual commercial marine emission tests.1,2  Together, these reports present test data for a total of 46 main propulsion engines and 2 auxiliary engines as summarized in Table 3-1.  Emission limits for marine engines have historically been established by engine size expressed in terms of engine rated speed, with nearly all commercial marine engines falling into the low and medium speed categories.  The Lloyd’s data are quite comprehensive, covering engines in both speed ranges, and the test program reports provide a listing of nearly all critical test data parameters, including:

- raw concentration-based emission measurements for nitrogen oxide (NO), sulfur dioxide (SO2), carbon monoxide (CO), carbon dioxide (CO2), oxygen (O2), and hydrocarbons (HC),

- test engine load, speed, and volumetric fuel consumption,

- test engine specifications,

- test fuel density and carbon, hydrogen, nitrogen, and sulfur mass fractions, and

- ambient test conditions.

Nevertheless, it is important to recognize that exhaust mass flow rates are not measured, so the conversion of measured emission concentrations to emissions mass must be based on theoretical relationships.  With the various parameters measured by Lloyd’s, it is possible to estimate emissions mass (and thus mass emission rates) through the determination of the mass of intake air required to produce the observed (i.e., measured) combustion products.  Ignoring the potential effects of exhaust non-homogeneity and emissions measurement error as well as the unaccounted influences of non-measured combustion products (e.g., particulate matter (PM) and nitrogen

dioxide (NO2)), there is only one specific mass of intake air that will produce a given quantity of combustion products for a given fuel.  This specific mass can be calculated by chemically mass

TABLE 3-1

# OVERVIEW OF THE LLOYD’S EMISSION TEST DATABASE

| Ship Types Tested | Number of Ships Tested | No. of Main Engines Tested | No. of Main Engine Tests | Average Tests per Main Engine | No. of Auxiliary Engines Tested | No. of Auxiliary Engine Tests | Average Tests per Auxiliary Engine |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Bulk Carrier | 6 | 6 | 37 | 6.2 | 0 | 0 | 0 |
| Container | 2 | 2 | 11 | 5.5 | 1 | 5 | 5.0 |
| Dredger | 6 | 6 | 32 | 5.3 | 0 | 0 | 0 |
| Roll-on/Roll-off | 9 | 16 | 90 | 5.6 | 1 | 5 | 5.0 |
| Tug | 7* | 7 | 71 | 10.1 | 0 | 0 | 0 |
| Tanker | 9 | 9 | 58 | 6.4 | 0 | 0 | 0 |
| Total Tests | 39 | 46 | 299 | 6.5 | 2 | 10 | 5.0 |

*	For tugs, testing was performed both with (38 tests) and without (33 tests) another vessel being pushed.  However, the net effect of this dual testing simply represents an increase in the number of engine loading scenarios tested for tugs.

balancing the input fuel characteristics with measured emission products (both of which are reported by Lloyd’s).  Such an approach is analogous to the carbon balance technique employed in motor vehicle emissions testing to estimate dilution air volumes in constant volume sampling (CVS) systems.

Given a complete and accurate characterization of: (1) emissions, (2) fuel, and (3) intake air, chemical mass balancing will produce an accurate determination of intake air mass.  Ignoring any measurement error, the Lloyd’s database does provide a complete characterization of the combustion fuel.  Characterization of major emission species (i.e., CO2 and O2) as well as several minor emission species is also provided.  While the widest possible scope of emission measurements is desirable for increased precision, relatively accurate mass balancing can be performed using emission measurements for CO2 and O2 alone, as these compounds account for the bulk of exhaust carbon and oxygen.  For marine engines for example, emissions of either are one to two or more orders of magnitude higher than emissions of either CO or HC.  However, no measurements of intake air characteristics are provided by Lloyd’s.  Intake air containing significant concentrations of carbon or hydrogen can significantly influence chemical mass balance accuracy.  In the absence of specific intake air characteristics, it is typical to assume an “average” air composition of 21 percent oxygen and 79 percent nitrogen (representing nitrogen plus other minor, relatively inert, air constituents).  Such a presumption was employed in all mass balance analysis performed for this study.

Several additional issues should be considered in interpreting the Lloyd’s emissions test data used in this study.  No PM testing was performed and, therefore, the Lloyd’s data are of no value in determining marine PM emission factors.  Additionally, HC measurements are missing for 26 of the 309 emission tests performed.  In instances where detailed chemical mass balancing, as described below, included measured HC, a value of zero was assumed for these 26 tests.  This assumption is expected to result in only minor precision losses for calculated intake air mass as most combustion hydrogen is emitted as water (H2O), not HC (emitted HC is typically two to three orders of magnitude lower than emitted H2O).  However, all 26 tests were excluded from the statistical analysis underlying the determination of HC emission factors.

Oxides of nitrogen (NOx) emission factors are of particular interest in this study as NOx represents a major pollutant emission species from diesel engines such as those used for marine propulsion.  However, the Lloyd’s database includes only NO measurements, omitting other NOx components such as NO2.  To estimate total NOx emissions from measured NO data, EEA relied on supplementary data presented in the text portion of the Lloyd’s report1 that summarized NO to NOx ratios for a range of marine engine emission tests conducted prior to those reported.  These tests reportedly cover a diverse range of fuels and test conditions, but the observed NO to NOx ratio, as presented in Table 3-2, varies over a relatively narrow range of 0.86 to 0.98, with a mean and standard deviation of 0.94 and 0.03 respectively.  Based on this data, EEA assumed for the purpose of this study, that emitted NOx is equal to measured NO divided by 0.94.

TABLE 3-2

LLOYD’S NO TO NOx RATIO FOR MARINE ENGINES

| Engine Type | Test Fuel | Idle | 25% Load | 50% Load | 75% Load | Rated Load |
| --- | --- | --- | --- | --- | --- | --- |
| Propeller Law | Fuel 1 | 0.93 | 0.93 | 0.95 | 0.96 | 0.96 |
|  | Fuel 2 | 0.96 | 0.89 | 0.91 | 0.93 | 0.93 |
|  | Fuel 3 | 0.91 | 0.91 | 0.92 | 0.92 | 0.96 |
|  | Fuel 4 | 0.86 | 0.87 | 0.89 | 0.92 | 0.94 |
| Constant Speed | Fuel 1 |  | 0.97 | 0.98 | 0.97 | 0.96 |
|  | Fuel 2 |  | 0.92 | 0.93 | 0.92 | 0.93 |
|  | Fuel 3 |  | 0.96 | 0.94 | 0.97 | 0.96 |
|  | Fuel 4 |  | 0.95 | 0.94 | 0.94 | 0.94 |
| Overall Average = 0.94, Standard Deviation = 0.03 |

Even though Lloyd’s reported ambient temperature, pressure, and humidity data, no ambient corrections have been applied to any of the emission estimates presented in this study.  The decision to ignore ambient corrections was based on the fact that: (1) no generally accepted correction algorithms have been developed for marine engines, (2) ambient data is not available for the USCG data that were combined with the Lloyd’s data to generate emission factors (see Section 3.3 below), and (3) the magnitude of ambient corrections are expected to be minor relative to the overall variability of the emissions data.

All emissions data for one of the tankers tested by Lloyd’s (designated as ship TK7) have been excluded from statistical emission factor analysis because exhaust O2 measurements are not reported.  Unlike HC, O2 is a major exhaust constituent and no reliable assumptions can be made regarding intake air mass (and thus exhaust and emissions mass) in the absence of reliable O2 data.  As a result, the seven emission tests conducted on tanker TK7 were excluded from the analysis database.

All Lloyd’s test data not otherwise excluded as described above have been treated with equal weight in the emission factor analysis conducted for this study.  This may result in some bias of analysis results toward engines with an above average number of associated emission tests, but there is no obvious means of weighting the data that would ensure less bias than simply treating all data with equal weight.  Lloyd’s stated test program design criteria was to conduct testing at idle and 25, 50, 75, and 100 percent of rated engine output.  Therefore, ideally, each engine would be tested five times at five distinct operating modes.  However, as indicated in Table 3-1, the number of actual tests per engine ranged from five to ten, with tug testing representing the upper bound due to testing in both “pushing” and “non-pushing” modes.

Because all testing was performed at variable load conditions, applying a weighting factor to all the test data for a given engine to equate that engine’s overall statistical influence to that of a “five test” engine can result in an unintended bias at specific loads where the weighted engine’s test data carries less influence than data from another engine, even though both represent equally valid test measurements at the given load.  An alternative approach of simply discarding all but five test data points across the load range for any given test engine is less problematic, but requires some methodology to select those data points to either retain or exclude.  Given the considerable variability in observed test data, it was concluded that the overall bias induced by simply retaining all data points was likely to be minor and thus no specific data weighting or selection/exclusion scheme was employed in this analysis.  Follow-up analysis to quantify the potential magnitude of any bias can be conducted, but is beyond the scope of this analysis.

3.3	U.S. COAST GUARD EMISSION TEST DATA

Environmental Transportation Consultants produced a report for the Volpe National Transportation Systems Center and the USCG that presents the results of marine engine emission tests on six USCG vessels.4  In total, the report presents comprehensive test data for 12 main diesel propulsion engines as summarized in Table 3-3.  Summary data are also presented for two additional gas turbine propulsion engines, but supporting detailed test data are omitted from the report necessitating the exclusion of detailed gas turbine engine analysis from this study.  In general, the USCG data are less detailed that the Lloyd’s data described in Section 3.2 above, but reported test data parameters include:

- raw concentration-based emission measurements for NOx, SO2, CO, CO2, O2, and HC,

- raw mass-based emission measurements for PM,

- test engine load, speed, and volumetric fuel consumption, and

- test engine specifications.

Data on fuel specifications, density, and composition was not included, representing the most critical omission for purposes of this study.  Data on ambient test conditions was also omitted, but this omission is a lesser concern as any ambient adjustments to emissions are expected to be minor relative to overall data variability.

As described in Section 3.2, fuel characteristics are a necessary element in constructing an accurate chemical mass balance as required to estimate intake air mass and subsequently exhaust and emissions mass.  Unfortunately, the USCG test data report only describes the combustion fuel as “diesel” and presents no supporting test data.  Therefore, EEA undertook an alternative analysis approach in an attempt to estimate the characteristics of the unknown USCG diesel “fuel” as follows.(

Using reported O2 and CO2 emission concentrations, the stoichiometric CO2 concentration for the USCG fuel was derived through regression analysis as summarized in Figure 3-1.  The derived stoichiometric CO2 concentration (15.2 percent at zero percent O2) can readily be translated through chemical mass balance to an implied fuel hydrogen to fuel carbon (H to C) ratio of 1.9127.  Such a ratio is not typical for a diesel fuel, instead being more reflective of a lighter fuel such as gasoline and implying a bias toward a slight under-measurement of CO2, O2, or both.  Although diesel fuels with H to C ratios above 1.9 have been reported, they generally represent upper bound H to C fuels and would be quite uncommon as an average fuel

# TABLE 3-3

# OVERVIEW OF THE USCG EMISSION TEST DATABASE

| Ship Types Tested | Number of Ships Tested | No. of Main Engines Tested | No. of Main Engine Tests | Average Tests per Main Engine | No. of Auxiliary Engines Tested |
| --- | --- | --- | --- | --- | --- |
| High Endurance Cutter (WHEC) | 1 | 2* | 30 | 15.0 | 0 |
| Medium Endurance Cutter (WHEC) | 2 | 4 | 60 | 15.0 | 0 |
| Patrol Boat (WPB) | 2 | 4 | 52 | 13.0 | 0 |
| Utility Boat (UTB) | 1 | 2 | 30 | 15.0 | 0 |
| Total Tests | 6 | 12* | 172 | 14.3 | 0 |

*	The report actually presents summary results for 2 WHEC diesel propulsion engines and 2 WHEC gas turbine propulsion engines, but only includes detailed test data for the two diesel engines.  This “missing” data required that the two gas turbine engines be excluded from detailed statistical emission factor analysis in this study.

characteristic over the entire USCG emissions testing program.  As a result, EEA elected to utilize the average fuel specifications for the various “diesel” fuels included in the Lloyd’s marine engine test program as a better means of approximating the average unknown fuel characteristics associated with the USCG data.  Table 3-4 presents the statistical specifications of the various Lloyd’s test fuels.  The average “all fuels” specifications were used for all USCG chemical mass balance analysis in this study.

Like the Lloyd’s data, several additional assumptions are required in processing the USCG database.  In general, however, required assumptions for the USCG data are more extensive than those associated with processing the Lloyd’s database, but inclusion of the USCG data in this study is considered to be critical for two primary reasons.  First, the USCG data serves as the only independent means of validating the basic trends observed through the Lloyd’s test data.  Second, the USCG database is the only database provided to EEA for review that includes PM

#### FIGURE 3-1

TABLE 3-4

LLOYD’S MARINE ENGINE FUEL SPECIFICATIONS

| Parameter | Gas Oil | Heavy Fuel Oil | Intermediate Fuel Oil | Light Fuel Oil | All Fuels |
| --- | --- | --- | --- | --- | --- |
| Number of Observations | 25 | 9 | 2 | 19 | 55 |
| Density | Average | 0.8553 | 0.9816 | 0.9900 | 0.9539 | 0.9149 |
|  | Standard Deviation | 0.0056 | 0.0055 | 0.0000 | 0.0297 | 0.0587 |
| Carbon Content | Average | 0.8651 | 0.8606 | 0.8580 | 0.8601 | 0.8624 |
|  | Standard Deviation | 0.0032 | 0.0078 | 0.0004 | 0.0047 | 0.0052 |
| Hydrogen Content | Average | 0.1293 | 0.1080 | 0.1042 | 0.1150 | 0.1200 |
|  | Standard Deviation | 0.0030 | 0.0024 | 0.0001 | 0.0075 | 0.0103 |
| Nitrogen Content | Average | 0.0020 | 0.0040 | 0.0019 | 0.0033 | 0.0028 |
|  | Standard Deviation | 0.0021 | 0.0024 | 0.0003 | 0.0005 | 0.0019 |
| Sulfur Content | Average | 0.0036 | 0.0274 | 0.0358 | 0.0215 | 0.0149 |
|  | Standard Deviation | 0.0021 | 0.0077 | 0.0002 | 0.0094 | 0.0125 |
| H to C Ratio | Average | 1.7812 | 1.4954 | 1.4477 | 1.5937 | 1.6576 |
|  | Standard Deviation | 0.0468 | 0.0338 | 0.0010 | 0.1029 | 0.1385 |
| N to C Ratio | Average | 0.0020 | 0.0040 | 0.0019 | 0.0033 | 0.0028 |
|  | Standard Deviation | 0.0020 | 0.0024 | 0.0003 | 0.0005 | 0.0019 |
| S to C Ratio | Average | 0.0016 | 0.0120 | 0.0156 | 0.0094 | 0.0065 |
|  | Standard Deviation | 0.0009 | 0.0034 | 0.0001 | 0.0041 | 0.0055 |

data.  Nevertheless, the following issues should be considered in evaluating the USCG marine emissions data analysis.

Many of the HC measurements included in the USCG database are questionable and five of the 172 tests are missing HC measurements altogether.  Additionally, about 17 percent of the reported HC measurements indicate concentrations below 0.001 ppmC, while nearly all of the remaining 83 percent exhibit concentrations over four orders of magnitude higher (often for the same engine at the same test conditions).  For purposes of this analysis, these concentrations were assumed to equal 0.001 ppmC, but more in depth follow-up analysis beyond the scope of this study may yield sufficient information to exclude these data as erroneous.  As was the case with the Lloyd’s data, in instances where detailed chemical mass balancing, as described below, included measured HC, a value of zero was assumed for all five tests where HC was unreported.  This assumption will result in only minor precision losses for calculated intake air mass as most combustion hydrogen is emitted as H2O, not HC.  As with the Lloyd’s data, all five tests were excluded from the statistical analysis underlying the determination of HC emission factors.  At the same time, all HC measurements reported as being below 0.001 ppmC were retained throughout the entire analysis and could serve as a downward bias on estimated HC emission factors should such measurements ultimately be identified as erroneous.

USCG HC measurements were assumed to be reported as dry since they were based on bag sampling at a point apparently downstream of a sample line water trap.  Since Lloyd’s HC measurements are report as wet, a conversion factor was applied to the USCG HC data to convert the reported data to a wet measurement equivalent.  This conversion factor was derived from analysis of the Lloyd’s test data, through which it was determined that the average wet to dry exhaust concentration ratio was 0.9658, with a standard deviation of 0.0158 (based on 1215 data points associated with 302 individual test records evaluated over four mass balance techniques plus 7 individual test records evaluated over a single mass balance technique).

In an analogous fashion, the USCG data reports NOx while the Lloyd’s data reports NO as a NOx surrogate.  As described in Section 3.2, Lloyd’s claims an average NO to NOx ratio of 0.94, a factor used by EEA to convert Lloyd’s NO data to a NOx equivalent.  This same factor was also used to convert USCG reported NOx data to an NO equivalent.

Unlike the Lloyd’s data, which was treated without weighting individual data points, the USCG data was aggregated before statistical processing.  This aggregation was necessary to address the fact that USCG data was reported individually for each of up to three tests performed on the same engine at the same load conditions.  In effect, multiple data points were reported for identical test conditions, creating an inherent weighting factor of up to three for the USCG data versus the Lloyd’s data.  To reduce the weight of the USCG data to unity, all data points applying to identical test conditions were collapsed into a single data point representative of the average reported test results for the component data.

Such an approach is generally consistent with the “average” test results for each unique set of test conditions as reported in the USCG test document.4  Nevertheless, the USCG reported average test results will vary in some circumstances from those used in this study.  This results from the fact that the average test results presented in the USCG report include the effects of partial tests, whereas those used in this study do not.  For example, in the USCG report, results for three tests, two of which include measurement of HC, CO, NOx, SO2, O2, CO2, and PM and one of which only includes measurement of HC are averaged over two tests for CO, NOx, SO2, O2, CO2, and PM and over three tests for HC.  In this study, all species are averaged over only the two comprehensive tests and the third, HC-only test is ignored.  This is deemed a more appropriate aggregation methodology since there is no way of knowing how unmeasured emission species will have varied over the third test in accordance within any observed variation in HC.  In addition, any individual tests for which inconsistent air/fuel ratios were calculated across the differing estimation methodologies described in Section 3.4 below, were also excluded from the aggregation process.

Finally, the USCG report also included specific fuel consumption estimates only for the average engine speed and output calculated for each unique set of test conditions.  Since individual test results were re-aggregated for this study in accordance with the modified “acceptance” criteria described above, it was necessary to estimate fuel consumption for each individual test, instead of simply knowing the aggregate test average.  In the absence of specific engine maps, EEA employed a simplifying assumption that fuel consumption varies linearly with engine speed for outputs “near” the specific engine output for which the USCG reported fuel consumption.  Observed engine speed variations ranged from only –3 to +4 percent of reported average engine speed so that calculated fuel consumption adjustments averaged only 0.01 percent, with a maximum adjustment of 1.1 percent.

3.4	EMISSIONS DATA ANALYSIS

As described above, exhaust mass is not a measured component of either the Lloyd’s or USCG databases.  Nevertheless, an estimate of exhaust mass is necessary to covert concentration-based emission measurements into mass-based equivalents.  To estimate exhaust flow for each emissions test included in the combined Lloyd’s/USCG database, a chemical mass balance was employed using intake fuel characteristics and measured exhaust components to estimate the effective combustion air/fuel (A/F) ratio.  This A/F ratio estimate can then be combined with fuel flow measurements reported for each emissions test to derive an estimate for intake air mass, that when added to intake fuel mass results in the required estimate of exhaust mass.  In referring to intake air, it is worth noting that this includes both intake and scavenge air (as applicable, typically for two stroke engines) and that the estimated A/F ratio is the effective mass ratio of all air (regardless of the timing or location of its injection into the flow stream) to combustion fuel.  While it is not possible to separate actual intake air from scavenge air based on exhaust measurements alone, such a separation is not required to estimate total exhaust mass, which is the critical analysis parameter for this study.

Figure 3-2 presents a summary of the A/F ratios calculated on the basis of Lloyd’s and USCG reported exhaust components.  Based on the calculated ratios, EEA has some concern over the integrity of the reported emissions data.  This concern stems primarily from the magnitudes of the calculated A/F ratios over the entire engine load range, defined by EEA as the “fractional load” or the ratio of the reported engine output during the emissions test to the reported rated engine output.  Even at 100 percent rated load, the Lloyd’s database generally implies A/F ratios between 30:1 and 40:1.  This is substantially higher than the 20:1 or so A/F ratios that would be expected from previous experience with on-road diesel engines.  Moreover, while calculated A/F ratios approaching 80:1 are not unexpected at low load ranges, values of 1000:1 or, in one case, 4000:1 are certainly cause for concern.  As noted above, scavenge airflow for two stroke engines could explain some of the excessive A/F ratios, but the generally apparent over-prediction is observed for both two and four stroke engines.  Since EEA has no information on the number of engines employing secondary air scavenging or the mass of air flow associated with such

#### FIGURE 3-2

systems on marine engines, it is not possible to elaborate further (for this study) as to the role that secondary scavenging systems may have on apparent A/F ratio over-prediction.

In an attempt to isolate those data that are most highly suspect, EEA undertook a series of alternative chemical mass balance approaches to estimating effective A/F ratio.  The first approach, designated for this study as the simple carbon balance approach, estimates A/F ratio on the basis of fuel H to C ratio and exhaust O2 to CO2 ratio alone.  Without presenting the detailed mass balance derivation here, this method presumes that all intake fuel and air is fully represented in the exhaust as CO2, H2O, and unreacted air (represented as 21 percent O2 and 79 percent molecular nitrogen (N2)).  Furthermore, this method represents a commonly employed mass balance approach in that it accounts for major exhaust constituents, providing a reasonably reliable A/F ratio estimate.  However, in instances where exhaust constituents may not be measured accurately, there are more detailed alternative chemical mass balance methods that can be employed for validation purposes.

A more detailed carbon balance approach considers all measured exhaust constituents that contain either carbon or hydrogen (HC, CO, and CO2 in the database available for this study).  This approach can provide a considerably more accurate A/F ratio estimate when significant concentrations of either CO or HC are measured.  A third A/F ratio estimation approach employing a detailed oxygen (rather than carbon) balance considers all measured oxygen, nitrogen, and hydrogen containing exhaust species (CO, CO2, O2, NO, SO2, and HC in the database available for this study).  Finally, a fourth A/F ratio estimation approach based solely on the amount of intake air required to completely combust the intake fuel and provide the measured quantity of “excess air” in the exhaust was also employed.  This excess air approach uses only measured exhaust oxygen and measured fuel characteristics to satisfy the required chemical mass balance criteria.

Figures 3-3 through 3-5 present the results of the alternative A/F ratio evaluations.  The three figures each present a plot of the estimated A/F ratio for one of the three alternative mass balance methods employed in this study versus the A/F ratio estimated using the simple carbon balance approach.  The considerable variation between three of the four approaches is easily observed.  As might be expected, the simple carbon balance and detailed carbon balance approaches produce similar A/F estimates since both principally rely on a balance of intake and exhaust carbon.  The excess air approach, which relies on the major exhaust oxygen containing component (i.e., air) as its primary mass balance criteria indicates significant deviation from the carbon-based approaches, but the greatest deviation is observed for the detailed oxygen balance, which relies on all exhaust oxygen containing compounds as its mass balance criteria.  Moreover, the disagreement between the four approaches gets more pronounced as the estimated A/F ratio increases, with the oxygen-based approaches generally estimating lower A/F ratios than the carbon-based approaches.  Given that exhaust mass and thus emissions mass are directly dependent on A/F ratio, there are clear concerns associated with the raw exhaust measurements reported in the marine engine database employed in this study.

Further evidence of the potential problems with the marine engine emissions databases can be observed by comparing measured CO2 and O2 concentrations.  Figure 3-6 presents such a comparison, where the dashed lines represent the theoretical relationship between measured CO2 and O2 as implied by the measured characteristics of the Lloyd’s test fuels.  Deviations from these theoretical relationships are indicative of instances in which measurement error for either CO2, O2, or both are likely.  Clearly, such deviations are quite common at low CO2 concentrations, which correspond to high O2 and thus high A/F ratios.  More troubling, however, is the fact that significant deviations are observed across the full measured CO2 spectrum.

Given the concerns associated with the reported exhaust emissions data, it would be advantageous to perform a more in depth analysis of the test programs underlying the reported data.  However, such an analysis is beyond the scope of this study.  As an alternative, EEA quantified the magnitude of the variation between the alternative A/F ratio estimation methodologies and retained for statistical analysis, only those tests for which consistent A/F ratios were observed across the alternative estimation approaches.  For this study, consistent A/F ratios were defined as instances in which: (1) three of the four employed A/F ratio estimation

#### FIGURE 3-3

#### FIGURE 3-4

#### FIGURE 3-5

#### FIGURE 3-6

methodologies produced cumulative absolute estimate deviations of no more than 15 percent relative to the estimate produced by the simple carbon balance approach and (2) none of the three otherwise consistent A/F ratio estimates varied by more than 10 percent from the estimate produced by the simple carbon balance approach.  The choice of these retention criteria are somewhat arbitrary, but deviations of this magnitude yield reasonably consistent mass emissions estimates, well within the overall uncertainty of the underlying test programs.

All figures presented in this section allow inspection of both consistent and inconsistent A/F ratio test data.  Mass emission estimates presented in these figures and used for subsequent emission factor analysis represent the arithmetic average of the mass emission rates associated with the three most consistent A/F ratio estimation methodologies: the simple carbon balance, the detailed carbon balance, and the excess air approaches.  Figure 3-7 presents a distribution of the cumulative absolute deviations associated with these same three A/F ratio estimation approaches for the combined Lloyd’s and USCG database.  As can be noted, approximately 18 percent of all reported emission tests do not meet the consistent A/F ratio criteria.  Such records are excluded from all emission factor analysis in this study but have been included on all figures to allow the reader to evaluate the potential impact associated with this exclusion.

3.5	EMISSION FACTOR DEVELOPMENT

Based on the database development and acceptance criteria presented in the preceding sections, EEA compiled an overall emission factor analysis database consisting of 291 “consistent A/F ratio” emission tests spanning the full range of engine operating loads (i.e., from idle to 100 percent rated output).  Figure 3-8 summarizes the overall test engine and operating loads represented in this database.  As indicated, the bulk of the large engines tested by Lloyd’s fail to meet the A/F ratio acceptance criteria, so that the overall database includes only a modest number of tests on engines rated above 10,000 kilowatts (kW).  Given the under-representation of large marine engines in this database, further investigation of large engine performance relative to both emissions measurement accuracy and consistency with the emission factor algorithms presented below is recommended.

#### FIGURE 3-7

#### FIGURE 3-8

Figures 3-9 through 3-15 present measured (i.e., concentration-based) emissions by fractional engine load for each of the emission species represented in the analysis database.  Although overall measurements for most species span several orders of magnitude, clear trends are observable for all species except CO, HC, and SO2.  The lack of a distinguishable trend in the raw CO and HC data is likely the result of the relatively low production of both species across the entire load range of diesel engines.  The lack of a load-based trend for SO2 is due to the direct relationship of SO2 emissions to fuel sulfur content, which varies considerably across the emission test database.

Figures 3-16 and 3-17 present reported fuel consumption by absolute and fractional test load respectively.  As indicated, the distribution of reported fuel consumption over fractional load space is quite “well behaved.”  Regression analysis indicates that fuel consumption is inversely related to fractional engine load as follows:

Fuel Consumption (g/kW-hr) = 14.1205 (1/Fractional Load) + 205.7169

(t = 22.75)	(t = 32.88)

[r2 = 0.64, F = 518, Observations = 291]

Based on this behavior, along with the previously illustrated (see Figure 3-2) well defined behavior of A/F ratio (and thus exhaust mass) with fractional load, statistical regression structures based on emissions mass by fractional load were investigated as the most promising basis for emission factor algorithms.  It is worth noting that previous studies have investigated emission mass in terms of fuel consumption alone and while such an approach may yield reasonable emission estimates, fuel consumption is itself dependent on fractional load as illustrated in Figure 3-17 and, therefore, is not an appropriate independent regression parameter in instances where fuel consumption is not measured directly (with the exception of SO2 emissions, which are directly dependent on highly variable fuel sulfur content).  While a two step conversion from fractional load to fuel consumption to emissions mass is certainly feasible, the combined uncertainty associated with such a process is surely larger than the single step estimation of emissions mass from a given fractional load.

#### FIGURE 3-9

#### FIGURE 3-10

#### FIGURE 3-11

#### FIGURE 3-12

#### FIGURE 3-13

#### FIGURE 3-14

#### FIGURE 3-15

#### FIGURE 3-16

#### FIGURE 3-17

Figures 3-18 through 3-26 summarize work-specific mass emission rates by species based on the chemical mass balance of parameters reported in the combined Lloyd’s and USCG database.  In general, all species display an inverse exponential distribution with fractional load.  Although the behavior of the work-specific emission rate data is at least as good as expected given the wide range of engines tested, an expected upturn in the work-specific emission rate for NOx at high fractional loads is not readily apparent.  Nevertheless, to check for the potential existence of such a trend, both full and partial load range regression structures were evaluated.

To confirm the validity of an inverse exponential relationship between mass emissions and fractional load as opposed to a simple linear relation, EEA regressed the emissions/load data over both linear and inverse exponential structures.  In all cases, excepting SO2 as discussed below, the inverse exponential relations exhibited substantially better statistics (i.e., higher correlation coefficients and more significant regression parameter statistics).  Restricted load range regressions evaluated to determine whether the inverse exponential relations were most appropriate over the entire fractional load range or whether specific fractional load ranges were better represented with alternative linear algorithms, revealed similar results.  Specifically, separate regressions over the 0-20 percent and 20-100 percent fractional load ranges were constructed to determine if a better inverse exponential fit over the lower load range or an alternative linear fit over the upper load range might be more appropriate than an inverse exponential fit over the full fractional load range.  For all emission species (again excepting SO2), it was evident that the best statistical fit of the reported emissions data was obtained with the inverse exponential relations over the full fractional load range.  In no case did any linear relation over the full or upper load range (20-100 percent) yield better statistics.  After determining the superiority of the inverse exponential approach, the most appropriate values for the fractional load exponents were evaluated, although all regressions yielded surprisingly good fits for an initially evaluated exponent of negative unity.  Alternative exponent value regressions were selected as the basis for the best fit regression only in cases where such values produced significantly improved statistics relative to a unity exponent.  Table 3-5 presents the results of this regression analysis for each emission species evaluated.

#### FIGURE 3-18

#### FIGURE 3-19

#### FIGURE 3-20

#### FIGURE 3-21

#### FIGURE 3-22

#### FIGURE 3-23

#### FIGURE 3-24

#### FIGURE 3-25

#### FIGURE 3-26

# TABLE 3-5

# MARINE ENGINE EMISSION FACTOR ALGORITHMS

| Statistical Parameter | PM | NO | NOx | NO2 | SO2 | CO | CO2 | O2 | HC | Dry Exhaust | H2O | Wet Exhaust |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Exponent (x) | 1.5 | 1.5 | 1.5 | 1.5 | n/a | 1 | 1 | 1.5 | 1.5 | 1.5 | 1 | 1.5 |
| Intercept (b) | 0.2551 | 9.5181 | 10.4496 | 15.5247 | -0.4792 | 0.1548 | 648.6 | 1298.1 | 0.3859 | 8982 | 220.09 | 9243 |
| Intercept t-stat | 7.780 | 24.154 | 24.154 | 24.154 | -1.124 | 0.323 | 33.957 | 4.101 | 1.429 | 6.390 | 29.806 | 6.557 |
| Significant intercept t? | Yes | Yes | Yes | Yes | No | No | Yes | Yes | No | Yes | Yes | Yes |
| Coefficient (a) | 0.0059 | 0.1146 | 0.1255 | 0.1865 | 2.3735 | 0.8378 | 44.1 | 107.9 | 0.0667 | 489 | 15.92 | 491 |
| Coefficient t-stat | 23.143 | 19.391 | 19.391 | 19.391 | 28.924 | 17.700 | 23.374 | 22.769 | 17.064 | 23.239 | 21.839 | 23.271 |
| Significant coefficient t? | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| r2 | .95 | .57 | .57 | .57 | .78 | .52 | .65 | .64 | .52 | .65 | .62 | .65 |
| F-stat | 536 | 376 | 376 | 376 | 837 | 313 | 546 | 512 | 291 | 540 | 477 | 541 |
| Significant F-stat? | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |
| Observations | 31 | 291 | 291 | 291 | 239 | 291 | 291 | 291 | 271 | 291 | 291 | 291 |

1. All regressions but SO2 are in the form of:  Emission Rate (g/kW-hr) = a (Fractional Load)-x + b

2. Fractional load is equal to actual engine output divided by rated engine output.

3. The SO2 regression is in the form of:  Emission Rate (g/kW-hr) = a (Fuel Sulfur Flow in g/kW-hr) + b

SO2, due to its obvious dependence on fuel sulfur content,( is treated in a different fashion than the remainder of the emission species.  Theoretically, work-specific SO2 emissions should approach two times work-specific fuel sulfur consumption (i.e., the ratio of the molecular weight of SO2 to elemental sulfur is 64.0628/32.064, or 1.998), depending on the relative insignificance of other sulfur sources (e.g., sulfur compounds in intake air) and sinks (e.g., sulfate emissions).  Since a direct linear relationship (with a zero intercept and a coefficient of about two) should be evidenced, such a regression structure was evaluated for SO2 in lieu of the load-based regression structures described above for other emission species.

The resulting regression statistics are presented in Table 3-5, where it is evident that the proper zero intercept was derived, but that the derived fuel sulfur coefficient (2.37) is about 20 percent too high.  While this lends further support to an overestimation bias in the implied effective A/F ratio of the underlying emission test data (i.e., A/F overestimation implies exhaust mass overestimation, thereby implying emission species overestimation) and further investigation into this phenomenon is recommended, it is not possible within the time or resource constraints of this study to elaborate further.  Certainly, a 20 percent error in emissions estimates in not unreasonable given the overall variability of emission rates across engines.  Nevertheless, the apparent overestimation of SO2 implies a directional bias that should be addressed.  In the interim, EEA recommends using the theoretical coefficient for SO2 production (i.e., 1.998) in place of that presented in Table 3-5.

It is also important to note that statistics presented for NO2 do not represent direct nitrogen dioxide emissions, but rather the NO2 equivalent mass of emitted NOx.  In effect, NO2 emission rates reflect the net emission rate of NOx assuming all NOx is converted to NO2 (through oxidation from a source not accounted for in the intake/exhaust stream, such as post-exhaust atmospheric oxidation).  This emission rate was produced as requested by the EPA, but should be recognized as the maximum potential post-exhaust contribution to atmospheric NO2 and not an indication of directly emitted NO2.

Statistics associated with each of the various regression structures evaluated by EEA are presented in Appendix A.  This includes both the full and partial load range regression structures evaluated as well as separate regressions for: (1) all database records and (2) only those database records satisfying the A/F ratio acceptance criteria discussed above.  The improvement in regression statistics for consistent A/F ratio records (designated in Appendix A as the “Yes Data” regressions under the column labeled “A/F Criteria”) relative to those of the “All Data” regressions across emission species is obvious and further illustrates the need to address any remaining uncertainty in A/F ratios (and thus exhaust and emission species mass) to minimize emission factor uncertainty.

The regression statistics presented in Table 3-5 apply to the aggregate emissions test database and do not distinguish between the various engine types (e.g., two stroke versus four stoke) or diesel fuels (e.g., distillate, light residual, etc.) encountered in marine vessel operations.  Study time and resource constraints as well as underlying test program structure prohibit an in-depth evaluation of whether a finer resolution of marine vessel emission rates is appropriate.  For example, more two stroke engine data for which consistent A/F ratio estimates can be developed, more larger engine emission data in general, more data using less common fuels, and data collected from the same engine while operating on different fuels is critical to isolating and quantifying distinctions between any or all of these elements.  Given the current size and construction of the underlying emissions test database, it is not possible to separate simple engine-to-engine variability from potential engine or fuel type influences.

Nevertheless, to investigate the potential for such distinctions and provide an indication of the need for further database enhancement, regression statistics for both two versus four stroke engines and the various fuel types identified in the Lloyd’s database were generated.  Regression statistics for these various data sets are included in Appendix A.  Figures A-1 through A-11 plot all consistent A/F ratio test data by engine type and emission species, while Figures A-12 through A-21 plot the same data by test fuel type.(

A review of Figures A-1 through A-21 and the regression statistics presented in Appendix A reveals that it is certainly possible that both engine configuration and fuel type could be significant influences on marine engine emission rates for one or more emission species.  Unfortunately, it is not possible given existing database structure and available time and resource constraints to determine whether the apparent influences are attributable to simple variability across engines or to specific engine or fuel characteristics.  However, it is also apparent that the scatter for most, if not all, of the separated engine type and fuel specific data is sufficiently wide to support the general usage of the regression statistics presented in Table 3-5 until such time as supplemental test data can be collected and supporting analysis performed.  Nevertheless, EEA certainly recommends that such evaluation be performed as soon as possible to validate the general applicability of the presented regressions.

An initial investigation of the dependence of exhaust NOx on fuel nitrogen content was also conducted.  As shown in Figures 3-27 through 3-29, the scatter of estimated NOx emissions at any given fuel nitrogen content is considerably wider than any trend in NOx with increasing fuel nitrogen content.  In fact, the only trend across fuel nitrogen content appears to be flat.  Given the overwhelming significance of intake air nitrogen on overall NOx formation, such a trend is not surprising.

Lastly, all presented emission factors and emission factor analysis in this study apply solely to marine internal combustion engines operating on diesel fuel (either distillate or residual).  Moreover, no distinction has been made between main propulsion engines and auxiliary engines.  This lack of distinction is based on two major factors, one technical and one logistical.  Technically, no significant differences are expected between the emission profiles of marine engines used for propulsion versus auxiliary operations as the same engine makes and models are

used to satisfy both applications.  Logistically, the entire marine engine database used for this study contains test data for only two auxiliary engines, prohibiting any detailed independent assessment of auxiliary engines alone.  Similarly, no emissions data for steam engines was provided to EEA for review.  For gas turbines, EPA provided a summary data sheet for only a single oil tanker engine tested at two loads,11 while the USCG report4 cites summary test results for two additional gas turbines, but provides no supporting data such as that included for all diesel engines tested.  Therefore, the ability to develop detailed emission factors for gas turbines is also quite limited.

Table 3-6 and Figure 3-30 summarize the available gas turbine emissions data and present several arithmetic averages of reported mass emission rate data.  Regressions were not performed over the full load range of these turbines as no emissions rate data was provided at loads below about 50 percent of rated output.  While both NOx and CO may exhibit trends (NOx increasing with load, CO decreasing with load), there simply is no data available to indicate whether these trends hold true over the lower load ranges and, if so, what the general shape of the emissions curve might be.  Therefore, at this time, the use of simple arithmetic averages over the entire range of test data or at each individual test data load point (50, 75, and 100 percent of rated output) represents the only viable emission factor estimation technique.  The resulting emission factors for either approach are presented in Table 3-6.  With appropriate qualifications given the gas turbine database size, gas turbine emissions would, in general, appear to be about half those of diesel marine engines for NOx and similar to diesel marine engine emissions for HC, CO, and PM.

#### FIGURE 3-27

#### FIGURE 3-28

#### FIGURE 3-29

# TABLE 3-6

# MARINE GAS TURBINE EMISSION RATE DATA

| Parameter | Chevron "Louisiana" | USCG "Sherman" | Overall Average | 50% Load Average | 75% Load Average | Full Load Average |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Starboard | Port |  |  |  |  |
| Test Load (mW) | 6.30 | 4.60 | 13.42 | 9.84 | 6.71 | 13.42 | 9.84 | 6.71 |  |
| Rated Load (mW) | 8.05 | 8.05 | 13.42 | 13.42 | 13.42 | 13.42 | 13.42 | 13.42 |  |
| Fractional Load | 0.78 | 0.57 | 1.00 | 0.73 | 0.50 | 1.00 | 0.73 | 0.50 |  |
| Reported Emission Rate (pounds per hour) |  |
| PM | 2.21 | 4.31 |  |  |  |  |  |  |  |
| SO2 | 12.35 | 12.64 | 10.50 | 3.87 | 4.10 | 8.54 | 2.89 | 3.68 |  |
| NOx | 62.50 | 33.60 | 177.00 | 80.40 | 50.60 | 205.00 | 87.10 | 53.60 |  |
| CO | -1.17 | 0.31 | 2.98 | 27.40 | 39.50 | 31.60 | 26.90 | 43.50 |  |
| HC |  |  | 2.67 | 16.00 | 3.41 | 0.50 | 7.23 | 1.47 |  |
| Reported Emission Rate (g/kW-hr) |  |
| PM | 0.16 | 0.42 |  |  |  |  |  |  | 0.29 | 0.42 | 0.16 |  |
| SO2 | 0.89 | 1.25 | 0.35 | 0.18 | 0.28 | 0.29 | 0.13 | 0.25 | 0.45 | 0.59 | 0.40 | 0.32 |
| NOx | 4.50 | 3.31 | 5.98 | 3.71 | 3.42 | 6.93 | 4.01 | 3.62 | 4.44 | 3.45 | 4.07 | 6.45 |
| CO | -0.08 | 0.03 | 0.10 | 1.26 | 2.67 | 1.07 | 1.24 | 2.94 | 1.15 | 1.88 | 0.81 | 0.58 |
| HC |  |  | 0.09 | 0.74 | 0.23 | 0.02 | 0.33 | 0.10 | 0.25 | 0.16 | 0.54 | 0.05 |

#### FIGURE 3-30

4.  MARINE VESSEL CLASSIFICATIONS AND POWER RATINGS

4.1	CLASSIFICATIONS EMPLOYED IN LITERATURE

Three of the reports provided by EPA had utilized specific classifications of marine vessels that varied both in detail and grouping, and these groupings are reviewed below.

The 1991 report by Booz-Allen9 categorizes oceangoing vessels into four types:

- container ships;

- tankers and bulk carriers;

- general cargo/vehicle carriers/RORO/and ocean-going tugs; and

- passenger liners and cruise ships.

Each particular category is then divided into weight classes in 25,000 ton deadweight ton (DWT) steps (0 to 25, 25 to 50, etc) and an average horsepower is associated with each weight class for every ship type.  However, the horsepower data is identical across all ship types, except for tankers and bulk carriers.  The report also identifies horsepower for tankers and bulk carriers as being higher than the horsepower (see Table 4-1) for other types within each weight class.  The Booz-Allen data is potentially incorrect, since tankers and bulk carriers cruise relatively slowly (their cargo is not perishable or high cost), and typically have the lowest horsepower for a given deadweight.

The Acurex report10 for SCAQMD also has a categorization scheme by deadweight and ship type.  The analysis relied on data from Lloyds, from the ships visiting San Pedro Bay.  Acurex classified ships by type and ‘design category’ where:

Design Category = (DWT)0.667 * (Service Speed)3/104

TABLE 4-1

BOOZ-ALLEN CLASSIFICATION OF VESSELS

| Type | DWT (x1000) Range | Horsepower |
| --- | --- | --- |
| (1) Tankers & Bulk Carriers | 0-25 | 16862 |
|  | 25-50 | 35742 |
|  | 50-75 | 59342 |
|  | 75-100 | 80582 |
|  | 100+ | 104182 |
| (2) All Others* | 0-25 | 8560 |
|  | 25-50 | 11920 |
|  | 50-75 | 16120 |
|  | 75-100 | 19900 |
|  | 100+ | 24100 |

*	Booz-Allen has three categories for vessels: (a) container ships, (b) general cargo/vehicle carriers/RORO/ ocean-going tugs, and (c) passenger and cruise ships.  However, all use the same HP to DWT relationship.

This equation is based on the well-known relationship between power to overcome drag, which varies as the surface area in the water and the cube of speed.  From the Lloyds registration data, Acurex developed eight ship type categories namely:

- auto carriers;

- bulk carriers;

- container ships;

- general cargo ships;

- passenger ships;

- refrigerated cargo (reefer) ships;

- ‘roll-on, roll-off,’ or RORO; and

- tankers.

Each of the eight ship types is then further subdivided into design categories (up to eight) in step of 200.  These classifications are provided in Appendix C.  However, it is not clear how many ships were available in the sample for each combination of design category and ship type.  An examination of the data suggests significant sample variation since, in several instances, horsepower declines with increasing design category range.  The Acurex analysis showed that the design category approach reduced the dispersion in horsepower within a ship type, but also showed the dispersion reduction relative to using deadweight as an indicator was not large.  In addition, these are large variations in the percentage increase in horsepower for every 200 step in design category range, indicating significant unexplained variation in horsepower.

The Arcadis (1999) report8 for the EPA utilizes the same ship types as the Acurex study cited above, but also provided cruise speeds by ship type.  Bulk carriers, tankers and general cargo ships had cruise speeds in the range of 15 to 16 knots, while reefers, RORO and container ships had speeds of 20 to 22 knots.  Auto carriers had an average speed of 18.3 knots while passenger liner had an average speed of 19.9 knots.  These estimates appear reasonable except for passenger liners, where the relatively low average speed may have been influenced by the sample selected; many passenger liners have speeds of 30 knots or higher.  In addition, the Arcadis report stated that there was considerable dispersion of speeds within ship type, but a majority of ships were within ( 2 knots of the averages cited.  This would suggest that bulk carriers and tankers would have similar relationships between deadweight and horsepower, while reefers, container ships and RORO may also have similar relationships.

Non-oceangoing vessels are typically more simply classified by type and horsepower.  The Booz-Allen report classifies these vessels into the following:

- fishing vessels;

- tugs;

- passenger ferries;

- dredging and construction ships;

- work/crew boats.

The Acurex report uses a virtually identical classification for non-oceangoing vessels as the Booz-Allen classification, but further groups all vessels except for tugs and fishing vessels into a single category called ‘other’ for emission estimation.

4.2	OPERATING MODE CLASSIFICATIONS IN LITERATURE

In general, ocean-going ships approach a port area at cruise speed, but reduce speed when they are positioned within a few miles of the port (known as a precautionary area) to a speed of about 10 to 12 knots.  Much closer to the docking area (about one mile), the ships slow to about five knots and, assisted by tugboats, maneuver into the harbor and dock at the pier.  Once at the pier, only the auxiliary engines are used to provide electrical and accessory power, in a mode called “hoteling.”  The literature reviewed uniformly cites these four modes, through not all four modes are used in all reports reviewed.

The Booz-Allen report cites these four modes, called full, half, slow and moored.  The power ratings, as a function of rated maximum power are 80, 40, 10, and zero for the four modes respectively with regard to main engines.  It was also assumed that for all ocean-going vessels, the auxiliary power engines were operated at 500 kW.  For harbor and fishing vessels, three modes are utilized: full at 80 percent power, cruise at 50 percent power and slow at 20 percent power.  No hoteling emissions appear to be included from these classes of vessels.

The Acurex report assumed that at cruise, engines are operated at 80 percent of the maximum continuous rating (MCR).  Slow cruise was estimated as 12 knots, and the percent of power required was calculated based on the cube of the ratio of 12 knots to actual cruise speed.  Hence, the percent of power used varies according to ship type, since for example, RORO and container ship cruse much faster than bulk carriers and tankers.  As a result, the percent of power used varies from a little as 14 percent of MCR for container ships to 40 percent of MCR for bulk carriers.  For maneuvering, container ships were estimated to use only 10 percent of MCR, while at the other extreme, bulk carriers were assumed to use 20 percent of MCR, based on ‘engineering judgement.”

The Acurex report also attempted to estimate auxiliary power loads under all modes including hoteling.  A survey based method was used, but no good relationships were found between auxiliary loads and ship size or weight.  Acurex recommend the following auxiliary power loads independent of ship type (except for passenger ships) or weight:

- slow/fast cruise	-	750 kW

- maneuvering	-	1250 kW

- hoteling	-	1000 kW

For passenger ships only, auxiliary power loads of 5000 kW were estimated under all conditions.

Acurex did not develop mode specific emission rates for harbor and fishing vessels, but simply used annual fuel consumption average per horsepower to estimate emissions for tugs.  Harbor vessel activity was characterized at three modes representing 80, 50, and 20 percent of MCR.  Fishing vessel activity was characterized at 80 and 25 percent of MCR and at idle.  (Fishing vessels do not have large “hoteling” loads).

The newer Arcadis report8 does not vary significantly in its assessment of loads and operating modes relative to the Acurex report.  Table 4-2 shows the loads by vessel type and mode for ocean going vessels, as provided in this report.

The Environment Canada report6 also cites four modes, but does not have specific values for percent of power used by ship type on these modes.

4.3	ANALYSIS OF SHIP TYPE AND WEIGHT CATEGORIES

Under this work assignment, EPA provided a data base on ships operating at the West Coast that contained information on ship type, weight, cruise speed and engine horsepower, obtained from Lloyds.  The database was similar in content to the one used by Arcadis in earlier analyses, and has been provided to Arcadis for some current (ongoing) analyses.

While the date base contained about 5000 records, it included some data with incomplete records for ship horsepower, type or weight.  It also included data on non-oceangoing vessels such as tugs, construction vessels and fishing vessels. Oceangoing vessels were classified in the scheme cited in the Acurex report and included eight broad classifications by ship type as listed in Section 4-1.  The total sample of oceangoing ships with all necessary data was about 4100 vessels.

Ideally, rated horsepower would be more closely related to the maximum loaded weight of the ship (i.e., empty weight + payload) but data on empty weight was not available for a large fraction of the data records, and only deadweight (DWT) data is constantly available.  EEA attempted two sets of regressions that link horsepower to ship characteristics.  The first is between horsepower and DWT by ship type for each of the eight types.  The second has horsepower as the independent variable and uses (DWT)0.667 and (speed)3 as the independent variables.  In addition, a regression across all ship types was performed using both regression specifications.

TABLE 4-2

ENGINE LOADS BY SHIP TYPE FOR EACH OPERATING MODE

| Ship Type | Cruise | Slow Cruise | Maneuvering |
| --- | --- | --- | --- |
| Auto Carrier | 80 | 20 | 15 |
| Bulk Carrier | 80 | 40 | 20 |
| Container | 80 | 10 | 10 |
| General Cargo | 80 | 35 | 20 |
| Passenger | 80 | 20 | 15 |
| Reefer | 80 | 20 | 15 |
| RORO | 80 | 15 | 10 |
| Tanker | 80 | 40 | 20 |

Source:  Reference 8.

Table 4-3 shows the regressions for the eight types and across all ship types using (DWT) as the independent variable.  The regression has poor explanatory power when all ship types are combined, but has reasonable explanatory power when each ship type is considered separately.  Most of the regressions by ship type have r2 values in excess of 0.55.

Table 4-4 shows the regressions for the same ship types when (DWT)0.667 and (speed)3 are the independent variables. These regressions have better explanatory power than the regressions using DWT alone, but the improvements are not very large, except for the case when all ship types are considered as one group.  This is consistent with the observation that cruise speeds within a ship type do not vary much, but vary significantly across ship types.

Our contacts with a few ports established that its is easier to obtain information on a ship’s deadweight tonnage that to obtain cruise speed or horsepower (which would require purchase of Lloyd’s data).  Hence, the use of the (DWT) based regressions may be preferable to determine horsepower.  In examining the regression and the related scatter plots (not included in this report), it was obvious that certain ship type categories could be combined

The regression coefficient for bulk carriers and tankers are very similar, and Arcadis also reports a very similar top speed, so that combining these categories is appropriate.  In addition, Table 4-4 also shows that the DWT coefficient for auto carriers, RORO, container ship and reefers are quite similar (between 15 and 20) and could be combined.  Plots of horsepower against (DWT) for these ship types show that RORO reefers and auto carriers are distributed in the 5000 to 20,000 ton DWT range while most of the container ships are the 20,000 to 70,000 ton DWT range.  Because of their relatively high horsepower to weight ratio in comparison to general cargo ships and tankers, and because of the fact that the sample size for these ship types was (individually) only about 100 to 160, they were combined with container ships.  Regression coefficients for the combined categories are shown in Table 4-5.

TABLE 4-3

RESULTS OF REGRESSIONS BETWEEN HORSEPOWER

## AND DEADWEIGHT TONNAGE

| SHIP TYPE | INTERCEPT | DWT COEFF | R-SQUARE |
| --- | --- | --- | --- |
| ALL ( N= 4103 ) | 9070 (42.05 ) | 0.1097 (26.01) | 0.14 |
| AUTO CARRIER ( N= 157 ) | 7602 (7.33) | 0.4172 (5.75) | 0.176 |
| BULK CARRIER (N= 1644) | 6726 (54.54) | 0.0985 (26.01) | 0.55 |
| CONTAINER (N=489) | -749.4 (-0.61) | 0.800 (26.29) | 0.59 |
| GENERAL CARGO (N=641) | 3046 (15.67) | 0.288 (28.43) | 0.56 |
| PASSENGER (N= 40) | -4877 (-1.24) | 6.81 (9.97) | 0.72 |
| REEFER (N=160) | 1364 (2.23) | 1.007 (14.93) | 0.58 |
| RORO (N= 110) | 4358 (6.70) | 0.5364 (18.34) | 0.76 |
| TANKER (N=861) | 6579 (34.61) | 0.1083 (41.16) | 0.66 |

T-statistics in parentheses under coefficients.

TABLE 4-4

## REGRESSIONS OF HORSE POWER vs DEADWEIGHT AND CRUISE SPEED

| SHIP TYPE | INTERCEPT | DWT COEFF | SPEED COEFF | R-SQUARED |
| --- | --- | --- | --- | --- |
| ALL ( N= 4103) | -4585 (23.18) | 6.711 (51.95) | 2.662 (92.66) | 0.73 |
| AUTOCARRIER ( N=157) | 2956 (1.947) | 14.41 (5.788) | 0.381 (3.38) | 0.25 |
| BULK CARRIER ( N=1644) | 1586 (6.514) | 5.901 (48.55) | 0.791 (13.11) | 0.61 |
| CONTAINER ( N=489) | -13924 (-10.36) | 20.06 (12.60) | 2.342 (16.63) | 0.73 |
| GENERAL CARGO (N=839) | -1307 (-7.73) | 8.819 (34.94) | 1.202 (34.84) | 0.80 |
| PASSENGER ( N= 40) | -25305 (-4.43) | 118.45 (5.228) | 2,612 (3.498) | 0.73 |
| REEFER ( N= 160) | -2357 (-3.68) | 17.00 (8.749) | 0.861 (10.98) | 0.77 |
| RORO ( N= 110) | -3664 (-5.02) | 16.18 (15.68) | 1.386 (9.040) | 0.88 |
| TANKER ( N= 861) | 156.6 (0.544) | 6.271 (49.32) | 1.291 (16.40) | 0.78 |

T-statistics in parentheses.  Equation uses (DWT)0.667 and (SPEED)3 as independent variables.

TABLE 4-5

RECCOMENDED SHIP TYPES AND REGRESSIONS

OF HORESEPOWER TO DEADWEIGHT

| SHIP TYPE | INTERCEPT | DWT COEFF. | R-SQUARE |
| --- | --- | --- | --- |
| BULK CARRIERS +TANKERS (N=2505) | 9070 (48.52) | 0.101 (49.55) | 0.67 |
| PASSENGER (N= 40) | -4877 (-1.24) | 6.81 (9.97) | 0.72 |
| GENERAL CARGO (N= 641) | 3046 (15.67) | 0.288 (28.43) | 0.56 |
| CONTAINER/RORO AUTO CARRIER/REEFER (N= 917) | 2581 (5.50) | 0.719 (47.27) | 0.71 |

T-statistics in parentheses under coefficients.

Passenger ships posed a dilemma since there are only 40 ships in the database.  The regression show extremely high horsepower per DWT, and it implies that a 15,000 DWT ship would have engines whose output is about 100,000 HP.  In contrast, the Arcadis report estimates a similar ship would have engines rated at 33,000 HP.  It should be noted that the passenger ships in the Arcadis report had relatively low top speeds of about 20 knots.  If typical speeds are closer to 30 knots, the cubic relationship with speed would explain the differences in horsepower, since (30/20)3 is 3.375, i.e., passenger ships capable of 30 knots cruise would require 3.375 times the power of ships capable of 20 knot cruise.  Nevertheless, the regressions should be treated with caution because of the very small sample.

No independent data on the possible modes of operation and load factors was received. The Arcadis report utilizing estimates of load factor derived from speeds appears more defensible than using constant load factors across ship types for each mode.  However, the load factor for slow cruise (in the precautionary area) derived by Arcadis is based on an assumption that all ships slow to 12 knots. It is entirely possible that larger ships such as bulk carriers and tankers may operate slower as they cannot be maneuvered or stopped as easily as small ships, so that using 12 knots for all ships may be incorrect.  Due to the cubic relationship of power to speed, slowing to ten knots would imply a load factor almost half that of slowing to 12 knots.  The cubic relationship also assumes that propeller and drivetrain efficiency remains constant over the speed range which is likely incorrect.  Due to the grouping of vessel types, and due to modest changes to speed assumptions, EEA suggests load factors that are slightly different from the Arcadis factors by mode, and these are listed in Table 4-6.

No alternatives to hoteling loads other than Arcadis survey based data are available.  Hence, we suggest these be utilized until more extensive survey based data becomes available.

TABLE 4-6

SUGGESTED LOADS BY MODE

(as percent of maximum continuous rating)

|  | Cruise | Slow Cruise | Maneuvering |
| --- | --- | --- | --- |
| Bulk Carrier & Tankers | 80 | 40 | 20 |
| General Cargo | 80 | 35 | 20 |
| Passenger* | 80 | 20 | 10 |
| Container/RORO/Reefer/Auto Carrier | 80 | 30 | 15 |
| Auxiliary Loads in kW |
|  | Fast/Slow Cruise | Maneuvering | Hoteling |
| Passenger Ships | 5000 | 5000 | 5000 |
| All Others | 750 | 1250 | 1000 |

*	All values except main engine load categories marked are from Reference 8.

Data on the horsepower and operating modes of all non-oceangoing hips is much more sparse.  Based on the data provided by EPA, EEA calculated the following average rated horsepower by vessel type:

- Fishing Vessels	-	1106

- Tug			-	4268

- Ferries			-	2415

- Yachts			-	1863

- Harbor Operations	-	5046

No data is available to compare these estimates, but these estimates are based on samples of about 100 vessels in each class.

Operating mode data on non-oceangoing vessels is not easy to characterize.  Typical estimates have been based on power factors of 80 percent, 40 percent, 20 percent and idle, for cruise, slow cruise, maneuvering, and trawling or waiting.  No estimates of auxiliary loads for such vessels are available.

The operating mode data on both oceangoing and non-oceangoing vessels appears to be derived from numerous assumptions that have not been subjected to any validation by EEA.  However, this is the best available data within the time and resource constraints of this project.

5.  EMISSION FACTOR SUMMARY

The analysis presented in this report derives new emission factors for marine vessels, based on data from the Lloyds Marine Exhaust Emissions Research Program, and the Coast Guard Test Program.  Unlike marine emission factors that were historically specified in units of fuel consumption, the emission factors are specified in units of work (kW-hr) and are dependent on engine load factor, which is the ratio of actual output to rated output based on the maximum continuous rating.

The computation of emissions (and fuel consumption, if required) can be performed by ship type for a given port and requires the following inputs:

- The number of calls to the port by vessel class and deadweight tonnage.

- The time spent, by ship type, in each of four operating modes defined as: normal cruise, slow cruise, maneuvering and hoteling.

Alternatively, if ship horsepower is directly available for each ship, classification by deadweight tonnage is not required.  In addition, the user may define alternative modes of operation and typical engine load factors by mode.

The basic equations used for the calculation are:

TIMEVCC, DWT, MODE = CALLSVCC, DWT ( LENGTHVCC,DWT ( %TIMEVCC, DWT, MODE/100

EMISSIONSVCC,DWT,MODE = (EF)(LFMODE) ( (HP)(DWT) ( LFMODE ( TIMEVCC, DWT, MODE

where:

VCC is the vessel class (tanker, RORO, etc.)

DWT is the deadweight tons

EF is the emissions factor

LF is the mode specific load factor

For the calculation, the TIME equation requires port specific inputs, while this report provides the EF and HP relationships.

The emission factors and fuel consumption rates are derived from substantially more data than earlier emission factors, and represent an improvement over the current fuel based emission factors.  However, the emission factors derived are subject to the following cautions:

- A significant portion of the database had measurements that yielded inconsistent values of air-fuel ratio depending on the calculation methodology employed.  These records were excluded from the analysis, but the remaining database was still adequate for analysis.

- Some of the data reported suspiciously low values of HC concentrations (below one ppb), but these data were retained in the analysis.  However, the number of records with low HC values is small.

- There are concerns regarding the determination of output power at each test mode, for about ten percent of the records.

- Most of the data analyzed is on engines rated at less than 8000 kW.  Most of the data points eliminated from analysis due to errors are from higher output engines, which are mostly two-stroke engines.  Hence, the applicability of the derived emission factors to all engine sizes is not firmly established.

The emissions factor algorithms derived are of the form:

E (g/kW-hr) = a (Fractional Load)-x + b

where E is the emissions rate per unit of work.  The data analysis showed no statistically significant differences in emissions rates by engine size or output range, or by two-stroke/four-stoke, subject to the caveats detailed above.  Emissions rates for SO2 are based on (fuel consumption x sulfur content of fuel) since all SO2 emissions are fuel derived.  Table 5-1 provides a summary of HC, CO, NOx, NO2, PM, CO2, and SO2 emission factors and fuel consumption as a function of load.  The fuel consumption factor algorithm (derived from the same database as the emission factors) is also in the same equation form as emission factor algorithms.  These emissions factor and fuel consumption rate algorithms are applicable to all engine sizes since the emissions data showed no statistically significant difference across engine sizes. In all cases (including fuel consumption), the algorithms provide the rates per unit of work, i.e. per kW-hr.  In order to obtain the absolute emission or fuel consumption level in grams, it is

TABLE 5-1

# MARINE ENGINE EMISSION FACTOR

# AND FUEL CONSUMPTION ALGORITHMS

(in g/kW-hr, for all marine engines)

| Pollutant | Exponent (x) | Intercept (b) | Coefficient (a) |
| --- | --- | --- | --- |
| PM | 1.5 | 0.2551 | 0.0059 |
| NOx | 1.5 | 10.4496 | 0.1255 |
| NO2 | 1.5 | 15.5247 | 0.18865 |
| SO2 | n/a | n/s | 2.3735 |
| CO | 1 | n/s | 0.8378 |
| HC | 1.5 | n/s | 0.0667 |
| CO2 | 1 | 648.6 | 44.1 |

1.	All regressions but SO2 are in the form of:

Emissions Rate (g/kW-hr) = a (Fractional Load)-x + b

2.	Fractional load is equal to actual engine output divided by rated engine output.

3.	The SO2 regression is the form of:

### Emissions Rate (g/kW-hr) = a (Fuel Sulfur Flow in g/kW-hr) + b

4.	Fuel Consumption (g/kW-hr) = 14.12/(Fractional Load) + 205.717

5.	n/a is not applicable, n/s is not statistically significant.

necessary to multiply the rates per unit of work by the work in kilowatts and the time in hours, as indicated by the equation listed on page 5-1 for emissions.

While the rederivation of emission factors and fuel consumption rate are central to this report, the relationship of engine rated horsepower to ship type and deadweight tonnage was also investigated.  Oceangoing ships were classified into four types and their horsepower was related to deadweight (DWT) using linear regressions.  The results are:

- Bulk Carriers and Tankers:  HP = 9070 + 0.101 (DWT)

- General Cargo Ships:  HP = 3046 + 0.288 (DWT)

- Container/RORO/Auto Carriers/Refrigerated Ships:  HP =  2581 + 0.719 (DWT)

- Passenger Ships:  HP = -4877 + 6.81 (DWT)

The relationship for the passenger ship category is the most uncertain since the sample of ships in this category was very small (40).

For all non-ocean going vessels, the empty weight or deadweight is generally not available in the Lloyd’s registration data, so that for these classes of vessels, only an average horsepower across the class was computed.  The values are based on a sample of about 100 vessels in each category and the results are:

- fishing vessels		-	1106 HP;

- tugs			-	4268 HP;

- ferries			-	2415 HP;

- yachts			-	1863 HP;

- harbor operations	-	5046 HP;

The values could be used as default values in the absence of actual HP data on the vessels operating at a specific port.

Operating modes were divided into four types:

- normal cruise;

- slow cruise;

- maneuvering;

- docking (hoteling).

No independent data analysis was performed on the load factors for the engines (main and auxiliary) at these operating modes. Results from literature are summarized, and the best source of load factor data is from a recent report by Arcadis.  Nevertheless, this data relies on a number of assumptions that may not be true, especially for a specific port.  The auxiliary engine loads (in absolute kilowatts) may be the most arbitrary as they are specified independent of ship size or weight.

Computation of emissions from auxiliary engines require the use of the same emission factors specified in Table 5-1, and are evaluated at a load factor equal to one (i.e., at full load).  Hence, the equation for emission from auxiliary engines is given by

Emissions = (EF)(LF=1) ( Auxiliary Power (kW) ( TimeVCC,DWT,HOTEL

Table 5-2 shows the suggested load factors for both ocean-going vessels and non-ocean-going vessels.  While these values could be reasonable default values, the use of port specific load factors is preferable, if available.

TABLE 5-2

SUGGESTED LOAD FACTORS

(as percent of maximum continuous rating)

| Vessel Type | Cruise | Slow Cruise | Maneuvering |
| --- | --- | --- | --- |
| Bulk Carriers & Tankers | 80 | 40 | 20 |
| General Cargo | 80 | 35 | 20 |
| Passenger | 80 | 20 | 10 |
| Container/RORO/Reefer/Auto Carrier | 80 | 30 | 15 |
| All non-oceangoing | 80 | 40 | 20 |

SUGGESTED AUXILIARY LOADS IN KW

(ocean-going vessels only)*

|  | Slow Cruise | Maneuvering | Hoteling |
| --- | --- | --- | --- |
| Passenger Ships | 5000 | 5000 | 5000 |
| All others | 750 | 1250 | 1000 |

*	Non-oceangoing vessels do not have separate auxiliary loads of significance.

6.  REFERENCES

1.	Marine Exhaust Emissions Research Programme: Steady State Operation, Lloyd’s Register of Shipping, London, United Kingdom, 1990.

2.	Marine Exhaust Emissions Research Programme: Steady State Operation, Slow Speed Addendum, Lloyd’s Register of Shipping, London, United Kingdom, 1991.

3.	Marine Exhaust Emissions Research Programme, Lloyd’s Register of Shipping, London, United Kingdom, 1995.

4.	Shipboard Marine Engines Emission Testing for the United States Coast Guard, Delivery Order Number 31, Final Report, prepared by Environmental Transportation Consultants for the Volpe National Transportation Systems Center and the United States Coast Guard Headquarters Naval Engineering Division, undated (emissions testing conducted in 1995).

5.	BC Ferries Emissions Test Program, Report for the BC Ferry Corporation, ERMD #98-26711, Environment Canada, Ottawa, Ontario, Canada, 1998

6.	Port of Vancouver Marine Vessel Emissions Test Project, Final Report, ERMD #97-04, Environment Canada, Ottawa, Ontario, Canada, 1997

7.	Marine Emissions Quantification – BCFC Ferries operating in Greater Vancouver Regional District Airshed, 97/EE/7002, Final Report, prepared by Lloyd’s Register of Shipping for the British Columbia Ferry Corporation, London, United Kingdom, 1997.

8.	Analysis of Marine Emissions in the South Coast Air Basin, Draft Report, EPA Contract Number 68-C6-0068, Work Assignment Number 0-02, prepared by Acurex Environmental Corporation for the U.S. Environmental Protection Agency, 1999.

- Inventory of Air Pollutant Emissions from Marine Vessels, Final Report, prepared by Booz-Allen & Hamilton for the California Air Resources Board, Revised March 1991

- Marine Vessel Emission Inventory and Control Strategies, Final Report, prepared by Acurex Environmental Corp., for the South Coast Air Quality Management District, 1996

- Facsimile transmittal on gas turbine emission rates from the Chevron “Louisiana,” Brian Shafritz of the Santa Barbara County (California) Air Pollution Control District to Gregg Jansen [sic] of the U.S. Environmental Protection Agency, June 1, 1999.

APPENDIX A

EMISSION FACTOR REGRESSION SUMMARIES

KEY TO APPENDIX TERMS:

1.	All regressions are of the form:

Emission rate (g/kW-hr) = (Coefficient ( Independent Variable) + Intercept

where:	Coefficient = Value in column labeled “Coeff,”

Intercept = Value in column labeled “Intercept,” and

Independent Variable = Parameter indicated in column labeled “Param” as follows:

“FL” = Fractional Load,

“1/(FL^e)” = Fractional Load to the negative “e” power, and

“Fuel S” = Fuel sulfur flow in g/kW-hr.

2.	Where applicable, the exponent “e” is indicated in the upper center of each regression summary.

3.	Entries in the column labeled “A/F Criteria” have the following meanings:

“All Data” indicates that no data was excluded from the regression analysis due to inconsistencies in estimated A/F ratio.

“Yes Data” indicates that only data meeting the consistent A/F ratio criteria described in Section 3 is included in the regression analysis.

4.	Entries in the column labeled “Loads Covered” have the following meanings:

“FL ge 0” means all data with an indicated fractional load greater than or equal to zero.

“FL ge 20” means all data with an indicated fractional load greater than or equal to 20 percent.

“FL lt 20” means all data with an indicated fractional load of less than 20 percent.

KEY TO APPENDIX TERMS

(Continued)

5.	Entries in the column labeled “Cycles Covered” have the following meanings:

“All” means all reported engine types are included in the regression analysis.

“2 Stroke” means only data for reported two stroke engines are included in the regression analysis.

“4 Stroke” means only data for reported four stroke engines are included in the regression analysis.

“Not Ind.” (not indicated) means only data for USCG engines not reported as either two or four stroke are included in the regression analysis.

6.	Entries in the column labeled “Fuels Covered” have the following meanings:

“All” means all reported fuel types are included in the regression analysis.

“Diesel” means only USCG fuel types (all identified simply as “diesel”) are included in the regression analysis.

“Gas Oil” means only data for reported gas oil fuel are included in the regression analysis.

“Gas Oil” means only data for reported gas oil fuel are included in the regression analysis.

“Hvy FO” means only data for reported heavy fuel oil fuel are included in the regression analysis.

“Int FO” means only data for reported intermediate fuel oil fuel are included in the regression analysis.

“Light FO” means only data for reported light fuel oil fuel are included in the regression analysis.

KEY TO APPENDIX TERMS

(Continued)

7.	Entries in the columns labeled “Int-T” and Coeff-T” indicate the regression t statistics for the intercept and coefficient respectively.

8.	Entries in the column labeled “r2” indicate the regression correlation coefficient.

9.	Entries in the column labeled “F” indicate the regression model variance F statistic.

10.	Entries in the three columns labeled “Sig?” indicate, from left to right, whether (“Yes”) or not (“No”) the indicated intercept t statistic, coefficient t statistic, and variance F statistic are significant at the 99 percent confidence level.

11.	Entries in the column labeled “Obs” indicate the number of observations used in the regression analysis.

| REGRESSION SUMMARY FOR: | PM | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 2.4352 | 2.981 | Yes | -3.6383 | -1.892 | No | FL | 0.10 | 3.58 | No | 35 | 2.435 | 2.435 | 2.435 | 2.435 | 2.435 |
| All Data | FL ge 0 | All | All | 0.8332 | 1.430 | No | 0.0066 | 1.593 | No | 1/(FL^e) | 0.07 | 2.54 | No | 35 |  |  |  |  |  |
| All Data | FL ge 20 | All | All | 0.3344 | 2.696 | No | -0.0482 | -0.221 | No | FL | 0.00 | 0.05 | No | 19 |  |  |  |  |  |
| All Data | FL lt 20 | All | All | 4.5556 | 2.245 | No | -25.4900 | -1.300 | No | FL | 0.11 | 1.69 | No | 16 |  |  |  |  |  |
| All Data | FL lt 20 | All | All | 1.8897 | 1.272 | No | 0.0035 | 0.486 | No | 1/(FL^e) | 0.02 | 0.24 | No | 16 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | All | 0.9289 | 4.369 | Yes | -1.1052 | -2.346 | No | FL | 0.16 | 5.50 | No | 31 | 0.929 | 0.929 | 0.929 | 0.929 | 0.929 |
| Yes Data | FL ge 0 | All | All | 0.2551 | 7.780 | Yes | 0.0059 | 23.143 | Yes | 1/(FL^e) | 0.95 | 535.58 | Yes | 31 | 0.784 | 0.442 | 0.279 | 0.263 | 0.261 |
| Yes Data | FL ge 20 | All | All | 0.3344 | 2.696 | No | -0.0482 | -0.221 | No | FL | 0.00 | 0.05 | No | 19 |  |  |  |  |  |
| Yes Data | FL lt 20 | All | All | 2.4562 | 6.000 | Yes | -15.5027 | -4.426 | No | FL | 0.66 | 19.59 | Yes | 12 | 2.456 | 2.456 | 2.456 | 2.456 | 2.456 |
| Yes Data | FL lt 20 | All | All | 0.1797 | 3.921 | Yes | 0.0061 | 27.472 | Yes | 1/(FL^e) | 0.99 | 754.73 | Yes | 12 | 0.726 | 0.373 | 0.204 | 0.188 | 0.186 |
| Yes Data | FL ge 0 | Not Ind. | All | 0.9533 | 3.927 | Yes | -1.1154 | -1.967 | No | FL | 0.14 | 3.87 | No | 25 | 0.953 | 0.953 | 0.953 | 0.953 | 0.953 |
| Yes Data | FL ge 0 | 2 Stroke | All | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | All | 0.4088 | 4.140 | Yes | -0.2656 | -1.443 | No | FL | 0.34 | 2.08 | No | 6 | 0.409 | 0.409 | 0.409 | 0.409 | 0.409 |
| Yes Data | FL ge 0 | Not Ind. | All | 0.2558 | 6.235 | Yes | 0.0059 | 20.590 | Yes | 1/(FL^e) | 0.95 | 423.95 | Yes | 25 | 0.785 | 0.443 | 0.279 | 0.264 | 0.262 |
| Yes Data | FL ge 0 | 2 Stroke | All | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | All | 0.1828 | 2.955 | No | 0.0274 | 1.602 | No | 1/(FL^e) | 0.39 | 2.57 | No | 6 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Diesel | 0.9289 | 4.369 | Yes | -1.1052 | -2.346 | No | FL | 0.16 | 5.50 | No | 31 | 0.929 | 0.929 | 0.929 | 0.929 | 0.929 |
| Yes Data | FL ge 0 | All | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Hvy FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Int FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Light FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Diesel | 0.2551 | 7.780 | Yes | 0.0059 | 23.143 | Yes | 1/(FL^e) | 0.95 | 535.58 | Yes | 31 | 0.784 | 0.442 | 0.279 | 0.263 | 0.261 |
| Yes Data | FL ge 0 | All | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Hvy FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Int FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Light FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 0.9533 | 3.927 | Yes | -1.1154 | -1.967 | No | FL | 0.14 | 3.87 | No | 25 | 0.953 | 0.953 | 0.953 | 0.953 | 0.953 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 0.4088 | 4.140 | Yes | -0.2656 | -1.443 | No | FL | 0.34 | 2.08 | No | 6 | 0.409 | 0.409 | 0.409 | 0.409 | 0.409 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | FL | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 0.2558 | 6.235 | Yes | 0.0059 | 20.590 | Yes | 1/(FL^e) | 0.95 | 423.95 | Yes | 25 | 0.785 | 0.443 | 0.279 | 0.264 | 0.262 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 0.1828 | 2.955 | No | 0.0274 | 1.602 | No | 1/(FL^e) | 0.39 | 2.57 | No | 6 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 0.0000 | 0.000 |  | 0.0000 | 0.000 |  | 1/(FL^e) | 0.00 | 0.00 |  | 0 |  |  |  |  |  |

| REGRESSION SUMMARY FOR: | NO | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 20.0268 | 19.658 | Yes | -14.9792 | -7.862 | No | FL | 0.15 | 61.81 | Yes | 356 | 20.027 | 20.027 | 20.027 | 20.027 | 20.027 |
| All Data | FL ge 0 | All | All | 10.4583 | 18.481 | Yes | 0.1110 | 14.647 | Yes | 1/(FL^e) | 0.38 | 214.54 | Yes | 356 | 20.386 | 13.968 | 10.897 | 10.613 | 10.569 |
| All Data | FL ge 20 | All | All | 10.7756 | 22.772 | Yes | -1.7939 | -2.449 | No | FL | 0.02 | 6.00 | No | 241 | 10.776 | 10.776 | 10.776 | 10.776 | 10.776 |
| All Data | FL lt 20 | All | All | 36.0476 | 11.209 | Yes | -158.9668 | -5.124 | No | FL | 0.19 | 26.25 | Yes | 115 | 36.048 | 36.048 | 36.048 | 36.048 | 36.048 |
| All Data | FL lt 20 | All | All | 14.1805 | 7.215 | Yes | 0.0939 | 6.270 | Yes | 1/(FL^e) | 0.26 | 39.31 | Yes | 115 | 22.577 | 17.149 | 14.552 | 14.312 | 14.274 |
| Yes Data | FL ge 0 | All | All | 16.9497 | 17.580 | Yes | -10.8279 | -6.407 | No | FL | 0.12 | 41.06 | Yes | 291 | 16.950 | 16.950 | 16.950 | 16.950 | 16.950 |
| Yes Data | FL ge 0 | All | All | 9.5181 | 24.154 | Yes | 0.1143 | 19.391 | Yes | 1/(FL^e) | 0.57 | 376.02 | Yes | 291 | 19.746 | 13.134 | 9.970 | 9.678 | 9.632 |
| Yes Data | FL ge 20 | All | All | 10.3842 | 21.257 | Yes | -1.6405 | -2.207 | No | FL | 0.02 | 4.87 | No | 217 | 10.384 | 10.384 | 10.384 | 10.384 | 10.384 |
| Yes Data | FL lt 20 | All | All | 33.9582 | 8.753 | Yes | -144.4380 | -4.358 | No | FL | 0.21 | 18.99 | Yes | 74 | 33.958 | 33.958 | 33.958 | 33.958 | 33.958 |
| Yes Data | FL lt 20 | All | All | 11.4486 | 7.186 | Yes | 0.1070 | 8.884 | Yes | 1/(FL^e) | 0.52 | 78.93 | Yes | 74 | 21.015 | 14.831 | 11.871 | 11.598 | 11.556 |
| Yes Data | FL ge 0 | Not Ind. | All | 18.6862 | 11.938 | Yes | -14.8995 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 18.686 | 18.686 | 18.686 | 18.686 | 18.686 |
| Yes Data | FL ge 0 | 2 Stroke | All | 9.5052 | 6.425 | Yes | 3.3223 | 1.239 | No | FL | 0.03 | 1.54 | No | 45 | 9.505 | 9.505 | 9.505 | 9.505 | 9.505 |
| Yes Data | FL ge 0 | 4 Stroke | All | 17.7374 | 14.654 | Yes | -12.2715 | -5.936 | No | FL | 0.14 | 35.23 | Yes | 220 | 17.737 | 17.737 | 17.737 | 17.737 | 17.737 |
| Yes Data | FL ge 0 | Not Ind. | All | 10.8992 | 17.308 | Yes | 0.0461 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 15.022 | 12.357 | 11.081 | 10.964 | 10.945 |
| Yes Data | FL ge 0 | 2 Stroke | All | 11.5228 | 15.199 | Yes | -0.0331 | -1.394 | No | 1/(FL^e) | 0.04 | 1.94 | No | 45 | 11.523 | 11.523 | 11.523 | 11.523 | 11.523 |
| Yes Data | FL ge 0 | 4 Stroke | All | 8.7618 | 24.437 | Yes | 0.1701 | 27.588 | Yes | 1/(FL^e) | 0.78 | 761.12 | Yes | 220 | 23.980 | 14.142 | 9.434 | 9.000 | 8.932 |
| Yes Data | FL ge 0 | All | Diesel | 13.8772 | 11.302 | Yes | -7.2368 | -3.571 | No | FL | 0.21 | 12.76 | Yes | 49 | 13.877 | 13.877 | 13.877 | 13.877 | 13.877 |
| Yes Data | FL ge 0 | All | Gas Oil | 20.6879 | 9.899 | Yes | -18.7851 | -4.675 | No | FL | 0.16 | 21.86 | Yes | 114 | 20.688 | 20.688 | 20.688 | 20.688 | 20.688 |
| Yes Data | FL ge 0 | All | Hvy FO | 10.7749 | 4.684 | Yes | 2.3879 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 10.775 | 10.775 | 10.775 | 10.775 | 10.775 |
| Yes Data | FL ge 0 | All | Int FO | 14.3115 | 3.934 | Yes | 0.8539 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 14.311 | 14.311 | 14.311 | 14.311 | 14.311 |
| Yes Data | FL ge 0 | All | Light FO | 14.9135 | 14.592 | Yes | -7.4032 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 14.913 | 14.913 | 14.913 | 14.913 | 14.913 |
| Yes Data | FL ge 0 | All | Diesel | 8.9596 | 13.947 | Yes | 0.0466 | 7.634 | Yes | 1/(FL^e) | 0.55 | 58.29 | Yes | 49 | 13.129 | 10.434 | 9.144 | 9.025 | 9.006 |
| Yes Data | FL ge 0 | All | Gas Oil | 8.5884 | 13.755 | Yes | 0.1679 | 20.753 | Yes | 1/(FL^e) | 0.79 | 430.69 | Yes | 114 | 23.604 | 13.897 | 9.252 | 8.823 | 8.756 |
| Yes Data | FL ge 0 | All | Hvy FO | 12.5316 | 11.263 | Yes | -0.0974 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 12.532 | 12.532 | 12.532 | 12.532 | 12.532 |
| Yes Data | FL ge 0 | All | Int FO | 16.4739 | 8.921 | Yes | -0.2364 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 16.474 | 16.474 | 16.474 | 16.474 | 16.474 |
| Yes Data | FL ge 0 | All | Light FO | 8.8753 | 23.720 | Yes | 0.1754 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.25 | Yes | 96 | 24.562 | 14.421 | 9.569 | 9.120 | 9.051 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 18.6862 | 11.938 | Yes | -14.8995 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 18.686 | 18.686 | 18.686 | 18.686 | 18.686 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 5.7116 | 39.867 | Yes | 0.8915 | 3.117 | No | FL | 0.58 | 9.72 | No | 9 | 5.712 | 5.712 | 5.712 | 5.712 | 5.712 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 9.3553 | 3.353 | No | -3.7954 | -0.572 | No | FL | 0.14 | 0.33 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 10.7749 | 4.684 | Yes | 2.3879 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 10.775 | 10.775 | 10.775 | 10.775 | 10.775 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 14.3115 | 3.934 | Yes | 0.8539 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 14.311 | 14.311 | 14.311 | 14.311 | 14.311 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 10.3081 | 4.813 | Yes | -2.9725 | -1.180 | No | FL | 0.10 | 1.39 | No | 14 | 10.308 | 10.308 | 10.308 | 10.308 | 10.308 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 21.2210 | 9.822 | Yes | -19.4814 | -4.720 | No | FL | 0.17 | 22.28 | Yes | 110 | 21.221 | 21.221 | 21.221 | 21.221 | 21.221 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 14.9135 | 14.592 | Yes | -7.4032 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 14.913 | 14.913 | 14.913 | 14.913 | 14.913 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 10.8992 | 17.308 | Yes | 0.0461 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 15.022 | 12.357 | 11.081 | 10.964 | 10.945 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 6.2249 | 74.161 | Yes | -0.0058 | -4.130 | No | 1/(FL^e) | 0.71 | 17.06 | Yes | 9 | 6.225 | 6.225 | 6.225 | 6.225 | 6.225 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 6.3121 | 6.932 | No | 0.0575 | 3.339 | No | 1/(FL^e) | 0.85 | 11.15 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 12.5316 | 11.263 | Yes | -0.0974 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 12.532 | 12.532 | 12.532 | 12.532 | 12.532 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 16.4739 | 8.921 | Yes | -0.2364 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 16.474 | 16.474 | 16.474 | 16.474 | 16.474 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 8.4415 | 3.834 | Yes | -0.0495 | -0.096 | No | 1/(FL^e) | 0.00 | 0.01 | No | 14 | 8.441 | 8.441 | 8.441 | 8.441 | 8.441 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 8.7582 | 13.922 | Yes | 0.1695 | 20.995 | Yes | 1/(FL^e) | 0.80 | 440.78 | Yes | 110 | 23.917 | 14.118 | 9.428 | 8.995 | 8.928 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 8.8753 | 23.720 | Yes | 0.1754 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.25 | Yes | 96 | 24.562 | 14.421 | 9.569 | 9.120 | 9.051 |

| REGRESSION SUMMARY FOR: | NOx | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 21.9867 | 19.658 | Yes | -16.4451 | -7.862 | No | FL | 0.15 | 61.81 | Yes | 356 | 21.987 | 21.987 | 21.987 | 21.987 | 21.987 |
| All Data | FL ge 0 | All | All | 11.4817 | 18.481 | Yes | 0.1219 | 14.647 | Yes | 1/(FL^e) | 0.38 | 214.54 | Yes | 356 | 22.381 | 15.335 | 11.963 | 11.652 | 11.604 |
| All Data | FL ge 20 | All | All | 11.8301 | 22.772 | Yes | -1.9694 | -2.449 | No | FL | 0.02 | 6.00 | No | 241 | 11.830 | 11.830 | 11.830 | 11.830 | 11.830 |
| All Data | FL lt 20 | All | All | 39.5753 | 11.209 | Yes | -174.5233 | -5.124 | No | FL | 0.19 | 26.25 | Yes | 115 | 39.575 | 39.575 | 39.575 | 39.575 | 39.575 |
| All Data | FL lt 20 | All | All | 15.5683 | 7.215 | Yes | 0.1031 | 6.270 | Yes | 1/(FL^e) | 0.26 | 39.31 | Yes | 115 | 24.787 | 18.828 | 15.976 | 15.712 | 15.671 |
| Yes Data | FL ge 0 | All | All | 18.6084 | 17.580 | Yes | -11.8876 | -6.407 | No | FL | 0.12 | 41.06 | Yes | 291 | 18.608 | 18.608 | 18.608 | 18.608 | 18.608 |
| Yes Data | FL ge 0 | All | All | 10.4496 | 24.154 | Yes | 0.1255 | 19.391 | Yes | 1/(FL^e) | 0.57 | 376.02 | Yes | 291 | 21.678 | 14.419 | 10.946 | 10.625 | 10.575 |
| Yes Data | FL ge 20 | All | All | 11.4004 | 21.257 | Yes | -1.8011 | -2.207 | No | FL | 0.02 | 4.87 | No | 217 | 11.400 | 11.400 | 11.400 | 11.400 | 11.400 |
| Yes Data | FL lt 20 | All | All | 37.2814 | 8.753 | Yes | -158.5718 | -4.358 | No | FL | 0.21 | 18.99 | Yes | 74 | 37.281 | 37.281 | 37.281 | 37.281 | 37.281 |
| Yes Data | FL lt 20 | All | All | 12.5690 | 7.186 | Yes | 0.1174 | 8.884 | Yes | 1/(FL^e) | 0.52 | 78.93 | Yes | 74 | 23.071 | 16.282 | 13.033 | 12.733 | 12.686 |
| Yes Data | FL ge 0 | Not Ind. | All | 20.5149 | 11.938 | Yes | -16.3577 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 20.515 | 20.515 | 20.515 | 20.515 | 20.515 |
| Yes Data | FL ge 0 | 2 Stroke | All | 10.4352 | 6.425 | Yes | 3.6475 | 1.239 | No | FL | 0.03 | 1.54 | No | 45 | 10.435 | 10.435 | 10.435 | 10.435 | 10.435 |
| Yes Data | FL ge 0 | 4 Stroke | All | 19.4732 | 14.654 | Yes | -13.4724 | -5.936 | No | FL | 0.14 | 35.23 | Yes | 220 | 19.473 | 19.473 | 19.473 | 19.473 | 19.473 |
| Yes Data | FL ge 0 | Not Ind. | All | 11.9658 | 17.308 | Yes | 0.0506 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 16.492 | 13.566 | 12.166 | 12.037 | 12.016 |
| Yes Data | FL ge 0 | 2 Stroke | All | 12.6504 | 15.198 | Yes | -0.0363 | -1.394 | No | 1/(FL^e) | 0.04 | 1.94 | No | 45 | 12.650 | 12.650 | 12.650 | 12.650 | 12.650 |
| Yes Data | FL ge 0 | 4 Stroke | All | 9.6193 | 24.437 | Yes | 0.1868 | 27.588 | Yes | 1/(FL^e) | 0.78 | 761.12 | Yes | 220 | 26.327 | 15.526 | 10.358 | 9.880 | 9.806 |
| Yes Data | FL ge 0 | All | Diesel | 15.2353 | 11.302 | Yes | -7.9452 | -3.572 | No | FL | 0.21 | 12.76 | Yes | 49 | 15.235 | 15.235 | 15.235 | 15.235 | 15.235 |
| Yes Data | FL ge 0 | All | Gas Oil | 22.7124 | 9.899 | Yes | -20.6235 | -4.675 | No | FL | 0.16 | 21.86 | Yes | 114 | 22.712 | 22.712 | 22.712 | 22.712 | 22.712 |
| Yes Data | FL ge 0 | All | Hvy FO | 11.8293 | 4.684 | Yes | 2.6216 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 11.829 | 11.829 | 11.829 | 11.829 | 11.829 |
| Yes Data | FL ge 0 | All | Int FO | 15.7119 | 3.934 | Yes | 0.9377 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 15.712 | 15.712 | 15.712 | 15.712 | 15.712 |
| Yes Data | FL ge 0 | All | Light FO | 16.3730 | 14.592 | Yes | -8.1277 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 16.373 | 16.373 | 16.373 | 16.373 | 16.373 |
| Yes Data | FL ge 0 | All | Diesel | 9.8363 | 13.947 | Yes | 0.0512 | 7.634 | Yes | 1/(FL^e) | 0.55 | 58.28 | Yes | 49 | 14.413 | 11.454 | 10.039 | 9.908 | 9.887 |
| Yes Data | FL ge 0 | All | Gas Oil | 9.4289 | 13.755 | Yes | 0.1843 | 20.753 | Yes | 1/(FL^e) | 0.79 | 430.69 | Yes | 114 | 25.913 | 15.257 | 10.157 | 9.686 | 9.613 |
| Yes Data | FL ge 0 | All | Hvy FO | 13.7580 | 11.263 | Yes | -0.1069 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 13.758 | 13.758 | 13.758 | 13.758 | 13.758 |
| Yes Data | FL ge 0 | All | Int FO | 18.0862 | 8.921 | Yes | -0.2595 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 18.086 | 18.086 | 18.086 | 18.086 | 18.086 |
| Yes Data | FL ge 0 | All | Light FO | 9.7439 | 23.720 | Yes | 0.1925 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.24 | Yes | 96 | 26.966 | 15.833 | 10.505 | 10.013 | 9.936 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 20.5149 | 11.938 | Yes | -16.3577 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 20.515 | 20.515 | 20.515 | 20.515 | 20.515 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 6.2705 | 39.887 | Yes | 0.9784 | 3.118 | No | FL | 0.58 | 9.72 | No | 9 | 6.270 | 6.270 | 6.270 | 6.270 | 6.270 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 10.2705 | 3.354 | No | -4.1654 | -0.572 | No | FL | 0.14 | 0.33 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 11.8293 | 4.684 | Yes | 2.6216 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 11.829 | 11.829 | 11.829 | 11.829 | 11.829 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 15.7119 | 3.934 | Yes | 0.9377 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 15.712 | 15.712 | 15.712 | 15.712 | 15.712 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 11.3168 | 4.813 | Yes | -3.2635 | -1.180 | No | FL | 0.10 | 1.39 | No | 14 | 11.317 | 11.317 | 11.317 | 11.317 | 11.317 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 23.2977 | 9.822 | Yes | -21.3880 | -4.720 | No | FL | 0.17 | 22.28 | Yes | 110 | 23.298 | 23.298 | 23.298 | 23.298 | 23.298 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 16.3730 | 14.592 | Yes | -8.1277 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 16.373 | 16.373 | 16.373 | 16.373 | 16.373 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 11.9658 | 17.308 | Yes | 0.0506 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 16.492 | 13.566 | 12.166 | 12.037 | 12.016 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 6.8337 | 74.147 | Yes | -0.0064 | -4.127 | No | 1/(FL^e) | 0.71 | 17.03 | Yes | 9 | 6.834 | 6.834 | 6.834 | 6.834 | 6.834 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 6.9302 | 6.932 | No | 0.0631 | 3.339 | No | 1/(FL^e) | 0.85 | 11.15 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 13.7580 | 11.263 | Yes | -0.1069 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 13.758 | 13.758 | 13.758 | 13.758 | 13.758 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 18.0862 | 8.921 | Yes | -0.2595 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 18.086 | 18.086 | 18.086 | 18.086 | 18.086 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 9.2673 | 3.834 | Yes | -0.0543 | -0.096 | No | 1/(FL^e) | 0.00 | 0.01 | No | 14 | 9.267 | 9.267 | 9.267 | 9.267 | 9.267 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 9.6153 | 13.922 | Yes | 0.1861 | 20.995 | Yes | 1/(FL^e) | 0.80 | 440.78 | Yes | 110 | 26.257 | 15.499 | 10.351 | 9.875 | 9.801 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 9.7439 | 23.720 | Yes | 0.1925 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.24 | Yes | 96 | 26.966 | 15.833 | 10.505 | 10.013 | 9.936 |

| REGRESSION SUMMARY FOR: | NO2 Equivalent NOx | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 32.6651 | 19.659 | Yes | -24.4322 | -7.862 | No | FL | 0.15 | 61.81 | Yes | 356 | 32.665 | 32.665 | 32.665 | 32.665 | 32.665 |
| All Data | FL ge 0 | All | All | 17.0581 | 18.481 | Yes | 0.1810 | 14.647 | Yes | 1/(FL^e) | 0.38 | 214.54 | Yes | 356 | 33.250 | 22.783 | 17.774 | 17.311 | 17.239 |
| All Data | FL ge 20 | All | All | 17.5759 | 22.772 | Yes | -2.9262 | -2.449 | No | FL | 0.02 | 6.00 | No | 241 | 17.576 | 17.576 | 17.576 | 17.576 | 17.576 |
| All Data | FL lt 20 | All | All | 58.7960 | 11.209 | Yes | -259.2844 | -5.124 | No | FL | 0.19 | 26.25 | Yes | 115 | 58.796 | 58.796 | 58.796 | 58.796 | 58.796 |
| All Data | FL lt 20 | All | All | 23.1294 | 7.215 | Yes | 0.1531 | 6.270 | Yes | 1/(FL^e) | 0.26 | 39.31 | Yes | 115 | 36.825 | 27.972 | 23.735 | 23.343 | 23.283 |
| Yes Data | FL ge 0 | All | All | 27.6461 | 17.580 | Yes | -17.6612 | -6.408 | No | FL | 0.12 | 41.06 | Yes | 291 | 27.646 | 27.646 | 27.646 | 27.646 | 27.646 |
| Yes Data | FL ge 0 | All | All | 15.5247 | 24.154 | Yes | 0.1865 | 19.391 | Yes | 1/(FL^e) | 0.57 | 376.02 | Yes | 291 | 32.207 | 21.423 | 16.262 | 15.785 | 15.711 |
| Yes Data | FL ge 20 | All | All | 16.9374 | 21.257 | Yes | -2.6760 | -2.207 | No | FL | 0.02 | 4.87 | No | 217 | 16.937 | 16.937 | 16.937 | 16.937 | 16.937 |
| Yes Data | FL lt 20 | All | All | 55.3881 | 8.753 | Yes | -235.5868 | -4.358 | No | FL | 0.21 | 18.99 | Yes | 74 | 55.388 | 55.388 | 55.388 | 55.388 | 55.388 |
| Yes Data | FL lt 20 | All | All | 18.6734 | 7.186 | Yes | 0.1744 | 8.884 | Yes | 1/(FL^e) | 0.52 | 78.93 | Yes | 74 | 34.277 | 24.190 | 19.363 | 18.917 | 18.848 |
| Yes Data | FL ge 0 | Not Ind. | All | 30.4786 | 11.938 | Yes | -24.3023 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 30.479 | 30.479 | 30.479 | 30.479 | 30.479 |
| Yes Data | FL ge 0 | 2 Stroke | All | 15.5034 | 6.425 | Yes | 5.4192 | 1.239 | No | FL | 0.03 | 1.54 | No | 45 | 15.503 | 15.503 | 15.503 | 15.503 | 15.503 |
| Yes Data | FL ge 0 | 4 Stroke | All | 28.9309 | 14.654 | Yes | -20.0158 | -5.936 | No | FL | 0.14 | 35.23 | Yes | 220 | 28.931 | 28.931 | 28.931 | 28.931 | 28.931 |
| Yes Data | FL ge 0 | Not Ind. | All | 17.7773 | 17.308 | Yes | 0.0752 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 24.502 | 20.155 | 18.074 | 17.882 | 17.852 |
| Yes Data | FL ge 0 | 2 Stroke | All | 18.7945 | 15.199 | Yes | -0.0539 | -1.394 | No | 1/(FL^e) | 0.04 | 1.94 | No | 45 | 18.794 | 18.794 | 18.794 | 18.794 | 18.794 |
| Yes Data | FL ge 0 | 4 Stroke | All | 14.2911 | 24.437 | Yes | 0.2775 | 27.588 | Yes | 1/(FL^e) | 0.78 | 761.12 | Yes | 220 | 39.113 | 23.067 | 15.388 | 14.679 | 14.569 |
| Yes Data | FL ge 0 | All | Diesel | 22.6347 | 11.302 | Yes | -11.8040 | -3.572 | No | FL | 0.21 | 12.76 | Yes | 49 | 22.635 | 22.635 | 22.635 | 22.635 | 22.635 |
| Yes Data | FL ge 0 | All | Gas Oil | 33.7434 | 9.899 | Yes | -30.6400 | -4.675 | No | FL | 0.16 | 21.86 | Yes | 114 | 33.743 | 33.743 | 33.743 | 33.743 | 33.743 |
| Yes Data | FL ge 0 | All | Hvy FO | 17.5747 | 4.684 | Yes | 3.8949 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 17.575 | 17.575 | 17.575 | 17.575 | 17.575 |
| Yes Data | FL ge 0 | All | Int FO | 23.3426 | 3.934 | Yes | 1.3935 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 23.343 | 23.343 | 23.343 | 23.343 | 23.343 |
| Yes Data | FL ge 0 | All | Light FO | 24.3249 | 14.592 | Yes | -12.0752 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 24.325 | 24.325 | 24.325 | 24.325 | 24.325 |
| Yes Data | FL ge 0 | All | Diesel | 14.6136 | 13.947 | Yes | 0.0760 | 7.634 | Yes | 1/(FL^e) | 0.55 | 58.28 | Yes | 49 | 21.414 | 17.018 | 14.914 | 14.720 | 14.690 |
| Yes Data | FL ge 0 | All | Gas Oil | 14.0083 | 13.755 | Yes | 0.2738 | 20.753 | Yes | 1/(FL^e) | 0.79 | 430.69 | Yes | 114 | 38.499 | 22.667 | 15.091 | 14.391 | 14.282 |
| Yes Data | FL ge 0 | All | Hvy FO | 20.4401 | 11.263 | Yes | -0.1589 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 20.440 | 20.440 | 20.440 | 20.440 | 20.440 |
| Yes Data | FL ge 0 | All | Int FO | 26.8702 | 8.922 | Yes | -0.3856 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 26.870 | 26.870 | 26.870 | 26.870 | 26.870 |
| Yes Data | FL ge 0 | All | Light FO | 14.4763 | 23.720 | Yes | 0.2861 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.24 | Yes | 96 | 40.062 | 23.522 | 15.607 | 14.876 | 14.762 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 30.4786 | 11.938 | Yes | -24.3023 | -4.426 | No | FL | 0.45 | 19.59 | Yes | 26 | 30.479 | 30.479 | 30.479 | 30.479 | 30.479 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 9.3158 | 39.863 | Yes | 1.4542 | 3.117 | No | FL | 0.58 | 9.72 | No | 9 | 9.316 | 9.316 | 9.316 | 9.316 | 9.316 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 15.2591 | 3.353 | No | -6.1893 | -0.572 | No | FL | 0.14 | 0.33 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 17.5747 | 4.684 | Yes | 3.8949 | 0.616 | No | FL | 0.02 | 0.38 | No | 22 | 17.575 | 17.575 | 17.575 | 17.575 | 17.575 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 23.3426 | 3.934 | Yes | 1.3935 | 0.128 | No | FL | 0.00 | 0.02 | No | 10 | 23.343 | 23.343 | 23.343 | 23.343 | 23.343 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 16.8134 | 4.813 | Yes | -4.8488 | -1.180 | No | FL | 0.10 | 1.39 | No | 14 | 16.813 | 16.813 | 16.813 | 16.813 | 16.813 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 34.6129 | 9.822 | Yes | -31.7759 | -4.720 | No | FL | 0.17 | 22.28 | Yes | 110 | 34.613 | 34.613 | 34.613 | 34.613 | 34.613 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 24.3249 | 14.592 | Yes | -12.0752 | -4.384 | No | FL | 0.17 | 19.22 | Yes | 96 | 24.325 | 24.325 | 24.325 | 24.325 | 24.325 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 17.7773 | 17.308 | Yes | 0.0752 | 10.252 | Yes | 1/(FL^e) | 0.81 | 105.10 | Yes | 26 | 24.502 | 20.155 | 18.074 | 17.882 | 17.852 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 10.1530 | 74.148 | Yes | -0.0094 | -4.129 | No | 1/(FL^e) | 0.71 | 17.05 | Yes | 9 | 10.153 | 10.153 | 10.153 | 10.153 | 10.153 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 10.2959 | 6.932 | No | 0.0937 | 3.339 | No | 1/(FL^e) | 0.85 | 11.15 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 20.4401 | 11.263 | Yes | -0.1589 | -0.611 | No | 1/(FL^e) | 0.02 | 0.37 | No | 22 | 20.440 | 20.440 | 20.440 | 20.440 | 20.440 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 26.8702 | 8.922 | Yes | -0.3856 | -1.546 | No | 1/(FL^e) | 0.23 | 2.39 | No | 10 | 26.870 | 26.870 | 26.870 | 26.870 | 26.870 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 13.7683 | 3.834 | Yes | -0.0807 | -0.096 | No | 1/(FL^e) | 0.00 | 0.01 | No | 14 | 13.768 | 13.768 | 13.768 | 13.768 | 13.768 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 14.2852 | 13.922 | Yes | 0.2764 | 20.995 | Yes | 1/(FL^e) | 0.80 | 440.78 | Yes | 110 | 39.010 | 23.027 | 15.378 | 14.672 | 14.562 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 14.4763 | 23.720 | Yes | 0.2861 | 13.124 | Yes | 1/(FL^e) | 0.65 | 172.24 | Yes | 96 | 40.062 | 23.522 | 15.607 | 14.876 | 14.762 |

| REGRESSION SUMMARY FOR: | CO | Exponent = | 1 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 17.9327 | 11.404 | Yes | -23.1061 | -7.856 | No | FL | 0.15 | 61.72 | Yes | 356 | 17.933 | 17.933 | 17.933 | 17.933 | 17.933 |
| All Data | FL ge 0 | All | All | -0.7044 | -0.757 | No | 1.2802 | 16.633 | Yes | 1/(FL^e) | 0.44 | 276.67 | Yes | 356 | 25.603 | 12.802 | 3.200 | 1.600 | 1.280 |
| All Data | FL ge 20 | All | All | 2.8330 | 12.807 | Yes | -1.4384 | -4.200 | No | FL | 0.07 | 17.64 | Yes | 241 | 2.833 | 2.833 | 2.833 | 2.833 | 2.833 |
| All Data | FL lt 20 | All | All | 47.6066 | 9.888 | Yes | -299.4701 | -6.447 | No | FL | 0.27 | 41.57 | Yes | 115 | 47.607 | 47.607 | 47.607 | 47.607 | 47.607 |
| All Data | FL lt 20 | All | All | -0.8009 | -0.203 | No | 1.2891 | 6.867 | Yes | 1/(FL^e) | 0.29 | 47.15 | Yes | 115 | 25.782 | 12.891 | 3.223 | 1.611 | 1.289 |
| Yes Data | FL ge 0 | All | All | 9.9821 | 9.983 | Yes | -11.4844 | -6.553 | No | FL | 0.13 | 42.94 | Yes | 291 | 9.982 | 9.982 | 9.982 | 9.982 | 9.982 |
| Yes Data | FL ge 0 | All | All | 0.1548 | 0.323 | No | 0.8378 | 17.700 | Yes | 1/(FL^e) | 0.52 | 313.29 | Yes | 291 | 16.756 | 8.378 | 2.094 | 1.047 | 0.838 |
| Yes Data | FL ge 20 | All | All | 2.7465 | 12.135 | Yes | -1.3058 | -3.791 | No | FL | 0.06 | 14.38 | Yes | 217 | 2.746 | 2.746 | 2.746 | 2.746 | 2.746 |
| Yes Data | FL lt 20 | All | All | 30.8036 | 7.784 | Yes | -179.5074 | -5.309 | No | FL | 0.28 | 28.19 | Yes | 74 | 30.804 | 30.804 | 30.804 | 30.804 | 30.804 |
| Yes Data | FL lt 20 | All | All | -0.5190 | -0.218 | No | 0.8653 | 7.175 | Yes | 1/(FL^e) | 0.42 | 51.48 | Yes | 74 | 17.306 | 8.653 | 2.163 | 1.082 | 0.865 |
| Yes Data | FL ge 0 | Not Ind. | All | 7.1043 | 4.138 | Yes | -7.1069 | -1.925 | No | FL | 0.13 | 3.71 | No | 26 | 7.104 | 7.104 | 7.104 | 7.104 | 7.104 |
| Yes Data | FL ge 0 | 2 Stroke | All | 10.0714 | 2.787 | Yes | -12.2131 | -1.865 | No | FL | 0.07 | 3.48 | No | 45 | 10.071 | 10.071 | 10.071 | 10.071 | 10.071 |
| Yes Data | FL ge 0 | 4 Stroke | All | 10.4487 | 9.169 | Yes | -12.0126 | -6.172 | No | FL | 0.15 | 38.09 | Yes | 220 | 10.449 | 10.449 | 10.449 | 10.449 | 10.449 |
| Yes Data | FL ge 0 | Not Ind. | All | 1.2052 | 2.717 | No | 0.3414 | 14.485 | Yes | 1/(FL^e) | 0.90 | 209.81 | Yes | 26 | 6.828 | 3.414 | 0.853 | 0.427 | 0.341 |
| Yes Data | FL ge 0 | 2 Stroke | All | -0.0311 | -0.016 | No | 1.0290 | 3.637 | Yes | 1/(FL^e) | 0.24 | 13.23 | Yes | 45 | 20.580 | 10.290 | 2.572 | 1.286 | 1.029 |
| Yes Data | FL ge 0 | 4 Stroke | All | -0.8389 | -1.956 | No | 1.1081 | 23.705 | Yes | 1/(FL^e) | 0.72 | 561.94 | Yes | 220 | 22.161 | 11.081 | 2.770 | 1.385 | 1.108 |
| Yes Data | FL ge 0 | All | Diesel | 4.9827 | 5.218 | Yes | -3.4791 | -2.208 | No | FL | 0.09 | 4.88 | No | 49 | 4.983 | 4.983 | 4.983 | 4.983 | 4.983 |
| Yes Data | FL ge 0 | All | Gas Oil | 12.3421 | 5.885 | Yes | -16.0776 | -3.988 | No | FL | 0.12 | 15.90 | Yes | 114 | 12.342 | 12.342 | 12.342 | 12.342 | 12.342 |
| Yes Data | FL ge 0 | All | Hvy FO | 2.2926 | 1.739 | No | 0.7222 | 0.325 | No | FL | 0.01 | 0.11 | No | 22 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Int FO | -0.0250 | -0.338 | No | 1.6230 | 11.935 | Yes | FL | 0.95 | 142.44 | Yes | 10 | 0.081 | 0.162 | 0.649 | 1.298 | 1.623 |
| Yes Data | FL ge 0 | All | Light FO | 12.9905 | 8.795 | Yes | -15.6928 | -6.429 | No | FL | 0.31 | 41.34 | Yes | 96 | 12.991 | 12.991 | 12.991 | 12.991 | 12.991 |
| Yes Data | FL ge 0 | All | Diesel | 1.1761 | 3.294 | Yes | 0.3111 | 12.743 | Yes | 1/(FL^e) | 0.78 | 162.38 | Yes | 49 | 7.398 | 4.287 | 1.954 | 1.565 | 1.487 |
| Yes Data | FL ge 0 | All | Gas Oil | -1.5152 | -1.755 | No | 1.1578 | 15.205 | Yes | 1/(FL^e) | 0.67 | 231.19 | Yes | 114 | 23.156 | 11.578 | 2.894 | 1.447 | 1.158 |
| Yes Data | FL ge 0 | All | Hvy FO | 3.1895 | 3.905 | Yes | -0.2032 | -0.755 | No | 1/(FL^e) | 0.03 | 0.57 | No | 22 | 3.189 | 3.189 | 3.189 | 3.189 | 3.189 |
| Yes Data | FL ge 0 | All | Int FO | 1.1732 | 9.474 | Yes | -0.1249 | -4.351 | No | 1/(FL^e) | 0.70 | 18.93 | Yes | 10 | 1.173 | 1.173 | 1.173 | 1.173 | 1.173 |
| Yes Data | FL ge 0 | All | Light FO | -0.6867 | -1.058 | No | 1.3344 | 13.786 | Yes | 1/(FL^e) | 0.67 | 190.05 | Yes | 96 | 26.687 | 13.344 | 3.336 | 1.668 | 1.334 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 7.1043 | 4.138 | Yes | -7.1069 | -1.925 | No | FL | 0.13 | 3.71 | No | 26 | 7.104 | 7.104 | 7.104 | 7.104 | 7.104 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 1.6026 | 3.847 | Yes | -0.8657 | -1.041 | No | FL | 0.13 | 1.08 | No | 9 | 1.603 | 1.603 | 1.603 | 1.603 | 1.603 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 56.3283 | 2.555 | No | -89.1275 | -1.701 | No | FL | 0.59 | 2.89 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 2.2926 | 1.739 | No | 0.7222 | 0.325 | No | FL | 0.01 | 0.11 | No | 22 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | -0.0250 | -0.338 | No | 1.6230 | 11.935 | Yes | FL | 0.95 | 142.44 | Yes | 10 | 0.081 | 0.162 | 0.649 | 1.298 | 1.623 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 3.6282 | 5.165 | Yes | -1.5295 | -1.851 | No | FL | 0.22 | 3.43 | No | 14 | 3.628 | 3.628 | 3.628 | 3.628 | 3.628 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 10.3567 | 5.510 | Yes | -13.1566 | -3.664 | No | FL | 0.11 | 13.42 | Yes | 110 | 10.357 | 10.357 | 10.357 | 10.357 | 10.357 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 12.9905 | 8.795 | Yes | -15.6928 | -6.429 | No | FL | 0.31 | 41.34 | Yes | 96 | 12.991 | 12.991 | 12.991 | 12.991 | 12.991 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 1.2052 | 2.717 | No | 0.3414 | 14.485 | Yes | 1/(FL^e) | 0.90 | 209.81 | Yes | 26 | 6.828 | 3.414 | 0.853 | 0.427 | 0.341 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 0.7511 | 4.762 | Yes | 0.0725 | 5.278 | Yes | 1/(FL^e) | 0.80 | 27.86 | Yes | 9 | 2.201 | 1.476 | 0.932 | 0.842 | 0.824 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | -2.3730 | -1.597 | No | 3.6561 | 28.520 | Yes | 1/(FL^e) | 1.00 | 813.41 | Yes | 4 | 73.122 | 36.561 | 9.140 | 4.570 | 3.656 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 3.1895 | 3.905 | Yes | -0.2032 | -0.755 | No | 1/(FL^e) | 0.03 | 0.57 | No | 22 | 3.189 | 3.189 | 3.189 | 3.189 | 3.189 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 1.1732 | 9.474 | Yes | -0.1249 | -4.351 | No | 1/(FL^e) | 0.70 | 18.93 | Yes | 10 | 1.173 | 1.173 | 1.173 | 1.173 | 1.173 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 1.7660 | 1.824 | No | 0.3854 | 0.954 | No | 1/(FL^e) | 0.07 | 0.91 | No | 14 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | -1.7160 | -2.700 | No | 1.0740 | 19.151 | Yes | 1/(FL^e) | 0.77 | 366.75 | Yes | 110 | 21.480 | 10.740 | 2.685 | 1.343 | 1.074 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | -0.6867 | -1.058 | No | 1.3344 | 13.786 | Yes | 1/(FL^e) | 0.67 | 190.05 | Yes | 96 | 26.687 | 13.344 | 3.336 | 1.668 | 1.334 |

| REGRESSION SUMMARY FOR: | CO2 | Exponent = | 1 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 1361.0 | 24.928 | Yes | -911.9 | -8.931 | No | FL | 0.18 | 79.76 | Yes | 356 | 1361.0 | 1361.0 | 1361.0 | 1361.0 | 1361.0 |
| All Data | FL ge 0 | All | All | 653.1 | 20.189 | Yes | 46.5 | 17.363 | Yes | 1/(FL^e) | 0.46 | 301.48 | Yes | 356 | 1582.8 | 1117.9 | 769.3 | 711.2 | 699.5 |
| All Data | FL ge 20 | All | All | 807.0 | 64.326 | Yes | -120.6 | -6.210 | No | FL | 0.14 | 38.56 | Yes | 241 | 807.0 | 807.0 | 807.0 | 807.0 | 807.0 |
| All Data | FL lt 20 | All | All | 2361.5 | 14.126 | Yes | -10017.0 | -6.211 | No | FL | 0.25 | 38.57 | Yes | 115 | 2361.5 | 2361.5 | 2361.5 | 2361.5 | 2361.5 |
| All Data | FL lt 20 | All | All | 731.2 | 5.373 | Yes | 43.8 | 6.749 | Yes | 1/(FL^e) | 0.29 | 45.55 | Yes | 115 | 1606.9 | 1169.0 | 840.6 | 785.9 | 775.0 |
| Yes Data | FL ge 0 | All | All | 1186.3 | 26.161 | Yes | -647.5 | -8.148 | No | FL | 0.19 | 66.38 | Yes | 291 | 1186.3 | 1186.3 | 1186.3 | 1186.3 | 1186.3 |
| Yes Data | FL ge 0 | All | All | 648.6 | 33.957 | Yes | 44.1 | 23.374 | Yes | 1/(FL^e) | 0.65 | 546.34 | Yes | 291 | 1530.3 | 1089.4 | 758.8 | 703.7 | 692.7 |
| Yes Data | FL ge 20 | All | All | 819.5 | 66.563 | Yes | -132.5 | -7.072 | No | FL | 0.19 | 50.02 | Yes | 217 | 819.5 | 819.5 | 819.5 | 819.5 | 819.5 |
| Yes Data | FL lt 20 | All | All | 2207.6 | 12.978 | Yes | 8823.5 | -6.072 | No | FL | 0.34 | 36.86 | Yes | 74 | 2207.6 | 2207.6 | 2207.6 | 2207.6 | 2207.6 |
| Yes Data | FL lt 20 | All | All | 639.4 | 6.831 | Yes | 44.5 | 9.365 | Yes | 1/(FL^e) | 0.55 | 87.71 | Yes | 74 | 1529.4 | 1084.4 | 750.7 | 695.0 | 683.9 |
| Yes Data | FL ge 0 | Not Ind. | All | 1228.3 | 11.111 | Yes | -684.5 | -2.879 | No | FL | 0.26 | 8.29 | Yes | 26 | 1228.3 | 1228.3 | 1228.3 | 1228.3 | 1228.3 |
| Yes Data | FL ge 0 | 2 Stroke | All | 1045.2 | 8.284 | Yes | -479.9 | -2.099 | No | FL | 0.09 | 4.40 | No | 45 | 1045.2 | 1045.2 | 1045.2 | 1045.2 | 1045.2 |
| Yes Data | FL ge 0 | 4 Stroke | All | 1202.2 | 22.388 | Yes | -662.2 | -7.220 | No | FL | 0.19 | 52.13 | Yes | 220 | 1202.2 | 1202.2 | 1202.2 | 1202.2 | 1202.2 |
| Yes Data | FL ge 0 | Not Ind. | All | 742.8 | 36.310 | Yes | 24.5 | 22.528 | Yes | 1/(FL^e) | 0.95 | 507.49 | Yes | 26 | 1232.4 | 987.6 | 804.0 | 773.4 | 767.2 |
| Yes Data | FL ge 0 | 2 Stroke | All | 667.1 | 9.719 | Yes | 35.8 | 3.571 | Yes | 1/(FL^e) | 0.23 | 12.75 | Yes | 45 | 1382.6 | 1024.8 | 756.5 | 711.8 | 702.9 |
| Yes Data | FL ge 0 | 4 Stroke | All | 606.0 | 32.861 | Yes | 55.8 | 27.754 | Yes | 1/(FL^e) | 0.78 | 770.29 | Yes | 220 | 1721.6 | 1163.8 | 745.5 | 675.7 | 661.8 |
| Yes Data | FL ge 0 | All | Diesel | 1060.2 | 16.674 | Yes | -389.8 | -3.715 | No | FL | 0.23 | 13.80 | Yes | 49 | 1060.2 | 1060.2 | 1060.2 | 1060.2 | 1060.2 |
| Yes Data | FL ge 0 | All | Gas Oil | 1355.3 | 13.847 | Yes | -986.7 | -5.244 | No | FL | 0.20 | 27.50 | Yes | 114 | 1355.3 | 1355.3 | 1355.3 | 1355.3 | 1355.3 |
| Yes Data | FL ge 0 | All | Hvy FO | 939.8 | 23.391 | Yes | -302.1 | -4.464 | No | FL | 0.50 | 19.93 | Yes | 22 | 939.8 | 939.8 | 939.8 | 939.8 | 939.8 |
| Yes Data | FL ge 0 | All | Int FO | 680.3 | 3.872 | Yes | 72.7 | 0.225 | No | FL | 0.01 | 0.05 | No | 10 | 680.3 | 680.3 | 680.3 | 680.3 | 680.3 |
| Yes Data | FL ge 0 | All | Light FO | 1142.9 | 22.495 | Yes | -556.0 | -6.622 | No | FL | 0.32 | 43.85 | Yes | 96 | 1142.9 | 1142.9 | 1142.9 | 1142.9 | 1142.9 |
| Yes Data | FL ge 0 | All | Diesel | 721.3 | 28.580 | Yes | 22.5 | 13.065 | Yes | 1/(FL^e) | 0.78 | 170.71 | Yes | 49 | 1172.3 | 946.8 | 777.7 | 749.5 | 743.9 |
| Yes Data | FL ge 0 | All | Gas Oil | 574.8 | 15.544 | Yes | 59.5 | 18.240 | Yes | 1/(FL^e) | 0.75 | 332.68 | Yes | 114 | 1764.2 | 1169.5 | 723.5 | 649.1 | 634.3 |
| Yes Data | FL ge 0 | All | Hvy FO | 670.6 | 31.198 | Yes | 41.8 | 5.900 | Yes | 1/(FL^e) | 0.64 | 34.81 | Yes | 22 | 1506.5 | 1088.6 | 775.1 | 722.9 | 712.4 |
| Yes Data | FL ge 0 | All | Int FO | 820.3 | 7.151 | Yes | -31.8 | -1.197 | No | 1/(FL^e) | 0.15 | 1.43 | No | 10 | 820.3 | 820.3 | 820.3 | 820.3 | 820.3 |
| Yes Data | FL ge 0 | All | Light FO | 634.8 | 46.184 | Yes | 53.0 | 25.879 | Yes | 1/(FL^e) | 0.88 | 669.74 | Yes | 96 | 1695.4 | 1165.1 | 767.3 | 701.1 | 687.8 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 1228.3 | 11.111 | Yes | -684.5 | -2.879 | No | FL | 0.26 | 8.29 | Yes | 26 | 1228.3 | 1228.3 | 1228.3 | 1228.3 | 1228.3 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 733.4 | 73.288 | Yes | -28.2 | -1.413 | No | FL | 0.22 | 2.00 | No | 9 | 733.4 | 733.4 | 733.4 | 733.4 | 733.4 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 2407.9 | 2.562 | No | 2852.9 | -1.277 | No | FL | 0.45 | 1.63 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 939.8 | 23.391 | Yes | -302.1 | -4.464 | No | FL | 0.50 | 19.93 | Yes | 22 | 939.8 | 939.8 | 939.8 | 939.8 | 939.8 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 680.3 | 3.872 | Yes | 72.7 | 0.225 | No | FL | 0.01 | 0.05 | No | 10 | 680.3 | 680.3 | 680.3 | 680.3 | 680.3 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 982.6 | 22.744 | Yes | -273.4 | -5.378 | No | FL | 0.71 | 28.92 | Yes | 14 | 982.6 | 982.6 | 982.6 | 982.6 | 982.6 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 1308.4 | 13.646 | Yes | -915.1 | -4.995 | No | FL | 0.19 | 24.95 | Yes | 110 | 1308.4 | 1308.4 | 1308.4 | 1308.4 | 1308.4 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 1142.9 | 22.495 | Yes | -556.0 | -6.622 | No | FL | 0.32 | 43.85 | Yes | 96 | 1142.9 | 1142.9 | 1142.9 | 1142.9 | 1142.9 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 742.8 | 36.310 | Yes | 24.5 | 22.528 | Yes | 1/(FL^e) | 0.95 | 507.49 | Yes | 26 | 1232.4 | 987.6 | 804.0 | 773.4 | 767.2 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 710.3 | 143.907 | Yes | 1.7 | 3.983 | Yes | 1/(FL^e) | 0.69 | 15.86 | Yes | 9 | 744.5 | 727.4 | 714.5 | 712.4 | 712.0 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 395.8 | 3.159 | No | 133.6 | 12.357 | Yes | 1/(FL^e) | 0.99 | 152.70 | Yes | 4 | 2671.0 | 1335.5 | 333.9 | 166.9 | 133.6 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 670.6 | 31.198 | Yes | 41.8 | 5.900 | Yes | 1/(FL^e) | 0.64 | 34.81 | Yes | 22 | 1506.5 | 1088.6 | 775.1 | 722.9 | 712.4 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 820.3 | 7.151 | Yes | -31.8 | -1.197 | No | 1/(FL^e) | 0.15 | 1.43 | No | 10 | 820.3 | 820.3 | 820.3 | 820.3 | 820.3 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 586.2 | 7.950 | Yes | 98.9 | 3.215 | Yes | 1/(FL^e) | 0.46 | 10.34 | Yes | 14 | 2565.0 | 1575.6 | 833.6 | 709.9 | 685.2 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 573.7 | 16.696 | Yes | 57.1 | 18.836 | Yes | 1/(FL^e) | 0.77 | 354.79 | Yes | 110 | 1715.9 | 1144.8 | 716.5 | 645.1 | 630.8 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 634.8 | 46.184 | Yes | 53.0 | 25.879 | Yes | 1/(FL^e) | 0.88 | 669.74 | Yes | 96 | 1695.4 | 1165.1 | 767.3 | 701.1 | 687.8 |

| REGRESSION SUMMARY FOR: | O2 | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 17437.0 | 6.247 | Yes | -22996.0 | -4.405 | No | FL | 0.05 | 19.40 | Yes | 356 | 17437.0 | 17437.0 | 17437.0 | 17437.0 | 17437.0 |
| All Data | FL ge 0 | All | All | 3007.9 | 1.720 | No | 161.2 | 6.886 | Yes | 1/(FL^e) | 0.12 | 47.41 | Yes | 356 | 14421.9 | 5098.9 | 637.4 | 225.3 | 161.2 |
| All Data | FL ge 20 | All | All | 2378.7 | 21.528 | Yes | 1375.3 | -8.040 | No | FL | 0.21 | 64.64 | Yes | 241 | 2378.7 | 2378.7 | 2378.7 | 2378.7 | 2378.7 |
| All Data | FL lt 20 | All | All | 47341.0 | 4.810 | Yes | -302256.0 | -3.183 | No | FL | 0.08 | 10.13 | Yes | 115 | 47341.0 | 47341.0 | 47341.0 | 47341.0 | 47341.0 |
| All Data | FL lt 20 | All | All | 9630.8 | 1.513 | No | 130.8 | 2.698 | No | 1/(FL^e) | 0.06 | 7.28 | No | 115 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | All | 7798.3 | 9.080 | Yes | 9141.2 | -6.072 | No | FL | 0.11 | 36.87 | Yes | 291 | 7798.3 | 7798.3 | 7798.3 | 7798.3 | 7798.3 |
| Yes Data | FL ge 0 | All | All | 1298.1 | 4.101 | Yes | 107.9 | 22.769 | Yes | 1/(FL^e) | 0.64 | 518.42 | Yes | 291 | 10945.2 | 4708.8 | 1724.4 | 1448.8 | 1405.9 |
| Yes Data | FL ge 20 | All | All | 2130.4 | 22.334 | Yes | 1137.9 | -7.839 | No | FL | 0.22 | 61.45 | Yes | 217 | 2130.4 | 2130.4 | 2130.4 | 2130.4 | 2130.4 |
| Yes Data | FL lt 20 | All | All | 25276.0 | 7.256 | Yes | -152436.0 | -5.122 | No | FL | 0.27 | 26.24 | Yes | 74 | 25276.0 | 25276.0 | 25276.0 | 25276.0 | 25276.0 |
| Yes Data | FL lt 20 | All | All | 2076.7 | 1.484 | No | 104.8 | 9.917 | Yes | 1/(FL^e) | 0.58 | 98.34 | Yes | 74 | 9377.5 | 3315.5 | 414.4 | 146.5 | 104.8 |
| Yes Data | FL ge 0 | Not Ind. | All | 7018.9 | 4.036 | Yes | 9675.1 | -2.587 | No | FL | 0.22 | 6.69 | No | 26 | 7018.9 | 7018.9 | 7018.9 | 7018.9 | 7018.9 |
| Yes Data | FL ge 0 | 2 Stroke | All | 4761.9 | 9.196 | Yes | 4395.3 | -4.683 | No | FL | 0.34 | 21.93 | Yes | 45 | 4761.9 | 4761.9 | 4761.9 | 4761.9 | 4761.9 |
| Yes Data | FL ge 0 | 4 Stroke | All | 8415.0 | 7.630 | Yes | 9864.1 | -5.236 | No | FL | 0.11 | 27.42 | Yes | 220 | 8415.0 | 8415.0 | 8415.0 | 8415.0 | 8415.0 |
| Yes Data | FL ge 0 | Not Ind. | All | 1038.3 | 5.831 | Yes | 47.2 | 37.143 | Yes | 1/(FL^e) | 0.98 | 1379.57 | Yes | 26 | 5262.3 | 2531.7 | 1225.0 | 1104.3 | 1085.5 |
| Yes Data | FL ge 0 | 2 Stroke | All | 1999.4 | 9.461 | Yes | 51.3 | 7.767 | Yes | 1/(FL^e) | 0.58 | 60.33 | Yes | 45 | 6591.4 | 3622.9 | 2202.3 | 2071.1 | 2050.7 |
| Yes Data | FL ge 0 | 4 Stroke | All | 877.2 | 2.897 | Yes | 155.1 | 29.779 | Yes | 1/(FL^e) | 0.80 | 886.80 | Yes | 220 | 14749.4 | 5781.8 | 1490.3 | 1094.0 | 1032.3 |
| Yes Data | FL ge 0 | All | Diesel | 4711.8 | 4.819 | Yes | 4607.4 | -2.856 | No | FL | 0.15 | 8.16 | Yes | 49 | 4711.8 | 4711.8 | 4711.8 | 4711.8 | 4711.8 |
| Yes Data | FL ge 0 | All | Gas Oil | 10081.0 | 5.295 | Yes | -13574.0 | -3.709 | No | FL | 0.11 | 13.76 | Yes | 114 | 10081.0 | 10081.0 | 10081.0 | 10081.0 | 10081.0 |
| Yes Data | FL ge 0 | All | Hvy FO | 4830.9 | 7.861 | Yes | 4262.3 | -4.118 | No | FL | 0.46 | 16.96 | Yes | 22 | 4830.9 | 4830.9 | 4830.9 | 4830.9 | 4830.9 |
| Yes Data | FL ge 0 | All | Int FO | 4385.2 | 4.346 | Yes | 3544.2 | -1.915 | No | FL | 0.31 | 3.67 | No | 10 | 4385.2 | 4385.2 | 4385.2 | 4385.2 | 4385.2 |
| Yes Data | FL ge 0 | All | Light FO | 7885.8 | 7.613 | Yes | 8944.3 | -5.225 | No | FL | 0.23 | 27.31 | Yes | 96 | 7885.8 | 7885.8 | 7885.8 | 7885.8 | 7885.8 |
| Yes Data | FL ge 0 | All | Diesel | 968.0 | 9.310 | Yes | 47.4 | 48.006 | Yes | 1/(FL^e) | 0.98 | 2304.57 | Yes | 49 | 5211.2 | 2468.2 | 1155.6 | 1034.3 | 1015.5 |
| Yes Data | FL ge 0 | All | Gas Oil | 580.4 | 1.196 | No | 152.5 | 24.247 | Yes | 1/(FL^e) | 0.84 | 587.90 | Yes | 114 | 13638.7 | 4822.0 | 602.7 | 213.1 | 152.5 |
| Yes Data | FL ge 0 | All | Hvy FO | 1578.6 | 6.138 | Yes | 199.7 | 5.418 | Yes | 1/(FL^e) | 0.59 | 29.36 | Yes | 22 | 19441.7 | 7894.2 | 2368.0 | 1857.7 | 1778.3 |
| Yes Data | FL ge 0 | All | Int FO | 2385.1 | 3.481 | No | 38.0 | 0.670 | No | 1/(FL^e) | 0.05 | 0.45 | No | 10 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Light FO | 1016.8 | 2.438 | No | 177.4 | 11.914 | Yes | 1/(FL^e) | 0.60 | 141.94 | Yes | 96 | 15869.4 | 5610.7 | 701.3 | 248.0 | 177.4 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 7018.9 | 4.036 | Yes | 9675.1 | -2.587 | No | FL | 0.22 | 6.69 | No | 26 | 7018.9 | 7018.9 | 7018.9 | 7018.9 | 7018.9 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 4082.7 | 3.220 | No | 4183.2 | -1.653 | No | FL | 0.28 | 2.73 | No | 9 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 6724.9 | 2.253 | No | 8951.3 | -1.262 | No | FL | 0.44 | 1.59 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 4830.9 | 7.861 | Yes | 4262.3 | -4.118 | No | FL | 0.46 | 16.96 | Yes | 22 | 4830.9 | 4830.9 | 4830.9 | 4830.9 | 4830.9 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 4385.2 | 4.346 | Yes | 3544.2 | -1.915 | No | FL | 0.31 | 3.67 | No | 10 | 4385.2 | 4385.2 | 4385.2 | 4385.2 | 4385.2 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 1329.9 | 4.721 | Yes | -579.7 | -1.749 | No | FL | 0.20 | 3.06 | No | 14 | 1329.9 | 1329.9 | 1329.9 | 1329.9 | 1329.9 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 10238.0 | 5.173 | Yes | -13783.0 | -3.645 | No | FL | 0.11 | 13.29 | Yes | 110 | 10238.0 | 10238.0 | 10238.0 | 10238.0 | 10238.0 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 7885.8 | 7.613 | Yes | 8944.3 | -5.225 | No | FL | 0.23 | 27.31 | Yes | 96 | 7885.8 | 7885.8 | 7885.8 | 7885.8 | 7885.8 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 1038.3 | 5.831 | Yes | 47.2 | 37.143 | Yes | 1/(FL^e) | 0.98 | 1379.57 | Yes | 26 | 5262.3 | 2531.7 | 1225.0 | 1104.3 | 1085.5 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 1132.5 | 41.841 | Yes | 46.4 | 102.674 | Yes | 1/(FL^e) | 1.00 | 10542.03 | Yes | 9 | 5283.6 | 2600.2 | 1316.0 | 1197.4 | 1179.0 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 1194.0 | 10.283 | Yes | 82.9 | 37.767 | Yes | 1/(FL^e) | 1.00 | 1426.33 | Yes | 4 | 8608.3 | 3815.4 | 1521.7 | 1309.9 | 1276.9 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 1578.6 | 6.138 | Yes | 199.7 | 5.418 | Yes | 1/(FL^e) | 0.59 | 29.36 | Yes | 22 | 19441.7 | 7894.2 | 2368.0 | 1857.7 | 1778.3 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 2385.1 | 3.481 | No | 38.0 | 0.670 | No | 1/(FL^e) | 0.05 | 0.45 | No | 10 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 312.8 | 1.501 | No | 182.5 | 3.752 | Yes | 1/(FL^e) | 0.54 | 14.08 | Yes | 14 | 16320.5 | 5770.2 | 721.3 | 255.0 | 182.5 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 615.3 | 1.236 | No | 153.4 | 24.010 | Yes | 1/(FL^e) | 0.84 | 576.47 | Yes | 110 | 13720.3 | 4850.9 | 606.4 | 214.4 | 153.4 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 1016.8 | 2.438 | No | 177.4 | 11.914 | Yes | 1/(FL^e) | 0.60 | 141.94 | Yes | 96 | 15869.4 | 5610.7 | 701.3 | 248.0 | 177.4 |

| REGRESSION SUMMARY FOR: | HC | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 8.3003 | 8.497 | Yes | -10.9026 | -6.050 | No | FL | 0.10 | 36.60 | Yes | 321 | 8.300 | 8.300 | 8.300 | 8.300 | 8.300 |
| All Data | FL ge 0 | All | All | 1.1654 | 2.036 | No | 0.0810 | 11.057 | Yes | 1/(FL^e) | 0.28 | 122.26 | Yes | 321 | 7.249 | 2.563 | 0.320 | 0.113 | 0.081 |
| All Data | FL ge 20 | All | All | 0.9744 | 12.004 | Yes | -0.5558 | -4.478 | No | FL | 0.09 | 20.06 | Yes | 218 | 0.974 | 0.974 | 0.974 | 0.974 | 0.974 |
| All Data | FL lt 20 | All | All | 22.1000 | 6.861 | Yes | -141.1223 | -4.437 | No | FL | 0.16 | 19.69 | Yes | 103 | 22.100 | 22.100 | 22.100 | 22.100 | 22.100 |
| All Data | FL lt 20 | All | All | 3.8756 | 1.846 | No | 0.0691 | 4.530 | Yes | 1/(FL^e) | 0.17 | 20.52 | Yes | 103 | 6.178 | 2.184 | 0.273 | 0.097 | 0.069 |
| Yes Data | FL ge 0 | All | All | 4.1802 | 6.502 | Yes | -5.0538 | -4.513 | No | FL | 0.07 | 20.37 | Yes | 271 | 4.180 | 4.180 | 4.180 | 4.180 | 4.180 |
| Yes Data | FL ge 0 | All | All | 0.3859 | 1.429 | No | 0.0667 | 17.064 | Yes | 1/(FL^e) | 0.52 | 291.17 | Yes | 271 | 5.970 | 2.111 | 0.264 | 0.093 | 0.067 |
| Yes Data | FL ge 20 | All | All | 0.8851 | 11.272 | Yes | -0.4455 | -3.762 | No | FL | 0.07 | 14.16 | Yes | 201 | 0.885 | 0.885 | 0.885 | 0.885 | 0.885 |
| Yes Data | FL lt 20 | All | All | 14.0632 | 5.101 | Yes | -86.3093 | -3.656 | No | FL | 0.16 | 13.37 | Yes | 70 | 14.063 | 14.063 | 14.063 | 14.063 | 14.063 |
| Yes Data | FL lt 20 | All | All | 0.3131 | 0.265 | No | 0.0670 | 7.710 | Yes | 1/(FL^e) | 0.47 | 59.45 | Yes | 70 | 5.995 | 2.120 | 0.265 | 0.094 | 0.067 |
| Yes Data | FL ge 0 | Not Ind. | All | 1.7494 | 3.541 | Yes | -2.6120 | -2.321 | No | FL | 0.21 | 5.39 | No | 22 | 1.749 | 1.749 | 1.749 | 1.749 | 1.749 |
| Yes Data | FL ge 0 | 2 Stroke | All | 0.7667 | 3.957 | Yes | -0.3210 | -0.904 | No | FL | 0.02 | 0.82 | No | 43 | 0.767 | 0.767 | 0.767 | 0.767 | 0.767 |
| Yes Data | FL ge 0 | 4 Stroke | All | 5.1403 | 6.175 | Yes | -6.1653 | -4.388 | No | FL | 0.09 | 19.25 | Yes | 206 | 5.140 | 5.140 | 5.140 | 5.140 | 5.140 |
| Yes Data | FL ge 0 | Not Ind. | All | 0.1789 | 1.807 | No | 0.0113 | 17.361 | Yes | 1/(FL^e) | 0.94 | 301.40 | Yes | 22 | 1.010 | 0.357 | 0.045 | 0.016 | 0.011 |
| Yes Data | FL ge 0 | 2 Stroke | All | 0.5473 | 5.503 | Yes | 0.0052 | 1.705 | No | 1/(FL^e) | 0.07 | 2.91 | No | 43 | 0.547 | 0.547 | 0.547 | 0.547 | 0.547 |
| Yes Data | FL ge 0 | 4 Stroke | All | 0.1150 | 0.543 | No | 0.1106 | 31.223 | Yes | 1/(FL^e) | 0.83 | 974.85 | Yes | 206 | 9.890 | 3.497 | 0.437 | 0.155 | 0.111 |
| Yes Data | FL ge 0 | All | Diesel | 0.9475 | 3.450 | Yes | -0.9892 | -2.214 | No | FL | 0.11 | 4.90 | No | 42 | 0.947 | 0.947 | 0.947 | 0.947 | 0.947 |
| Yes Data | FL ge 0 | All | Gas Oil | 6.0535 | 4.370 | Yes | -8.1345 | -3.055 | No | FL | 0.08 | 9.33 | Yes | 114 | 6.054 | 6.054 | 6.054 | 6.054 | 6.054 |
| Yes Data | FL ge 0 | All | Hvy FO | 1.0406 | 4.630 | Yes | -0.7845 | -2.046 | No | FL | 0.19 | 4.19 | No | 20 | 1.041 | 1.041 | 1.041 | 1.041 | 1.041 |
| Yes Data | FL ge 0 | All | Int FO | 0.1605 | 0.575 | No | 1.3609 | 2.658 | No | FL | 0.47 | 7.06 | No | 10 |  |  |  |  |  |
| Yes Data | FL ge 0 | All | Light FO | 4.7410 | 6.578 | Yes | -5.6510 | -4.871 | No | FL | 0.22 | 23.73 | Yes | 85 | 4.741 | 4.741 | 4.741 | 4.741 | 4.741 |
| Yes Data | FL ge 0 | All | Diesel | 0.0657 | 0.969 | No | 0.0110 | 18.455 | Yes | 1/(FL^e) | 0.89 | 340.58 | Yes | 42 | 0.985 | 0.348 | 0.044 | 0.015 | 0.011 |
| Yes Data | FL ge 0 | All | Gas Oil | -0.0980 | -0.301 | No | 0.1102 | 26.184 | Yes | 1/(FL^e) | 0.86 | 685.59 | Yes | 114 | 9.860 | 3.486 | 0.436 | 0.154 | 0.110 |
| Yes Data | FL ge 0 | All | Hvy FO | 0.5361 | 4.376 | Yes | 0.0167 | 0.995 | No | 1/(FL^e) | 0.05 | 0.99 | No | 20 | 0.536 | 0.536 | 0.536 | 0.536 | 0.536 |
| Yes Data | FL ge 0 | All | Int FO | 1.0607 | 6.147 | Yes | -0.0325 | -2.273 | No | 1/(FL^e) | 0.39 | 5.17 | No | 10 | 1.061 | 1.061 | 1.061 | 1.061 | 1.061 |
| Yes Data | FL ge 0 | All | Light FO | 0.4183 | 1.347 | No | 0.1051 | 9.612 | Yes | 1/(FL^e) | 0.53 | 92.40 | Yes | 85 | 9.404 | 3.325 | 0.416 | 0.147 | 0.105 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 1.7494 | 3.541 | Yes | -2.6120 | -2.321 | No | FL | 0.21 | 5.39 | No | 22 | 1.749 | 1.749 | 1.749 | 1.749 | 1.749 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 0.2060 | 3.164 | No | -0.1509 | -1.162 | No | FL | 0.16 | 1.35 | No | 9 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 2.2633 | 2.224 | No | -3.4396 | -1.422 | No | FL | 0.50 | 2.02 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 1.0406 | 4.630 | Yes | -0.7845 | -2.046 | No | FL | 0.19 | 4.19 | No | 20 | 1.041 | 1.041 | 1.041 | 1.041 | 1.041 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 0.1605 | 0.575 | No | 1.3609 | 2.658 | No | FL | 0.47 | 7.06 | No | 10 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 0.0218 | 2.350 | No | 0.0059 | 0.589 | No | FL | 0.04 | 0.35 | No | 11 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 6.2336 | 4.330 | Yes | -8.3627 | -3.041 | No | FL | 0.08 | 9.25 | Yes | 110 | 6.234 | 6.234 | 6.234 | 6.234 | 6.234 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 4.7410 | 6.578 | Yes | -5.6510 | -4.871 | No | FL | 0.22 | 23.73 | Yes | 85 | 4.741 | 4.741 | 4.741 | 4.741 | 4.741 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 0.1789 | 1.807 | No | 0.0113 | 17.361 | Yes | 1/(FL^e) | 0.94 | 301.40 | Yes | 22 | 1.010 | 0.357 | 0.045 | 0.016 | 0.011 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 0.0999 | 3.036 | No | 0.0017 | 3.023 | No | 1/(FL^e) | 0.57 | 9.14 | No | 9 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 0.2000 | 2.820 | No | 0.0299 | 22.278 | Yes | 1/(FL^e) | 1.00 | 496.29 | Yes | 4 | 2.672 | 0.945 | 0.118 | 0.042 | 0.030 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 0.5361 | 4.376 | Yes | 0.0167 | 0.995 | No | 1/(FL^e) | 0.05 | 0.99 | No | 20 | 0.536 | 0.536 | 0.536 | 0.536 | 0.536 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 1.0607 | 6.147 | Yes | -0.0325 | -2.273 | No | 1/(FL^e) | 0.39 | 5.17 | No | 10 | 1.061 | 1.061 | 1.061 | 1.061 | 1.061 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 0.0235 | 2.608 | No | 0.0009 | 0.370 | No | 1/(FL^e) | 0.02 | 0.14 | No | 11 |  |  |  |  |  |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | -0.0432 | -0.132 | No | 0.1113 | 26.559 | Yes | 1/(FL^e) | 0.87 | 705.36 | Yes | 110 | 9.956 | 3.520 | 0.440 | 0.156 | 0.111 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 0.4183 | 1.347 | No | 0.1051 | 9.612 | Yes | 1/(FL^e) | 0.53 | 92.40 | Yes | 85 | 9.404 | 3.325 | 0.416 | 0.147 | 0.105 |

| REGRESSION SUMMARY FOR: | Dry Exhaust Mass | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 81773 | 6.739 | Yes | -103985 | -4.582 | No | FL | 0.06 | 21.00 | Yes | 356 | 81773.0 | 81773.0 | 81773.0 | 81773.0 | 81773.0 |
| All Data | FL ge 0 | All | All | 16654 | 2.196 | No | 725 | 7.136 | Yes | 1/(FL^e) | 0.13 | 50.92 | Yes | 356 | 64821.6 | 22917.9 | 2864.7 | 1012.8 | 724.7 |
| All Data | FL ge 20 | All | All | 13974 | 29.048 | Yes | 6660 | -8.942 | No | FL | 0.25 | 79.96 | Yes | 241 | 13974.0 | 13974.0 | 13974.0 | 13974.0 | 13974.0 |
| All Data | FL lt 20 | All | All | 215837 | 5.064 | Yes | -1354570 | -3.294 | No | FL | 0.09 | 10.85 | Yes | 115 | 215837.0 | 215837.0 | 215837.0 | 215837.0 | 215837.0 |
| All Data | FL lt 20 | All | All | 46871 | 1.699 | No | 586 | 2.788 | Yes | 1/(FL^e) | 0.06 | 7.77 | Yes | 115 | 52414.7 | 18531.4 | 2316.4 | 819.0 | 586.0 |
| Yes Data | FL ge 0 | All | All | 38787 | 10.070 | Yes | -42156 | -6.244 | No | FL | 0.12 | 38.99 | Yes | 291 | 38787.0 | 38787.0 | 38787.0 | 38787.0 | 38787.0 |
| Yes Data | FL ge 0 | All | All | 8982 | 6.390 | Yes | 489 | 23.239 | Yes | 1/(FL^e) | 0.65 | 540.03 | Yes | 291 | 52701.8 | 24439.3 | 10914.2 | 9665.2 | 9470.9 |
| Yes Data | FL ge 20 | All | All | 12856 | 30.853 | Yes | 5551 | -8.754 | No | FL | 0.26 | 76.63 | Yes | 217 | 12856.0 | 12856.0 | 12856.0 | 12856.0 | 12856.0 |
| Yes Data | FL lt 20 | All | All | 118345 | 7.628 | Yes | -693710 | -5.234 | No | FL | 0.28 | 27.39 | Yes | 74 | 118345.0 | 118345.0 | 118345.0 | 118345.0 | 118345.0 |
| Yes Data | FL lt 20 | All | All | 13054 | 2.103 | No | 473 | 10.086 | Yes | 1/(FL^e) | 0.59 | 101.73 | Yes | 74 | 42309.6 | 14958.7 | 1869.8 | 661.1 | 473.0 |
| Yes Data | FL ge 0 | Not Ind. | All | 35710 | 4.504 | Yes | -44675 | -2.620 | No | FL | 0.22 | 6.86 | No | 26 | 35710.0 | 35710.0 | 35710.0 | 35710.0 | 35710.0 |
| Yes Data | FL ge 0 | 2 Stroke | All | 25164 | 9.547 | Yes | -21223 | -4.442 | No | FL | 0.31 | 19.73 | Yes | 45 | 25164.0 | 25164.0 | 25164.0 | 25164.0 | 25164.0 |
| Yes Data | FL ge 0 | 4 Stroke | All | 41490 | 8.401 | Yes | -45285 | -5.368 | No | FL | 0.12 | 28.82 | Yes | 220 | 41490.0 | 41490.0 | 41490.0 | 41490.0 | 41490.0 |
| Yes Data | FL ge 0 | Not Ind. | All | 8207 | 10.211 | Yes | 216 | 37.625 | Yes | 1/(FL^e) | 0.98 | 1415.64 | Yes | 26 | 27522.5 | 15036.4 | 9061.1 | 8509.3 | 8423.4 |
| Yes Data | FL ge 0 | 2 Stroke | All | 11780 | 10.838 | Yes | 252 | 7.401 | Yes | 1/(FL^e) | 0.56 | 54.77 | Yes | 45 | 34284.1 | 19736.4 | 12774.5 | 12131.6 | 12031.6 |
| Yes Data | FL ge 0 | 4 Stroke | All | 7100 | 5.325 | Yes | 700 | 30.514 | Yes | 1/(FL^e) | 0.81 | 931.13 | Yes | 220 | 69690.4 | 29229.0 | 9866.1 | 8078.0 | 7799.8 |
| Yes Data | FL ge 0 | All | Diesel | 25056 | 5.642 | Yes | -21595 | -2.946 | No | FL | 0.16 | 8.68 | Yes | 49 | 25056.0 | 25056.0 | 25056.0 | 25056.0 | 25056.0 |
| Yes Data | FL ge 0 | All | Gas Oil | 49392 | 5.783 | Yes | -62686 | -3.818 | No | FL | 0.12 | 14.57 | Yes | 114 | 49392.0 | 49392.0 | 49392.0 | 49392.0 | 49392.0 |
| Yes Data | FL ge 0 | All | Hvy FO | 24582 | 9.202 | Yes | -19331 | -4.297 | No | FL | 0.48 | 18.47 | Yes | 22 | 24582.0 | 24582.0 | 24582.0 | 24582.0 | 24582.0 |
| Yes Data | FL ge 0 | All | Int FO | 21717 | 4.339 | Yes | -14896 | -1.623 | No | FL | 0.25 | 2.63 | No | 10 | 21717.0 | 21717.0 | 21717.0 | 21717.0 | 21717.0 |
| Yes Data | FL ge 0 | All | Light FO | 38883 | 8.479 | Yes | -40817 | -5.386 | No | FL | 0.24 | 29.01 | Yes | 96 | 38883.0 | 38883.0 | 38883.0 | 38883.0 | 38883.0 |
| Yes Data | FL ge 0 | All | Diesel | 7715 | 15.764 | Yes | 216 | 46.522 | Yes | 1/(FL^e) | 0.98 | 2164.33 | Yes | 49 | 27070.0 | 14558.1 | 8570.5 | 8017.5 | 7931.5 |
| Yes Data | FL ge 0 | All | Gas Oil | 5900 | 2.745 | No | 688 | 24.725 | Yes | 1/(FL^e) | 0.85 | 611.34 | Yes | 114 | 61579.4 | 21771.6 | 2721.5 | 962.2 | 688.5 |
| Yes Data | FL ge 0 | All | Hvy FO | 9835 | 8.921 | Yes | 905 | 5.729 | Yes | 1/(FL^e) | 0.62 | 32.82 | Yes | 22 | 90791.8 | 38457.2 | 13412.3 | 11099.5 | 10739.6 |
| Yes Data | FL ge 0 | All | Int FO | 13652 | 4.138 | Yes | 114 | 0.416 | No | 1/(FL^e) | 0.02 | 0.17 | No | 10 | 13652.0 | 13652.0 | 13652.0 | 13652.0 | 13652.0 |
| Yes Data | FL ge 0 | All | Light FO | 7526 | 4.210 | Yes | 811 | 12.697 | Yes | 1/(FL^e) | 0.63 | 161.23 | Yes | 96 | 80024.7 | 33158.1 | 10729.9 | 8658.6 | 8336.4 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 35710 | 4.504 | Yes | -44675 | -2.620 | No | FL | 0.22 | 6.86 | No | 26 | 35710.0 | 35710.0 | 35710.0 | 35710.0 | 35710.0 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 20751 | 3.847 | Yes | -17801 | -1.653 | No | FL | 0.28 | 2.73 | No | 9 | 20751.0 | 20751.0 | 20751.0 | 20751.0 | 20751.0 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 40881 | 2.327 | No | -52924 | -1.268 | No | FL | 0.45 | 1.61 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 24582 | 9.202 | Yes | -19331 | -4.297 | No | FL | 0.48 | 18.47 | Yes | 22 | 24582.0 | 24582.0 | 24582.0 | 24582.0 | 24582.0 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 21717 | 4.339 | Yes | -14896 | -1.623 | No | FL | 0.25 | 2.63 | No | 10 | 21717.0 | 21717.0 | 21717.0 | 21717.0 | 21717.0 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 10269 | 7.703 | Yes | 3880 | -2.474 | No | FL | 0.34 | 6.12 | No | 14 | 10269.0 | 10269.0 | 10269.0 | 10269.0 | 10269.0 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 49800 | 5.609 | Yes | -63187 | -3.725 | No | FL | 0.11 | 13.88 | Yes | 110 | 49800.0 | 49800.0 | 49800.0 | 49800.0 | 49800.0 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 38883 | 8.479 | Yes | -40817 | -5.386 | No | FL | 0.24 | 29.01 | Yes | 96 | 38883.0 | 38883.0 | 38883.0 | 38883.0 | 38883.0 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 8207 | 10.211 | Yes | 216 | 37.625 | Yes | 1/(FL^e) | 0.98 | 1415.64 | Yes | 26 | 27522.5 | 15036.4 | 9061.1 | 8509.3 | 8423.4 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 8199 | 67.122 | Yes | 197 | 96.782 | Yes | 1/(FL^e) | 1.00 | 9366.66 | Yes | 9 | 25857.0 | 14442.2 | 8979.6 | 8475.1 | 8396.6 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 8215 | 13.124 | Yes | 489 | 41.328 | Yes | 1/(FL^e) | 1.00 | 1707.97 | Yes | 4 | 51952.0 | 23678.6 | 10148.3 | 8898.7 | 8704.3 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 9835 | 8.921 | Yes | 905 | 5.729 | Yes | 1/(FL^e) | 0.62 | 32.82 | Yes | 22 | 90791.8 | 38457.2 | 13412.3 | 11099.5 | 10739.6 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 13652 | 4.138 | Yes | 114 | 0.416 | No | 1/(FL^e) | 0.02 | 0.17 | No | 10 | 13652.0 | 13652.0 | 13652.0 | 13652.0 | 13652.0 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 4285 | 4.130 | Yes | 979 | 4.044 | Yes | 1/(FL^e) | 0.58 | 16.36 | Yes | 14 | 91857.6 | 35246.4 | 8154.9 | 5653.0 | 5263.8 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 5980 | 2.699 | No | 691 | 24.304 | Yes | 1/(FL^e) | 0.85 | 590.69 | Yes | 110 | 61811.2 | 21853.6 | 2731.7 | 965.8 | 691.1 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 7526 | 4.210 | Yes | 811 | 12.697 | Yes | 1/(FL^e) | 0.63 | 161.23 | Yes | 96 | 80024.7 | 33158.1 | 10729.9 | 8658.6 | 8336.4 |

| REGRESSION SUMMARY FOR: | H2O | Exponent = | 1 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 477.17 | 29.543 | Yes | -331.90 | -10.987 | No | FL | 0.25 | 120.72 | Yes | 356 | 477.17 | 477.17 | 477.17 | 477.17 | 477.17 |
| All Data | FL ge 0 | All | All | 222.44 | 25.956 | Yes | 16.49 | 23.250 | Yes | 1/(FL^e) | 0.60 | 540.55 | Yes | 356 | 552.25 | 387.35 | 263.67 | 243.05 | 238.93 |
| All Data | FL ge 20 | All | All | 280.42 | 57.875 | Yes | -51.20 | -6.824 | No | FL | 0.16 | 46.57 | Yes | 241 | 280.42 | 280.42 | 280.42 | 280.42 | 280.42 |
| All Data | FL lt 20 | All | All | 825.06 | 18.584 | Yes | 3478.26 | -8.121 | No | FL | 0.37 | 65.94 | Yes | 115 | 825.06 | 825.06 | 825.06 | 825.06 | 825.06 |
| All Data | FL lt 20 | All | All | 259.05 | 7.286 | Yes | 15.20 | 8.966 | Yes | 1/(FL^e) | 0.42 | 80.40 | Yes | 115 | 563.00 | 411.03 | 297.04 | 278.05 | 274.25 |
| Yes Data | FL ge 0 | All | All | 416.44 | 24.781 | Yes | -238.44 | -8.095 | No | FL | 0.18 | 65.53 | Yes | 291 | 416.44 | 416.44 | 416.44 | 416.44 | 416.44 |
| Yes Data | FL ge 0 | All | All | 220.09 | 29.806 | Yes | 15.92 | 21.839 | Yes | 1/(FL^e) | 0.62 | 476.93 | Yes | 291 | 538.52 | 379.31 | 259.89 | 239.99 | 236.01 |
| Yes Data | FL ge 20 | All | All | 284.37 | 56.590 | Yes | -53.02 | -6.933 | No | FL | 0.18 | 48.07 | Yes | 217 | 284.37 | 284.37 | 284.37 | 284.37 | 284.37 |
| Yes Data | FL lt 20 | All | All | 782.36 | 12.204 | Yes | 3163.97 | -5.777 | No | FL | 0.32 | 33.38 | Yes | 74 | 782.36 | 782.36 | 782.36 | 782.36 | 782.36 |
| Yes Data | FL lt 20 | All | All | 220.34 | 6.104 | Yes | 15.94 | 8.698 | Yes | 1/(FL^e) | 0.51 | 75.65 | Yes | 74 | 539.05 | 379.69 | 260.18 | 240.26 | 236.27 |
| Yes Data | FL ge 0 | Not Ind. | All | 423.18 | 11.379 | Yes | -236.35 | -2.955 | No | FL | 0.27 | 8.73 | Yes | 26 | 423.18 | 423.18 | 423.18 | 423.18 | 423.18 |
| Yes Data | FL ge 0 | 2 Stroke | All | 366.65 | 6.640 | Yes | -210.79 | -2.106 | No | FL | 0.09 | 4.44 | No | 45 | 366.65 | 366.65 | 366.65 | 366.65 | 366.65 |
| Yes Data | FL ge 0 | 4 Stroke | All | 424.42 | 21.963 | Yes | -241.36 | -7.312 | No | FL | 0.20 | 53.47 | Yes | 220 | 424.42 | 424.42 | 424.42 | 424.42 | 424.42 |
| Yes Data | FL ge 0 | Not Ind. | All | 257.01 | 38.289 | Yes | 8.30 | 23.289 | Yes | 1/(FL^e) | 0.96 | 542.37 | Yes | 26 | 423.10 | 340.05 | 277.77 | 267.39 | 265.31 |
| Yes Data | FL ge 0 | 2 Stroke | All | 198.53 | 6.678 | Yes | 16.22 | 3.739 | Yes | 1/(FL^e) | 0.25 | 13.98 | Yes | 45 | 522.93 | 360.73 | 239.08 | 218.81 | 214.75 |
| Yes Data | FL ge 0 | 4 Stroke | All | 208.46 | 30.979 | Yes | 20.06 | 27.350 | Yes | 1/(FL^e) | 0.77 | 748.01 | Yes | 220 | 609.57 | 409.02 | 258.60 | 233.53 | 228.52 |
| Yes Data | FL ge 0 | All | Diesel | 366.09 | 17.044 | Yes | -136.04 | -3.838 | No | FL | 0.24 | 14.73 | Yes | 49 | 366.09 | 366.09 | 366.09 | 366.09 | 366.09 |
| Yes Data | FL ge 0 | All | Gas Oil | 498.35 | 13.593 | Yes | -362.12 | -5.138 | No | FL | 0.19 | 26.40 | Yes | 114 | 498.35 | 498.35 | 498.35 | 498.35 | 498.35 |
| Yes Data | FL ge 0 | All | Hvy FO | 275.59 | 23.913 | Yes | -78.35 | -4.037 | No | FL | 0.45 | 16.30 | Yes | 22 | 275.59 | 275.59 | 275.59 | 275.59 | 275.59 |
| Yes Data | FL ge 0 | All | Int FO | 200.29 | 3.937 | Yes | 21.87 | 0.234 | No | FL | 0.01 | 0.06 | No | 10 | 200.29 | 200.29 | 200.29 | 200.29 | 200.29 |
| Yes Data | FL ge 0 | All | Light FO | 380.12 | 23.514 | Yes | -190.68 | -7.138 | No | FL | 0.35 | 50.95 | Yes | 96 | 380.12 | 380.12 | 380.12 | 380.12 | 380.12 |
| Yes Data | FL ge 0 | All | Diesel | 249.71 | 28.157 | Yes | 7.61 | 12.542 | Yes | 1/(FL^e) | 0.77 | 157.31 | Yes | 49 | 401.83 | 325.77 | 268.72 | 259.21 | 257.31 |
| Yes Data | FL ge 0 | All | Gas Oil | 212.09 | 14.629 | Yes | 21.80 | 17.051 | Yes | 1/(FL^e) | 0.72 | 290.73 | Yes | 114 | 648.02 | 430.06 | 266.58 | 239.34 | 233.89 |
| Yes Data | FL ge 0 | All | Hvy FO | 205.72 | 32.352 | Yes | 10.86 | 5.181 | Yes | 1/(FL^e) | 0.57 | 26.84 | Yes | 22 | 422.87 | 314.30 | 232.86 | 219.29 | 216.58 |
| Yes Data | FL ge 0 | All | Int FO | 242.25 | 7.336 | Yes | -9.52 | -1.244 | No | 1/(FL^e) | 0.16 | 1.55 | No | 10 | 242.25 | 242.25 | 242.25 | 242.25 | 242.25 |
| Yes Data | FL ge 0 | All | Light FO | 209.17 | 48.104 | Yes | 17.37 | 26.800 | Yes | 1/(FL^e) | 0.88 | 718.24 | Yes | 96 | 556.66 | 382.92 | 252.60 | 230.88 | 226.54 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 423.18 | 11.379 | Yes | -236.35 | -2.955 | No | FL | 0.27 | 8.73 | Yes | 26 | 423.18 | 423.18 | 423.18 | 423.18 | 423.18 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 248.95 | 415.284 | Yes | 0.06 | 0.053 | No | FL | 0.00 | 0.00 | No | 9 | 248.95 | 248.95 | 248.95 | 248.95 | 248.95 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 1003.21 | 2.547 | No | 1202.47 | -1.285 | No | FL | 0.45 | 1.65 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 275.59 | 23.913 | Yes | -78.35 | -4.037 | No | FL | 0.45 | 16.30 | Yes | 22 | 275.59 | 275.59 | 275.59 | 275.59 | 275.59 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 200.29 | 3.937 | Yes | 21.87 | 0.234 | No | FL | 0.01 | 0.06 | No | 10 | 200.29 | 200.29 | 200.29 | 200.29 | 200.29 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 343.21 | 24.260 | Yes | -100.48 | -6.036 | No | FL | 0.75 | 36.44 | Yes | 14 | 343.21 | 343.21 | 343.21 | 343.21 | 343.21 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 475.58 | 13.613 | Yes | -328.57 | -4.923 | No | FL | 0.18 | 24.23 | Yes | 110 | 475.58 | 475.58 | 475.58 | 475.58 | 475.58 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 380.12 | 23.514 | Yes | -190.68 | -7.138 | No | FL | 0.35 | 50.95 | Yes | 96 | 380.12 | 380.12 | 380.12 | 380.12 | 380.12 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 257.01 | 38.289 | Yes | 8.30 | 23.289 | Yes | 1/(FL^e) | 0.96 | 542.37 | Yes | 26 | 423.10 | 340.05 | 277.77 | 267.39 | 265.31 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 248.92 | 529.531 | Yes | 0.01 | 0.196 | No | 1/(FL^e) | 0.01 | 0.04 | No | 9 | 248.92 | 248.92 | 248.92 | 248.92 | 248.92 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 156.49 | 3.046 | No | 56.12 | 12.662 | Yes | 1/(FL^e) | 0.99 | 160.34 | Yes | 4 | 1122.49 | 561.24 | 140.31 | 70.16 | 56.12 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 205.72 | 32.352 | Yes | 10.86 | 5.181 | Yes | 1/(FL^e) | 0.57 | 26.84 | Yes | 22 | 422.87 | 314.30 | 232.86 | 219.29 | 216.58 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 242.25 | 7.336 | Yes | -9.52 | -1.244 | No | 1/(FL^e) | 0.16 | 1.55 | No | 10 | 242.25 | 242.25 | 242.25 | 242.25 | 242.25 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 197.86 | 7.716 | Yes | 36.20 | 3.383 | Yes | 1/(FL^e) | 0.49 | 11.44 | Yes | 14 | 921.87 | 559.86 | 288.36 | 243.11 | 234.06 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 210.71 | 16.687 | Yes | 20.68 | 18.560 | Yes | 1/(FL^e) | 0.76 | 344.46 | Yes | 110 | 624.33 | 417.52 | 262.42 | 236.56 | 231.39 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 209.17 | 48.104 | Yes | 17.37 | 26.800 | Yes | 1/(FL^e) | 0.88 | 718.24 | Yes | 96 | 556.66 | 382.92 | 252.60 | 230.88 | 226.54 |

| REGRESSION SUMMARY FOR: | Wet Exhaust Mass | Exponent = | 1.5 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fractional Load … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 0.10 | 0.40 | 0.80 | 1.00 |
| All Data | FL ge 0 | All | All | 82250 | 6.775 | Yes | -104317 | -4.594 | No | FL | 0.06 | 21.11 | Yes | 356 | 82250.0 | 82250.0 | 82250.0 | 82250.0 | 82250.0 |
| All Data | FL ge 0 | All | All | 16926 | 2.231 | No | 727 | 7.155 | Yes | 1/(FL^e) | 0.13 | 51.20 | Yes | 356 | 65019.9 | 22988.0 | 2873.5 | 1015.9 | 726.9 |
| All Data | FL ge 20 | All | All | 14254 | 29.641 | Yes | 6711 | -9.014 | No | FL | 0.25 | 81.25 | Yes | 241 | 14254.0 | 14254.0 | 14254.0 | 14254.0 | 14254.0 |
| All Data | FL lt 20 | All | All | 216662 | 5.082 | Yes | -1358048 | -3.302 | No | FL | 0.09 | 10.90 | Yes | 115 | 216662.0 | 216662.0 | 216662.0 | 216662.0 | 216662.0 |
| All Data | FL lt 20 | All | All | 47241 | 1.712 | No | 588 | 2.796 | Yes | 1/(FL^e) | 0.06 | 7.82 | Yes | 115 | 52572.6 | 18587.2 | 2323.4 | 821.4 | 587.8 |
| Yes Data | FL ge 0 | All | All | 39204 | 10.141 | Yes | -42395 | -6.257 | No | FL | 0.12 | 39.15 | Yes | 291 | 39204.0 | 39204.0 | 39204.0 | 39204.0 | 39204.0 |
| Yes Data | FL ge 0 | All | All | 9243 | 6.557 | Yes | 491 | 23.271 | Yes | 1/(FL^e) | 0.65 | 541.52 | Yes | 291 | 53151.2 | 24767.0 | 11183.6 | 9929.2 | 9734.0 |
| Yes Data | FL ge 20 | All | All | 13140 | 31.522 | Yes | 5604 | -8.834 | No | FL | 0.27 | 78.04 | Yes | 217 | 13140.0 | 13140.0 | 13140.0 | 13140.0 | 13140.0 |
| Yes Data | FL lt 20 | All | All | 119128 | 7.655 | Yes | -696874 | -5.242 | No | FL | 0.28 | 27.47 | Yes | 74 | 119128.0 | 119128.0 | 119128.0 | 119128.0 | 119128.0 |
| Yes Data | FL lt 20 | All | All | 13376 | 2.149 | No | 475 | 10.097 | Yes | 1/(FL^e) | 0.59 | 101.95 | Yes | 74 | 42476.7 | 15017.8 | 1877.2 | 663.7 | 474.9 |
| Yes Data | FL ge 0 | Not Ind. | All | 36133 | 4.536 | Yes | -44911 | -2.622 | No | FL | 0.22 | 6.87 | No | 26 | 36133.0 | 36133.0 | 36133.0 | 36133.0 | 36133.0 |
| Yes Data | FL ge 0 | 2 Stroke | All | 25531 | 9.545 | Yes | -21433 | -4.421 | No | FL | 0.31 | 19.54 | Yes | 45 | 25531.0 | 25531.0 | 25531.0 | 25531.0 | 25531.0 |
| Yes Data | FL ge 0 | 4 Stroke | All | 41914 | 8.457 | Yes | -45527 | -5.378 | No | FL | 0.12 | 28.93 | Yes | 220 | 41914.0 | 41914.0 | 41914.0 | 41914.0 | 41914.0 |
| Yes Data | FL ge 0 | Not Ind. | All | 8491 | 10.529 | Yes | 217 | 37.678 | Yes | 1/(FL^e) | 0.98 | 1419.65 | Yes | 26 | 27898.3 | 15352.7 | 9349.0 | 8794.5 | 8708.3 |
| Yes Data | FL ge 0 | 2 Stroke | All | 12009 | 10.877 | Yes | 254 | 7.368 | Yes | 1/(FL^e) | 0.56 | 54.29 | Yes | 45 | 34767.4 | 20055.3 | 13014.8 | 12364.6 | 12263.4 |
| Yes Data | FL ge 0 | 4 Stroke | All | 7358 | 5.506 | Yes | 703 | 30.568 | Yes | 1/(FL^e) | 0.81 | 934.41 | Yes | 220 | 70198.2 | 29575.1 | 10134.7 | 8339.4 | 8060.1 |
| Yes Data | FL ge 0 | All | Diesel | 25422 | 5.699 | Yes | -21731 | -2.952 | No | FL | 0.16 | 8.72 | Yes | 49 | 25422.0 | 25422.0 | 25422.0 | 25422.0 | 25422.0 |
| Yes Data | FL ge 0 | All | Gas Oil | 49890 | 5.820 | Yes | -63048 | -3.826 | No | FL | 0.12 | 14.64 | Yes | 114 | 49890.0 | 49890.0 | 49890.0 | 49890.0 | 49890.0 |
| Yes Data | FL ge 0 | All | Hvy FO | 24858 | 9.288 | Yes | -19409 | -4.306 | No | FL | 0.48 | 18.54 | Yes | 22 | 24858.0 | 24858.0 | 24858.0 | 24858.0 | 24858.0 |
| Yes Data | FL ge 0 | All | Int FO | 21917 | 4.337 | Yes | -14874 | -1.605 | No | FL | 0.24 | 2.58 | No | 10 | 21917.0 | 21917.0 | 21917.0 | 21917.0 | 21917.0 |
| Yes Data | FL ge 0 | All | Light FO | 39264 | 8.541 | Yes | -41008 | -5.398 | No | FL | 0.24 | 29.14 | Yes | 96 | 39264.0 | 39264.0 | 39264.0 | 39264.0 | 39264.0 |
| Yes Data | FL ge 0 | All | Diesel | 7985 | 16.194 | Yes | 217 | 46.390 | Yes | 1/(FL^e) | 0.98 | 2152.06 | Yes | 49 | 27428.6 | 14859.1 | 8844.0 | 8288.5 | 8202.0 |
| Yes Data | FL ge 0 | All | Gas Oil | 6175 | 2.865 | Yes | 691 | 24.758 | Yes | 1/(FL^e) | 0.85 | 612.94 | Yes | 114 | 68005.0 | 28035.5 | 8908.0 | 7141.5 | 6866.7 |
| Yes Data | FL ge 0 | All | Hvy FO | 10050 | 9.107 | Yes | 909 | 5.745 | Yes | 1/(FL^e) | 0.62 | 33.01 | Yes | 22 | 91334.5 | 38788.4 | 13642.3 | 11320.1 | 10958.8 |
| Yes Data | FL ge 0 | All | Int FO | 13888 | 4.177 | Yes | 110 | 0.400 | No | 1/(FL^e) | 0.02 | 0.16 | No | 10 | 13888.0 | 13888.0 | 13888.0 | 13888.0 | 13888.0 |
| Yes Data | FL ge 0 | All | Light FO | 7760 | 4.340 | Yes | 814 | 12.752 | Yes | 1/(FL^e) | 0.63 | 162.62 | Yes | 96 | 80592.1 | 33510.2 | 10979.0 | 8898.3 | 8574.5 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 36133 | 4.536 | Yes | -44911 | -2.622 | No | FL | 0.22 | 6.87 | No | 26 | 36133.0 | 36133.0 | 36133.0 | 36133.0 | 36133.0 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 21000 | 3.894 | Yes | -17801 | -1.653 | No | FL | 0.28 | 2.73 | No | 9 | 21000.0 | 21000.0 | 21000.0 | 21000.0 | 21000.0 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 41885 | 2.332 | No | -54126 | -1.268 | No | FL | 0.45 | 1.61 | No | 4 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 24858 | 9.288 | Yes | -19409 | -4.306 | No | FL | 0.48 | 18.54 | Yes | 22 | 24858.0 | 24858.0 | 24858.0 | 24858.0 | 24858.0 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 21917 | 4.337 | Yes | -14874 | -1.605 | No | FL | 0.24 | 2.58 | No | 10 | 21917.0 | 21917.0 | 21917.0 | 21917.0 | 21917.0 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 10612 | 7.901 | Yes | 3980 | -2.519 | No | FL | 0.35 | 6.34 | No | 14 | 10612.0 | 10612.0 | 10612.0 | 10612.0 | 10612.0 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 50276 | 5.643 | Yes | -63516 | -3.731 | No | FL | 0.11 | 13.92 | Yes | 110 | 50276.0 | 50276.0 | 50276.0 | 50276.0 | 50276.0 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 39264 | 8.541 | Yes | -41008 | -5.398 | No | FL | 0.24 | 29.14 | Yes | 96 | 39264.0 | 39264.0 | 39264.0 | 39264.0 | 39264.0 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | 8491 | 10.529 | Yes | 217 | 37.678 | Yes | 1/(FL^e) | 0.98 | 1419.65 | Yes | 26 | 27898.3 | 15352.7 | 9349.0 | 8794.5 | 8708.3 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 8448 | 69.083 | Yes | 197 | 96.674 | Yes | 1/(FL^e) | 1.00 | 9345.81 | Yes | 9 | 26106.0 | 14691.2 | 9228.6 | 8724.1 | 8645.6 |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 8479 | 13.329 | Yes | 500 | 41.585 | Yes | 1/(FL^e) | 1.00 | 1729.27 | Yes | 4 | 53202.0 | 24290.9 | 10455.4 | 9177.7 | 8978.9 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | 10050 | 9.107 | Yes | 909 | 5.745 | Yes | 1/(FL^e) | 0.62 | 33.01 | Yes | 22 | 91334.5 | 38788.4 | 13642.3 | 11320.1 | 10958.8 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | 13888 | 4.177 | Yes | 110 | 0.400 | No | 1/(FL^e) | 0.02 | 0.16 | No | 10 | 13888.0 | 13888.0 | 13888.0 | 13888.0 | 13888.0 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | 4511 | 4.293 | Yes | 993 | 4.049 | Yes | 1/(FL^e) | 0.58 | 16.40 | Yes | 14 | 93343.6 | 35918.3 | 8437.2 | 5899.3 | 5504.5 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | 6250 | 2.812 | Yes | 694 | 24.324 | Yes | 1/(FL^e) | 0.85 | 591.66 | Yes | 110 | 68301.0 | 28188.1 | 8991.9 | 7219.1 | 6943.4 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | 7760 | 4.340 | Yes | 814 | 12.752 | Yes | 1/(FL^e) | 0.63 | 162.62 | Yes | 96 | 80592.1 | 33510.2 | 10979.0 | 8898.3 | 8574.5 |

| REGRESSION SUMMARY FOR: | SO2 |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A/F | Loads | Cycles | Fuels |  |  |  |  |  |  |  |  |  |  |  | Prediction at Fuel Sulfur Flow (g/kW-hr) … |
| Criteria | Covered | Covered | Covered | Intercept | Int-T | Sig? | Coeff | Coeff-T | Sig? | Param | r2 | F | Sig? | Obs | 0.05 | 1.00 | 5.00 | 25.00 | 75.00 |
| All Data | FL ge 0 | All | All | -0.7670 | -1.669 | No | 2.4938 | 33.454 | Yes | Fuel S | 0.79 | 1119.20 | Yes | 298 | 0.125 | 2.494 | 12.469 | 62.345 | 187.035 |
| All Data | FL ge 20 | All | All | 0.0724 | 0.239 | No | 2.0971 | 33.125 | Yes | Fuel S | 0.84 | 1097.25 | Yes | 207 | 0.105 | 2.097 | 10.486 | 52.429 | 157.286 |
| All Data | FL lt 20 | All | All | 0.0202 | 0.016 | No | 2.6144 | 17.230 | Yes | Fuel S | 0.77 | 296.87 | Yes | 91 | 0.131 | 2.614 | 13.072 | 65.360 | 196.081 |
| Yes Data | FL ge 0 | All | All | -0.4792 | -1.124 | No | 2.3735 | 28.924 | Yes | Fuel S | 0.78 | 836.57 | Yes | 239 | 0.119 | 2.374 | 11.868 | 59.338 | 178.013 |
| Yes Data | FL ge 20 | All | All | 0.2349 | 0.730 | No | 2.0600 | 29.266 | Yes | Fuel S | 0.83 | 856.49 | Yes | 183 | 0.103 | 2.060 | 10.300 | 51.499 | 154.497 |
| Yes Data | FL lt 20 | All | All | -0.2861 | -0.215 | No | 2.6365 | 13.595 | Yes | Fuel S | 0.77 | 184.83 | Yes | 56 | 0.132 | 2.636 | 13.182 | 65.912 | 197.737 |
| Yes Data | FL ge 0 | 2 Stroke | All | -2.0526 | -3.454 | No | 2.4836 | 28.628 | Yes | Fuel S | 0.96 | 819.59 | Yes | 36 | 0.124 | 2.484 | 12.418 | 62.089 | 186.266 |
| Yes Data | FL ge 0 | 4 Stroke | All | -0.4113 | -0.877 | No | 2.4005 | 24.802 | Yes | Fuel S | 0.75 | 615.13 | Yes | 203 | 0.120 | 2.401 | 12.003 | 60.013 | 180.038 |
| Yes Data | FL ge 0 | All | Diesel | -1.0787 | -3.670 | No | 0.6258 | 9.525 | Yes | Fuel S | 0.66 | 90.72 | Yes | 49 | 0.031 | 0.626 | 3.129 | 15.646 | 46.938 |
| Yes Data | FL ge 0 | All | Gas Oil | 0.2231 | 0.228 | No | 2.6522 | 3.218 | Yes | Fuel S | 0.09 | 10.35 | Yes | 111 | 0.133 | 2.652 | 13.261 | 66.306 | 198.917 |
| Yes Data | FL ge 0 | All | Hvy FO | -2.0296 | -2.124 | No | 2.4103 | 16.769 | Yes | Fuel S | 0.93 | 281.20 | Yes | 22 | 0.121 | 2.410 | 12.052 | 60.258 | 180.774 |
| Yes Data | FL ge 0 | All | Int FO | -0.6356 | -0.518 | No | 2.4319 | 16.579 | Yes | Fuel S | 0.97 | 274.85 | Yes | 10 | 0.122 | 2.432 | 12.160 | 60.798 | 182.394 |
| Yes Data | FL ge 0 | All | Light FO | -3.4758 | -7.517 | No | 2.7430 | 41.171 | Yes | Fuel S | 0.95 | 1695.06 | Yes | 96 | 0.137 | 2.743 | 13.715 | 68.574 | 205.722 |
| Yes Data | FL ge 0 | Not Ind. | Diesel | -0.5717 | -2.039 | No | 0.5481 | 9.863 | Yes | Fuel S | 0.80 | 97.28 | Yes | 26 | 0.027 | 0.548 | 2.740 | 13.702 | 41.106 |
| Yes Data | FL ge 0 | 2 Stroke | Diesel | 14.7217 | 1.918 | No | -4.2272 | -1.899 | No | Fuel S | 0.34 | 3.61 | No | 9 |  |  |  |  |  |
| Yes Data | FL ge 0 | 2 Stroke | Gas Oil | 0.2575 | 4.072 | No | 0.9920 | 31.242 | Yes | Fuel S | 1.00 | 976.09 | Yes | 4 | 0.050 | 0.992 | 4.960 | 24.801 | 74.402 |
| Yes Data | FL ge 0 | 2 Stroke | Hvy FO | -2.0296 | -2.124 | No | 2.4103 | 16.769 | Yes | Fuel S | 0.93 | 281.20 | Yes | 22 | 0.121 | 2.410 | 12.052 | 60.258 | 180.774 |
| Yes Data | FL ge 0 | 2 Stroke | Int FO | -0.6356 | -0.518 | No | 2.4319 | 16.579 | Yes | Fuel S | 0.97 | 274.85 | Yes | 10 | 0.122 | 2.432 | 12.160 | 60.798 | 182.394 |
| Yes Data | FL ge 0 | 4 Stroke | Diesel | -1.1326 | -1.275 | No | 0.7276 | 3.179 | Yes | Fuel S | 0.46 | 10.11 | Yes | 14 | 0.036 | 0.728 | 3.638 | 18.189 | 54.568 |
| Yes Data | FL ge 0 | 4 Stroke | Gas Oil | -0.0069 | -0.007 | No | 3.0026 | 3.340 | Yes | Fuel S | 0.10 | 11.16 | Yes | 107 | 0.150 | 3.003 | 15.013 | 75.065 | 225.196 |
| Yes Data | FL ge 0 | 4 Stroke | Light FO | -3.4758 | -7.517 | No | 2.7430 | 41.171 | Yes | Fuel S | 0.95 | 1695.06 | Yes | 96 | 0.137 | 2.743 | 13.715 | 68.574 | 205.722 |

#### FIGURE A-1

#### FIGURE A-2

#### FIGURE A-3

#### FIGURE A-4

#### FIGURE A-5

#### FIGURE A-6

#### FIGURE A-7

#### FIGURE A-8

#### FIGURE A-9

#### FIGURE A-10

#### FIGURE A-11

#### FIGURE A-12

#### FIGURE A-13

#### FIGURE A-14

#### FIGURE A-15

#### FIGURE A-16

#### FIGURE A-17

#### FIGURE A-18

#### FIGURE A-19

#### FIGURE A-20

#### FIGURE A-21

APPENDIX B

SUMMARY OF REPORTS REVIEWED

APPENDIX B IS NOT AVAILABLE

IN THE

ELECTRONIC VERSION OF THE REPORT

APPENDIX C

ACUREX CLASSIFICATION OF SHIPTYPES

APPENDIX C IS NOT AVAILABLE

IN THE

ELECTRONIC VERSION OF THE REPORT

# Footnotes

( 	Certainly USCG test fuel specifications varied across test engines.  However, fuel specifications can only be inferred from the aggregate USCG data and, therefore, derived specifications represent average, rather than specific fuel characteristics.

( 	Of course, carbon containing emission species are equally dependent on fuel carbon content.  However, while total fuel consumption is an acceptable surrogate for fuel carbon consumption due to the fact that carbon comprises the bulk of the total fuel, the considerable variability of sulfur content across fuels makes SO2 emissions dependent not on just fuel consumption per se (and thus co-dependent on load), but on fuel sulfur consumption in particular.

( 	The USCG database does not identify the two versus four stroke configuration of several of its component test engines and does not distinguish the various test fuels employed during testing, except to indicate that all fuels were “diesel.”  Therefore, all engine type statistics for “not indicated” engines and “diesel” fuel are based on USCG data only.  Conversely, all statistics for specific types of diesel fuel are based on Lloyd’s data only.

# Text boxes

3-9

3-14

3-17

3-18

3-19

3-20

3-22

3-23

3-25

3-26

3-27

3-28

3-29

3-30

3-31

3-32

3-33

3-35

3-36

3-37

3-38

3-39

3-40

3-41

3-42

3-43

3-44

3-51

3-50

3-49

3-52

3-53

A-5

A-6

A-7

A-8

A-9

A-10

A-11

A-12

A-13

A-14

A-15

A-16

A-18

A-19

A-20

A-21

A-22

A-23

A-24

A-25

A-26

A-27

A-28

A-29

A-30

A-31

A-32

A-33

A-34

A-35

A-36

A-37

A-17