03E03/29/06

S105-03E.doc

Use on all projects.

Section 105. - CONTROL OF MATERIAL

105.01  Source of Supply and Quality Requirements.  Add the following:

Submit samples of materials for quality verification testing for materials required to conform to Sections 703, 704, and 705.

Materials containing petroleum-based solvents such as cutback asphalts and traffic paints may be restricted from use by local laws or ordinances in certain geographic areas.  Upon presenting proof of such restrictions, alternate materials considered acceptable to the CO may be substituted for the materials specified in the contract.

Use as appropriate. NOTE TO DESIGNER: Listing potential sources (105.02(b)) for the Contractor's information is not recommended as the government may be found to have liability as to the suitability, or availability of the source even though the disclaimer is included.

105.02  Material Sources

List source(s) when there is a government-provided source and it is mandatory.

(a) Government-provided sources.  Add the following:

Obtain material for use in the production of aggregates under Sections          (list items)

_____________________________________ from               (name source)_________.

Include when there is a government-provided source and it is optional.

Material for use in the production of aggregates under Sections         (list items)         may be obtained from                                         (name source)                                         .

Include if there is a royalty on material taken from the source.

Pay     (name person or company)      a royalty fee of     (name dollar amount)     per cubic yard, or if the material is weighed,    (name dollar amount)     per ton for material furnished from this source and used on the project.

Make monthly royalty payments directly to:

(owner of the source and address)  .

_____________________________

_____________________________

_____________________________

Include when the Contractor is responsible for locating material sources.

(b) Contractor-located sources.  Add the following to the end of the first paragraph:

For Contractor-located, non-commercial sources, secure environmental clearances according to Subsection 107.10.

Include the following when there is a specific site available for a staging area.

105.04  Storing and Handling Material.  Add the following after the third sentence of the second paragraph:

For Contractor-located, non-commercial staging, storing, and material handling areas, secure environmental clearances according to Subsection 107.10.

Add the following:

The Contractor     (may/will)      use the        (description)         for       (a staging area/storage of materials/hot plant site/stockpiles/ etc)         .