Appendix

| Table A-1. Energy consumption rates for LDV classes operating on near-term alternative fuel/engine technology combinations. |
| --- |
|  | Vehicle Energy Consumption (Btu/Mile) | Full Fuel Cycle Energy Consumption (Btu/Mile) |
| Fuel | Auto | LDT1 (1) | LDT2 (2) | LDV Fleet (3) | Auto | LDT1 (1) | LDT2 (2) | LDV Fleet (3) |
| Conventional Gasoline | 5,156 | 6,875 | 8,021 | 6,261 | 6,495 | 8,659 | 10,103 | 7,886 |
| Reformulated Gasoline (Federal Phase 2) | 5,156 | 6,875 | 8,021 | 6,261 | 6,549 | 8,732 | 10,187 | 7,952 |
| Baseline (70%CG/30%RFG) | 5,156 | 6,875 | 8,021 | 6,261 | 6,511 | 8,681 | 10,128 | 7,906 |
| Ethanol (E85) | 4,911 | 6,548 | 8,021 | 6,028 | 7,652 | 10,203 | 12,498 | 9,393 |
| Methanol (M85) | 4,911 | 6,548 | 8,021 | 6,028 | 7,461 | 9,948 | 12,187 | 9,159 |
| CNG (Bi-Fuel Vehicle) | 5,729 | 7,639 | 8,912 | 6,957 | 7,051 | 9,401 | 10,967 | 8,561 |
| CNG (Dedicated Vehicle) | 5,544 | 7,392 | 8,625 | 6,732 | 6,823 | 9,097 | 10,614 | 8,285 |
| LNG | 5,544 | 7,392 | 8,625 | 6,732 | 6,631 | 8,842 | 10,403 | 8,067 |
| LPG | 5,156 | 6,875 | 8,021 | 4,638 | 5,896 | 7,862 | 9,172 | 7,160 |
| Petroleum Diesel | 3,819 | 5,093 | 5,941 | 4,638 | 4,567 | 6,090 | 7,105 | 5,546 |
| Bio-Diesel (B20) | 3,819 | 5,093 | 5,941 | 4,638 | 4,728 | 6,305 | 7,358 | 5,742 |
| Electricity | 0 | 0 | 0 | 0 | 5,608 | 7,477 | 8,723 | 6,809 |
| (1) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |
| (3) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model, Argonne National Laboratories, January 2000. |

| Table A-2. Greenhouse gas emissions rates for LDV classes with near-term alternative fuel/engine technology combinations. |
| --- |
| Fuel | Automobiles | Light-Duty Trucks 1 (1) | Light-Duty Trucks 2 (2) | Light-Duty Fleet (3) |
|  | CO2 (4) | CH4 (5) | N2O (6) | GHGs (7) | CO2 | CH4 | N2O | GHGs | CO2 | CH4 | N2O | GHGs | CO2 | CH4 | N2O | GHGs |
|  | Greenhouse Gas Emissions from Vehicle Operation Only (grams/vehicle-mile) |
| Gasoline | 390 | 0.084 | 0.028 | 401 | 521 | 0.09 | 0.033 | 533 | 607 | 0.09 | 0.04 | 622 | 474 | 0.087 | 0.032 | 486 |
| Reform. Gasoline (Federal Phase 2) | 361 | 0.077 | 0.028 | 372 | 482 | 0.083 | 0.033 | 494 | 562 | 0.083 | 0.040 | 576 | 439 | 0.080 | 0.032 | 450 |
| Baseline (70% Gasoline/30%RFG) | 382 | 0.082 | 0.028 | 392 | 509 | 0.088 | 0.033 | 521 | 594 | 0.088 | 0.040 | 608 | 463 | 0.085 | 0.032 | 475 |
| Ethanol (E85) | 83 | 0.126 | 0.028 | 94 | 111 | 0.135 | 0.033 | 124 | 139 | 0.135 | 0.040 | 154 | 103 | 0.131 | 0.032 | 115 |
| Methanol (M85) | 356 | 0.042 | 0.028 | 366 | 475 | 0.045 | 0.033 | 486 | 582 | 0.045 | 0.040 | 596 | 437 | 0.044 | 0.032 | 448 |
| CNG (Bi-Fuel) | 341 | 0.840 | 0.017 | 364 | 455 | 0.900 | 0.020 | 480 | 532 | 0.900 | 0.024 | 558 | 415 | 0.872 | 0.019 | 439 |
| CNG (Dedicated) | 330 | 0.840 | 0.022 | 355 | 441 | 0.900 | 0.026 | 468 | 514 | 0.900 | 0.032 | 543 | 401 | 0.872 | 0.025 | 427 |
| LNG | 326 | 0.840 | 0.022 | 350 | 435 | 0.900 | 0.026 | 462 | 508 | 0.900 | 0.032 | 536 | 396 | 0.872 | 0.025 | 422 |
| LPG | 369 | 0.109 | 0.028 | 380 | 492 | 0.117 | 0.033 | 505 | 574 | 0.117 | 0.040 | 589 | 448 | 0.113 | 0.032 | 460 |
| Petroleum Diesel | 307 | 0.011 | 0.016 | 312 | 410 | 0.014 | 0.024 | 417 | 478 | 0.017 | 0.032 | 488 | 373 | 0.013 | 0.022 | 380 |
| Bio-Diesel (B20) | 246 | 0.011 | 0.016 | 211 | 328 | 0.014 | 0.024 | 283 | 382 | 0.017 | 0.032 | 331 | 299 | 0.013 | 0.022 | 257 |
| Electricity | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 |
|  | Greenhouse Gas Emissions from Full Fuel Cycle (grams/vehicle-mile) |
| Gasoline | 475 | 0.665 | 0.0291 | 498 | 634 | 0.864 | 0.034 | 663 | 739 | 0.993 | 0.042 | 773 | 577 | 0.792 | 0.033 | 604 |
| Reform. Gasoline (Federal Phase 2) | 474 | 0.791 | 0.047 | 505 | 631 | 1.034 | 0.059 | 671 | 737 | 1.193 | 0.070 | 783 | 575 | 0.946 | 0.055 | 612 |
| Baseline (70% Gasoline/30%RFG) | 475 | 0.702 | 0.035 | 500 | 633 | 0.915 | 0.042 | 665 | 739 | 1.053 | 0.050 | 776 | 576 | 0.838 | 0.040 | 606 |
| Ethanol (E85) | 308 | 0.580 | 0.176 | 374 | 411 | 0.741 | 0.230 | 497 | 506 | 0.877 | 0.281 | 611 | 378 | 0.688 | 0.213 | 459 |
| Methanol (M85) | 464 | 0.675 | 0.029 | 487 | 619 | 0.890 | 0.035 | 648 | 758 | 1.080 | 0.042 | 794 | 570 | 0.821 | 0.034 | 597 |
| CNG (Bi-Fuel) | 428 | 2.085 | 0.018 | 478 | 572 | 2.560 | 0.022 | 632 | 667 | 2.837 | 0.026 | 735 | 521 | 2.384 | 0.021 | 577 |
| CNG (Dedicated) | 414 | 2.045 | 0.024 | 465 | 553 | 2.507 | 0.028 | 615 | 646 | 2.774 | 0.034 | 715 | 504 | 2.335 | 0.027 | 561 |
| LNG | 417 | 2.051 | 0.024 | 468 | 557 | 2.514 | 0.029 | 618 | 650 | 2.783 | 0.035 | 719 | 507 | 2.342 | 0.028 | 565 |
| LPG | 423 | 0.661 | 0.029 | 446 | 565 | 0.853 | 0.034 | 593 | 659 | 0.976 | 0.041 | 692 | 514 | 0.784 | 0.033 | 541 |
| Petroleum Diesel | 364 | 0.407 | 0.017 | 377 | 485 | 0.542 | 0.025 | 504 | 566 | 0.633 | 0.033 | 589 | 441 | 0.494 | 0.023 | 459 |
| Bio-Diesel (B20) | 309 | 0.328 | 0.019 | 282 | 412 | 0.436 | 0.028 | 377 | 481 | 0.510 | 0.036 | 441 | 375 | 0.398 | 0.025 | 343 |
| Electricity | 354 | 0.509 | 0.003 | 365 | 472 | 0.679 | 0.003 | 487 | 551 | 0.792 | 0.004 | 568 | 430 | 0.618 | 0.003 | 444 |
| (1) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |  |  |  |  |  |  |  |  |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |  |  |  |  |  |  |  |  |
| (3) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| (4) Carbon dioxide; used as numeraire to express "Global Warming Potential" (GWP) of other GHGs. |  |  |  |  |  |  |  |  |  |
| (5) Methane; GWP relative to carbon dioxide = 21 (100-year value). |  |  |  |  |  |  |  |  |  |  |  |
| (6) Nitrous oxide; GWP relative to carbon dioxide = 310 (100-year value). |  |  |  |  |  |  |  |  |  |  |
| (7) CO2 equivalent, with methane and nitrous oxide weighted by GWPs. |  |  |  |  |  |  |  |  |  |  |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model (with Volpe input assumptions), Argonne National Laboratories, January 2000. |

| Table A-3. Criteria pollutant emission rates for LDV classes operating on near-term alternative fuel/engine technology combinations. |  |
| --- | --- |
| Fuel | Automobiles | Light-Duty Trucks 1 (1) | Light-Duty Trucks 2 (2) | Light-Duty Vehicle Fleet (3) |
|  | VOC (4) | CO (5) | NOx (6) | SOx (7) | PM-10 (8) | VOC | CO | NOx | SOx | PM10 | VOC | CO | NOx | SOx | PM10 | VOC | CO | NOx | SOx | PM10 |
|  | Criteria Pollutant Emissions from Vehicle Operation Only (grams/vehicle-mile) |
| Gasoline | 0.207 | 5.517 | 0.275 | 0.050 | 0.033 | 0.198 | 8.247 | 0.381 | 0.066 | 0.036 | 0.785 | 16.846 | 1.173 | 0.078 | 0.036 | 0.302 | 8.425 | 0.466 | 0.061 | 0.035 |
| Reform. Gasoline (Federal Phase 2) | 0.161 | 4.414 | 0.261 | 0.008 | 0.032 | 0.157 | 6.598 | 0.362 | 0.010 | 0.035 | 0.675 | 13.477 | 1.114 | 0.012 | 0.035 | 0.247 | 6.740 | 0.443 | 0.009 | 0.034 |
| Baseline (70% Gasoline/30%RFG) | 0.193 | 5.186 | 0.271 | 0.037 | 0.033 | 0.186 | 7.752 | 0.375 | 0.050 | 0.036 | 0.752 | 15.835 | 1.155 | 0.058 | 0.036 | 0.286 | 7.919 | 0.459 | 0.045 | 0.034 |
| Ethanol (E85) | 0.176 | 3.310 | 0.248 | 0.010 | 0.026 | 0.168 | 4.948 | 0.343 | 0.013 | 0.027 | 0.589 | 7.581 | 0.997 | 0.016 | 0.027 | 0.243 | 4.625 | 0.409 | 0.012 | 0.026 |
| Methanol (M85) | 0.176 | 4.138 | 0.248 | 0.013 | 0.026 | 0.168 | 6.185 | 0.343 | 0.017 | 0.027 | 0.589 | 12.635 | 0.997 | 0.020 | 0.027 | 0.243 | 6.319 | 0.409 | 0.015 | 0.026 |
| CNG (Bi-Fuel) | 0.112 | 4.414 | 0.275 | 0.002 | 0.022 | 0.108 | 6.598 | 0.381 | 0.002 | 0.023 | 0.393 | 11.792 | 1.173 | 0.003 | 0.023 | 0.158 | 6.453 | 0.466 | 0.002 | 0.022 |
| CNG (Dedicated) | 0.045 | 4.414 | 0.248 | 0.002 | 0.022 | 0.047 | 6.598 | 0.343 | 0.002 | 0.022 | 0.204 | 10.108 | 1.173 | 0.003 | 0.022 | 0.073 | 6.167 | 0.439 | 0.002 | 0.022 |
| LNG | 0.045 | 4.414 | 0.248 | 0.002 | 0.022 | 0.047 | 6.598 | 0.343 | 0.002 | 0.022 | 0.204 | 10.108 | 1.173 | 0.003 | 0.022 | 0.073 | 6.167 | 0.439 | 0.002 | 0.022 |
| LPG | 0.077 | 4.138 | 0.248 | 0.000 | 0.022 | 0.084 | 6.185 | 0.343 | 0.000 | 0.023 | 0.456 | 12.635 | 0.997 | 0.000 | 0.023 | 0.144 | 6.319 | 0.409 | 0.000 | 0.022 |
| Petroleum Diesel | 0.080 | 1.070 | 0.600 | 0.048 | 0.121 | 0.091 | 1.139 | 0.600 | 0.064 | 0.121 | 0.540 | 1.208 | 1.224 | 0.075 | 0.130 | 0.162 | 1.118 | 0.706 | 0.058 | 0.123 |
| Bio-Diesel (B20) | 0.049 | 2.759 | 0.063 | 0.006 | 0.030 | 0.080 | 5.518 | 0.135 | 0.009 | 0.039 | 0.112 | 5.518 | 0.180 | 0.010 | 0.039 | 0.071 | 4.220 | 0.109 | 0.008 | 0.035 |
| Electricity | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 |
|  | Criteria Pollutant Emissions from Full Fuel Cycle (grams/vehicle-mile) |
| Gasoline | 0.296 | 5.646 | 0.461 | 0.164 | 0.051 | 0.316 | 8.420 | 0.630 | 0.219 | 0.060 | 0.923 | 17.047 | 1.463 | 0.256 | 0.064 | 0.410 | 8.582 | 0.692 | 0.200 | 0.056 |
| Reform. Gasoline (Federal Phase 2) | 0.278 | 4.580 | 0.531 | 0.164 | 0.091 | 0.313 | 6.819 | 0.722 | 0.218 | 0.114 | 0.857 | 13.735 | 1.534 | 0.255 | 0.127 | 0.389 | 6.942 | 0.770 | 0.199 | 0.105 |
| Baseline (70% Gasoline/30%RFG) | 0.290 | 5.326 | 0.482 | 0.164 | 0.063 | 0.315 | 7.939 | 0.657 | 0.219 | 0.076 | 0.903 | 16.054 | 1.484 | 0.255 | 0.083 | 0.404 | 8.090 | 0.716 | 0.199 | 0.071 |
| Ethanol (E85) | 0.460 | 3.532 | 0.938 | 0.441 | 0.367 | 0.547 | 5.244 | 1.263 | 0.589 | 0.482 | 1.053 | 7.943 | 2.125 | 0.721 | 0.584 | 0.592 | 4.898 | 1.257 | 0.542 | 0.445 |
| Methanol (M85) | 0.238 | 4.364 | 0.462 | 0.068 | 0.037 | 0.252 | 6.486 | 0.629 | 0.090 | 0.042 | 0.691 | 13.004 | 1.348 | 0.110 | 0.045 | 0.320 | 6.596 | 0.673 | 0.083 | 0.040 |
| CNG (Bi-Fuel) | 0.142 | 4.576 | 0.623 | 0.118 | 0.034 | 0.148 | 6.814 | 0.845 | 0.157 | 0.038 | 0.440 | 12.045 | 1.714 | 0.183 | 0.041 | 0.195 | 6.651 | 0.888 | 0.143 | 0.037 |
| CNG (Dedicated) | 0.074 | 4.571 | 0.584 | 0.114 | 0.033 | 0.086 | 6.807 | 0.792 | 0.152 | 0.037 | 0.250 | 10.352 | 1.697 | 0.177 | 0.040 | 0.108 | 6.358 | 0.848 | 0.138 | 0.036 |
| LNG | 0.092 | 4.729 | 0.792 | 0.039 | 0.035 | 0.113 | 7.114 | 1.083 | 0.052 | 0.040 | 0.328 | 10.578 | 2.212 | 0.061 | 0.043 | 0.140 | 6.581 | 1.138 | 0.047 | 0.038 |
| LPG | 0.112 | 4.245 | 0.376 | 0.050 | 0.031 | 0.130 | 6.329 | 0.514 | 0.067 | 0.035 | 0.510 | 12.802 | 1.197 | 0.078 | 0.037 | 0.186 | 6.449 | 0.565 | 0.061 | 0.034 |
| Petroleum Diesel | 0.114 | 1.161 | 0.719 | 0.113 | 0.132 | 0.136 | 1.261 | 0.758 | 0.150 | 0.136 | 0.593 | 1.350 | 1.409 | 0.175 | 0.147 | 0.203 | 1.229 | 0.850 | 0.137 | 0.136 |
| Bio-Diesel (B20) | 0.127 | 2.901 | 0.250 | 0.058 | 0.044 | 0.184 | 5.707 | 0.384 | 0.077 | 0.058 | 0.234 | 5.739 | 0.471 | 0.090 | 0.061 | 0.166 | 4.392 | 0.336 | 0.070 | 0.052 |
| Electricity | 0.033 | 0.106 | 0.758 | 0.928 | 0.076 | 0.045 | 0.141 | 1.011 | 1.238 | 0.094 | 0.052 | 0.164 | 1.180 | 1.444 | 0.106 | 0.041 | 0.128 | 0.921 | 1.127 | 0.088 |
| (1) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |  |  |  |  |  |  |  |  |  |  |  |  |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |  |  |  |  |  |  |  |  |  |  |  |  |
| (3) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| (4) Volatile organic compounds. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (5) Carbon monoxide. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (6) Nitrogen oxides. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (7) Sulfur oxides. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (8) Particulate matter 10 microns or less in diameter. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model (with Volpe input assumptions), Argonne National Laboratories, January 2000. |

| Table A-4. Energy consumption rates for LDV classes operating on long-term alternative fuel/engine technology combinations. |
| --- |
|  | Engine Technology (1) | Vehicle Energy Consumption (Btu/Mile) | Full Fuel Cycle Energy Consumption (Btu/Mile) |
| Fuel |  | Auto | LDT1 (2) | LDT2 (3) | LDV Fleet (4) | Auto | LDT1 (2) | LDT2 (3) | LDV Fleet (4) |
| Reformulated Gasoline | Spark-Ignition ICE | 4,678 | 6,237 | 7,290 | 5,734 | 5,914 | 7,885 | 9,217 | 7,250 |
|  | Spark-Ignition Hybrid Electric | 2,462 | 3,283 | 3,837 | 3,018 | 3,113 | 4,150 | 4,851 | 3,816 |
| Ethanol (E90) | Spark-Ignition ICE | 4,252 | 5,670 | 6,943 | 5,270 | 10,444 | 13,925 | 17,051 | 12,942 |
|  | Spark-Ignition Hybrid Electric | 2,462 | 3,283 | 3,837 | 3,018 | 6,047 | 8,062 | 9,423 | 7,412 |
| Methanol (M90) | Spark-Ignition ICE | 4,252 | 5,670 | 6,943 | 5,270 | 6,602 | 8,803 | 10,779 | 8,181 |
|  | Spark-Ignition Hybrid Electric | 2,462 | 3,283 | 3,837 | 3,018 | 3,822 | 5,096 | 5,957 | 4,686 |
| CNG | Spark-Ignition ICE | 4,455 | 5,940 | 7,290 | 5,523 | 5,382 | 7,176 | 8,807 | 6,673 |
|  | Spark-Ignition Hybrid Electric | 2,752 | 3,669 | 4,288 | 3,373 | 3,324 | 4,432 | 5,181 | 4,075 |
| LNG | Spark-Ignition ICE | 4,455 | 5,940 | 7,290 | 5,523 | 5,542 | 7,389 | 9,069 | 6,871 |
|  | Spark-Ignition Hybrid Electric | 2,752 | 3,669 | 4,288 | 3,373 | 3,423 | 4,564 | 5,335 | 4,196 |
| LPG | Spark-Ignition ICE | 4,252 | 5,670 | 6,943 | 5,270 | 4,855 | 6,473 | 7,926 | 6,016 |
|  | Spark-Ignition Hybrid Electric | 2,752 | 3,669 | 4,288 | 3,373 | 3,141 | 4,189 | 4,896 | 3,851 |
| Petroleum Diesel | Compression-Ignition ICE | 3,118 | 4,158 | 4,860 | 3,823 | 3,813 | 5,084 | 5,942 | 4,674 |
|  | Compression-Ignition Hybrid Electric | 2,034 | 2,712 | 3,170 | 2,493 | 2,487 | 3,316 | 3,875 | 3,048 |
| Bio-Diesel (B20) | Compression-Ignition ICE | 3,118 | 4,158 | 4,860 | 3,823 | 4,027 | 5,370 | 6,276 | 4,937 |
|  | Compression-Ignition Hybrid Electric | 2,034 | 2,712 | 3,170 | 2,493 | 2,627 | 3,502 | 4,093 | 3,220 |
| Electricity | Battery-Powered Electric Drive | 0 | 0 | 0 | 0 | 3,587 | 4,783 | 6,389 | 4,541 |
| Hydrogen (NG) | Proton-Exchange Membrane Fuel Cell | 1,559 | 2,079 | 2,430 | 1,911 | 3,039 | 4,052 | 4,736 | 3,726 |
| Hydrogen (Solar) | Proton-Exchange Membrane Fuel Cell | 1,559 | 2,079 | 2,430 | 1,911 | 2,198 | 2,931 | 3,426 | 2,695 |
| (1) ICE indicates internal combustion engine. |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |  |
| (3) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |  |
| (4) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model, Argonne National Laboratories, January 2000. |

| Table A-5. Greenhouse gas emissions rates for LDV classes operating on long-term alternative fuel/engine technology combinations. |
| --- |
| Fuel | Engine Technology (1) | Automobiles | Light-Duty Trucks 1 (2) | Light-Duty Trucks 2 (3) | Light-Duty Fleet (4) |
|  |  | CO2 (5) | CH4 (6) | N2O (7) | GHGs (8) | CO2 | CH4 | N2O | GHGs | CO2 | CH4 | N2O | GHGs | CO2 | CH4 | N2O | GHGs |
|  |  | Greenhouse Gas Emissions from Vehicle Operation Only (grams/vehicle-mile) |
| RFG | ICE | 328 | 0.065 | 0.028 | 338 | 437 | 0.065 | 0.033 | 449 | 511 | 0.091 | 0.040 | 525 | 402 | 0.070 | 0.032 | 413 |
|  | Hybrid | 172 | 0.065 | 0.028 | 182 | 230 | 0.065 | 0.033 | 242 | 269 | 0.091 | 0.040 | 283 | 211 | 0.070 | 0.032 | 223 |
| Ethanol (E90) | ICE | 49 | 0.098 | 0.028 | 60 | 65 | 0.098 | 0.033 | 77 | 82 | 0.137 | 0.040 | 97 | 61 | 0.104 | 0.032 | 73 |
|  | Hybrid | 30 | 0.098 | 0.028 | 41 | 39 | 0.098 | 0.033 | 51 | 49 | 0.137 | 0.040 | 64 | 37 | 0.104 | 0.032 | 49 |
| Methanol (M90) | ICE | 310 | 0.033 | 0.028 | 319 | 413 | 0.033 | 0.033 | 424 | 506 | 0.046 | 0.040 | 519 | 384 | 0.035 | 0.032 | 395 |
|  | Hybrid | 179 | 0.033 | 0.028 | 189 | 239 | 0.033 | 0.033 | 250 | 280 | 0.046 | 0.040 | 293 | 220 | 0.035 | 0.032 | 231 |
| CNG | ICE | 266 | 0.325 | 0.014 | 277 | 355 | 0.325 | 0.017 | 367 | 436 | 0.455 | 0.020 | 451 | 330 | 0.348 | 0.016 | 342 |
|  | Hybrid | 164 | 0.325 | 0.014 | 175 | 219 | 0.325 | 0.017 | 231 | 256 | 0.455 | 0.020 | 272 | 201 | 0.348 | 0.016 | 214 |
| LNG | ICE | 263 | 0.325 | 0.014 | 274 | 350 | 0.325 | 0.017 | 362 | 430 | 0.455 | 0.020 | 446 | 326 | 0.348 | 0.016 | 338 |
|  | Hybrid | 162 | 0.325 | 0.014 | 173 | 216 | 0.325 | 0.017 | 228 | 252 | 0.455 | 0.020 | 268 | 199 | 0.348 | 0.016 | 211 |
| LPG | ICE | 304 | 0.072 | 0.028 | 314 | 406 | 0.072 | 0.033 | 417 | 497 | 0.100 | 0.040 | 511 | 377 | 0.077 | 0.032 | 389 |
|  | Hybrid | 197 | 0.072 | 0.028 | 207 | 262 | 0.072 | 0.033 | 274 | 307 | 0.100 | 0.040 | 321 | 241 | 0.077 | 0.032 | 253 |
| Reformulated Diesel | ICE | 252 | 0.011 | 0.016 | 257 | 336 | 0.014 | 0.024 | 343 | 392 | 0.017 | 0.032 | 403 | 309 | 0.013 | 0.022 | 316 |
|  | Hybrid | 164 | 0.011 | 0.016 | 169 | 219 | 0.014 | 0.024 | 227 | 256 | 0.017 | 0.032 | 266 | 201 | 0.013 | 0.022 | 208 |
| Bio-Diesel (B20) | ICE | 206 | 0.011 | 0.016 | 211 | 275 | 0.014 | 0.024 | 283 | 321 | 0.017 | 0.032 | 331 | 253 | 0.013 | 0.022 | 260 |
|  | Hybrid | 134 | 0.011 | 0.016 | 140 | 180 | 0.014 | 0.024 | 188 | 210 | 0.017 | 0.032 | 220 | 165 | 0.013 | 0.022 | 172 |
| Electricity | Electric | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 |
| Hydrogen (NG) | Fuel Cell | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 |
| Hydrogen (Solar) | Fuel Cell | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 | 0 | 0.000 | 0.000 | 0 |
|  |  | Greenhouse Gas Emissions from Full Fuel Cycle (grams/vehicle-mile) |
| RFG | ICE | 426 | 0.711 | 0.043 | 454 | 568 | 0.926 | 0.054 | 604 | 664 | 1.097 | 0.064 | 706 | 522 | 0.861 | 0.051 | 556 |
|  | Hybrid | 224 | 0.405 | 0.036 | 244 | 299 | 0.518 | 0.044 | 323 | 349 | 0.621 | 0.053 | 379 | 275 | 0.486 | 0.042 | 298 |
| Ethanol (E90) | ICE | 28 | 0.274 | 0.199 | 96 | 36 | 0.333 | 0.261 | 124 | 48 | 0.424 | 0.319 | 155 | 35 | 0.323 | 0.244 | 117 |
|  | Hybrid | 18 | 0.200 | 0.127 | 62 | 23 | 0.234 | 0.165 | 79 | 30 | 0.296 | 0.194 | 96 | 22 | 0.230 | 0.153 | 74 |
| Methanol (M90) | ICE | 410 | 0.609 | 0.032 | 433 | 547 | 0.801 | 0.038 | 576 | 670 | 0.986 | 0.046 | 705 | 508 | 0.749 | 0.037 | 535 |
|  | Hybrid | 237 | 0.366 | 0.030 | 254 | 317 | 0.477 | 0.036 | 338 | 370 | 0.565 | 0.043 | 395 | 291 | 0.444 | 0.035 | 311 |
| CNG | ICE | 329 | 1.283 | 0.015 | 361 | 439 | 1.602 | 0.018 | 478 | 539 | 2.022 | 0.022 | 588 | 408 | 1.536 | 0.017 | 446 |
|  | Hybrid | 203 | 0.917 | 0.015 | 227 | 271 | 1.114 | 0.017 | 300 | 316 | 1.377 | 0.021 | 352 | 249 | 1.073 | 0.017 | 277 |
| LNG | ICE | 331 | 1.286 | 0.015 | 363 | 442 | 1.607 | 0.018 | 481 | 542 | 2.028 | 0.022 | 592 | 411 | 1.540 | 0.018 | 449 |
|  | Hybrid | 204 | 0.919 | 0.015 | 228 | 273 | 1.117 | 0.018 | 302 | 318 | 1.380 | 0.021 | 354 | 251 | 1.076 | 0.017 | 278 |
| LPG | ICE | 349 | 0.527 | 0.029 | 369 | 466 | 0.679 | 0.034 | 490 | 570 | 0.844 | 0.041 | 601 | 433 | 0.641 | 0.033 | 456 |
|  | Hybrid | 226 | 0.366 | 0.028 | 242 | 301 | 0.465 | 0.034 | 321 | 352 | 0.560 | 0.041 | 376 | 277 | 0.438 | 0.033 | 296 |
| Reformulated Diesel | ICE | 304 | 0.342 | 0.017 | 317 | 406 | 0.455 | 0.025 | 423 | 474 | 0.533 | 0.033 | 496 | 373 | 0.419 | 0.023 | 389 |
|  | Hybrid | 198 | 0.227 | 0.016 | 208 | 264 | 0.302 | 0.025 | 278 | 309 | 0.353 | 0.033 | 327 | 243 | 0.278 | 0.022 | 256 |
| Bio-Diesel (B20) | ICE | 304 | 0.342 | 0.017 | 317 | 406 | 0.455 | 0.025 | 423 | 474 | 0.533 | 0.033 | 496 | 373 | 0.419 | 0.023 | 389 |
|  | Hybrid | 176 | 0.217 | 0.018 | 186 | 235 | 0.289 | 0.026 | 249 | 274 | 0.339 | 0.035 | 292 | 216 | 0.266 | 0.024 | 229 |
| Electricity | Electric | 240 | 0.358 | 0.003 | 248 | 320 | 0.477 | 0.004 | 331 | 427 | 0.638 | 0.006 | 443 | 304 | 0.453 | 0.004 | 315 |
| Hydrogen (NG) | Fuel Cell | 183 | 0.417 | 0.001 | 192 | 244 | 0.556 | 0.002 | 256 | 285 | 0.650 | 0.002 | 299 | 224 | 0.512 | 0.002 | 235 |
| Hydrogen (Solar) | Fuel Cell | 41 | 0.089 | 0.001 | 44 | 55 | 0.119 | 0.001 | 58 | 65 | 0.139 | 0.001 | 68 | 51 | 0.109 | 0.001 | 53 |
| (1) ICE indicates internal combustion engine. |  |  |  |  |  |  |  |  |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |  |  |  |  |  |  |  |  |  |
| (3) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |  |  |  |  |  |  |  |  |  |
| (4) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| (5) Carbon dioxide; used as numeraire to express "Global Warming Potential" (GWP) of other GHGs. |  |  |  |  |  |  |  |  |  |  |
| (6) Methane; GWP relative to carbon dioxide = 21 (100-year value). |  |  |  |  |  |  |  |  |  |  |  |  |
| (7) Nitrous oxide; GWP relative to carbon dioxide = 310 (100-year value). |  |  |  |  |  |  |  |  |  |  |  |  |
| (8) CO2 equivalent, with methane and nitrous oxide weighted by GWPs. |  |  |  |  |  |  |  |  |  |  |  |  |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model (with Volpe input assumptions), Argonne National Laboratories, January 2000. |  |

| Table A-6. Criteria pollutant emission rates for LDV classes operating on long-term alternative fuel/engine technology combinations. |
| --- |
| Fuel | Engine Technology (1) | Automobiles | Light-Duty Trucks 1 (2) | Light-Duty Trucks 2 (3) | Light-Duty Vehicle Fleet (4) |
|  |  | VOC (5) | CO (6) | NOx (7) | SOx (8) | PM-10 (9) | VOC | CO | NOx | SOx | PM10 | VOC | CO | NOx | SOx | PM10 | VOC | CO | NOx | SOx | PM10 |
|  |  | Criteria Pollutant Emissions from Vehicle Operation Only (grams/vehicle-mile) |
| Reform. Gasoline (Federal Phase 2) | ICE | 0.125 | 2.759 | 0.036 | 0.007 | 0.031 | 0.125 | 2.759 | 0.036 | 0.009 | 0.031 | 0.158 | 5.518 | 0.135 | 0.011 | 0.041 | 0.131 | 3.253 | 0.054 | 0.009 | 0.033 |
|  | Hybrid | 0.106 | 2.759 | 0.036 | 0.004 | 0.033 | 0.106 | 2.759 | 0.036 | 0.005 | 0.033 | 0.135 | 5.518 | 0.135 | 0.006 | 0.045 | 0.111 | 3.253 | 0.054 | 0.005 | 0.035 |
| Ethanol (E90) | ICE | 0.125 | 2.759 | 0.036 | 0.001 | 0.027 | 0.125 | 2.759 | 0.036 | 0.001 | 0.027 | 0.158 | 5.518 | 0.135 | 0.001 | 0.033 | 0.131 | 3.253 | 0.054 | 0.001 | 0.028 |
|  | Hybrid | 0.106 | 2.759 | 0.036 | 0.001 | 0.030 | 0.106 | 2.759 | 0.036 | 0.001 | 0.030 | 0.135 | 5.518 | 0.135 | 0.001 | 0.038 | 0.111 | 3.253 | 0.054 | 0.001 | 0.031 |
| Methanol (M90) | ICE | 0.125 | 2.759 | 0.036 | 0.001 | 0.027 | 0.125 | 2.759 | 0.036 | 0.002 | 0.027 | 0.158 | 5.518 | 0.135 | 0.002 | 0.033 | 0.131 | 3.253 | 0.054 | 0.001 | 0.028 |
|  | Hybrid | 0.106 | 2.759 | 0.036 | 0.001 | 0.030 | 0.106 | 2.759 | 0.036 | 0.001 | 0.030 | 0.135 | 5.518 | 0.135 | 0.001 | 0.038 | 0.111 | 3.253 | 0.054 | 0.001 | 0.031 |
| CNG | ICE | 0.059 | 1.655 | 0.036 | 0.001 | 0.023 | 0.059 | 1.655 | 0.036 | 0.002 | 0.023 | 0.072 | 4.414 | 0.135 | 0.002 | 0.025 | 0.061 | 2.150 | 0.054 | 0.002 | 0.023 |
|  | Hybrid | 0.059 | 1.655 | 0.036 | 0.001 | 0.026 | 0.059 | 1.655 | 0.036 | 0.001 | 0.026 | 0.080 | 4.414 | 0.135 | 0.001 | 0.031 | 0.063 | 2.150 | 0.054 | 0.001 | 0.027 |
| LNG | ICE | 0.059 | 1.655 | 0.036 | 0.000 | 0.023 | 0.059 | 1.655 | 0.036 | 0.000 | 0.023 | 0.072 | 4.414 | 0.135 | 0.000 | 0.025 | 0.061 | 2.150 | 0.054 | 0.000 | 0.023 |
|  | Hybrid | 0.059 | 1.655 | 0.036 | 0.000 | 0.026 | 0.059 | 1.655 | 0.036 | 0.000 | 0.026 | 0.080 | 4.414 | 0.135 | 0.000 | 0.031 | 0.063 | 2.150 | 0.054 | 0.000 | 0.027 |
| LPG | ICE | 0.065 | 1.655 | 0.036 | 0.000 | 0.023 | 0.065 | 1.655 | 0.036 | 0.000 | 0.023 | 0.088 | 4.414 | 0.135 | 0.000 | 0.025 | 0.069 | 2.150 | 0.054 | 0.000 | 0.023 |
|  | Hybrid | 0.066 | 1.655 | 0.036 | 0.000 | 0.026 | 0.066 | 1.655 | 0.036 | 0.000 | 0.026 | 0.088 | 4.414 | 0.135 | 0.000 | 0.031 | 0.070 | 2.150 | 0.054 | 0.000 | 0.027 |
| Petroleum Diesel | ICE | 0.049 | 2.759 | 0.063 | 0.008 | 0.031 | 0.080 | 5.518 | 0.135 | 0.011 | 0.041 | 0.112 | 5.518 | 0.180 | 0.012 | 0.041 | 0.072 | 4.295 | 0.111 | 0.010 | 0.037 |
|  | Hybrid | 0.049 | 2.759 | 0.063 | 0.005 | 0.031 | 0.080 | 5.518 | 0.135 | 0.007 | 0.041 | 0.112 | 5.518 | 0.180 | 0.008 | 0.041 | 0.072 | 4.295 | 0.111 | 0.006 | 0.037 |
| Bio-Diesel (B20) | ICE | 0.049 | 2.759 | 0.063 | 0.006 | 0.030 | 0.080 | 5.518 | 0.135 | 0.009 | 0.039 | 0.112 | 5.518 | 0.180 | 0.010 | 0.039 | 0.072 | 4.295 | 0.111 | 0.008 | 0.035 |
|  | Hybrid | 0.049 | 2.759 | 0.063 | 0.004 | 0.030 | 0.080 | 5.518 | 0.135 | 0.006 | 0.039 | 0.112 | 5.518 | 0.180 | 0.007 | 0.039 | 0.072 | 4.295 | 0.111 | 0.005 | 0.035 |
| Electricity | Electric | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 |
| Hydrogen (NG) | Fuel Cell | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 |
| Hydrogen (Solar) | Fuel Cell | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 | 0.000 | 0.000 | 0.000 | 0.000 | 0.021 |
|  |  | Criteria Pollutant Emissions from Full Fuel Cycle (grams/vehicle-mile) |
| Reform. Gasoline (Federal Phase 2) | ICE | 0.229 | 2.908 | 0.251 | 0.106 | 0.082 | 0.264 | 2.957 | 0.323 | 0.141 | 0.099 | 0.321 | 5.749 | 0.470 | 0.165 | 0.121 | 0.259 | 3.435 | 0.317 | 0.130 | 0.095 |
|  | Hybrid | 0.161 | 2.837 | 0.149 | 0.056 | 0.060 | 0.179 | 2.863 | 0.187 | 0.074 | 0.069 | 0.220 | 5.640 | 0.311 | 0.087 | 0.087 | 0.179 | 3.349 | 0.193 | 0.068 | 0.068 |
| Ethanol (E90) | ICE | 0.236 | 3.262 | 0.849 | 0.005 | 0.112 | 0.273 | 3.429 | 1.120 | 0.006 | 0.141 | 0.339 | 6.339 | 1.462 | 0.008 | 0.173 | 0.268 | 3.876 | 1.061 | 0.006 | 0.134 |
|  | Hybrid | 0.170 | 3.050 | 0.507 | 0.003 | 0.079 | 0.192 | 3.147 | 0.664 | 0.004 | 0.095 | 0.234 | 5.971 | 0.869 | 0.004 | 0.115 | 0.190 | 3.610 | 0.631 | 0.003 | 0.092 |
| Methanol (M90) | ICE | 0.180 | 2.970 | 0.220 | 0.038 | 0.042 | 0.198 | 3.040 | 0.281 | 0.051 | 0.047 | 0.248 | 5.862 | 0.435 | 0.062 | 0.057 | 0.199 | 3.514 | 0.281 | 0.047 | 0.047 |
|  | Hybrid | 0.138 | 2.881 | 0.142 | 0.022 | 0.038 | 0.149 | 2.922 | 0.178 | 0.029 | 0.041 | 0.184 | 5.708 | 0.301 | 0.034 | 0.051 | 0.150 | 3.403 | 0.184 | 0.027 | 0.042 |
| CNG | ICE | 0.075 | 1.775 | 0.271 | 0.058 | 0.031 | 0.080 | 1.815 | 0.349 | 0.077 | 0.034 | 0.098 | 4.611 | 0.519 | 0.094 | 0.039 | 0.081 | 2.298 | 0.345 | 0.071 | 0.034 |
|  | Hybrid | 0.069 | 1.729 | 0.181 | 0.036 | 0.031 | 0.072 | 1.754 | 0.229 | 0.047 | 0.033 | 0.095 | 4.530 | 0.361 | 0.055 | 0.039 | 0.075 | 2.240 | 0.232 | 0.044 | 0.033 |
| LNG | ICE | 0.094 | 1.837 | 0.367 | 0.020 | 0.033 | 0.105 | 1.897 | 0.478 | 0.026 | 0.036 | 0.129 | 4.711 | 0.677 | 0.032 | 0.042 | 0.104 | 2.374 | 0.464 | 0.024 | 0.036 |
|  | Hybrid | 0.080 | 1.767 | 0.241 | 0.012 | 0.032 | 0.088 | 1.805 | 0.309 | 0.016 | 0.034 | 0.113 | 4.589 | 0.454 | 0.019 | 0.041 | 0.089 | 2.287 | 0.305 | 0.015 | 0.035 |
| LPG | ICE | 0.093 | 1.744 | 0.135 | 0.032 | 0.030 | 0.102 | 1.773 | 0.167 | 0.043 | 0.033 | 0.133 | 4.559 | 0.296 | 0.052 | 0.037 | 0.104 | 2.259 | 0.176 | 0.040 | 0.033 |
|  | Hybrid | 0.084 | 1.713 | 0.100 | 0.021 | 0.031 | 0.090 | 1.732 | 0.121 | 0.028 | 0.032 | 0.116 | 4.503 | 0.234 | 0.032 | 0.039 | 0.092 | 2.220 | 0.132 | 0.025 | 0.033 |
| Petroleum Diesel | ICE | 0.077 | 2.836 | 0.161 | 0.056 | 0.041 | 0.117 | 5.621 | 0.266 | 0.075 | 0.054 | 0.155 | 5.639 | 0.333 | 0.088 | 0.057 | 0.106 | 4.390 | 0.231 | 0.069 | 0.049 |
|  | Hybrid | 0.067 | 2.810 | 0.127 | 0.037 | 0.038 | 0.104 | 5.585 | 0.220 | 0.049 | 0.050 | 0.140 | 5.597 | 0.280 | 0.057 | 0.051 | 0.094 | 4.357 | 0.190 | 0.045 | 0.045 |
| Bio-Diesel (B20) | ICE | 0.127 | 2.901 | 0.250 | 0.058 | 0.044 | 0.184 | 5.707 | 0.384 | 0.077 | 0.058 | 0.234 | 5.739 | 0.471 | 0.090 | 0.061 | 0.168 | 4.468 | 0.340 | 0.071 | 0.052 |
|  | Hybrid | 0.100 | 2.851 | 0.185 | 0.038 | 0.039 | 0.148 | 5.641 | 0.298 | 0.050 | 0.051 | 0.191 | 5.662 | 0.370 | 0.059 | 0.053 | 0.134 | 4.408 | 0.261 | 0.046 | 0.046 |
| Electricity | Electric | 0.022 | 0.071 | 0.429 | 0.408 | 0.056 | 0.029 | 0.094 | 0.573 | 0.544 | 0.067 | 0.038 | 0.126 | 0.765 | 0.727 | 0.083 | 0.027 | 0.089 | 0.544 | 0.516 | 0.065 |
| Hydrogen (NG) | Fuel Cell | 0.015 | 0.128 | 0.208 | 0.057 | 0.029 | 0.020 | 0.171 | 0.278 | 0.076 | 0.032 | 0.023 | 0.200 | 0.325 | 0.088 | 0.034 | 0.018 | 0.157 | 0.255 | 0.070 | 0.031 |
| Hydrogen (Solar) | Fuel Cell | 0.007 | 0.035 | 0.126 | 0.061 | 0.027 | 0.010 | 0.047 | 0.167 | 0.082 | 0.029 | 0.011 | 0.055 | 0.196 | 0.095 | 0.031 | 0.009 | 0.043 | 0.154 | 0.075 | 0.029 |
| (1) ICE indicates internal combustion engine. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (2) Light-duty trucks with Gross Vehicle Weight Rating 6,000 pounds or less. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (3) Light-duty trucks with Gross Vehicle Weight Rating 6,001-8,500 pounds. |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (4) Weighted average of Auto, LDT1, and LDT2 rates, computed using fleet shares shown in Table 1 as weights. |
| (5) Volatile organic compounds. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (6) Carbon monoxide. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (7) Nitrogen oxides. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (8) Sulfur oxides. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| (9) Particulate matter 10 microns or less in diameter. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Source: Calculated using Wang, Michael Q., GREET 1.5a -- Transportation Fuel-Cycle Model (with Volpe input assumptions), Argonne National Laboratories, January 2000. |  |

| Table A-7. Near-term light-duty vehicle manufacturing, fuel production, and fuel infrastructure costs for alternative fuel use. |
| --- |
| Fuel | Feedstock | Added Vehicle Production Cost (1) | Fuel Infrastructure Costs (2) | Fuel Price ($/million Btu) (4) |
|  |  | Original Estimate | in $ of | Equivalent in 2000 $ (3) | Original Estimate | in $ of | Equivalent in 2000 $ (3) | Basis for Estimate | Number of Vehicles | per-Vehicle Equivalent |  |
| Gasoline | Petroleum | $0 | 2000 | $0 | $0 | 2000 | $0 | Baseline | -- | $0 | $7.64 |
| Ethanol (E85) | Corn | $200 | 1990 | $247 | $59,181 | 1999 | $60,442 | 33,000 gal/mo | 438 | $138 | $15.37 |
| Methanol (M85) | Natural Gas | $200 | 1990 | $247 | $59,181 | 1999 | $60,442 | 33,000 gal/mo | 325 | $186 | $9.22 |
| CNG (Bi-Fuel) | Natural Gas | $964 | 1990 | $1,192 | $310,775 | 1989 | $399,351 | 50,000 GGE/mo (one pump) | 977 | $409 | $6.52 |
| CNG (Dedicated) | Natural Gas | $526 | 1990 | $650 | $310,775 | 1989 | $399,351 | 50,000 GGE/mo (one pump) | 977 | $409 | $6.52 |
| LNG | Natural Gas | $2,000 | 2000 | $2,000 | $0.193 | 1995 | $0.211 | $ per GGE | 0.00013023 | $1,616 | $9.46 |
| LPG | Petroleum/ Natural Gas | $198 | 1990 | $245 | $0.111 | 1995 | $0.121 | $ per GGE | 0.00013280 | $912 | $10.94 |
| Petroleum Diesel | Petroleum | $2,500 | 2000 | $2,500 | $25,000 | 2000 | $25,000 | 33,000 gal/mo | 977 | $26 | $5.95 |
| Bio-Diesel (B20) | Petroleum/Soy | $2,500 | 2000 | $2,500 | $25,000 | 2000 | $25,000 | 50,000 GGE/mo (one pump) | 977 | $26 | $7.40 |
| Electricity | Projected U.S. Mix | $17,000 | 2000 | $17,000 | $120 | 2000 | $120 | home charger (one/vehicle) | 1 | $120 | $13.47 |
| (1) Additional manufacturing costs for vehicles capable of operating on alternative fuel. |  |  |  |  |  |
| (2) Costs for additional fuel distribution, storage, and retailing infrastrutcture required to allow fuel to replace gasoline use. |  |  |  |
| (3) Adjusted to year-2000 dollars using change in Implicit Price Deflator for Gross Domestic Product. |  |  |  |  |
| (4) Source: Energy Information Administration, Annual Energy Outlook 2002: Reference Case Forecast, Table 3; converted to pre-tax value using fuel taxe rates reported in Federal Highway Adminisrtration, Highway Statistics 1999, Tables FE-21B and MF-121T. |
| Sources: Arthur D. Little, Inc., Alternative Fuel Infrastructure Economics and Issues, March 1997; Greene, David L., An Assessment of Energy and Environmental Issues Related to the Use of Gas-to-Liquid Fuels in Transportation, ORNL/TM-1999/258, Center for Transportation Analysis, Oak Ridge National Laboratory, November 1999; E.A. Mueller, Inc., An Assessment of the Infrastructure Required to Refuel a Large Population of Natural Gas Vehicles, January, 1989; U.S. Environmental Protection Agency, Analysis of the Economic and Environmental Effects of Compressed Natural Gas as a Vehicle Fuel, Volume I: Passenger Cars and Light Trucks, April 1990; Argonne National Laboratory, Assessment of PNG Fuels Infrastructure: Phase 1 Report: Additional Capital Needs and Fuel-Cycle Energy and Emissions Impacts, ANL/ESD/TM-140, January 1997, and Assessment of PNG Fuels Infrastructure: Phase 2 Report: Additional Capital Needs and Fuel-Cycle Energy and Emissions Impacts, ANL/ESD-37, August 1998; Williams, Larson, et al., Methanol and Hydrogen from Biomass for Transportation, with Comparisons to Methanol and Hydrogen from Natural Gas, PU/CEES Report No. 292, July 1995. |

| Table A-8. Near-term alternative fuel and feedstock production and energy content. |
| --- |
| Fuel | Feedstock | Units of Measure | Baseline 2010 Production (quadrillion Btu) (1) | Btu Equivalent of Measurement Units (2) | Baseline 2010 Production (Billion Units) (3) |
|  |  | Fuel | Feedstock | Fuel | Feedstock | Fuel | Feedstock | Fuel | Feedstock |
| Gasoline | Petroleum | gallon | gallon | 19.39 | 35.87 | 114,540 | 130,000 | 169 | 276 |
| Ethanol (E85) | Corn | gallon | bushel | 0.24 | -- | 81,781 | -- | 2.93 | 11.08 |
| Methanol (M85) | Natural Gas | gallon | cubic foot | 0.1 | 23.09 | 65,631 | 928 | 1.52 | 24,881 |
| CNG | Natural Gas | cubic foot | cubic foot | 0.23 | 23.09 | 928 | 928 | 248 | 24,881 |
| LNG | Natural Gas | gallon | cubic foot | 0.80 | 23.09 | 72,900 | 928 | 10.91 | 24,881 |
| LPG | Petroleum | gallon | gallon | 3.03 | 35.87 | 84,000 | 130,000 | 36 | 276 |
|  | Natural Gas | gallon | cubic foot | 3.03 | 23.09 | 84,000 | 928 | 36 | 24,881 |
| Petroleum Diesel | Petroleum | gallon | gallon | 8.16 | 35.87 | 128,500 | 130,000 | 64 | 276 |
| Bio-Diesel (B20) | Soy | gallon | pound | (4) | -- | 126,218 | -- | (4) | 22.5 |
| Electricity | Projected U.S. Mix | kwh | various | 14.23 | -- | 3,412 | -- | 4,170 | -- |
| (1) Source:U.S. Energy Information Administration, Annual Energy Outlook 2002 -- Reference Case Forecast, Appendix A, Tables A-1 and A-2. |
| (2) Source: Wang, Michael, GREET 1.5a -- Transportation Fuel-Cycle Model: Volume 1, Methodology, Use, and Results, ANL/ESD-39, Argonne National Laboratories, 1999, Table 3.3 (low heating values). |
| (3) Computed from Baseline Production in quadrillion Btu divided by Btui equivalent of measurement units. |  |  |
| (4) No production anticipated in absence of use as a transportation fuel. |  |  |
| -- Indicates data not available. |  |  |

Table A-9.  Long-term alternative fuel and feedstock production and energy content.