AA-F-358H

AMENDMENT 3

# April 20, 2007

SUPERSEDING

INTERIM AMENDMENT 2

December 10, 2001

FEDERAL SPECIFICATION

# FILING CABINET, LEGAL AND LETTER SIZE, UNINSULATED, SECURITY

The General Services Administration has authorized the use of this amendment, which forms a part of AA-F-358H, dated May 18, 2000, by all federal agencies.

Page 2

Add the following to Paragraph 2.1 under Federal Specifications:

FF-L-2937 Combination Lock, Mechanical

TT-C-490 - Chemical Conversion Coatings and Pretreatments for Ferrous 
Surfaces (Base for Organic Coatings)

Page 3

Delete the first entry in Paragraph 2.2 (American National Standards Institute (ANSI) / American Society for Quality (ASQ)) in its entirety and substitute the following:

2.2

American Society for Quality (ASQ):

ASQ Z1.4 - Sampling Procedures and Tables for Inspection by Attributes

(Private sector and civil agencies may purchase copies of this voluntary 	standard from the American Society for Quality, P. O. Box 3005, 	Milwaukee, WI  53201-3005.)

FSC 7110

Page 3

Delete the reference for UL 768.

Page 9

Delete Paragraph 3.4.2 in its entirety and substitute the following:

3.4.2  Changeable combination lock.  A changeable combination lock of the type specified herein shall be installed as an integral part of the cabinet.  The lock dial and ring shall be of top reading, spy resistant design with dial and ring protected by a snap-on dust cover.  Class 6, Size VIII cabinets shall be furnished with locks that meet the requirements of Federal Specification FF-L-2937.  Class 6, Size VII cabinets may have locks that meet requirements of Federal Specification FF-L-2937 if the container is going to be used in a tactical vehicle only.  For all other applications, the Class 6, Size VII container shall have a lock approved in accordance with the requirements of Federal Specification FF-L-2740, Class TR, Type NT, Size LD.  Locks used on all other Classes and Sizes shall meet the requirements of Federal Specification FF-L-2740, Class TR, Type NT, Size LD.  The cabinet’s design shall incorporate a method of inspecting and servicing the lock and the cabinet’s bolt and cam without completely removing the drawer head.  The method used may be an inspection plate in the drawer head installed in a manner as not to affect the integrity of the container.

Page 11

Delete Paragraph 3.8 in its entirety and substitute the following:

3.8  Identification labels.  Each cabinet supplied under a contract or order under this specification shall bear metallic labels showing the information specified hereunder.  Labels shall be attached with a durable adhesive sufficient to preclude removing the label without destroying the label.  Regardless of the method used, the label attachment shall not degrade the cabinet security.

Page 11

Delete Paragraph 3.8.2 in its entirety and substitute the following:

3.8.2  Cabinet identification and contract number.  This label or labels shall be affixed to the external side of the drawer containing the lock.  The label shall show, in easily read letters, the manufacturer's name and address, the cabinet's model and serial numbers, date of manufacture, and the Government contract number.  On ML and DM cabinets, the label shall be on the top or second drawer.

Page 12

Delete Paragraph 3.8.4 in its entirety and substitute the following:

3.8.4  Number label.  Security cabinets under this specification shall have a number label securely affixed to the front face of the product.  The label shall be mounted on the cabinet frame above or to the left side of the top drawer.  The label shall be nominal 0.020 inch thick, satin finished aluminum and shall be 2-1/2 by 11/16 inches.  The label numbering system shall be established by the manufacturer to provide non-repetitive numbers.  The label characters (numbers or letters) shall be minimum 3/16 inches high and shall be embossed.

Page 12

Add the following Paragraph:

3.8.5  Warning label.  A warning label shall be affixed to the top inside of the control drawer head.  The label shall show, in red lettering not less than 1/8 inch high, the following:

Notice:  Any modification of this container not in accordance with Federal Standard 809 will invalidate the GSA approval and the GSA approval label shall be removed.

Page 12

Delete Paragraph 3.10 in its entirety and substitute the following:

3.10  Assembly drawing and parts list.  A parts list of all cabinet parts which may be subject to subsequent replacement because of wear or damage shall be furnished with each cabinet delivered under contract.  The parts list shall clearly identify the parts by description, location and part number.  When necessary, assembly drawings shall be provided to show the location of the parts. The parts list shall be printed on heavy paper or other suitable material and bonded by glue or adhesive to an inside surface of the cabinet in a location accessible to maintenance personnel.

Preparing Activity:

GSA-FSS

FSC 7110