# ENERGY STAR Electronics:

Sample Procurement Language

TVs, VCRs, and TV/VCR Combo Units

The Vendor Must:

Provide TVs, VCRs, and TV/VCR combination units that earn the Energy Star and meet the Energy Star specifications for energy efficiency, as outlined below, including standby mode wattages. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

| Product Type | Current Criteria—Effective through June 30, 2005 | New Criteria—Effective July 1, 2005 |
| --- | --- | --- |
|  | Standby Mode | Standby Mode |
| TV, Television Monitor | Analog: ≤ 1 Watt * Digital: ≤ 3 Watts | ≤ 1 Watt |
| VCR | ≤ 1 Watt | ≤ 1 Watt |
| Component Television Unit | ≤ 3 Watts | ≤ 1 Watt |
| TV/VCR Combination Units | ≤ 6 Watts | ≤ 1 Watt |
| TV/DVD, VCR/DVD, and TV/VCR/DVD Combinations | ≤ 4 Watts | ≤ 1 Watt |
| Digital Cable-Ready TV receivers (DCR TVs) that incorporate a Point Of Deployment (POD) slot | No POD Installed: < 3 Watts POD Installed: < 15 Watts | TBD |

Illuminated Display Allowance: Beginning in July 2004, manufacturers may add an additional 1-Watt to the 1-Watt specification for products with an illuminated or backlit display (e.g., clock) or other electronic status indicator (e.g., recording status or video mode indicator). For example, a VCR with an illuminated display must consume 2 Watts or less to qualify for the ENERGY STAR label beginning on July 1, 2004. All other VCRs must consume 1 Watt or less to qualify.

*NOTE: This allowance does not apply to Digital TVs as they are allowed 3 Watts in the current criteria and not required to adhere to the 1-Watt specification until July 2005.

DVD & Home Audio

The Vendor Must:

Provide DVD players and home audio equipment that earn the Energy Star and meet the Energy Star specifications for energy efficiency, as outlined below, including standby mode wattages. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

| Product | Current Criteria—Effective January 1, 2003 |
| --- | --- |
|  | Standby Mode |
| Consumer Audio Products | ≤ 1.0 Watt |
| DVD Products | ≤ 1.0 Watt |

# Set-top Boxes

The Vendor Must:

Provide set-top boxes that earn the Energy Star and meet the Energy Star specifications for energy efficiency, as outlined below, including standby mode wattages. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

| Product Category | Current Criteria—Effective January 1, 2004 |
| --- | --- |
|  | Standby/Low power Mode |
| Category 1 • Analog Cable TV Set-top Box • Advanced Analog Cable TV Set-top Box • Digital TV Converter Set-top Box • Internet Access Device • Video Game Console • Videophone Set-top Box • Set-top Box (e.g., Internet access device) with Cable Modem for enhanced communications in Standby/Low-power Mode | One specification for all set-top boxes: ≤ 7 Watts (for satellite systems, add ≤ 5 Watts for each Low Noise Blockers (LNB)) |
| Category 2 • Digital Cable TV Set-top Box • Satellite TV Set-top Box* • Wireless TV Set-top Box • Personal Video Recorder |  |
| Category 3 • Multifunction Device (i.e., a physically integrated device that has the core function of a satellite TV set-top box, digital cable TV set-top box, wireless TV set-top box, or personal video recorder plus one or more additional functionalities, such as an Internet access device or video game console) |  |

*NOTE: The current Energy Star specification for each stand-alone satellite receiver is 7 Watts or less; manufacturers may add an additional 5 Watts or less to the specification for each LNB sold with a receiver. Please note that LNBs sold separately may not qualify for the label.

Answering Machines & Cordless Phones

The Vendor Must:

Provide answering machines and cordless phones that earn the Energy Star and meet the Energy Star specifications for energy efficiency, as outlined below, including standby mode wattages. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

| Product Category | Current Criteria—Effective January 1, 2004 |
| --- | --- |
|  | Standby Mode |
| • Answering Machine • Cordless Telephone | ≤ 1.0 watt |
| • Answering Machine with Spread Spectrum Technology (SST) • Cordless Telephone with SST | ≤ 1.5 watts |
| • Combination Cordless Telephone/Answering Machine | ≤ 1.0 watt |
| • Combination Cordless Telephone/Answering Machine with SST | ≤ 2.0 watts |

Note: Any power consumed by an external power supply must be included when metering the unit for

ENERGY STAR Program Requirements for Telephony ENERGY STAR qualification.