# ENERGY STAR Residential Appliances:

Sample Procurement Language

Refrigerators and Freezers

The Vendor Must:

Provide refrigerators and freezers that earn the ENERGY STAR and meet the ENERGY STAR criteria for energy efficiency as outlined below. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

Table 1: Criteria for ENERGY STAR Qualified Refrigerators

| Equipment | Volume | Criteria |
| --- | --- | --- |
| Full Size Refrigerators and Refrigerator-Freezers | 7.75 cubic feet or greater | At least 15% more energy efficient than the minimum federal government standard (NAECA). |
| Full Size Residential Freezers | 7.75 cubic feet or greater | At least 10% more energy efficient than the minimum federal government standard (NAECA) |
| Compact Refrigerators and/or Freezers | Less than 7.75 cubic feet and 36 inches or less in height | At least 20% more efficient than the minimum federal government standard (NAECA) |

| Refrigerator Product Class | NAECA maximum energy use (kWh/year) |
| --- | --- |
| 1. Refrigerators and Refrigerator-freezers with manual defrost | 8.82*AV + 248.4 |
| 2. Refrigerator-Freezer—partial automatic defrost | 8.82*AV + 248.4 |
| 3. Refrigerator-freezers—automatic defrost with top-mounted freezer without through-the-door ice service and all refrigerators—automatic defrost | 9.80*AV + 276 |
| 4. Refrigerator-Freezers—automatic defrost with side-mounted freezer without through-the-door ice service | 4.91*AV + 507.5 |
| 5. Refrigerator-Freezers—automatic defrost with bottom-mounted freezer without through-the-door ice service | 4.60*AV + 459 |
| 6. Refrigerator-Freezers—automatic defrost with top-mounted freezer with through-the-door ice service | 10.20*AV + 356 |
| 7. Refrigerator-Freezers—automatic defrost with side-mounted freezer with through-the-door ice service | 10.10*AV + 406 |
| 8. Upright Freezers with Manual Defrost | 7.55*AV+258.3 |
| 9. Upright Freezers with Automatic Defrost | 12.43*AV+326.1 |
| 10. Chest Freezers and all other Freezers except Compact Freezers | 9.88*AV+143.7 |
| 11. Compact Refrigerators and Refrigerator-Freezers with Manual Defrost | 10.70*AV+299 |
| 12. Compact Refrigerator-Freezer—partial automatic defrost | 7.00*AV+398 |
| 13. Compact Refrigerator-Freezers—automatic defrost with top-mounted freezer and compact all-refrigerators—automatic defrost | 12.70*AV+355 |
| 14. Compact Refrigerator-Freezers—automatic defrost with side-mounted freezer | 7.60*AV+501 |
| 15. Compact Refrigerator-Freezers—automatic defrost with bottom-mounted freezer | 12.1*AV+367 |
| 16. Compact Upright Freezers with Manual Defrost | 9.78*AV+250.8 |
| 17. Compact Upright Freezers with Automatic Defrost | 11.40*AV+391 |
| 18. Compact Chest Freezers | 10.45*AV+152 |

Refrigerator-Freezer Adjusted volume (AV) = Fresh Volume + (1.63 x Freezer Volume)

Refrigerator Adjusted Volume (AV) = (1.63 x Total Volume)

Freezer Adjusted volume (AV) = (1.73 x Total Volume)

NOTE: The previous ENERGY STAR criteria was set at 10% above the federal minimum efficiency standard that went into effect on July 1, 2001, and only covered products classes 3 – 7.  On January 1, 2003, the ENERGY STAR criteria expanded to include all sizes and configurations of refrigerators and freezers.  ENERGY STAR criteria for full size freezers was set at 10% above minimum federal standards.  ENERGY STAR criteria for compact refrigerators and freezers was set at 20% above minimum federal standards.

On January 1, 2004, the ENERGY STAR criteria changed to require all full-size refrigerators to be at least 15% above the minimum federal standard to qualify for ENERGY STAR. The ENERGY STAR criteria for full-sized freezers and compact refrigerators and freezers did not change at this time.

Additional considerations for the procurement official:

When purchasing a refrigerator, just specify the capacity that is the actual square footage of the refrigerator and freezer combined. Then specify that the energy consumption shall not exceed the ENERGY STAR specification. Include the "AV" and "Maximum kWh/yr" equations, so that the vendor can calculate the maximum energy consumption allowable by that model. Also, request that the vendor include the individual capacities of the freezer and refrigerator compartments so that compliance can be checked.

Dishwashers

The Vendor Must:

Provide dishwashers that earn the ENERGY STAR and meet the ENERGY STAR criteria for energy efficiency as outlined below. Only standard dishwashers that have a capacity greater than or equal to eight place settings plus six serving pieces can earn the ENERGY STAR. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

Current Criteria—Effective Jan. 1, 2001

Minimum Energy Factor of .58

Clothes Washers

The Vendor Must:

Provide clothes washers that earn the ENERGY STAR and meet the ENERGY STAR criteria for energy efficiency as outlined below. Only front and top loader clothes washers with capacities of greater than 1.6 ft3 are eligible to earn the ENERGY STAR. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

Current Criteria—Effective Jan. 1, 2004

Minimum Modified Energy Factor of 1.42

Dehumidifiers

The Vendor Must:

Provide dehumidifiers that earn the ENERGY STAR and meet the ENERGY STAR specifications for energy efficiency as outlined below. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

Table 1: Criteria for ENERGY STAR Qualified Standard Capacity Dehumidifiers

| Product Capacity (L/day) | Energy Factor Under Test Conditions (L/kWh) |
| --- | --- |
| L/day < 10 | ≥ 1.20 |
| 10 ≤ L/day < 25 | ≥ 1.30 |
| 25 ≤ L/day ≤ 35 | ≥ 1.50 |

Standard Capacity Dehumidifiers: Dehumidifiers with daily water-removal capacities up to 35 Liters (74.0 US pints)

Table 2: Criteria for ENERGY STAR Qualified High Capacity Dehumidifiers

| Product Capacity (L/day) | Energy Factor Under Test Conditions (L/kWh) |
| --- | --- |
| 36 ≤ L/day ≤ 57 | ≥ 2.25 |

High Capacity Dehumidifiers: Dehumidifiers with daily water-removal capacities up to 57 Liters (120.5 US pints)

Room Air Cleaners

The Vendor Must:

Provide room air cleaners that earn the Energy Star and meet the Energy Star specifications for energy efficiency as outlined below. The vendor is encouraged to visit energystar.gov for complete product specifications and an updated list of qualifying products.

| Current Criteria—Effective July 1, 2004 |
| --- |
| Room air cleaner minimum performance requirement * | ≥ 2.0 CADR/Watt (Dust) |
| Standby Power Requirement ** | ≤ 2 Watt(s) |
| UL Safety Requirements | Models that emit ozone as a byproduct of air cleaning must meet UL Standard 867 (ozone production must not exceed 50 ppb) |

CADR: Clean Air Delivery Rate

* Note: CADR for Dust must be used when determining the energy efficiency (CADR/Watt) of the room air cleaner. Qualifying air cleaner models must produce a minimum 50 CADR for Dust.

** Note: Qualifying models that perform secondary consumer functions (e.g. clock, remote control) must meet the standby power requirement. Combination products and ozone generators cannot qualify at this time.