U.S. Department of Transportation

Federal Aviation Administration

AIRPORT SAFETY SELF-INSPECTION CHECKLIST

| DATE: |  |  | DAY: |  | ( (p) | Satisfactory |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | ((o) | Unsatisfactory |
| Day Inspector/Time: |  |  | Night Inspector/Time: |  |

| FACILITIES | CONDITIONS | D | N | REMARKS | RESOLVED BY (Date/Initials |
| --- | --- | --- | --- | --- | --- |
| Pavement Areas | Pavement lips over 3” |  |  |  |  |
|  | Hole – 5” diam. 3 deep |  |  |  |  |
|  | Cracks/spalling/heaves |  |  |  |  |
|  | FOD: gravel/debris/sand |  |  |  |  |
|  | Rubber deposits |  |  |  |  |
|  | Ponding/edge dams |  |  |  |  |
| Safety Areas | Ruts/humps/erosion |  |  |  |  |
|  | Drainage/construction |  |  |  |  |
|  | Support equipment/aircraft |  |  |  |  |
|  | Frangible bases |  |  |  |  |
|  | Unauthorized objects |  |  |  |  |
| Markings | Clearly visible/standard |  |  |  |  |
|  | Runway markings |  |  |  |  |
|  | Taxiway markings |  |  |  |  |
|  | Holding position markings |  |  |  |  |
|  | Glass beads |  |  |  |  |
| Signs | Standard/meet Sign Plan |  |  |  |  |
|  | Obscured/operable |  |  |  |  |
|  | Damaged/retroreflective |  |  |  |  |

Certified current 5/15/2007

| FACILITIES | CONDITIONS | D | N | REMARKS | RESOLVED BY (Date/Initials |
| --- | --- | --- | --- | --- | --- |
| Lighting | Obscured/dirty/operable |  |  |  |  |
|  | Damaged/missing |  |  |  |  |
|  | Faulty aim/adjustment |  |  |  |  |
|  | Runway lighting |  |  |  |  |
|  | Taxiway lighting |  |  |  |  |
|  | Pilot control lighting |  |  |  |  |
| Navigational Aids | Rotating beacon operable |  |  |  |  |
|  | Wind Indicators |  |  |  |  |
|  | RENLs/VGSI systems |  |  |  |  |
| Obstructions | Obstruction lights operable |  |  |  |  |
|  | Cranes/trees |  |  |  |  |
| Fueling Operations | Fencing/gates/signs |  |  |  |  |
|  | Fuel marking/labeling |  |  |  |  |
|  | Fire extinguishers |  |  |  |  |
|  | Frayed wires |  |  |  |  |
|  | Fuel leaks/vegetation |  |  |  |  |
| Snow & Ice | Surface conditions |  |  |  |  |
|  | Snowbank clearances |  |  |  |  |
|  | Lights & signs obscured |  |  |  |  |
|  | NAVAIDs |  |  |  |  |
|  | Fire access |  |  |  |  |

Certified current 5/15/2007

| FACILITIES | CONDITIONS | D | N | REMARKS | RESOLVED BY (Date/Initials |
| --- | --- | --- | --- | --- | --- |
| Construction | Barricades/lights |  |  |  |  |
|  | Equipment parking |  |  |  |  |
|  | Material stockpiles |  |  |  |  |
|  | Confusing signs/markings |  |  |  |  |
| Aircraft Rescue and Fire Fighting | Equipment/crew availability |  |  |  |  |
|  | Communications/Alarms |  |  |  |  |
|  | Response routes affected |  |  |  |  |
| Public Protection | Fencing/gates/signs |  |  |  |  |
|  | Jet blast problems |  |  |  |  |
| Wildlife Hazards | Wildlife present/location |  |  |  |  |
|  | Complying with WHMP |  |  |  |  |
|  | Dead birds |  |  |  |  |
| Comments/Remarks: |

#### Certified current 5/15/2007                                                                                        Airfield Map on Reverse Side

### AIRFIELD MAP

Certified current 5/15/2007