### ITEM T-903  SPRIGGING

DESCRIPTION

903-1.1   This item shall consist of planting sprigs of living grass plants at the locations shown on the plans or as directed by the Engineer in accordance with these specifications.

MATERIALS

903-2.1  SPRIGS.  Sprigs shall be healthy living stems (stolons or rhizomes), of the grass species stated in the special provisions, harvested without adhering soil and obtained from sources where the sod is heavy and thickly matted.  The presence of weeds or other material that might be detrimental to the proposed planting will be cause for rejection of sprigs.

903-2.2  LIME.  Lime shall conform to the requirements of 901-2.2.

903-2.3  FERTILIZER.  Fertilizer shall conform to the requirements of 901-2.3.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

Paragraphs 2.2 and 2.3 shall be deleted if not applicable.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

903-2.4  WATER.  All water used shall be sufficiently free from oil, acid, alkali, salt, or other harmful materials that would inhibit the growth of grass.  Brackish water shall not be used at any time.  It shall be subject to the approval of the Engineer prior to use.

903-2.5  SOIL FOR REPAIRS.  The soil for fill, and topsoiling of areas to be repaired, shall conform to the requirements of 901-2.4.

CONSTRUCTION METHODS

903-3.1  GENERAL.  Areas to be sprigged and the location of sprigging material, if available on the site, shall be shown on the plans.  Areas requiring special ground surface preparation such as tilling, and those in a satisfactory condition to remain undisturbed, shall also be shown on the plans.

Suitable equipment necessary for proper preparation of the ground surface and for the handling and placing of all required materials shall be on hand, in good condition, and shall be approved by the Engineer before the various operations are started.  The Contractor shall demonstrate to the Engineer, before starting the various operations, that the planting and application of required materials will be made at the specified rates.

When weather conditions are such that unsatisfactory results may occur, the work shall be stopped until the desired results can be obtained.

903-3.2  ADVANCE PREPARATION AND CLEANUP.  After grading of areas has been completed and before applying fertilizer and limestone, areas to be sprigged shall be raked or otherwise cleared of stones larger than 2 inches (50 mm) in any diameter, sticks, stumps, and other debris which might interfere with sprigging, growth of grasses, or subsequent maintenance of grass-covered areas.  If any damage by erosion or other causes has occurred after grading of areas and before beginning the application of fertilizer and ground limestone, the Contractor shall repair such damage.  This may include filling gullies, smoothing irregularities, and repairing other incidental damage.

903-3.3  APPLYING FERTILIZER AND GROUND LIMESTONE.  Following advance preparation and cleanup, fertilizer shall be uniformly spread at a rate that will provide not less than the minimum quantity of each fertilizer ingredient as stated in the special provisions.  If use of ground limestone is required, it shall then be spread at a rate that will provide not less than the minimum quantity stated in the special provisions.  These materials shall be incorporated into the soil to a depth of not less than 2 inches (50 mm) by discing, raking, or other methods acceptable to the Engineer.  Any stones larger than 2 inches (50 mm) in any diameter, large clods, roots, and other litter brought to the surface by this operation shall be removed.

In steep slopes where fertilizer and ground limestone cannot be incorporated effectively by mechanical equipment, they may be applied with power sprayers, blower equipment, or other approved method, and need not be incorporated into the soil.

903-3.4  HARVESTING SPRIGS.  The sprigs obtained from sources off the site shall be from suitable areas as close as practical to the planting site.  Regardless of the source, sprigging material that contains grass and weeds taller than 6 inches (150 mm) shall be mowed to a height of 3 inches (75 mm), and the clippings raked and removed before harvesting begins.  Harvesting may be performed by any method acceptable to the Engineer, including crisscross cultivation, shallow plowing, or other acceptable methods to thoroughly loosen the sprigs from the soil and to bring them to the surface.  After loosening the sprigs from the soil, they shall be gathered in small piles or windrows, watered, and kept moist until planted.

Not more than 24 hours shall elapse between harvesting and planting sprigs, except that, when weather or other uncontrollable conditions interrupt the work, a time extension may be granted, provided the sprigs are still moist and viable.  Sprigs that have heated in stockpiles, have become frozen, permitted to dry out, or otherwise seriously damaged during harvesting or delivery shall be rejected and shall be disposed of as directed by the Engineer.

903-3.5  PLANTING SPRIGS.  Sprigging shall be done only within the periods stipulated in the special provisions.  Sprigging shall not be done during windy weather, or when the ground is dry, excessively wet, frozen, or otherwise untillable.  If the soil is not moist when the sprigs are being set, water shall be applied until the soil is moist and in a workable condition.  One or more of the following methods shall be used, whichever is shown on the plans or stated in the special provisions:

a.  Broadcast Sprigging.  Sprigs shall be broadcast by hand or by suitable equipment in a uniform layer over the prepared surface with spacing between sprigs not to exceed 6 inches (150 mm).  The sprigs shall then be forced into the soil to a depth of 2 to 4 inches (50 to 100 mm) with a straight spade or similar tool, or with a disc harrow or other equipment set to cover the sprigs to the required depth.

b.  Row Sprigging.  Furrows shall be opened along the approximate contour of slopes at the spacing and depth stated in the special provisions.  Sprigs shall be placed without delay in a continuous row in the open furrow with successive sprigs touching, and they shall be covered immediately.

c.  Spot Sprigging.  Spot sprigging shall be performed as specified under row sprigging, except that groups of 4 sprigs or more shall be spaced 18 inches (45 cm) apart in the rows.

903-3.6  MULCHING AND COMPACTING.  After planting of sprigs has been completed and prior to compacting, the surface shall be cleared of stones larger than 2 inches (50 mm) in any diameter, large clods, roots, and other litter brought to the surface during sprigging.

If mulching of sprigged areas is shown on the plans or stated in the special provisions, the sprigged areas shall be covered with mulch in accordance with the requirements of Item T-908 within 24 hours from the time sprigging has been completed, weather and soil conditions permitting.

If mulching is not shown on the plans nor stated in the special provisions, the sprigged area shall be compacted within 24 hours from the time sprigging has been completed, weather and soil conditions permitting, by cultipackers, rollers, or other satisfactory equipment operated at right angles to the slope.  Compaction shall not be done when the soil is in such condition that it is picked up by the equipment.

903-3.7  ESTABLISHING TURF.  The Contractor shall be responsible for the proper care of the sprigged areas during the period when the plants are becoming established and he shall protect the sprigged areas against traffic by warning signs or barricades approved by the Engineer.  Surfaces gullied or otherwise damaged following sprigging shall be repaired by regrading and resprigging as directed.  The Contractor shall mow, water as directed, and otherwise maintain sprigged areas in a satisfactory condition until final inspection and acceptance of the work.

METHOD OF MEASUREMENT

903-4.1  Sprigging shall be measured by the number of units of 1,000 square feet (100 square meters), measured on the ground surface, completed and accepted.

BASIS OF PAYMENT

903-5.1  Payment will be made at the contract unit price per 1,000 square feet (100 square meters) or fraction thereof.  This price shall be full compensation for furnishing and placing all material including any required mulching of sprigged areas, and for all labor, equipment, tools, and incidentals necessary to complete the work prescribed in this item.

Payment will be made under:

Item 903-5.1	Sprigging—per 1,000 square feet (100 square meters)

END OF ITEM T-903

Intentionally Left Blank