Fifth Meeting of the Cross Polar Trans East Air Traffic Management Providers’ Work Group (CPWG/5)

(Ft. Worth, TX, 1-3 April 2008)

Agenda Item 5:  Review Action Items

PROPOSED TEST PLAN FOR A TRIAL OF AIR TRAFFIC FLOW MANAGEMENT PROCEDURES FOR RUSSIAN TRANS EAST FIX LISKI

(Presented by the United States of America)

SUMMARY

This paper presents information and seeks customer participation in a proposed trial to improve operations from eastern and midwestern North America via the Russian Trans East gateway fix LISKI.  The paper describes the trial procedures and feedback process.

- Background

  - Based on the successful outcome of the trial of air traffic flow management (ATFM) procedures on Polar routes DEVID, RAMEL, NIKIN and ORVIT, the FAA and NAV CANADA have agreed to expand the trial procedures to include Russian Trans East (RTE) fix LISKI.  This paper provides details of the trial.

- Schedule

  - The trial will begin at 1430 UTC on April 7, 2008 and continue through May 10, 2008.

  - Reviews of the trial will be conducted weekly by telcon hosted by the Federal Aviation Administration’s Air Traffic Control System Command Center (ATCSCC), permitting a consensus decision to be made at the end of the trial period concerning the permanent adoption of the trial concept and procedures.  Changes to the agreed procedures will be coordinated with the customers in advance of implementation.

  - Telcon participants will be Anchorage Air Route Traffic Control Center (ARTCC), NAV CANADA National Operations Centre (NOC), Edmonton Area Control Centre (ACC), and interested airspace operators.  Telcons will be conducted on Fridays from April 11 through May 9 at 1900 UTC.  Participants may dial in by calling +1 703 925 5387 and entering PIN 2777#.

- Procedures

  - Customers planning to fly via gateway fix LISKI will continue to comply with the existing requirements of the Dynamic Ocean Tracking System Plus (DOTS+) Track Advisory program.  This will permit flight dispatchers to remain aware of other traffic which may have flight planned over LISKI.  DOTS+ will provide 10 minutes longitudinal separation between flights going to the same fix at the same altitude.  No additional buffer will be provided.

  - The ATCSCC will coordinate with dispatch when appropriate and U.S. ATC units if a conflict or resolution takes place in U.S. airspace. The NOC will coordinate with dispatch when appropriate and Canadian ATC units if a conflict or resolution takes place in Canadian airspace.

  - The appropriate facility or facilities (i.e., ATCSCC, NOC, Edmonton ACC and/or Anchorage ARTCC) will determine the appropriate mitigation.

- Trial Responsibilities

  - Operators:

- Will brief dispatchers/flight crews about this trial.

- Although Controlled Departure Times (CDTs) will no longer be issued, flight crews are expected to depart during their 10-minute departure window.

- Dispatchers must continue to comply with all current Anchorage ARTCC track advisory procedures.

- Will provide feedback during ATCSCC hosted review telcons.

  - ATCSCC:

- Will no longer issue CDTs for flights destined to RTE entry fix LISKI.

- Will monitor Enhanced Traffic Management System (ETMS) and DOTS+ systems to identify possible flight conflicts.

- Will implement any conflict resolution directed by NAV CANADA.

- In conjunction with airline operators, the NOC, and Anchorage ARTCC Traffic Management Unit (TMU), will collect documentation related to the test on flights filed over LISKI.  Documentation may include, but is not limited to:

  - Actual departure times

  - Flight planned altitude at the Polar fix

  - Actual altitude crossing the Polar fix

  - NOC:

- Will work with the ATCSCC and NAV CANADA enroute ATC facilities to determine and implement an appropriate conflict resolution decision.

- Will provide feedback during ATCSCC hosted review telcons.

  - Edmonton ACC:

- Will work with NOC to determine and implement appropriate conflict resolutions decisions if required.

- Will provide feedback during ATCSCC hosted review telcons.

  - Anchorage TMU:

- Will maintain and operate the Polar DOTS+ Track Advisory program.

- Will collect documentation to provide actual crossing times/altitudes at Polar fixes.

- Will provide feedback to ATCSCC hosted review telecons.

- Recommendation

  - The meeting is invited to:

- note the information in this working paper, and

- agree to support the proposed trial.