### SECTION 60 
CONTROL OF MATERIALS

60-01  SOURCE OF SUPPLY AND QUALITY REQUIREMENTS.  The materials used on the work shall conform to the requirements of the contract, plans, and specifications.  Unless otherwise specified, such materials that are manufactured or processed shall be new (as compared to used or reprocessed).

In order to expedite the inspection and testing of materials, the Contractor shall furnish complete statements to the Engineer as to the origin, composition, and manufacture of all materials to be used in the work.  Such statements shall be furnished promptly after execution of the contract but, in all cases, prior to delivery of such materials.

At the Engineer's option, materials may be approved at the source of supply before delivery is stated.  If it is found after trial that sources of supply for previously approved materials do not produce specified products, the Contractor shall furnish materials from other sources.

The Contractor shall furnish airport lighting equipment that conforms to the requirements of cited materials specifications.  In addition, where an FAA specification for airport lighting equipment is cited in the plans or specifications, the Contractor shall furnish such equipment that is:

a.  Listed in FAA Advisory Circular (AC) 150/5345-53, Airport Lighting Equipment Certification Program, that is in effect on the date of advertisement; and,

b.  Produced by the manufacturer qualified (by FAA) to produce such specified and listed equipment.

The following airport lighting equipment is required for this contract and is to be furnished by the Contractor in accordance with the requirements of this subsection:

EQUIPMENT NAME

CITED FAA SPECIFICATIONS

EFFECTIVE FAA AC OR APPROVAL LETTER FOR EQUIPMENT AND

MANUFACTURER

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

To avoid errors, the design Engineer should furnish the above listing after having conformed the list to those specifications cited on the plans or in the technical specifications.  Both the individual FAA material specifications and the AC 150/5345-53, Airport Lighting Equipment Certification Program, should be listed to indicate the edition that is effective on the date the contract is advertised.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

60-02  SAMPLES, TESTS, AND CITED SPECIFICATIONS.  Unless otherwise designated, all materials used in the work shall be inspected, tested, and approved by the Engineer before incorporation in the work.  Any work in which untested materials are used without approval or written permission of the Engineer shall be performed at the Contractor's risk.  Materials found to be unacceptable and unauthorized will not be paid for and, if directed by the Engineer, shall be removed at the Contractor's expense.  Unless otherwise designated, tests in accordance with the cited standard methods of ASTM, AASHTO, Federal Specifications, Commercial Item Descriptions, and all other cited methods, which are current on the date of advertisement for bids, will be made by and at the expense of the Engineer.  The testing organizations performing on site field tests shall have copies of all referenced standards on the construction site for use by all technicians and other personnel, including the Contractor's representative at his/her request.  Unless otherwise designated, samples will be taken by a qualified representative of the Engineer.  All materials being used are subject to inspection, test, or rejection at any time prior to or during incorporation into the work.  Copies of all tests will be furnished to the Contractor's representative at his/her request.

The Contractor shall employ a testing organization to perform all Contractor required tests.  The Contractor shall submit to the Engineer resumes on all testing organizations and individual persons who will be performing the tests.  The Engineer will determine if such persons are qualified.  All the test data shall be reported to the Engineer after the results are known.  A legible, handwritten copy of all test data shall be given to the Engineer daily, along with printed reports, in an approved format, on a weekly basis.  After completion of the project, and prior to final payment, the Contractor shall submit a final report to the Engineer showing all test data reports, plus an analysis of all results showing ranges, averages, and corrective action taken on all failing tests.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

The Engineer may wish to include a requirement that all test data from the Contractor be furnished in electronic format.  The Engineer shall provide detailed specifications to specify the acceptable format to be used.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

60-03  CERTIFICATION OF COMPLIANCE.  The Engineer may permit the use, prior to sampling and testing, of certain materials or assemblies when accompanied by manufacturer's certificates of compliance stating that such materials or assemblies fully comply with the requirements of the contract.  The certificate shall be signed by the manufacturer.  Each lot of such materials or assemblies delivered to the work must be accompanied by a certificate of compliance in which the lot is clearly identified.

Materials or assemblies used on the basis of certificates of compliance may be sampled and tested at any time and if found not to be in conformity with contract requirements will be subject to rejection whether in place or not.

The form and distribution of certificates of compliance shall be as approved by the Engineer.

When a material or assembly is specified by ``brand name or equal'' and the Contractor elects to furnish the specified ``brand name,'' the Contractor shall be required to furnish the manufacturer's certificate of compliance for each lot of such material or assembly delivered to the work.  Such certificate of compliance shall clearly identify each lot delivered and shall certify as to:

a.  Conformance to the specified performance, testing, quality or dimensional requirements; and,

b.  Suitability of the material or assembly for the use intended in the contract work.

Should the Contractor propose to furnish an ``or equal'' material or assembly, he shall furnish the manufacturer's certificates of compliance as hereinbefore described for the specified brand name material or assembly.  However, the Engineer shall be the sole judge as to whether the proposed ``or equal'' is suitable for use in the work.

The Engineer reserves the right to refuse permission for use of materials or assemblies on the basis of certificates of compliance.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

When it is necessary to specify a material or assembly by ``brand name or equal,'' the technical requirements (performance, testing, quality, or dimensions) must be accurately described in enough detail to ensure a suitable product while not restricting competition unduly.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

60-04  PLANT INSPECTION.  The Engineer or his/her authorized representative may inspect, at its source, any specified material or assembly to be used in the work.  Manufacturing plants may be inspected from time to time for the purpose of determining compliance with specified manufacturing methods or materials to be used in the work and to obtain samples required for his/her acceptance of the material or assembly.

Should the Engineer conduct plant inspections, the following conditions shall exist:

a.  The Engineer shall have the cooperation and assistance of the Contractor and the producer with whom he has contracted for materials.

b.  The Engineer shall have full entry at all reasonable times to such parts of the plant that concern the manufacture or production of the materials being furnished.

c.  If required by the Engineer, the Contractor shall arrange for adequate office or working space that may be reasonably needed for conducting plant inspections. Office or working space should be conveniently located with respect to the plant.

It is understood and agreed that the Owner shall have the right to retest any material that has been tested and approved at the source of supply after it has been delivered to the site.  The Engineer shall have the right to reject only material which, when retested, does not meet the requirements of the contract, plans, or specifications.

60-05  ENGINEER'S FIELD OFFICE.  The Contractor shall furnish for the duration of the project one building for the use of the field engineers and inspectors, as a field office.  This facility shall be an approved weatherproof building meeting the current State Highway Specifications (for example, Class I Field Office or Type C Structure).  This building shall be located conveniently near to the construction and shall be separate from any building used by the Contractor.  A land line telephone and answering machine shall be provided.  The Contractor shall be responsible for payment of the basic monthly charge and local calls only.  Any Long Distance Tolls shall be the responsibility of the caller.  The Contractor shall furnish [ FAX machine, photocopy machine, water, sanitary facilities, heat, air conditioning, and electricity ].  No direct payment will be made for this building or labor, materials, ground rental, or other expense in connection therewith.  The cost hereof shall be included in the price bid for the various items of the contract.  The Contractor and his/her superintendent shall provide all reasonable facilities to enable to the Engineer to inspect the workmanship and materials entering into the work.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

Requirements for specifying the Engineer's field office should be coordinated with the Owner and the Engineer since such facilities are not needed for all airport construction projects.

* * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * *

60-06  STORAGE OF MATERIALS.  Materials shall be so stored as to assure the preservation of their quality and fitness for the work.  Stored materials, even though approved before storage, may again be inspected prior to their use in the work.  Stored materials shall be located so as to facilitate their prompt inspection.  The Contractor shall coordinate the storage of all materials with the Engineer.  Materials to be stored on airport property shall not create an obstruction to air navigation nor shall they interfere with the free and unobstructed movement of aircraft.  Unless otherwise shown on the plans, the storage of materials and the location of the Contractor's plant and parked equipment or vehicles shall be as directed by the Engineer.  Private property shall not be used for storage purposes without written permission of the owner or lessee of such property.  The Contractor shall make all arrangements and bear all expenses for the storage of materials on private property.  Upon request, the Contractor shall furnish the Engineer a copy of the property owner's permission.

All storage sites on private or airport property shall be restored to their original condition by the Contractor at his/her entire expense, except as otherwise agreed to (in writing) by the owner or lessee of the property.

60-07  UNACCEPTABLE MATERIALS.  Any material or assembly that does not conform to the requirements of the contract, plans, or specifications shall be considered unacceptable and shall be rejected.  The Contractor shall remove any rejected material or assembly from the site of the work, unless otherwise instructed by the Engineer.

Rejected material or assembly, the defects of which have been corrected by the Contractor, shall not be returned to the site of the work until such time as the Engineer has approved its used in the work.

60-08  OWNER FURNISHED MATERIALS.  The Contractor shall furnish all materials required to complete the work, except those specified herein (if any) to be furnished by the Owner.  Owner-furnished materials shall be made available to the Contractor at the location specified herein.

All costs of handling, transportation from the specified location to the site of work, storage, and installing Owner-furnished materials shall be included in the unit price bid for the contract item in which such Owner-furnished material is used.

After any Owner-furnished material has been delivered to the location specified, the Contractor shall be responsible for any demurrage, damage, loss, or other deficiencies that may occur during the Contractor's handling, storage, or use of such Owner-furnished material.  The Owner will deduct from any monies due or to become due the Contractor any cost incurred by the Owner in making good such loss due to the Contractor's handling, storage, or use of Owner-furnished materials.

END OF SECTION 60