`

### The Twentieth Meeting of the Informal South Pacific ATS Coordinating Group

(ISPACG/20)

Honolulu, USA, 30 January – 1 February 2006

Agenda Item 4:  Review progress on Open Action Items

###### HF CONGESTION

(Presented by Airways New Zealand)

- INTRODUCTION

  - HF congestion in the TASMAN and Pacific areas of AA OCA has been an issue for some time and in a customer survey undertaken in 2005 this issue was voted the number one problem facing airlines operating in this region.

2.	DISCUSSION

  - There have been various papers presented at ISPACG over the years that have attempted to address the issue of HF congestion but with the number of aircraft using HF as a primary means of communication in the south pacific ever increasing it is possible that the time for a more strategic frequency management plan is necessary.

  - Airways New Zealand is currently in discussions with operators regarding Selcal checks for flights using HF as the primary means of communication. A typical transtasman flight from New Zealand to Australia will often undertake a Selcal check on the ground during pre-flight, again when airborne entering the AA OCA and then another entering an adjacent FIR. If for example selcal checks in this example were able to be reduced from 3 to 1 then the saving in RTF time will here would be one step forward in reducing HF congestion.

  - Another solution is to develop an HF frequency management plan in the south pacific whereby Auckland, Brisbane and Nadi radio utilise different HF frequencies at various times of the day.

  - The use of regional HF frequencies, such as Nadi currently have, could possibly be utilized further thus reducing the congestion on the main HF bands.

  - While these discussions are in an early stage, solutions to this issue will ultimately be a compromise of what flight crews are required to undertake, agreement between Air Traffic Units and what can be achieved practically without affecting safety.

3.	RECOMMENDATION

  - The meeting acknowledges that HF congestion is a problem facing airlines in the south pacific.

  - An ISPACG working group is set up to address the issues above and others raised from this paper with the intention of finding a workable solution to the problem.