# Implementation Guidance

## April 2005

# Environmental Evaluation

## NE-CPA-52

# Table of contents

Page #

Introduction	1

National Application

State Application

Tiering	3

Comment Boxes	4

General Instructions	4

Spreadsheet Tips	5

Special Environmental Concerns/Guide Sheets	6

Comment Boxes text

Economic & Social Considerations	16

Economic & Social Considerations Help Sheet	18

See separate Excel spreadsheet for form:

NE-CPA-52 April 2005

See separate Excel spreadsheet for tiering references:

Nebraska NEPA Tiering References April 2005

# Environmental Evaluation

## NE-CPA-52

# Introduction

National Application

The Natural Resources Conservation Service (NRCS) planning policy defines the environmental evaluation (EE) as the part of planning that inventories and estimates the potential effects on the human environment of alternative solutions to resource problems.  A wide range of environmental data together with social and economic information is considered in determining affects on the human environment.  The EE aids in the consideration of alternatives and in the identification of available resources.  The EE for a program, regulation, or individual action is documented on a CPA-52, “Environmental Evaluation Worksheet,” or state equivalent and is used to make NEPA compliance decisions.  The EE is where NEPA and the NRCS planning process come together.

The National Planning Procedures Handbook states that the EE is “a concurrent part of the planning process in which the potential long-term and short-term impacts of an action on people, their physical surroundings, and nature are evaluated and alternative actions explored.”

# NRCS begins consideration of environmental concerns when information gathered during the EE is used to:

## 1.	Identify environmental concerns that may be affected, gather baseline data, and predict effects of alternative courses of actions.

## 2.	Provide data to applicants for use in establishing objectives commensurate with the scope and complexity of the proposed action.

## 3.	Assist in the development of alternative courses of action.  In NRCS-assisted project actions, nonstructural, water conservation, and other alternatives that are in keeping with the Water Resources Council's Economic and Environmental Principles and Guidelines for Water and Related Land Resources Implementation Studies are considered.

## 4.	Perform other related investigations and analyses as needed, including economic evaluation, engineering investigations, etc.

## 5.	Assist in the development of detailed plans for implementation, operation and maintenance.

NRCS provides conservation planning assistance on individual land units and to groups through a variety of programs.  All NRCS planning activities are concerned with the effects on the environment, as is NEPA.  The purpose of NRCS assistance is to improve the condition and function of natural resources, increase the sustainability of agriculture and, when feasible, improve the economic well-being of NRCS clients.  As a federal agency, NRCS must assure that its assistance is provided in compliance with all applicable federal, state, Tribal, and local laws, program rules, policy statements, Executive Orders, and international agreements.  Satisfying NEPA requirements, therefore, is an integral part of the NRCS planning process and should not be viewed as a separate process.

State Application

NRCS planning and NEPA compliance stems from the EE.  The EE is a preliminary scoping process, which identifies the ecological, social, and economic factors that the proposed action is likely to affect and briefly considers what those effects are likely to be.  The results of the EE are documented on form NE-CPA-52, "Environmental Evaluation for Conservation Planning."  When NRCS provides planning assistance, field offices must conduct an EE and document the results to ensure consideration of all resource concerns, including those that are specially protected.

An important result of the EE process is to determine the need for a NEPA document to be prepared.  Thus, the RFO (Responsible Federal Official), usually the district conservationist for field-level actions, must document a “finding” in section “P” of the NE-CPA-52 indicating their decision about whether NEPA documentation needs to be prepared before a proposed action is implemented, and the reasons for making that finding.  The EE process applies to all assistance provided by NRCS, including both financial and technical assistance, so the NE-CPA-52 must also be completed in all cases.

Throughout the EE, the NE-CPA-52 should be supplemented with attachments and assistance notes as needed.  The form provides the basic template to work from but often there are circumstances that require additional space for documenting things such as qualitative and quantitative data describing the current condition of the natural resources in the planning area, the resource condition after application of conservation practices, and the relationship between the resource conditions and the quality criteria.

At a minimum, document the effects of the proposed action and the no action alternative.  Consider both long-term and short-term effects.  Consider effects which may be individually minor but cumulatively significant at a larger scale or over an extended time period.  As necessary, attach additional pages to quantify effects.  At the request of the client, additional alternatives may be developed and their effects evaluated.  The differences between the no action, proposed action, and the other alternatives should become apparent.

Overall guidance on the EE and NEPA process are provided in the National Environmental Compliance Handbook (NECH) October 2003.  The NECH (link given below) defines the NRCS’s role in NEPA, and gives strong recommendations on how to implement compliance.

http://policy.nrcs.usda.gov/scripts/lpsiis.dll/H/H_190_610_Content.htm

# Environmental Evaluation

## NE-CPA-52

# Tiering

The purpose of tiering is to avoid duplication of paperwork, eliminate repetitive discussions of the same issues, and to focus on the actual issues pertinent for decision making at each level of environmental review.  Tiering is the coverage of general matters in broader documents with subsequent narrower statements or environmental analyses.

When a broad NEPA document, such as an EIS or EA (environmental impact statement or environmental assessment), has been prepared regarding an entire program, policy, watershed plan, etc., a subsequent assessment or evaluation that is site specific is then prepared (CPA-52).  The issues discussed in the broader statement may be summarized and included by reference (CPA-52 section Q.).  This process allows for incorporation by reference the discussions and effects analysis from previous NEPA documentation and then concentrates on the issues specific for the proposed action.

The CPA-52 Resource Considerations, Economic and Social Considerations, and Special Environmental Concerns sections assist in summarizing alternatives and effects, and identify special conditions that either may or may not have been sufficiently analyzed in an appropriate NEPA document.

A listing of NEPA documents that are available for tiering is maintained by the State Office.  Only those documents on that list may be used to tier to.  Documents prepared by other agencies (i.e., FSA, Bureau of Land Management) may not be used until the NRCS has officially adopted them for their specific use.  If your action does not match those that have already been analyzed in a national NRCS or NRCS Nebraska specific NEPA document on that list, or the effects are unknown, then refer to the State Office Environmental Specialist for further guidance.  An individual EA or EIS may need to be prepared.

See separate Excel spreadsheet for tiering references:

Nebraska NEPA Tiering References April 2005

# Environmental Evaluation

## NE-CPA-52

# Comment Boxes

Blocks with associated comments are indicated by a small red triangle in the upper right corner.

Aim the mouse pointer at the text area and the comment box will pop-up.  When the pointer is moved off the text box area the comment box will disappear.  If you wish to have the comment box stay active, then right click with the mouse and select “Show Comment” and then to hide the comment box, right click with the mouse and select “Hide Comment.”

Comment boxes have specific information that will assist you in completing the form.  Some of the information is repetitive of portions of this “Implementation Guidance,” but be sure to become familiar with both to fully understand the EE and NEPA processes and properly complete the documentation.

# General Instructions

## General form instructions are included as a worksheet tab “instructions” in the NE-CPA-52.  These are standard form instructions and help to clarify some basic principals of the form.  This tab also contains information regarding “Criteria for Identifying Extraordinary Circumstances”.  Here is where you will find guidance so that when you prepare to make the NEPA finding (P. Findings), you can review the action to see if there is something that would “red flag’ your activity as being of additional concern and possibly needing further review.  This is very important when saying something is “categorically excluded” since that determination is dependent of there NOT being any extraordinary circumstances.  Extraordinary circumstances could also move your activity from the “sufficiently analyzed” category to “unknown” if you aren’t sure if those specific extraordinary circumstances were reviewed in the NEPA document you plan on citing for tiering application.  Contact the state office Environmental Specialist for assistance in these areas.

# Environmental Evaluation

## NE-CPA-52

# Spreadsheet Tips

Economic and Social Considerations pop-up help screen:

This pop-up screen assists in completing the form by containing suggestions for the economic and social effect of each practice.  After making the selection from pick list be sure to press “enter” to activate that selection.   This Help screen is only available when it is activated.  Use the “print Scrn” option to copy and paste the view to a word document if you desire a hard copy to view when completing the form or working with a client.

Comment boxes (small red triangle in upper right of cell):

Contain information pertinent to filling in form.  Some of the boxes are quite large and may need to be locked open to be able to scroll screen:

Right click on box

Pick “Show Comment” to lock box open

When done right click box and pick “Hide Comment”

Drop-down lists:

Some boxes have a drop down list with possible choices to select from.  If other answers are desired, then the box can be filled out manually or the information should be put in the Other/notes sections of the form.  Effects boxes that are available to fill electronically are: Resource Considerations, Economic and Social Considerations, and Special Environmental Concerns.  Some examples of various choices are:

Resource Considerations/

Economic & Social Considerations

significant decrease

moderate decrease

slight decrease

No Effect

To Be Determined

Not Applicable

See Attached Documentation

See Other/notes below

slight increase

moderate increase

significant increase

good

average

poor

minor

major

Special Environmental Concerns

No Effect-see documentation

No Effect

Consultation needed

To Be Determined

See Attached Documentation

May Affect

NLAA concur

# Environmental Evaluation

## NE-CPA-52

# Special Environmental Concerns/Guide Sheets

Special environmental concerns (NE-CPA-52 section J) are specific requirements for the protection of the environment that must be taken into account during the planning process.  Some special environmental concerns are based on laws and their implementing regulations, others are based on Executive Orders or NRCS policy, while still others are based on local rules or ordinances.  Some special environmental concerns require that we follow different procedures than others, and some require that the responsible federal official (RFO) consult or coordinate with another Federal agency under certain conditions or that a permit or other action may be required.  For each of the concerns listed on the NE-CPA-52 there is an Evaluation Procedure Guide Sheet to assist you in following the proper procedures.  These Guide Sheets provide a step by step process to help clarify whether or not there are concerns that need to be addressed in your planning process and alternative development.

# Not all special environmental concerns apply in all areas.  For example, if you are in Box Butte County, you do not have to consider Wild and Scenic Rivers when you develop a conservation plan; however, it is important to ensure that the special environmental concerns that do apply are addressed during the planning process.  It should be noted that the Guide Sheets for Cultural Resources and Endangered and Threatened Species are required attachments for all NE-CPA-52s (as well as the Resource Considerations Field Inventory Guide Sheet).  The other Guide Sheets should be attached as needed to help clarify the decision making process and compliance with that specific concern.

The person/planner who completes the NE-CPA-52 is the person who is providing the technical conservation assistance.  The individual responsible for completing the NE-CPA-52 must sign, indicate their title, and date the first signature block “N” on the form to indicate that the information recorded on the NE-CPA-52 is the best available information. This signature is particularly important when a third party technical service provider (TSP) is completing the NE-CPA-52 or when NRCS is providing technical assistance on behalf of another agency.  In such cases, the individual carrying out the EE process and documenting the results on the NE-CPA-52 is not the responsible federal official (RFO) and does not have authority to make the NEPA “P. Findings” or conduct consultations on behalf of the responsible agency.  In this situation, the RFO is required to carry out these responsibilities and then complete the second signature block.  It is critical that the responsible agency be able to rely on the information provided in the NE-CPA-52 so it can appropriately carry out its environmental compliance responsibilities.

For example, if NRCS is providing technical assistance for CRP and NRCS determines an endangered species may be affected by the conservation practices to be implemented, then NRCS must document this effect on the NE-CPA-52, and indicate that the Farm Service Agency (FSA), as the RFO, should consult with the U.S. Fish and Wildlife Service (FWS).  NRCS should not conduct the consultation on FSA’s behalf.  Likewise, if a Technical Service Provider (TSP) is developing a conservation plan for a client who hopes to receive Environmental Quality Incentive Program (EQIP) funds from NRCS, the TSP must indicate on the NE-CPA-52 whether any listed or proposed species or designated critical habitat may be affected if the plan is implemented and document the types of effects that are expected.  The TSP may not, however, consult with USFWS on NRCS’s behalf.

Don’t forget that if you’re only providing technical assistance and you don’t work directly for the agency that’s providing the financial assistance, you just need to check for the presence of the affected resources and evaluate the anticipated effects on those resources, thus making a recommendation about whether the funding agency needs to consult.  You are not to do the actual consultation yourself.

If you do need a consultation, contact the applicable State Office contact, as indicated on the Guide Sheet, to assist with that coordination.

If there are any questions pertaining to addressing these concerns, please contact the state office Environmental Specialist.

Refer to the Field Office Technical Guide for specific information such as detailed area maps for endangered species, wild and scenic rivers, etc.  The technical guide will continue to be updated with information to clarify and help address the concerns.

Below is the text for the comment boxes that are on the NE-CPA-52 for each of the Special Environmental Concerns.

Cultural Resources: These resources are artifacts, buildings, other structures, objects and places, of historical, cultural or scientific importance to our society. They occur on public, private and Indian land; most are not known in any formal inventory, nor to anyone. It is NRCS policy to protect significant resources in place to the maximum practical extent, and to mitigate unavoidable adverse effects. Mere presence of cultural resources does not make them significant. Formal evaluation using National Register of Historic Places criteria may show them to be significant and eligible, and others may already be listed. This process does not diminish any private property rights. It does affect what and how NRCS actions may be implemented.

FO employees and the DC at all levels of operations are the most critical component to successfully fulfilling NRCS cultural resource responsibilities. NRCS employees locate and assist in identifying the presence of cultural resources, evaluated or not, that may be affected by, because of NRCS approval, or technical or financial assistance.

The most effective cultural resource reviews are those initiated at the field office level during planning by employees who have completed Modules 1 through 8 of the basic cultural resource training. Inspections gather basic information and appropriately consider whether indicators are present. FO employees will contact their FOCRC or the State CRS if further assistance is needed. The FO documents resource decisions in case files and CPA 52.

Endangered & Threatened Species: Consult Section II of the NETG for implementation guidance that will assist you in the threatened and endangered species review process.  If you are still uncertain about the status of endangered or threatened species or their habitats in the planning area and/or impact zone, consult with a

Nebraska NRCS biologist or environmental specialist.  Refer to GM 190 Part 410.22 for NRCS's policy concerning endangered and threatened species

Environmental Justice: Executive Order 12898, Feb 11 1994

Environmental Justice means that, to the greatest extent practicable and permitted by law, all populations are provided the opportunity to comment before decisions are rendered on proposed federal actions. Furthermore, the principles of environmental justice require that populations are allowed to share in the benefits of, are not excluded from, and are not affected in a disproportionately high and adverse manner by, government programs and activities affecting human health or the environment.

Executive Order 12898 issued February 11, 1994 requires each Federal Agency to make Environmental Justice a part of its mission.  Agencies are to identify and address disproportionately high and adverse human health or environmental effects of its programs, policies, and activities on minority populations, low-income populations, and Indian Tribes. Environmental Justice must be applied throughout the United States, its territories and possessions, the District of Columbia, the Commonwealths of Puerto Rico and the Mariana Islands.  Environmental Justice issues encompass a broad range of impacts covered by NEPA, including impacts on the natural or physical environment and related social, cultural, and economic impacts.  The primary means to attain compliance with environmental justice considerations is through the inclusion of low-income, minority, and tribal populations in the planning process and by translating documents into other languages when members of the affected area are not English-speaking.

Fish and Wildlife Coordination Act: If a consultation is needed with the U.S. Fish and Wildlife Service (USFWS) then NRCS shall give full consideration to the recommendations and those recommendations shall be made an integral part of any plan submitted for authorization or approval by any agency or person.

Fish and Wildlife Coordination Act, March 10, 1943 as amended

The Fish and Wildlife Coordination Act (FWCA), as amended, proposes to assure that fish and wildlife resources receive equal consideration with other values during the planning of water resources development projects and programs. The Act was passed because the goals of water-related actions (e.g., flood control, irrigation, hydroelectric power) may conflict with the goal of conserving fish and wildlife resources.

The FWCA requires NRCS to consult with the U S Fish and Wildlife Service (FWS) whenever the waters of any stream or other body of water are proposed or authorized to be impounded, diverted, the channel deepened, or the stream or other body of water otherwise controlled or modified for any purpose whatever. The Act also requires consultation with the head of the state agency that administers wildlife resources in the affected state. The purpose of this process is to promote conservation of wildlife resources by preventing loss of and damage to such resources and to provide for the development and improvement of wildlife resources in connection with the action.

Although the recommendations of the FWS and state officials are not binding, NRCS must give them full consideration. Any recommendations made by those officials shall become an integral part of any plan prepared by NRCS that is subject to authorization or approval by any agency or person. The plan must also include an estimate of the wildlife benefits or losses to be derived from the proposed project and a description of the conservation measures NRCS finds should be adopted to obtain maximum overall project benefits.

Floodplain Management: Executive Order 11988, May 24 1977

Floodplains are defined as lowlands or relatively flat areas adjoining inland or coastal waters, including at a minimum areas subject to a one percent or greater chance of flooding in any given year.

The "base" floodplain is set equal to the "100-year" floodplain, the so-called "one percent chance floodplain".  The "critical action" floodplain is defined as the 500-year floodplain (the 0.2 percent chance floodplain) where there is the presence of a facility, such as a school, hospital, nursing home, utility or a facility producing volatile, toxic or water-reactive materials.  Floodplains may be shown on maps produced by the Federal Emergency Management Agency (FEMA) and on the Natural Resources Conservation Service (NRCS) Watershed Plans and Floodplain Management Studies.

NRCS policy on floodplains is found in the General Manual (GM 190 Part 410.25) and reflects Executive Order 11988, which was signed by President Jimmy Carter on May 24, 1977.  The E.O. requires that decisions by Federal agencies must recognize that floodplains have unique and significant public values.  Federal agencies are instructed to consider the natural and beneficial values of floodplains and the public benefits to be derived from floodplain restoration or preservation.

The objectives of E.O. 11988 are to avoid, to the extent possible, the long and short-term adverse impacts associated with occupancy and modification of floodplains and to avoid direct and indirect support of floodplain development where there is a practical alternative.

Through proper planning, floodplains can be managed to reduce the threat to human life, health and property in ways that are environmentally sensitive.  Most floodplains contain areas with valuable assets that sustain and enhance human existence.  Some of these assets are agricultural and forest food and fiber, fish and wildlife, temporary floodwater storage, parks and recreation, and environmental values.

The Natural Resources Conservation Service provides leadership, and takes actions, where practicable, to conserve, preserve and restore existing natural and beneficial functions and values in base (100 year) floodplains as part of the technical and financial assistance program that it administers.

Invasive Species: Executive Order 13112, 1999

An invasive species is an alien species whose presence does or is likely to cause economic or environmental harm or harm to human health. Alien species means species not native to a particular ecosystem. Invasive species may include all terrestrial and aquatic life forms including plants, animals, and fungi.

Executive order 13112, 1999- Invasive Species- directs Federal agencies to prevent the introduction of invasive species and provide for their control and to minimize the economic, ecological, and human health impacts that invasive species cause.

NRCS shall not authorize, fund, or carry out actions that it believes are likely to cause or promote the introduction or spread of invasive species in the United States or elsewhere.

All NRCS actions and activities shall be planned and implemented with the cooperation of stakeholders.  Stakeholders include, but are not limited to, State, tribal, and local government agencies, academic institutions, the scientific community, nongovernmental entities including environmental, agricultural, and conservation organizations, trade groups, commercial interests, and private landowners.

Migratory Birds: Migratory Bird Treaty Act, 1918 as amended and Executive Order 13186

Migratory birds included are all native wild birds found in the United States except the house sparrow, starling, feral pigeon, and resident game birds such as pheasant, grouse, quail, and wild turkeys. Resident game birds are managed separately by each State. A reference list of migratory game birds is found in Title 50, Code of Federal Regulations, Part 10. The Bald Eagle Protection Act provides further protection to all Bald and Golden eagles. The Endangered Species Act further protects endangered species like the Peregrine falcon, the Northern spotted owl, and the Bald Eagle.

The Migratory Bird Treaty Act makes it unlawful for anyone to kill, capture, collect, possess, buy, sell, trade, ship, import, or export any migratory bird, including feathers, parts, nests, or eggs.

The Bald Eagle Protection Act prohibits all commercial activities and some non-commercial activities involving Bald or Golden eagles, including their feathers or parts.

The Endangered Species Act makes it illegal to sell, harm, harass, possess or remove protected animals from the wild.

Executive Order 13186 “Responsibilities of Federal Agencies to Protect Migratory Birds” requires NRCS to consider the impacts of planned actions on migratory bird populations and habitats for all planning activities.  Reasonable measures may be designed to avoid impacts, or where avoidance is not practicable, minimize impact, rectify the impact, reduce or eliminate the impact over time, or compensate for impacts.

Alternatives should be designed and implemented in a manor that avoids or minimizes, to the extent practicable, adverse impacts on migratory bird resources.

Natural Areas: Natural areas are defined as land and water units where natural conditions are maintained.  Natural conditions result when ordinary physical and biological processes operate with a minimum of human intervention.  Manipulations of natural areas may be needed to maintain or restore features where degradation or change of those natural features has occurred (GM 190 Part 410.23).

Natural areas may be designated areas of the Federal Government, Nonfederal government, or privately controlled land.  Designation may be formal, as provided under Federal regulations, or by foundations or conservation organizations specifically created to acquire and maintain natural areas.  Designation may be informal in the case of private landowners that specify an area as a natural area and manage it accordingly.

It is the policy of the NRCS to support the designation of appropriate natural areas and to recognize dedicated natural areas as a land use.

Natural Resources Conservation Service (NRCS) employees who provide technical assistance to land users must inform them about the impact their decisions may have on adjacent or nearby natural areas. Land users will be encouraged to consult with concerned agencies, societies, and individuals to arrive at mutually satisfactory land use and treatment.

Prime and Unique Farmlands: 7 CFR 658.5

Prime farmland is land that has the best combination of physical and chemical characteristics for producing food, feed, fiber, forage, oilseed, and other agricultural crops with minimum inputs of fuel, fertilizer, pesticides, and labor, and without intolerable soil erosion, as determined by the Secretary of Agriculture. Prime farmland includes land that possesses the above characteristics but is being used currently to produce live stock and timber. It does not include land already in or committed to urban development or water storage.

Unique farmland is land other than prime farmland that is used for production of specific high-value food and fiber crops, as determined by the Secretary. It has the special combination of soil quality, location, growing season, and moisture supply needed to economically produce sustained high quality or high yields of specific crops when treated and managed according to acceptable farming methods. Examples of such crops include citrus, tree nuts, olives, cranberries, fruits, and vegetables.

Farmland, other than prime or unique farmland, that is of statewide or local importance for the production of food feed, fiber, forage, or oilseed crops, as determined by the appropriate State or unit of local government agency or agencies, and that the Secretary of Agriculture determines should be considered the same as prime or unique farmland for the purposes of this evaluation.

The NRCS should take steps to assure that its actions do Not cause United States farmland to be irreversibly converted to Nonagricultural uses in cases in which other national interest do Not override the importance of the protection of farmland Nor otherwise outweigh the benefits of maintaining farmland resources.

The purpose of this regulation is to minimize the extent to which Federal programs contribute to the unnecessary and irreversible conversion of farmland to Nonagricultural uses and to assure that Federal programs are administered in a manner that, to the extent practicable, will be compatible with State, unit of local government, and private programs and policies to protect farmland.

NRCS shall use the criteria provided in regulations found at 7 CFR 658.5 to identify and take into account the adverse effects of Federal programs on the protection of farmland. NRCS is to consider alternative actions, as appropriate, that could lessen such adverse effects, and assure that such Federal programs, to the extent practicable, are compatible with State, unit of local government and private programs and policies to protect farmland.

Riparian Area: NRCS policy (190 GM, part 411.03(d)

Riparian areas are ecosystems that occur along watercourses or water bodies.  They are distinctively different from the surrounding lands because of unique soil and vegetative characteristics that are strongly influenced by free or unbound water in the soil.  Riparian ecosystems occupy the transitional area between the terrestrial and aquatic ecosystems.  Typical examples would include floodplains, streambanks, and lakeshores. Riparian areas may exist within all landuses, such as cropland, hayland, pastureland, rangeland, and forestland.

Although riparian areas constitute only a fraction of the total land area, they are generally more productive in terms of plant and animal species, diversity and biomass.  Riparian areas are vital components of the ecosystems in which they occur and are extremely important for flood control and hydrologic function (water quantity, quality, and timing).  It is important to recognize that Not all riparian areas have the same potential or react to management in the same way, therefore, they should be managed according to their unique characteristics.

An understanding of watershed scale processes is necessary to fully understand how riparian areas function.  The attributes of a watershed system such as soils, geology, landuse, and topography directly influence riparian area structure, function, and values.

Conservation planning in riparian areas requires special considerations.  A resource problem within the riparian zone may be the manifestation of upland management decisions.  Planners working with riparian areas should consider soils, the present plant community, the site potential, geomorphology of both the stream and the watershed, the stage of stream evolution, fish and wildlife needs, the management of the upland areas of the watershed and the producer’s objectives.

Federal law does not specifically regulate riparian areas.  However, portions of riparian areas, such as wetlands and other waters of the U.S., may be subject to federal regulation under provisions of The Food Security Act, The Clean Water Act, The National Environmental Policy Act and state and local legislation.

NRCS policy (190 GM, part 411.03(d)) for riparian areas requires:

-riparian area management to be integrated into plans and alternatives

-plans to maintain or improve water quality and quantity benefits

-development of alternatives when land user’s objectives are in conflict with conservation of the riparian area resources.

Scenic Beauty: Scenic beauty can be defined as the viewer's positive perceived value of the special, unique and memorable physical elements of a landscape. A beautiful landscape scene has definable visual elements that combine to provide a high-quality visual resource. A landscape with a high visual quality generates emotional impacts within the viewer's mind and links to sense of place and quality of life. Retaining people's connection to a beautiful natural environment affects their well-being. Through proper planning, the visual characteristics of a scenic landscape can be protected, maintained and improved.

Management of the visual landscape is the process of manipulating the physical elements and functions of the landscape to achieve specific resource objectives. The landscape has a consistently definable appearance that can be described by the measurable visual elements of landform, water, vegetation, structures and sky. Four of the visual elements (landform, water, vegetation, and structures) provide a ready basis for describing the changing countryside landscape as altered by human decisions.

Landform - The shape of the land (topography, slope, and aspect) seems to be the most noticeable element, particularly as it relates to the horizon. For example, the horizontal nature of crop landscapes makes them especially sensitive to the presence of vertical elements, such as streamside vegetation, shelterbelt trees, farmstead structures and utility poles. When agricultural activities, such as tree rows and fences are aligned with the topography, they tend to emphasize and enhance the landform. In flat or rolling areas the horizontal line is the most conspicuous landscape element because it is so uniformly horizontal.

Water – Water can add to aesthetic quality, modify temperatures, serve as a buffer between use areas, and direct attention from undesirable views. Its characteristics are gurgling, rushing, spurting, falling, calm or placid, It’s shape, whether water course or waterbody, also adds value to the landscape.

Vegetation - Vegetation within the landscape includes agricultural crops, which can vary widely in size, form, color, texture, and planting pattern. Shelterbelt and drainage way trees are visually significant in landscapes where low crops or pastures are present. When that pattern is repeated year after year, often the trees provide the only spatial differentiation in an otherwise horizontal landscape. Row crops create visually strong lines to the viewer on the ground or from the air, so any curved (nonlinear) pattern that is located among the straight lines will be prominent.

Structures - From a human emotional standpoint, structures evoke the most obvious and describable of our mental images of "countryside."  Farmhouses, barns, silos, wooden fences, stone walls, windmills and two-lane roads are some of the agriculturally related structures that fulfill our romantic notion of countryside. Today's countryside is more likely to be populated with highways, transmission lines, steel and. concrete bridges, warehouses, subdivisions, theme parks, and airports, few of which evoke any images directly related to agriculture. New technologies, such as metal farm buildings and silos and prefabricated houses, are part of today's countryside landscape. When all of the above elements are combined, they form patterns or images that collectively we label as the "landscape."  While the identified "landscape" will vary from region to region, the recognition that a particular landscape pattern is characteristic of a certain part of the country is obvious to everyone who lives there or who passes through the region.

Contributions to the scenic beauty of the landscape are part of providing planning assistance to landowners and land users. Emphasis should be given to natural resource conservation practices that contribute to the attractiveness of the landscape while increasing agricultural efficiency and productivity.

Wetlands – NRCS: Food Security Act of 1985, GM 190 Part 410.26, Executive Order 11990, “Protection of Wetlands”, and with Revised NRCS Wetland Technical Assistance Policy at 7 CFR Part 650, dated November 17, 1997.

It is the policy of the NRCS to protect and promote wetland functions and values in all NRCS planning and application assistance. NRCS recognizes the beneficial and varied functional attributes of the different wetland types, and as such, strives to reconcile the need for wetland protection with that of promoting viable agricultural enterprises.  NRCS supports the restoration, enhancement, creation, and preservation of wetlands as important and realistic components of comprehensive conservation plans, not only on a farm-by-farm basis, but also on a watershed or landscape basis.  When providing technical assistance, NRCS will conduct an environmental evaluation, considering the objectives of the client in the context of environmental, economic, and other pertinent factors.  NRCS activities must comply with Executive Order 11990, “Protection of Wetlands”, and with Revised NRCS Wetland Technical Assistance Policy at 7 CFR Part 650, dated November 17, 1997.

If wetlands will be impacted by a proposed activity, the NRCS will identify whether practicable alternatives exist that either enhance wetland functions and values, or avoid or minimize harm to wetlands.  If such alternatives exist, the client will be given the opportunity to select one of those alternatives.  If the client selects the practicable alternative, the NRCS may continue technical assistance for the conversion activity as well as the development of the mitigation plan.  However, if the practicable alternative is not selected, the NRCS may assist with the development of an acceptable mitigation plan, but no further financial or technical assistance for the wetland conversion activity may be provided.

In addition to NRCS requirements, activities that impact wetlands and “other waters of the U.S.” often require a Section 404 permit from the Corps of Engineers prior to beginning work.  Early coordination with the appropriate Corps Regulatory Office to determine possible permit requirements is highly recommended for the client.  (Refer to the Wetlands - Other Guide Sheet).  Many states also have laws restricting activities in wetlands. Prior to or concurrent with NRCS assistance, the client should obtain all necessary permits or approvals related to work in wetlands.

Wetlands – Other: Clean Water Act, GM 190 Part 410.27 & 28

The client is responsible for obtaining permits and complying with the CWA.  Early coordination with the Corps and state regulatory personnel is encouraged, and in many cases documentation of authorization from the Corps, state, or tribe is required before beginning work on a project.  Refer to the Evaluation Procedure Guide Sheet for a link to more detailed information describing "Waters of the U.S. and Clean Water Act".

Title 117 Nebraska's Surface Water Quality Standards

Although a Department of the Army permit pursuant to Section 404 of the Clean

Water Act and/or Section 10 of the River and Harbor Act is not required for

this project, this does not eliminate the requirement that you obtain other

applicable Federal, State, Tribal and/or Local permits as required.  One such

requirement is complying with Title 117 of Nebraska's Surface Water Quality

Standards.  The Nebraska Department of Environmental Quality (NDEQ)

administers this regulation.  These standards apply to all "Waters of the

State", including isolated and adjacent wetlands, creeks, lakes, rivers, etc.

Wild and Scenic Rivers: Public Law 90-542

A Wild and Scenic River is a free-flowing river or river-segment that has outstanding scenic, recreational, geologic, fish-and-wildlife, historic, cultural, or other similar values.  National wild and scenic rivers are  designated by act of Congress (PL 90-542) or by the Secretary of the Interior at the request of a governor as part of the National Wild and Scenic Rivers System.

The designation of a river under the Wild and Scenic Rivers Act provides legal protections from adverse development and provides a mechanism for management of the river's resources.  The principal effect of the Act is to preclude or to severely limit the construction of dams and other water resources projects that might affect the free-flowing character of the river or adversely affect the values for which a river was designated.

The designation affects the management of federal lands in the river's corridor.  Rights to future development of private lands can be purchased under land acquisition authorities.  Boundaries of Wild and Scenic Rivers are limited to no more than 320 acres per river mile and purchase of fee title within this boundary is limited to no more than 100 acres per mile.

Management standards or requirements have been developed for three classes of rivers: (1) Wild , (2) Scenic , and (3) Recreational .  These labels refer to the degree of development along a river not necessarily to the type of river or how scenic or heavily used it is.  The definitions of wild, scenic and recreational from the law are:

 "Wild" River area: Those rivers or sections of rivers that are free of impoundment’s and generally inaccessible except by trail, with watersheds or shorelines essentially primitive and waters unpolluted.  These represent vestiges of primitive America.

 "Scenic" River areas: Those rivers or sections of rivers that are free of impoundment’s, with shorelines or watersheds still largely primitive and shorelines largely undeveloped, but accessible in places by roads.

 "Recreational" River areas: Those rivers or sections of rivers that are readily accessible by road or railroad, that may have some development along their shorelines, and that may have undergone some impoundment or diversion in the past.

Ongoing regular uses of private lands, particularly those existing at the time of the river's designation, are not directly affected.  Most private land uses, such as homes and farms are compatible with Wild, Scenic and Recreational River management.  The river's management plan identifies the types of land uses and developments that are considered compatible or incompatible with the river's wild and scenic values.

Designation has no effect on existing water rights or irrigation systems or other existing developed facilities.  New projects and alterations to existing systems, which require Federal permits, may be allowed when they will not have an adverse effect on the values for which the river was designated.

Generally, timber harvests and agricultural operations on privately owned lands are unaffected in Wild, Scenic and Recreational River designations.  However, some activities may require permits or may be covered under special provisions of the management plan.

Every river in the National System is required to have a manager responsible for assuring protection.  The federal river manager can assist and cooperate with states or other local organizations, landowners, and individuals to plan, protect, and manage river resources.  The assistance can include limited financial assistance.  Management of natural and cultural values is emphasized rather than public purchasing and owning of land.  A great deal of cooperation may be required as management may include local zoning, restrictions on land use, donations of development rights to land trusts, and other methods.

# Environmental Evaluation

## NE-CPA-52

# Economic & Social Considerations

NRCS policy states that economics is an essential consideration in all agency decision making.  Economic principles must be applied in the planning, implementation, and evaluation of agency policies and program activities to provide the most cost-effective assistance to customers, cooperators, and partners for the sustained use of natural resources.

Economic principles and techniques, including cost effectiveness, economic feasibility, and benefit-cost analysis will be applied to all program formulation, management, and evaluation activities of the agency.

Economic effects of alternative actions should be provided to NRCS customers in order for them to make informed resource conservation decisions.  NRCS policy permits cost effectiveness analysis, partial budgeting, profitability analysis, and other appropriate analyses when requested by the client.  NRCS policy prohibits field offices from obtaining financial information beyond that volunteered by the client.

For nationwide consistency in the application of economics in all NRCS activities, the National Resource Economics Handbooks, Part 610 Conservation Planning and other directives will be used as guidance.

Economic principles and techniques shall be used at all levels of the agency in order to satisfy the goal of maximizing benefits per dollar expended as legislated for selected U.S. Department of Agriculture conservation programs.  Contact the State Office Economist for additional information or assistance.

When reviewing the economic impacts of a conservation practice there are seven major areas to consider; land use, capital, labor, management level, profitability, risk, and social issues.

Land use, consider the following:

- Is the present land use suitable for the proposed practice?

- Will land use change after practice installation?

- How will a change effect the operation?  (Ex. Feed and Forage Balance Sheet)

- Does client understand the inputs needed to implement the practice and the client's responsibility in obtaining these inputs?

- Will the action affect community institutions, traditions or values, or the way of life for individuals in the community?

- Will the action affect resources on which people depend for subsistence, employment or recreation?

Capital, consider the following:

- What are the impacts of the cost of the initial investment for this conservation practice?

- What are the impacts of any additional annual costs for Operation and Maintenance on this conservation practice?

- What possible impact does implementing this conservation practice have on the client’s future eligibility for farm programs?

- Does the producer have the funds or ability to obtain the funds needed to implement the proposed conservation practice?

Labor, consider the following:

- Does the client understand the amount and kind of labor needed to implement, operate and maintain the proposed practice?

- Does the client have the skills and time to carry out the conservation practice as it is planned or will they have to hire someone?

Management level, consider the following:

- Does the client understand the inputs needed to manage the practice and the client's responsibility in obtaining these inputs?

- Does the client understand their responsibility to maintain the practice as planned and implemented?

Profitability of a conservation practice, consider the following:

- Profitability describes the relative benefits and costs of the farm or ranch operation, and is often measured in dollars.  An activity is profitable if the benefits are greater than the costs.

- Is the proposed practice needed and feasible?

- Do the benefits of improving the current operation outweigh the installation and maintenance costs (positive benefit/cost ratio)?

- Is there a reasonable expectation of long-term profitability/benefits for the operation if the practice is implemented?

Risk, consider the following:

- Risk is the exposure to monetary loss, physical injury, or damage to resources or the environment.

- Will the proposed practice aid/risk client participation in USDA programs?

- What are the possible impacts due to a change in yield?

- Is there flexibility in modifying the conservation plan at a future date?

- What issues are involved with the timing of installation and maintenance?

- What are the cash flow requirements of this conservation practice?

- Will the implementation of the proposed practice have an adverse impact on the community at large (what are the off-site effects)?

- What, if any, are the hazards involved?

Social issues, consider the following:

- Social evaluation is a valuable planning tool because it identifies areas of potential conflict and options for decision making that might not otherwise be apparent.

- What are the values of the client?

- What is the social climate of the community in which you are working?

# Economic & Social Considerations Help Sheet

To activate the table be sure to press “enter” after the practice has been selected.

Prescribed Grazing example

# Text boxes

In comment boxes there are lots of tips and specific guidance that assist you in understanding and completing the NE-CPA-52 and associated documentation.  If you choose to use the form in “hard copy” form, BE SURE to go through the electronic form and utilize it as a help/teaching tool to be sure you get started the right direction.

To document this planning process and environmental compliance the following are REQUIRED documentation:

  - NE-CPA-52 form

  - Attachments/Guide Sheets (3)

-Resource Considerations Field Evaluation

-Cultural Resources

-Endangered and Threatened Species