Geostationary Operational Environmental Satellite (GOES)

R Series

Flight Project

Spacecraft

Work Breakdown Structure (WBS)

Dictionary

October 30, 2007

Goddard Space Flight Center

Greenbelt, Maryland

GOES-R Spacecraft

Work Breakdown Structure (WBS)

Dictionary

Prepared by:

_______________________________________	____________

Paul W Richards 	Date

NASA/GSFC 417

GOES-R Observatory Manager

Contracting Officer Technical Representative

Review by:

_______________________________________	____________

Bob Melis	Date

NASA/GSFC 417

GOES-R Deputy Project Manager-Resources

Review by:

_______________________________________		____________

Tim Walsh		Date

NASA/GSFC 417

GOES-R Deputy Project Manager

Approved by:

_______________________________________		____________

Michael L. Donnelly 	Date

NASA/GSFC 417

GOES-R Project Manager

1.0	Spacecraft #1	1

1.1	Program Management	1

1.1.1	Program Management Office	1

1.1.1.1	Travel	1

1.1.2	Resource Management	1

1.1.2.1	Configuration Management	1

1.1.2.2	Information Technology Management	1

1.1.3	Risk Management	1

1.1.4	Government Resident Office	2

1.1.5	Customer Communication	2

1.1.6	Design Reviews	2

1.1.7	Miscellaneous Reviews	2

1.1.8	Review Support	2

1.2	Systems Engineering (SE)	3

1.2.1	Systems Engineering Management	3

1.2.2	Systems Engineering Support	3

1.2.3	System Designs, Analyses and Trades	3

1.2.4	Requirements and Specification Generation	3

1.2.5	Performance Verification Plans and Procedures	3

1.2.6	Interface Definition and Control	3

1.2.6.1	Instrument Interfaces	3

1.2.6.2	Ground Interfaces	4

1.2.6.3	Launch Vehicle Interfaces	4

1.2.7	Contamination	4

1.3	Safety and Mission Assurance (S&MA)	4

1.3.1	S&MA Management	4

1.3.2	Safety	4

1.3.3	Parts Control	4

1.3.4	Materials and Processes Control	4

1.3.5	Reliability	4

1.3.6	Quality Assurance	4

1.3.7	Software Assurance	4

1.3.7.1	Software Safety	5

1.3.7.2	Software Validation and Verification	5

1.3.7.3	Independent Validation and Verification	5

1.3.7.4	Software Problem Reporting and Corrective Action	5

1.4	Spacecraft	5

1.4.1	Spacecraft Management	5

1.4.2	Mechanical	5

1.4.3	Thermal	5

1.4.4	Guidance, Navigation and Control (GN&C)	5

1.4.5	Command and Data Handling (C&DH)	6

1.4.5.1	C&DH Harnesses	6

1.4.6	Communications (COMM)	6

1.4.6.1	Space/Ground Communication	6

1.4.6.2	Auxiliary Communication Services	6

1.4.6.3	COMM Harnesses	6

1.4.7	Power	6

1.4.7.1	Battery	6

1.4.7.2	Solar Array	6

1.4.7.3	Power Regulation and Conditioning	7

1.4.7.4	Power Harnesses	7

1.4.8	Propulsion	7

1.4.9	Flight Software	7

1.4.10	Magnetometer	7

1.5	Ground Support Equipment (GSE)	7

1.5.1	Mechanical GSE (MGSE)	7

1.5.2	Electrical GSE (EGSE)	7

1.5.3	GSE Software	7

1.5.4	Simulators	7

1.6	Integration and Test (I&T)	8

1.6.1	Spacecraft I&T	8

1.6.2	Satellite I&T	8

1.6.2.1	Special Testing	8

1.6.2.2	End-to-End (ETE) Testing	8

1.6.3	Transportation and Handling	8

1.6.4	Storage	8

1.7	Launch and Operations	8

1.7.1	Satellite/Launch Vehicle I&T	8

1.7.2	Flight Operations	8

1.7.3	Operations Training	8

1.7.4	Simulator Training	8

1.8	Post Acceptance Support	9

1.9	Special Studies & Tasks	9

1.10	Education & Public Outreach	9

2.0	Spacecraft #2	9

2.1	Program Management	9

2.1.1	Program Management Office	9

2.1.2	Resource Management	9

2.1.2.1	Configuration and Information Management	9

2.1.2.2	Information Technology Management	10

2.1.3	Risk Management	10

2.1.4	Government Resident Office	10

2.1.5	Program Communication	10

2.1.6	Design Reviews	10

2.1.7	Miscellaneous Reviews	10

2.1.8	Review Support	11

2.2	Systems Engineering (SE)	11

2.2.1	Systems Engineering Management	11

2.2.2	Systems Engineering Support	11

2.2.3	System Designs, Analysis and Trades	11

2.2.4	Requirements and Specification Generation	11

2.2.5	Performance Verification Plans and Procedures	11

2.2.6	Interface Definition and Control	12

2.2.6.1	Instrument Interfaces	12

2.2.6.2	Ground Interfaces	12

2.2.6.3	Launch Vehicle Interfaces	12

2.2.7	Image Navigation and Registration (INR)	12

2.2.8	Contamination	12

2.3	Safety & Mission Assurance (S&MA)	12

2.3.1	Safety	12

2.3.2	Parts Control	12

2.3.3	Materials and Processes Control	12

2.3.4	Reliability	12

2.3.5	Quality Assurance	13

2.3.6	Software Assurance	13

2.3.6.1	Software Safety	13

2.3.6.2	Software Validation and Verification	13

2.3.6.3	Independent Validation and Verification	13

2.3.6.4	Software Problem Reporting and Corrective Action	13

2.4	Spacecraft	13

2.4.1	Spacecraft Management	13

2.4.2	Mechanical	13

2.4.3	Thermal	14

2.4.4	Guidance, Navigation and Control (GN&C)	14

2.4.5	Command and Data Handling (C&DH)	14

2.4.5.1	C&DH Harnesses	14

2.4.6	Communications (COMM)	14

2.4.6.1	Space/Ground Communication	14

2.4.6.2	Auxiliary Communication Services	14

2.4.6.3	COMM Harnesses	14

2.4.7	Power	15

2.4.7.1	Battery	15

2.4.7.2	Solar Array	15

2.4.7.3	Power Regulation and Conditioning	15

2.4.7.4	Power Harnesses	15

2.4.8	Propulsion	15

2.4.9	Flight Software	15

2.4.10	Magnetometer	15

2.5	Ground Support Equipment (GSE)	15

2.5.1	Mechanical GSE (MGSE)	16

2.5.2	Electrical GSE (EGSE)	16

2.5.3	GSE Software	16

2.5.4	Simulators	16

2.6	Integration and Test (I&T)	16

2.6.1	Spacecraft Bus I&T	16

2.6.2	Satellite I&T	16

2.6.2.1	Special Testing	16

2.6.2.2	End-to-End (ETE) Testing	16

2.6.3	Transportation and Handling	16

2.6.4	Storage	16

2.7	Launch and Operations	16

2.7.1	Satellite/Launch Vehicle I&T	16

2.7.2	Flight Operations	17

2.7.3	Operations Training	17

2.7.4	Simulator Training	17

2.8	Post Acceptance Support	17

2.9	Special Studies & Tasks	17

2.10	Education & Public Outreach	17

3.0	Spacecraft #3	18

4.0	Spacecraft #4	18

5.0	Spares	18

5.1	Spare Parts and Material	18

5.2	Spare Assemblies/Subassemblies	18

5.2.1	Mechanical Spares	18

5.2.2	Thermal Spares	18

5.2.3	GN&C Spares	18

5.2.4	C&DH Spares	18

5.2.5	COMM Spares	19

5.2.6	Power Spares	19

5.2.7	Propulsion Spares	19

5.2.8	Magnetometer Spares	19

Document Change Record	20

# Spacecraft #1

The Contractor will include within this WBS element at a minimum, all sub-elements to the level described in this document. This will assist the government in organizing, describing, and reporting the design, analysis, fabrication, assembly, integration, testing, and operation of the GOES-R satellite.

The Contractor will organize and report design and analysis separately from fabrication, assembly and test in separate WBS sub-elements.

The Contractor will organize and report non-recurring and recurring cost in separate WBS sub-elements.

## Program Management

### Program Management Office

This element defines the business and administrative planning, organizing, directing, coordinating, controlling, and approval processes used to accomplish overall program objectives, which are not associated with specific hardware or software elements. This element includes project reviews and documentation, non-project owned facilities, and project reserves. It excludes costs associated with technical planning and management, and costs associated with delivering specific engineering, hardware and software products.

#### Travel

This element defines the travel and travel related expenses required to perform the GOES-R mission.

### Resource Management

This element defines the program control and management systems that provide for Work-Breakdown Structure (WBS) development, acquisition management, information technology management, resource management, Earned-Value Management (EVM), facilities, environmental, logistics and schedule management.

#### Configuration Management

This element defines the control of performance, functional and physical characteristics over the program and product life cycle. Configuration management is applied to requirements, documentation, software and hardware. Hardware includes qualification hardware; engineering, proto-flight, flight hardware; and ground support equipment.

#### Information Technology Management

This element defines the technical and management efforts to provided software and hardware infrastructure support.

### Risk Management

This element defines the continuous, iterative, and proactive process to manage risk and achieve mission success. The process involves identifying, analyzing, planning, tracking, controlling, documenting, and communicating risks effectively. Risk is characterized by the combination of the probability or likelihood that the program will experience an event and the consequences, impact, or severity of the event, were it to occur.

### Government Resident Office

This element defines the resources to provide access, office space, furniture, printers, copier(s), facsimile machine(s), phones, and broadband access to the internet and contractor's intranet through launch of the last spacecraft for NASA residents and Government visitors.

### Customer Communication

This element defines the technical preparation and administrative support for all program reviews and joint meetings.

- Kick-Off Meeting

- Teleconferences

- Project Management Reviews (PMR)

- Technical Interchange Meetings (TIM)

### Design Reviews

- Systems Definition Review (SDR)

- Subsystem Reviews

- Subcontract Reviews

- Preliminary Design Review (PDR)

- Critical Design Review (CDR)

- Design Modification Reviews

- Program System Integration Review (SIR)

- Pre-Environmental Review (PER)

- Satellite Pre-Storage/Pre-Shipment Review (PSR)

### Miscellaneous Reviews

The element defines the resources required for the following reviews:

- Integrated Baseline Review (IBR)

- Engineering Peer Reviews

- Software Reviews including the Software Test Readiness Review and the Software Qualification Review.

- Test Reviews

- Instrument Receiving Reviews

### Review Support

The element defines the support to the Government for the following reviews:

- Independent Review Team (IRT) reviews

- Standing Review Board (SRB) reviews.

- Instrument design reviews.

- Ground Segment design reviews.

- Mission Operation Review (MOR).

- Management Readiness Review (MRR)

- Flight Readiness Review (FRR).

- Launch Readiness Review (LRR).

- Flight Operations Review (FOR).

- Operation Readiness Review (ORR).

- Phase 0/I, II, III Safety Reviews at the Kennedy Space Center (KSC).

## Systems Engineering (SE)

Systems engineering is the technical and management efforts of directing and controlling an integrated engineering effort for the project. This element includes the efforts to define the spacecraft, conducting trade studies; the integrated planning and control of the technical program efforts of design engineering, software engineering, system architecture development, and integrated test planning, system requirements writing, configuration control, technical oversight, control and monitoring of the technical program. Documentation Products include mission/system requirements document (MSRD); interface control documents (ICDs); and verification and validation (V&V) plan. Excludes any design engineering costs.

### Systems Engineering Management

This element is the activities that directly manage all systems engineering efforts for each spacecraft development.

### Systems Engineering Support

This element is the systems engineering to support the functional design and development of the spacecraft and incorporation of the instruments.

### System Designs, Analyses and Trades

This element is the system studies and trades and risk assessment to develop the design for the spacecraft.

### Requirements and Specification Generation

This element is the activities that define, implement, and maintain a Systems Engineering Requirements Management System for managing, detailing, organizing, controlling, and linking the spacecraft requirements.

### Performance Verification Plans and Procedures

This element is the system performance verification program documenting the overall verification plan, implementation, and result which provide traceability from system requirements specification to launch and initial on-orbit capability. This will also provide the baseline for tracking on-orbit performance versus pre-launch capability.

### Interface Definition and Control

#### Instrument Interfaces

This element is the systems analysis and engineering to define all aspects of the spacecraft-to-instrument interfaces.

#### Ground Interfaces

This element is the systems analyses and engineering to define all aspects of the space communications interfaces.

#### Launch Vehicle Interfaces

This element is the systems analyses and engineering to define all aspects of the spacecraft-to-launch vehicle interface.

### Contamination

This element is the resources to assure that appropriate contamination control is maintained through all phases the development and of integration and test of the spacecraft.

## Safety and Mission Assurance (S&MA)

This element is all resources to support the performance assurance and verification effort for the spacecraft as documented in the GOES-R Spacecraft Mission Assurance Requirements (SCMAR).

### S&MA Management

This element is all resources to manage the performance assurance and verification effort for the spacecraft as documented in the GOES-R Spacecraft Mission Assurance Requirements (SCMAR).

### Safety

This element is all resources to perform all work to comply with safety requirements for the spacecraft as documented in the SCMAR 417-R-SCMAR-0011 and AFSPCMAN 91-710.

### Parts Control

This element is all resources to perform parts control for the spacecraft as defined in the SCMAR.

### Materials and Processes Control

This element is all resources to comply with the Materials and Processes Control requirements for the spacecraft as defined in the SCMAR.

### Reliability

This element is all resources to comply with the Reliability requirements for the spacecraft as defined in the SCMAR.

### Quality Assurance

This element is all resources to comply with the Quality Assurance requirements for the spacecraft as defined in the SCMAR.

### Software Assurance

This element is all resources to comply with the Software Assurance requirements for the spacecraft as defined in the NASA-STD-8739.8, Software Assurance Standard.

#### Software Safety

This element is all resources to comply with the Software Safety requirements for the spacecraft as defined in the NASA-STD-8719.13B; NASA Software Safety Technical Standard.

#### Software Validation and Verification

This element is all resources to implement a Software Validation and Verification (V&V) program to ensure that software being developed or maintained satisfies functional, performance, and other requirements at each stage of the development process, and that the final product meets customer requirements.

#### Independent Validation and Verification

This element is all resources to support Independent Validation and Verification efforts.

#### Software Problem Reporting and Corrective Action

This element is all resources for Software Problem Reporting and Corrective Action that addresses reporting, analyzing and correcting software non-conformances and software test failures reported in Software Problem Reports (SPR's) throughout the development lifecycle.

## Spacecraft

The spacecraft bus is the platform for carrying payloads, instruments, and other mission-oriented equipment in space to achieve the mission objectives. This element includes all design, analysis, fabrication, assembly, test efforts required to deliver the spacecraft subsystems for integration and test. This element does not include integration and test of the spacecraft bus, spacecraft, or satellite.

### Spacecraft Management

The Spacecraft Management element includes all resources related to systems engineering, project management of the bus hardware and software.  As stated above, this element does not include integration and test with instruments, ground system, or launch vehicle.

### Mechanical

The Mechanical subsystem is the bus structure and mechanisms.  It includes all resources related to the design, development, production, positioning, integration and test of the bus structure and mechanical parts.  Any structure and mechanism support equipment is also included.

### Thermal

The Thermal subsystem is the active and passive devices, and thermal support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the active and passive thermal components.

### Guidance, Navigation and Control (GN&C)

The GN&C subsystem includes all orbit determination, orbit control, attitude determination and attitude control functions.  It includes all related GN&C flight hardware components and propulsion interfaces; as well any necessary GN&C support equipment.  It includes all activities related to the design, development, production, integration, test, launch and on-orbit checkout of the above components.

### Command and Data Handling (C&DH)

The C&DH subsystem is command and telemetry electronics, Spacewire and GN&C support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### C&DH Harnesses

This element is the harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Communications (COMM)

#### Space/Ground Communication

The Communications subsystem is the, antennas, all active and passive Radio Frequency (RF) components including but not limited to MMICs, filters, hybrids, attenuators and communications support equipment.  This includes the RF sections of the Telemetry, Tracking, and Command (TT&C) subsystem.   It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Auxiliary Communication Services

The Auxiliary Communication Services subsystem encompasses the structure, software, and support equipment of the GOES Rebroadcast service (GRB) and the Unique Payload Services.  The Unique Payload Services consist of Data Collection System (DCS), Low-Rate Information Transfer (LRIT), Search-and-Rescue Satellite (SARSAT), and Emergency Managers Weather Information Network (EMWIN).  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### COMM Harnesses

This element is the harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Power

This subsystem is the power generation, power conditioning, power storage, harnesses, cables, and electrical support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Battery

This element is the power storage.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Solar Array

This element is the power generation.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Power Regulation and Conditioning

This element is the power conditioning.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Power Harnesses

This element is the power distribution including all harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Propulsion

This subsystem is the tanks, plumbing, thrusters, propellants, and propulsion support equipment.  It includes all activities related to the design, development, production, integration, test, launch and on-orbit checkout of the above components.

### Flight Software

The Flight Software subsystem for the Bus subsystem encompasses the flight software for components of the bus, to include the Thermal, GN&C, C&DH, Communications, Electrical, Magnetometer, and Propulsion elements.  The primary activities for the Flight Software element are systems engineering, software project management, algorithm development, and subsystem integration and test.  The activities of requirements analysis, design, coding and unit testing, and unit integration and testing are also included.

### Magnetometer

The Magnetometer instrument (subsystem) encompasses the magnetometer sensor, structure, mechanisms, and magnetometer support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

## Ground Support Equipment (GSE)

This element includes the resources all GSE required to assemble, integrate, and test the spacecraft.

### Mechanical GSE (MGSE)

This element includes the resources required to provide MGSE.

### Electrical GSE (EGSE)

This element includes the resources required to provide EGSE.

### GSE Software

This element includes the resources required to provide non-flight software.

### Simulators

This element includes the resources required to provide spacecraft simulators.

## Integration and Test (I&T)

This element includes the resources required to perform the integration and test of the spacecraft bus, payloads, and instruments to form the satellite, transportation, handling, shipment and storage through delivery of the satellite.

### Spacecraft I&T

This element includes the resources required to perform the integration and test of the spacecraft subsystems including the COMM and the magnetometer payloads onto the spacecraft bus.

### Satellite I&T

This element includes the resources required to perform the integration and test of the GFP instruments onto the spacecraft.

#### Special Testing

This element includes the resources required to perform Special Testing.

#### End-to-End (ETE) Testing

This element includes the resources required to perform ETE Testing.

### Transportation and Handling

This element includes the resources required to perform transportation and handling

### Storage

This element includes the resources required to provide storage of the spacecraft bus, spacecraft, GFP instruments, and satellite.

## Launch and Operations

This element includes the resources required after delivery and before acceptance of the satellite.  These resources include launch site processing, pre-launch/flight operations support, and operations support through completion of satellite deployment and checkout.

### Satellite/Launch Vehicle I&T

This element includes the resources required to perform integration of the satellite onto the launch vehicle.

### Flight Operations

This element includes the resources required to flight operations support.

### Operations Training

This element includes the resources required to perform training for flight operations.

### Simulator Training

This element includes the resources required to perform training for flight simulator support.

## Post Acceptance Support

This element includes the resources required to perform sustaining engineering support of the satellite after acceptance by the government.

## Special Studies & Tasks

This element includes the resources required to perform special studies and tasks as directed by the government.

## Education & Public Outreach

This element includes the resources required to perform education and public outreach.

# Spacecraft #2

The Contractor will include within this WBS element at a minimum, all sub-elements to the level described in this document. This will assist the government in organizing, describing, and reporting the design, analysis, fabrication, assembly, integration, testing, and operation of the GOES-R satellite.

The Contractor will organize and report design and analysis separately from fabrication, assembly and test in separate WBS sub-elements.

The Contractor will organize and report non-recurring and recurring cost in separate WBS sub-elements.

## Program Management

### Program Management Office

This element defines the business and administrative planning, organizing, directing, coordinating, controlling, and approval processes used to accomplish overall program objectives, which are not associated with specific hardware or software elements. This element includes project reviews and documentation, non-project owned facilities, and project reserves. It excludes costs associated with technical planning and management, and costs associated with delivering specific engineering, hardware and software products.

### Resource Management

This element defines the program control and management systems that provide for Work-Breakdown Structure (WBS) development, acquisition management, information technology management, resource management, Earned-Value Management (EVM), facilities, environmental, logistics and schedule management.

#### Configuration and Information Management

This element defines the control of performance, functional and physical characteristics over the program and product life cycle. Configuration management is applied to requirements, documentation, software and hardware. Hardware includes qualification hardware; engineering, proto-flight, flight hardware; and ground support equipment.

#### Information Technology Management

This element defines the technical and management efforts to provided software and hardware infrastructure support.

### Risk Management

This element defines the continuous, iterative, and proactive process to manage risk and achieve mission success. The process involves identifying, analyzing, planning, tracking, controlling, documenting, and communicating risks effectively. Risk is characterized by the combination of the probability or likelihood that the program will experience an event and the consequences, impact, or severity of the event, were it to occur.

### Government Resident Office

This element defines the resources to provide access, office space, furniture, printers, copier(s), facsimile machine(s), phones, and broadband access to the internet and contractor's intranet through launch of the last spacecraft for NASA residents and Government visitors.

### Program Communication

This element defines the technical preparation and administrative support for all program reviews and joint meetings.

- Kick-Off Meeting

- Teleconferences

- Project Management Reviews (PMR)

- Technical Interchange Meetings (TIM)

### Design Reviews

- Systems Definition Review (SDR)

- Subsystem Reviews

- Subcontract Reviews

- Preliminary Design Review (PDR)

- Critical Design Review (CDR)

- Design Modification Reviews

- Program System Integration Review (SIR)

- Pre-Environmental Review (PER)

- Satellite Pre-Storage/Pre-Shipment Review (PSR)

### Miscellaneous Reviews

The element defines the resources required for the following reviews:

- Integrated Baseline Review (IBR)

- Engineering Peer Reviews

- Software Reviews including the Software Test Readiness Review and the Software Qualification Review.

- Test Reviews

- Instrument Receiving Reviews

### Review Support

The element defines the support to the Government for the following reviews:

- Independent Review Team (IRT) reviews

- Standing Review Board (SRB) reviews.

- Instrument design reviews.

- Ground Segment design reviews.

- Mission Operation Review (MOR).

- Management Readiness Review (MRR)

- Flight Readiness Review (FRR).

- Launch Readiness Review (LRR).

- Flight Operations Review (FOR).

- Operation Readiness Review (ORR).

- Phase 0/I, II, III Safety Reviews at the Kennedy Space Center (KSC).

## Systems Engineering (SE)

Systems engineering is the technical and management efforts of directing and controlling an integrated engineering effort for the project. This element includes the efforts to define the spacecraft, conducting trade studies; the integrated planning and control of the technical program efforts of design engineering, software engineering, system architecture development, and integrated test planning, system requirements writing, configuration control, technical oversight, control and monitoring of the technical program. Documentation Products include mission/system requirements document (MSRD); interface control documents (ICDs); and verification and validation (V&V) plan. Excludes any design engineering costs.

### Systems Engineering Management

This element is the activities that directly manage all systems engineering efforts for each spacecraft development.

### Systems Engineering Support

This element is the systems engineering to support the functional design and development of the spacecraft and incorporation of the instruments.

### System Designs, Analysis and Trades

This element is the system studies and trades and risk assessment to develop the design for the spacecraft.

### Requirements and Specification Generation

This element is the activities that define, implement, and maintain a Systems Engineering Requirements Management System for managing, detailing, organizing, controlling, and linking the spacecraft requirements.

### Performance Verification Plans and Procedures

This element is the system performance verification program documenting the overall verification plan, implementation, and result which provide traceability from system requirements specification to launch and initial on-orbit capability. This will also provide the baseline for tracking on-orbit performance versus pre-launch capability.

### Interface Definition and Control

#### Instrument Interfaces

This element is the systems analysis and engineering to define all aspects of the spacecraft-to-instrument interfaces.

#### Ground Interfaces

This element is the systems analyses and engineering to define all aspects of the space communications interfaces.

#### Launch Vehicle Interfaces

This element is the systems analyses and engineering to define all aspects of the spacecraft-to-launch vehicle interface.

### Image Navigation and Registration (INR)

This element is the l analyses and tests to verify that the spacecraft meets the interfaces required to ensure instrument INR performance.  The INR interfaces include physical and data interfaces.

### Contamination

This element is the resources to assure that appropriate contamination control is maintained through all phases the development and of integration and test of the spacecraft.

## Safety & Mission Assurance (S&MA)

This element is all resources to support the performance assurance and verification effort for the spacecraft as documented in the GOES-R Spacecraft Mission Assurance Requirements (SCMAR).

### Safety

This element is all resources to perform all work to comply with safety requirements for the spacecraft as documented in the SCMAR 417-R-SCMAR-0011 and AFSPCMAN 91-710.

### Parts Control

This element is all resources to perform parts control for the spacecraft as defined in the SCMAR.

### Materials and Processes Control

This element is all resources to comply with the Materials and Processes Control requirements for the spacecraft as defined in the SCMAR.

### Reliability

This element is all resources to comply with the Reliability requirements for the spacecraft as defined in the SCMAR.

### Quality Assurance

This element is all resources to comply with the Quality Assurance requirements for the spacecraft as defined in the SCMAR.

### Software Assurance

This element is all resources to comply with the Software Assurance requirements for the spacecraft as defined in the NASA-STD-8739.8, Software Assurance Standard.

#### Software Safety

This element is all resources to comply with the Software Safety requirements for the spacecraft as defined in the NASA-STD-8719.13B; NASA Software Safety Technical Standard.

#### Software Validation and Verification

This element is all resources to implement a Software Validation and Verification (V&V) program to ensure that software being developed or maintained satisfies functional, performance, and other requirements at each stage of the development process, and that the final product meets customer requirements.

#### Independent Validation and Verification

This element is all resources to support Independent Validation and Verification efforts.

#### Software Problem Reporting and Corrective Action

This element is all resources for Software Problem Reporting and Corrective Action that addresses reporting, analyzing and correcting software non-conformances and software test failures reported in Software Problem Reports (SPR's) throughout the development lifecycle.

## Spacecraft

The spacecraft bus is the platform for carrying payloads, instruments, and other mission-oriented equipment in space to achieve the mission objectives. This element includes all design, analysis, fabrication, assembly, test efforts required to deliver the spacecraft subsystems for integration and test. This element does not include integration and test of the spacecraft bus, spacecraft, or satellite.

### Spacecraft Management

The Spacecraft Management element includes all resources related to systems engineering, project management of the bus hardware and software.  As stated above, this element does not include integration and test with instruments, ground system, or launch vehicle.

### Mechanical

The Mechanical subsystem is the bus structure and mechanisms.  It includes all resources related to the design, development, production, positioning, integration and test of the bus structure and mechanical parts.  Any structure and mechanism support equipment is also included.

### Thermal

The Thermal subsystem is the active and passive devices, and thermal support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the active and passive thermal components.

### Guidance, Navigation and Control (GN&C)

The GN&C subsystem includes all orbit determination, orbit control, attitude determination and attitude control functions.  It includes all related GN&C flight hardware components and propulsion interfaces; as well any necessary GN&C support equipment.  It includes all activities related to the design, development, production, integration, test, launch and on-orbit checkout of the above components.

### Command and Data Handling (C&DH)

The C&DH subsystem is command and telemetry electronics, Spacewire and GN&C support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### C&DH Harnesses

This element is the harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Communications (COMM)

#### Space/Ground Communication

The Communications subsystem is the, antennas, all active and passive Radio Frequency (RF) components including but not limited to MMICs, filters, hybrids, attenuators and communications support equipment.  This includes the RF sections of the Telemetry, Tracking, and Command (TT&C) subsystem.   It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Auxiliary Communication Services

The Auxiliary Communication Services subsystem encompasses the structure, software, and support equipment of the GOES Rebroadcast service (GRB) and the Unique Payload Services.  The Unique Payload Services consist of Data Collection System (DCS), Low-Rate Information Transfer (LRIT), Search-and-Rescue Satellite (SARSAT), and Emergency Managers Weather Information Network (EMWIN).  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### COMM Harnesses

This element is the harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Power

This subsystem is the power generation, power conditioning, power storage, harnesses, cables, and electrical support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Battery

This element is the power storage.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Solar Array

This element is the power generation.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Power Regulation and Conditioning

This element is the power conditioning.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

#### Power Harnesses

This element is the power distribution including all harnesses, cables, and support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

### Propulsion

This subsystem is the tanks, plumbing, thrusters, propellants, and propulsion support equipment.  It includes all activities related to the design, development, production, integration, test, launch and on-orbit checkout of the above components.

### Flight Software

The Flight Software subsystem for the Bus subsystem encompasses the flight software for components of the bus, to include the Thermal, GN&C, C&DH, Communications, Electrical, Magnetometer, and Propulsion elements.  The primary activities for the Flight Software element are systems engineering, software project management, algorithm development, and subsystem integration and test.  The activities of requirements analysis, design, coding and unit testing, and unit integration and testing are also included.

### Magnetometer

The Magnetometer instrument (subsystem) encompasses the magnetometer sensor, structure, mechanisms, and magnetometer support equipment.  It includes all resources related to the design, analysis, fabrication, assembly, and test of the above components.

## Ground Support Equipment (GSE)

This element includes the resources all GSE required to assemble, integrate, and test the spacecraft.

### Mechanical GSE (MGSE)

This element includes the resources required to provide MGSE.

### Electrical GSE (EGSE)

This element includes the resources required to provide EGSE.

### GSE Software

This element includes the resources required to provide non-flight software.

### Simulators

This element includes the resources required to provide spacecraft simulators.

## Integration and Test (I&T)

This element includes the resources required to perform the integration and test of the spacecraft bus, instruments, payloads, launch vehicle, and ground system.

### Spacecraft Bus I&T

This element includes the resources required to perform the integration and test of the spacecraft subsystems including COMM and the magnetometer onto the spacecraft bus.

### Satellite I&T

This element includes the resources required to perform the integration and test of the GFP instruments onto the spacecraft.

#### Special Testing

This element includes the resources required to perform Special Testing.

#### End-to-End (ETE) Testing

This element includes the resources required to perform ETE Testing.

### Transportation and Handling

This element includes the resources required to perform transportation and handling

### Storage

This element includes the resources required to provide storage of the spacecraft bus, spacecraft, GFP instruments, and satellite.

## Launch and Operations

This element includes the resources required to perform launch site processing, pre-launch flight operations support, and operations support through completion of satellite deployment and checkout.

### Satellite/Launch Vehicle I&T

This element includes the resources required to perform integration of the satellite onto the launch vehicle.

### Flight Operations

This element includes the resources required to flight operations support.

### Operations Training

This element includes the resources required to perform training for flight operations.

### Simulator Training

This element includes the resources required to perform training for flight simulator support.

## Post Acceptance Support

This element includes the resources required to perform sustaining engineering support of the satellite after acceptance by the government.

## Special Studies & Tasks

This element includes the resources required to perform special studies and tasks as directed by the government.

## Education & Public Outreach

This element includes the resources required to perform education and public outreach.

# Spacecraft #3

The Contractor will include within this WBS element at a minimum, all sub-elements to the level described in this document. This will assist the government in organizing, describing, and reporting the design, analysis, fabrication, assembly, integration, testing, and operation of the GOES-R satellite.

The Contractor will organize and report design and analysis separately from fabrication, assembly and test in separate WBS sub-elements.

The Contractor will organize and report non-recurring and recurring cost in separate WBS sub-elements.

# Spacecraft #4

The Contractor will include within this WBS element at a minimum, all sub-elements to the level described in this document. This will assist the government in organizing, describing, and reporting the design, analysis, fabrication, assembly, integration, testing, and operation of the GOES-R satellite.

The Contractor will organize and report design and analysis separately from fabrication, assembly and test in separate WBS sub-elements.

The Contractor will organize and report non-recurring and recurring cost in separate WBS sub-elements.

# Spares

## Spare Parts and Material

This element includes spare parts and material including wire and connectors to support two spacecraft.

## Spare Assemblies/Subassemblies

This element includes fabrication, assembly and testing of assemblies and subassemblies.

### Mechanical Spares

This element includes fabrication, assembly and testing of Mechanical Subsystem spares.

### Thermal Spares

This element includes fabrication, assembly and testing of Thermal Subsystem spares.

### GN&C Spares

This element includes fabrication, assembly and testing of GN&C Subsystem spares.

### C&DH Spares

This element includes fabrication, assembly and testing of C&DH Subsystem spares.

### COMM Spares

This element includes fabrication, assembly and testing of COMM Subsystem spares.

### Power Spares

This element includes fabrication, assembly and testing of Power Subsystem spares.

### Propulsion Spares

This element includes fabrication, assembly and testing of Propulsion Subsystem spares.

### Magnetometer Spares

This element includes fabrication, assembly and testing of Magnetometer Instrument spares.

# Document Change Record (DCR)

CCR #: XXXX

(Note: DCR will be automatically generated from Windchill document and CCR database)