- Page 25, Table 2, second row -- "Ultra-High Energy" cell B,  targeted performance,----> please change "C/10" to "C/2".

The new table should look like this

Table 2 - Definition of terms used in Figure 1 and Table 1.

| Term | Definition |
| --- | --- |
| “High Energy” Cell A | Expected cell-level specific energy: 180 Wh/kg specific energy at C/10 and 0°C to 3.000 Volts/cell Expected components: NASA-defined Li(Li,NMC)O2 cathode, electrolyte, and separator and conventional carbonaceous anode NMC= Ni,Mn,Co Targeted Performance: 2,000 cycles at 100% DOD to 80% of original capacity at C/2 |
| “Ultra-High Energy” Cell B | Expected cell-level specific energy: 260 Wh/kg specific energy at C/10 and 0°C to 3.000 Volts/cell Expected components: NASA-defined Li(Li,NMC)O2 cathode, electrolyte, separator, and silicon-composite anode NMC= Ni,Mn,Co Targeted Performance: 200 cycles to 100% DOD to 80% of original capacity at C/2 |