Cryopump Specifications:

1) 2 each 10 inch cyro-pumps with 14 inch conflate flange inlet only. (Oxford Instruments Cryo-Plex 10 or equivalent.)

2) Each pump must have minimum pumping speed of 3000 liter/min (air). (Oxford Instruments Cryo-Plex 10 or equivalent.)

3) A single water cooled fixed bypass valve helium compressor (200/230 three phase) capable of handling both pumps individually or simultaneously.  (Oxford Instruments M600 Helium Compressor or equivalent)

4) Remote digital temperature monitor capable of monitoring both pumps, individually or simultaneously.  (Oxford Instruments E1000 or equivalent)

5) Electrical purge valves for each pump.

6) Purge gas heater for each pump.

7) Electrical roughing pump valve for each pump.

8) Splitter box capable of driving up to three cryo-pumps from one helium compressor.

9) Complete set of 10 ft SS helium lines (4 each), drive motor cables, tees, tools, manuals and instructions needed for complete installation and operation of both pumps, separately or simultaneously.