|  | Simulator Platform Motion Requirements for Recurrent Airline Pilot Training and Evaluation Judith Bürki-Cohen U.S. Department of Transportation Research and Special Programs Administration John A. Volpe National Transportation Systems Center Cambridge, MA 02142 Tiauw H. Go Massachusetts Institute of Technology Cambridge, MA 02139 William W. Chung Science Applications International Corporation Lexington Park, MD 20653 Jeffery A. Schroeder NASA Ames Research Center Moffett Field, CA 94035 Final Report September 2004 |
| --- | --- |

ACKNOWLEDGEMENTS

Many people contributed to this work, and we are very grateful to all of them. The work has been requested by the Federal Aviation Administration’s Flight Standards Service Voluntary Safety Programs Branch managed by Dr. Tom Longridge. We greatly appreciate his insights. In his office, we would also like to thank Dr. Douglas Farrow for his support. Dr. Eleana Edens is the perfect FAA Program Manager. We thank her for her encouragement and effective guidance. The Chief Scientific and Technical Advisor for Human Factors, Dr. Mark D. Rodgers, sponsored the work. We thank him and Dr. Tom McCloy in his office for their involvement. The discussions with Dr. Ed Cook and Paul Ray, the present and former managers of the National Simulator Program Office, were always enlightening. Members of other branches of the FAA’s Flight Standard Services that provided helpful suggestions are Jan Demuth and Archie Dillard.

At the Volpe National Transportation Systems Center, we thank Dr. Donald Sussman, the Chief of the Operator Performance and Safety Division, for his direction. Young Jin Jo provided critical support for the First Study, and Sean Jacobs and Kristen Harmon for the Second Study. Dr. Nancy Soja of Battelle provided expert advice on the experimental design and analyses throughout. Dr. Shuang Wu also of Battelle performed the extraordinary feat of programming the laptop that allowed completely hands-off administration of the experiments in the First Study, which eliminated any experimenter effect and saved us innumerable trips to the experiment site.

The first two authors are greatly indebted to the regional-airline officials and the training facility that made the First Study possible. This involved donating some of pilots' training time and volunteering instructor/evaluator expertise on part of the airline. The training facility liberally shared simulator-engineering expertise and time. This involved simulator calibration, extensive data collection from the simulator, and programming the simulator interface with the experiment laptop. We feel extremely lucky to have enjoyed the generosity and competence of these collaborations and would love to thank them personally, but our Memorandum of Understanding promised them anonymity.

Dr. Vic Lebacqz, Lynda Haines, Dr. Mary Connors, Dr. Key Dismukes, and Julie Mikula made it possible for us to conduct the Second Study at NASA Ames Research Center by contributing not only their expertise, but also financial support. They provided the simulator facilities with a wonderful team of highly qualified professionals: Ghislain Saillant, Charley Ross, Jerry Jones, Jim Miller, Norm Gray and Tom Standifur, Gary Uyehara (and Carlos and Steve). We are also indebted to Bob Shipley, Diane Carpenter, Conrad Grabowski, and Dave Lambert. We received constructive feedback on the simulator-motion tuning from Terry Rager, Dan Renfroe, Mietek Steglinski, Bob Cornell, Gordon Hardy and Dick Bray. We thank you all very much, and it was great to work with you!

But nothing would have been accomplished without the many regional-airline crews serving as experiment subjects in the First Study and B747-400 pilots serving as experiment subjects in the Second Study. We thank them for their tolerance to fly many very difficult maneuvers, and for sharing their expertise with us in the long questionnaires. For the Second Study, we thank Bill Edmunds of the Airline Pilots Association, Michael Brown of United Airlines, and Bill Bulfer of Bluecoat Forum. Our desperate pleas always yielded new phone calls to Wendy Krikorian and Mary K. Tracey, our competent recruiters.

In conclusion, we would like to remember Edward M. Boothe, who supported this work from the very beginning. He was a key member of the team for the First Study and participated in the design of the Second Study until a few days before his death. We miss him.

TABLE OF CONTENTS

ACKNOWLEDGEMENTS	2

TABLE OF CONTENTSLIST OF FIGURES	4

LIST OF FIGURES	8

LIST OF TABLES	9

ACRONYMS AND ABBREVIATIONS	11

EXECUTIVE SUMMARY	13

SIMULATOR PLATFORM MOTION REQUIREMENTS FOR RECURRENT AIRLINE PILOT TRAINING AND EVALUATION	17

1.	Background	17

2.	Requirements Review: Initial Findings and Research Questions	18

2.1	Subject Matter Expert Opinion	18

2.2	Literature Review	18

3.	Empirical Research	19

3.1	Research Approach	19

3.2	Research Strategy	20

3.2.1	Magnify Any Existing Evidence For An Effect Of Motion	20

3.2.2	Avoid Spurious Effects	21

4.	First Study	21

4.1	Research Question	21

4.2	Method	21

4.3	Procedure	22

4.4	Results	23

4.4.1	Test Simulator Motion Performance	23

4.4.2	Pilot Performance and Behavior	24

4.5	Discussion	24

5.	Second Study	25

5.1	Introduction	25

5.2	Method	26

5.2.1	Experiment Design Overview	26

5.2.2	Environmental Variables and Maneuver Choice	27

5.2.2.1	Airport, weather and airplane variables	27

5.2.2.2	Continued takeoffs with engine failure	27

5.2.2.3	Engine-out landing maneuvers	28

5.2.3	Simulator	29

5.2.3.1	Visual system	29

5.2.3.2	Sound system	30

5.2.3.3	Control loading	30

5.2.3.4	Motion system	31

5.2.3.5	Motion tuning	36

5.2.3.6	Simulator calibration	38

5.2.4	Participants	38

5.2.4.1	Pilots Flying (PF)	38

5.2.4.2	Pilots Not Flying (PNF)	39

5.2.4.3	Air Traffic Controller (ATC)	39

5.2.5	Procedures	39

5.2.6	Performance Feedback Displays	40

5.2.6.1	Takeoff feedback displays	40

5.2.6.2	Approach and landing performance feedback displays	42

5.2.7	Data Collection	43

5.2.7.1	Simulator data	43

5.2.7.2	Questionnaires	44

5.3	Results Based On Simulator Recordings	45

5.3.1	Data Analysis	45

5.3.1.1	Performance standards	45

5.3.2	Success Rates	45

5.3.3	Performance and Behavior During Maneuvers	46

5.3.3.1	Types of measures	47

5.3.3.2	Data analysis procedure	47

5.3.3.3	Resolution (Power)	49

5.3.3.4	V2 cut	50

5.3.3.5	V1 Cut	53

5.3.3.6	Precision Instrument Approach	57

5.3.3.7	Sidestep landing	60

5.3.3.8	Discussion	66

5.3.4	Individual Training Progress	67

5.3.4.1	V2 Cut	68

5.3.4.2	V1 Cut	69

5.3.4.3	Precision instrument approach	70

5.3.4.4	Sidestep landing	71

5.3.4.5	Discussion	71

5.3.5	Pilot Grades	72

5.3.5.1	Determination and calculation	72

5.3.5.2	Grade analysis	72

5.3.5.3	Discussion	74

5.3.5.4	Comparison with First Study	74

5.4	Opinions from Questionnaires	74

5.4.1	Data Analysis Overview	74

5.4.2	Pilots Flying	75

5.4.2.1	Data Analyses	75

5.4.2.2	Were there any differences between the Motion and No-Motion groups?	75

5.4.2.3	Did Pilots Flying recognize the absence of motion?	77

5.4.2.4	Did Pilots Flying perceive the test simulator as different than the last simulator flown/airplane?	79

5.4.2.5	Effects of Phase, Maneuver, and Control	79

5.4.3	Pilots Not Flying (PNF)	80

5.4.3.1	Data Analyses	80

5.4.3.2	Did Pilots-Not-Flying perceive differences between the Motion and No-Motion groups?	81

5.4.3.3	Effects of Pilot-Not-Flying and Maneuver	82

5.4.3.4	Did Pilots-Not-Flying perceive Pilots Flying as different than an average Pilot Flying?	82

5.4.4	Summary of Opinions	83

5.5	Summary of Second Study	83

6.	General Discusssion and Conclusions	85

References	87

Appendix 1. FIRST STUDY RESULTS	90

A1.1. Resolution (power)	90

A1.2. V1 Cut Pilot-Vehicle Performance and Pilot Behavior	90

A1.3. Rejected Takeoff (RTO) Pilot-Vehicle Performance and Pilot Behavior	91

A1.4. Individual Training Progress	93

A1.5. Comparison of Failure-Induced Lateral Acceleration of Several Simulators	94

A1.6. Instructor/Evaluator Grades	95

Appendix 2. SAMPLE DAILY CALIBRATION TEST	97

Appendix 3. BRIEFING OF PILOT FLYING	104

Appendix 4. AIR-TRAFFIC-CONTROL SCRIPT	106

Appendix 5. EXPERIMENT PROTOCOL	113

Appendix 6. PILOT-FLYING QUESTIONNAIRES	128

Appendix 7. PILOT-NOT-FLYING QUESTIONNAIRES	165

Appendix 8. LIST OF RECORDED SIMULATOR VARIABLES	185

Appendix 9. LIST OF MEASURES CALCULATED PER SEGMENT	188

Appendix 10. GRADING CRITERIA AND WEIGHTS	205

Appendix 11. COMMENTS ON MOTION BY NO-MOTION GROUP	211

Appendix 12. COMMENTS ON MOTION BY MOTION GROUP	223

Appendix 13. COMMENTS ON SIMULATOR ACCEPTABILITY	229

Appendix 14. COMMENTS ON PHYSICAL COMFORT	231

Appendix 15. COMMENTS ON WORKLOAD	233

Appendix 16. COMMENTS ON CONTROL FEEL	239

Appendix 17. COMMENTS ON CONTROL SENSITIVITY	244

Appendix 18. COMMENTS ON STRATEGY & TECHNIQUE	250

Appendix 19. COMMENTS ON HANDLING QUALITIES	256

Appendix 20. COMMENTS ON PERFORMANCE	263

Appendix 21. COMMENTS ON OTHER CUES	270

Appendix 22. COMMENTS ON GAINING PROFICIENCY	277

Appendix 23. FINAL COMMENTS ACCEPTIBILITY	279

Appendix 24. FINAL COMMENTS PHYSICAL COMFORT	281

Appendix 25. FINAL COMMENTS CONTROL FEEL, SENSITIVITY, OTHER CUES				283

Appendix 26. FINAL COMMENTS HANDLING QUALITIES, CONTROL STRATEGY	286

Appendix 27. FINAL COMMENTS GAINING PROFICIENCY	295

Appendix 28. FINAL COMMENTS MISCELLANEOUS	304

Appendix 29. PNF COMMENTS ON MOTION	306

Appendix 30. PNF COMMENTS ON PF PERFORMANCE	307

Appendix 31. PNF COMMENTS ON PF’S STRATEGY	310

Appendix 32. PNF COMMENTS ON PF’S WORKLOAD	315

Appendix 33. PNF COMMENTS ON PF’S GAINING PROFICIENCY	318

LIST OF FIGURES

Figure 3-1. Research Approach to Determine Motion Requirements	20

Figure 5-1. Vertical Upward Gust Profile during SSL	29

Figure 5-2. B747-400 Simulation Cueing Transport Delay Response	32

Figure 5-3. B747-400 Heave Acceleration Frequency Response	33

Figure 5-4. A Typical Motion-Cueing Generation Process For Ground-Based Flight Simulators	33

Figure 5-5. B747-400 Motion-Drive Algorithm	35

Figure 5-6. Before (empty symbols) and After (filled symbols) High-Pass-Filter Tuning	36

Figure 5-7. Comparison Of Lateral Side Force Before and After Tuning	37

Figure 5-8. Feedback for Takeoff Heading and Speed	41

Figure 5-9. Feedback for Takeoff Altitude and Bank Angle	42

Figure 5-10. Feedback on Glide Path, Localizer, and Approach Speed Deviation	43

Figure 5-11. Success Rates by Phase and Maneuver	46

Figure 5-12. Grade Means by Phase and Maneuver	73

Figure A1-1. First Study Percentage of Grades in Each Grading Category as a Function of Maneuver, Phase, and Group	96

LIST OF TABLES

Table 5-1. Detectable Group and Phase Effect	49

Table 5-2. V2 Cut Group Effects by Phase (shading indicates significant group difference)	51

Table 5-3. V2 Cut Phase Effects by Group	51

Table 5-4. V2 Cut Group Differences	52

Table 5-5. V2 Cut Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	52

Table 5-6. V1 Cut Group Effects by Phase (shading indicates significant group difference)	54

Table 5-7. V1 Cut Phase Effects by Group	55

Table 5-8. V1 Cut Group Differences	55

Table 5-9. V1 Cut Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	55

Table 5-10. Precision Instrument Approach Fix-to-DH Results for Group	58

Table 5-11. Precision Instrument Approach Fix-to-DH Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	58

Table 5-12. Precision Instrument Approach DH-to-TD Results for Group	59

Table 5-13. Precision Instrument Approach DH-to-TD Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	60

Table 5-14. Sidestep Landing Fix-to-BC Results for Group	61

Table 5-15. Sidestep Landing Fix-to-BC Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	62

Table 5-16. Sidestep Landing BC-to-Gust Results for Group	63

Table 5-17. Sidestep Landing BC-to-Gust Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	63

Table 5-18. Sidestep Landing Gust-to-TD Results for Group	64

Table 5-19. Sidestep Landing Gust-to-TD Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	65

Table 5-20. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for V2 Cut (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	69

Table 5-21. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for V1 Cut (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	69

Table 5-22. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for Precision Instrument Approach (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	71

Table 5-23. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for Sidestep Landing (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	71

Table 5-24. Grade Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	73

Table A1-1. First Study Detectable Group and Phase Effects	90

Table A1-2. First Study V1 Cut Group Differences (Marginal)	91

Table A1-3. First Study V1 Phase Differences (I=Evaluation, II=Training, III=Quasi –Transfer Testing)	91

Table A1-4. RTO Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)	92

Table A1-5 Fisher’s Exact Statistics of Group Differences in Percentage Improvement Among First Training, Last Training, and Quasi-Transfer Testing for V1 Cut	93

Table A1-6. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Among First Training, Last Training, and Quasi-Transfer Testing for RTO	94

Table A1-7. V1 Cut Lateral Acceleration Data from Several Simulators	95

ACRONYMS AND ABBREVIATIONS

AC				Advisory Circular

acg				Acceleration at center of gravity

AGL				Above Ground Level

ANOVA			Analyses of Variance

APU				Auxiliary Power Unit

ATC				Air Traffic Controller

(C				degrees Celsius

CAE Inc.			simulator manufacturer (formerly Canadian Aviation

Electronics)

CRT				Cathode Ray Tube

deg				degrees

DFW				Dallas Fort Worth

DOF				Degrees of Freedom

F				F ratio computed from a sample

(F				degrees Fahrenheit

FAA				Federal Aviation Administration

FD				Flight Director

ft				feet

g				gravitational constant

GS				Glide slope

Hz				Hertz

I/E				Instructor/Evaluator

in				inches

ILS				Instrument Landing System

LOC				Localizer

LOE				Line Oriented Evaluation

MANOVA			Multivariate Analyses of Variance

ms				milliseconds

MSL				Mean Sea Level

NASA ARC		National Aeronautics and Space Administration Ames

Research Center

nm				Nautical Miles

n.s.				not significant (p>.05)

NSP				National Simulator Program

p				probability

PIA				Precision Instrument Approach

PF				Pilot Flying

PFQ				Pilot Flying Questionnaire

PNF				Pilot Not Flying

PNFQ				Pilot Not Flying Questionnaire

PTS				Practical Test Standards

r				Pearson’s correlation coefficient

RMS				Root Mean Square

RTO				Rejected Takeoff

RVR				Runway Visual Range

s				seconds

SASTM				statistical analysis software

SMEs 				Subject Matter Experts

STD				Standard Deviation

SSL				Sidestep Landing

V1				Takeoff decision speed

V2				Takeoff safety speed (minimum)

Vmca				Minimum control airspeed

Volpe Center			Volpe National Transportation Systems Center

VR				Takeoff rotation speed

xs				Surge

ys				Sway

zs				Heave

(				Roll

(				Pitch

(				Yaw

*				significant (p<.05)

EXECUTIVE SUMMARY

This report presents the results of two studies that examined the effect of enhanced hexapod-simulator motion on recurrent evaluation in the simulator, on the course of recurrent training in the simulator, and on "quasi-transfer" of this recurrent training to the simulator with motion as a stand-in for the airplane. These studies were conducted in the framework of the Volpe Center’s Flight Simulator Fidelity Requirements Research Program and sponsored by the Federal Aviation Administration.

Today, airline pilots are almost exclusively trained and evaluated in flight simulators. That means that the first time a pilot flies a particular airplane or in a particular capacity in the air, the airplane is carrying paying passengers. It is therefore critical that, when evaluating a pilot in the simulator, the skills and behaviors comprising the expertise of this pilot when flying the airplane are accurately reflected in the simulator. Similarly, the skills and behaviors a pilot acquires in the simulator must transfer to the airplane. The definition of an effective simulator is therefore one that allows full transfer of performance and behavior from the airplane to the simulator for evaluation and from the simulator to the airplane for training.

The Federal Aviation Administration, who regulates simulator use for total training and evaluation of airline pilots, is responsible for ensuring that simulator requirements are sufficient for transfer of performance and behavior between airplane and simulator. To prevent simulator rental, acquisition, and maintenance costs from excluding smaller airlines from the benefits of simulator training and evaluation, however, requirements must also be necessary.

One requirement that remains controversial is the need for platform motion. Of course, the airplane does move; however, there are inherent limitations to the fidelity of the hexapod-motion platforms used for airline-pilot training. These motion platforms have been shown to be useful in some aerospace applications, but there is currently no empirical research that shows that platform motion improves transfer for airline-pilot training and evaluation. Studies to date have been limited by factors such as: (1) the quality of the available visual and motion systems, (2) the experience level of the subject population (e.g., studies often used novice pilots that may not yet have learned to capitalize on motion cues), (3) the number of subjects used, (4) the choice of maneuver selection (e.g., using tracking maneuvers that may not require motion cues), (5) individual differences in the pilot population, and (6) combinations of these factors (e.g., the number of pilots was not sufficient to wash out individual differences between pilots that could have masked the effects of motion).

Volpe was attempting to overcome these limitations by adopting a design philosophy using a simulator with a wide field-of-view visual system known to induce the illusion of motion (vection); testing experienced and highly motivated pilots that were asked to perform diagnostic pilot-in-the-loop maneuvers with asymmetric disturbances and high workload; and measuring at a high-sampling rate the motion-performance of the simulator, pilot flight-path precision, and pilot-control inputs. Also, any factors that could mask an effect of motion, such as between-group differences in experience, were minimized by calibrating the simulator, choosing a homogenous group of pilots, and counterbalancing across groups anything else that could not be controlled. A so-called quasi-transfer design was used to control many nuisance variables such as weather or traffic. In this design, pilots that came fresh from an airplane (to prevent adaptation to the simulator) were divided into two groups, a Motion and a No-Motion group. Pilots in both groups were first evaluated to measure transfer from the airplane. Pilots in the Motion group were then trained in the simulator with motion whereas pilots in the No-Motion group were trained in the simulator without motion. Following the training session, both groups were quasi-transferred to the simulator with motion as a stand-in for the airplane in order to compare the effect of the two training methods on transfer of training. Impostor effects that might masquerade as an effect of motion, such as rater or pilot bias, were avoided by concealing the purpose of the experiment and the motion condition (on or off) of the simulator from participants.

The first Volpe study (First Study) was aimed at testing the effect of “as is” motion, i.e., the motion provided by a qualified Level C simulator that is used around the clock for airline-pilot training and checking (Bürki-Cohen, Boothe, Soja, DiSario, Go, and Longridge, 2000; Go, Bürki-Cohen, and Soja, 2000). Because the initial concern was with the affordability of simulators for regional airlines, regional-airline crews were tested on a simulator of a 30 passenger turboprop airplane with wing-mounted engines. The data was collected from approximately 40 Captains flying engine failures on takeoff before their recurrent evaluation (V1 cuts and rejected takeoffs).

No systematic differences between the two groups were found, during Evaluation, Training, and Quasi Transfer to all motion. This was true for the measurements from the simulator and for the grades provided by instructor/evaluators, and also for the crew and instructor opinions collected in extensive questionnaires. Power analyses showed that the number of pilots was sufficient to wash out individual differences between pilots, so that even small effects of motion could have been found.

Does this mean that “as is” motion is equivalent to having no motion with regard to transfer between simulator and airplane for recurrent evaluation and training? The failure-induced lateral acceleration of the “as is” motion simulator, which was supposed to serve as an alerting cue for the pilot that there was an engine problem, was found to be very mild, certainly milder than the one recommended based on the flight data. It was unclear whether this is typical for other simulators used in airline-pilot evaluation and training, and a comparison with eight airline simulators showed that it might be. This would lead to the conclusion that the requirements for airplane simulators used for airline-pilot training and checking should be tightened, and such efforts are currently being discussed by regulators and industry. Given the burden to the simulator operators to provide such motion and to the Federal Aviation Administration to enforce it, however, and the fact that airline pilots have been successfully trained and evaluated in simulators qualified under the current requirements for over twenty years, it seemed necessary to document that motion that was improved with tighter standards would result in improved transfer for airline-pilot simulator checking (evaluation) and training. This was the purpose of the Second Study, which is described in this report.

For this Second Study, the motion of a CAE Level D simulator was re-engineered to optimize the motion stimulation for the planned test maneuvers in collaboration with the National Aeronautics and Space Administration’s Ames Research Center. The device simulates a Boeing 747-400 airplane with four wing-mounted engines. Its lateral acceleration and heave were enhanced trading off rotational motion (mainly yaw) based on findings in the literature. Forty current B747-400 Captains and First Officers participated, aided by two cohort pilots performing non-flying duties. The participants departed with an engine failure either just before (V1 cut) or just after takeoff (V2 cut), and then continued with either a precision instrument approach and landing with shifting crosswinds or a sidestep landing with a vertical upward gust just after sidestepping to a parallel runway. To make the maneuvers even more difficult (and participants subjective comments suggested that they did find them very difficult!), the autopilot and autothrottle were inoperative throughout and the flight director was inoperative during the landings only, so they had to be hand flown. These maneuvers were chosen to 1) replicate the V1 cut tested in the First Study and 2) reduce any visual reference to the runway and require control in multiple axes compared to the First Study.

The results obtained with enhanced motion were very different from the First Study with “as is” motion. Several differences between the Motion and the No-Motion groups were found, and a fairly clear picture of the effect of motion emerges. First, motion did appear to alert pilots of a disturbance, as stipulated in the literature, but only for the V1 cut. This may be because the V1 cut occurs close to the ground and any delay in response would result in scraping the wings or the tail (which did happen, but equally rarely in the two groups, and usually because of applying the wrong rudder). Due to the motion alert, the Motion group had a faster pedal response and tracked heading slightly better, but the latter showed only during Evaluation. The No-Motion pilots, as long as they did not have the motion cue, were unable to significantly improve their pedal-response time, even during Training when they were told what failure to expect. Once they quasi-transferred to motion for Quasi-Transfer Testing however, their pedal-response time was identical to the one of the Motion group. Hence, the No-Motion pilots did not seem to need recurrent training with motion to be able to sense and appropriately respond to motion cues.

Second, training with motion cues clearly increased the control activity of the Motion pilots, especially for wheel inputs. However, this reduced their flight precision, at least for the landing maneuvers. These performance decrements in localizer, heading, or airspeed tracking were in fact the largest effects found in the study, and may be operationally relevant. Most importantly, the performance deficit of the Motion group persisted even when both groups had motion during Quasi-Transfer Testing.

Perhaps inherent to the increased control activity of the Motion group was a curious result found for the V2 cut during Quasi-Transfer Testing, namely, that the Motion group responded slower to the engine failure than the No-Motion group, with apparently no effect on flight precision. One hypothesis is that the Motion group was fatigued. An alternative explanation is that both groups were equally fatigued and that the emergence of the motion cues may have had “stimulating” effect on the No-Motion group. Overall, the V2 cut does appear to have been especially fatiguing for both groups, with several variables that had significantly improved during Training compared to Evaluation significantly deteriorating between Training and Quasi-Transfer Testing for both groups.

Third, motion affected the sidestep-landing strategy in a predictable manner. When motion was available, pilots landed softer. However, pilots also landed slightly farther from the runway threshold, but still well within the landing box. Like all effects on the landing maneuvers, this effect seems to have been consolidated during Training, because it persisted even during Quasi-Transfer Testing.

Finally, the results show that both groups improved their performance for all maneuvers in the course of the experiment, regardless of whether they were trained with or without motion. Initial Evaluation, however, was subject to motion effects for all four maneuvers, as discussed above.

These results were reflected in Pilot-Flying (PF) and Pilot-Not-Flying (PNF) opinions. The PFs found the simulator equally acceptable than their company simulator regardless of group. They were also equally comfortable in it. Moreover, there was no difference between groups with respect to their comparisons of the simulator to the airplane for Control Sensitivity and Control Strategy and Technique.

For all the in-depth probing, there were only four questions on which the two PF groups disagreed, and for one of these it was the No-Motion pilots that answered more favorably: After Training, the No-Motion group gave the simulator higher handling-quality ratings than the ones given by the Motion group. The ratings of the Motion group were higher than the ones of the No-Motion group for Control Feel (even at Quasi Transfer, when the No-Motion group also had motion), Other Cues (the majority of No-Motion pilots did recognize that something was amiss) and Performance (only after Evaluation).

The PNFs ratings always were in favor of the No-Motion group, but sometimes this was due to one of the two PNFs, while the other didn’t always see a difference. They felt that the No-Motion pilots were more similar to the average pilot than the motion pilots with respect to Control Strategy and Technique (but not during Evaluation). They gave higher performance and lower workload ratings to the No-Motion pilots, except during Training. For Quasi Transfer only, they gave better Gaining Proficiency ratings to the No-Motion pilots.

In conclusion, this study showed that enhanced hexapod motion, configured based on the guidelines in the literature, does have an effect. It appears to affect the accuracy of recurrent evaluation. However, the benefits for recurrent training remain questionable.

Results of these studies and the previous hexapod motion research should assist the FAA in determining future research directions in the effort to develop improved motion standards. It also may contribute to finding a cost-effective solution to today’s airline evaluation and training needs via an appropriate combination of fixed-base and motion-base simulators.

SIMULATOR PLATFORM MOTION REQUIREMENTS FOR RECURRENT AIRLINE PILOT TRAINING AND EVALUATION

# Background

The goal of this work is to enhance the safety of air travel by promoting the use of effective airplane simulators for airline-pilot training and evaluation. Over the past twenty-two years, transport pilots have come to be trained and evaluated almost exclusively in the simulator, so that the first time a pilot serves in a new position or in a new airplane type, the airplane will be carrying paying passengers. This is certainly true for all major airlines, and may become a fact for all airlines as a consequence of flight simulation device aviation rulemaking activities (see http://www.faa.gov/nsp/Part60_FTD.htm, accessed August, 2004, for more information).

Given that the practice of “total training and evaluation in the simulator” may become regulatory, the FAA is committed to ensure that flight simulators are both effective and accessible to all airlines. This must include regional airlines that find it cost-effective, for small airplanes with comparatively low operating cost and loss in revenue, to conduct some of their pilot training and evaluation in the air.

A simulator is effective if it supports full transfer of performance and behavior between simulator and airplane. That is, for effective training, any skills that pilots acquire in the simulator must be available to them in the airplane. Similarly, for accurate evaluation, the level of skills pilots display in the airplane must be reflected during evaluation in the simulator. Strategies and techniques as well as physical and mental workload of the pilots must also transfer between simulator and airplane.

Ideally the simulator systems must stimulate pilots as the airplane would. Only then the simulator will accurately represent all cognitive and motor challenges encountered in flight. However, not all stimuli encountered in flight may affect performance or behavior. And likewise, not all stimuli may need to be, or can be, presented exactly as they are encountered in flight. Some may have to be generated psychologically using different underlying physics than the ones present in the air, such as when the simulator tilts forward or backward to create the illusion of the negative/positive surge acceleration experienced during landing and takeoff. Similarly, the illusion of motion induced by the visual system, i.e., vection, may help compensate for some of the other limitations of a standard hexapod-platform-motion system in generating exactly the same vestibular stimulation experienced in the airplane (see also Roscoe, 1991).

FAA regulations therefore must be sufficient to ensure that all stimuli necessary for full transfer of performance and behavior between simulator and airplane are presented. However, they also must be necessary, i.e., they should avoid requiring stimuli with no operationally relevant effect on training and evaluation outcomes, because this would unnecessarily reduce the availability of qualified simulators. To achieve this goal, the FAA asked the Volpe National Transportation Systems Center (Volpe Center) to review the FAA’s flight simulator fidelity requirements as outlined in Advisory Circular AC 120-40B (FAA, 1991). The initial focus of this research was recurrent evaluation.

# Requirements Review: Initial Findings and Research Questions

## Subject Matter Expert Opinion

As a first step, Volpe organized a series of joint FAA-industry symposia on the most costly aspects of airplane simulation attended by subject matter experts (SMEs) from industry, academia, and FAA (Longridge, Ray, Boothe, and Bürki-Cohen, 1996). These led to a focus on platform motion, which is mandatory for simulators used as the sole means for training and evaluation. The participating SMEs in the symposium on simulator motion generally perceived that the absence of platform-motion cueing in fixed-base devices is likely to have a detrimental effect on pilot control performance, particularly in maneuvers with an external disturbance entailing sudden motion-onset cueing with limited visual reference. It was also noted, however, that there was no scientific evidence that training in a fixed-base device would lead to degraded control performance in the actual aircraft (Bürki-Cohen (Ed.), 1996). This issue is especially pertinent in a device equipped with a wide field-of-view visual system, which can generate an illusion of motion (vection) (Young, 1978), albeit with a slower onset than vestibular motion.

## Literature Review

An extensive literature review (Bürki-Cohen, Soja, and Longridge, 1998) confirmed that platform motion in the simulator might improve the perceived acceptability of the simulator, at least when the pilots were aware of the motion manipulation (Reid and Nahon, 1988; but see Bussolari, Young, and Lee, 1987). Motion also improved pilot performance and control behavior in the simulator, especially for tasks with an external disturbance or tracking tasks in aircraft with low dynamic stability (Hall, 1978; Hall, 1989; Hosman and van der Vaart, 1981). Some of the benefits of platform motion have also been shown to transfer to a higher-fidelity simulator (Levison, 1981). However, the literature review also showed that the benefits of platform motion have not been proven in the case of transfer of training to the airplane (see, e.g., Waag, 1981).

In conclusion, many experts believe that the simulator should provide all cues that a pilot experiences in the airplane. For motion, however, the actuator travels and filter algorithms typical for the type of simulators accessible to airlines severely limit the ability to fully match the magnitude and phasing of the cues experienced in the air. This may have been one of the reasons why none of the earlier studies has been able to demonstrate an effect of motion on transfer of skills to the airplane. Motion systems have been greatly improved, however, since these studies were conducted, and so has the ability to avoid other flaws in the experimental design.

The FAA asked Volpe to revisit the question of simulator motion empirically, using a rigorous research design and data analysis process and state-of-the-art motion and visual systems. Questions to be answered include, but are not limited to, the following: Are there any flight tasks for which a measurable difference in simulator training and evaluation effectiveness can be found with and without platform motion? What is the relationship in motion-cueing effectiveness for a wide field-of-view visual display versus platform motion? Are current platform-motion qualification criteria optimal? Is there a relationship between pilot experience level and the effectiveness of platform motion for training?

# Empirical Research

## Research Approach

The research approach adopted by the Volpe Flight Simulator Fidelity Requirements Research Program is illustrated in Figure 3-1. First, it is necessary to establish that the type of motion that is currently used by airlines has an operationally relevant effect on recurrent training and evaluation. This test is performed on a turboprop airplane simulator used round-the-clock by regional airlines. The rationale for this is that some regional airlines do not have ready access to qualified simulators with motion systems, and many conduct at least some of their recurrent training in the airplane. This deprives them of the benefits of safely practicing carefully constructed emergency scenarios in the simulator. It is therefore necessary to establish that the benefits from experiencing motion outweigh the cost of this loss in training opportunities.

If no operationally relevant effect of motion was found with such a “typical” motion system, the next step was to test whether the standard Stewart hexapod-platform-motion systems available to airlines can be re-engineered so as to produce an operationally relevant effect of motion. Other aspects of the experiment may be modified as well to enhance the possibility of finding an effect of motion.

If still no operationally relevant effect of motion is found, the next step will be to test whether the previous finding that motion has no effect on training transfer and evaluation extends to initial training of airline pilots. Another question may be the role of motion in maneuvers where pilots must learn to ignore motion cues, such as when vestibular motion perception leads to dangerous illusions with regard to the airplane’s attitude.

Whenever an operationally relevant effect of motion is found, however, the next logical step will be to develop comprehensive motion qualification criteria. Current regulations, although they do require the presence of motion for certain types of training and evaluation, do not provide a means to objectively assess the quality of such motion (Lahiri, 2000). For this purpose, the nature of effective motion cues and which maneuvers are sensitive to them and why must be determined.

To prevent that such tightened motion standards limit access to simulators, it will also be important to examine whether there are alternative means than full six-degree-of-freedom platform motion to provide effective motion cueing, such as providing motion onset cues with vibration and dynamic seats.

Figure 3-1. Research Approach to Determine Motion Requirements

## Research Strategy

The research strategy adopted in this work is very much informed by the fact that previous attempts to show an effect of simulator motion on transfer to the airplane have failed. Most of the studies testing transfer of training to the airplane suffer from the use of now outdated motion systems, the possibility of pilot and rater bias, insufficient measurements and statistical power, and the use of maneuvers for which motion may not be important. In this work, everything possible will be done to magnify any positive evidence for an effect of motion that may exist, and to avoid any spurious effects due to factors other than motion.

### Magnify Any Existing Evidence For An Effect Of Motion

It is much more convincing to reject a null hypothesis, such as “simulator motion has no effect on transfer between airplane and simulator,” based on positive evidence for a motion effect, than to accept it when no evidence for a motion effect is found. Therefore, this research program will use the following tactics to prevent that an effect of motion is overlooked:

Compare pilot performance and behavior between extreme conditions, i.e., in a Level C/D motion simulator vs. the fixed-base simulator

Use subjects and maneuvers that are described in the literature as susceptible to feedback from vestibular motion cues rather than from vection arising from visual  cues, namely, experienced pilots and skill-based disturbance maneuvers

Measure or record at high sampling rates any variables and parameters that are potentially useful to assess pilot performance and workload

Ensure sufficient statistical power of the experiment, i.e., test enough subjects to wash-out unavoidable within-group differences that might mask an effect of motion

### Avoid Spurious Effects

Spurious effects due to factors other than motion that may either impersonate or camouflage an effect of motion will be avoided using the following tactics:

Counterbalance or randomly assign participants to groups to minimize any known or unknown between-group subject variables

Prevent variability in pilot stimulation and measurement error by calibrating the simulator systems (motion, force feedback, visual system, sound, etc.) and measurement systems regularly before, during, and after data collection

Counterbalance any other uncontrollable variables

Conceal the motion status of the simulator to prevent participant bias

Use a quasi-transfer paradigm, where the simulator with motion is used as a stand-in for the airplane during transfer testing, to avoid other uncontrolled variability such as weather and traffic

# First Study

## Research Question

Following the research plan shown in Figure 3-1, the First Study investigated the effect of “typical” motion on recurrent training and evaluation of regional airline pilots in the presence of a wide field-of-view visual system (Bürki-Cohen et al., 2000; Bürki-Cohen, Soja, Go, Boothe, DiSario, and Jo, 2001; Go et al., 2000).

## Method

The experiment used an FAA qualified Level C flight simulator of a 30 passenger, three crew, turboprop airplane with wing-mounted twin engines and counter-rotating propellers. The six-degree-of-freedom synergistic motion system had hydraulically actuated legs capable of a 60-inch stroke. The high quality visual system provided wide angle collimated cross-cockpit viewing with a 150 degrees horizontal and 40 degrees vertical field of view available to each pilot.

The subjects of the experiment were experienced regional-airline captains. Half of the captains were first evaluated and trained with and the other half without motion. Then the transfer of the skills acquired by both groups during Evaluation and Training was tested in the simulator with the motion system turned on as a stand-in for the airplane (Quasi-Transfer Testing). The test maneuvers selected were engine failures on takeoff with either rejected takeoff (RTO) or continued takeoff (V1/R cut) with a quarter mile Runway Visual Range (RVR) and 10 knots crosswind, which satisfied the criteria described in the literature as diagnostic for the detection of a motion requirement. These criteria included:

Skill- instead of procedure-based, to increase reliance on motion feedback (Hosman, 1999)

Closed loop, to allow for motion to be part of the control-feedback loop to the pilot

Disturbance maneuver, to highlight an early alerting function of motion (Gundry, 1976; Hall, 1989)

High gain, to magnify any motion effects and to reduce the stability of the pilot-airplane control loop (Hall, 1989)

High workload with crosswind and low visibility, to increase the need for redundant cues such as provided by motion, out-the-window view, instruments and sound

Short duration, to prevent pilots from adjusting to a lack of cues

Neither the captains, nor the not-flying co-pilots, nor the instructors/evaluators (I/Es) knew the purpose of the experiment or the motion status of the simulator.

## Procedure

First, the crews flew one V1 cut followed by one RTO (Evaluation). Half of them did it with the motion system on (Motion group) and the other half with the motion system off (No-Motion group). Any additional training needed to reach the company standards for RTO and V1 cut came next, with motion on or off depending on group. At most, there were two additional training trials for each type of maneuver. After Training, all participants filled out a questionnaire. This was followed by two normal takeoffs with the same motion configuration. Then the crews flew one last V1 cut followed by one last RTO with motion on for all crews (Quasi-Transfer Testing). After Quasi-Transfer Testing, all participants filled out a second questionnaire, to see whether their opinions had changed after all had experienced motion. The engine-failure side was randomly varied during the course of the experiment.

Phase I: Evaluation/First Training

Evaluate V1 cut

Evaluate RTO

Phase II: Training

Train to criterion, or a maximum of additional 2 V1 cuts and 2 RTOs

Perform 2 normal takeoffs as a distraction

PF and PNF complete Questionnaire 1

Phase III: Quasi-Transfer Testing

Quasi Transfer to motion V1 cut

Quasi Transfer to motion RTO

PF and PNF complete Questionnaire 2

The stimulation of the PF by the simulator, pilot-vehicle control performance, and pilots' responses were measured by recording 78 simulator state and control-input variables at a 50 Hz sampling rate, resulting in a vast amount of objective data on simulator performance and pilot performance and behavior/workload. Two forms of subjective data were also collected. First, at the conclusion of each maneuver the I/E provided a grade for the just-completed maneuver. Second, as already mentioned in the previous paragraph, at the end of the training phase and again at the end of the Quasi-Transfer phase all participants were queried on PF performance and workload as well as simulator comfort and acceptability. From all these data, four types of results were obtained:

Motion stimulation at the PF station

Effect of motion and experiment phase on measured performance and workload of the PFs, either as a group or individually

Effect of motion on the performance of the PFs as perceived by the I/Es and reflected in their grading

Effect of motion on participants opinion regarding PF performance/workload and simulator comfort and acceptability

## Results

Multivariate analyses of variance (MANOVA) determined the Group and Phase effects on the pilot performance and behavior (see 5.3.3.2 for an explanation of analysis procedures). Sufficient statistical power was ascertained by calculating the minimum difference between the standardized means leading to the rejection of the null hypothesis with a probability of .80 (effect size). Table A1-1 in Appendix 1 summarizing the Group and Phase effect sizes of several important variables shows that the analyses performed could detect sufficiently small Group or Phase differences to capture operationally relevant effects.

### Test Simulator Motion Performance

For the test simulator, the actually measured roll and longitudinal accelerations followed the airplane model fairly well given the limitations inherent to all simulators. For vertical acceleration, however, the motion system of the test simulator did not respond much to the command provided by the equations of motion. This was especially true for V1 cut maneuvers. However, because the engine failures used in our experiment do not produce much vertical acceleration, the lack of vertical acceleration cueing may not be very important.

More important, however, is the finding that failure-induced lateral acceleration was not well represented by the motion system of the test simulator (see Table A1-7 in A1.5). Not only was it greatly attenuated, but visual inspection of the measured response did not lead to an easy distinction of failure-induced lateral acceleration, unlike the response derived from the equations of motion (relatively high peak shortly after engine failure). This may represent a significant deficiency in pilot stimulation, because lateral acceleration may act as a useful cue for proper failure recognition and for initiation of appropriate response.

### Pilot Performance and Behavior

The results of the study indicate that the motion provided by the test simulator did not, in an operationally significant way for the tasks tested, affect evaluation, training progress, or quasi transfer to the simulator with motion of the training acquired in the simulator with or without motion. It also didn’t consistently affect the Pilots’ Flying (PF), Pilots’ Not Flying (PNF), and instructor/evaluator’s perception of the PFs’ performance, workload, and training progress, or of their own comfort in the simulator. Neither did it affect the acceptability of the simulator to the PF and the PNF. Details of these results are given in Appendix 1 and will be discussed further in comparison with the results of the Second Study (Section 5.3).

## Discussion

There are several questions that can be raised regarding the validity of these results, which will be answered in turn below.

First, it was found that the lateral acceleration produced by the simulator shortly following the engine failure was greatly attenuated compared to the lateral acceleration from the aircraft mathematical model. This suggests that the simulator used in the study may not have provided sufficient motion stimulation to the captains to produce an effect. The first response to this objection is that the test simulator was FAA qualified and used 20 out of 24 hours daily for pilot training and evaluation. So, it cannot be excluded that the motion stimulation produced by this simulator may be representative for at least some of the simulators in service. With help from the National Simulator Program Office (NSPO), data from eight other simulators representing aircraft with wing-mounted engines were gathered. Initial evaluation was done on those sets (Boothe, 2000), but unfortunately, only four sets were available for further examination. A1.5. Comparison of Failure Induced Lateral Acceleration in Appendix 1 summarizes the findings from these comparisons, including the test simulator. The results indicate that the motion-system performance of the test simulator was not atypical. One major question to be answered in the Second Study, therefore, is whether standard hexapod-motion systems can be tuned so that they provide motion that is representative enough to affect continuing qualification of airline pilots.

A second question is whether the regional-airline Captains were experienced and motivated enough. In response to this question, it must be noted that the short-haul operations of a regional airline require these captains to fly many takeoffs. Moreover, not one of the approximately 300 takeoffs in the experiment resulted in a crash (compare with the Success Rates in the Second Study given in 5.3.2, which tested very senior pilots flying long-haul operations across continents). With regard to the captains’ motivation, they were tested by the same instructor/evaluator that would grade them during their recurrent evaluation immediately afterwards, when their job was in jeopardy. It is safe to assume that they were motivated to make a good initial impression.

A third question is whether the takeoff maneuvers tested were sensitive enough to detect a need for motion. As laid out in Method, both V1/R cuts and RTOs fully satisfy the criteria laid out in the literature. However, although the maneuvers were flown at the lowest legal RVR, there may have been some residual visual reference to the runway centerline, which may have helped the pilots control their flight path even without motion cues. This may have been true even for the V1/R cut, because in the airplane configuration tested, the takeoff decision speed V1 and rotation speed VR were identical. Also, although the two maneuvers perfectly fulfill the three criteria of unpredictability, asymmetry, and short duration, a longer lasting maneuver may be needed to let a measurable motion advantage develop. These considerations will be taken into account when choosing the maneuvers for the Second Study.

The last concern regarding the validity of the results of the First Study is that quasi transfer to the simulator with motion as a stand-in for the airplane was tested instead of transfer to the airplane itself. The first response to this concern is that after years of successful total training and checking in the simulator with motion, the simulator with motion has been validated as a stand-in for the airplane. Second, if motion really makes a difference, then pilots trained in the simulator without motion should perform differently when motion is turned on compared to pilots that were trained under exactly the same configuration that they are being tested in. Third, it would be impossible to design a valid and reliable experiment transferring to the airplane. This is because, on the one hand, sensitive maneuvers would be too dangerous to test in the air. On the other hand, it would be impossible to control for unpredictable environmental nuisance variables such as weather and traffic.

# Second Study

## Introduction

Based on the work described in the previous sections and a growing awareness that the motion requirement needs to be better defined, an ongoing international effort aims at tightening motion standards (see, e.g., Lahiri, 2000). Such standards, however, would represent a considerable burden for both simulator users and simulator regulators. Users would face increased leasing, purchasing, and maintenance costs, as well as loss of training opportunities, e.g., when the simulator motion is malfunctioning and crews have to be sent home. The FAA would need to increase its resources to enforce the tighter standards. Prudence would dictate to first show that tighter motion standards increase the training and evaluation value of simulators sufficiently to increase passenger safety before changing the standards.

The purpose of the Second Study is to test whether the Results of the First Study extend to a high-quality research simulator with its six-degree-of-freedom hexapod re-engineered so as to maximize motion cues and phase match for each of the maneuvers tested. Simultaneously, any other potential reasons for the absence of a motion effect mentioned in the Discussion of the First Study will be avoided as much as possible. To achieve this, the maneuver range will be expanded based on recommendations from the literature and the FAA’s National Simulator Program (NSP). In addition to replicating the V1 cut, they will now include engine-out landings with weather requiring very tight multi-axes flight-path control and a V2 cut providing no visual reference to the runway centerline. Again, experienced pilots will be used, namely, pilots qualified on the Boeing 747-400. Pilots will be motivated to keep tightly in the control loop by providing feedback displays on their flight-path precision on the navigation display. The quasi-transfer paradigm will be maintained to preserve control over variables such as weather and traffic.

## Method

For the general strategy and tactics guiding the design of this experiment, see the overall Research Strategy described earlier.

### Experiment Design Overview

Participants serving as Pilots Flying (PF) were divided into two groups: Motion and No-Motion (between-subjects design). In Phase I and Phase II, i.e., Evaluation and Training, the Motion group was evaluated and trained in the simulator with motion. The No-Motion group was evaluated and trained in the simulator with the motion system turned off. Both groups were then quasi-transferred to the simulator with motion as a stand-in for the airplane to examine whether any effect of motion during Training would persist in the airplane (Phase III, Quasi-Transfer Testing).

This design resulted in two independent variables, the Group variable with two levels (Motion group and No-Motion group) and the Phase variable with three levels (Training, Evaluation, and Quasi-Transfer Testing). Participants belonged to either the Motion or the No-Motion group, but all participants were subjected to the three phases. The dependent variables were derived from over 100 variables, from which the directional, lateral, and longitudinal pilot-vehicle performance and pilot control-input behaviors appropriate for each maneuver were calculated. PFs and Pilots Not Flying (PNFs) also provided their opinions in detailed questionnaires.

Precautions were taken to assure that no effects were overlooked or, conversely, emerged as a result of nuisance variables unrelated to the independent variables. First, quasi transfer to the simulator with motion, instead of real transfer to the airplane, kept constant any extraneous variables other than motion that could affect PF performance and behavior (e.g., weather and traffic). Quasi transfer to the simulator also removed any restrictions on the maneuver choice due to safety reasons. Also, PFs were randomly assigned to the Motion or No-Motion group, provided that they were equally distributed across groups with respect to seat, PNF, and experience (number of landings in the past 12 months). To prevent bias, the purpose of the experiment was concealed from the PFs. Finally, simulator-calibration checks were performed before each experiment run to ensure the consistency of all functions.

### Environmental Variables and Maneuver Choice

The maneuvers were selected from the most critical phases of flight, namely, takeoff and landing. Each engine-out takeoff maneuver was paired with a landing maneuver into one scenario. All maneuvers were tailored to satisfy the criteria listed in the Method of the First Study. To include the engine-out landing maneuvers mentioned in the Introduction to this study, however, the short-duration criterion to prevent pilot adaptation had to be relaxed. To reduce the visual reference during the VR cut even further, the engine was failed at a specified height Above Ground Level (AGL), resulting in an engine failure after V2 (V2 cut). To be able to compare the results of this study with the First Study, the V1 cut was maintained as a test maneuver. The Pilot-Not-Flying declared the engine failures as not recoverable. As in the previous experiment, maneuvers and airport/meteorological conditions were chosen to correspond as much as possible, while being a good diagnostic tool for detecting the effect of motion, to real-life simulator training and evaluation. They are based on the FAA Practical Test Standards (PTS) (FAA, 2001). The environmental conditions and the maneuvers are described in detail below.

#### Airport, weather and airplane variables

Dallas Forth Worth (DFW) airport was chosen for its configuration and for its presumed equal familiarity to potential study participants.

A light simulated-aircraft gross weight of 550,000 lbs was intended to increase the handling difficulty and motion cues of the simulator during the test maneuvers. Pilots were told that the fuel would remain constant at 60,000 lbs. To further increase pilot workload, the autothrottle was inoperative throughout the experiment.

#### Continued takeoffs with engine failure

In these maneuvers, an outboard engine failure occurred after V1 had been reached and the takeoff must be continued. The failure represented an engine flame-out with failure profile showing exponential loss of 90% of initial thrust in about two seconds.

All takeoffs occurred from runway 36 Right at an altimeter altitude reading of 29.92 inches of mercury. There was a constant 10-knots tailwind. The runway visible range was 600 ft with fog top height of 500 ft. The sky conditions were overcast, with broken clouds at 3000 feet.

The engine-failure triggering variables were varied to generate two maneuvers with different visual reference, motion stimulation and workload as described below.

Takeoff with engine failure after V2

For the V2 cut, an outboard-engine failure was triggered after V2 (150 knots) at 40 feet AGL. Because the airplane was pitched up at this point in the takeoff envelope, pilots could no longer refer to the runway visually and had to fully rely on their instruments and motion perception, if available. Compared to earlier engine failures where the wheels are still on the ground or the airplane is just rotating, pilots need to control pitch in addition to heading, resulting in high workload.

Takeoff with engine failure after V1

For the V1 cut maneuver, an outboard engine was failed when the simulator reached the minimal controllable airborne speed Vmca (124 knots). Compared to a V2 cut, fewer axes need to be controlled when the wheels are still on the ground, but the asymmetry introduced by the engine failure is larger than at higher speeds. Moreover, application of the rudder is less effective at a lower speed. Finally, fast action is critical to avoid contact with the ground. Other reasons to replicate the V1 cut in this study included the ability to compare it with the V1 cut tested in the First Study and the fact that it is an integral part of any simulator qualification ride.

#### Engine-out landing maneuvers

Both landing maneuvers included an outboard-engine failure and were hand flown without autothrottle, autopilot, and FD. Both require the pilot to tightly control the simulator in all three translational (sway, surge, heave) and rotational (pitch, roll, sway) degrees of freedom. Under these circumstances, it was expected to be difficult, without motion feedback, to follow a narrow flight path and land softly in a tight box, especially with weather disturbances added to divert from the flight path.

Precision Instrument Approach

The NSP recommended a hand-flown out-board engine-out Precision Instrument Approach (PIA) with shifting crosswind as particularly hard to fly without motion feedback. This maneuver consisted of landing the airplane on runway 36 Left guided by the Instrument Landing System (ILS, localizer and glide slope). The visibility was kept low with 500 ft cloud ceiling and 5200 ft RVR.

A disturbance from a 10-12 knots terminal area crosswind shifting counterclockwise from a 310 degrees quartering headwind at 3500 ft Mean Sea Level (MSL) to a 220 degrees quartering tailwind on the ground added to the challenges of this hand-flown approach and landing. During training, when Engine 4 was failed instead of Engine 1, the wind shifted clockwise from 40 degrees to 130 degrees to maintain the symmetry of the task.

Sidestep Landing with vertical upward gust

White (1994) used an offset approach followed by an S turn onto the runway at a very low altitude “to generate the kind of high-gain pilot behaviour which is necessary to bring out vehicle or simulator deficiencies.” Sidestep-Landing (SSL) maneuvers with a vertical upward gust have a long history of use (see, e.g., Schroeder, Chung, Tran, Laforce, 1998, based on Bjorkman, 1986). In the current study, the pilot had to switch landing from runway 36 Left to the 1200 ft (measured from centerline to centerline) apart parallel runway 36 Right at the relatively low altitude of 1000 ft AGL The visibility was 5 miles with a cloud ceiling of 1100 ft.

The wind was a constant 10 knots at 310 degrees, with the exception of a vertical upward gust peaking at 25 ft/s applied on the runway rollout to increase the workload of the pilot during this critical phase of the maneuver. As shown in Figure 5-1, the gust profile started at 2.15 nautical miles (nm) from the runway 36 Right threshold (measured along the runway centerline) and peaked at an altitude of 25 ft/s between 2.05 and 2 nm from the threshold. By 1.95 nm from threshold, the gust had completely died down. The gust was programmed so that all pilots would experience the same wind strength regardless of their lateral deviation from the runway centerline.

Figure 5-1. Vertical Upward Gust Profile during SSL

### Simulator

The FAA-NASA (National Aeronautics and Space Administration) Ames Research Center (ARC) Boeing 747-400 simulator was used in the experiment. It was manufactured by the Canadian company CAE and FAA qualified at the Level D (FAA, 1991).

The main characteristics of the B747-400 simulator were:

Four engines

Glass cockpit with six cathode ray tube (CRT) displays:

Primary Flight Display (PFD) Captain

PFD First Officer

Navigational Display Captain

Navigational Display First Officer

Engine Indication and Crew Alerting System (EICAS) displays in the middle. During the experiment, the EICAS Displays were in Primary Engine Indications and Secondary Engine Indications mode (as usual). This gave the crew a real-time indication using graphical gauge representation of the engine parameters. The graphical representation made it easy for pilots to see which engine was failed.

#### Visual system

The simulator was equipped with a FlightSafety Vital 8i visual system with the following capabilities:

A wide field-of-view (180 degree horizontal and 40 degree vertical) uninterrupted panoramic out-the-window scene with cross-cockpit viewing

High brightness and resolution, permitting high ambient lighting in the cockpit without washing out the scene or causing unwanted reflections

Geo-specific, full color texture that greatly enhanced scene realism

Over 2000 texture patterns available on-line simultaneously

General transparency that enhanced cloud simulation

Up to 2500 polygons and 1000 light points per channel processor in day mode; 5000 light points in dusk and night modes

Landing-light simulation that gave roll and pitch cues. Lobe shafts in fog were also simulated.

#### Sound system

The simulator was equipped with a multi-channel and multi-speaker sound system. Simulation of aircraft sounds was realistic to the degree that direction as well as frequency and amplitude were represented. Sound data was compiled from high-quality tape recordings supplied as part of the approved data package.

Sound simulation was automatic and included, e.g., the following effects:

Power plant sounds covered the whole operating range and varied according to pressure, altitude and airspeed. Simulated engine sounds represented acceleration, reverse sounds, engine surge, compressor stall, fan noise, engine seizure, turbine whine and rumble.

Aerodynamic hiss varied as a function of airspeed, cabin differential pressure, altitude, sideslip, turbulence, and was modified as applicable by the use of flaps, slats, spoilers, landing gear, and landing gear doors.

Runway effects and taxi rumble sounds reflected taxiing, takeoff and landing noise for the specified levels of runway roughness. Taxi rumble varied as a function of speed, runway roughness, and load on the nose wheel. Special sounds were provided for sliding after gear collapse.

Sounds produced by pneumatic and electrical ground power units, Auxiliary Power Unit (APU) operation, hydraulic pumps, air-conditioning airflow, generator relays or other relay switching sounds, windshield wipers, nose gear up lock

Special effects, such as cabin explosive decompression, tire burst, crash, rain, hail and thunder

#### Control loading

An advanced fully digital hydrostatic control loading system provided the following accurate control-feel cues as necessary for FAA Level D qualification:

Elevators (dual load units: Captain, First Officer)

Ailerons (dual load units)

Rudder

Nose wheel steering (dual load units)

Brake pedals (dual load units)

The simulation included appropriate pilot forces and surface deflections. Powered operation was simulated including the effects of aerodynamic forces on the control surfaces. The simulation included accurate reproduction of the following effects as applicable:

Inertia forces

Frictions (coulomb and viscous)

Breakout forces

Centering spring forces

Surface blowdown and float

Aerodynamic forces and q-feel forces

Bob weight

Cable stretch

Loss of hydraulic pressure

Autopilot control and manual override

Deadband

Trim position and rates

Pilot forces

Velocity limits

Travel limits

#### Motion system

The motion system of the test simulator was a 48-inch-stroke hexapod platform with allowable travel of 40 inches for each actuator. The dynamic characteristics of this motion platform met FAA Level D requirements of visual/motion cueing transport delay and bandwidth as shown in Figure 5-2 and Figure 5-3, respectively.

The top curve in Figure 5-2 shows how the back-driven column was manipulated during the test duration to initiate a pitch command. The middle curve shows the pitch-accelerometer response from the simulator. The bottom curve shows the video-signal response due to the pitch command. The transport delays for the motion and visual cues are measured from the initiation of the column command to the motion-system response and the visual-system response. Figure 5-2 indicates that there were a 92.4 millisecond (ms) transport delay in the motion-system response and 130.8 ms transport delay in the visual-system response. Both transport delays comply with the AC 120-40B's (FAA, 1991) performance guideline of 150 ms.

Figure 5-3 shows the acceleration frequency response of the motion system in heave, which indicates that the B747-400 simulator had sufficient bandwidth (9 Hz at 90 degree phase lag) to produce desirable dynamic responses.

Figure 5-2. B747-400 Simulation Cueing Transport Delay Response

Figure 5-3. B747-400 Heave Acceleration Frequency Response

Figure 5-4 illustrates how motion cues are generated for typical ground-based flight simulators. The motion-drive algorithms generate motion-system travel commands corresponding to the airplane states at the pilot station. The motion system follows the motion commands and produces motion cues that pilots perceive in the cockpit. The dynamic characteristics of the motion-drive algorithms and the motion system, therefore, dictate the fidelity of the perceived motion cues.

Figure 5-4. A Typical Motion-Cueing Generation Process For Ground-Based Flight Simulators

The B747-400 simulator at NASA ARC employed a common motion-drive algorithm as shown in Figure 5-5. The translational motion commands are functions of three translational washout filters, i.e., longitudinal, lateral, and vertical, and respective motion-command gains. This is shown in the top row of the diagram, where aircraft acceleration at the center of gravity (acg) is transformed, scaled, limited, high-pass filtered and twice integrated (shown in Laplace transform) to eventually result in simulator surge (xs), sway (ys), and heave (zs). The angular motion commands are functions of three angular washout filters, i.e., roll ((), pitch ((), and yaw ((), and corresponding motion command gains. This is shown in the bottom row of the diagram, where the input from the aircraft model is angular rate ((a/c) and thus needs to be integrated only once. All six motion-command gains are adaptive according to the travels, rates, and accelerations. Low-frequency surge and sway specific forces are generated by tilting the motion system in pitch or roll axis, respectively. This is shown in the middle portion of the diagram.

Figure 5-5. B747-400 Motion-Drive Algorithm

#### Motion tuning

The fidelity of the motion cues, i.e., how well the magnitude and the phase of the motion cues correspond to the airplane response, was critical to the purpose of this study. Therefore, one of the objectives of this effort was to maximize the travels of the B747-400 for the maneuvers selected for this study to achieve the maximum allowable motion-cueing fidelity.

For this purpose, the motion washout filters were adjusted according to the recommendations found in Sinacori (1977), Schroeder (1999), and Mikula, Chung, and Tran (1999). The goal was to maximize actuator travels for the maneuvers for this study, namely, V2 and V1 cut and PIA and SSL. Trade-offs were made to focus on the lateral side forces and heave motion cues, which are the critical motion cues perceived by pilots for these maneuvers, as explained by Bray (1972; see also experimental results described in Schroeder, 1999): “For large aircraft, due to size and to the basic nature of their maneuvering dynamics, the cockpit lateral acceleration cues appear to be much more important than the roll acceleration cues. There was the indication that this observation might be extended to the generalization that in each plane of motion the linear cues are much more valuable than the rotational cues.”

Figure 5-6. Before (empty symbols) and After (filled symbols) High-Pass-Filter Tuning

Before-and-after-tuning motion-cueing fidelity according to Sinacori (1977) and Schroeder (1999) are shown in Figure 5-6. In this figure, the respective gains are given along the x-axis, and the phase distortions on the y-axis. The original configuration is given as empty symbols, and the modified configuration as filled symbols.

The magnitude of the roll-motion cues was traded off to generate lateral side-force cues that would exceed the perceptual threshold of .005-0.01 g (Meiry, 1966; Zaichik, Rodchenko, Rufov, Yashin and White,1999). The reduced roll motion is especially justified given the lack of coordinated translational compensation in the motion-drive algorithm for the erroneous specific force induced by roll motion (Mikula et al., 1999).

The sway specific force, however, was provided by a combination of a high-pass washout filter for the onset cues, and a low-pass tilt for the sustained cues. The comparison between the original configuration and the modified one is shown in Figure 5-7 using a .5 Hz pulse (a pilot control-input frequency observed during V1 cut and V2 cut).

Figure 5-7. Comparison Of Lateral Side Force Before and After Tuning

In what was perhaps the largest tuning trade-off, yaw motion was eliminated for both ground and up-and-away flight conditions. This trade-off was based on Schroeder’s 1999 finding that pilots perceive strong rotational lateral motion cues from translational lateral motion alone. By eliminating yaw motion, the translational motion cues in sway and heave were strengthened, which were deemed more important for the test maneuvers. This was true especially for the engine failures, which cause substantial side forces, and for the vertical upset. Only minor adjustments were made to the pitch and longitudinal motion axes.

#### Simulator calibration

All four FAA Level D certification quarterly checks for the B747-400 simulator were performed prior to the start of the experiment, thus covering the entire FAA Qualification Test Guide. Test results showed full compliance with FAA performance guidelines. The morning-readiness test provided by the simulator manufacturer, which checked visual, instruments, lights, control, sound, and motion, was run on a weekly basis. Functional checks of the simulator, which included control loading, motion, visual, Flight Management System, autopilot, and radio communication were performed manually every morning prior to the test. In addition, an automated approach and landing with full simulator systems was flown every morning to ensure the motion-system performance was consistent throughout the experiment. The time trace of this automated daily calibration check is shown in Appendix 2. The FAA inspected the B747-400 simulator in early March and the Level D certification was renewed on March 12, 2002.

### Participants

#### Pilots Flying (PF)

Data were collected from 40 currently qualified Boeing 747-400 captains and first officers volunteering for the study. They were compensated for their expenses and time. Because the experiment was a between-subjects design, they were counterbalanced across the two motion conditions to avoid any spurious effects due to differences in the seat occupied during flying (captains left, first officers right), experience (low vs. high, the latter defined as more than 14 landings flown in the airplane in the past year), and Pilot-Not-Flying (PNF, one of two).

Total flight hours for the PFs in the experiment (20 Motion and 20 No-Motion) averaged 12,144. The average for the Motion group was 12,755 hours compared to 11,534 in the No-Motion group. The number of hours in the B747-400 airplane averaged 2,025 for the combined groups, with 2,260 hours for the Motion and 1,790 for the No-Motion group. The average number of landings in the past 12 months was 19 and 17 for the Motion and No-Motion groups, respectively.

Pilots were briefed orally and in writing that the overall purpose of the experiment was to improve simulator design for training and evaluation of airline pilots. They were informed that they would be flying challenging maneuvers to test different simulator configurations and specifically told to fly the flight director and/or guidance systems as precisely as possible. Also, they were informed that they would fly in the vicinity of a specific airport and were given airport, weather, and airplane information on the reverse side of the pilot briefing page (Appendix 3). The latter information was briefed by the PNF just before starting the experiment. They were told that they would be given a chance to practice the maneuvers with graphical feedback on their flight-path precision and were shown generic feedback displays depicting the performance criteria. For the best performances, an award was promised. They were given complete responsibility and command of the airplane and told that the PNF would only follow commands.

They were also given a schedule of approximate flying, questionnaire, break and refreshment times. They were asked to hold any comments for the questionnaires. Finally, they were asked to use discretion and not discuss the experiment with their colleagues, so that new participants would be fresh to the experiment.

#### Pilots Not Flying (PNF)

The PNFs were two retired airline pilots, one a former B747-200 Captain, the other a former B767 Captain. They were familiar with the purpose of the experiment, the simulator and the maneuver sequence flown, but they were not informed on the motion configuration. They were instructed to assist the pilot flying as requested in all non-flying duties, but not to initiate any actions.

#### Air Traffic Controller (ATC)

A retired air route traffic control center controller who was also responsible for running the simulator impersonated ATC. Instructions were kept as simple as possible. The script used by ATC can be found in Appendix 4.

### Procedures

An experiment run could last up to seven hours including lunch, dependent on the smoothness of the runs and the time it took to complete the questionnaires. Pilots were asked to arrive at eight o’clock in the morning and started the day with refreshments and paperwork. They were assigned to the Motion or No-Motion group based on their experience and on the seat they were flying from. They were briefed on the experiment and shown sample performance-feedback displays to motivate them to fly as precisely as possible. The detailed experiment protocol can be found in Appendix 5.

During Evaluation, which tested the effect of motion on reverse-transfer of skills from the airplane to the simulator, and Quasi-Transfer Testing, which tested the effect of motion on transfer from the simulator to the simulator with motion as a stand-in for the airplane, the pilots flew two full scenarios consisting of a takeoff with an unrecoverable engine failure from DFW runway 36 Right followed by a loop around the airport to land on runway 36 Left or Right. After completion of the two scenarios, the PF and PNF returned to the briefing room and completed the first questionnaire. For the PF, this consisted mainly of an evaluation of the simulator. The PNF evaluated the PF (see Appendix 6 for all PF questionnaires and Appendix 7 for all PNF questionnaires).

During Training, pilots flew each maneuver three times in a row, with the opposite engine failed compared to Evaluation. The maneuver training sequence was counterbalanced across groups to control for sequence effects. Each pilot within a group experienced a different one of the 4!=24 possible sequences, and the same 20 sequences were used in each group. Pilots were told which maneuver to expect to enhance the effect of practice. Each training-maneuver run was followed by a display of the main performance variables specified in the PTS as a function of distance from the runway, with “perfect” flight precision given as a reference. After completion of Training, pilots returned to the briefing room to fill out another questionnaire.

During Quasi-Transfer Testing, pilots repeated the scenarios tested during Evaluation, now all with motion. The same engine was failed as during Evaluation. After having flown both scenarios, a third questionnaire was administered to both pilots in the briefing room. Then, the two scenarios were repeated one last time, followed by a final questionnaire. Pilots were thanked and encouraged to send their colleagues, without informing them about the details of the experiment. The experiment phases are outlined below.

Morning: Evaluation and Training with motion on or off dependent on group

# Phase I: Evaluation

Evaluate Scenario 1: V2 cut (Engine 1) followed by PIA

Evaluate Scenario 2: V1 cut (Engine 4) followed by SSL

PF and PNF complete PF and PNF Questionnaire 1

Briefing on feedback displays using display copies printed during the last maneuver

Phase II: Training

Train 3 V2 cuts, PIAs, V1 cuts, SSLs, failing the opposite engine

Show feedback displays after each individual maneuver

PF and PNF complete Questionnaire 2

Lunch

Afternoon: Quasi-Transfer Testing with motion on for all

# Phase III:  Quasi-Transfer Testing

Test 1

Quasi Transfer to motion Scenario 1

Quasi Transfer to motion Scenario 2

PF and PNF complete Questionnaire 3

Test 2

Quasi Transfer to motion Scenario 1

Quasi Transfer to motion Scenario 2

PF and PNF complete PF Final Questionnaire and PNF Questionnaire 4

### Performance Feedback Displays

After each training maneuver, pilots were shown, on the navigation display screen, the flight profile of the maneuver just performed in comparison with the ideal profile and the boundaries defined in the FAA PTS. The PTS performance criteria are described in 5.3.1.1. Pilots could take as much time as they needed to assess their performance and strategize on how to improve it.

#### Takeoff feedback displays

Takeoff performance feedback for the V2 and the V1 cuts was given as a function of distance from the runway on two pages displayed in sequence. The x-axis ranged from minus one to plus three nautical miles longitudinal distance from the runway threshold. The engine-failure location was marked with a red arrow. The first page showed heading deviation and airspeed deviation, the second page showed bank angle and altitude. Where applicable, the tolerances defined in the PTS were marked with a green line. The airplane’s time trace was shown as a dotted line from start to reaching an altitude of 800 ft AGL. The dots were magenta as long as the airplane was within tolerances, and turned red once the tolerances were exceeded.

Page 1: Heading and airspeed deviation

Page 1 is shown in Figure 5-8. The heading deviation plot y-axis ranged from plus to minus 10 degrees deviation from takeoff heading. Two solid green lines indicated the range of desired performance of plus/minus 5 degrees.

The airspeed deviation plot y-axis ranged from plus to minus 10 knots deviation from the desired speed, which was V2 + 10 knots for the V2 cut and V2 for the V1 cut (160 and 150 knots, respectively). Two solid green lines indicated the range of desired performance of plus/minus 5 knots.

Figure 5-8. Feedback for Takeoff Heading and Speed

Page 2: Altitude and bank-angle plot

Page 2 is shown in Figure 5-9. The altitude profile y-axis ranged from zero to 1000 ft in 250 ft intervals. No PTS are available or given.

The bank-angle plot y-axis ranged from 10 degrees bank angle to the right to 10 degrees to the left, with the origin at zero degrees bank angle/3 nm from runway threshold. Plus/minus 5 degrees bank angle were given in dashed green as a reference (see 5.3.1.1 for the PTS for banking performance).

Figure 5-9. Feedback for Takeoff Altitude and Bank Angle

#### Approach and landing performance feedback displays

The approach and landing performance feedback for the PIA and SSL was given on one page, containing three plots showing glide path, localizer, and approach-speed deviation (see Figure 5-10). The x-axis again showed longitudinal distance from runway threshold, ranging from plus four to minus two nautical miles. A red arrow indicated the point of landing. The airplane performance was shown as a green dotted line when within PTS. Outside of PTS criteria, the dotted line turned red.

Glide-path and localizer deviations were shown as plus/minus one dot on the y-axis. Plus/minus one dot was also shown as the performance criterion (this time in white). For the glide path, the dots represented altitude, resulting in an altitude profile view. For the localizer, the dots represented horizontal distance from the runway centerline, resulting in a bird’s eye view. The plus/minus one dot criterion is more lenient than the PTS criterion of plus/minus 0.5 dot, to compensate for the added difficulty of mandatory removal of the flight director during the maneuvers.

The speed deviation plot showed a range of plus/minus 20 knots deviation from the speed selected by the pilots on the Mode Control Panel on the y-axis. Compliance with the PTS was indicated by the dotted airplane performance curve turning red when the criterion of plus/minus 5 knots was violated.

Figure 5-10. Feedback on Glide Path, Localizer, and Approach Speed Deviation

### Data Collection

#### Simulator data

During each run of the experiment, variables that were considered useful for assessing the simulator performance, pilot performance, and pilot control activities, were recorded from the simulator computer at 30 Hz sampling rate. The list of the recorded variables is given in Appendix 8.

The statistics of some variables were also generated immediately after each run. These statistic data were saved in an Excel compatible text file. Note that the statistics calculations were done for each segment of a maneuver. The segments used in the maneuver analysis will be described in the 5.3.1.

#### Questionnaires

As described in 5.2.5, PFs and PNFs completed questionnaires immediately after each phase of the experiment, i.e., Evaluation, Training, and Quasi-Transfer Testing 1 and Quasi-Transfer Testing 2. Pilots were asked to relate the questionnaires only to the maneuvers flown or observed so far or since the last break.

PF questionnaires

The purpose of the PF questionnaires was to tap Boeing 747-400 pilots’ expertise with regard to the Control Feel, Control Sensitivity, Handling Qualities, and overall Acceptability of the simulator. They were asked to assess their Control Strategy and Technique, Performance, and ease of Gaining Proficiency. They were also asked the Comfort and Workload experienced in the NASA simulator. As appropriate, PFs were asked compare these assessments to the airplane and in some cases to the last simulator flown. Finally, PFs were asked whether any “other” cues did not correspond to the airplane, without directly naming visual, auditory, or motion cues. Where appropriate, the questions were asked separately for each control and each maneuver. It was acknowledged that the PFs may not have experienced some of the maneuvers in the airplane, but they were asked to use their overall experience with the airplane to develop an expectation on how the airplane would have “behaved” during the maneuver. Most questions were asked on a scale from one to seven, with one anchored as “much worse,” four “the same” and seven “much better” than the (aircraft). All PF questionnaires are reproduced in Appendix 6.

The questionnaires after the Evaluation (PFQ1) and Quasi-Transfer Training 1 (PFQ3) were identical, with the exception that PFQ3 had one additional page on Gaining Proficiency. The questionnaire after Training, PFQ2, was an abbreviated version of PFQ1, asking first for an overall rating and then for an indication as to which control or maneuver the judgment applies to. During analysis, the responses were translated into the same format as PFQ1. In general, responses consisted of checkmarks with the opportunity to add comments, with the exception of the final questionnaire, PFQfinal, which asked for open-ended responses to all aspects previously covered.

PNF questionnaires

PNFs were asked to rate the PFs’ Control Performance, Control Strategy and Technique, Physical Workload and, in the questionnaire after training, ease of Gaining Proficiency. Specifically, they were asked, on a seven-point scale, whether, e.g., the PFs “performance” was “much worse (1),” “the same (4),”or “much better (7)” than the “performance” of the average pilot. When considering the results of the PNF questionnaires, the fact that PNFs in this study knew that the motion configuration of the simulator served as the main independent variable must be kept in mind. Although the motion status was concealed from both pilots, PNFs awareness of it for each particular experimental run may have been heightened through that knowledge, resulting in a potential for bias. PNFs were counterbalanced across motion conditions, taking into account PF experience and seat, to control for potential differences in bias between the PNFs. All PNF questionnaires are reproduced in Appendix 7.

## Results Based On Simulator Recordings

### Data Analysis

#### Performance standards

One critical question with regard to analyzing the results of the experiment is what performance criteria to apply. The following guidance for each maneuver was found in the FAA’s Practical Test Standards (FAA, 2001).

Engine failures with continued takeoff

The PTS require that desired heading is maintained within plus/minus 5 degrees, and desired airspeed within plus/minus 5 knots. With regard to bank angle, it is recommended that a bank of approximately 5 degrees toward the operating engines is established, as appropriate for the airplane flown.

Engine-out approaches

In flight, the PTS for multiengine airplanes require that with an engine failure, positive airplane control and coordinated flight are maintained, with a bank angle of approximately 5 degrees, as required, and proper trim for that condition. Altitude, airspeed, and heading have to be within plus/minus 100 ft, 10 knots, and 10 degrees, respectively. Touchdown should be 500 to 3000 feet past the runway threshold, not to exceed one third of the runway length. The runway centerline has to be between the main gears.

For hand-flown PIAs and SSLs with an engine failure, a one-dot deflection from the localizer/glide slope indicators is tolerated. However, in the following analysis, localizer/glide slope exceedance calculations were based on half-dot (one-quarter scale) deflections from the on-localizer or on-glide slope position.

Engine-out landings

Again, a bank of approximately 5 degrees to maintain coordinated flight is permitted. Prior to beginning the final approach segment, pilots are to maintain the desired altitude, airspeed, and heading within plus/minus 100 ft, 10 knots, and 5 degrees. During the stabilized approach, desired airspeed/V-speed is to be maintained within plus/minus 5 knots.

### Success Rates

Only data from successful trials were included in the analyses. A successful trial was defined as one without loss of control or abnormal ground contact (such as a wing or tail scrape). To be considered a success, takeoff maneuvers must also have been flown within four standard deviations (STD) of the mean maximum heading and bank deviation, while landing maneuvers must have been flown within four STDs of the mean maximum GS or LOC deviations found in the data. In calculating the success rate, missed approaches were excluded from the number of total maneuvers. As can be seen in Figure 5-11, the success rates of the two groups across maneuvers and phases were remarkably similar, with no significant Group differences (Fisher’s Exact p>.5 for all maneuvers in all phases).

Figure 5-11. Success Rates by Phase and Maneuver

### Performance and Behavior During Maneuvers

For the purpose of the data analyses, the maneuvers were divided into several flight segments. For each segment, a list of critical variables considered discriminative of pilot performance/behavior for the flying task of that particular flight segment was developed. The division of a maneuver into several flight segments was necessary because each segment requires a different set of variables to capture descriptive pilot flight-precision performance and behavior.

The segments used in the current analysis are as follows:

For engine failure on takeoff (V1 cut and V2 cut):

After engine failure to 800 ft AGL

For Precision Instrument Approach:

From final Approach-Fix to Decision-Height (1020 ft MSL)

From Decision-Height to Touchdown

For sidestep landing:

From final Approach-Fix to Breakout-of-Clouds (1688 ft MSL)

From Breakout-of-Clouds to Upward-Gust (2 nm from runway threshold)

From Upward-Gust to Touchdown

The list of measures calculated for each segment can be found in Appendix 9

#### Types of measures

Generally, the measures used in the analysis can be categorized into measures related to pilot-vehicle flight-precision performance (performance measures) and measures relating to pilot control actions (behavior measures). The list of measures for each maneuver and flight segment and their definitions are given in Appendix 9. Most of these measures were calculated from the time-history data recorded during the experiment. Some behavior measures, however, were derived from frequency domain analyses, specifically power spectrum analyses. This was necessary to capture pilot-response characteristics such as the frequency bandwidth of a pilot’s control inputs, which is defined as the frequency below which half of the control-input power occurs. All the calculations were done using SASTM.

#### Data analysis procedure

Only data from successful trials were included in the analysis. The criteria for a successful trial can be found in the section on Success Rates (5.3.2). This led to the exclusion of less than 2.2 percent of trials in each group.

Given the physics of airplane motion and the characteristics of human pilot control, the performance and behavior measures discussed above are interrelated. Therefore, multivariate analysis of variance (MANOVA) was used to examine the effects of the independent variables of the experiment. The use of MANOVA instead of multiple univariate analyses of variance (ANOVA) was also intended to reduce the possibility of Type I error, i.e., a false rejection of the null hypothesis that motion has no effect. MANOVAs were performed on each flight segment separately. All the analyses included dependent variables to assess performance and behavior in all axes, which were derived from the measurements of heading deviation, bank angle, pitch angle, roll rate, yaw rate, airspeed deviation, wheel response, pedal response, and column response. In some cases, additional dependent variables were used as necessary, e.g. reaction time based on pedal response in takeoff maneuvers, and localizer and glide slope deviations in landing maneuvers. Although MANOVA is specifically designed to handle multiple correlated dependent variables, too many highly correlated dependent variables will result in a loss of degrees of freedom and power. This, in turn, will increase the probability of Type II errors, i.e., a false acceptance of the null hypothesis that motion has no effect. Hence, first a correlation analysis was performed to examine the interdependency of the measures. Only one representative from two or more highly correlated (r>.85) variables was then entered into MANOVA to preserve its power.

The main analysis involved a two-way MANOVA to examine the effect of the independent variables Group (Motion vs. No-Motion) by Phase (Evaluation, Training, Transfer) on the dependent variables. Interactions between Group and Phase were examined with two separate one-way MANOVAs on each group with Phase as the independent variable. A third set of MANOVAs examined the effect of Group and, where applicable, Trial separately for each phase, resulting in a one-way MANOVA for Evaluation and in two-way MANOVAs for Training (2 Groups by 3 Trials) and Transfer (2 Groups by 2 Trials). Because no effects of, or interactions with, Trial were found, no further analyses were warranted for the effect of the trial variable. Significant MANOVAs were followed up by univariate ANOVAs on the chosen variables. Differences between means were analyzed with Bonferroni t tests. All analyses were performed in SASTM.

Any difference with a probability to have occurred by chance of lower than 5 percent (p<.05) was considered a statistically significant effect (note that statistical significance is not necessarily synonymous with operational relevance). Probabilities of lower than 10 percent were considered a trend (p<.10). In Phase III, the data for Tests 1 and 2 were collapsed, because no statistically significant differences were found between them. Phase II was treated similarly, collapsing the data for all the successful training trials of each maneuver. Although results from all segments are presented, the emphasis will be on the results from the most critical flight segment of each maneuver.

It should also be mentioned that of the four statistics commonly used to evaluate the MANOVA results (Wilks’ Lambda, Pillai’s Trace, Hotelling-Lawley Trace, and Roy’s Greatest Root), only Wilks’ Lambda is reported. These four statistics did not yield exactly the same values, but they agreed with each other in terms of the level of significance or p-value.

The purpose of these analyses is to answer the following questions:

Did the Motion and the No-Motion groups differ in flight-precision performance and/or control activities?

Was there improvement across the different phases of the experiment?

Did this improvement quasi-transfer to the simulator with motion as a stand-in for the airplane?

Was there a difference in improvement and quasi transfer as a function of Group?

Successful quasi transfer was defined as having been achieved if any of the following results was found:

Significant improvement between Phase I (Evaluation) and Phase III (Quasi-Transfer Testing), but no differences between Phase I and Phase II (Training) and Phase II and Phase III, indicating that there must have been some improvement between Evaluation and Training that did quasi-transfer, but that additional improvement during Quasi-Transfer Testing was needed to result in significant improvement from Evaluation

Significant improvement between Phase I and Phase II, and I and III (Quasi-Transfer Testing), indicating that the improvement achieved during Training has quasi-transferred without additional improvement during Quasi-Transfer Testing.

Significant improvement from Phase I to Phase II, and no differences between II and III and I and III, indicating that some, but not all of the improvement during Training has quasi-transferred

Significant improvement between Phase I and II, and II and III, and thus also between I and III, indicating that the improvement during Training has quasi-transferred, and that additional improvement has been achieved during Quasi-Transfer Testing

#### Resolution (Power)

It is very important for consideration of experimental results to know whether the data gathered was consistent enough to reveal an operationally relevant effect (resolution of the study). The detectable effect size can be assessed using power analysis. The power of an experiment to reveal a relevant effect is directly proportional to the size of such effect and the number of subjects in each compared group, and indirectly proportional to the variability between subjects within each group. A finding of no difference between two groups does not necessarily mean that the difference is absent, but that the difference may be small enough to be masked by the variability of subjects within groups. For this study, the resolution of the analysis was inferred by calculating the required size of an effect to reach a power level of .80. That means that the effect size was defined as the minimum difference between the standardized means that will lead to the rejection of the null hypothesis with a probability of .80.

| Maneuver | Measure | Effect Size |
| --- | --- | --- |
|  |  | Group | Phase |
| V2 Cut | STD bank | 1.45 deg | 1.72 deg |
|  | STD HDG deviation | .75 deg | .89 deg |
|  | Pedal RT | .43 s | .51 s |
| V1 Cut | STD bank | .52 deg | .61 deg |
|  | STD HDG deviation | .51 deg | .59 deg |
|  | Pedal RT (s) | .18 s | .22 s |
| PIA | STD GS deviation | .07 dot | .08 dot |
|  | STD LOC deviation | .14 dot | .17 dot |
| SSL | STD GS deviation | .07 dot | .08 dot |
|  | STD LOC deviation) | .11 dot | .13 dot |

Table 5-1. Detectable Group and Phase Effect

In this study, power analyses were done on the dependent variables that were related to the variables presented to pilots as feedback on their performance during the training phase. Only the data from the most important flight segments were considered, namely, the segment after engine failure during takeoffs and the segment before reaching decision height for PIA and before touchdown for SSL. Table 5-1 summarizes the group and phase effect sizes for the analyses done here.

These calculations show that the analyses could detect sufficiently small group or phase differences. Therefore, this study should serve the purpose of capturing the operationally relevant effects.

#### V2 cut

For this maneuver, the dependent variables used in the MANOVA are as follows (15 variables):

Performance

STD and average failure-induced heading deviation (average of heading deviation in the direction of the failed engine)

STD bank angle

STD pitch angle

Average airspeed exceedance (average of airspeed exceeding the plus/minus 5 knots about the desired airspeed)

Behavior

Pedal reaction time

Root mean square (RMS) and number of reversals of column, wheel, and pedal responses

Response bandwidth of the column, wheel, and pedal actions (frequency below which the corresponding power spectral density curves are .5 of total area)

The V2 cut was affected by Group and Phase. This means that pilots performed and behaved differently dependent on whether they received or didn’t receive motion cues or whether they had been trained with or without motion cues. It also means that they were affected by the Phase of the experiment they were in, i.e., whether they had just come fresh from the airplane and were evaluated in the simulator, were being trained in the simulator knowing which maneuver was to come and were provided with feedback, or had quasi-transferred to the simulator with motion on for all for final testing. However, the Group and Phase variables also significantly interacted with each other, which means that Group effects were depended on the Phase and vice versa. The overall statistics for the V2 cut are, Wilks’ Lambda (=.66, F(15,99)=3.35 (Group) and (=.31, F(30,198)=5.23 (Phase), both p<.0001; interaction (=.65, F(30,198)=1.59, p<.05.

The effect of Group on three of the 15 variables interacted with Phase (F(2, 113)(3.88, p<.05). Table 5-2 shows the Group effects for each phase. The Motion-trained group activated the pedal 0.76 s slower in response to the engine failure than the No-Motion group, but this effect emerged only at Quasi Transfer, when both groups received motion cues. Also only during Quasi-Transfer Testing, the Motion group had a 0.28 inch (in) higher column RMS than the No-Motion group. Finally, the Motion group reversed the pedal 0.45 times more often than the No-Motion group during Evaluation, but this effect disappeared during Training and did not re-emerge at Quasi Transfer.

| Variable | Phase | Mean | Stats |
| --- | --- | --- | --- |
|  |  | Motion | No-motion | F | p |
| Pedal-reaction time (s) | I | 3.40 | 3.77 | (1,38)=1.81 | .19 |
|  | II | 2.49 | 2.30 | (1,111)=1.16 | .28 |
|  | III | 3.10 | 2.34 | (1,71)=8.69 | .004 |
| Pedal reversals | I | 1.50 | 1.05 | (1,38)=9.68 | .004 |
|  | II | 1.29 | 1.31 | (1,111)=.04 | .83 |
|  | III | 1.49 | 1.61 | (1,71)=.75 | .39 |
| RMS column (in) | I | 1.17 | 1.23 | (1,38)=.40 | .53 |
|  | II | .99 | 1.03 | (1,111)=.49 | .48 |
|  | III | 1.14 | .86 | (1,71)=10.22 | .002 |

Table 5-2. V2 Cut Group Effects by Phase (shading indicates significant group difference)

Table 5-3 shows the effects of Phase for each group. Both groups lowered their pedal-reaction time during Training. However, this improvement quasi-transferred for the No-Motion group only. Also only the No-Motion group increased its pedal activity (more pedal reversals) and lowered its column activity (lower RMS column) between Evaluation and Quasi-Transfer Testing.

| Variable | Group | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F | p |
| Pedal-reaction time (s) | Motion | .90* | -.60 | .30 | (2,56)=6.49 | .003 |
|  | No-Motion | 1.47* | -.13 | 1.34* | (2,57)=18.27 | <.0001 |
| Pedal reversals | Motion | .22 | -.24 | -.03 | (2,56)=1.41 | .25 |
|  | No-Motion | -.26 | -.29 | -.55* | (2,57)=8.10 | .0008 |
| RMS column (in) | Motion | .18 | -.14 | .04 | (2,56)=1.76 | .18 |
|  | No-Motion | .21 | .17 | .37* | (2,57)=9.67 | .0002 |

* indicates significant difference (p<.05)

Table 5-3. V2 Cut Phase Effects by Group

Group, regardless of Phase, affected three control related variables (Table 5-4). The Motion group demonstrated higher wheel activity (RMS, reversals) and lower pedal-response bandwidth.

Seven variables were affected by Phase regardless of Group (Table 5-5). Heading STD and average failure-induced heading deviation improved during Training, but the improvement did not quasi-transfer. This was true also for bank STD and wheel RMS. A pedal RMS decrease during Training quasi-transferred, but some of the improvement was lost. The increased wheel and pedal-response bandwidths found during Training compared to Evaluation were exhibited during Quasi-Transfer Testing for pedal only.

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,113) | p |
| Wheel reversals | 3.27 | 2.53 | 14.46 | .0002 |
| RMS wheel (deg) | 6.97 | 5.44 | 16.05 | .0001 |
| Pedal-response BW (Hz) | .04 | .05 | 4.84 | .03 |

Table 5-4. V2 Cut Group Differences

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,113) | p |
| STD HDG (deg) | 3.66 | .85* | -.96* | -.11 | 5.29 | .01 |
| Failure-induced HDG (deg) | 5.47 | 5.40* | -4.03* | 1.37 | 23.92 | <.0001 |
| STD bank (deg) | 5.69 | 1.54* | -1.71* | -.16 | 4.54 | .01 |
| RMS wheel (deg) | 6.20 | 1.22* | -1.15* | .07 | 4.38 | .01 |
| Wheel response BW (Hz) | .063 | -.02 * | .01 | -.01 | 3.16 | .05 |
| RMS pedal (in) | 1.07 | .19* | -.11 | .08 | 7.61 | .0008 |
| Pedal-response BW (Hz) | .04 | -.02* | .001 | -.02* | 10.63 | <.0001 |

* indicates significant difference (p<.05)

Table 5-5. V2 Cut Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Summary

Motion did not appear to alert of the engine malfunction for the V2 cut. On the contrary, the Motion group slowed down its pedal response compared to the No-Motion group at Quasi Transfer, losing two-thirds of the improvement it had gained during Training, possibly due to fatigue. Only the No-Motion group, which may have been refreshed by the emergence of motion (the so-called Hawthorne effect, Homans, 1958), fully quasi-transferred the pedal-reaction time improvement achieved during Training. Nevertheless, there were only behavioral differences between the two groups, performance doesn’t appear to have been affected by the presence or absence of Motion during any of the phases.

Of seven (counting also an increase in pedal-response bandwidth) variables that had significantly improved between Evaluation and Training regardless of Group, four significantly deteriorated during Quasi-Transfer Testing compared to Training. This may be another indication of fatigue.

During Evaluation only, the Motion group had more pedal reversals. This difference was lost across the experiment because the No-Motion group significantly increased its reversals between Evaluation and Quasi-Transfer Testing. The Motion group generally had a lower pedal-response bandwidth. Wheel activity was generally higher for the Motion group regardless of Phase. Unlike the Motion group, the No-Motion reduced its column activity between Evaluation and Quasi-Transfer Testing.

#### V1 Cut

In addition to the dependent variables used in the V2 cut analysis, four more variables are used in the MANOVA for the V1 cut maneuver (resulting in a total of 19 dependent variables):

Additional performance variables

Average heading exceedance (average of the heading deviation exceeding ( 5( around the desired heading direction)

Average failure induced bank angle (average of bank angle in the direction of the failed engine)

Additional behavior variables

Roll and yaw activities (average of absolute roll and yaw rates)

The overall effects of Group and Phase were again significant (Wilks’ Lambda (=.47, F(19,92)=5.47 (Group) and (=.41, F(38,184)=2.74 (Phase), both p<.0001), and, just as for the V2 cut, interacted significantly with each other ((=.56, F(38,184)=1.63, p=.02). This showed that for some of the dependent variables, the effects of one independent variable depended on the level of the other independent variable.

For five of the 19 dependent variables, Phase and Group interacted with each other (F(2,110)(4.13, p<.05), and for one (STD heading), there was a trend of interaction (F(2,110)=2.59, p<.10). Table 5-6 shows the effects of Group for each phase. The Motion group responded 0.4 s and 0.3 s faster to the engine failure than the No-Motion group during Evaluation and Training, respectively. This difference disappeared when all pilots quasi-transferred to motion. It may be this decrease in pedal-reaction time that allowed the Motion group to apply lower pedal RMS and higher pedal-response bandwidth than the No-Motion group before quasi-transferring to all motion. Some other Group effects that appeared during Evaluation only were lower yaw activity, lower pitch STD, and lower heading STD for the Motion group (although this latter finding is weakened by the fact that for heading STD, there was only a trend of an interaction between Phase and Group, which renders the follow-up Bonferroni tests questionable).

| Variable | Phase | Mean | Stats |
| --- | --- | --- | --- |
|  |  | Motion | No-motion | F | p |
| Pedal-reaction time (s) | I | 1.53 | 1.92 | (1,34)=5.02 | .03 |
|  | II | 1.40 | 1.68 | (1,110)=14.72 | .0002 |
|  | III | 1.46 | 1.42 | (1,74)=2.18 | .14 |
| STD heading (deg) | I | 2.28 | 3.04 | (1,34)=4.34 | .04 |
|  | II | 2.41 | 2.59 | (1,110)=.97 | .33 |
|  | III | 2.14 | 1.93 | (1,74)=1.16 | .28 |
| Yaw activity (deg/s) | I | .55 | .79 | (1,34)=7.26 | .01 |
|  | II | .60 | .66 | (1,110)=2.17 | .14 |
|  | III | .56 | .50 | (1,74)=1.59 | .21 |
| STD pitch (deg) | I | 5.63 | 6.40 | (1,34)=7.21 | .01 |
|  | II | 6.43 | 6.44 | (1,110)=.00 | .96 |
|  | III | 6.39 | 6.12 | (1,74)=3.73 | .06 |
| RMS pedal (in) | I | .62 | .77 | (1,34)=21.53 | <.0001 |
|  | II | .60 | .70 | (1,110)=51.64 | <.0001 |
|  | III | .61 | .61 | (1,74)=.05 | .83 |
| Pedal-response BW (Hz) | I | .11 | .08 | (1,34)=9.42 | .004 |
|  | II | .11 | .09 | (1,110)=17.58 | <.0001 |
|  | III | .12 | .12 | (1,74)=.38 | .54 |

Table 5-6. V1 Cut Group Effects by Phase (shading indicates significant group difference)

Phase effects for each group are shown in Table 5-7. The Motion group lowered its pedal-reaction time during Training, but this effect did not quasi-transfer completely. At the same time, the Motion group had increased pitch STD during Training and this effect fully quasi-transferred. The No-Motion group did not lower its pedal-reaction time during Training, but lowered it significantly during Quasi-Transfer Testing in the simulator with motion. With lower pedal-reaction time at Quasi Transfer, the No-Motion group also improved heading and yaw control (reducing STD heading and yaw activity), lowered pedal RMS, and increased pedal-response bandwidth compared to the earlier phases.

| Variable | Group | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,55) | p |
| Pedal-reaction time (s) | Motion | .13* | -.06 | .07 | 4.81 | .01 |
|  | No-Motion | .22 | .29 | .50* | 5.68 | .006 |
| STD heading (deg) | Motion | -.20 | .30 | .09 | .46 | .63 |
|  | No-Motion | .45 | .60 | 1.04* | 6.82 | .002 |
| Yaw activity (deg/s) | Motion | -.07 | .06 | -.01 | .51 | .60 |
|  | No-Motion | .12 | .16 | .28* | 8.73 | .0005 |
| STD pitch (deg) | Motion | -.81* | .05 | -.76* | 8.95 | .0004 |
|  | No-Motion | -.01 | .34 | .33 | 1.54 | .22 |
| RMS pedal (in) | Motion | .02 | -.01 | .01 | .48 | .62 |
|  | No-Motion | .07* | .10* | .17* | 24.44 | <.0001 |
| Pedal-response BW (Hz) | Motion | .002 | -.0005 | .002 | .01 | .99 |
|  | No-Motion | -.006 | -.03* | -.04* | 16.57 | <.0001 |

* indicates significant difference (p<.05)

Table 5-7. V1 Cut Phase Effects by Group

Three variables showed Group differences regardless of Phase (Table 5-8). The Motion group used the wheel more aggressively (more reversals, higher RMS), but had fewer pedal reversals throughout.

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,110) | p |
| Wheel reversals | 5.72 | 4.49 | 11.74 | .0009 |
| RMS wheel (deg) | 3.99 | 3.41 | 5.68 | .02 |
| Pedal reversals | 1.16 | 1.45 | 11.60 | .0009 |

Table 5-8. V1 Cut Group Differences

Two roll variables improved across Phase regardless of Group (Table 5-9). Failure-induced bank increased during Training, but decreased at Quasi Transfer. Roll activity decreased at Quasi Transfer.

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,110) | p |
| Failure-induced bank (deg) | 1.20 | -.44* | .54* | .10 | 9.55 | .0001 |
| Roll activity (deg/s) | 1.36 | .11 | .10 | .20* | 3.14 | .05 |

* indicates significant difference (p<.05)

Table 5-9. V1 Cut Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Summary

Pilots did use the motion cues to speed up their pedal-response time to the V1 cut, for which a timely response is critical to prevent scraping the tail or a wing. However, although the No-Motion pilots were unable to significantly improve their response time even when they were told that an engine and even which engine would fail during Training, they immediately did use the motion cues to speed up their pedal response once available during Quasi-Transfer Testing. As might be expected, the faster pedal-reaction time of the Motion group compared to the No-Motion group during Evaluation and Training had beneficial effects on the Motion group’s control performance and behavior.

Like for the V2 cuts, the Motion group was generally more active with regard to the aileron wheel. Unlike for the V2 cut, however, the Motion group had fewer pedal reversals, even at Evaluation. Unlike for the V2 cut as well, motion seemed to induce higher pedal-response bandwidth for the Motion group, and for the No-Motion group when motion cues were made available during Quasi-Transfer Testing. General improvement regardless of Group was limited to roll variables.

Comparison with First Study

As described in Appendix 1, the same dependent variables as in the Second Study were analyzed for the V1 cut of the First Study, except that average heading exceedance was omitted as it was heavily correlated (r>.85) with the other two heading variables. As in the Second Study, there was a significant overall Phase effect, but the overall Group effect was only marginal and there was no interaction between the overall Group and Phase effects. Table A1-3 shows that regardless of Group, general improvement was observed on bank and pitch performance as well as reduction in lateral-directional control activities at Quasi Transfer. For the Second Study, improvement was limited to roll variables.

Table A1-2 shows the results of further examining the Group effect—however the fact that the overall MANOVA for Group was only marginally significant needs to be kept in mind when considering these results. Throughout all phases, i.e., even during Quasi Transfer to the simulator with motion, the No-Motion pilots reversed the aileron wheel slightly more often, but with a lower bandwidth, than the Motion pilots. In contrast, they reversed the pedal slightly less frequently than the Motion pilots. There was no difference in how fast they activated the pedal (or the wheel) after engine failure. This shows that the motion cues in the First Study only affected (albeit only marginally) pilots’ lateral-directional control activities. Interestingly, although differences between groups on wheel and pedal reversals were also found in the Second Study, the pattern was opposite: the Motion group had fewer pedal reversals and more wheel reversals than the No-Motion group. Potential explanations for these differences are the dynamics of the simulated airplane and the difference in simulator motion performance.

#### Precision Instrument Approach

Approach-Fix to Decision-Height

The Approach-Fix to Decision-Height (Fix-to-DH) flight segment was considered the most important for the Precision-Instrument-Approach maneuver, because in this segment the pilots had to track glide slope and localizer closely with disturbances from shifting cross winds. The MANOVA for this segment used 17 dependent variables as follows:

Performance

STD heading deviation

STD bank angle

STD pitch angle

Average airspeed exceedance

STD and average exceedance of glide slope and localizer deviations (average of integral of deviations exceeding plus/minus .5 dot)

Behavior

RMS and number of reversals of column, wheel, and pedal responses

Column, wheel, and pedal-response bandwidths

For the Fix-to-DH segment, both overall Group and Phase effects were significant (Wilks’ Lambda (=.71, F(17,88)=2.10 and (=.57, F(34,176)=1.68, respectively, both p<.05). There was no interaction between Phase and Group [(=.77, F(34,176)<1; p>.10]. This means that any Group effects for the Precision Instrument Approach Fix-to-DH occurred during all three phases, and that any Phase effects occurred for both groups. Most importantly, this means that any effects found due to the motion condition persisted even when the No-Motion group quasi-transferred to motion.

The Group variable significantly affected seven of the 17 dependent variables examined. Table 5-10 presents these results collapsed over phases, because the analysis showed that these results were present during all phases, including Quasi-Transfer Testing when both groups flew with motion. The No-Motion group flew more precisely than the Motion group, with lower STDs around the desired heading and localizer, and lower bank STD. The No-Motion group seemed to achieve this performance with wheel-control inputs of lower magnitude, i.e., lower root mean square (RMS) and fewer reversals (number of times the wheel exceeds a ten-degree band around the neutral position). It used higher pedal-response bandwidth (which is the frequency below which the area under the pedal power spectral density curve constitutes half of the total area) than the Motion group.

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,104) | p |
| STD heading (deg) | 3.77 | 2.84 | 11.96 | .0008 |
| STD bank (deg) | 3.35 | 2.92 | 5.61 | .02 |
| STD localizer deviation (dot) | .55 | .36 | 14.39 | .0003 |
| Localizer exceedance (dot) | .25 | .09 | 16.98 | <.0001 |
| Wheel reversals | 8.93 | 6.68 | 6.00 | .02 |
| RMS Wheel (deg) | 2.39 | 2.08 | 8.44 | .005 |
| Pedal-response BW (Hz) | .015 | .025 | 6.68 | .01 |

Table 5-10. Precision Instrument Approach Fix-to-DH Results for Group

Table 5-11 shows the dependent variables that were significantly affected by Phase. Both groups improved flight-precision performance (heading, bank, pitch, and localizer STD) and reduced control inputs (wheel and column reversals, RMS, and bandwidths) progressively with Phase, indicating that both simulator configurations resulted in effective training.

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,104) | p |
| STD heading (deg) | 3.32 | 1.27* | -.15 | 1.13* | 7.90 | .0006 |
| STD bank (deg) | 3.15 | .66* | -.25 | .41 | 4.19 | .02 |
| STD pitch (deg) | 1.21 | .28* | -.004 | .27* | 3.92 | .02 |
| STD localizer deviation (dot) | .46 | .21* | .004 | .21* | 6.36 | .003 |
| Wheel reversals | 7.84 | 2.61 | .94 | 3.55* | 5.02 | .008 |
| Column reversals | 4.57 | 2.03 | 1.20 | 3.22* | 3.65 | .03 |
| RMS wheel (deg) | 2.24 | .46* | -.04 | .42* | 7.18 | .001 |
| Wheel BW (Hz) | .12 | -.004 | .03* | .02 | 3.86 | .02 |
| RMS column (in) | .51 | .10* | .03 | .13* | 5.93 | .004 |
| Column BW (Hz) | .093 | -.01 | .03* | .02 | 3.59 | .03 |

* indicates significant difference (p<.05)

Table 5-11. Precision Instrument Approach Fix-to-DH Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Decision-Height to Touch-Down

For the Decision-Height to Touchdown (DH-to-TD) flight segment, which is the shorter of the two segments and occurred with the runway in sight, 19 dependent variables are used in the MANOVA. The same variables as in the Fix-to-DH segment were used here with the addition of two performance variables, namely:

Touchdown descent rate (the vertical speed of the airplane at touchdown)

Touchdown distance (distance from the runway threshold at touchdown)

Group and Phase again significantly affected the results (Wilks’ Lambda (=.63, F(19,86)=2.70 and (=.42, F(38,172)=2.43, respectively, both p<.001) without interacting ((=.66, F(38,172)=1.06, p>.10). As in the previous segment, the Motion group showed higher wheel activity, lower pedal response bandwidth, and a tendency for worse directional control than the No-Motion group (Table 5-12). In addition, the Motion group controlled airspeed worse than the No-Motion group and had lower column-response bandwidth. As in the previous segment, both groups were successfully trained, showing progressive improvement in flight precision (heading, bank, pitch, and localizer tracking) and reduction in control activities (wheel and column) with Phase (Table 5-13).

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,104) | p |
| STD heading (deg) | 2.95 | 2.38 | 3.55 | .06 |
| Average airspeed exceedance (kts) | 5.07 | 3.55 | 4.55 | .04 |
| RMS wheel (deg) | 3.81 | 3.20 | 7.54 | .007 |
| Column response BW (Hz) | .08 | .11 | 13.80 | .0003 |
| Pedal response BW (Hz) | .05 | .09 | 10.98 | .001 |

Table 5-12. Precision Instrument Approach DH-to-TD Results for Group

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,104) | p |
| STD heading (deg) | 2.68 | 1.15* | -.19 | .96* | 5.80 | .004 |
| STD bank (deg) | 3.78 | 1.05* | -.45 | .60 | 3.46 | .04 |
| STD pitch (deg) | 1.24 | .24* | -.12 | .12 | 4.18 | .02 |
| Average glide slope exceedance (dot) | .29 | .09 | .01 | .10* | 4.43 | .01 |
| Wheel reversals | 5.85 | 1.56* | .46 | 2.02* | 8.13 | .0005 |
| Column reversals | 5.45 | 2.13* | .89 | 3.02* | 8.09 | .0005 |
| RMS wheel (deg) | 3.52 | .71* | .21 | .92* | 6.41 | .002 |
| Wheel response BW (Hz) | .14 | .01 | .03* | .04* | 6.29 | .003 |
| RMS column (in) | 1.26 | .14* | -.0003 | .14* | 4.84 | .01 |
| Column response BW (Hz) | .09 | .02 | .05* | .07* | 15.00 | <.0001 |

* indicates significant difference (p<.05)

Table 5-13. Precision Instrument Approach DH-to-TD Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Summary

Two separate segments of the PIA were analyzed, the approach Fix-to-Decision-Height segment and the Decision-Height-to-Touchdown segment. For neither of the segments was there an interaction between Group and Phase effects, so, whatever differences existed between the two groups, they persisted even when the No-Motion group quasi-transferred to motion. Both groups significantly improved on many variables across phases.

For both segments, the Motion group controlled the ailerons more actively than the No-Motion group, as it had also done for the takeoff maneuvers. But this increase in control activity did not lead to better lateral-directional control, on the contrary, the flight precision of the Motion group was inferior to the No-Motion group during all phases.

Also for both segments, the Motion group had a lower pedal-response bandwidth than the No-Motion group, as it had had for the V2 cut but not the V1 cut. Only for the DH-to-TD segment the No-Motion pilots had higher column-response bandwidth and better speed control.

#### Sidestep landing

Approach-Fix to Breakout-of-Clouds

The dependent variables used in the MANOVA for the Approach-Fix to Breakout-of-Clouds (Fix-to-BC) segment are as follows (a total of 20 variables):

Performance

Maximum, STD, and average exceedance of heading deviation (average of heading deviations exceeding (5( from the desired heading)

STD and average exceedance of bank angle (average of bank angle exceeding (5( from level attitude)

STD pitch angle

Average airspeed exceedance

STD and average exceedance of glide slope and localizer deviations

Behavior

RMS and number of reversals of column, wheel, and pedal responses

Column, wheel, and pedal response bandwidths

Except for the constant 10-knots quartering headwind instead of the shifting crosswinds, the Fix-to-BC flight segment was similar to the Precision Instrument Approach from Fix to DH and thus yielded similar effects. The MANOVA results showed significant Group and Phase effects (Wilks’ Lambda (=.66, F(20,95)=2.43, p=.002, and (=.39, F(40,190)=2.87, p<.0001, respectively), without interaction ((=.62, F(40,190)=1.30, p>.10). The similarity of the Group effects found in this segment to the Precision Instrument Approach Fix-to-DH segment can be seen in Table 5-14. The No-Motion group performed better compared to the Motion group with regard to directional control (heading and localizer tracking), and with lower wheel control activity. However, the significantly lower bank-angle STD and higher pedal bandwidth found for the No-Motion group with the Precision Instrument Approach were not found here, suggesting that these effects were related to the shifting winds. The effects of Phase were also similar to those found for the Precision Instrument Approach (Table 5-15). Both groups benefited from Training with better directional performance, lower column activity, and lower wheel-response bandwidth, and these benefits quasi-transferred.

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,114) | p |
| Max heading deviation (deg) | 6.53 | 5.66 | 4.14 | .04 |
| STD heading (deg) | 2.58 | 2.04 | 4.81 | .03 |
| STD localizer (dot) | .23 | .17 | 7.57 | .007 |
| Average localizer exceedance (dot) | .11 | .05 | 6.15 | .02 |
| Wheel reversals | 2.61 | 1.62 | 9.16 | .003 |
| RMS wheel (deg) | 2.24 | 1.79 | 11.46 | .001 |

Table 5-14. Sidestep Landing Fix-to-BC Results for Group

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,114) | p |
| Max heading deviation (deg) | 6.10 | 2.47* | -1.35* | 1.12 | 11.28 | <.0001 |
| Average heading exceedance (deg) | .44 | .55* | -.15 | .40* | 8.78 | .0003 |
| Column reversals | 1.33 | .85 | .38 | 1.23* | 4.79 | .01 |
| Wheel response BW (Hz) | .12 | .01 | .02 | .03* | 4.52 | .01 |

* indicates significant difference (p<.05)

Table 5-15. Sidestep Landing Fix-to-BC Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Breakout-of-Clouds to the Upward-Gust

The Breakout-of-Clouds to the Upward-Gust (BC-to-Gust) segment was the flight segment where sidestepping occurred. For this segment, 20 dependent variables were used in the MANOVA, as follows:

Performance

STD heading, bank, and pitch angle

Maximum heading and bank angle during sidestep

Average airspeed exceedance

Sidestep rate (the lateral speed going from 800 ft to within 200 ft lateral distance from the centerline of runway 36 Right)

Sidestep lateral overshoot (the rightmost lateral distance from the centerline of runway 36 Right after sidestep)

Maximum, STD, and average exceedance of glide slope deviation

Behavior

RMS and number of reversals of column, wheel, and pedal

Column, wheel, and pedal response bandwidths

The analyses of this segment again yielded significant overall Group and Phase effects (Wilks’ Lambda (=.72, F(20,95)=1.86, p=.02, and (=.25, F(40,190)=4.72, p<.0001, respectively) with no interaction ((=.73, F(40,190)<1, p>.10). The only significant Group effect for this flight segment was the higher wheel activity of the Motion group compared with the No-Motion group (Table 5-16). This difference, however, did not result in any difference in the flight-precision performance between the two groups. The effect on Phase (Table 5-17) showed that Training, regardless of the motion configuration, had the following significant effects on Quasi Transfer: better directional performance (heading), more accurate glide-slope tracking, lower control activity (column, wheel, pedal) with lower wheel response bandwidth, and less aggressive sidestep (lower sidestep rate and lower sidestep overshoot).

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,114) | p |
| Wheel reversals | 2.89 | 2.23 | 7.07 | .009 |
| RMS wheel (deg) | 2.74 | 2.32 | 10.19 | .002 |

Table 5-16. Sidestep Landing BC-to-Gust Results for Group

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,114) | p |
| Max heading (deg) | 10.62 | .89 | .75 | 1.64* | 3.43 | .04 |
| Sidestep rate (ft/s) | 50.34 | 11.69* | -5.08 | 6.61* | 11.15 | <.0001 |
| Sidestep lateral overshoot (dot) | .46 | .41* | -.15 | .27 | 5.84 | .004 |
| STD glide slope (dot) | .28 | .07* | .03 | .10* | 8.07 | .0005 |
| Max glide slope (dot) | .91 | .19 | .03 | .22* | 4.70 | .01 |
| Average glide slope exceedance (dot) | .09 | .05 | .03 | .08* | 3.09 | .05 |
| Wheel reversals | 2.56 | .85* | .06 | .91* | 5.65 | .005 |
| Column reversals | 1.90 | .76 | .65 | 1.41* | 5.19 | .007 |
| Wheel response BW (Hz) | .085 | .005 | .05* | .05* | 10.91 | <.0001 |
| RMS pedal (in) | .15 | .08* | -.01 | .06* | 5.02 | .008 |

* indicates significant difference (p<.05)

Table 5-17. Sidestep Landing BC-to-Gust Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Upward-Gust to Touchdown

The Upward-Gust to Touchdown (Gust-to-TD) segment is considered the most diagnostic flight segment of the Sidestep Landing for the emergence of an effect of motion, because in this segment the pilots had to respond quickly and appropriately to maintain precise flight path. The 20 dependent variables used for MANOVA of this segment are as follows:

Performance

STD heading, bank, and pitch angles

Roll and yaw activities

Average airspeed exceedance

STD localizer deviation

STD and average exceedance of glide slope deviation

Touchdown descent rate

Touchdown distance

Behavior

RMS and number of reversals of column, wheel, and pedal responses

Column, wheel, and pedal response bandwidths

As in the other segments, the overall Group and Phase effects were significant for this segment (Wilks’ Lambda (=.62, F(20,95)=2.93, and (=.37, F(40,190)=3.08, respectively, both p<.001). Again, they didn’t interact with each other ((=.66, F(40,190)=1.10, p>.10), so all Group effects were present during all phases (i.e., even when both groups had motion), and both groups were equally affected by Phase.

Group effects were observed on three of the 20 individual variables analyzed for this particular segment (Table 5-18). The two groups appear to use different TD strategies regardless of Phase: The Motion group landed softer, but at a farther distance from the runway threshold (yet within the landing box) compared to the No-Motion group. The landing box is 500 ft to 3000 ft from the runway threshold. The No-Motion group again employed higher pedal-response bandwidths than the Motion group.

| Variable | Mean | Stats |
| --- | --- | --- |
|  | Motion | No-motion | F(1,114) | p |
| Pedal response BW (Hz) | .04 | .08 | 14.08 | .0003 |
| TD distance (ft) | 1660 | 1435 | 12.09 | .0007 |
| TD descent rate (ft/min) | 285 | 327 | 6.02 | .02 |

Table 5-18. Sidestep Landing Gust-to-TD Results for Group

Both groups significantly improved on nine variables across phases for the Gust-to-TD segment (Table 5-19), showing again that Training was effective. For flight-precision performance, improvement was only observed in glide-slope tracking (lower deviation STD and average exceedance). In behavior, progressively with Phase, pilots were found to significantly reduce their yaw activity, wheel reversals, wheel and pedal RMS, and wheel, pedal, and column response bandwidths.

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,114) | p |
| Yaw activity (deg/s) | .41 | .07* | -.01 | .06* | 4.58 | .01 |
| STD glide slope deviation (dot) | .56 | .05 | .04 | .09* | 4.76 | .01 |
| Glide slope exceedance (dot) | .23 | .10 | .03 | .12* | 4.08 | .02 |
| Wheel reversals | 8.07 | 1.84* | .82 | 2.66* | 6.51 | .002 |
| RMS wheel (deg) | 2.93 | .46* | -.06 | .40 | 4.52 | .01 |
| Wheel response BW (Hz) | .15 | .02 | .07* | .09* | 18.56 | <.0001 |
| Column response BW (Hz) | .10 | .05* | .04 | .08* | 11.61 | <.0001 |
| RMS pedal (in) | .40 | .12* | -.04 | .07 | 7.72 | .0007 |
| Pedal response BW (Hz) | .06 | -.03 | .04* | .02 | 7.08 | .001 |

* indicates significant difference (p<.05)

Table 5-19. Sidestep Landing Gust-to-TD Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Summary

The sidestep-landing maneuver was analyzed in three segments, Approach-Fix-to-Breakout-of-Clouds, Breakout-of-Clouds-to-Upward Gust segment, and Upward-Gust-to-Touchdown. All pilots improved across phases, regardless of Group.

During the Fix-to-BC segment, the No-Motion pilots had better directional control using fewer wheel inputs than the Motion group, just like for the PIA. The lower wheel-activity effect for the No-Motion group also held during the BC-to-Gust segment, but was not accompanied by any performance differences.

For the most challenging Gust-to-TD segment, however, the increased pedal-response bandwidth for the No-Motion group returned. Also, the Motion pilots landed slightly softer than the No-Motion pilots even when all pilots had motion, but also slightly further away from runway threshold.

#### Discussion

Takeoff maneuvers

The most important result for the takeoff maneuvers was the faster pedal reaction time to the V1 cut of the Motion compared with the No-Motion group during Evaluation and Training. This does point to an early alerting function of the enhanced motion, providing sufficient lateral acceleration cues, as this result was not found in the First Study using “as is” motion. Despite the fact that PFs were told which engine failure to expect during Training, the No-Motion group continued to be unable to match the reaction time of the Motion group. Once the No-Motion group did quasi-transfer to motion, however, it was immediately able to avail itself of the motion cues, and the pedal reaction time and related differences disappeared. That the pedal reaction time advantage during the V1 cut was not replicated for the V2 cut might be explained by the higher altitude during the V2 cut, which renders a response less time-critical, and the reduced visual reference to the ground, which may have led to consultation of the instruments before responding.

One curious result for the V2 cut is that at Quasi Transfer, the pedal reaction time of the Motion group is slower than for the No-Motion group. Further statistical examination showed that both groups do quasi-transfer the reaction time improvement achieved during Training, but the Motion group less completely than the No-Motion group. This may be due to fatigue of the Motion group, which in the No-Motion group may be counteracted by the emergence of motion. Another indication that fatigue may have been a factor with the V2 cut is the number of variables that significantly improved during Training, but then significantly deteriorated at Quasi Transfer regardless of Group. This doesn’t happen with any of the other maneuvers.

Landing maneuvers

The differences in landing strategy for the Sidestep Landing between the two groups make intuitive sense. The Motion group appears to use the vertical acceleration cues to arrest sink rate, resulting in softer landings but farther-from-runway-threshold touchdowns than the ones of the No-Motion group. The fact that these performance differences were not replicated for the Precision Instrument Approach might be explained by the lower visibility and the shifting head- and tailwinds distracting the Motion group from taking advantage of the vertical acceleration cues.

The more striking result from the landing maneuvers is the consistent finding of lower control activity with higher flight precision for the No-Motion group, and that this finding persisted even at Quasi Transfer to the simulator with motion. This shows that even when the No-Motion group is exposed to motion cues, it continues the steady control strategy adopted without motion cues. This was found for all segments of both maneuvers, with the exception of Sidestep Landing Gust-to-TD. The lower control activity refers to the wheel only. Pedal and column inputs were usually the same.

Pedal-response bandwidth showed some interesting patterns. There were no differences between the two groups during the “easier” segments of the Sidestep Landing before the upward-gust disturbance. However, during the V2 cut, both segments of the PIA, and the Gust-to-TD segment of the Sidestep Landing, the pedal-response bandwidth of the No-Motion group was higher than for the Motion group. Finally, the one case where the Motion group had higher pedal-response bandwidth than the No-Motion group was during the V1 cut, but only before both groups had motion, the difference disappeared at Quasi Transfer due to the No-Motion group significantly increasing its pedal-response bandwidth. In all cases but the V2 cut, which didn’t reveal any performance differences between groups, whenever there was a difference between groups in pedal-response bandwidth, the group with the higher bandwidth also had better directional control.

These results are different from some of the previous tracking studies that have found increased control activity when motion was reduced (Schroeder, 1999). Other studies, however, are consistent with the results of the present study (Scanlon, 1987; Mulder, Chiecchio, Pritchett and van Paassen, 2003). Whether or not control activity increases or decreases as platform motion varies depends on several factors. If the pilot has been utilizing motion to improve the stabilization of the pilot-vehicle loop, as in Schroeder’s helicopter tasks, control activity usually increases as the motion cue becomes less usable. This is explained by the theoretical pilot model offered by Hess (1989). On the other hand, if motion is making the pilot aware of high-frequency disturbances, then control activity can increase when motion cues become more salient, as the pilot attempts to counter those disturbances. For large vehicles, with relatively low control bandwidths, this increased control activity may not translate to improved pilot-vehicle performance. However, this conclusion may depend on task complexity, or, perhaps, task bandwidth (Scanlon, 1987).

### Individual Training Progress

As a complement to the assessment of the phase effects in the group analyses, the effect of motion on pilot’s individual training progress was assessed by looking at the difference in the percentage of pilots that improved across phases. Variables examined were related to PF control performance (pedal reaction time, STD heading, and STD bank for the takeoff maneuvers; STD localizer and STD glide slope for the landing maneuvers) and control activities (RMS wheel and RMS pedal) from the most important segment of each maneuver.

In this report, reduction in the value of a variable is considered an improvement. While this is true for performance-related variables, it may not be obvious for variables related to control activities. However, because the pilots seemed to aim towards lower RMS values on wheel and pedal during training, this definition of improvement was also applied to the control-activity variables.

Because maneuvers and scenarios, respectively, were repeated during Training and Quasi-Transfer Testing, and did not yield an effect of Trial (see 5.3.3.2), the values of the variables collected during each of these phases were averaged to determine improvement across phases. The criterion for improvement was set to greater than 15% reduction in the average value of variables from one phase to the next. The number of pilots in each group who improved was counted for every variable considered. Fisher’s Exact test was then used to examine whether the difference in the percentages of improved pilots between groups was significant.

The purpose of the comparisons of pilots’ individual performance and behavior during Evaluation vs. during Training (Phase I vs. Phase II) and during Evaluation vs. during Quasi-Transfer Testing (Phase I vs. Phase III) for each group was to determine whether pilots improved across phases, and whether the nature of training (with or without motion) affected the percentage of pilots that improved. The purpose of the comparison of pilots’ individual performance and behavior during Training with their performance and behavior during Quasi-Transfer Testing for each group was to determine whether the nature of transfer, from the simulator without motion to the simulator with motion for the No-Motion group or from motion to motion for the Motion group, had a differential effect on quasi-transfer of the performance and behavior of individual pilots. The summary of the results for each maneuver is given below.

#### V2 Cut

Table 5-20 presents the percentage of improvement in the Motion group compared with the percentage of improvement in the No-Motion groups between Evaluation and Training (I to II), Evaluation and Quasi-Transfer Testing (I to III), and between Training and Quasi-Transfer Testing (II to III). Five significant differences were found, all in favor of the No-Motion group.

Only two of these differences were between Training and Quasi-Transfer Testing, the comparison that would indicate that the fact of adding motion had an effect on certain control activities. However, they were only marginally significant, and neither of the improvements was strong enough to reach significance at the group level, where there were no corresponding Group effects (see 5.3.3.4).

Two differences in percent improvement were found between Evaluation and Quasi-Transfer Testing. One was for pedal-reaction time. This difference was reflected in the Group comparisons, which showed that the No-Motion group improved its mean pedal-reaction time significantly between Evaluation and Quasi-Transfer Testing (the Motion group had lost some of the improvement gained during training, so any difference between the means disappeared at Quasi Transfer) (see Table 5-2). The other was a marginally higher percentage of improved pilots for pedal RMS. Finally, the percentage of the No-Motion pilots improving their pedal-response reaction time also tended to be higher than the one for the Motion pilots from Evaluation to Training (at the group level, both improvements had been significant).

| Variable | I to II | I to III | II to III |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| Pedal RT | 65 | 90 | .06 | 40 | 80 | .01 | 10 | 30 | .12 |
| STD heading | 60 | 50 | .37 | 40 | 45 | .50 | 20 | 35 | .24 |
| STD bank | 70 | 55 | .26 | 40 | 50 | .37 | 15 | 20 | .50 |
| RMS Wheel | 65 | 40 | .10 | 30 | 45 | .26 | 0 | 20 | <.06 |
| RMS Pedal | 55 | 50 | .50 | 35 | 60 | .07 | 0 | 20 | <.06 |

Table 5-20. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for V2 Cut (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

#### V1 Cut

As can be seen from Table 5-21, again all of the now six significant differences were in favor of the No-Motion group. Four of these involved the pedal; there was a significantly higher percentage of No-Motion pilots who shortened their pedal reaction time and lowered their pedal activity from Evaluation to Quasi-Transfer Testing as well as from Training to Quasi-Transfer Testing compared to the Motion pilots. These differences reflect the finding in the group data that the No-Motion pilots’ pedal-reaction time remained stagnant as long as there were no motion cues alerting them of the V1 cut, but then immediately caught up with the motion pilots during Quasi-Transfer Testing with motion cues. Similarly, as long as there were no motion cues, the No-Motion pilots had significantly higher pedal RMS compared to the Motion pilots, a difference that also disappeared with quasi transfer to motion.

The improvement in the pedal-reaction time may also have effected an improvement in heading and bank control, as there was a marginally higher percentage of No-Motion pilots who lowered bank angle and heading STD from Evaluation to Quasi Transfer. However, the group data show that the difference between groups in heading control had disappeared already during Training, and there were no group differences in bank-angle STD.

| Variable | I to II | I to III | II to III |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| Pedal RT | 30 | 55 | .21 | 20 | 80 | .0002 | 0 | 60 | .00002 |
| STD heading | 35 | 55 | .17 | 40 | 70 | .06 | 40 | 60 | .17 |
| STD bank | 30 | 40 | .37 | 35 | 65 | .06 | 40 | 50 | .37 |
| RMS Wheel | 35 | 45 | .37 | 40 | 45 | .50 | 45 | 40 | .50 |
| RMS Pedal | 25 | 40 | .25 | 20 | 85 | .00004 | 5 | 50 | .002 |

Table 5-21. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for V1 Cut (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Comparison with First Study

Despite the fact that no pedal-reaction-time advantages were found for the Motion group in the First Study, the individual training data suggest that transferring to motion may have helped the No-Motion pilots improve their heading performance and reduce their pedal control activity. Comparisons of the percent of Motion and No-Motion pilots that improved between phases show that a higher percentage of No-Motion pilots improved in heading STD (p<.10)) and pedal RMS (p<.05) than the Motion pilots from Last Training to Quasi Transfer (see Table A1-5, note the differences in comparison procedures). The improvements were not large enough to result in a difference at the group level. Similar differences in individual pedal RMS improvement were also observed in the Second Study between Training and Quasi-Transfer Testing, but not for heading STD improvement.

A second indication from the First Study that motion might assist pilots to improve pedal control for the V1 cut may be the marginal difference in percent improvement from First to Last Training in pedal RMS, although it did not effect a performance improvement. In this case, a marginally higher percentage of Motion pilots reduced the number of pedal reversals than No-Motion pilots. This result was not replicated in the Second Study.

For the RTO maneuver, no differences between the Motion and No-Motion groups were found in percentage improvement from the First to Last Training, from the first training to Quasi Transfer, and from the last training to Quasi Transfer (see Table A1-6).

#### Precision instrument approach

During the Approach-Fix-to-Decision-Height segment of the Precision Instrument Approach, it was the Motion group that generally showed a higher percentage of improved pilots than the No-Motion group in four cases, although two of these differences were only marginally significant. More Motion pilots lowered their pedal activity (lower RMS) between Evaluation and Training and marginally more between Evaluation and Quasi-Transfer Testing (Table 5-22). In this case, training might have helped the Motion pilots recognize that too much counteraction to the disturbance-motion cues from the shifting winds reduces flight-path precision. However, although there was one marginally significant higher percentage of the Motion group improving localizer STD from Training to Quasi Transfer, the group analyses show that the Motion pilots never caught up with the No-Motion pilots on pilot-vehicle performance (see Table 5-10).

| Variable | I to II | I to III | II to III |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| STD LOC | 70 | 60 | .37 | 60 | 55 | .50 | 30 | 60 | .06 |
| STD GS | 65 | 50 | .26 | 60 | 55 | .50 | 30 | 40 | .37 |
| RMS Wheel | 65 | 60 | .50 | 60 | 40 | .17 | 20 | 30 | .36 |
| RMS Pedal | 70 | 35 | .03 | 65 | 35 | .06 | 30 | 50 | .17 |

Table 5-22. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for Precision Instrument Approach (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

#### Sidestep landing

For Sidestep Landingfrom Gust-to-Touchdown, the Motion-group improvement percentages were higher than the ones of the No-Motion group for localizer and glide-slope tracking between Evaluation and Training. Some of the motion pilots that had improved seem to have lost this improvement during the next phase, because the effect is reduced to a trend for localizer and entirely lost for glide slope when comparing Evaluation not with Training, but with Quasi-Transfer Testing (Table 5-23). Marginally more Motion than No-Motion pilots improved in localizer tracking from Evaluation to Quasi Transfer, but may be that is why also marginally fewer reduced their pedal activity (RMS). None of these differences, however, were reflected in the analyses by group (Table 5-18).

| Variable | I to II | I to III | II to III |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| STD LOC | 45 | 15 | .04 | 65 | 35 | .06 | 40 | 50 | .37 |
| STD GS | 65 | 30 | .03 | 50 | 45 | .5 | 20 | 40 | .15 |
| RMS Wheel | 55 | 70 | .26 | 50 | 35 | .26 | 15 | 20 | .5 |
| RMS Pedal | 60 | 70 | .37 | 30 | 60 | .08 | 5 | 5 | .75 |

Table 5-23. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Between Two Phases for Sidestep Landing (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

Table 5-23 also shows that the quasi transfer from motion to motion vs. from a fixed-base simulator to the (same) simulator with motion did not have an effect, as there was no difference in the percentage of improvement between the groups from Training to Quasi-Transfer Testing.

#### Discussion

For the takeoff maneuvers, it was the No-Motion pilots who showed higher percentages of improvement. In fact, the percentage of Motion pilots improving never exceeded the one of No-Motion pilots. One argument against interpreting this as an advantage of the No-Motion simulator configuration for training would be that at least some of the Motion pilots, for the takeoff maneuvers, have reached their performance and/or behavioral peak. Then, however, there should be a performance advantage of the Motion pilots, at least for those variables where an increased number of No-Motion pilots improves, and in the earlier of the two compared phases. This is indeed true for the V1 cut, where a slight majority of the improvement advantages occurred, but not for the V2 cut. The final result of training was that the No-Motion group had caught up with any initial advantages of the Motion group by the time it quasi-transferred to the simulator with motion.

For the landing maneuvers, it was the Motion group that showed more individual training progress, with the exception of RMS pedal during the side step. However, this was restricted to two variables for each landing maneuver. The final result of training was that the Motion group was never able to catch up with the initial advantage of the No-Motion group, not even when the No-Motion group also transferred to motion, and that any other differences persisted.

### Pilot Grades

#### Determination and calculation

The pilot grades for each maneuver trial were determined based on the feedback displays. A set of criteria based on the FAA PTS was developed to determine the grades. These criteria can be seen in Appendix 10. The grade for each criterion (criterion grade) varied from 1 to 5 with 1 being the worst and 5 being the best. In general, the criteria looked at the ability of the PFs to stay within the PTS bounds, the magnitude of the out-of-bound deviations (if any), the locus of occurrence of any out-of-bound deviations relative to a specific event such as engine failure or runway threshold crossing, and control steadiness. The final grade for each maneuver was calculated by combining the criterion grades using specific weights, as also described in Appendix 10.

Two evaluators independently determined the criterion grades from the recorded performance-feedback variables of each maneuver without knowing whether the platform motion was on or off. The resulting criterion grades from these evaluators were compared and a third evaluator settled any differences found in the criterion grades from the two evaluators. This was all done to avoid mistakes or data misreading especially in boundary cases.

#### Grade analysis

The effects of Group and Phase on the pilot grades was determined using Analyses of Variance (ANOVA). Each maneuver was analyzed separately and the grades were averaged across the maneuvers/scenarios in Training and Quasi-Transfer Testing phases before analysis. The results are summarized below.

Figure 5-12. Grade Means by Phase and Maneuver

The means of the grades for each group, phase, and maneuver are shown in Figure 5-12. First of all, there was no interaction between Group and Phase for any of the four maneuvers (V2 cut, PIA, V1 cut, Side Step Landing F(2,114)≤1.18). Group did not have a significant effect on the grades, except for the V2 cut where a marginally significant difference between groups was observed (F(1,114)=3.17, p<.10). In this case, the No-Motion group had marginally better grades than the Motion group (3.36 vs. 3.14).

Phase significantly affected the pilot grades for both groups in all four maneuvers (Table 5-24). In most cases, the grades improved progressively with Phase, except for the V2 cut, where the grades significantly deteriorated between Training and Quasi-Transfer Testing. This is another indication that the V2 cut results may have been affected by pilot fatigue (see 5.3.3.8). The progressive improvement in grades observed in the other cases showed that the training performed benefited both groups.

| Maneuver | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,114) | p |
| V2 Cut | 3.25 | -.92* | .56* | -.36 | 18.55 | <.0001 |
| PIA | 3.66 | -.66* | .10 | -.56 | 4.00 | .02 |
| V1 Cut | 3.84 | -.24 | -.39 | -.63* | 5.90 | .004 |
| SSL | 4.33 | -.26* | -.12 | -.38* | 7.70 | .0007 |

* indicates significant difference (p<.05)

Table 5-24. Grade Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

#### Discussion

The purpose of the pilot grades was to independently verify the validity of the linear combination of the many different dependent variables measured during the experiment calculated by the MANOVAs. Using an approach based on the FAA’s Practical Test Standards, the Phase effects were well replicated, showing the validity of the MANOVA procedure. The Group effects were too small to be captured by applying the PTS.

#### Comparison with First Study

During the First Study, a counterbalanced set of I/Es that were kept unaware of the purpose of the experiment or the motion status of the simulator graded each maneuver. Platform motion did not affect Evaluation in the simulator, nor did it affect the grades at Quasi Transfer to the simulator with motion. The latter was true when comparing the group means or the number of low vs. high grades in each group (i.e., grades of 1 and 2 vs. grades of 3 and 4). However, as can be seen in Appendix 1, there was one single analysis where motion appears to have affected I/E grades. During Quasi-Transfer Testing, I/Es gave more grades of 1 to V1 cuts flown by pilots trained without motion than to pilots with motion. This was only true when comparing the percentages of grades 1 and 2, both groups received an equal number of grades 3 and none of the pilots received a grade of 4. Improvement across the two phases can also be seen for both groups. Despite this single effect of motion, there was no effect of motion on the course of Training or on the amount of Training required before reaching the criterion needed to move to Quasi-Transfer Testing. Overall, the grades did show that the pilots improved across the maneuvers, but similarly for the two groups (see Bürki-Cohen et al., 2001). The true I/E grades of the First Study thus yielded similar results as the grades constructed from the feedback displays in the Second Study.

## Opinions from Questionnaires

### Data Analysis Overview

The responses to the Pilot-Flying questionnaires were examined to determine whether there were differences in how the Motion and the No-Motion groups compared the simulator to the airplane or to the last simulator flown on different properties (see Appendix 6). The Pilot-Not-Flying questionnaire responses were examined for differences between how the two groups compared to average pilots on various performance and behavior variables (see Appendix 7). As appropriate, the effects of factors such as Phase (Evaluation, Training, Quasi-Transfer Testing), type of Control input (aileron, rudder, etc), and type of Maneuver were also analyzed. Finally, because most average responses were very close to “same as” the simulator/airplane/average pilot, one-sample T-tests determined whether the PF/PNF ratings were significantly different from the “same as” rating. These tests were performed separately for each questionnaire and question, using the mean ratings for each control or maneuver. They were performed with both groups combined when there was no effect of Group in any of the analyses, and separate if there was a significant or a trend of a difference between groups. As in the rest of this report, any difference between conditions was considered statistically significant if it had a probability of chance occurrence lower than five percent (p<.05) given no effect of the condition variable. Differences where the probability was larger than five but smaller than ten percent (.05<p<.10) were considered a statistical trend.

### Pilots Flying

#### Data Analyses

For general properties such as Acceptability, Comfort, and Physical and Mental Workload, PFs were asked to give a general rating without distinguishing between type of Control or Maneuver. These ratings were analyzed using ANOVAs with Group (Motion vs. No-Motion evaluated/trained) as a two-level between-subjects factor and Phase (Evaluation, Training, and Quasi-Transfer Testing) as a three-level within-subjects factor.

For properties such as Handling Qualities, Control Feel and Control Sensitivity, PFs gave both an overall rating and specific ratings for each type of Control. For these, first the Group-by-Phase ANOVA described above was performed with the overall rating as the dependent variable. Then, separate ANOVAs for each questionnaire (i.e., Phase), with Group as a two-level between-subjects factor and type of Control as a within-subjects factor (varying between five and eight levels including the overall rating) were performed. To prevent inflation of degrees of freedom when calculating the main effect of motion in these comparisons, the degrees of freedom were adjusted so that each PF was counted only once instead of separately for each control rating.

For Control Strategy and Technique and Gaining Proficiency, PFs gave a rating for each Maneuver in addition to the overall rating. Here, the Group-by-Phase ANOVA with the overall ratings was followed by separate ANOVAs for each questionnaire examining the effects and interactions of Group and Maneuver. Maneuver was treated as a within-subjects factor. The same Group-by-Maneuver ANOVAs were used to analyze the answers on Performance and Other Cues, where no overall rating was requested. PFs were not asked to rate their performance after Training, where they had received performance feedback, and they were not asked about their ease of Gaining Proficiency after Evaluation, when they had been exposed to each scenario only once. Again, the degrees of freedom were adjusted by counting each pilot only once instead of for each maneuver when calculating the main effect of motion.

#### Were there any differences between the Motion and No-Motion groups?

Only eight of the 26 analyses found an effect of the Group (i.e., Motion vs. No-Motion) variable, and half of these effects were only a trend (p<.10). They involved less than half of the properties examined (5 of 11). Moreover, for Handling Qualities, it was the No-Motion group that perceived the simulator significantly more similar to the airplane than the Motion group, but only for the ratings after Training analyzed in the separate Group-by-Control ANOVA. On a scale from -3 (much worse than the airplane) to +3 (much better than the airplane), both groups rated the simulator as less than “slightly different” from the airplane, but the mean rating of the No-Motion group was higher than the one of the Motion group (-.18 vs. -.5; F(1,38)=4.82, p<.05). The four remaining properties with their mean ratings are listed below:

For Control Feel, the Group-by-Phase ANOVA showed that the Motion group rated it significantly more like the airplane than the No-Motion group (-.24 vs. -.68 where -3 means “much lighter” and +3 means “much heavier than airplane”; F(1,114)=8.00, p<.01). The Group-by-Control ANOVAs after each phase found only trends of a Group effect, and only after Training and Quasi-Transfer Testing (F(1,38)=3.99 for Training and 4.01 for Quasi-Transfer Testing, p<.06).

For “Other Cues,” the Group-by-Maneuver ANOVA after Training showed that the No-Motion pilots perceived them significantly less like the airplane than the Motion pilots (3.03 vs. 3.54, where 4 means “the same as” and 1 “very different than in the airplane;” F(1,38)=4.78, p<.05). After Evaluation, this difference had only been a trend (F(1,38)=3.13, p<.10).

For Performance, the Group-by-Maneuver ANOVAs showed that the Motion pilots rated their performance significantly more like in the airplane than the No-Motion pilots did, but only after Evaluation (-.68 vs. –1.16 on a scale from –3 to +3; F(1,38)=4.31, p<.05).

For Gaining Proficiency, the Group-by-Maneuver ANOVAs found a trend for the Motion pilots to rate their Gaining Proficiency as easier than the No-Motion pilots did, but only after Training (.21 vs. -.32 on a scale from –3 to +3; F(1,38)=3.30, p<.10).

There were no interactions between Group and Phase (F(2,113-114)≤1.57). This means that any effects found in the Group-by-Phase ANOVAs were present in all phases, even during Quasi-Transfer Testing when both groups had motion, and that no Group main effects were masked by Phase effects.

There were also no interactions between Group and Maneuver or Type of Control (all FGroup x Maneuver either F(3,150-152)≤1.77 or F(4,190)<1, all FGroup x Control either F(7,286-303)≤1.28 or F(6,265-266)<1 or F(4,188-190)<1; all p>.10). This means that any motion effects found in the Group-by-Maneuver and Group-by-Control ANOVAs held for all controls and maneuvers, and that no potential motion main effects were masked by control or maneuver effects, respectively.

In summary, these results do not lead to the conclusion that motion was a powerful variable affecting PF’s perception of the simulator, for two reasons. First, they show that the vast majority of the comparisons was unaffected by whether the groups had or had not been trained with motion cues (all F(1,112-114)≤1.73 or F(1,38-39)≤2.71, p>.10). Notably, none of the comparisons relating to the following properties were at all affected by or interacted with Group (all p>.10):

Acceptability (compared with the last simulator flown; all F(1 or 2,114)<1)

Physical Comfort (compared with the last simulator flown; all F(1 or 2,113)≤1.66)

Mental and Physical Workload (compared to the airplane; all F(1 or 2,114)≤1.03)

Control Sensitivity (defined as “the amount of response generated by the control actions” and compared with the airplane; all F(1 or 2,112)≤1.45, all F(1,38)<1, all F(4,188-190)<1)

Control Strategy and Technique (compared with the airplane; all F(1,38)≤1.04, all F(3,152)≤1.77, all F(4, 190)<1) (all compared with the actual airplane)

The lack of a difference for Physical Comfort is especially important because it removes any concerns that the lack of motion would induce motion sickness. There are several theories that would support this prediction, most are based on the stipulation that motion sickness arises when there is a conflict between vestibular and visual sensations (see, e.g., Oman, 1991). Of course, this conflict was very high during Evaluation and Training for the No-Motion group, yet they reported feeling just as comfortable as the Motion group did.

Second, the status of the motion variable is further weakened by the fact that the differences between groups persisted even after the motion variable was removed. If the presence or absence of motion had greatly affected PFs’ ratings, differences between groups should have disappeared once both groups had motion.

Comparison with First Study

The First Study had found three differences between the ratings by the crews in the two groups (remember that in the First Study, each Captain flying was paired with a new PNF that knew nothing about the study). In each of these cases, it was the absence of motion that led to higher ratings (see Bürki-Cohen et al., 2001, for statistics).

After Quasi Transfer to motion, the No-Motion PFs rated Control Precision as less worse than in the airplane than the Motion group. This was due to the Motion group rating the simulator worse after Quasi-Transfer Testing, while the No-Motion PFs gave equivalent ratings.

There was also a trend for the No-Motion PF to perceive Gaining Proficiency easier in the test simulator compared to the last simulator flown (which was the same simulator with the motion on), compared to the Motion group. The Motion PF perceived no differences between the test simulator and the last simulator flown (which was the same simulator in the same configuration).

After Training, the No-Motion PNFs rated their PFs as having better control precision than the Motion PNFs rated their PFs.

In summary, the First Study had found even fewer differences between the two groups, and these differences did not show a preference for motion.

#### Did Pilots Flying recognize the absence of motion?

Although the question of “motion” was never directly addressed in the questionnaires, pilots had many opportunities to comment on their perception of the simulator motion. For pilots that didn’t mention motion when evaluating the simulator’s Control Feel and Sensitivity, Handling Qualities, and overall Acceptability, they could mention it when commenting on their own Performance, Workload, or Comfort. If they failed to do so, a final opportunity was offered when they were asked to compare “Other cues” provided by the simulator with those experienced in the airplane. Pilots were encouraged to make comments and asked to elaborate on all ratings that expressed a difference between the test simulator and the airplane/last simulator flown, in the space provided on the questionnaires (see Appendix 6).

Nevertheless, not all of the 20 No-Motion pilots appeared to notice the lack of motion, despite the fact that any reference to the quality of the motion was counted as an indication that the No-Motion pilots did perceive the absence of motion (see Appendix 11). Thirteen commented on the quality of the motion on the questionnaire administered after Evaluation, but not all of these appeared to have noticed that motion was entirely turned off. Comments ranged from noting that the motion was “not rough enough” from one of the first pilots participating to “Motion off is disorienting and reduces feedback. My head was almost spinning once breaking out on the ILS [Instrument Landing System]” from one of the final participants who was a simulator instructor in addition to flying the line.

Three No-Motion pilots realized that something was wrong with the motion only after Training. One asked whether there would be “probably better yaw feel in aircraft when you lose an engine?” Another noted the absence of motion during landing: “No ground feel. Only indication of landing is spoiler.” The third wrote that he “[d]id not feel yaw.”

Four No-Motion pilots gave no indication that they noticed anything amiss with the motion stimulation provided by the simulator. Three of these never commented on the motion, and one indicated the potential for physical discomfort with motion after the second Quasi-Transfer Test.

By the time the last six pilots (all from the same airline as many of the earlier pilots) were tested, word may have gotten out regarding the purpose of the experiment. In contrast to the first 14 No-Motion pilots, where never more than two consecutive pilots had commented on motion on the first questionnaire administered after evaluation, each of these final six No-Motion pilots commented on motion after evaluation.

Pilots did not only comment on motion when it was lacking, however. It is worth noting that although the No-Motion pilots made more comments on motion, the Motion pilots made many similar comments. These comments are listed in Appendix 12. The parallelism between comments such as “There seems to be more clues as to what is occurring in the aircraft vs. the simulator” from a Motion pilot and “Not as much motion visual cue’s (sic)” from a No-Motion pilot suggest that much of both groups’ dissatisfaction may be due to inherent simulator limitations regardless of whether hexapod-platform motion is turned on or off.

The complete set of comments on motion, including those from the Motion pilots, is listed in Appendix 11 and Appendix 12. All other comments are listed in Appendix 13 to Appendix 22. Comments from the Final Questionnaires are listed in Appendix 23 to Appendix 28.

Comparison with First Study

The regional-airline captains participating in the First Study were solicited for comments in addition to the ratings only at completion of the flying phase, i.e., after Quasi-Transfer Testing. In general, fewer pilots provided comments than in the Second Study, which may be due to the fact that they were invited to participate just before their jeopardy Line Oriented Evaluation (LOE). So, although they had the option to decline participation in the study, they were in a much more stressful situation than the B747-400 volunteers, who flew in for the experiment and were paid for their participation. More of the No-Motion PFs provided comments (13 vs. 6 Motion PFs), but only one (and none of the Motion PFs) referred to motion, noting its absence during the first set of maneuvers.

#### Did Pilots Flying perceive the test simulator as different than the last simulator flown/airplane?

Despite the difficulty of the maneuvers and the unusually light weight of the simulated airplane, there was no significant difference between average rating and the rating “just like [in] the last simulator [flown]” for Acceptability, Physical Comfort, and Gaining Proficiency (asked only after Training and Quasi-Transfer Testing). The T-tests performed after each Phase showed that these ratings never differed significantly from “just like the last simulator flown” (Acceptability: all T(39)<1.61; Physical comfort: all T(38 or 39)<1.05; Gaining Proficiency: all T(19)≤1.62 (although T(39)=1.84, p<.10 after Quasi-Transfer Testing); all p>.10).

All simulator properties that were compared to the properties of the airplane were considered as different in most but not all comparisons, although all of them less than “slightly” so:

“Other Cues” were always perceived as different from the airplane (all T(19)≥3.13, p<.01).

Average Handling Quality ratings indicated that they were always perceived as worse than in the airplane (T(19)>2.26, p<.05).

Control Strategy and Technique were always rated as different from the airplane (T(39)≥4.49; p<.001).

Pilots perceived their performance (rated after Evaluation and Quasi-Transfer Testing only) always as worse than in the airplane (T(19)≥3.04, p<.01).

Physical and Mental Workload were considered higher than in the airplane (all T(39)≥2.15, p<.05).

Average Control Feel was always perceived as lighter by the No-Motion group (T(19)≥3.12, p<.01), but by the Motion group after Evaluation only (F(1,19)=2.36; p<.05).

Average Control Sensitivity was considered higher than in the airplane (T(39)>2.74, p<.001).

In summary, the NASA/FAA simulator was perceived as equivalent to the company simulator, but as very slightly different from the airplane.

#### Effects of Phase, Maneuver, and Control

No effects of Phase were found on any of the ratings, and, as mentioned before, Phase and Group effects did not interact (all F(2,112-114)≤1.57; p>.10). There also were never any effects of Maneuver, and again no interactions with Group (all F(3,150-152)≤1.77, F(4,190)<1, all p>.10).

There were, however, some effects of type of Control, although they also never interacted with Group. Significant effects of Control were found for Handling Qualities and Control Feel (defined in terms of control loading), and a few trends for Control Sensitivity (defined in terms of the amount of response generated by a control action). These effects are described below.

Handling Qualities were significantly affected by type of Control during Evaluation and Quasi-Transfer Testing (both F(6,265-266)≥3.52; p<.005). Follow-up Bonferroni tests showed that after Evaluation, this difference was accounted for by yaw control, which was rated worse than any of the other five controls (significantly worse than airspeed, bank angle, heading and altitude, and as a trend than pitch). After Quasi-Transfer Testing, it was airspeed that was rated significantly better than yaw and pitch controls. After Training, the Control type effect on ratings was only a trend (F(6,266)=1.89; p<.10), and none of the Bonferroni comparisons between type of Control yielded any significance.

The Control Feel ratings were affected by type of Control after Evaluation and Training only (both F(7,286 or 303)≥3.20; p<.005). Follow-up Bonferroni tests showed that during Evaluation, rudder was perceived as more lighter than the airplane than pitch trim and throttle, and during Training, it was aileron that was perceived as more lighter than the airplane than pitch and roll trim.

There were only trends of a difference in ratings due to type of Control for Control Sensitivity (all F(4,188-190)≥2.06; p<.10), but they were there after each phase. However, none of the follow-up tests yielded any significant differences, with the exception of the tests after Quasi-Transfer Testing, which revealed that yaw control was perceived as more more sensitive than in the airplane than the throttle was perceived.

The T-tests on the ratings presented in 5.4.2.4 have already shown that the test simulator was perceived as slightly different from the airplane. The tests described above show that this may be due mainly to yaw and rudder control. This is confirmed also by some of PF’s comments (see Appendix 11 to Appendix 28).

### Pilots Not Flying (PNF)

#### Data Analyses

In the PNF questionnaires, the PNFs compared the PFs with an average pilot on Control Performance, Control Strategy and Technique, Physical Workload, and ease of Gaining Proficiency. The Gaining Proficiency comparison was made only after Training and Quasi-Transfer Test 1 and 2. All analyses were done separately for each phase and each question. PNF was included as a two-level between-subjects factor in the analyses to determine PNF differences in opinion. When the questions were asked separately for each maneuver, a Group-by-PNF-by-Maneuver ANOVA was performed. Whenever there was an “overall” or only one rating, Group-by-Phase ANOVAs were performed for this rating. No two-way or three-way interactions between Group and Maneuver, PNF and Maneuver, and Group, PNF, and Maneuver were found. Significant Group-by-PNF interactions were followed up with one-way ANOVAs examining the effect of PNF separately for each Group. Only significant results are given.

#### Did Pilots-Not-Flying perceive differences between the Motion and No-Motion groups?

PNFs (labeled here as PNF1 and PNF2) perceived differences between the two groups in all four parameters they were queried on, i.e., Control Performance, Control Strategy and Technique, Physical Workload, and Gaining Proficiency. These differences were mostly favorable to the No-Motion condition, but at times were due to only one of the two PNFs, while the other didn’t perceive any difference between groups.

Control Performance

For Evaluation, the two PNFs agreed on a higher rating for the No-Motion group than the Motion group (F(1,142)=5.05, p<.05). In fact, the average rating of .02 for the Motion group on a scale of -3 to +3 indicated that the PNFs perceived the performance of the Motion group as identical to the one of an average pilot. The .19 rating for the No-Motion group, however, indicated that this group was perceived as performing better than the average pilot (see 5.4.3.4).

For the Training phase, the two PNFs disagreed with each other, resulting in no overall Group effect but a significant Group x PNF interaction (F(1,144)=17.44, p<.0001). This was due to the fact that with average ratings of .63 vs. .25, PNF1 rated the control performance of the No-Motion group marginally higher than the one of the Motion group (F(1,17)=3.59, p<.10), while with ratings of -.02 and .33 PNF2 rated that of the Motion group as marginally higher (F(1, 19)=4.28, p<.10).

For both Quasi-Transfer Testing trials, PNF1 rated the No-Motion group as better than the Motion group on control performance (average No-Motion ratings .58 and .77, Motion ratings 0 and .23; F(1, 17)>5.10, p<.05). PNF2 did not perceive differences between the two groups (No-Motion ratings -.02 and -.03, Motion ratings both 0). So there were effects of Group (F(1,144)=10.59; p<.005) and PNF-by-Group interactions (F(1,144)=13.81; p<.0005).

Control Strategy and Technique

There were Group effects only during Training and Quasi-Transfer Testing 2, and only for PNF1, resulting in a PNF by Group interaction (Training: F(1,36)=4.45, p<.05; Quasi-Transfer Testing 2: F(1,151)=6.01, p<.05).

On a scale from 1 (very different than average pilot) to 4 (same as average pilot), PNF1 rated the strategy and technique of the Motion group as more different compared to the No-Motion group (3.20 vs. 3.89, after Training; 3.83 vs. 4.0 after Quasi-Transfer Testing 2; F(1,17)(4.50, p<.05). Note that both groups had motion during Quasi-Transfer Testing.

Physical Workload

For Evaluation, PNF1 (but not PNF2, FGroup x PNF(1,36)=5.43, p<.05) rated the No-Motion group’s workload lower than the one of the Motion group on a scale from –3 (much higher than average PF) to +3 (much lower than average PF) (.20 vs. -.25; F(1,36)=5.43, p<.05).

After Quasi-Transfer Test 2, the workload of the No-Motion group was rated lower than the one of the Motion group (.42 vs. 0, F(1,34)=6.21, p<.05) by both PNFs.

Gaining Proficiency

During Quasi-Transfer Testing 2, PNF1 perceived the No-Motion group as Gaining Proficiency more easier than an average PF than the Motion group on a scale from –3 (much harder than average PF) to +3 (much easier than average PF) (.80 vs. .15; F(1,17)=22.02, p<.001), while PNF2 rated the two groups similarly (F(1,17)<1). This resulted in a significant Group by PNF interaction (FGroup x PNF(1,34)=12.11, p=.001).

PNF comments on motion can be seen in Appendix 29. All comments were on No-Motion PFs. All but one of these were from PNF2, who commented on half of the No-Motion pilots who flew with him that they tended to overcontrol at quasi-transfer to motion. All other PNF comments are listed in Appendix 30 to Appendix 33.

Comparison with First Study

While I/Es in the First Study gave equivalent ratings to the two groups after Training with and without Motion, they did give higher control performance ratings to the PFs trained with motion after Quasi-Transfer Testing. Although this may suggest an effect of having been trained with motion on Quasi Transfer, this finding was not supported by the ratings of the crews. It is somewhat consistent, however, with the single Motion group difference found in the V1 cut grades (see 5.3.5.4). The Second Study found no such difference in performance ratings favoring the Motion group.

#### Effects of Pilot-Not-Flying and Maneuver

Most of the effects of PNF have been discussed already in 5.4.3.2, because they interacted with Group. The effects of PNF that did not interact with Group are discussed below:

For Control Strategy and Technique, during Evaluation, PNF1 perceived the PFs as more different compared to an average PF than PNF2 did (F(1,142)=12.45, p<.001).

For Physical Workload, PNF1 rated the PFs as having lower Physical Workload compared to an average PF than PNF2 did (F(1,34)=6.21, p<.05).

The effects of PNF described here coupled with the many interactions with Group described in 5.4.3.2 suggest that PNF1 employed a more sensitive rating scheme than PNF2.

Maneuver did not have an effect on PNF ratings, except for Control Performance during Quasi-Transfer Testing 1. In this case, the PNFs gave the PFs higher ratings for controlling the Sidestep Landing than for the V2 cut (F(3, 144)=3.07, p=.03).

#### Did Pilots-Not-Flying perceive Pilots Flying as different than an average Pilot Flying?

A significant Group effect on PNFs’ comparisons of the PFs with an average pilot (see 5.4.3.2) does not necessarily indicate that the PFs were perceived as different from an average pilot. Although some of the PNFs’ ratings of the PFs were statistically different from the “same as average PF” rating, all of the average PNF ratings were close to the “same as average PF” or “satisfactory” rating (i.e., never strayed from it even as much as one rating point).

For Control Performance, the PNFs rated the No-Motion group to be marginally better than “Satisfactory: The same as average PF” in all experiment phases (T(18)≥1.84, p<.10). For the Motion group, the PNFs rated the control performance “Satisfactory: The same as average PF,” except after Training, where the PNFs rated the Motion group to be better than an average PF (T(19)=2.93, p<.01).

For Control Strategy and Technique, the PNFs rated the PFs significantly different than “the same as average PF” in all experiment phases (T(39)≥2.33, p<.05).

For Physical Workload, PNFs rated PFs in each group as “the same as average PF” during Evaluation and Quasi-Transfer Testing 1 (T(19)≤1.42, p>.10). During Training and Quasi-Transfer Testing 2, the PNFs perceived the No-Motion group as having a slightly lower than average PF Physical Workload (T(19 or 18)≥2.70, p<.01), while still considering the Physical Workload of the Motion group to be the same as the one of an average PF (T(19 or 18)≤1.16, p>.10).

For ease of Gaining Proficiency of the No-Motion group, PF ratings differed significantly or marginally from “just like average PF” during Training and Quasi-Transfer Testing (T(19 or 18)≥1.81, p<.10), indicating that it was very slightly easier for the No-Motion pilots than for an average pilot. For the Motion group, however, the PNFs did not perceive differences in the ease of Gaining Proficiency compared to an average PF, except during Training, where they also perceived it as very slightly easier (T(19)=2.28, p<.05).

In summary, although the PNFs did perceive some differences between the PFs in the experiment and an average PF in various phases of the experiment, these differences were very small.

### Summary of Opinions

In general, these data indicate that the perceptions of PFs and PNFs were little affected by the absence of motion. Most importantly, the data show that the simulator was perceived as equally acceptable with and without motion, and that PFs seemed to be equally comfortable in the simulator regardless of its motion status. The former is especially remarkable because the No-Motion group did rate the simulator slightly less like the airplane in terms of “Other cues,” presumably because many noticed that motion was lacking. The latter is important because it dispels concerns that the sensory conflict of having visual but not vestibular motion might have resulted in simulator sickness (see, e.g., Oman, 1991).

## Summary of Second Study

The purpose of the Second Study was to determine whether it was possible to improve hexapod motion to a level where it would affect transfer of airline-pilot performance and behavior between simulator and airplane for recurrent training and evaluation. A First Study that had tested the effect of “as is” motion had not found any systematic differences between the effectiveness of the simulator with the motion on and off. For the Second Study, the FAA-NASA CAE Level D Boeing 747-400 simulator was re-engineered to optimize the motion stimulation for the planned test maneuvers. Its lateral acceleration and heave were enhanced trading off rotational motion (mainly yaw) based on findings in the literature. Forty current B747-400 Captains and First Officers participated, aided by two cohort pilots performing non-flying duties. They were divided into two groups, one a Motion group that was evaluated, trained, and quasi-transfer tested in the simulator with the motion turned on throughout, and a No-Motion group that was evaluated and trained with the motion turned off before quasi-transferring to the simulator with motion.

During Evaluation and Quasi-Transfer Testing, the pilots flew full scenarios, departing with an engine failure either just before (V1 cut) or just after takeoff (V2 cut), and then continuing with either a precision instrument approach and landing with shifting crosswinds, or a Sidestep Landing with a vertical upward gust just after sidestepping to a parallel runway. To make the maneuvers even more difficult (and pilots did find them very difficult!) the autopilot and autothrottle were inoperative throughout and the flight director during the landings, which had to be hand flown. During Training, pilots flew three of each maneuver in a row, with graphic feedback on their performance after each maneuver. The maneuvers were chosen to 1) replicate the V1 cut tested in the First Study and 2) reduce any visual reference to the runway and require control in multiple axes compared to the First Study.

The results obtained with enhanced motion were different from the ones obtained in the First Study with “as is” motion. Several differences between the Motion and the No-Motion groups were found and a fairly clear picture of the effect of motion emerged. First, motion did appear to alert pilots of a disturbance faster than the visual cues alone, as stipulated in the literature based on theoretical considerations such as the time it takes for vection to develop, but only for the V1 cut. This may be because the V1 cut occurs close to the ground and any delay in response would result in a higher penalty than for the V2 occurring at a higher altitude, such as scraping the wings or the tail (which did happen, but equally rarely in the two groups, and usually because of applying the wrong rudder). Due to the motion alert, the Motion group had a faster pedal response and tracked heading slightly better, but the latter only during Evaluation. The No-Motion pilots, as long as they did not have the motion cue, were unable to significantly improve their pedal-response time, even during Training when they were told what failure to expect and caught up with the motion group for heading control. Once they quasi-transferred to motion, however, they immediately caught up with the Motion group even for pedal reaction time.. So, they didn’t seem to need recurrent training with motion to be able to sense and appropriately respond to motion cues.

Second, training with motion cues clearly increased the control activity of the Motion pilots, especially for wheel inputs. However, this reduced their flight precision, at least for the landing maneuvers. These performance decrements, in localizer, heading, or airspeed tracking, were in fact the largest effects found in the study, and may be operationally relevant. Most importantly, the performance deficit of the Motion group persisted even when both groups had motion at Quasi Transfer.

Perhaps the increased control activity of the Motion group was behind the curious result that for the V2 cut at Quasi Transfer, the Motion group responded slower to the engine failure than the No-Motion group, with apparently no effect on flight precision. It may be that the Motion group was fatigued. An alternative explanation would be that both groups were equally fatigued and that the emergence of the motion cues may have had “stimulating” effect on the No-Motion group. Overall, the V2 cut does appear to have been especially fatiguing for both groups, with several variables that had significantly improved during Training compared to Evaluation significantly deteriorating between Training and Quasi-Transfer Testing for both groups.

Third, motion affected the sidestep-landing strategy in a predictable manner. With motion, pilots landed softer. However, they also landed slightly farther from the runway threshold, but still well within the landing box. Like all effects on the landing maneuvers, this effect seems to have been consolidated during training, because it persisted even during Quasi-Transfer Testing.

Finally, both groups, regardless of motion, improved in the course of the experiment. Evaluation, however, was subject to motion effects for all four maneuvers.

These results were reflected in PF and PNF opinions. The PFs found the simulator equally acceptable compared to their company simulator regardless of group. They were also equally comfortable in it. Moreover, there was no difference between groups with respect to their comparisons of the simulator to the airplane for Control Sensitivity and Control Strategy and Technique.

There were four questions on which the two PF groups disagreed, and one of these was in favor of no motion: after Training, the No-Motion group gave the simulator higher handling-quality ratings than the Motion group gave. The ratings of the Motion group were higher than the ones of the No-Motion group for Control Feel (even at Quasi Transfer, when the No-Motion group also had motion), Other Cues (the majority of No-Motion pilots did recognize that something was amiss) and Performance (only after Evaluation).

The PNFs ratings were mostly in favor of the No-Motion group, but sometimes this was due to one of the two PNFs, while the other didn’t always see a difference. They felt that the No-Motion pilots were more similar to the average pilot than the motion pilots with respect to Control Strategy and Technique (but not during Evaluation). They gave higher performance and lower workload ratings to the No-Motion pilots, except during Training. Only at Quasi Transfer, they gave better Gaining Proficiency ratings to the No-Motion pilots.

# General Discusssion and Conclusions

This report presents the results of two studies that examined the effect of enhanced hexapod-simulator motion on recurrent evaluation in the simulator, on the course of recurrent training in the simulator, and on quasi transfer of this recurrent training to the simulator with motion as a stand-in for the airplane.

The First Study examined the effect of motion on recurrent evaluation and training of commuter airline pilots in a Level C qualified simulator of a 30-seat turboprop airplane with wing-mounted engines. The simulator motion was left “as is," i.e., as it was FAA-qualified and used round-the-clock for airline-pilot training and checking. This study revealed no systematic differences due to motion or training with motion in pilot opinions, instructor/evaluator ratings and opinions, and in extensive data collected from the simulator.

In response to this study's and a follow-up investigation's findings that lateral acceleration in the simulator may be quite attenuated in at least some simulators used for airline-pilot training and evaluation, the Second Study was conducted using a Boeing 747-400 Level D simulator with modified lateral acceleration. The gain and the phase error distortion of sway and to a lesser of heave were improved. Because of the limitations of a hexapod-platform system, however, pitch and roll and especially yaw had to be attenuated accordingly. This enhanced motion resulted in several differences and leads to the emergence of a fairly clear picture of the role motion may have in recurrent airline-pilot training and evaluation.

Enhanced hexapod motion, such as the one used in this experiment, may be required for accurate recurrent evaluation of airline pilots. This conclusion is contingent upon whether the industry perceives the effect sizes found as operationally relevant.

For recurrent training, however, no benefit of the motion provided was found. In fact, results from the landing maneuvers showed that training without motion may lower control activity and improve pilot-vehicle performance at quasi transfer to the simulator with motion compared with training in the simulator with motion. Stimulation with motion cues may induce pilots to overcorrect, while training without motion may help pilots to adopt a more steady control strategy. Because this control strategy leads to successful performance, they maintained this strategy even at quasi transfer to motion. This conclusion may be dependent on task complexity.

The differential effects of motion on the test maneuvers confirm that the effect of motion depends on the characteristics of the flying task. The importance of the quality of motion is indicated by the emergence of an early alerting effect of motion during the V1 cut with enhanced lateral acceleration cues that was absent in the earlier study.

In conclusion, this study showed that enhanced hexapod motion, configured based on the guidelines in the literature, does have an effect. It appears to affect the accuracy of recurrent evaluation. However, the benefits for recurrent training remain questionable.

Results of this study and the previous hexapod motion research should assist the FAA in determining future research directions in the effort to develop improved motion standards. It may also contribute to finding a cost-effective solution to today’s airline evaluation and training needs via an appropriate combination of fixed-base and motion-base simulators.

References

Bjorkman, E.A. (1986). Flight Test Evaluation of Techniques to Predict Pilot Induced Oscillations. Masters Thesis, AFIT/GAE/AA/86J-1, Air Force Institute of Technology.

Boothe, E.M. (email with attached spreadsheet, October 26, 2000).

Bray, R.S. (1972). Initial Operating Experience with an Aircraft Simulator Having Extensive Lateral Motion. NASA TM X-62155.

Bürki-Cohen, J. (Ed.). (1996). Electronic Transcript of the Joint FAA/Industry Symposium on Level B Airplane Simulator Motion Requirements, Washington Dulles Airport Hilton, June 19-20.  Available: http://www.volpe.dot.gov/opsad/valreqju.html

Bürki -Cohen, J., Soja, N., and Longridge, T. (1998). Simulator Platform Motion—The Need Revisited. The International Journal of Aviation Psychology, 8(3), 293-317.

Bürki-Cohen, J., Boothe, E.M., Soja N.N., DiSario, R., Go, T., and Longridge T. (2000). Simulator fidelity – The effect of platform motion. Proceedings of the International Conference on Flight Simulation: The Next Decade. Royal Aeronautical Society, London, UK.

Bürki-Cohen, J., Soja, N.N., Go, T.H., Boothe, E.M., DiSario, R., Jo, Y.J. (2001): Simulator Fidelity: The Effect of Platform Motion. Report No. DOT/FAA/RD-01/XX, unpublished manuscript.

Bürki-Cohen, J., Go, T. H., Chung, W. W., Schroeder, J. A., Jacobs, S., and Longridge, T. (2003). Simulator Fidelity Requirements for Airline-Pilot Training and Evaluation Continued: An Update on Motion Requirements Research. Proceedings of the 12th International Symposium on Aviation Psychology. Dayton, OH.

Bussolari, S. R., Young, L. R., Lee, A. T. (1987). The use of vestibular models for design and evaluation of flight simulator motion. Paper presented at the Aerospace Medical Panel Symposium on Motion Cues in Flight Simulation and Simulator Induced Sickness, Brussels, Belgium, September.

Federal Aviation Administration (1991). Airplane Simulator Qualification. Advisory Circular No. 120-40B, U.S. Department of Transportation, Washington, DC.

Federal Aviation Administration (2001). Airline Transport Pilot and Aircraft Type Rating: Practical Test Standards for Airplane. FAA-S-8081-5D with change 1. Flight Standards Service. U.S. Department of Transportation, Washington, DC.

Go, T. H., Bürki-Cohen, J., and Soja, N.N. (2000). The effect of simulator motion on pilot training and evaluation (AIAA 2000-4296). American Institute of Aeronautics and Astronautics.

Go, T. H., Bürki-Cohen, J., Chung, W. W., Schroeder, J. A., Saillant, G., Jacobs, S., and Longridge, T. (2003). The Effects of Enhanced Hexapod Motion on Airline-Pilot Recurrent Training and Evaluation (AIAA 2003-5678). American Institute of Aeronautics and Astronautics.

Guedry, F.E. (1968). Conflicting sensory orientation cues as a factor in motion sickness. Paper presented at the Fourth Symposium on the Role of the Vestibular Organs in Space Exploration, Naval Aerospace Medical Institute, Pensacola, FL.

Gundry, J. (1976). Man and motion cues. Paper presented at the Third Flight Simulation Symposium, London, UK.

Hall, J.R. (1978). Motion versus visual cues in piloted flight simulation (AGARD CP-249). Paper presented at the Flight Mechanics Panel Specialists Meeting on Piloted Aircraft Environment Simulation Techniques, Brussels, Belgium.

Hall, J.R. (1989). The Need for Platform Motion in Modern Piloted Flight Training Simulators (Technical Memorandum FM 35). Royal Aerospace Establishment, London, UK.

Hess, R. A. (1989). Theory for Aircraft Handling Qualities Based on a Structural Pilot Model. Journal of Guidance, Control, and Dynamics, 12(6), 792-797.

Homans, G. C. (1958). Group Factors in Worker Productivity. In E. Maccoby, T. Newcombs, and E. Hartley (Eds.), Readings in Social Psychology, New York: Holt.

Hosman, R. (1999). Are Criteria for Motion Cueing and Time Delays Possible? (AIAA 99-4028). American Institute of Aeronautics and Astronautics.

Hosman, R.J.A.W. and van der Vaart, J.C. (1981). Effects of vestibular and visual motion perception on task performance. Acta Psychologica, 48, 271-287.

Lahiri, A. (2000). Significance of a qualitative handling assessment approach towards motion system requirements for flight simulators. Proceedings of the International Conference on Flight Simulation - A Decade of Regulatory Change: Has the Situation Changed for the Better? Royal Aeronautical Society, London, UK.

Levison, W. H. (1981). Effects of whole-body motion simulation on flight skill development (Final Report AFOSR-TR-82-006). Bolling Air Force Base, Air Force Office of Scientific Research, Washington, DC.

Longridge, T., Ray, P., Boothe, E., and Bürki-Cohen, J. (1996). Initiative towards more affordable flight simulators for U.S. commuter airline training. Proceedings of the International Conference on Training - Lowering the Cost, Maintaining the Fidelity. Royal Aeronautical Society, London, UK.

Meiry, J.L. (1966). The Vestibular System and Human Dynamic Space Orientation. NASA CR-628, 1966.

Mikula, J., Chung, W, and Tran, D. (1999). Motion Fidelity Criteria for Roll-Lateral Translational Tasks (AIAA 99-4329). American Institute of Aeronautics and Astronautics.

Mulder, M., Chiecchio, J., Pritchett, A., and van Paassen, M. (2003). Testing Tunnel-in-the-Sky Displays and Flight Control Systems With and Without Flight Simulator Motion. Proceedings of the 12th International Symposium on Aviation Psychology. Dayton, OH.

Oman, C. (1991). Sensory conflict in motion sickness: An observer theory approach. In S. R. Ellis, M. K. Kaiser, & A. C. Grunwald (Eds.), Pictorial communication in virtual and real environments (pp. 362-376). New York: Taylor and Francis.

Reid, L. D., & Nahon, M. A. (1988). Response of airline pilots to variations in flight simulator motion algorithms. Journal of Aircraft, 25(7), 639-646.

Roscoe, S. N. (1991). Simulator qualification: Just as phony as it can be. The International Journal of Aviation Psychology, 1(4), 335-339.

Scanlon, C. H. (1987). Effect of Motion Cues During Complex Curved Approach and Landing Tasks. NASA TP-2773.

Sinacori, J.B. (1977). The Determination of Some Requirements for a Helicopter Flight Research Simulation Facility. NASA CR-152066.

Schroeder, J.A. (1999) Helicopter Flight Simulator Motion Platform Requirements. NASA TP-208766.

Schroeder, J., Chung, W., Tran, D., Laforce, S. (1998). Pilot-induced oscillation prediction with three levels of simulation motion displacement (AIAA 98-4333). American Institute of Aeronautics and Astronautics.

Waag, W.L. (1981). Training Effectiveness of Visual and Motion Simulation (Report AFHRL-TR-79-72). Airforce Human Resource Laboratory, Brooks Air Force Base, Texas.

White, A. D. (1994). The impact of cue fidelity on pilot behaviour and performance. Bedford, United Kingdom: FDS Department, Defence Research Agency.

Young, L. R. (1978). Visually Induced Motion in Flight Simulation. AGARD CP-249, pp. 16-1-16-8.

Zaichik, L. E., Rodchenko, V. V., Rufov, I. V., Yashin, Y. P., White, A. D. (1999). Acceleration perception (AIAA 99-4334). American Institute of Aeronautics and Astronautics.

FIRST STUDY RESULTS

Resolution (power)

Table A1-1 summarizes the Group and Phase effect sizes (defined as the minimum difference between the standardized means that will lead to the rejection of the null hypothesis with a probability of .80) of several important variables for the analyses done here.

| Maneuver | Measure | Effect Size |
| --- | --- | --- |
|  |  | Group | Phase |
| V1 Cut | STD bank | .67 deg | .78 deg |
|  | STD HDG deviation | .64 deg | .74 deg |
|  | Pedal RT (s) | .70 s | .81 s |
| RTO | RMS lateral deviation | 6.10 ft | 7.58 ft |
|  | STD HDG deviation | .84 deg | 1.05 deg |
|  | Power lever RT (s) | .43 s | .54 s |

Table A1-1. First Study Detectable Group and Phase Effects

V1 Cut Pilot-Vehicle Performance and Pilot Behavior

For this maneuver, the dependent variables used in the MANOVA are listed below (18 variables). For a discussion of the results in comparison with the results of the Second Study, see 5.3.3.5.

# Performance

STD and average failure-induced heading deviation (average of heading deviation in the direction of the failed engine)

STD bank angle and average failure induced bank angle (average of bank angle in the direction of the failed engine)

STD pitch angle

Average airspeed exceedance (average of airspeed exceeding the (5 knots about the desired airspeed)

# Behavior

Roll and yaw activities (average of absolute roll and yaw rates)

Pedal reaction time

Root mean square (RMS) and number of reversals of column, wheel, and pedal responses

Response bandwidth of the column, wheel, and pedal actions (frequency below which the corresponding power spectral density curves are .5 of total area)

# MANOVA results for Group and Phase effects

Marginally significant Group effect: Wilks’ Lambda (=.745, F(18,89)=1.69, p=.06

Highly significant Phase effect: (=.50, F(36,178)=2.04, p=.001

No Group and Phase interaction: (=.72, F(36,178)=.87, p=.68

| Variable | Mean | Statistics |
| --- | --- | --- |
|  | Motion | No-motion | F(1,106) | p |
| Wheel reversals | 3.00 | 3.58 | 4.23 | .04 |
| Wheel BW (Hz) | .12 | .09 | 6.03 | .02 |
| Pedal reversals | 1.50 | 1.08 | 10.17 | .002 |

Table A1-2. First Study V1 Cut Group Differences (Marginal)

| Variable | Mean | Differences | Statistics |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,106) | p |
| Failure-induced bank (deg) | 3.12 | .40 | 1.26* | 1.66* | 11.62 | <.0001 |
| STD pitch (deg) | 4.18 | .29 | .73* | 1.02* | 10.48 | <.0001 |
| Roll activity (deg/s) | 3.90 | .21 | .50 | .71* | 3.26 | .04 |
| RMS pedal (in) | .80 | .06 | .10 | .16* | 3.79 | .03 |

* indicates significant difference (p<.05)

Table A1-3. First Study V1 Phase Differences (I=Evaluation, II=Training, III=Quasi –Transfer Testing)

V1 Cut Summary

The finding of no difference between Motion and No-Motion group in pedal reaction time indicated that the motion of the test simulator did not provide the alerting function to the pilots. The motion cues in this case only affected pilots’ lateral-directional control activities as indicated by differences in wheel reversals and bandwidth as well as pedal reversals between the groups. Regardless of Group, general improvement was observed on bank and pitch performance as well as reduction in lateral-directional control activities at Quasi Transfer.

Rejected Takeoff (RTO) Pilot-Vehicle Performance and Pilot Behavior

The dependent variables used in the MANOVA for RTO are as follows (8 variables):

# Performance

STD and maximum heading deviation

RMS lateral deviation (from runway centerline)

# Behavior

Yaw activities (average of absolute roll and yaw rates)

Power lever reaction time (the duration from the time when the failed engine torque reduces to 80% of its full power to the time when the torque of the good engine has been reduced to 80%)

Root mean square (RMS) and number of reversals of pedal responses

Pedal response bandwidth

# MANOVA results for Group and Phase effects

No Group effect: Wilks’ Lambda (=.89, F(8,81)=1.28, p=.27

Highly significant Phase effect: (=.62, F(16,162)=2.74, p=.0006

No Group and Phase interaction: (=.80, F(16,161)=1.21, p=.27

| Variable | Mean | Differences | Stats |
| --- | --- | --- | --- |
|  |  | I-II | II-III | I-III | F(2,88) | p |
| Max heading (deg) | 7.56 | 1.56 | 1.84* | 3.40* | 9.85 | .0001 |
| RMS pedal (in) | .98 | .13 | .26 | .39* | 5.01 | .009 |
| Pedal BW (Hz) | .06 | -.01 | -.05* | -.07* | 7.19 | .001 |

* indicates significant difference (p<.05)

Table A1-4. RTO Results for Phase (I=Evaluation, II=Training, III=Quasi-Transfer Testing)

# RTO Summary

The motion cues did not have any effects on RTO, as no differences between groups were found for any of the variables. This result might be driven by the fact that in the RTO maneuver, the airplane was always on the ground, and hence the pilots relied more on runway visual cues than motion cues. Regardless of Group, improvement was observed during Quasi-Transfer Testing on heading performance, and this seemed to be achieved by using a different control strategy (lower pedal RMS but higher bandwidth).

Individual Training Progress

The individual training progress was examined by looking at the difference in the percentage of pilots that improved from First (Evaluation) to Last Training, Last Training to Quasi-Transfer Testing, and from First Training to Quasi-Transfer Testing. Variables examined were related to PF control performance (pedal reaction time, STD heading, and STD bank for V1 cut; power lever reaction time, STD heading, and RMS lateral deviation for RTO) and control activities (RMS wheel and RMS pedal). A greater than 15% reduction in the value of a variable from one level of the experiment to the later one was considered an improvement. Fisher’s Exact test was then used to examine whether the difference in the percentages of improved pilots between groups was significant. The summary of the results for V1 cut and RTO is shown in Table A1-5 and Table A1-6.

| Variable | 1st to Last Training | 1st Training to QT | Last Training to QT |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| Pedal RT | 22.2 | 36.8 | .27 | 20.0 | 31.3 | .38 | 25.0 | 27.8 | .58 |
| STD heading | 27.8 | 26.3 | .60 | 33.3 | 43.8 | .41 | 18.8 | 50.0 | .06 |
| STD bank | 27.8 | 15.8 | .31 | 40.0 | 62.5 | .19 | 50.0 | 50.0 | .63 |
| RMS Wheel | 16.7 | 10.5 | .47 | 26.7 | 43.8 | .27 | 12.5 | 11.1 | .74 |
| RMS Pedal | 27.8 | 5.3 | .08 | 53.3 | 81.3 | >.1 | 43.8 | 83.3 | .02 |

Table A1-5 Fisher’s Exact Statistics of Group Differences in Percentage Improvement Among First Training, Last Training, and Quasi-Transfer Testing for V1 Cut

| Variable | 1st to Last Training | 1st Training to QT | Last Training to QT |
| --- | --- | --- | --- |
|  | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p | % Improved | Fisher’s Exact p |
|  | Mot | No-Mot |  | Mot | No-Mot |  | Mot | No-Mot |  |
| Power lever RT | 46.7 | 38.5 | .48 | 40.0 | 40.0 | .66 | 25.0 | 23.1 | .63 |
| STD heading | 53.3 | 38.5 | .34 | 60.0 | 50.0 | .47 | 25.0 | 38.5 | .35 |
| RMS lateral deviation | 53.3 | 38.5 | .34 | 60.0 | 50.0 | .47 | 37.5 | 23.1 | .34 |
| RMS Wheel | 26.7 | 15.4 | .40 | 26.7 | 40.0 | .39 | 12.5 | 38.5 | .12 |
| RMS Pedal | 40.0 | 46.2 | .52 | 53.3 | 80.0 | .18 | 43.8 | 53.8 | .43 |

Table A1-6. Fisher’s Exact Statistics of Group Differences in Percentage Improvement Among First Training, Last Training, and Quasi-Transfer Testing for RTO

Comparison of Failure-Induced Lateral Acceleration of Several Simulators

| Simulator | Aircraft Weight (lbs) | Engine Type | Engine Failure Speed (kts) | Failed Engine Power Decay Time (s) | Maximum Failure-Induced Lateral Acceleration from EOM at cg (g) | Maximum Failure-Induced Lateral Acceleration from motion drive equations at pilot station (g) |
| --- | --- | --- | --- | --- | --- | --- |
| B737-200 | 99330 | Turbofan | 135 | 7.6 | 0.078 |  |
| B737-800 | 151699 | Turbofan | 129 | 8.9 | 0.062 |  |
| A-320#1 | 141975 | Turbofan | 131 | 14.3 | 0.04 | 0.04 |
| B747-400 | 626400 | Turbofan | 125 | 7.0 | 0.071 | 0.070 |
| B737-300* |  | Turbofan | 118 |  | 0.062 | 0.047 |
| A-330-300* |  | Turbofan | 135 |  | 0.065 | 0.059 |
| B757* |  | Turbofan | 120 |  | 0.002 | 0.003 |
| SAAB 340* |  | Turboprop | 117 |  | 0.078 | 0.025 |
| Test sim (auto test) | 17893 | Turboprop | 84 | 1.2 | 0.1 | 0.06 |
| Test sim (from experiment)# | 20500 | Turboprop | 110 | 1.2 | 0.21 | 0.069 |

*From initial analysis only (Boothe, 2000).

#For this comparison, a V1 cut maneuver with grade 3 is used.

Note: Blank cells on the table indicate the data are not available.

Table A1-7. V1 Cut Lateral Acceleration Data from Several Simulators

As can be seen from 0, the values of the maximum failure-induced lateral acceleration from the equations of motion at cg as obtained from the automatic testing, mostly fell within .04 and .1 g. An exception is the value reported for the B757 simulator, which was unusually low (.002 g). Unfortunately, this information could not be studied further due to the data loss. The values of the maximum failure-induced lateral acceleration from the equations of motion of the test simulator obtained in the experiment were in general higher than the values from the automatic testing (.2 to .3 g). The values of the failure-induced lateral acceleration from the motion drive equations were in general about the same or lower than the respective values from the equations of motion. With the exception of the B757 simulator, these values ranged from .025 to .07 g. Again, the value of the lateral acceleration from the motion drive equations of the B757 simulator was unusually low. The discrepancy between the maximum failure-induced acceleration from the equations of motion and from the motion drive equations was relatively large for the Saab 340 simulator and the test simulator.

Instructor/Evaluator Grades

A set of fourteen I/Es tested between one and nine crews and provided grades after each maneuver. To control bias, they were counterbalanced across motion conditions and were unaware of the purpose of the experiment. The simulator displays indicated that the motion was on and the motion was washed out only after initialization. The grades ranged between 1 (unsatisfactory) and 4 (excellent). Grades of 2 and 3 meant that the crew satisfied the PTS or company standards, respectively.

The I/E grades were examined in many different ways, for Group effects during the different phases, for differences in Group improvement between phases, for differences in percentages of crews improved, for differences between the number of crews receiving (extremely) low vs. high grades, etc. (see Bürki-Cohen et al., 2001, for details). Only one of these analyses found a statistically significant difference in grades due to the motion variable. Figure A1-1 shows the percentage of grades in each grading category as a function of maneuver, trial, and Motion group during Evaluation and Quasi-Transfer Testing. The I/Es did perceive differences in the performance of the V1 cut during Quasi-Transfer Testing, when both groups had motion: They gave more grades of 1 to the crews trained without motion (N = 32, Fisher Exact p=.05). The groups received an equal number of grades of 3 and neither group received any grades of 4, so the difference was all in the number of grades of 1 and 2.

Figure A1-1. First Study Percentage of Grades in Each Grading Category as a Function of Maneuver, Phase, and Group

SAMPLE DAILY CALIBRATION TEST

BRIEFING OF PILOT FLYING

###### PILOT BRIEFING

What is this all about?

Simulators have become indispensable for safe and effective pilot training and evaluation. You will be helping us to design simulators that will best serve that purpose.

U.S. DOT Volpe Center, NASA Ames Research Center, and FAA have jointly determined the test plan. We have made every effort to design an experiment that will lead to improved simulator training and evaluation for all pilots.

What are we asking you to do?

Flying

You will be asked to fly challenging scenarios in the simulator. We rely on you to fly as precisely as possible. For example, no matter how difficult a departure or a landing maneuver is, you should try to align the flight path with the runway centerline as accurately as possible. You will be given a chance to practice the maneuvers with graphical feedback on the precision of your flight path. It is critical that you make any effort to improve your performance based on the feedback. The best performers before and after practice will receive an award after completion of the experiment. But remember, you are an experienced pilot, and your ability to perform well (or not so well) reflects on the simulator, not on your performance on the line.

Please note that you are the Pilot Flying and have total responsibility and command of the aircraft. Your non-flying pilot is not familiar with your airline’s procedures, so just command what you wish and he will execute that command.

Questionnaires

After each flying phase, you will be filling out a questionnaire. Your opinions are critical in improving the simulator. We will ask some questions over and over again--please answer them based on the maneuvers you have flown since the last questionnaire. Feel free to add any comments. At the end, you will be given chance to give us additional feedback.

Please reserve all comments for the questionnaires, so that your opinions are documented. Do not discuss them with the Pilot Not Flying or the technicians.

Sequence

##### Morning

Briefing (30 min)

Phase I: Flying & Questionnaires (1.5 hrs)

Break with refreshments (30 min)

Phase II: Flying w/ feedback, Quest. (2.5 hrs)

##### Afternoon

Lunch (1 hr 15 min)

Phase III: Flying & Questionnaires (2 hrs)

Debriefing

Need for Discretion

To draw valid conclusions from this experiment, it is critical that all participants are fresh to the experiment without expectations or preconceived opinions. Thus, please encourage your colleagues to participate, but don’t discuss your experience with them. We will provide you with a full report after the conclusion of the experiment.

###### Local Area Flight Plan for NASA 123

This is a training flight remaining in the DFW area.

Weather and equipment are legal for takeoff and landing.

All takeoffs are to use maximum thrust.

NOTAM: ILS 36R inoperative.

Airport, Weather, and Aircraft Information

| For takeoff |
| --- |
| Dallas Forth Worth Airport, TX |
|  | Runway | 36 R |
|  | Runway Length | 11,388 feet |
|  | Elevation | 575 feet MSL |
|  | Time of Day | Day |
| Weather |
|  | Ceiling | 600 feet |
|  | Visibility | RVR 600/600/600 |
|  | Temperature | 15 oC |
|  | Wind | 175o at 10 knots |
|  | Altimeter Setting | 29.92 |
|  | Takeoff Alternate | DEN |
| Airplane |  |
|  | Inoperative Systems | Autothrottle |
|  | Takeoff Weight | 550,000 pounds |
|  | Zero Fuel Weight | 490,000 pounds |
|  | Center of Gravity | 22% Mac |
|  | Flap Setting | 10 |
|  | V1 | 121 KIAS |
|  | VR | 129 KIAS |
|  | V2 | 150 KIAS |

AIR-TRAFFIC-CONTROL SCRIPT

# EVALUATION & TRANSFER TESTING PHASES: SCENARIO 1

Scen_1   FAA Motion Vr Cut  #1  Land 36L      Scenario 111  Button 2  

Aircraft positioned on DFW Runway 36R and configured for takeoff with 10º Flaps.  No Autothrottles.

Dept ATIS		 “Tango”

# TANGO  (T.O.  R36R  V1 and VR cuts)

Dallas Ft. Worth International departure information TANGO, 1750 Zulu weather, Winds 170 at 10,  visibility one quarter mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Right in use.  Advise you have information TANGO.

Twr Freq:		   124.15

DFW Tower:		Nasa 123, after departure, maintain runway heading, climb and 3,500, wind 170   degrees at 10, runway 36R, cleared for takeoff.

After VR & 20 feet AGL    # 1 engine failure         (flameout..... later a loss of oil, to preclude a restart)

Runway heading, during engine shutdown and aircraft cleanup, to maintain 3,500 feet MSL.

Pilot will notify DFW Tower of engine problem.  (Confederate pilot will ensure no engine restart).

DFW Tower:	Nasa 123, roger, continue on runway heading, maintain 3,500, contact departure on 118.55

After Nasa123 contacts departure control, vector the flight, left turn to west (270 degrees) for about 5 NM from DFW for approach to 36L.

Regional DEP:	Nasa 123, departure, radar contact, maintain 3,500, pilots discretion turn left heading 270 for vector to ILS runway 36L final approach course.

# Pilot will then acknowledge instructions.

# Regional DEP gives weather update

Regional DEP: 	Nasa 123, new DFW weather, visibility 1 mile, fog, ceiling 500 overcast, altimeter 29.92.

Vector the flight, left turn to south (180 degrees) on downwind leg, about 5 NM abeam DFW.

Regional DEP:	Nasa 123, turn left heading 180, contact Approach on 118.42.

# Pilot contacts approach control and approach control acknowledges.

At a point abeam the airport on downwind:

# Regional APP: 	Nasa 123, descend and maintain 2,500. Verify you have Information Lima.

# LIMA  (Land  R36L,  after VR cut)

Dallas Ft. Worth International arrival information LIMA, 1810 Zulu weather, Wind 220 at 10,  visibility one mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Left and runway 36 Right in use.  Advise you have information LIMA.

When flight abeam CHARR, vector the flight, left turn to east (090 degrees).

DFW Tower gives latest RVR:     Runway 36L RVR 5200 Feet

Regional APP:	Nasa 123, turn left heading 090, Runway 36L RVR 5,200

2 1/2 NM from LOC intercept, vector the flight, left turn to 020 degrees, cleared ILS 36L.

Regional APP:	Nasa 123, 6 miles from BOBIN, turn left heading 020, maintain 2,500 until established on the localizer, cleared ILS Runway 36L Approach.

# Disconnect Autopilot when wings level and before localizer capture.

At BOBIN, disconnect  flight directors.      (Raw Data Approach with GS out minimums of MDA 1020¹ (432¹ AGL) and RVR 5200 or 1-mile visibility).

At BOBIN or when established on localizer switch to Tower Freq.

Regional APP:	Nasa 123, contact tower on 124.15

DFW Tower:		Nasa 123, Wind 220 degrees at 10, Runway 36L RVR 5,200, cleared to land Runway 36L.

After landing:

DFW Tower:		Nasa 123, after landing roll, stop on the runway.

FREEZE SIMULATOR WHEN A/C COMES TO A FULL STOP                 

EVALUATION & TRANSFER TESTING PHASES: SCENARIO 2

Scen_2   FAA Motion V1 Cut #4 S/S Land 36R    Scenario 121  Button 3 

Aircraft positioned on DFW Runway 36R and configured for takeoff with 10º Flaps.  No Autothrottles.

Dept ATIS		 “Tango”

TANGO  (T.O.  R36R  V1 and VR cuts)

Dallas Ft. Worth International departure information TANGO, 1750 Zulu weather, Wind 170 at 10,  visibility one quarter mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Right in use.  Advise you have information TANGO.

Twr Freq:		   124.15

DFW clears NASA 123 for takeoff.

DFW Tower:		Nasa 123, after departure, maintain runway heading, climb and maintain 3,500, wind 170 degrees at 10, Runway 36R, cleared for takeoff.

After V1    # 4 engine failure         (flameout..... later a loss of oil, to preclude a restart)

Runway heading, during engine shutdown and aircraft cleanup, to maintain 3,500 feet MSL.

Pilot will notify DFW Tower of engine problem.  (Confederate pilot will ensure no engine restart).

DFW Tower:		Nasa 123, roger, continue on runway heading, maintain 3,500, contact departure on 118.55

After Nasa123 contacts departure control, vector the flight, left turn to west (270 degrees) for about 5 NM from DFW for approach to 36L.

Regional DEP: 	Nasa 123, departure, radar contact, maintain 3,500, pilots discretion turn left heading 270 for vector to ILS runway 36L final approach course.

Pilot will then acknowledge instructions.

Regional DEP gives weather update

Regional DEP: 	Nasa 123, new DFW weather, visibility 5, mist, ceiling 1,100 overcast, altimeter 29.92.

Vector the flight, left turn to south (180 degrees) on downwind leg, about 5 NM abeam DFW.

Regional DEP: 	Nasa 123, turn left heading 180, contact Approach on 118.42.

# Pilot contacts approach control and approach control acknowledges.

# At a point abeam the airport on downwind.

Regional APP: 	Nasa 123, descend and maintain 2,500, expect ILS Runway 36L Approach, sidestep to Runway 36R. Verify you have Information Mike.

b

MIKE  (Land   R36 L or R36R)

Dallas Ft. Worth International arrival information MIKE, 1810 Zulu weather, Wind 310 at 10,  visibility five mile, ceiling 1100 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Left and runway 36 Right in use.  Advise you have information MIKE.

When flight abeam CHARR, vector the flight, left turn to east (090 degrees).

Regional APP: 	Nasa 123, turn left heading 090.

2 1/2 NM from LOC intercept, vector the flight, left turn to 020 degrees, cleared ILS 36L.

Regional APP: 	Nasa 123, six miles from BOBIN, turn left heading 020, maintain 2,500 until established on the localizer, cleared for ILS Runway 36L Approach, sidestep Runway 36R.

Disconnect Autopilot when wings level and before localizer capture.

At BOBIN, disconnect flight directors.      (Raw Data Approach with GS out minimums of MDA 1020¹ (432¹ AGL) and RVR 5000 or 1-mile visibility).

When Nasa 123 is established on the localizer.

# Regional APP: 	Nasa 123 contact DFW tower on 124.15.

# After Nasa 123 contacts DFW tower.

# DFW Tower:		Nasa 123, report Runway 36R in sight.

# When Nasa 123 reports Runway 36R in sight.

DFW Tower:		Nasa 123, wind 310 degrees at 10,  cleared to land Runway 36R.

After landing:

DFW Tower:		Nasa 123, after landing roll, stop on the runway.

FREEZE SIMULATOR WHEN A/C COMES TO A FULL STOP

# TRAINING PHASE: MANEUVER 1

m1(scen_1) FAA Motion Vr Cut #4 T/O Only   Scenario 211   Button 5 

Aircraft positioned on DFW Runway 36R and configured for takeoff with 10º Flaps and no Autothrottles.

Dept ATIS		 “Tango”

# TANGO  (T.O.  R36R  V1 and VR cuts)

Dallas Ft. Worth International departure information TANGO, 1750 Zulu weather, Wind 170 at 10,  visibility one quarter mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Right in use.  Advise you have information TANGO.

Twr Freq:		   124.15

DFW Tower:		Nasa 123, after departure, maintain runway heading, climb and 3,500, wind 170 degrees at 10, Runway 36R, cleared for takeoff.

After VR & 20 feet AGL    # 4 engine failure         (flameout)

Runway heading, during engine shutdown and aircraft cleanup commencing at 800¹ AGL.

SIMULATOR  WILL FREEZE AT 2000 FEET MSL.

# TRAINING PHASE: MANEUVER 2

m2(scen_1) FAA E4 36L (Land Only)     Scenario 212   Button 9

Aircraft positioned outside of CHARR heading 020º to intercept the ILS 36L Localizer, with #4 Engine shutdown, no Autothrottles, Autopilots on for approximately 15 seconds until aircraft stabilizes then OFF and Flight Directors OFF at BOBIN (OM).

Arr ATIS		 “Echo”

# ECHO  (Land R36 L,  #4 eng cut)

Dallas Ft. Worth International arrival information ECHO, 1810 Zulu weather, Wind 130 at 10,  visibility one mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Left and runway 36 Right in use.  Advise you have information ECHO.

APP Freq:		  118.42

Regional APP:	Nasa 123, continue heading 020, maintain 2500 until established on the localizer, cleared for ILS 36L Approach. Runway 36L RVR 5,200.

Approaching Outer Marker:

# Regional APP:	Nasa123, Contact Tower on 124.15

DFW Tower:		Nasa 123, wind 130 degrees at 10, cleared to land Runway 36L.

DFW Tower:		Nasa 123, after landing roll, stop on the runway.

FREEZE SIMULATOR WHEN A/C COMES TO  A FULL STOP

# TRAINING PHASE: MANEUVER 3

m3(scen_2) FAA Motion V1 Cut #1 T/O    Scenario 221   Button 6

Aircraft positioned on DFW Runway 36R and configured for takeoff with 10º Flaps. No Autothrottles.

Dept ATIS		 “Tango”

# TANGO  (T.O.  R36R  V1 and VR cuts)

Dallas Ft. Worth International departure information TANGO, 1750 Zulu weather, Wind 170 at 10,  visibility one quarter mile fog, ceiling 500 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Right in use.  Advise you have information TANGO.

Twr Freq:		   124.15

DFW Tower:		Nasa 123, after departure, maintain runway heading, climb and maintain 3,500 hundred, wind 170 degrees at 10, Runway 36R, cleared for takeoff.

After V1    # 1 engine failure         (flameout)

Runway heading, during engine shutdown and aircraft cleanup commencing at 800¹ AGL.

SIMULATOR  WILL FREEZE AT 2000 FEET MSL.

# TRAINING PHASE: MANEUVER 4

m4(scen_2) FAA E1 36R (Land Only S/S)    Scenario 222   Button 8

Aircraft positioned outside of CHARR heading 020º to intercept the ILS 36L Localizer, with #1 Engine shutdown, no Autothrottles, Autopilots on for approximately 15 seconds until aircraft stabilizes then OFF and Flight Directors off at OM. Microburst on approximately a 2 mile final.

Arr ATIS		 “Mike”

MIKE  (Land   R36 L or R36R)

Dallas Ft. Worth International arrival information MIKE, 1810 Zulu weather, Wind  310 at 10,  visibility five mile, ceiling 1100 overcast, temperature 15, dewpoint 13, altimeter 29.92.  Runway 36 Left and runway 36 Right in use.  Advise you have information MIKE.

APP Freq:		  118.42

Regional APP:	Nasa 123, continue heading 020, maintain 2500 until established on the localizer, cleared for ILS Runway 36L Approach, sidestep Runway 36R.

Approaching Outer Marker:

# Regional APP:	Nasa 123 contact DFW tower on 124.15.

After Nasa 123 contacts DFW tower:

DFW Tower:		Nasa 123, report runway 36R in sight.

When Runway 36R reported in sight:

DFW Tower:		Nasa 123, wind 310 degrees at 10, cleared to land Runway 36R.

After landing:

DFW Tower:	 	Nasa 123, after landing roll, stop on the runway.

FREEZE SIMULATOR WHEN A/C COMES TO A FULL STOP

EXPERIMENT PROTOCOL

| #34, P17FRN4213 Date: 8/19/02 Motion: off Seat: R Training Sequence: 4-2-1-3 PF: John Doe (17 ldgs) PNF: John Doe ATC: John Doe Handedness: L Airline: Anonymous |
| --- |
| Abnormalities | Action |  | Comments |
| Eval, crash on t/o | Print and put in air for landing |  | Has happened |
| Eval go around | Print, go to next scenario |  | Has happened |
| Trg, crash on t/o | Print and beam up, go to next training |  | Has happened |
| Trg go around | Print and beam up, go to next training |  | Has happened |
| Test, crash on t/o | Print and restart scenario |  | Has happened |
| Test, go around | Print, go to next scenario |  | Has happened |
| PIA instead of SS set up during trg | Freeze as soon as possible, print, do correct scenario |  | Has happened |
| Motion off during evaluation scenario | Turn motion on ASAP. If full scenario is flown, administer extra PFQ3, then continue. |  | Has happened |
| Time/Phase/Place | Action | Responsible | Check/Comments |
| Day before |  |  |  |
|  | Check that enough disk space on system next to VCRs for daily checks. If not, type “mv *.0 /tmp/chung/” |  |  |
|  | Check that pilot lounge “clean” | BC/jbc/TG/GS |  |
|  | Make sure that there are 16 blank tapes (and ask Gary to reorder when stock gets low) | BC/jbc/TG/GS |  |
|  | Determine PNF and Seat, check which counterbalancing cells are open for high and low experience | BC/jbc/TG/GS/Jerry |  |
|  | Check coffee and paper cup stocks (in pilot lounge) | BC/jbc/TG/GS |  |
|  | Unwrap 16 and label at least 8 audio/video tapes (4 for backups), remove cover, label top and back Name Condition Seat PNF Training Sequence Tape recorder (1 in rack, 2, 3, 4 stacked on table--3 for backup of 2, 4 for backup of 1) and number, e.g., for first tape, 1/1; 2/1; BU 1/1; BU2/1). Note: ‘BU’ means ‘BackUp’ Date Insert first tapes, have second tape ready on rack/recorder (hide label) | BC/jbc/TG/GS |  |
|  | Paperwork in brown binder and folders Protocols Consent form: fill in PI fields and study PFBriefing Display examples 3 PFQuestionnaires PFFinal Comments 4 PNFQuestionnaires Flyers for pilot to recruit | BC/jbc/TG/GS |  |
| Throughout | Keep track of protocol and mark GTM time in left hand column | BC/jbc/TG/GS |  |
|  | NASA experiment log | Jim/Charley |  |
|  | Check that correct maneuver set up (especially for ldg, where it can be seen on plot) | BC/jbc/TG/GS |  |
|  | Do tell them that training phase will be longest, and that they will be told what’s coming. Do not tell them about any others, just that they’ll do “some more flying.” | BC/jbc/TG/GS |  |
|  | Hide anything that could give away purpose of study, pilots wander into control room. | All |  |
| Before PF arrives |  |  |  |
|  | Buy refreshments (water and doughnuts, napkins) for morning and afternoon breaks | BC/jbc/TG/GS |  |
|  | Simulator set up for correct airline, see Comments on Airline configuration at the end of this document. | Jerry |  |
|  | Simulator check ride | Jerry |  |
|  | Data recording set up | Charley |  |
|  | Color printer on, paper tray full, no color low indicator (call Gary) | BC/jbc/TG/GS |  |
|  | Feedback displays | Dave |  |
|  | Make sure coffee is ready all day | BC/jbc/TG/GS |  |
|  | Daily Check: motion, sound, visual, force feedback, graphs from sim and displays. Procedure in Phase 1 folder, password on back. | Jerry |  |
|  | Collect daily check paper work and label (1 p. color, 7 pp b/w) | BC/jbc/TG/GS |  |
|  | Set up sim for exp (FMC, etc) | Jerry |  |
|  | Communication check | Jerry |  |
|  | Engine sound full power | Jerry |  |
|  | “Motion on” and initialization | Jerry |  |
|  | Check cameras (must be on correct seat) | BC/jbc/TG/GS |  |
|  | Check video/audiotape sound w/ headphones on both recorders | BC/jbc/TG/GS |  |
| After PF arrives |  |  |  |
| In briefing room | Below 1000 total hrs/Above 1000 hrs in 747 and number of landings in the past 12 months. | BC/jbc/TG/GS |  |
|  | Sign consent form three times, including authorization to videotape and release of data! Also, address and phone number | BC/jbc/TG/GS |  |
|  | Briefing by experimenter. Show displays(mention to fly flight director as precisely as possible). “NASA test pilot.” | BC/jbc/TG/GS |  |
|  | Briefing by Jerry, but no info on maneuvers. Fuel constant. | Jerry |  |
| In control room | Determine motion group and maneuver training sequence based on PFQ1, 1st page (# of landings in the past 12 months, also 747-400 hours). | BC/jbc/TG/GS |  |
|  | Print out protocol w/ all available info filled in, ONE-SIDED for copying | BC/jbc/TG/GS |  |
|  | Configure simulator motion | Charley |  |
|  | Configure training sequence | Charley |  |
|  | Data collection standby | Charley |  |
|  | Audio/video standby On VCR 3, make sure that set for S-VHS | BC/jbc/TG/GS |  |
|  | Script standby | Charley |  |
|  | Communications standby | Charley |  |
| PHASE I | EVALUATION |  |  |
| PF and PNF enter cab | Safety briefing | Jerry |  |
|  | Establish communications | Charley |  |
|  | Initialize motion regardless of config | Charley |  |
|  | Washout motion if no-motion | Charley |  |
|  | Set-up | Charley/ PNF |  |
| GTM: | Play/Record on (ALWAYS) Do VCR 3 first because of delays: 1) Wait for “00:00” display 2) Press “Rec” and wait for calibration to finish For VCR4: press “Rec” and “Pause” buttons at the same time to bring the VCR to the ready-to-record state. Wait for red circle. Press “Play” button hard to start the recording. Make sure that #s scroll. | BC/jbc/TG/GS |  |
|  | Briefing, no info on maneuvers & failures | PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL |  |  |
| GTM: | Fly Scenario 1 (VR w/ PIA on 36L) # 1 failure. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
| GTM: | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, no info on maneuvers & failures | PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly Scenario 2 (V1 cut w/SS to 36R) # 4 failure. After microburst, PNF mentions microburst so that pilot knows that it is not something wrong with sim. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Turn off motion regardless of config, tell pilots | Charley |  |
|  | Data collection off | Charley |  |
| PF and PNF exit cab to briefing room |  |  |  |
| GTM: | Stop Audio/video taping, new tape? | BC/jbc/TG/GS |  |
|  | PF fills out PF Questionnaire 1 (“NASA test pilot,” difference between Control Feel and Control Sensitivity, browse headings to see where to put comments, ensure correct comparison, “we want to know how well the sim represents the airplane,” point out comparison (sim - a/c or sim-sim), make sure that they compare their performance in the sim with their presumed performance in the a/p under exactly the same condition) | BC/jbc/TG/GS |  |
|  | PNF fills out PNF Questionnaire 1 | PNF |  |
|  | Food & Drink | BC/jbc/TG/GS |  |
|  | Detail brief pilot on displays collected during scenario 2. “Shows whether you are w/in Practical Test Standard tolerances.” Point out if they violate something grossly (new after P01MRT ignored speed—mention to follow flight director. | BC/jbc/TG/GS |  |
|  | Bathroom |  |  |
| PHASE II | TRAINING: fail opposite engine. FD always off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. |  |  |
| In control room | Training sequence standby | Charley |  |
|  | Data collection standby | Charley |  |
|  | Audio/video standby | BC/jbc/TG/GS |  |
|  | Feedback displays standby | Charley |  |
| PF and PNF enter cab |  |  |  |
|  | Establish communications | Charley |  |
|  | Initialize motion regardless of config | Charley |  |
|  | Washout motion if no-motion run | Charley |  |
| Training 1 | Set-up | Charley/ PNF |  |
| GTM: | Play/Record on: All scrolling? | BC/jbc/TG/GS |  |
|  | Briefing, announce failure/weather. First of three. | PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly first training maneuver | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilots ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. 2nd of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL |  |  |
| GTM: | Fly first training maneuver 2nd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. Last of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly first training maneuver 3rd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
| Training 2 | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. First of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 2nd training maneuver | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilots ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. 2nd of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 2nd training maneuver 2nd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. Last of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 2nd training maneuver 3rd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Check audio/videotape. NEW TAPE? (make sure that done with discussion before changing!) | BC/jbc/TG/GS |  |
|  | Verify that new tape is correctly labeled, stow used tape, put third tape ready on recorder or rack, respectively | BC/jbc/TG/GS |  |
| Training 3 | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. First of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 3rd training maneuver | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilots ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. 2nd of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 3rd training maneuver 2nd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. Last of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 3rd training maneuver 3rd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Check hardcopies and printer messages. Erase when pilot ready | Charley |  |
| Training 4 | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. First of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 4th training maneuver | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilots ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. 2nd of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM | Fly 4th training maneuver 2nd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase displays when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, announce failure/weather. Last of 3. | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly 4th training maneuver 3rd time | Charley/ PNF |  |
|  | Print and beam up display(s) | Charley |  |
|  | Check hardcopies and printer messages. Erase when pilot ready | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Ensure understandability of PFQ1 | BC/jbc/TG/GS |  |
|  | Turn off motion regardless of config, tell pilots | Charley |  |
|  | Data collection off | Charley |  |
| PF and PNF exit cab to briefing room |  |  |  |
|  | Stop Audio/video taping, new tape? | BC/jbc/TG/GS |  |
|  | PF fills out PF Questionnaire 2 | BC/jbc/TG/GS |  |
|  | PNF fills out PNF Questionnaire 2 | PNF |  |
|  | Lunch | Jerry |  |
|  | Bathroom |  |  |
| PHASE III | TESTING ALL WITH MOTION |  |  |
| PF and PNF enter cab |  |  |  |
|  | Establish communications | Charley |  |
|  | Initialize motion | Charley |  |
|  | Do Not Wash it Out | Charley |  |
|  | Set-up | Charley/ PNF |  |
| GTM: | Play/Record on: All scrolling? | BC/jbc/TG/GS |  |
| Testing 1 | Briefing, no info on maneuvers & failures | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly Scenario 1 (VR w/ PIA on 36L) # 1 failure. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, no info on maneuvers & failures | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly Scenario 2 (V1 cut w/SS to 36R) # 4 failure. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Ensure understandability of PFQ2 | BC/jbc/TG/GS |  |
|  | Turn off motion regardless of config, tell pilots | Charley |  |
|  | Data collection off | Charley |  |
| PF and PNF exit cab to briefing room |  |  |  |
| GTM: | Stop Audio/video taping, NEW TAPE? | BC/jbc/TG/GS |  |
|  | Verify that new tape is correctly labeled, stow used tape | BC/jbc/TG/GS |  |
|  | PF fills out PF Questionnaire 3 | BC/jbc/TG/GS |  |
|  | PNF fills out PNF Questionnaire 3 | PNF |  |
|  | Coffee | BC/jbc/TG/GS |  |
|  | Bathroom |  |  |
| PF and PNF enter cab |  |  |  |
|  | Establish communications | Charley |  |
|  | Initialize motion | Charley |  |
|  | Do Not Wash it Out | Charley |  |
|  | Set-up | Charley/ PNF |  |
| GTM: | Play/Record on: All scrolling? | BC/jbc/TG/GS |  |
| Testing 2 | Briefing, no info on maneuvers & failures | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly Scenario 1 (VR w/ PIA on 36L) # 1 failure. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Set-up | Charley/ PNF |  |
|  | Briefing, no info on maneuvers & failures | Charley/ PNF |  |
|  | Feedback displays on, collect data | Charley |  |
|  | Check: Motion status, Record (all scrolling?), HDG SEL | BC/jbc/TG/GS |  |
| GTM: | Fly Scenario 2 (V1 cut w/SS to 36R) # 4 failure. FD off at outer marker (Bobin). Turn autopilot off before diamond on FD is w/in ½ dot of centerline. | Charley/ PNF |  |
|  | Print displays (t/o 2 p., app. 1 p.) But don’t beam up | Charley |  |
|  | Check hardcopies and printer messages and erase (for app., check that erased after turn) | Charley |  |
|  | Label hardcopies close to frame: Phase, Scenario/ Maneuver, Date | BC/jbc/TG/GS |  |
|  | Ensure understandability of PFQ3 | BC/jbc/TG/GS |  |
|  | Turn off motion regardless of config, tell pilots | Charley |  |
|  | Data collection off | Charley |  |
| PF and PNF exit cab to debriefing room |  |  |  |
| GTM: | Stop Audio/video taping | BC/jbc/TG/GS |  |
|  | PF fills out Final Comments | BC/jbc/TG/GS |  |
|  | PNF fills out PFQ4 | BC/jbc/TG/GS |  |
|  | Ensure understandability of PFFC | BC/jbc/TG/GS |  |
| Pilot leaves | THANK YOU & send friends! | All |  |
|  | Experimenter talks to PNF | BC/jbc/TG/GS |  |
| POST EXPERIMENT CHORES (Please fill out and give dates) |
|  | Secure data and label | Dave |  |
|  | Back-up data | Dave |  |
|  | FTP data to Volpe | Dave |  |
|  | Secure videotapes and verify label | BC/jbc/TG/GS |  |
|  | Secure paperwork, incl. NASA log & protocol | BC/jbc/TG/GS |  |
|  | Copy paperwork | BC/jbc/TG/GS |  |
|  | Double check paperwork copies | BC/jbc/TG/GS |  |
|  | File paperwork and videotapes | BC/jbc/TG/GS |  |
|  | Send data on CD to Volpe | Dave |  |
|  | Send paperwork to Volpe (bring to Sally in shipping in Bill’s building) | BC/jbc/TG/GS |  |
|  | Send videotapes to Volpe (ditto) | BC/jbc/TG/GS |  |

# Comments on Airline configuration:

If the pilot is from Northwest airline then the Northwest configuration is selected.  For UAL pilots, the UAL configuration is used.

For other airline’s pilots, ask whether they use the dual or single cue flight director and then select the UAL or NWA configuration respectively.

UAL configuration (default), as described by Jerry:

- The UAL PFD is a dual cue flight director.

- The radio altimeter is at the bottom of the attitude indicator just above the localizer scale.

- The DH is displayed beneath the bottom right corner of the attitude indicator, and the MDA is displayed above the top right corner of the attitude indicator.

- On landing there are aural callouts for 50 ft, 30 ft and 10 ft.

Northwest configuration, as described by Jerry:

- The Northwest PFD is a single cue flight director.

- The radio altimeter is displayed above the top right corner of the attitude indicator and so is the DH.

- The MDA is displayed below the bottom right corner of the attitude indicator.

On landing the radio altimeter emits aural tones at 100 ft, 35 ft and 20 ft.

PILOT-FLYING QUESTIONNAIRES

###### Pilot Flying ( Questionnaire 1

General Information

# Today’s Date: _____________

Time: _____________

First Name: ________________Last Name:_________________

Currently flying as a B-747-400 Captain ____First Officer____

Name of PNF during experiment: _______________________

Experience in airplanes

# Last time you have flown the B747-400 airplane:  ___________

# Number of landings in B747-400 airplane in past 12 months: _______

# Pilot time in B747 airplanes: ___________ hours

# Pilot time in glass cockpit airplanes (incl. B747): ___________ hours

# Total flight time: ___________ hours

Experience in 747-400 full flight simulator (Level C/D) before today:

# Number of simulator landings in past 12 months: ________

# Pilot time in 747-400 simulator: ___________ hours

Last 747-400 full flight simulator flown (Level C or D):

When: _____________Where: _____________________

Instructions for Questionnaires:

- In these questionnaires you are asked to evaluate the NASA 747-400 simulator. You are asked to make one of two comparisons, as indicated on each page:

  - the NASA 747-400 simulator (as flown today) to the B747-400 airplane

  - the NASA 747-400 simulator today to the last 747-400 simulator you have flown.

- Please base all of your judgments on the maneuvers that you have flown so far today or, if applicable, since you have filled out the last questionnaire.

- For comparisons with the airplane, you may have to base your judgments on how you would expect the airplane to behave during these maneuvers.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Control Feel

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of control loading, i.e., the amount of effort you need to operate the controls.

Note: Control sensitivity (amount of response generated by the control inputs) will be treated on the next page.

# The control feel in the NASA 747-400 simulator was...

| Controls | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much lighter than airplane | moderately lighter | slightly lighter | just like the airplane | slightly heavier | moderately heavier | much heavier than airplane |
| Rudder input |  |  |  |  |  |  |  |
| Aileron input |  |  |  |  |  |  |  |
| Elevator input |  |  |  |  |  |  |  |
| Throttles |  |  |  |  |  |  |  |
| Yaw trim input |  |  |  |  |  |  |  |
| Roll trim input |  |  |  |  |  |  |  |
| Pitch trim input |  |  |  |  |  |  |  |
| Overall control feel |  |  |  |  |  |  |  |
| Please elaborate if control feel is different from airplane |

Control Sensitivity

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the amount of response generated by the control actions (control sensitivity).

# The control sensitivity of the NASA 747-400 simulator was...

| Controls | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much less sensitive than airplane | moderately less sensitive | slightly less sensitive | just like the airplane | slightly more sensitive | moderately more sensitive | much more sensitive than airplane |
| Yaw control |  |  |  |  |  |  |  |
| Roll control |  |  |  |  |  |  |  |
| Pitch control |  |  |  |  |  |  |  |
| Throttle control |  |  |  |  |  |  |  |
| Overall control sensitivity |  |  |  |  |  |  |  |
| Please elaborate if control sensitivity is different from airplane |

Handling Qualities

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of ease and precision in performing the tasks.

# Remember: You have already evaluated control feel and sensitivity.

# The handling qualities of the NASA747-400 simulator were...

| Task | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than airplane | moderately worse | slightly worse | just like the airplane | slightly better | moderately better | much better than airplane |
| Pitch control |  |  |  |  |  |  |  |
| Bank angle control |  |  |  |  |  |  |  |
| Yaw control |  |  |  |  |  |  |  |
| Altitude control |  |  |  |  |  |  |  |
| Heading control |  |  |  |  |  |  |  |
| Airspeed control |  |  |  |  |  |  |  |
| Overall handling qualities |  |  |  |  |  |  |  |
| Please elaborate if handling qualities are different from airplane |

Control Strategy and Technique

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of how you flew the maneuvers and compensated for mechanical and weather disturbances, i.e., whether you had to adapt the sequence, amount, and type of controls you used.

My strategy and technique to fly the maneuvers in the NASA 747-400 simulator was...

| Maneuver | 1 | 2 | 3 | 4 | Please elaborate if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Other Cues

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of any other cues perceived during the maneuvers.

Remember: You have already evaluated control feel, sensitivity, and handling qualities.

I perceived other cues in the NASA 747-400 simulator during each maneuver as…

| Maneuver | 1 | 2 | 3 | 4 | Please elaborate if different than airplane |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Pilot Performance

Compare your performance in the NASA 747-400 simulator to your performance in the B747-400 airplane.

# My performance in the NASA747-400 simulator was...

| Task | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than in airplane | moderately worse | slightly worse | just like in the airplane | slightly better | moderately better | much better than in airplane |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Please elaborate if different from performance in airplane |

Physical and Mental Workload

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the physical and mental workload

associated with flying the maneuvers.

# Workload in the NASA 747-400 simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than airplane | moderately higher | slightly higher | the same as airplane | slightly lower | moderately lower | much lower than airplane |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is different from airplane |
| Mental |  |  |  |  |  |  |  |
| Please elaborate if mental workload is different from airplane |

Physical Comfort

Compare the NASA 747-400 simulator to the last 747-400 SIMULATOR you have flown

in terms of the absence of nausea or simulator-induced disorientation.

# My physical comfort in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than in the last simulator | moderately worse | slightly worse | just like the last simulator | slightly better | moderately better | much better than in the last simulator |
| Overall comfort |  |  |  |  |  |  |  |
| Please elaborate if comfort is different from last simulator |

Acceptability

# Compare the NASA 747-400 simulator to

the last 747-400 simulator you have flown

in terms of your acceptance based on your perception of the presence or absence of deficiencies that might affect your flying.

# Acceptability of the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than last simulator flown | moderately worse | slightly worse | just like the last simulator flown | slightly better | moderately better | much better than last simulator flown |
| Overall acceptability |  |  |  |  |  |  |  |
| Please elaborate if acceptability is different from last simulator |

###### Pilot Flying ( Questionnaire 2

General Information

# Today’s Date: _____________

Time: _____________

First Name: _________________ Last Name: _________________

Currently flying as a B-747-400 Captain ____First Officer____

Name of PNF during experiment: _______________________

Instructions for Questionnaire 2

- As in the previous questionnaire, you are asked to make one of two comparisons, as indicated on each page:

  - the NASA 747-400 simulator (as flown today) to the B747-400 airplane

  - the NASA 747-400 simulator today to the last 747-400 simulator you have flown.

- Please answer all questions based on the maneuvers that you have flown since Questionnaire 1. Some questions are the same as in Questionnaire 1.  This is to see whether your opinions have changed after spending more time in the simulator.

- Again, for comparisons with the airplane, you may have to base your judgments on how you would expect the airplane to behave during these maneuvers.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Gaining Proficiency

Compare the NASA 747-400 simulator to the last 747-400 simulator you have flown in terms of the ease of gaining the proficiency necessary to perform satisfactorily in controlling the airplane.

Gaining proficiency in the NASA simulator compared to the last simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much harder | moderately harder | slightly harder | just like in the last simulator | slightly easier | moderately easier | much easier |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Overall gain of proficiency |  |  |  |  |  |  |  |
| Please elaborate if gaining proficiency is different from the last simulator |

Control Feel

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of control loading, i.e., the amount of effort you need to operate the controls.

Note: Control sensitivity (amount of response generated by the control inputs) will be treated on the next page).

During training, the control feel in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much lighter than airplane | moderately lighter | slightly lighter | just like the airplane | slightly heavier | moderately heavier | much heavier than airplane |
| Overall control feel |  |  |  |  |  |  |  |
| If overall control feel is different from airplane, please indicate which of the controls mainly affect your opinion Rudder input Aileron input Elevator input Throttles Yaw trim input Roll trim input Pitch trim input All of the above |

Control Sensitivity

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the amount of response generated by the control actions (control sensitivity).

During training, the control sensitivity of the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much less sensitive than airplane | moderately less sensitive | slightly less sensitive | just like the airplane | slightly more sensitive | moderately more sensitive | much more sensitive than airplane |
| Overall control sensitivity |  |  |  |  |  |  |  |
| If overall control sensitivity is different from airplane, please indicate which of the controls mainly affect your overall opinion Yaw control Roll control Pitch control Throttle control All of the above |

Handling Qualities

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of ease and precision in performing the tasks.

# Remember: You have already evaluated control feel and sensitivity.

During training, the handling qualities of the NASA747-400 simulator were...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than airplane | moderately worse | slightly worse | just like the airplane | slightly better | moderately better | much better than airplane |
| Overall handling qualities |  |  |  |  |  |  |  |
| If overall handling qualities are different from the airplane, please indicate which of the tasks mainly affect your opinion Pitch control Bank angle control Yaw control Altitude control Heading control Airspeed control All of the above |

Control Strategy and Technique

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of how you flew the maneuvers and compensated for mechanical and weather disturbances, i.e., whether you had to adapt the sequence, amount, and type of controls you used.

During training, my strategy & technique to fly the maneuvers in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |
| Overall control strategy and technique |  |  |  |  |
| If overall control strategy and technique are different from the airplane, please indicate during which of the maneuvers and how Engine cut at V1 Engine cut at VR Engine-out straight-in approach/ldg Engine-out side-step landing All of the above |

Other Cues

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of any other cues perceived during the maneuvers.

Remember: You have already evaluated control feel, sensitivity, and handling qualities.

During training, I perceived other cues in the NASA 747-400 simulator during each maneuver as…

| Maneuver | 1 | 2 | 3 | 4 | Please elaborate if different than airplane |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Physical and Mental Workload

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the physical and mental workload

associated with flying the maneuvers.

# During training, workload in the NASA 747-400 simulator was …

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than airplane | moderately higher | slightly higher | the same as airplane | slightly lower | moderately lower | much lower than airplane |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is different from airplane |
| Mental |  |  |  |  |  |  |  |
| Please elaborate if mental workload is different from airplane |

Physical Comfort

Compare the NASA 747-400 simulator to the last 747-400 SIMULATOR you have flown

in terms of the absence of nausea or simulator-induced disorientation.

During training, my physical comfort in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than in the last simulator | moderately worse | slightly worse | just like the last simulator | slightly better | moderately better | much better than in the last simulator |
| Overall comfort |  |  |  |  |  |  |  |
| Please elaborate if comfort is different from last simulator |

Acceptability

# Compare the NASA 747-400 to

the last 747-400 simulator you have flown

in terms of your acceptance based on your perception

of the presence or absence of deficiencies that might affect your flying.

# Acceptability of the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than last simulator flown | moderately worse | slightly worse | just like the last simulator flown | slightly better | moderately better | much better than last simulator flown |
| Overall acceptability |  |  |  |  |  |  |  |
| Please elaborate if acceptability is different from last simulator |

###### Pilot Flying ( Questionnaire 3

General Information

Today’s Date: _____________

Time: _____________

# First Name: __________________Last Name: _________________

# Currently flying as a B-747-400 Captain ____First Officer____

# Name of PNF during experiment: _______________________

Instructions for Questionnaire 3:

- As in the previous questionnaires, you are asked to make one of two comparisons, as indicated on each page:

  - the NASA 747-400 simulator (as flown today) to the B747-400 airplane

  - the NASA 747-400 simulator today to the last 747-400 simulator you have flown.

- Please answer all questions based on the maneuvers that you have flown after the break. Some questions are the same as in the previous questionnaires.  This is to see whether your opinions have changed after performing the last two scenarios in the simulator.

- Again, for comparisons with the airplane, you may have to base your judgments on how you would expect the airplane to behave during these maneuvers.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Control Feel

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of control loading, i.e., the amount of effort you need to operate the controls.

Note: The amount of response generated by the control inputs will be treated on the next page.

After the break, the control feel in the NASA 747-400 simulator was...

| Controls | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much lighter than airplane | moderately lighter | slightly lighter | just like the airplane | slightly heavier | moderately heavier | much heavier than airplane |
| Rudder input |  |  |  |  |  |  |  |
| Aileron input |  |  |  |  |  |  |  |
| Elevator input |  |  |  |  |  |  |  |
| Throttles |  |  |  |  |  |  |  |
| Yaw trim input |  |  |  |  |  |  |  |
| Roll trim input |  |  |  |  |  |  |  |
| Pitch trim input |  |  |  |  |  |  |  |
| Overall control feel |  |  |  |  |  |  |  |

Control Sensitivity

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the amount of response generated by the control actions (control sensitivity).

After the break, the control sensitivity of the NASA 747-400 simulator was...

| Controls | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much less sensitive than airplane | moderately less sensitive | slightly less sensitive | just like the airplane | slightly more sensitive | moderately more sensitive | much more sensitive than airplane |
| Yaw control |  |  |  |  |  |  |  |
| Roll control |  |  |  |  |  |  |  |
| Pitch control |  |  |  |  |  |  |  |
| Throttle control |  |  |  |  |  |  |  |
| Overall control sensitivity |  |  |  |  |  |  |  |
| Please elaborate if control sensitivity is different from airplane |

Handling Qualities

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of ease and precision in performing the tasks.

# Remember: You have already evaluated control feel and sensitivity.

After the break, the handling qualities of the NASA747-400 simulator were...

| Tasks | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than airplane | moderately worse | slightly worse | just like the airplane | slightly better | moderately better | much better than airplane |
| Pitch control |  |  |  |  |  |  |  |
| Bank angle control |  |  |  |  |  |  |  |
| Yaw control |  |  |  |  |  |  |  |
| Altitude control |  |  |  |  |  |  |  |
| Heading control |  |  |  |  |  |  |  |
| Airspeed control |  |  |  |  |  |  |  |
| Overall handling qualities |  |  |  |  |  |  |  |
| Please elaborate if handling qualities are different than airplane |

Control Strategy and Technique

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of how you flew the maneuvers and compensated for mechanical and weather disturbances, i.e., whether you had to adapt the sequence, amount, and type of controls you used.

After the break, my control strategy and technique to perform the maneuvers in the NASA 747-400 simulator was...

| Tasks | 1 | 2 | 3 | 4 | Please elaborate if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Other Cues

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of any other cues perceived during the maneuvers.

Remember: You have already evaluated control feel, sensitivity and handling qualities.

After the break, I perceived other cues in the NASA 747-400 simulator during each maneuver as…

| Task | 1 | 2 | 3 | 4 | Please elaborate how if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Pilot Performance

Compare your performance in the NASA 747-400 simulator to your performance in the B747-400 airplane.

After the break, my performance in the NASA747-400 simulator was...

| Task | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than in airplane | moderately worse | slightly worse | just like in the airplane | slightly better | moderately better | much better than in airplane |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Please elaborate if different from performance in airplane |

Physical and Mental Workload

# Compare the NASA 747-400 simulator to the B747-400 airplane

in terms of the physical and mental workload

associated with performing the tasks.

# After the break, workload in the NASA 747-400 simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than airplane | moderately higher | slightly higher | the same as airplane | slightly lower | moderately lower | much lower than airplane |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is higher/lower than in the airplane |
| Mental |  |  |  |  |  |  |  |
| Please elaborate if mental workload is different than in the airplane |

Physical Comfort

Compare the NASA 747-400 simulator to the last 747-400 SIMULATOR you have flown

in terms of the absence of nausea or simulator-induced disorientation.

After the break, my physical comfort in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than in the last simulator | moderately worse | slightly worse | just like the last simulator | slightly better | moderately better | much better than in the last simulator |
| Overall comfort |  |  |  |  |  |  |  |
| Please elaborate if comfort is different than in last simulator |

Acceptability

# Compare the NASA 747-400 simulator to

the last 747-400 simulator you have flown

in terms of your acceptance based on your perception of the presence or absence of deficiencies that might affect your flying.

# After the break, acceptability of the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much worse than last simulator flown | moderately worse | slightly worse | just like the last simulator flown | slightly better | moderately better | much better than last simulator flown |
| Overall acceptability |  |  |  |  |  |  |  |
| Please elaborate if acceptability is different from last simulator |

Gaining Proficiency

Compare the NASA 747-400 simulator to the last 747-400 simulator you have flown in terms of the ease of gaining the proficiency necessary to perform satisfactorily in controlling the airplane.

After the break, I felt that gaining proficiency in the NASA simulator compared to the last simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much harder | moderately harder | slightly harder | just like in the last simulator | slightly easier | moderately easier | much easier |
| Overall gain of proficiency |  |  |  |  |  |  |  |
| If different from last simulator, please elaborate which maneuvers mainly affect your judgment Engine cut at V1 Engine cut at VR Engine-out straight-in approach/ldg Engine-out sidestep landing All of the above |

###### Pilot Flying ( Final Comments

General Information

# Today’s Date: _____________

# Time: _____________

# First Name: __________________ Last Name: _________________

# Currently flying as a B-747-400 Captain ____First Officer____

# Name of PNF during experiment: _______________________

Instructions:

Please feel free to add comments on your experiences in the simulator today and any other aspects related to the experiment as prompted on the following pages.

REMEMBER: Your opinion counts!

Further comments on the control feel, control sensitivity, and any other cues you experienced in the NASA 747-400 simulator compared to the B747-400 airplane:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

Further comments on the handling qualities of the NASA 747-400 simulator and the strategies you used to control it compared to the B-747-400 airplane:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

Further comments on your ability to gain proficiency in the NASA 747-400 simulator compared to the last 747-400 simulator you have flown:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

Further comments on your physical comfort in the NASA 747-400 simulator compared to the last 747-400 simulator you have flown:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

Further comments on the overall acceptability of the NASA 747-400 simulator:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

# Further comments on any other aspects of the experiment:

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

_________________________________________________________________

We greatly appreciate your expertise. You will receive a report on the conclusions from the experiment after completion of data collection and analysis.

PILOT-NOT-FLYING QUESTIONNAIRES

###### Pilot Not Flying ( Questionnaire 1

General Information

# Today’s Date: _____________

# Time: _____________

# Name: _____________________

# Name of PF during experiment: _______________________

Instructions for Questionnaires:

- In these questionnaires you are asked to evaluate the performance of the pilot flying (PF).  Please compare the performance/workload of the PF to the performance/workload of an average PF performing the same maneuvers in the simulator. You may base “average” on any experiences you have had in trying out the maneuvers in the simulator, any past simulator experiences, and on the practical test standard guidelines.

- Please base all of your judgments on the maneuvers that the PF have flown so far.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

# Control Performance

# Compare the performance of the PF to average PF

in terms of the precision in controlling the airplane to perform the required maneuvers.

# The performance of the PF in performing each maneuver was …..

| Maneuver | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
|  | Unacceptable: Much worse than average | Unsatisfactory: Moderately worse than average | Satisfactory: The same as average | Good: Moderately better than average | Excellent: Much better than average |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

# Control Strategy and Technique

# Compare the PF to average PF

in terms of how the PF flew the maneuvers and compensated for mechanical and weather disturbances, i.e., whether the PF had to adapt the sequence, amount, and type of controls

he used.

The strategy and technique of the PF to fly the maneuvers in the NASA 747-400 simulator was...

| Maneuver | 1 | 2 | 3 | 4 | Please elaborate if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than average PF | moderately different | slightly different | the same as average PF |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Physical Workload

# Compare the PF to average PF

in terms of the physical workload associated with flying the maneuvers.

# Workload of the PF in the NASA 747-400 simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than average PF | moderately higher | slightly higher | the same as average PF | slightly lower | moderately lower | much lower than average PF |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is higher/lower than average PF |

###### Pilot Not Flying ( Questionnaire 2

General Information

# Today’s Date: _____________

# Time: _____________

# Name: _____________________

# Name of PF during experiment: _______________________

Instructions for Questionnaires:

- In these questionnaires you are asked to evaluate the performance of the pilot flying (PF).  Please compare the performance/workload of the PF to the performance/workload of an average PF performing the same maneuvers in the simulator. You may base “average” on any experiences you have had in trying out the maneuvers in the simulator, any past simulator experiences, and on the practical test standard guidelines.

- Please answer all questions based on the maneuvers that the PF have flown since Questionnaire 1. Some questions are the same as in Questionnaire 1.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Gaining Proficiency

# Compare the PF to average PF

in terms of the ease of gaining the proficiency

necessary to perform satisfactorily in controlling the airplane.

# During training, the gaining proficiency of the PF was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much harder than average PF | moderately harder | slightly harder | just like average PF | slightly easier | moderately easier | much easier than average PF |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Overall gain of proficiency |  |  |  |  |  |  |  |
| Please elaborate if gaining proficiency is easier/harder than average PF |

# Control Performance

# Compare the performance of the PF to average PF

in terms of the precision in controlling the airplane to perform the required maneuvers.

During training, the overall performance of the PF was …..

| Maneuver | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
|  | Unacceptable: Much worse than average | Unsatisfactory: Moderately worse than average | Satisfactory: The same as average | Good: Moderately better than average | Excellent: Much better than average |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

# Control Strategy and Technique

# Compare the PF to average PF

in terms of how the PF flew the maneuvers and compensated for mechanical and weather disturbances, i.e., whether PF had to adapt the sequence, amount, and type of controls

he used.

During training, the strategy and technique of the PF to fly the maneuvers in the NASA 747-400 simulator was...

|  | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
|  | very different than average PF | moderately different | slightly different | the same as average PF |
| Overall control strategy and technique |  |  |  |  |
| If overall control strategy and technique are different from average PF, please indicate during which of the maneuvers and how Engine cut at V1 Engine cut at VR Engine-out straight-in approach/ldg Engine-out sidestep landing All of the above |

Physical Workload

# Compare the PF to average PF

in terms of the physical workload associated with flying the maneuvers.

# During training, the physical workload of the PF in the simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than average PF | moderately higher | slightly higher | the same as average PF | slightly lower | moderately lower | much lower than average PF |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is higher/lower than average PF |

###### Pilot Not Flying ( Questionnaire 3

General Information

# Today’s Date: _____________

# Time: _____________

# Name: _____________________

# Name of PF during experiment: _______________________

Instructions for Questionnaires:

- In these questionnaires you are asked to evaluate the performance of the pilot flying (PF).  Please compare the performance/workload of the PF to the performance/workload of an average PF performing the same maneuvers in the simulator. You may base “average” on any experiences you have had in trying out the maneuvers in the simulator, any past simulator experiences, and on the practical test standard guidelines.

- Please answer all questions based on the maneuvers that the PF have flown after the break. Some questions are the same as in the previous questionnaires.  This is to see whether you noticed any changes in the PF performance/workload in performing the last two scenarios in the simulator.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Gaining Proficiency

# Compare the PF to average PF

in terms of the ease of gaining the proficiency

necessary to perform satisfactorily in controlling the airplane.

# After the break, the gaining proficiency of the PF was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much harder than average PF | moderately harder | slightly harder | just like average PF | slightly easier | moderately easier | much easier than average PF |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Overall gain of proficiency |  |  |  |  |  |  |  |
| Please elaborate if gaining proficiency is easier/harder than average PF |

# Control Performance

# Compare the performance of the PF to average PF

in terms of the precision in controlling the airplane to perform the required maneuvers.

# After the break, the overall performance of the PF was …..

| Maneuver | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
|  | Unacceptable: Much worse than average | Unsatisfactory: Moderately worse than average | Satisfactory: The same as average | Good: Moderately better than average | Excellent: Much better than average |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

# Control Strategy and Technique

# Compare the PF to average PF

in terms of how the PF flew the maneuvers and compensated for mechanical and weather disturbances, i.e., the sequence, amount, and type of controls  the PF used.

After the break, the strategy and technique of the PF to fly the maneuvers in the NASA 747-400 simulator was...

| Tasks | 1 | 2 | 3 | 4 | Please elaborate if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Physical Workload

# Compare the PF to average PF

in terms of the physical workload associated with flying the maneuvers.

# After the break, the physical workload of the PF in the simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than average PF | moderately higher | slightly higher | the same as average PF | slightly lower | moderately lower | much lower than average PF |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is higher/lower than average PF |

###### Pilot Not Flying ( Questionnaire 4

General Information

# Today’s Date: _____________

# Time: _____________

# Name: _____________________

# Name of PF during experiment: _______________________

Instructions for Questionnaires:

- In these questionnaires you are asked to evaluate the performance of the pilot flying (PF).  Please compare the performance/workload of the PF to the performance/workload of an average PF performing the same maneuvers in the simulator. You may base “average” on any experiences you have had in trying out the maneuvers in the simulator, any past simulator experiences, and on the practical test standard guidelines.

- Please answer all questions based on the maneuvers that the PF have flown during the final scenarios. Some questions are the same as in the previous questionnaires.  This is to see whether you noticed any changes in the PF performance/workload in performing the last two scenarios in the simulator.

- Please indicate each judgment by placing an X in the appropriate box. You may be asked to elaborate on your judgment in the space provided. Feel free to elaborate even if you are not specifically asked to do so.

Gaining Proficiency

# Compare the PF to average PF

in terms of the ease of gaining the proficiency

necessary to perform satisfactorily in controlling the airplane.

# During the final scenarios, the gaining proficiency of the PF was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | much harder than average PF | moderately harder | slightly harder | just like average PF | slightly easier | moderately easier | much easier than average PF |
| Engine cut at V1 |  |  |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |  |  |
| Overall gain of proficiency |  |  |  |  |  |  |  |
| Please elaborate if gaining proficiency is easier/harder than average PF |

# Control Performance

# Compare the performance of the PF to average PF

in terms of the precision in controlling the airplane to perform the required maneuvers.

# During the final scenarios, the overall performance of the PF was …..

| Maneuver | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
|  | Unacceptable: Much worse than average | Unsatisfactory: Moderately worse than average | Satisfactory: The same as average | Good: Moderately better than average | Excellent: Much better than average |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

# Control Strategy and Technique

# Compare the PF to average PF

in terms of how the PF flew the maneuvers and compensated for mechanical and weather disturbances, i.e., the sequence, amount, and type of controls  the PF used.

During the final scenarios, the strategy and technique of the PF to fly the maneuvers in the NASA 747-400 simulator was...

| Tasks | 1 | 2 | 3 | 4 | Please elaborate if different |
| --- | --- | --- | --- | --- | --- |
|  | very different than in airplane | moderately different | slightly different | the same as in airplane |  |
| Engine cut at V1 |  |  |  |  |  |
| Engine cut at VR |  |  |  |  |  |
| Engine-out straight-in approach/ldg |  |  |  |  |  |
| Engine-out sidestep landing |  |  |  |  |  |

Physical Workload

# Compare the PF to average PF

in terms of the physical workload associated with flying the maneuvers.

During the final scenarios, the physical workload of the PF in the simulator was…

|  | 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type of Workload | much higher than average PF | moderately higher | slightly higher | the same as average PF | slightly lower | moderately lower | much lower than average PF |
| Physical |  |  |  |  |  |  |  |
| Please elaborate if physical workload is higher/lower than average PF |

LIST OF RECORDED SIMULATOR VARIABLES

# Aircraft Motion

| No. | Variables | Unit |
| --- | --- | --- |
| 1 | Indicated Airspeed | knots |
| 2 | True Airspeed | knots |
| 3 | Ground Speed | knots |
| 4 | Vertical Speed | knots |
| 5 | Altitude | ft, MSL |
| 6 | Radar Altitude | ft, AGL |
| 7 | Rate Of Climb | ft/min |
| 8 | Pitch Attitude | degs |
| 9 | Pitch Rate, body axis | rad/s |
| 10 | Pitch Acceleration, body axis | rad/s2 |
| 11 | Roll Attitude | degs |
| 12 | Roll Rate, body axis | rad/s |
| 13 | Roll Acceleration, body axis | rad/s2 |
| 14 | Magnetic Heading | degs |
| 15 | True Heading | degs |
| 16 | Yaw Rate, body axis | rad/s |
| 17 | Yaw Acceleration, body axis | rad/s2 |
| 18 | Angle of Attack | degs |
| 19 | Angle of Sideslip | degs |
| 20 | X-body acceleration @ c.g., EOM | ft/s2 |
| 21 | Y-body acceleration @ c.g., EOM | ft/s2 |
| 22 | Z-body acceleration @ c.g., EOM | ft/s2 |
| 23 | Lateral Deviation (from initial position of aircraft) | ft |
| 24 | Ground Distance | ft |
| 25 | Longitude | degs |
| 26 | Latitude | degs |

# Aircraft Configuration

| No. | Variables | Unit |
| --- | --- | --- |
| 1 | Flap Position | degs |
| 2 | Spoiler Position | degs |
| 3 | Fuel Weight | lbs |
| 4 | c.g. location, w.r.t. aerodynamic center | %MAC |
| 5 | Engine 1 Failed Flag | T=failed |
| 6 | Engine 4 Failed Flag | T=failed |
| 7 | Engine 1 Thrust | lbs |
| 8 | Engine 2 Thrust | lbs |
| 9 | Engine 3 Thrust | lbs |
| 10 | Engine 4 Thrust | lbs |
| 11 | EPR 1 |  |
| 12 | EPR 2 |  |
| 13 | EPR 3 |  |
| 14 | EPR4 |  |
| 15 | Weight On Wheel, Nose Flag | T=weight on |
| 16 | Weight On Wheel, Left Main Flag | T=weight on |
| 17 | Weight On Wheel, Right Main Flag | T=weight on |
| 18 | Rudder Trim Position | units |
| 19 | Aileron Trim Position | units |
| 20 | Elevator Trim Position | units |
| 21 | Elevator Position | degs |
| 22 | Aileron Position | degs |
| 23 | Rudder Position | degs |
| 24 | Landing Gear Selector Handle Position Flag | T=up |

# Pilot Response

| No. | Variables | Unit |
| --- | --- | --- |
| 1 | Column Position | inches |
| 2 | Wheel Position | degs |
| 3 | Pedal Position | inches |
| 4 | Column Rate | lbs |
| 5 | Wheel Rate | lbs |
| 6 | Pedal Rate | lbs |
| 7 | Power Lever Position | % |
| 8 | Applied Brake Pressure, Pilot Left | psi |
| 9 | Applied Brake Pressure, Pilot Right | psi |
| 10 | Applied Brake Pressure, Copilot Left | psi |
| 11 | Applied Brake Pressure, Copilot Right | psi |
| 12 | Brake Pedal Position, Pilot Left | inches |
| 13 | Brake Pedal Position, Pilot Right | inches |
| 14 | Brake Pedal Position, Copilot Left | inches |
| 15 | Brake Pedal Position, Copilot Right | inches |

# Simulator/Motion Drive

| No. | Variables | Unit |
| --- | --- | --- |
| 1 | Aural volume | % |
| 2 | X-body acceleration @ pilot station | ft/s2 |
| 3 | Y-body acceleration @ pilot station | ft/s2 |
| 4 | Z-body acceleration @ pilot station | ft/s2 |
| 5 | Translational motion command gain, X-body |  |
| 6 | Translational motion command gain, Y-body |  |
| 7 | Translational motion command gain, Z-body |  |
| 8 | Roll motion command gain |  |
| 9 | Pitch motion command gain |  |
| 10 | Yaw motion command gain |  |
| 11 | Scaled and limited translational motion command, X-body | ft/s2 |
| 12 | Scaled and limited translational motion command, Y-body | ft/s2 |
| 13 | Scaled and limited translational motion command, Z-body | ft/s2 |
| 14 | Scaled and limited roll rate motion command | rad/s |
| 15 | Scaled and limited roll rate motion command | rad/s |
| 16 | Scaled and limited roll rate motion command | rad/s |
| 17 | Motion gain from the adaptive cost function, X-inertial |  |
| 18 | Motion gain from the adaptive cost function, Y-inertial |  |
| 19 | Motion gain from the adaptive cost function, Z-inertial |  |
| 20 | Motion gain from the adaptive cost function, roll |  |
| 21 | Motion gain from the adaptive cost function, pitch |  |
| 22 | Motion gain from the adaptive cost function, yaw |  |
| 23 | Roll attitude simulator command due to tilting | rad |
| 24 | Pitch attitude simulator command due to tilting | rad |
| 25 | Simulator translational displacement command, X-inertial | inch |
| 26 | Simulator translational displacement command, Y-inertial | inch |
| 27 | Simulator translational displacement command, Z-inertial | inch |
| 28 | Simulator angular displacement command, roll | degs |
| 29 | Simulator angular displacement command, pitch | degs |
| 30 | Simulator angular displacement command, yaw | degs |
| 31 | X-body acceleration @ pilot station, accelerometer | g |
| 32 | Y-body acceleration @ pilot station, accelerometer | g |
| 33 | Z-body acceleration @ pilot station, accelerometer | g |
| 34 | Roll rate body axis, rate gyro | rad/s2 |
| 35 | Pitch rate body axis, rate gyro | rad/s2 |
| 36 | Yaw rate body axis, rate gyro | rad/s2 |
| 37 | Roll attitude, potentiometer | degs |
| 38 | Pitch attitude, potentiometer | degs |
| 39 | Yaw attitude, potentiometer | degs |
| 40 | Actuator extension, leg 1 | inches |
| 41 | Actuator extension, leg 2 | inches |
| 42 | Actuator extension, leg 3 | inches |
| 43 | Actuator extension, leg 4 | inches |
| 44 | Actuator extension, leg 5 | inches |
| 45 | Actuator extension, leg 6 | inches |

LIST OF MEASURES CALCULATED PER SEGMENT

Engine Failure on Takeoff (V1 cut and V2 cut)

After Engine Failure to 800 ft AGL:

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate. |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation from the desired heading. |
|  |  | RMS Heading Deviation | Root mean square of deviation from the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Average Heading Exceedance | Average of the absolute heading deviation exceeding 5o around the desired heading |
|  |  | Average Failure Induced Heading | Integral of the heading deviation in the direction of the failed engine. |
|  | Time | Pedal Reaction Time | Time for the pedal position to exit 0.75-inch band about its initial position in response to engine failure. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | RMS Bank Angle | Root mean square of bank angle |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of 5o band around wing level position. |
|  |  | Average Failure Induced Bank Angle | Average of the absolute bank angle in the direction of the failed engine. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute Indicated Airspeed deviation outside 5 knots band about V2 (for V1 cut) or about V2+10 kts (for V2 cut) |
|  | Pitch Angle | STD Pitch Angle | Standard deviation of pitch angle. |

Engine Failure on Takeoff (V1 cut and V2 cut)

After Engine Failure to 800 ft AGL:

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal position power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectral density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position after engine failure (20 s for V1 cut and 10 s for V2 cut). |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel position power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectral density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position after engine failure (20 s for V1 cut and 10 s for V2 cut). |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position after engine failure (20 s for V1 cut and 10 s for V2 cut). |

Precision Instrument Approach

From Final Approach-Fix to the Decision-Height (432 ft AGL/1020 ft MSL):

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate. |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation around the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Average Heading Exceedance | Average of the absolute deviation exceeding (5o around the desired heading. |
|  | Localizer Deviation | STD Localizer Deviation | Standard deviation of horizontal deviation of the airplane from the localizer centerline. |
|  |  | Maximum Localizer Deviation | The maximum deviation of the airplane from the localizer centerline. |
|  |  | Average Localizer Exceedance | Average of absolute deviation exceeding (0.5 dot around localizer centerline. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of (5o band around wing level position. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute deviation outside 5 knots band about the desired airspeed. |
|  | Pitch Angle | STD Pitch Angle | Standard deviation of pitch angle. |
|  | Glide Slope Deviation | STD Glide Slope Deviation | Standard deviation of vertical deviation from the glide slope reference path. |
|  |  | Maximum Glide Slope Deviation | Maximum deviation from the glide slope reference path. |
|  |  | Average Glide Slope Exceedance | Average of vertical deviation exceeding (0.5 dot around the glide slope reference. |

Precision Instrument Approach

From Final Approach-Fix to the Decision-Height (432 ft AGL/1020 ft MSL):

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectral density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position during the first 70 s. |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectrum density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position during the first 70 s. |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position during the first 70 s. |

Precision Instrument Approach

From Decision-Height to Touchdown:

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate during the maneuver. |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation around the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Average Heading Exceedance | Average of the absolute deviation exceeding (5o around the desired heading. |
|  | Localizer Deviation | STD Localizer Deviation | Standard deviation of horizontal deviation of the airplane from the localizer centerline. |
|  |  | Maximum Localizer Deviation | The maximum deviation of the airplane from the localizer centerline. |
|  |  | Average Localizer Exceedance | Average of horizontal deviation exceeding (0.5 dot around localizer centerline. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of 5o band around wing level position. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute deviation outside 5 knots about the desired airspeed. |
|  |  | Touchdown Descent Rate | The initial vertical speed of the airplane at touchdown. |
|  | Pitch Angle | STD Pitch Angle | Standard deviation of pitch angle. |
|  | Glide Slope Deviation | STD Glide Slope Deviation | Standard deviation of vertical deviation from the glide slope reference path. |
|  |  | Maximum Glide Slope Deviation | Maximum vertical deviation from the glide slope reference path. |
|  |  | Average Glide Slope Exceedance | Average of vertical deviation exceeding (0.5 dot around the glide slope reference. |
|  | Distance | Touchdown Distance | Distance from runway threshold to the touchdown point. |

Precision Instrument Approach

From Decision-Height to Touchdown:

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectral density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position during the first 25 s. |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectral density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position during the first 25 s. |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position during the first 25 s. |

Sidestep Landing

From Final Approach-Fix to Breakout-of-Clouds (1688 ft MSL):

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate. |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation around the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Average Heading Exceedance | Average of the absolute deviation exceeding (5o around the desired heading. |
|  | Localizer Deviation | STD Localizer Deviation | Standard deviation of horizontal deviation of the airplane from the localizer centerline. |
|  |  | Maximum Localizer Deviation | The maximum deviation of the airplane from the localizer centerline. |
|  |  | Average Localizer Exceedance | Average of absolute deviation exceeding (0.5 dot around localizer centerline. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of (5o band around wing level position. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute deviation outside 5 knots band about the desired airspeed. |
|  | Pitch Angle | STD Pitch Angle | Standard deviation of pitch angle. |
|  | Glide Slope Deviation | STD Glide Slope Deviation | Standard deviation of vertical deviation from the glide slope reference path. |
|  |  | Maximum Glide Slope Deviation | Maximum deviation from the glide slope reference path. |
|  |  | Average Glide Slope Exceedance | Average of vertical deviation exceeding (0.5 dot around the glide slope reference. |

Sidestep Landing

From Final Approach-Fix to Breakout-of-Clouds (1688 ft MSL):

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectral density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position during the last 20 s. |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectral density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position during the last 20 s. |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position during the last 20 s. |

Sidestep Landing

From Breakout-of-Clouds to Upward-Gust:

Note: sidestep segment is defined from 800 ft to 200 ft to the left of target runway centerline.

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate . |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation from the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Maximum Sidestep Heading | Maximum deviation from desired heading in the sidestep segment. |
|  |  | Average Heading Exceedance | Average of the heading deviation exceeding (5o around the desired heading. |
|  | Localizer Deviation | Maximum Localizer Overshoot | Maximum deviation from the localizer centerline after sidestep. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Maximum Sidestep Bank Angle | Maximum absolute bank angle during sidestep. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of (5o band around wing level position. |
|  | Time | Sidestep Time | The time required to perform the sidestep maneuver. |
|  | Translational rate | Sidestep Rate | Lateral translational rate to travel through the sidestep segment. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute deviation outside 5 knots band about the desired airspeed. |
|  | Pitch Rate | Pitch Activity | Mean absolute pitch rate after. |
|  | Pitch Angle | STD Upset Pitch Angle | Standard deviation of pitch angle after the application of vertical gust. |
|  | Glide Slope Deviation | STD Glide Slope Deviation | Standard deviation of vertical deviation from the glide slope reference path. |
|  |  | Maximum Glide Slope Deviation | Maximum deviation from the glide slope reference path. |
|  |  | Average Glide Slope Exceedance | Average of vertical deviation exceeding (0.5 dot around the glide slope reference. |

Sidestep Landing

From Breakout-of-Clouds to Upward-Gust:

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectral density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position during the first 20 s. |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectral density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position during the first 20 s. |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position during the first 20 s. |

Sidestep Landing

From Upward-Gust to Touchdown:

| PERFORMANCE |
| --- |
| Type | Variable | Measure | Description |
| Directional | Yaw rate | Yaw Activity | Mean absolute yaw rate. |
|  | Heading | STD Heading Deviation | Standard deviation of the deviation from the desired heading. |
|  |  | Maximum Heading Deviation | Maximum deviation from the desired heading. |
|  |  | Average Heading Exceedance | Average of the absolute deviation exceeding (5o around the desired heading. |
|  | Localizer Deviation | STD Localizer Deviation | Standard deviation of horizontal deviation of the airplane from the localizer centerline. |
|  |  | Maximum Localizer Deviation | The maximum deviation of the airplane from the localizer centerline. |
|  |  | Average Localizer Exceedance | Average of horizontal deviation exceeding (0.5 dot around localizer centerline. |
| Lateral | Roll rate | Roll Activity | Mean absolute roll rate. |
|  | Bank Angle | STD Bank Angle | Standard deviation of bank angle. |
|  |  | Maximum Bank Angle | Maximum absolute bank angle. |
|  |  | Average Bank Angle Exceedance | Average of the absolute bank angle outside of (5o band around wing level position. |
| Longitudinal | Airspeed | Average Airspeed Exceedance | Average of absolute deviation outside (5 knots band about the desired airspeed. |
|  |  | Touchdown Descent Rate | The initial vertical speed of the airplane at touchdown. |
|  | Pitch Angle | STD Pitch Angle | Standard deviation of pitch angle during the maneuver. |
|  | Glide Slope Deviation | STD Glide Slope Deviation | Standard deviation of vertical deviation from the glide slope reference path. |
|  |  | Maximum Glide Slope Deviation | Maximum deviation from the glide slope reference path. |
|  |  | Average Glide Slope Exceedance | Average of vertical deviation exceeding (0.5 dot around the glide slope reference. |
|  | Distance | Touchdown Distance | Distance from runway threshold to the touchdown point. |

Sidestep landing

From Upward-Gust to Touchdown:

| WORKLOAD/BEHAVIOR |
| --- |
| Type | Variable | Measure | Description |
| Directional | Pedal position | RMS Pedal Response | Root mean square of pedal response, calculated by taking the square root of the total area under the pedal power spectral density curve. |
|  |  | STD Pedal Position | Standard deviation of pedal position. |
|  |  | Pedal Response Bandwidth | Frequency below which the area under the pedal power spectrum density curve constitutes 0.5 of total area. |
|  |  | Pedal Reversals | The number of times the pedal position exits a 1-inch band centered at its neutral position during the first 40 s. |
| Lateral | Wheel position | RMS Wheel Response | Root mean square of wheel response, calculated by taking the square root of the total area under the wheel power spectral density curve. |
|  |  | STD Wheel Position | Standard deviation of wheel position. |
|  |  | Wheel Response Bandwidth | Frequency below which the area under the wheel power spectral density curve constitutes 0.5 of total area. |
|  |  | Wheel Reversals | The number of times the wheel position exits a 10o band centered at its neutral position during the first 40 s. |
| Longitudinal | Column position | RMS Column Response | Root mean square of column position, calculated by taking the square root of the total area under the column power spectral density curve. |
|  |  | STD Column Position | Standard deviation of column position. |
|  |  | Column Response Bandwidth | Frequency below which the area under the column power spectral curve constitutes 0.5 of total area. |
|  |  | Column Reversals | The number of times the column position exits a 4-inch band centered at its neutral position during the first 40 s. |

GRADING CRITERIA AND WEIGHTS

I.  The Grade Scale

- Grade scale consists of five different levels

- 5 = Excellent     4 = Good     3 = Average     2 = Poor      1 = Unacceptable

- Each grading criteria for each plot will receive one of these grades

- These grades will be weighted based on the criteria to provide a weighted score for that particular plot

- Likewise, each plot will contribute this weighted score with its own weight to calculate the overall score for each of the four maneuvers

II.  Things to know for grading

- Bad results such as Crash, Rejected Takeoff and missed approaches will all automatically receive the lowest possible score, which is 1

- Only deviations of two or more red data-point dots will be considered as out-of-bound deviations. A deviation of only one dot can be considered to have never deviated outside of the bounds. If there are only two red data points, the second read data point must not be on the boundary line to be considered an out of bound deviation.

- Likewise, a plot that only re-enters the in-bounds region for one data point, will only be counted as having one out of bound (OB) deviation and not 2

- On the approach glide-path deviation plot, the final three data point dots to the left of the 0 nm point will be ignored, regardless of its color.

III.  Takeoff Heading Deviation Plot for both V1 and V2 Cut

- Plot weighting for score of maneuver  = .50

- The ability to stay in bounds   (Weight = .25)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 4

- 2 OB deviations result in a score of 3

- 3 OB deviations result in a score of 2

- 4 or more OB deviations result in a score of 1

- Length of out of bounds deviation   (Weight = .25)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 4

- A total deviation length between 0.5 and 1.0 nm results in a score of 3

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .25)

- A maximum deviation less than 5 degrees results in a score of 5

- A maximum deviation between 5 and 7.5 degrees results in a score of 4

- A maximum deviation between 7.5 and 10 degrees results in a score of 3

- A maximum deviation greater than 10 degrees results in a score of 1

- Location of out of bounds deviation   (Weight = .10)

- A plot with no deviations will result in a score of 5

- A plot with deviation only within 0.5 nm will result in a score of 4

- Any deviations that occurs from 0.5 to 1.5 nm after engine failure will result in a score of 3

- Any deviations that occurs beyond 1.5 nm after engine failure will result in a score of 1

- Steadiness (reversals)   (Weight = .15)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 3

- Any plot with two reversals will result in a score of 2

- Any plot with three or more reversals will result in a score of 1

- (See below graph for how to determine the # of reversals)

IV.  Takeoff Airspeed Deviation Plot for both V1 and V2 Cut

- Plot weighting for score of maneuver  = .10

- Attempt at maintaining speed within bounds

- Any plot with 0 deviations will result in a score of 5

- Any plot where it is apparent there was an attempt to try to maintain speed within the boundaries will result in a score of 4

- Any plot where the speed boundaries were clearly ignored will result in a score of 3

V.  Takeoff Altitude Deviation Plot for both V1 and V2 Cut

- This plot will not receive any grading due to the following factors

- Extreme similarity of the plots

- Lack of appropriate criteria to determine performance

- No instruction given to pilots in regard to this plot

VI.  Takeoff Bank Angle Plot for both V1 and V2 Cut

- Plot weighting for score of maneuver  = .40

- The ability to stay in bounds   (Weight = .20)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 4

- 2 OB deviations result in a score of 3

- 3 OB deviations result in a score of 2

- 4 or more OB deviations result in a score of 1

- Length of out of bounds deviation   (Weight = .15)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 4

- A total deviation length between 0.5 and 1.0 nm results in a score of 3

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .20)

- A maximum deviation less than 5 degrees results in a score of 5

- A maximum deviation between 5 and 7.5 degrees results in a score of 4

- A maximum deviation between 7.5 and 10 degrees results in a score of 3

- A maximum deviation of only one red data dot will result in a score of 2

- A maximum deviation greater than 10 degrees results in a score of 1

- Location of out of bounds deviation   (Weight = .15)

- A plot with no deviations will result in a score of 5

- The first deviation as result of the engine failure will be ignored, unless that deviation >10 degrees (even for just one dot), in that case 1 point will be subtracted from the location score (1 is still the lowest possible score)

- Any deviations that occurs from 0.5 to 1 nm after engine failure will result in a score of 1

- Any deviations that occurs beyond 1 nm after engine failure will result in a score of 3

- Examples:

- A plot with only one dot deviation >10 degrees that is the first deviation from the engine failure will receive a score of 4 because of the subtraction…. Had this first deviation not >10 degrees, the score would be 5

- A plot with a first deviation >10 degrees and a second deviation 1 nm after engine failure will receive a score of 2.  (3 - 1 = 2)

- Steadiness (reversals) – determined as in heading   (Weight = .20)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 3

- Any plot with two reversals will result in a score of 2

- Any plot with three or more reversals will result in a score of 1

- Bank Direction   (Weight = .10)

- A plot that if 0.5 nm after the engine failure it is apparent the tendency of the pilot was to try to maintain a bank towards the good engine will result in a score of 5

- A plot that if 0.5 nm after the engine failure it is unclear what the tendency of the pilot was (switched often between bank to the good engine and bank to bad engine) will result in a score of 3

- A plot that if 0.5 nm after the engine failure it is apparent the pilot was not trying to maintain a bank towards the good engine, but instead favored the bad engine will result in a score of 1

VII.  Approach Glide-Path Deviation Plot for both PIA and SSL

- Plot weighting for score of maneuver  = .40 for PIA and .50 for SSL

- (Note that the last three data points before 0 nm are ignored)

- 1)  The ability to stay in bounds   (Weight = .25)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 4

- 2 OB deviations result in a score of 3

- 3 OB deviations result in a score of 2

- 4 or more OB deviations result in a score of 1

- Length of out of bounds deviation   (Weight = .25)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 4

- A total deviation length between 0.5 and 1.0 nm results in a score of 3

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .25)

- A maximum deviation staying within one dot results in a score of 5

- A maximum deviation between plus/minus 1.5 dot results in a score of 4

- A maximum deviation between plus/minus two dot  results in a score of 3

- A maximum deviation greater than 2 DOT results in a score of 1

- Location of out of bounds deviation   (Weight = .15)

- A plot with no deviations will result in a score of 5

- A plot with only deviations less than +/- 2 dot between 2 – 0 nm will receive a score of 4

- Any deviations that occur from 4 to 2 nm will result in a score of 3

- Any deviations that occur beyond 2 nm that is greater than +/- 2 dot  will result in a score of 1

- Steadiness (reversals) – determined same as previous   (Weight = .10)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 3

- Any plot with two or more reversals will result in a score of 1

VIII.  Approach Localizer Deviation Plot for PIA

- Plot weighting for score of maneuver  = .40

- 1)  The ability to stay in bounds   (Weight = .25)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 3

- 2 OB deviations result in a score of 2

- 3  or more OB deviations result in a score of 1

- Length of out of bounds deviation   (Weight = .25)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 3

- A total deviation length between 0.5 and 1.0 nm results in a score of 2

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .25)

- A plot with no deviations will result in a score of 5

- A maximum deviation that does not have two or more data points in a straight line at the limit of the plot (top and bottom will result in a score of 3

- A maximum deviation that has two or more data points in a straight line at the limit of the plot (top and bottom) will result in a score of 1

- Location of out of bounds deviation   (Weight = .15)

- A plot with no deviations will result in a score of 5

- Any deviations that occur from 4 to 2 nm will result in a score of 3

- Any deviations that occurs beyond 2 nm will result in a score of 1

- Steadiness (reversals) – determined same as previous    (Weight = .10)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 3

- Any plot with two or more reversals will result in a score of 1

IX.  Approach Localizer Deviation Plot for SSL

- Plot weighting for score of maneuver  = .30

- 1)  The ability to stay in bounds   (Weight = .25)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 3

- 2 OB deviations result in a score of 2

- 3  or more OB deviations result in a score of 1

2)  Length of out of bounds deviation   (Weight = .25)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 3

- A total deviation length between 0.5 and 1.0 nm results in a score of 2

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .25)

- A plot with no deviations will result in a score of 5

- A maximum deviation that does not have two or more data points in a straight line at the limit of the plot (top and bottom will result in a score of 3

- A maximum deviation that has two or more data points in a straight line at the limit of the plot (top and bottom) will result in a score of 1

- Location of entry into one dot after Sidestep   (Weight = .15)

- A plot that enters the one-dot region before 1.5 nm to go before the runway will result in a score of 5

- A plot that enters the one-dot region before 1.5 nm but then deviates OB before 1 nm will result in a score of 3

- A plot that enters the one-dot region before 1.5 nm but then deviates OB after 1 nm will result in a score of 1.

- A plot that enters the one-dot region between 1.5 and 1.0 nm before the runway will result in a score of 3

- A plot that enters the one-dot region after 1.0 nm before the runway will result in a score of 1

- Steadiness (reversals) – determined same as previous   (Weight = .10)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 3

- Any plot with two or more reversals will result in a score of 1

X.  Approach Airspeed Deviation Plot for both PIA and SSL

- Plot weighting for score of maneuver  = .20

- The ability to stay in bounds   (Weight = .25)

- 0 OB deviations results in a score of 5

- 1 OB deviation results in a score of 4

- 2 OB deviations result in a score of 3

- 3 OB deviations result in a score of 2

- 4 or more OB deviations result in a score of 1

- Length of out of bounds deviation   (Weight = .25)

- A total deviation length of 0 nm results in a score of 5

- A total deviation length between 0 – 0.5 nm results in a score of 4

- A total deviation length between 0.5 and 1.0 nm results in a score of 3

- A total deviation length greater than 1.0 nm results in a score of 1

- Magnitude of out of bounds deviation   (Weight = .20)

- A maximum deviation staying within 10 results in a score of 5

- A maximum deviation staying between 10 –15 results in a score of 4

- A maximum deviation between 15 – 20 results in a score of 3

- A maximum deviation greater than 20 results in a score of 1

- Location of out of bounds deviation   (Weight = .20)

- A plot with no deviations will result in a score of 5

- Any deviations that occurs from 4 to 1 nm will result in a score of 3

- Any deviations that occurs beyond 1 nm will result in a score of 1

- Steadiness (reversals) – determined same as previous   (Weight = .10)

- A plot with no reversals will result in a score of 5

- Any plot with one reversal will result in a score of 2

- Any plot with two or more reversals will result in a score of 1

COMMENTS ON MOTION BY NO-MOTION GROUP

| PF | Questionnaire | Question | Subquestion | Comment |
| --- | --- | --- | --- | --- |
| NM-01 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Not as much motion visual cue's [sic] |
| NM-01 | 1 | physical comfort |  | I do not have problems with simulator-induced disorientation but the sim motion was not rough enough. It is hard to say if this perception is from other sims or the airplane. Because the engine out work is in the sim. |
| NM-01 | 2 | acceptability |  | The motion is less then [sic] the [company] sim. The [company] sim motion is greater at times then [sic] than the A/C. Of course both sim [sic] can not reproduce the feel of some maneuvers. But the [company] sim over compasates [sic] for lack of visual cue's [sic] with too much motion. |
| NM-01 | 2 | control strategy and technique | engine cut at V1; engine cut at VR | In A/C it is apperent [sic] which engine had [sic] failed. I would take a 100% rudder input and leave it for the 1st segmet [sic] of the manover [sic]. Here in this sim I had to constantly scan the yaw indicator. |
| NM-01 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | A/C flies like 767 sim, which differs to all other [sic], ie. rudder, yaw indicator is not dampand [sic]. Seems to not want to stay in steady state. The sim makes one work harder. For some reason the feel as to which engine has failed is not as good. The sim also feels as though the motion is off making the ID of engine fail [sic] difficult |
| NM-01 | 2 | mental workload |  | Less visual cue's [sic] and less motion. |
| NM-01 | 2 | other cues | engine cut at V1; engine cut at VR | There seemed to be less motion |
| NM-01 | 2 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | I was not sure the motion was on |
| NM-01 | 2 | physical comfort |  | I can not be certian [sic] the motion was on. |
| NM-01 | 4 | control feel, control sensitivity, and any other cues |  | I think the simulator motion input was increased on the last 2 periods. ELV [elevator] feel was difficult to estimate. The trim made no noise when running. |
| NM-02 | 2 | other cues | engine cut at V1; engine cut at VR | PROBABLY BETTER YAW feel in aircraft when you would lose an engine? |
| NM-02 | 3 | other cues | engine cut at V1; engine cut at VR | Engine cuts - hard to feel the yaw. |
| NM-02 | 4 | control feel, control sensitivity, and any other cues |  | Simulator is a little rough sometimes when you make aggressive inputs-the airplane is not quite as rough Throttles were a little sensitive - - maybe aircraft (simulator was light) Elevator was still a little heavy in light turbulence |
| NM-04 | 1 | acceptability |  | Feel, response + visuals would be 3-4, but the lack of accurate motion falls in the "1" category. |
| NM-04 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Motion response to an [sic] control inputs were non-existant [sic], particularly on large scale events/ inputs. (Eng. failures, landing, rapid control inputs) |
| NM-04 | 1 | physical comfort |  | Not better or worse, but the motion fidelity is not at all like other sims. Motion cues seemed non-existant [sic] throughout this session. Visual picture on landing roll seemed to appear "lower" to ground than normal. |
| NM-04 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Again motion was ineffective as a cue for any maneuvers. |
| NM-04 | 2 | physical comfort |  | Lack of accurate motion ques [sic] had no effect on my comfort. |
| NM-04 | 2 | physical workload; mental workload |  | Increased workload due to degrades , increased monitoring of basic control parameters. Trimming yaw is useless. |
| NM-04 | 3 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Can only compare to other sims. Never did any of these maneuvers in airplane. Exagerated [sic] yaw sensitivity resulted in excessive movement cues (transitory). |
| NM-04 | 3 | physical comfort |  | Excessive yaw sensitivities create excessive motions. It appears motions in all axes reflect what sim is doing however. |
| NM-04 | 4 | control feel, control sensitivity, and any other cues |  | Feel in all axes of control seem slightly lighter than normal. Control sensitivity in pitch + roll seem slightly higher than normal, but this may be explained by lighter gross weights used in the scenario. Control sensitivity in yaw is much higher than normal. Based on control movements (rudder or aileron through adverse yaw), trim effects or asymetric [sic] thrust. It was very difficult to make subtle changes without over controlling, even with practice. Motion cues varied throughout the day, with motion cues being imperceptible in first 2 sessions. Overall fidelity of sim is directly proportional to motion. |
| NM-04 | 4 | physical comfort |  | With the motion dialed up, the excessive yaw sensitivity leads to some pretty big motion transients, which I believe are exagerated [sic]. This could create some discomfort. |
| NM-05 | 2 | acceptability |  | Little ground feel. |
| NM-05 | 2 | control sensitivity | yaw control | No feel. |
| NM-05 | 2 | control sensitivity | yaw control; roll control; pitch control; throttle control | Don't feel motion in sim. |
| NM-05 | 2 | other cues | engine cut at V1; engine cut at VR | No feel. |
| NM-05 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No ground feel. Only indicaton [sic] of landing is spoiler. |
| NM-05 | 3 | other cues | engine cut at V1; engine cut at VR | Unable to simulate exact motion of aircraft. |
| NM-05 | 4 | acceptability |  | Very good simulator. Better with motion on, though |
| NM-06 | 1 | other cues | engine cut at V1 | Airplane will give cues (feel, noise.) Normal. |
| NM-06 | 1 | other cues | engine cut at VR | Airplane will give you cues (feel/noise) More cues in airplane. |
| NM-06 | 2 | other cues | engine cut at V1; engine cut at VR | No external cues - No noise. No feeling. The only thing that’s telling me what the aircraft is doing is the flight instruments. |
| NM-06 | 2 | other cues | engine-out straight-in approach/landing | No feel at touchdown. |
| NM-06 | 3 | other cues | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I would have cues in the airplane [like] seat of the pants. |
| NM-06 | 3 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | [Slightly worse] because of lack of cues. |
| NM-07 | 1 | acceptability |  | Very little or no motion felt. |
| NM-07 | 1 | control strategy and technique | engine cut at VR | Because no motion was felt throughout flight |
| NM-07 | 1 | handling qualities | bank angle control; yaw control; altitude control; overall handling qualities | Felt almost no motion |
| NM-07 | 1 | mental workload |  | Had to rely much more on instruments because of lack of motion in sim. |
| NM-07 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Very little motion felt if any. |
| NM-07 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Very little motion or no motion felt in sim. |
| NM-07 | 2 | acceptability |  | Would have been just like the sim. in [company simulator facility] except for motion and perhaps a more sensitive rudder. |
| NM-07 | 2 | control strategy and technique | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Felt |
| NM-07 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Needs more motion to accurately simulate A/C. |
| NM-07 | 2 | mental workload |  | Have to rely more on instruments because of lack of motion/ A/C feel. |
| NM-07 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Felt |
| NM-07 | 3 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Motion appeared to be on and functioning properly this session |
| NM-07 | 4 | gaining proficiency |  | Able to gain proficiency faster flying with the motion on. Less mental workload. Reduced reliance on instruments. |
| NM-08 | 2 | other cues | engine cut at V1; engine cut at VR | Did not feel yaw |
| NM-08 | 4 | control feel, control sensitivity, and any other cues |  | Overall feel of sim is very similar to the airplane. I found it somewhat more sensitive in pitch than the airplane. Visual system is very good |
| NM-10 | 1 | control feel | overall control feel | Overall control feel - seemed sensitive. Pitch and yaw primarily seemed lighter. It also seemed light. The motion was off. Not much seat of the pants especially on landing. |
| NM-10 | 3 | control feel | rudder input; elevator input; throttles; overall control feel | Rudder input - in terms of feel, in this period I had more recognition of rudder "feel". It was slightly heavier than what I would expect in the a/c. Elevator input - was slightly heavier as I noticed on rotation and level off. Throttles - seemed more sensitive than the actual a/c. The power reference points seemed further back and they were sensitive in terms of corrective responses. |
| NM-10 | 4 | control feel, control sensitivity, and any other cues |  | The last period seemed a bit more pitch sensitive. In the afternoon I could hear and feel the landings whereas in the morning period I did not. I did not feel as funky in the very last event set. The noise was more noticeable/audible in the afternoon set. |
| NM-10 | 4 | handling qualities and control strategies |  | The tactile feel seemed different from the morning to the afternoon sets. The afternoon sets had more tactile feel. |
| NM-11 | 1 | other cues | engine cut at VR | No "G" changes, of course. I think yaw sensation in aircraft would be much stronger |
| NM-11 | 3 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | The reaction to the shear was significant. The sim seemed to lurch/pitch |
| NM-13 | 3 | handling qualities | bank angle control; yaw control; airspeed control; overall handling qualities | Don’t feel as if--->After 3-4 hours in the sim, I have a "feel" for the sim. "Feels" like a/c very responsive to every input, but not overly sensitive. |
| NM-13 | 4 | physical comfort |  | Sim felt like it "free flowed" a lot more. Could make for some uneasy stomachs. |
| NM-14 | 1 | acceptability |  | My last simulator ride was more closely approximating the feel of the airplane. It felt heavier and more stable. |
| NM-14 | 1 | handling qualities | yaw control; overall handling qualities | Again the yaw was much different. Also part of the problem might be that without the motion, you lose a large source of sensory information. |
| NM-14 | 1 | other cues | engine cut at V1 | No feeling due to no motion in sim. The engine cut was silent and harder to detect. |
| NM-14 | 1 | other cues | engine cut at VR | Easier [than V1] to detect because the pilot has transitioned his scan to inside the a/c. [Pilot said VR was still different than the airplane because of lack of motion and sound.] |
| NM-14 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Harder to detect the engine failures which slowed down the response times. No motion and sound contributed to the quality of performance. Also on the sidestep procedure we had a slight wind sheer [sic] situation which resulted in us remaining high. This was not expected by the weather reports. |
| NM-14 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all situations there were less clues or cues to help identify the malfunction. -(Yaw- lack of feeling, when in the side-step procedure the windsheer [sic] is very smooth and you dont [sic] notice the airspeed green arrow increasing right away. What you first notice is the glide slope falling away. "lack of descent". |
| NM-14 | 3 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | With the addition of simulator motion there were more cues to help identify the malfunctions. It was helpful in all of the sequences. However the sim was still a little more tame than the airplane. |
| NM-14 | 4 | control feel, control sensitivity, and any other cues |  | This felt the most like the airplane. The cues provided helped identify the malfunctions. The controls felt heavy as they do in the airplane. Trimming is done more to releive [sic] control pressure than to maintain desired attitude. Without proper trimming the sim and plane feel very heavy making it uncomfortable. |
| NM-16 | 1 | control sensitivity | yaw control; pitch control; overall control sensitivity | Again, because yaw inputs on the line tend to be minor, it is difficult to judge the sensitivity. Based only on instrument feedback, the yaw response seemed quite sensitive for the amount of rudder deflection. The aircraft gives much more physical feedback of yaw motion. |
| NM-16 | 1 | handling qualities | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | Lack of motion feeback [sic] makes performing tasks require greater concentration than the airplane. The simulator tends to seem less stable than the airplane. That may be as much a function of pilot over control due to lack of sensory input (ie. motion/sound) |
| NM-16 | 1 | mental workload |  | When the flight path deviates from my target (speed, attitude etc.), I had to rely purely on my scan to detect it. There is little other input that you normally get in the a/c. I.E. changes in sound, sense of motion, etc. |
| NM-16 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Sensation |
| NM-16 | 1 | pilot performance | engine-out straight-in approach/landing; engine-out sidestep landing | During straight approach, I felt I was chasing needles. Lack of motion sensation put me behind and I had to try to consciously speed up my scan. |
| NM-16 | 2 | acceptability |  | Only in the lack of motion. |
| NM-16 | 2 | control strategy and technique | engine-out straight-in approach/landing; engine-out sidestep landing | On both I used less trim (elevator and rudder) because trim changes were hard to feel and created momentary instability. It was easier to trim approximately, then hand fly corrections. The a/c is much easier to trim. |
| NM-16 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Almost identical feel, however lack of motion makes gaining proficiency more difficult |
| NM-16 | 2 | handling qualities | pitch control; yaw control | The lack of motion is a distraction. It takes away from the sensation of flight. The simulator definitely lacks the stability of the a/c. The slightest force on the controls causes often unwanted attitude changes however slight. |
| NM-16 | 2 | mental workload |  | You have to constantly focus on your instruments to maintain desired attitude. The simulator feels less stable and ther [sic] is less other feedback to detect changes in attitude/ airspeed. |
| NM-16 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all cases, small changes in attitude are difficult to detect by feel in the simulator like they can be in the aircraft. Sound in the a/c is also a help. You can hear very subtle changes in air noise in the a/c. You can also feel changes in speed in the aircraft. |
| NM-16 | 3 | mental workload |  | Higher concentration required due to less cues as to changing airspeed or attitude. Also sim seems less stable. |
| NM-16 | 4 | acceptability |  | Other than the slightly unusual feel of the motion, the NASA sim was on par with other sims I've flown. All are acceptable for preparing fo [sic] initial operating flights in the a/c. |
| NM-16 | 4 | gaining proficiency |  | The last session was a bit unproductive as the motion felt unusual. The upside was that I gained confidence in my ability to ignore sensations which conflicted with my instrument indications. |
| NM-17 | 1 | control strategy and technique | engine-out straight-in approach/landing | Power changes and subsequent yaw changes do not give the same physical feel in the seat of the pants. |
| NM-17 | 1 | physical comfort |  | Less pitch and roll swing effect seemed to offer less disorientation. |
| NM-17 | 1 | physical workload |  | Especially in yaw imput [sic]. The sim requires more imput [sic] because of lack of subtle seat of the pants cues. If those cues were present much finer and more frequent adjustments can be made. |
| NM-17 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The seat of the pants physical cues and 3-D visual cues on breakout give a better feel for correction of errors. These added two cues help me refine what my instruments are telling me. |
| NM-17 | 3 | control strategy and technique | engine cut at VR | Without seat of pants cues correct the integration of instrument info was more difficult. [experimenter comment: motion was on during this phase] |
| NM-17 | 3 | mental workload |  | Interpretation of instrument info during Vr cut/windshear scenario was hampered by reduced physical cues. |
| NM-17 | 3 | other cues | engine cut at VR | Seat of the pants cues were off. |
| NM-17 | 3 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | Wheel touchdown feel was better so I was better able to judge my flare on the 2nd approach and maintained better directional control throughout landing roll. |
| NM-17 | 3 | pilot performance | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seat of the pants feel still lacking somewhat. Especially on Vr cut and windshear scenario. Felt my body would give me cues to assist me in instrument interpretation. |
| NM-18 | 1 | acceptability |  | Too smooth & I didn’t sense much yaw |
| NM-18 | 1 | other cues | engine cut at V1; engine cut at VR | Lack of good yaw sense made manuever (sic) less accurate. |
| NM-18 | 1 | other cues | engine-out straight-in approach/landing | Not much (air) feel. Bumps etc. |
| NM-18 | 2 | control feel | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input | Seems like motion is off many times. |
| NM-18 | 2 | control sensitivity | yaw control | Again to [sic] soft, hardly feel the rudder input |
| NM-18 | 2 | control sensitivity | roll control | Again to [sic] soft, hardly feel the rudder input Should be more abrupt movement of ailerons with flaps >25 |
| NM-18 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; | Motion in yaw & pitch axis too smooth |
| NM-18 | 2 | handling qualities | yaw control | Too nice. I can't feel the tail move (skid) |
| NM-18 | 2 | other cues | engine cut at V1; engine cut at VR | Cant [sic] feel the bumps on runway. Also yaw was not perceptible. |
| NM-18 | 2 | other cues | engine-out straight-in approach/landing | Cant [sic] feel the bumps in the air. (Turb) |
| NM-18 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The motion was not perceptible during many of these manuevers [sic]. |
| NM-18 | 3 | acceptability |  | Not sure now what is accurate to the acft feel. |
| NM-18 | 3 | control strategy and technique | engine-out straight-in approach/landing | Still didn’t notice WShear. |
| NM-18 | 3 | control strategy and technique | engine-out sidestep Landing | More bumps needed (Turb) |
| NM-18 | 3 | gaining proficiency | engine cut at V1; engine cut at VR | Over controlled the rudder (seat of pants) sensation of yaw is not dependable |
| NM-18 | 3 | other cues | engine-out straight-in approach/landing | More bumps! & turb |
| NM-18 | 3 | physical workload |  | More concentration required. Cant [sic] depend on senses! |
| NM-19 | 1 | other cues | engine cut at V1; engine cut at VR | I expected greater yaw at eng failure |
| NM-19 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Couldn’t seem to pick up cues - Visual seemed ok but feel was less than I expected (mainly yaw) for V1 VR cuts. Sidestep was ok but I didn’t get the usual cues from crosswind I'm used to--seemed that drift perception was subdued somewhat. |
| NM-19 | 3 | acceptability |  | More responsive in some controls and better cues. Seems more stable in roll/pitch |
| NM-19 | 3 | mental workload |  | Both about the same - maybe a little easier mentally/ physically in sim due to improved cues. (I'm beat - hard to tell) |
| NM-19 | 4 | acceptability |  | Certainly as acceptable as any other sim I've used. (With comments previously stated concerning slightly better stability, better cues, and somewhat greater control sensitivity. |
| NM-20 | 1 | handling qualities | yaw control; heading control; overall handling qualities | The sim is a little harder to control heading because of yaw/rudder sensitivity + lack of seat of pants yaw feel |
| NM-20 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of yaw feel |
| NM-20 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | With the nose up + few vis[ual] references the lack of yaw feel + extra sensitivity makes the VR cut harder in the sim. The V1 cut w/ center line info makes the yaw easier to solve on V1 cut + approaches |
| NM-20 | 2 | other cues | engine cut at V1; engine cut at VR | Lack of seat of pants yaw |
| NM-20 | 3 | control strategy and technique | engine cut at V1; engine cut at VR | Somewhat easier in the A/C Seat of pants yaw |
| NM-20 | 3 | gaining proficiency | engine cut at VR | Felt like it was harder to get yaw cues on this VR cut |
| NM-21 | 1 | acceptability |  | Need that motion. Flight director would be nice |
| NM-21 | 1 | control feel | rudder input; aileron input; elevator input; pitch trim input; overall control feel | Feels lighter, possibly due to motion off, or lighter gross weight than I normally use in the sim |
| NM-21 | 1 | handling qualities | pitch control; bank angle control; yaw control; altitude control; heading control; overall handling qualities | Motion off is disorienting and reduces feedback. My head was almost spinning once breaking out on the ILS |
| NM-21 | 1 | physical workload |  | Lack of flight directors, FPV's and motion made it more difficult. Also, slip indicator seemed too sensitive, causing distraction in my cross check |
| NM-21 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of motion and FD's off at no notice was surprising and created some difficulty. Also I use the flight path vector in the airplane for 3o glidepath assistance. |
| NM-21 | 2 | acceptability |  | Need the motion on. |
| NM-21 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Lack of motion reduced my learning curve |
| NM-21 | 2 | mental workload; other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of motion required more focus |
| NM-21 | 3 | control sensitivity | yaw control; pitch control | With motion on, really noticed rudder inputs |
| NM-21 | 3 | handling qualities | pitch control; yaw control; altitude control; overall handling qualities | Yaw seemed too touchy. Pitching down I didn't have the same sensation of less than 1g like in the airplane |
| NM-21 | 4 | gaining proficiency |  | No real difference with motion on. |
| NM-21 | 4 | handling qualities and control strategies |  | Hard to remain spatially oriented in the morning with the motion turned off |
| NM-21 | 4 | physical comfort |  | Same when the motion is on. |

COMMENTS ON MOTION BY MOTION GROUP

| PF | Questionnaire | Question | Subquestion | Comment |
| --- | --- | --- | --- | --- |
| M-01 | 1 | control strategy and technique | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | You can fly the aircraft easier because you can feel the aircraft a lot better than the simulator. |
| M-01 | 2 | mental workload |  | Since there seems to be less cues as to what the simulator is doing, the work load is much greater especially when you get off your a/s [airspeed] G/s & loc course. |
| M-01 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | easier to feel what the aircraft is doing vs simulator |
| M-01 | 3 | control sensitivity | roll control; pitch control | I tend to overcontrol the pitch & roll due to the lack of my awareness in what amt of input is needed & not having the same feel in the simulator as in the aircraft. |
| M-01 | 3 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | There seems to be more clues as to what is occurring in the aircraft vs. the simulator |
| M-01 | 3 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I feel there are more clues in the aircraft into what is occurring. This fact helps reduce the work load as you don’t get so far off your a/s [airspeed], alt, G/s, & LOC. |
| M-02 | 1 | mental workload |  | Sim practice always add slightly higher mental workloads almost just because. Mainly because the pilot knows that all the normal cues in the flying environment will not be there. |
| M-02 | 1 | pilot performance | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Simulators always have a different feel and cues to the aircrew cannot always be provided. The aircraft provides all those needed cues like sounds or actual motion. |
| M-02 | 2 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Sim seat-of-the pants cues were felt as more time in the sim was gained. |
| M-02 | 2 | handling qualities | pitch control; bank angle control; yaw control | Mainly because the sim feel causes or can cause over controling [sic] more than the aircraft. For example, simulator feels like "weak lateral stability" rather than "strong lateral stability". |
| M-02 | 2 | other cues | engine-out straight-in approach/landing | Shifting winds: I would have felt much sooner the dynamics of constant shifting winds. |
| M-02 | 2 | other cues | engine-out sidestep landing | Microburst: I would have felt much faster the effect of microburst in throttle positions and quick attitude changes. |
| M-03 | 1 | acceptability |  | The pitch variation on initiating turns caused some confusion for me. |
| M-03 | 1 | handling qualities | pitch control; overall handling qualities | Pitch seems a little erratic in turns, felt a pitch up and down when initiating a turn. Altitude- felt it a little harder to maintain altitude in the sim. Pitch caused more airspeed change than I expected. Overall - I think the sim is more sensitive than the airplane in pitch. |
| M-03 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | NOTE: The sim always feels different for me than the airplane in roll during a visual maneuver. It seems more sensitive |
| M-03 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Straight in approach was off localizer farther with rudder trim out of position than I could feel in the airplane Eng out side step was again off localizer - didn’t have rudder trim set for the correction needed. |
| M-03 | 2 | other cues | engine-out sidestep landing | I have more visual & feel cues in the airplane |
| M-03 | 3 | mental workload |  | Trying to adjust for different winds that I would be more alert to in the airplane. |
| M-03 | 3 | pilot performance | engine-out straight-in approach/landing; engine-out sidestep landing | Felt more visual clues in the airplane would help on flying the approach. Feel acceleration and turn forces better in the airplane. |
| M-03 | 4 | acceptability |  | Felt it is more sensitive once it goes into roll it almost feels like its hitting wind shear because the pitch changes so much. |
| M-03 | 4 | any other aspect |  | Enjoyed the practice on approaches. Thought the engine out feeling was very close to the airplane reaction would be. Thought tracking localizer more difficult and hard to control. |
| M-04 | 4 | control feel, control sensitivity, and any other cues |  | The final sim period, the feel, sensitivity felt worse than the earlier periods and worse than the airplane - significantly worse, expecially [sic] with regards to the pitch & aileron and throttle. Also, the control loading on the rudders [sic] seem too heavy. |
| M-04 | 4 | physical comfort |  | The last period seemed about the same and perhap [sic] a bit worse than the previous [company] sim - However, the earlier periods in the NASA sim were much more comfortable with regard to nausia [sic], vertigo, motion, etc. |
| M-06 | 3 | physical comfort |  | Seems to be a slightly more stable platform despite control inputs. |
| M-07 | 1 | acceptability |  | Fidelity/motion seemed a little "sloppier" or looser, yet speed/heading slightly easier to hold |
| M-07 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | ?No inflight experience with eng. failure- I imagine it would be slightly different in terms of feel and noise(?) |
| M-07 | 1 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No experience, but feel I may have done slightly better due to "seat of the pants" feel. |
| M-07 | 2 | physical comfort |  | My roll and yaw induced motion seemed to give me more motion sickness than my last simulator. |
| M-07 | 2 | physical workload |  | More crosschecking is required due to the lack of airplane "feel" and noise |
| M-07 | 3 | other cues | engine cut at V1; engine cut at VR | I imagine different yaw & noise cues for both |
| M-07 | 4 | control feel, control sensitivity, and any other cues |  | Perceived stability degradation in second half seemed to heighten workload to just fly the simulator. Not many brain cells left for working the engine problem etc. After t/o and climbout, the sim seemed to "bump" as if in mild turbulence and then seemed to start "wandering" becoming sloppy and harder to control. |
| M-09 | 1 | mental workload |  | Lack of outside references and seat-of-pants inputs require more crosscheck. |
| M-09 | 2 | mental workload |  | Due to lack of outside cues (both physical and visual) crosscheck must be faster in sim than airplane. |
| M-09 | 3 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I have never flown airplane with engine out and never sidestepped. Yaw can not be felt in sim, wind noise is different. There is a lag between control input and sim response. |
| M-09 | 3 | physical workload; mental workload |  | Sim lacks some cues and movement that airplane has. |
| M-10 | 1 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Most all clues good, but can't replace actual [vibrations (illegible, pilot clarified to experimenter)] / sound. |
| M-10 | 2 | acceptability |  | Very minor comment, a "thud" or two emanating from the sim mechanics could be heard on an occasion or two. |
| M-10 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Sims do a pretty good job, but the sounds and vibrations are slightly diferent [sic]. |
| M-10 | 3 | other cues | engine cut at V1; engine cut at VR | Cues are not exactltly [sic] same - - Good cues just different |
| M-10 | 3 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | Seemed like the acft was on the tip of a rod & seemed to "bobble" on occasion. |
| M-10 | 4 | control feel, control sensitivity, and any other cues |  | The aircraft is more stable than the sim, but I think one learns more from an unstable platform. The visual on this sim is one of the best I've seen. - Good feel for flair [sic] alt & rate of decent [sic]. The airplane speed and heading control is better. One can usually look away for a second or two without losing control (no, it really wasn't that bad!) For a light aircraft, the engines didn't seem to respond as in the real acft/ [sic]. |
| M-12 | 4 | any other aspect |  | My one missed approach felt like I was encountering a strong wind shear, which resulted in great increases in both airspeed and altitude |
| M-12 | 4 | control feel, control sensitivity, and any other cues |  | To me a simulator never feels exactly like the airplane. That means that to a great extent flying a simulator well means very quickly [determining] what the differences are. From that point on the problem is how to make the sim do what you want it to do. |
| M-12 | 4 | handling qualities and control strategies |  | Simulator ques [sic] (signals) are different from the airplane and require a different type of responses [sic] than the airplane. There never seems to be enough of the right kind of sensory feed back to make it feel like the airplane. Feed back always seems to be either too great or too small or non-exsistant [sic]. |
| M-15 | 1 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | Ground visuals & lack of feel both laterally & horizontally make visual flying very difficult |
| M-15 | 2 | other cues | engine-out straight-in approach/landing; engine-out sidestep landing | No feel for sink rate or lateral movement |
| M-15 | 3 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Sensitivity and lack of feedback in "seat of the pants" feel makes flying the sim much harder than the real airplane |
| M-15 | 4 | acceptability |  | A little more difficult to fly than the [company] sim do [sic] to increased sensitivity + waketurb + "burble" incorrect feel + design |
| M-15 | 4 | control feel, control sensitivity, and any other cues |  | Simulator vs the airplane - Controls are way too sensitive. The false feeling burbles on the turns were not realistic- windshear example was not realistic with airplane experience- having no fly by the seat of your pants feel adds to difficulty in flying visuals - also yaw control loading seemed way over sensitive when moving rudders [sic] quickly |
| M-16 | 2 | control sensitivity | yaw control; roll control; pitch control | Like most sims-feel doesn’t seem real |
| M-16 | 3 | control strategy and technique | engine-out straight-in approach/landing; engine-out sidestep landing | More sensitive to wind |
| M-17 | 1 | acceptability |  | Very different feel & the 3 axes seemed different from each other. Requires a new learning curve. |
| M-17 | 2 | mental workload |  | Simulators seem to require more mental effort than aircraft - kinesthetic feel differences? |
| M-17 | 3 | control sensitivity; handling qualities | pitch control; yaw control; airspeed control | Sim sentivity [sic] w/o kinesthetics |
| M-17 | 3 | pilot performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Scan needs & sim feel without kinesthics [sic] of a/c. |
| M-18 | 2 | other cues | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | as previously stated on the previous survey [The noise level in sim are [sic] usually more pronounce [sic] and no [sic] that realistic. The 747-400 is a noisy airplane. It seems that the noise and feeling on all sim [sic] (767, A-320 etc) are not different from the 747. I think that should be something to compensate according to specific aircraft.] |
| M-19 | 1 | control feel | rudder input; aileron input; elevator input; yaw trim input; overall control feel | The sim is a little more "mushy" than a/c - ie. The difference in time that you put the input in and you see or feel a response. |
| M-20 | 1 | handling qualities | altitude control | There is less somatic feel (visual & seat of pants) for small deviations in the sim, than there is in the acft. |
| M-20 | 1 | mental workload |  | As I stated earlier, there are less "cues" in the sim. [Therefore,] the crosscheck scan needs to be faster in the sim. There are less cues in the sim that would alert you to a change in the condition (deviation from steady state) of the aircraft. |
| M-20 | 4 | physical comfort |  | Very similar feel except for better visual in the clouds (as previously noted) |

COMMENTS ON SIMULATOR ACCEPTABILITY

| PF | Questionnaire | Comment |
| --- | --- | --- |
| M-02 | 1 | As compared to systems, ie. The autothrottle inoperative |
| M-03 | 1 | The pitch variation on initiating turns caused some confusion for me. |
| M-04 | 1 | More accurate in all areas especially (1) transition from instruments to visual, (2) x-wind landings, (3) landing maneuvers (4) visual presentation durning [sic] ldg maneuver. |
| M-07 | 1 | Fidelity/motion seemed a little "sloppier" or looser, yet speed/heading slightly easier to hold |
| M-08 | 1 | Overall response, control sensitivity is responsive in some areas. But overall great on downwind final mode. |
| M-11 | 1 | I felt rudder control was sensitive. |
| M-13 | 1 | Very similar to the last simulator I have flown. |
| M-16 | 1 | Visual seems improved. |
| M-17 | 1 | Very different feel & the 3 axes seemed different from each other. Requires a new learning curve. |
| M-20 | 1 | I wasn't looking outside too much, but the transition from IFR to VFR seemed less disorienting in this sim. This sim seemed a little "tighter" (less mushy). |
| NM-01 | 1 | This simulator flies more like the A/C [aircraft] in normal operations than the [company] sims. Some items are different cosmetically than the [company] A/C [aircraft]. Font size on PFD and ND are different |
| NM-04 | 1 | Feel, response + visuals would be 3-4, but the lack of accurate motion falls in the "1" category. |
| NM-07 | 1 | Very little or no motion felt. |
| NM-11 | 1 | Only very slight FD differences. |
| NM-14 | 1 | My last simulator ride was more closely approximating the feel of the airplane. It felt heavier and more stable. |
| NM-18 | 1 | Too smooth & I didn’t sense much yaw. |
| NM-19 | 1 | Once I get over overcontrolling I think I would like the slightly more sensitive control feel of this sim. |
| NM-20 | 1 | same as last sheet [The NASA sim is so close to the [company] sims I have a hard time knowing which one is better.] |
| NM-21 | 1 | Need that motion. Flight director would be nice |
| M-03 | 2 | Felt the roll and pitch to be more sensitive than the last simulator. |
| M-04 | 2 | In just about every category, the NASA simulator out perform, with regard to accuracy, controllability visual, over the simulators used in [company simulator facility]. |
| M-05 | 2 | Sensitivity in both roll and yaw axis is more sensitive than our [company] sim. |
| M-06 | 2 | Despite typically sensitive ailerons, this sim seems to stabilize a little more smoothly. |
| M-07 | 2 | Motion sickness due to simulator. |
| M-10 | 2 | Very minor comment, a "thud" or two emanating from the sim mechanics could be heard on an occasion or two. |
| M-11 | 2 | Again, I had difficulty wrt rudder. Not sure if it's me or not. |
| M-13 | 2 | Very much a [company] airplane/ simulator. |
| M-15 | 2 | Due to overly sensitive controls. |
| M-19 | 2 | Rudder and heading stability and refresh rate of PFD is slow and ratchets. |
| NM-01 | 2 | The motion is less then [sic] the [company] sim. The [company] sim motion is greater at times then [sic] than the A/C. Of course both sim [sic] can not reproduce the feel of some maneuvers. But the [company] sim over compasates [sic] for lack of visual cue's [sic] with too much motion. |
| NM-04 | 2 | Flying qualities are slightly worse than other sims, but the result would be greater proficiency in the airplane. |
| NM-05 | 2 | Little ground feel. |
| NM-07 | 2 | Would have been just like the sim. in [company simulator facility] except for motion and perhaps a more sensitive rudder. |
| NM-08 | 2 | Pitch sensitivity is higher than in the airplane. |
| NM-13 | 2 | At [airline company] we have 4 400 sims. Each one is config'd a little different with the visual ranging from good to xlnt [excellent]. This one here is equivalent to our best sim at [company airline]. Make training, flying and proficiency better. |
| NM-16 | 2 | Only in the lack of motion. |
| NM-18 | 2 | The ability to evaluate the approach on the (N.D.) is an excellent teaching tool. This should be incorporated in to all sims. |
| NM-19 | 2 | See previous [Had some disorientation before last sidestep maneuver. Never experienced that before in a sim - may have been lack of sleep night before!] |
| NM-20 | 2 | Noticed occasional heading jumps that I don’t rember [sic] from [company] sim. |
| NM-21 | 2 | Need the motion on. |
| M-03 | 3 | Seems to me that the pitch and yaw is more sensitive than other 747-400 simulator. |
| M-04 | 3 | Still better than last sim flown at [airline company] |
| M-07 | 3 | Heavier on controls, sloppy, wandering more. |
| M-10 | 3 | Didn't seem to be as stable as last sim. |
| M-13 | 3 | Visual system more life-like. |
| M-17 | 3 | Seems more squirelly [sic], i.e. mobile. |
| M-19 | 3 | The absence of flight director makes the approach more difficult. |
| M-20 | 3 | See previous page comments.[I normally don’t have much discomfort in the sim. However, I did notice this sim has more visual cues when it comes to flying through clouds (IFR) than the [company] sims. (There is a gray scale in the clouds)] |
| NM-01 | 3 | The yaw indicator. I think the [company] sim's yaw-skid indicators are less sensitive, thus move less. I am not sure how the aircraft truly reacts in a engine out situation. The [company] sim is easier to fly, but does not mean that it truly simulates the aircraft. |
| NM-04 | 3 | The yaw sensitivities made it slightly worse. |
| NM-10 | 3 | Short of feeling funky the simulator was fine. |
| NM-11 | 3 | Almost too sensitive, too reactive - borderline. |
| NM-17 | 3 | Better physical comfort. |
| NM-18 | 3 | Not sure now what is accurate to the acft feel. |
| NM-19 | 3 | More responsive in some controls and better cues. Seems more stable in roll/pitch |

COMMENTS ON PHYSICAL COMFORT

| PF | Questionnaire | Comment |
| --- | --- | --- |
| M-02 | 1 | With the exception of pitch trim of the NASA-400 sim. |
| M-04 | 1 | Visual syst much more accurate & realistic |
| M-06 | 1 | I do not tend to experience sim induced disorientation, but being "busy" while in the sim also seems to reduce those effects. Most occurances [sic] happen, (for me) while taxiing. |
| M-07 | 1 | Possibly from my own pilot-induced oscillations, but felt a bit queasy for a few seconds during rudder/aileron inputs/rolls. |
| M-17 | 1 | Lots of forces acting on body |
| NM-01 | 1 | I do not have problems with simulator-induced disorientation but the sim motion was not rough enough. It is hard to say if this perception is from other sims or the airplane. Because the engine out work is in the sim. |
| NM-04 | 1 | Not better or worse, but the motion fidelity is not at all like other sims. Motion cues seemed non-existant [sic] throughout this session. Visual picture on landing roll seemed to appear "lower" to ground than normal. |
| NM-12 | 1 | Just a little unfamiliar. No nausea. |
| NM-17 | 1 | Less pitch and roll swing effect seemed to offer less disorientation. |
| NM-19 | 1 | Visual seemed better - Pictures seemed to be update[d] more frequently -seemed more real time and not a[s] bright a picture as [company] sim (more realistic). |
| NM-20 | 1 | The NASA sim is so close to the [company] sims I have a hard time knowing which one is better. |
| NM-21 | 1 | My head was almost tumbling on final. |
| M-04 | 2 | Correlation between sim & visual much more accurate during visual segments, especially during transition from IMC to VMC, and during landings. |
| M-06 | 2 | No observed symptoms in this sim. Usually only have experienced any symptom while taxiing a simulator. |
| M-07 | 2 | My roll and yaw induced motion seemed to give me more motion sickness than my last simulator. |
| M-11 | 2 | First time I took note. Visual was great. |
| M-13 | 2 | Better visual - more life like especially in the clouds. |
| NM-01 | 2 | I can not be certian [sic] the motion was on. |
| NM-04 | 2 | Lack of accurate motion ques [sic] had no effect on my comfort. |
| NM-10 | 2 | At [airline company] when on the ground and taxiing around [in the sim], there is a slightly disorienting feeling. It seems the [company] sim may be more sensitive and therefore less real in that operating environment. |
| NM-14 | 2 | Maybe cool the simulator a little more. Its rather stuffy. |
| NM-16 | 2 | I don’t tend to suffer from these symptoms. |
| NM-17 | 2 | During maneuvering the visual orientation is less disorienting much better graphical representation. |
| NM-18 | 2 | The visual during set up was annoying. [pilot drew a circle surrounded by wavy lines] |
| NM-19 | 2 | Had some disorientation before last sidestep maneuver. Never experienced that before in a sim - may have been lack of sleep night before! |
| NM-21 | 2 | Discomfort was not too bad until I went visual on the sidestep, and then I had to focus more on gauges and attitude on the PFD for clues. |
| M-01 | 3 | Pretty much the same except in the simulator I knew if I crashed the consequences of that was not dying. |
| M-04 | 3 | Still better than that last flown at [airline company]. |
| M-06 | 3 | Seems to be a slightly more stable platform despite control inputs. |
| M-08 | 3 | Need better lighting in upper EICAS! Could not interpret engine parameters. |
| M-10 | 3 | NASA simulator seemed to "bobble" and "roll" more and graphics outside cockpit reflected that. |
| M-11 | 3 | The only exception is when making rapid/large pitch correction. I felt a little spacial disorientation wrt visual. |
| M-20 | 3 | I normally don’t have much discomfort in the sim. However, I did notice this sim has more visual cues when it comes to flying through clouds (IFR) than the [company] sims. (There is a gray scale in the clouds) |
| NM-01 | 3 | I never have experienced nausea of simulator-induced disorientation. |
| NM-04 | 3 | Excessive yaw sensitivities create excessive motions. It appears motions in all axes reflect what sim is doing however. |
| NM-10 | 3 | I felt wierd [sic]. Really focused on the instruments to get away from the sensations. My head was swirling the entire time. Real effort was expended to concentrate on the instruments. At times the instrumentation did not seem correct. However, I continued to fly the instruments. |
| NM-11 | 3 | Good headrests. |
| NM-14 | 3 | Need more temperature control. |
| NM-17 | 3 | Less sim-induced disorientation. |
| NM-18 | 3 | Yaw seems exaggerated at times…? |
| NM-20 | 3 | Had one case of disorientation on final that was not present before break. |

COMMENTS ON WORKLOAD

| PF | Questionnaire | Type of Workload | Comment |
| --- | --- | --- | --- |
| M-01 | 1 | mental workload | Because it is easier to fly the aircraft, it is mentally a lot harder to fly the simulator as you get off your airspeed, altitude, glidepath, centerline etc a lot more. |
| M-02 | 1 | mental workload | Sim practice always add slightly higher mental workloads almost just because. Mainly because the pilot knows that all the normal cues in the flying environment will not be there. |
| M-02 | 1 | physical workload | The same, because crews (same company) know their SOP's and can anticipate the sequence |
| M-03 | 1 | mental workload | Used to having VNAV programmed for engine out profile. |
| M-04 | 1 | physical workload; mental workload | Extremely proficient F/O w/ specific manevers [sic] |
| M-06 | 1 | physical workload; mental workload | Simulator flying is perceived to be more demanding and usually "not as real" as the plane. Its easier to get focused on a particular task and let checklists/flying slip by or stagnate. |
| M-07 | 1 | mental workload | In sim, less to worry/plan for the landing, passengers, flight attendants, company etc. |
| M-09 | 1 | mental workload | Lack of outside references and seat-of-pants inputs require more crosscheck. |
| M-09 | 1 | physical workload | Simulator controls are slightly harder and less responsive than airplane. |
| M-10 | 1 | physical workload | Only slightly higher due to the fact that we train to use the autopilot more (as a mater of fact, we never practice useing [sic] throttles on take off (autothrottle) and we turn on the a/p at 500' |
| M-10 | 1 | mental workload | Slightly higher due to not useing [sic] same aircraft config (and we almost always use flight director. - always in simulator) |
| M-11 | 1 | mental workload | I felt that I devoted a lot of brain power to rudder control. Also, being used to using the glass, reverting to raw data increases mental workload a lot. |
| M-12 | 1 | mental workload | Only have to think about the airplane (No WX, PAX, F/A problems) |
| M-13 | 1 | physical workload | Non [airline company] SOP's added a little work. |
| M-14 | 1 | mental workload | Difference in procedures (Those not required). Adjustments to mindset for deletion of operating equip mental lag from just completed trip (16+ hour time change) |
| M-15 | 1 | physical workload; mental workload | Again-rudder control made workload higher. |
| M-16 | 1 | physical workload | Some checklists are eliminated. |
| M-17 | 1 | mental workload | The [feel changes that are not the same in all 3 axes] cause a lot of mental adjustment. |
| M-17 | 1 | physical workload | Feel changes require learning a "new machine" and are not the same in all 3 axes. |
| M-18 | 1 | physical workload | see previous comments [In these sim you tend to overcompensate more than the airplane because sim is more light sensation. Airplane feels heavier. (This answer apply to other questions too).] |
| M-20 | 1 | mental workload | As I stated earlier, there are less "cues" in the sim. [Therefore,] the crosscheck scan needs to be faster in the sim. There are less cues in the sim that would alert you to a change in the condition (deviation from steady state) of the aircraft. |
| NM-01 | 1 | mental workload | Because I did not have to worry about: checklist, passengers, company, OPS, SAM (maintenance), FAR'S and real life consequences for my actions |
| NM-02 | 1 | mental workload | Different attitude in airplane vs. simulator. Wont actually die in the simulator - - just get embarrassed. In the aircraft, I would be fighting for my/our lives |
| NM-03 | 1 | mental workload | Rushed. |
| NM-03 | 1 | physical workload | Due to differences in control feel, sensitivity etc that were noted prior. |
| NM-04 | 1 | physical workload; mental workload | Multiple No-notice degrades on top of briefed degrades and PNF using "different" SOPs were tough. |
| NM-04 | 1 | mental workload | Several times I had to make "assumptions" real-time, based on my understanding of the study goals. |
| NM-07 | 1 | mental workload | Had to rely much more on instruments because of lack of motion in sim. |
| NM-08 | 1 | mental workload | Rarely have flown raw data ILS in airplane. |
| NM-10 | 1 | mental workload | Slightly higher to moderately higher. Did not expect the unexpected so soon. So my "cup" got full very quickly. |
| NM-11 | 1 | mental workload | No real danger of crashing, fortunately tough to simulate. |
| NM-11 | 1 | physical workload | The flight director off significantly increases the workload, especially engine out. |
| NM-12 | 1 | mental workload | Unfamiliar setting, slightly different set up. |
| NM-13 | 1 | mental workload | With all disc[ontinuities] + failures "corrected" immed, no more mental workload other than flying a/c is req'd. |
| NM-14 | 1 | mental workload | Being less stable, I couldn’t relax. I was always adjusting the trim to maintain HDG, alt. Constant control inputs were necessary. |
| NM-14 | 1 | physical workload | Because the sim was so light it didn’t take much effort to make the plane respond. |
| NM-15 | 1 | mental workload | Some displays / FMC functions are dissimilar to company a/c. |
| NM-16 | 1 | mental workload | When the flight path deviates from my target (speed, attitude etc.), I had to rely purely on my scan to detect it. There is little other input that you normally get in the a/c. I.E. changes in sound, sense of motion, etc. |
| NM-17 | 1 | physical workload | [slightly higher] Especially in yaw imput [sic]. The sim requires more input because of lack of subtle seat of the pants cues. If those cues were present much finer and more frequent adjustments can be made. |
| NM-18 | 1 | mental workload | F/D off was more [underlined] of a mental load. However, overall with F/D off in aircraft it was not as great a load due to less distractions… radios, passengers, flt att...etc. |
| NM-19 | 1 | physical workload | Other than pitch the physical (overall) workload seemed better because the sim flew more like a lighter A/C. |
| NM-20 | 1 | mental workload | The mental is less because their [sic] is less outside input as opposed to A/C. No F/A, dispatch etc. |
| NM-20 | 1 | physical workload | Keeping the yaw solved is harder in the sim which keeps the physical work load higher. |
| NM-21 | 1 | physical workload | Lack of flight directors, FPV's and motion made it more difficult. Also, slip indicator seemed too sensitive, causing distraction in my cross check |
| M-01 | 2 | mental workload | Since there seems to be less cues as to what the simulator is doing, the work load is much greater especially when you get off your a/s [airspeed] G/s & loc course. |
| M-02 | 2 | physical workload | Its higher because without watching aerodynamic cues sooner caused the workload to increase. |
| M-04 | 2 | physical workload; mental workload | Again, experienced F/O who is familiar with routine, but in airplane we would probably "unload" by using F/D and autopilot more during approaches and VNAV during T/O. |
| M-06 | 2 | physical workload | Simulator workloads generally seem, at least to me, to be a little higher than in the plane because more things are happening w/ regards to manuver [sic] accomplishment, briefings and procedural items. |
| M-07 | 2 | mental workload | Although more crosschecks, less mental preparation for briefing F/A's, PAX etc. |
| M-07 | 2 | physical workload | More crosschecking is required due to the lack of airplane "feel" and noise |
| M-09 | 2 | mental workload | Due to lack of outside cues (both physical and visual) crosscheck must be faster in sim than airplane. |
| M-09 | 2 | physical workload | Had to speed up crosscheck due to slightly different control responses in sim versus airplane. |
| M-10 | 2 | mental workload | Once again, I feel a little more "at home" in the normal tng environment but, this is not terribly different. |
| M-10 | 2 | physical workload | Slightly higher initially, only because of the non-std configuration, to slightly lower on 2nd & 3rd attempt. |
| M-11 | 2 | mental workload | Again, raw data approach adds to workload. |
| M-11 | 2 | physical workload | Raw data is a lot more work. |
| M-12 | 2 | mental workload | Flying the simulator is easier because there are no (fewer) external problems. |
| M-13 | 2 | mental workload | As above, a lot of mental workload on flying. |
| M-13 | 2 | physical workload | Seems to be not as stable i.e. I'm spending a lot of "mental time" flying. |
| M-14 | 2 | mental workload | Due to jet lag and fatigue. |
| M-14 | 2 | physical workload | Mainly due to compensating for control differences. Not significantly different. |
| M-15 | 2 | physical workload; mental workload | Have to compensate for overly sensitive controls. |
| M-16 | 2 | mental workload | Higher because of type of event. |
| M-17 | 2 | mental workload | Simulators seem to require more mental effort than aircraft - kinesthetic feel differences? |
| M-18 | 2 | physical workload | [all sic] For reasons stated before. Because you have to adjust for the sensitiveness of the sim. So you workload increases. Sometimes because of this, if a person is a little off in the sim and let this affect him because of the sim being not as stable as airplane their scan suffers. Making him overcompensate more. |
| M-19 | 2 | mental workload | Had to keep cross-check going faster and concentrate more because rudder and bank didn’t hold desired outcomes. |
| M-19 | 2 | physical workload | Once I made an input to rudder and/ or heading and it seemed to work, I had to change it. |
| NM-01 | 2 | mental workload | Less visual cue's [sic] and less motion. |
| NM-03 | 2 | physical workload; mental workload | Same as prior mostly due to sensitivity issues with controls. (This is OK). |
| NM-04 | 2 | physical workload; mental workload | Increased workload due to degrades , increased monitoring of basic control parameters. Trimming yaw is useless. |
| NM-07 | 2 | mental workload | Have to rely more on instruments because of lack of motion/ A/C feel. |
| NM-08 | 2 | mental workload | Pitch sensitivity caused glide slope mental workload to be higher. |
| NM-08 | 2 | physical workload | Pitch sensitivity caused higher workload. |
| NM-10 | 2 | mental workload | W/o FD or autothrottles increased scan and a different scan is required. Mentally more challenging in that aspect. |
| NM-11 | 2 | mental workload | Still lower stress than it would ever be in the aircraft. |
| NM-11 | 2 | physical workload | Engine out, no autothrottle, no flight director, sidestep, this is multiple problems hopefully seen only it simulator environment (but great training)! |
| NM-12 | 2 | mental workload | A little stress of adaptation. |
| NM-13 | 2 | mental workload | You know what is going to happen, no checklists or manuals to read. Just fly the plane. |
| NM-14 | 2 | physical workload | It seems that you have to be more vigilant to maintain hdg and glide slope. Once you get off your desired hdg you have to take care not to over correct. Roll rate seems quicker. |
| NM-16 | 2 | mental workload | You have to constantly focus on your instruments to maintain desired attitude. The simulator feels less stable and ther [sic] is less other feedback to detect changes in attitude/ airspeed. |
| NM-18 | 2 | mental workload | F/D of ILS requires much more attention than with the A/P and F/D (ie normal ops). Other distraction were not observed (i.e. radio, traffic etc.). |
| NM-18 | 2 | physical workload | Only because we normally use F/D and A/P more frequently on aircraft. |
| NM-19 | 2 | mental workload | Just a result of better cues (see previous) and less physical demands. |
| NM-19 | 2 | physical workload | Somewhat lighter control forces and slightly increased sensitivity - not a lot but seems noticeable. |
| NM-20 | 2 | mental workload | Less other distractions - F/A's, dispatch, ATC etc. |
| NM-20 | 2 | physical workload | More attention to yaw/HDG |
| NM-21 | 2 | mental workload | Lack of motion required more focus |
| M-01 | 3 | mental workload | Because the aircraft is easier to fly, the mental concentration is much higher in the simulator than the aircraft. |
| M-03 | 3 | mental workload | Trying to adjust for different winds that I would be more alert to in the airplane. |
| M-03 | 3 | physical workload | Lots of adjustment to rudder required more so than in the airplane with engine out. |
| M-04 | 3 | physical workload; mental workload | Again, seemed to require more attention. |
| M-06 | 3 | physical workload; mental workload | Sims seem to increase work load - more stuff happening more quickly |
| M-07 | 3 | mental workload | Now I have to scan more diligently, raising my mental effort to try to compensate. |
| M-07 | 3 | physical workload | Heavy, sloppy controls. |
| M-09 | 3 | physical workload; mental workload | Sim lacks some cues and movement that airplane has. |
| M-10 | 3 | physical workload; mental workload | Sim seemed more unstable [sic], requiring more input & faster cross-scan. |
| M-11 | 3 | mental workload | Again raw data flying and struggling with rudder makes more mental work. |
| M-12 | 3 | mental workload | No external problems added. |
| M-13 | 3 | mental workload | As mentioned before I mentally felt behind things. |
| M-14 | 3 | mental workload | As mentioned on page 7 [Definite impact of fatigue from jetlag (trans pacific crossing day prior) affecting problem recognition/solution time interval] |
| M-15 | 3 | physical workload; mental workload | Same as before. |
| M-16 | 3 | mental workload | Concerned now about LOC alignment. |
| M-17 | 3 | mental workload | More physical work means more mental work. |
| M-17 | 3 | physical workload | Difficulty in keeping up means there are corrections which require more work. |
| M-18 | 3 | physical workload; mental workload | Same reason stated page 7. [After the break and because the lunch my performance I felt I little worse. My concentration and scanning were different. Needed more time to concentrate.] |
| M-20 | 3 | mental workload | Must rely more heavily on crosscheck to detect deviations from steady state. |
| NM-01 | 3 | mental workload | Because of the nature of the sim environment, "Dark" low light no depth perception when looking at item on a CRT (out the window). The sim also flies a little different thus one has to be more attentive to hand flying. |
| NM-03 | 3 | physical workload | Same as prior - Sensitivity and stability cause more physical [workload]. |
| NM-03 | 3 | mental workload | Same for mental effort. (As previously stated this is ok because it makes it easier to fly aircraft) |
| NM-04 | 3 | physical workload | Same as before; briefed and unbriefed system degrades and increased yaw sensitivities increased workload. |
| NM-10 | 3 | mental workload | Since I feel funky it seemed like I was focusing very hard on the instrumentation to get away from that funky feeling. |
| NM-10 | 3 | physical workload | I felt like I was working harder than before. Or than when I work in the A/C. |
| NM-11 | 3 | mental workload | Still a sim. |
| NM-11 | 3 | physical workload | I seemed to overcontrol, a little P.I.O (pilot induced) (pitch and roll). |
| NM-16 | 3 | mental workload | Higher concentration required due to less cues as to changing airspeed or attitude. Also sim seems less stable. |
| NM-17 | 3 | mental workload | Interpretation of instrument info during Vr cut/windshear scenario was hampered by reduced physical cues. |
| NM-18 | 3 | mental workload | Non F/D approaches are always challenging. |
| NM-18 | 3 | physical workload | More concentration required. Cant [sic] depend on senses! |
| NM-19 | 3 | mental workload | Both about the same - maybe a little easier mentally/ physically in sim due to improved cues. (I'm beat - hard to tell) |
| NM-20 | 3 | mental workload | Again fewer outside distractions F/A / ATC / dispatch |
| NM-20 | 3 | physical workload | More crossceck for rudder and heading than in a/c. |

COMMENTS ON CONTROL FEEL

| PF | Questionnaire | Control Input | Comment |
| --- | --- | --- | --- |
| M-02 | 1 | rudder input; aileron input; elevator input; yaw trim input; roll trim input; pitch trim input; overall control feel | Simulator vs aircraft overall was heavier |
| M-03 | 1 | rudder input; aileron input; elevator input; overall control feel | Aileron feels more lighter in turns - elevator feels lighter with speed changes - rudder feels heavier with engine out of control - Overall controls felt a little lighter than airplane |
| M-06 | 1 | aileron input; roll trim input; overall control feel | Did not use Aileron/Roll trim. Overall very close to airplane w/ exception of ailerons- but most 400 simulators seem more sensitive in roll. |
| M-07 | 1 | rudder input | I have never made large rudder inputs in the airplane thus it is difficult to judge the difference (No eng failures in real airplane). |
| M-08 | 1 | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input; overall control feel | Slow to respond. |
| M-09 | 1 | roll trim input | Did not use roll trim. |
| M-09 | 1 | rudder input; aileron input; elevator input; yaw trim input; pitch trim input; overall control feel | Elevator input is stiffer and less responsive and has a time lag between input and pitch movement. |
| M-10 | 1 | elevator input; overall control feel | Elevator on takeoff feels slightly lighter to aircraft, but could be due to trim setting.- - Otherwise it feels close (in reality, it may also be due to max thrust take-off on a light acft) Overall control was very close, but it did seem on some occasions to be slightly lighter. |
| M-11 | 1 | roll trim input | Did not use roll trim. |
| M-12 | 1 | rudder input; aileron input | Rudder felt much too sensitive. |
| M-13 | 1 | rudder input; aileron input; throttles; overall control feel | Seems as though less trim (rudder especially) was required in this simulator to get desired response from my past experiences. |
| M-14 | 1 | rudder input; aileron input; elevator input; throttles; pitch trim input; overall control feel | Control loading feels as though pressure forces slightly less than required in normal aircraft. |
| M-16 | 1 | rudder input; aileron input; elevator input; yaw trim input; roll trim input; pitch trim input; overall control feel | Control inputs are lighter and respond quicker than aircraft. |
| M-17 | 1 | rudder input; elevator input; yaw trim input; pitch trim input | Yaw very light and sensitive. Pitch heavy and ponderous. Roll about normal. |
| M-18 | 1 | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input; overall control feel | In these sim you tend to overcompasate [sic] more than the airplane because sim is more light sensation. Airplane feels heavier. (This answer apply [sic] to other questions too). |
| M-19 | 1 | rudder input; aileron input; elevator input; yaw trim input; overall control feel | The sim is a little more "mushy" than a/c - ie. The difference in time that you put the input in and you see or feel a response. |
| NM-01 | 1 | throttles; yaw trim input; roll trim input | Throttles, yaw trim input, and roll trim input not normal [sic] used or used enough to make judgment |
| NM-02 | 1 | roll trim input | Never used Roll Trim input in airplane or simulation |
| NM-03 | 1 | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input; overall control feel | Overall control loading moderately lighter especially in very beginning of motion. |
| NM-04 | 1 | rudder input; aileron input; elevator input; pitch trim input; overall control feel | Appears to be a "slightly" lighter feel compared to airplane, but this is almost negligible, and not significant in my view. |
| NM-08 | 1 | rudder input; pitch trim input; overall control feel | Rudder feels just a little lighter than airplane. Pitch is more sensitive, slightly heavier. |
| NM-10 | 1 | rudder input; yaw trim input | Rudder input and yaw trim input-based on experience (engine out in simulators) was 3/4 of what I expected. Rudder was at 3 on engine out final, I expected 4 units. It seemed sensitive too. |
| NM-10 | 1 | elevator input | Elevator input - noticed lighter than what I expected. This could be based on low gross weight (550,000). I typically fly heavy gross weights (800,000). |
| NM-10 | 1 | overall control feel | Overall control feel - seemed sensitive. Pitch and yaw primarily seemed lighter. It also seemed light. The motion was off. Not much seat of the pants especially on landing. |
| NM-12 | 1 | rudder input; aileron input; elevator input; throttles; pitch trim input; overall control feel | The control feel seemed more responsive than the aircraft. The aircraft seems to be more pronounced in its control feel, a more positive feedback of control forces. |
| NM-14 | 1 | aileron input; elevator input; throttles; overall control feel | The trim happened faster than I am used to. Overall the sim seemed more responsive than the aircraft. |
| NM-15 | 1 | pitch trim input | Pitch Trim: Control feel a bit "unstable". |
| NM-16 | 1 | rudder input; aileron input; elevator input; pitch trim input; overall control feel | Pitch control seemed heavier while roll and yaw felt heavier. However, yaw inputs tend to be minimal when flying the line. |
| NM-17 | 1 | rudder input; aileron input; yaw trim input; pitch trim input; overall control feel | Controls in the sim seem mushier than the aircraft. Imputs [sic] incur a minute delay which has the tendency to want to make you add further input thus over controlling, even if slightly. The [This] forces more correction control movements than is required in the aircraft. |
| NM-18 | 1 | rudder input; yaw trim input; overall control feel | The rudder and yaw inputs seemed lighter than the acft. |
| NM-19 | 1 | rudder input; aileron input; elevator input; throttles; yaw trim input; pitch trim input; overall control feel | Control feel generally seems pretty accurate. I'm fairly ham fisted initially so I may have different opinion later. |
| NM-21 | 1 | rudder input; aileron input; elevator input; pitch trim input; overall control feel | Feels lighter, possibly due to motion off, or lighter gross weight than I normally use in the sim |
| M-01 | 2 | elevator input | Slightly lighter |
| M-02 | 2 | rudder input | Simulator pressure inputs required a little more effort to find the correct input. |
| M-03 | 2 | elevator input | Pitch Control seems lighter |
| M-04 | 2 | elevator input | Responds to movement and not as receptive to pressure inputs. |
| M-05 | 2 | rudder input; aileron input | More sensitive |
| M-05 | 2 | yaw trim input | A degree different from what I'm used to. |
| M-06 | 2 | aileron input | Lighter |
| M-06 | 2 | elevator input | Just slightly heavier |
| M-08 | 2 | rudder input | Rudder input was not as responsive. |
| M-09 | 2 | roll trim input | Did not use roll trim input |
| M-11 | 2 | rudder input | I seem to have trouble "keeping ball centered." Devoting a lot of time on rudder. Seems sensitive to me. |
| M-12 | 2 | rudder input | Rudder in airplane requires more effort |
| M-16 | 2 | rudder input | More sensitive could be the wind. |
| M-17 | 2 | rudder input; aileron input | Seem slightly lighter than airplane |
| M-19 | 2 | aileron input | To [sic] light |
| M-19 | 2 | elevator input | Doesn’t have hesitation on takeoff around 10.5 deg pitch - may be due to light weight t/o@ 550. Control loading about same otherwise. |
| NM-04 | 2 | rudder input; aileron input; elevator input | all yoke inputs seemed a little lighter. Throttles seemed ok |
| NM-05 | 2 | rudder input | Much to [sic] light |
| NM-05 | 2 | aileron input | Light |
| NM-05 | 2 | elevator input; throttles; yaw trim input; pitch trim input | Same |
| NM-06 | 2 | rudder input; aileron input | Lighter |
| NM-07 | 2 | rudder input | More sensitive than [company] sim and a/c [aircraft]. |
| NM-15 | 2 | rudder input; aileron input; elevator input; throttles; yaw trim input; pitch trim input | (A/C) sim felt a bit "unstable" in all axes. This instability may be attributed (corellated [sic]) to control feel. |
| NM-16 | 2 | rudder input; elevator input | Both seemed to require less force than the a/c to affect a change. |
| NM-18 | 2 | rudder input | Too soft not abrupt enough |
| NM-18 | 2 | aileron input | Too soft should be more abrupt with flaps > 25 |
| NM-18 | 2 | yaw trim input | Seems like more trim should be indicated 2-3 unts [units] |
| NM-18 | 2 | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input | Seems like motion is off many times. |
| NM-20 | 2 | rudder input | Mainly rudder. |
| M-03 | 3 | aileron input; elevator input; overall control feel | Overall still feels sensitive than airplane in roll and pitch. |
| M-07 | 3 | aileron input; elevator input; overall control feel | Did not use Roll trim. |
| M-08 | 3 | rudder input | Full rudder for a S/E failure? |
| M-18 | 3 | rudder input; aileron input; elevator input; throttles; yaw trim input; roll trim input; pitch trim input; overall control feel | Same reason as previously stated. [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light sensation. Airplane feels heavier.] Rudder input felt slightly heavier. |
| NM-02 | 3 | elevator input | Elevator in light turbulence feels too heavy. Feels like I’m fighting trim inputs. |
| NM-10 | 3 | rudder input; elevator input; throttles; overall control feel | Rudder input - in terms of feel, in this period I had more recognition of rudder "feel." It was slightly heavier than what I would expect in the a/c. Elevator input - was slightly heavier as I noticed on rotation and level off. Throttles - seemed more sensitive than the actual a/c. The power reference points seemed further back and they were sensitive in terms of corrective responses. |
| NM-15 | 3 | throttles | Throttles: Require constant manipulation to maintain target airspeed. |

COMMENTS ON CONTROL SENSITIVITY

| PF | Questionnaire | Control | Comment |
| --- | --- | --- | --- |
| M-02 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Aircraft is more precise with smaller inputs that do not lead to over control. The sim was very nose heavy and correct pitch trim was hard to find. On level off and establishing level flight at 250 IAS or 210 IAS setting known trim setting for cruise flight were not the same. When doing so, pitch was or took extra workload to stay at constant altitude. |
| M-03 | 1 | yaw control | Yaw - had to use more effort with rudder than I thought I would in the aircraft with engine out. |
| M-04 | 1 | yaw control; roll control | Sim appears more stable than a/c. Roll control in sim appears less sensitive during x-wind ldgs [cross wind landings]. |
| M-06 | 1 | roll control | Most sims (400) have difficulty matching aileron roll sensitivity. |
| M-07 | 1 | yaw control; roll control | Difficult to judge sensitivity due to lack of experience with large control inputs in airplane experience (no eng failures in airplane). |
| M-08 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Slow to respond |
| M-09 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Elevator is stiffer and time lag between input and pitch movement. |
| M-10 | 1 | pitch control | Once again, aircraft seemed to be somewhat light (but not too bad). |
| M-11 | 1 | yaw control; overall control sensitivity | I spent a lot of focus on rudder. Seems it was pretty sensitive and it lagged. (I was behind wrt. input & response). |
| M-12 | 1 | yaw control; roll control | Rudder input too sensitive at all times. |
| M-13 | 1 | roll control; overall control sensitivity | As in previous explanation, simulator seems "touchy" and inputs seem somewhat overcompensated i.e. Airplane seems more stable |
| M-14 | 1 | yaw control; roll control; pitch control; throttle control; overall control sensitivity | Sensitivity slightly less than operable aircraft. |
| M-15 | 1 | yaw control; pitch control; overall control sensitivity | Rudder seemed to generate a much larger response with very little rudder input. Difficult to control with slight pressure - Pitch was the same just a bit lighter. |
| M-16 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Sensitive enough that you have a tendency to over control. |
| M-18 | 1 | yaw control; roll control; pitch control; throttle control; overall control sensitivity | See previous comment [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light sensation. Airplane feels heavier. (This answer apply [sic] to other questions too).] |
| NM-03 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Overall control sensitivity slightly less sensitive again in initial phase of control movement. |
| NM-04 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Overall simulator appears to have "lighter" control response may be due to lighter gross weight used in this unit. |
| NM-05 | 1 | yaw control | Yaw in aircraft (is more responsive) |
| NM-10 | 1 | yaw control | Yaw control- seemed like slightly more sensitive. The turn/slip indicator moved alot [sic] with small rudder trim inputs. |
| NM-10 | 1 | pitch control | Pitch control- seemed like slightly more sensitive. Coming off the runway on 2nd take-off. With VR cut the aircraft seemed to jump off the ground with my input which seemed to be at about 2-3 [deg]/sec. Again, may be result of low gross weight. |
| NM-10 | 1 | overall control sensitivity | Overall control sensitivity- slightly more sensitive than the A/C for above stated reasons. |
| NM-12 | 1 | yaw control; roll control; pitch control; throttle control; overall control sensitivity | Again, the sim seems to be more sensitive than the aircraft with regards to sensitivity of the controls. |
| NM-13 | 1 | roll control; pitch control; overall control sensitivity | Sim is lighter in most responses. Aircraft feels heavier and has an initial slow response at initial input to ail + elev. |
| NM-14 | 1 | yaw control; roll control; pitch control; overall control sensitivity | The yaw control was significantly different than the aircraft. Just a little pressure resulted in large variations in the inclinometer. The airplane "feels" heavier and more stable. |
| NM-15 | 1 | roll control; pitch control; overall control sensitivity | Roll) requires seemingly less [aileron] input. Pitch) more pitch sensitive (requires trim inputs more often). Overall sensitivity) seems less stable than a/c. |
| NM-16 | 1 | yaw control; pitch control; overall control sensitivity | Again, because yaw inputs on the line tend to be minor, it is difficult to judge the sensitivity. Based only on instrument feedback, the yaw response seemed quite sensitive for the amount of rudder deflection. The aircraft gives much more physical feedback of yaw motion. |
| NM-17 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Throttles are just like the aircraft except the sound of spool up. They tend to spool up more radically, otherwise feel is identical. Feel in roll is mushy as is pitch. Yaw appears to require more imput [sic] than the real aircraft. |
| NM-18 | 1 | yaw control; throttle control; overall control sensitivity | Yaw was controllable once accustomed to required input. A/S [airspeed] seemed very stable. |
| NM-19 | 1 | yaw control; roll control; pitch control; overall control sensitivity | Seems as if control sensitivity is more like that of a heavier a/c. Rotation seems dampened for 500,000 lbs A/C. Yaw sensitivity could just be my initial overcontrolling of rudders [sic]. |
| NM-20 | 1 | yaw control; roll control | Yaw control is more sensitive. The yaw indicator moves quicker with less input from rudder than the airplane. |
| M-02 | 2 | roll control; pitch control | Simulator caused more overcontrol than actual aircraft. |
| M-03 | 2 | pitch control | Pitch seems a little more sensitive. |
| M-04 | 2 | pitch control | again-does not appear to be as sensitive to pressure inputs vrs actual control movement. |
| M-06 | 2 | roll control | Slightly lighter and quicker to roll inputs. |
| M-08 | 2 | yaw control | Slightly more sensitive. |
| M-11 | 2 | yaw control | I am chasing "the ball" a lot. |
| M-11 | 2 | yaw control; roll control; pitch control; throttle control | Note: in close, controls feels fine. Maybe the rudder perception is just me. |
| M-12 | 2 | yaw control | Rudder more sensitive than airplane |
| M-12 | 2 | roll control | Ailerons slightly more sensitive than airplane. |
| M-13 | 2 | yaw control; roll control; pitch control; throttle control | Overall the actual airplane seems to be more stable than this & most simulators |
| M-13 | 2 | roll control | Seems to "react" more than the airplane |
| M-15 | 2 | yaw control; roll control | Much more sensitive |
| M-16 | 2 | yaw control; roll control; pitch control | Like most sims-feel doesn’t seem real |
| M-20 | 2 | yaw control; roll control; pitch control; throttle control | The only major difference I can detect is in that when flaps are dropped from 10 [to] 20 degrees the simulator "balloons" excessively (pilot must pitch down in order to stay on glidepath). The aircraft has a tendency to balloon when flaps go from 25 to 30 but not nearly to the extent this sim does (aircraft is about 50% less than the sim). |
| NM-02 | 2 | throttle control | When on speed I properly configured approaching the glide path - the power reduction to attain : keep the glidepath is more than aircraft or [company Boeing] 747-400 sim. |
| NM-03 | 2 | yaw control; roll control; pitch control | Difference is in initial response or initial portion of control movement. |
| NM-04 | 2 | yaw control | Yaw seemed much more sensitive (trim + rudder inputs) than a/c. Once I severely restricted my yaw inputs my flying improved. This increased yaw sensitivity probably affects my perception of overall "more sensitivity" of the sim. |
| NM-05 | 2 | yaw control | No feel. |
| NM-05 | 2 | yaw control; roll control; pitch control; throttle control | Don't feel motion in sim. |
| NM-06 | 2 | yaw control; roll control; pitch control | Lighter |
| NM-10 | 2 | roll control | A slower roll response rate is what I remember from the a/c. Kind of a heavier feel. |
| NM-15 | 2 | yaw control; roll control; pitch control | Seems more sensitive than actual aircraft. |
| NM-16 | 2 | yaw control; pitch control | Both seemed much more sensitive than the a/c. The a/c tends to feel much more stable and not jump around with control inputs like simulator does. |
| NM-18 | 2 | yaw control | Again to [sic] soft, hardly feel the rudder input |
| NM-18 | 2 | roll control | Again to [sic] soft, hardly feel the rudder input Should be more abrupt movement of ailerons with flaps >25 |
| M-01 | 3 | roll control; pitch control | I tend to overcontrol the pitch & roll due to the lack of my awareness in what amt of input is needed & not having the same feel in the simulator as in the aircraft. |
| M-02 | 3 | throttle control | Throttle control: Deceleration takes longer than airplane, with a decrease in power. |
| M-03 | 3 | yaw control; pitch control | Roll more sensitive in starting turn, seems erratic at the initiation of turns. Pitch seems more sensitive than airplane. |
| M-04 | 3 | roll control; pitch control; overall control sensitivity | Just seems more sensitive?! |
| M-06 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Rudder & aileron seemed more sensitive Pitch trim seemed slower and a little heavier. |
| M-07 | 3 | roll control; pitch control; overall control sensitivity | Seemed very heavy in pitch, wandered more in pitch, my hand felt more tired and cramped, trimmed more. |
| M-09 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Yaw, roll & pitch were all slightly more sensitive with some lag between input and airplane response. |
| M-10 | 3 | roll control; pitch control; overall control sensitivity | Aircraft didn’t seem as responsive, initially, creating overcontrol situations. |
| M-11 | 3 | yaw control; pitch control; overall control sensitivity | Yaw - I am still spending a lot of time watching slip indicator. Response seems to lag slightly for me. I'm a little behind wrt this. Pitch - Slightly heavy for me, but not much. |
| M-12 | 3 | yaw control | Rudder feels slightly oversensitive. |
| M-13 | 3 | yaw control; roll control; overall control sensitivity | As before, the sensitivity of the simulator seemed higher than the plane. |
| M-14 | 3 | yaw control; roll control; pitch control; throttle control; overall control sensitivity | Just minor differences - nothing significant. |
| M-15 | 3 | yaw control; pitch control; overall control sensitivity | Same as before. |
| M-16 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Seems like small inputs move sim a lot. |
| M-17 | 3 | yaw control; pitch control | Sim sentivity [sic] w/o kinesthetics |
| M-18 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Same reason as previously stated. [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light [sic] sensation. Airplane feels heavier.] |
| M-19 | 3 | yaw control; roll control; pitch control; overall control sensitivity | I have to move the controls more in the sim than the a/c to get the same response. A/C is more solid when moving yoke for roll and rudders for yaw - Pitch is about the same. |
| NM-02 | 3 | pitch control | Elevator control seemed less sensitive than the airplane in light turbulence. |
| NM-03 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Same coment [sic] - Limited response during initial portion of control actions. |
| NM-04 | 3 | yaw control; roll control; pitch control | All yaw inputs generate exaggerated responses. |
| NM-05 | 3 | yaw control; roll control; overall control sensitivity | Rudder very much more sensitive, aileron, lesser so. |
| NM-06 | 3 | yaw control; roll control; overall control sensitivity | The rudders are more sensitive than the airplane. |
| NM-08 | 3 | pitch control | Pitch somewhat sensitive. |
| NM-10 | 3 | yaw control | Yaw control was slightly sensitive. |
| NM-10 | 3 | throttle control | Throttle control - seemed more sensitive in fine tuning. |
| NM-11 | 3 | yaw control; roll control; pitch control; throttle control; overall control sensitivity | Just all around more sensitive, felt I was often over controlling. |
| NM-13 | 3 | pitch control; throttle control | Just felt like pitch was more sensitive, throttles more direct response. |
| NM-14 | 3 | yaw control; roll control; pitch control; overall control sensitivity | Still it seems like the sim is more responsive than the airplane. |
| NM-15 | 3 | throttle control | Throttles: Require adjustment to maintain target airspeed. |
| NM-16 | 3 | yaw control; roll control; pitch control; overall control sensitivity | The a/c tends to be a little more stable and requires more control input to affect an attitud [sic] change. |
| NM-17 | 3 | pitch control | Pitch control appeared to hesitate some. Sluggish. Required more control and in some cases resulted in over control. |
| NM-18 | 3 | yaw control; roll control; overall control sensitivity | Completly [sic] different senstivity [sic] than earlier and feels just a bit more sensitve [sic] than acft. |
| NM-19 | 3 | yaw control; pitch control; overall control sensitivity | Controls just seem to be slightly more effective than A/C. |
| NM-20 | 3 | yaw control; roll control | Both roll and yaw seem more sensitive than the aircraft especially yaw. |
| NM-21 | 3 | yaw control; pitch control | With motion on, really noticed rudder inputs |

COMMENTS ON STRATEGY & TECHNIQUE

| PF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- |
| M-01 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | You can fly the aircraft easier because you can feel the aircraft a lot better than the simulator. |
| M-04 | 1 | engine cut at V1; engine cut at VR | Not experienced in a/c. |
| M-04 | 1 | engine-out straight-in approach/landing | Again, difficult to compare. 90% of approaches in airplane performed w/ flt directors on. |
| M-06 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | Sim seems more sensitive ie. looses[sic]/gains energy more quickly than plane. Upset has more effect in sim |
| M-07 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No flight experience with engine failures. |
| M-08 | 1 | engine-out straight-in approach/landing | Engine failure seemed to come from the 1 or 2 eng however it was the 3 or 4 that failed. [pilot may have given too much push] |
| M-08 | 1 | engine cut at V1 | Airplane tends to drift at a faster rate. |
| M-08 | 1 | engine cut at VR | Parameters were very absolute. |
| M-10 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | We tend to use autopilot more during [blown] engine approaches (F/Os usually turn off A/P after established on G/S. |
| M-12 | 1 | engine cut at V1; engine cut at VR | Seemed to be too sensitive in yaw. |
| M-13 | 1 | engine cut at V1; engine cut at VR | Have never performed "Non-LNAV" "Non-VNAV" takeoffs in line flying - so this had me "behind the airplane" from beginning of the takeoff. |
| M-16 | 1 | engine-out straight-in approach/landing | Sensitive to inputs. |
| M-18 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | these is [sic] slightly different because of the surprise of what happen [sic] F/D off suddenly |
| NM-01 | 1 | engine cut at V1; engine cut at VR | Could be the amount of thrust i.e. Full thrust T/O or not knowing that the engine would fail. |
| NM-05 | 1 | engine-out straight-in approach/landing | If you can fly sim a/c -- is easier to control [and] is more stable. [Also] a/c-responds slower than sim due to control lag - and physical domentions [sic]. |
| NM-06 | 1 | engine cut at VR | Airplane would [be] slower. |
| NM-06 | 1 | engine-out sidestep landing | Sim to[o] quick to move. |
| NM-06 | 1 | engine cut at V1 | Airplane would be slower to move |
| NM-06 | 1 | engine-out straight-in approach/landing | Airplane more stable. |
| NM-07 | 1 | engine cut at V1 | Unknown - but same as other simulators. |
| NM-07 | 1 | engine cut at VR | Because no motion was felt throughout flight |
| NM-11 | 1 | engine cut at VR | Only difference, I would level at 1000' AGL for clean up |
| NM-13 | 1 | engine-out sidestep landing | Appeared to require more rud and ail input to comp for eng fail. |
| NM-14 | 1 | engine cut at V1 | Unable to detect the yaw until Hdg started to change. Therefore, a slower response time. |
| NM-14 | 1 | engine-out straight-in approach/landing | The simulator seemed more sensitive regarding hdg, yaw. It required more sensitive control inputs. |
| NM-16 | 1 | engine-out straight-in approach/landing | Found using "approach mode" on ND more comfortable with no FD. |
| NM-17 | 1 | engine-out straight-in approach/landing | Power changes and subsequent yaw changes do not give the same physical feel in the seat of the pants. |
| NM-18 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | I had to adapt to lack of F/D. It is very rare not to use F/D. |
| NM-19 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Never had a V1 cut in a/c. |
| NM-21 | 1 | engine-out sidestep landing | I would load 36R on legs page in scratchpad, rather than FREQ/CRS on NAVRAD page. |
| M-02 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Strategy and technique were the same but effort was required to implement within the sim environment. |
| M-03 | 2 | engine-out sidestep landing | Slight difference in roll felt. The sim is more sensitive |
| M-04 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Same |
| M-05 | 2 | engine cut at V1 | I feel the V1 cut at this weight and power would require more rudder. |
| M-07 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I may unconsciously be adapting to the simulator characteristics, but don’t notice myself doing it. |
| M-08 | 2 | engine-out straight-in approach/landing | Rudder input slightly heavier. Aircraft did not respond as quickly. |
| M-10 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | While never experiencing either [of the landings], A/P use would have been different (but not much). Of course we would norm use F/D. |
| M-11 | 2 | engine cut at V1 | Rudder vs slip indicator confused me after liftoff. Thought I had right amount on liftoff but as it turns out, I had way too much. |
| M-13 | 2 | engine cut at V1; engine cut at VR | This simulator seems to have a very good visual system. Specifically seeing the clouds go by out the side window was somewhat distracting - just like it would be in the real airplane -->Engine out, low altitude |
| M-14 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Again due to slight differences in control loading/sensitivity. |
| M-15 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Adjust techniques for overly sensitive controls. |
| M-16 | 2 | engine-out straight-in approach/landing | Mainly microburst wasn’t realistic. |
| M-18 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | You have to compensate more than the airplane because the sim tends to get you out [of] your parameter more faster [sic]. So you have to compensate for that in your strategy and technique. Note: Put it in another words [sic] if we have passengers on the sim they will get very sick faster. |
| M-19 | 2 | engine cut at V1; engine cut at VR | Amount of rudder - it appears to me that I needed to keep changing the rudder inputs during the maneuver to keep wings level - even though my PWR didn’t change. Affected my heading control. |
| M-19 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Rudder - During approach, I had to keep changing rudder inputs even though PWR didn’t change. |
| NM-01 | 2 | engine cut at V1; engine cut at VR | In A/C it is apperent [sic] which engine had [sic] failed. I would take a 100% rudder input and leave it for the 1st segmet [sic] of the manover [sic]. Here in this sim I had to constantly scan the yaw indicator. |
| NM-03 | 2 | engine cut at V1; engine cut at VR | Aircraft I think would be more stable during maneuvers, especially during later part of maneuver. Initial simulator reaction seems normal. |
| NM-04 | 2 | engine cut at V1; engine cut at VR | On T/O profiles, I used more aileron and less active rudder adjustments to compensate for yaw sensitivities. Even slight changes in thrust or rudder had large effects on yaw and heading. |
| NM-04 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Pretty much the same on the approaches. [On T/O profiles, I used more aileron and less active rudder adjustments to compensate for yaw sensitivities. Even slight changes in thrust or rudder had large effects on yaw and heading.] |
| NM-07 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Felt |
| NM-08 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Pitch sensitivity higher in simulator than airplane |
| NM-14 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The same strategy, except you have to pay more attention to staying in trim and maintaining the desired hdg. It seems that I was using both left and right rudder to stay in trim. Normally with an engine out situation only one of the rudders is used primarily. |
| NM-16 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | On both I used less trim (elevator and rudder) because trim changes were hard to feel and created momentary instability. It was easier to trim approximately, then handfly corrections. The a/c is much easier to trim. |
| NM-16 | 2 | engine cut at VR | In order to maintain heading and bank angle, I used both aileron & rudder upon identification of engine failure. In the a/c, I would control direction initially w/ aileron, then blend in rudder. |
| NM-17 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Other than use of flight director through all phases of flight, especially non normal situations, procedures and techniques are the same as the aircraft for all of these. |
| NM-18 | 2 | engine cut at V1 | ACFT seems to weather-vane dramatically at lift off. |
| NM-18 | 2 | engine-out sidestep landing | Didn’t notice windshear just slight changes in A/S & G/S. |
| NM-19 | 2 | engine-out sidestep landing | seemed to be better able to handle windshear, sim seemed to be more responsive. |
| NM-20 | 2 | engine cut at VR | Not quite as much rapid aileron input to level wings |
| NM-21 | 2 | engine cut at VR | I flew about 2-3 degrees above the pitch bar to slow to V2 (150 kts) while the sim commanded 160 Knots with the pitch bar and 150 with the speed bug |
| M-01 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I knew somewhat as to what I might expect. That should have helped me. |
| M-02 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Only because I was behind on maneuver, so it was not the sim more or less, rather me adapting to catch up. |
| M-03 | 3 | engine-out straight-in approach/landing | Felt yaw and roll more difficult to control in the simulation. |
| M-04 | 3 | engine cut at VR; engine-out straight-in approach/landing | Required more finesse - more delicate handling. |
| M-07 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seemed to need heavier control pressure and more attention/ scan to keep simulator on track. Even the flight director didn’t seem to be as precise, would allow climb of 100', etc. |
| M-09 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Note: I have never flown the airplane with an engine out and have never sidestepped in the airplane. |
| M-10 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Slightly different due to use of equipment. I also tend not to use rudder trim during [blown] engine ops. (But, I have never actually accomplished any of the above situations in the acft). |
| M-11 | 3 | engine cut at V1 | My initial rudder correction on the runway becomes excessive @ liftoff. I usually overcorrect the opposite way and thus wing and rudder rock @ liftoff, then settle down. |
| M-12 | 3 | engine-out sidestep landing | Ailerons in sim felt more effective than in airplane. |
| M-12 | 3 | engine-out straight-in approach/landing | Simulator felt to be overly sensitive in pitch. |
| M-13 | 3 | engine cut at V1; engine cut at VR | After the break, it seems as though I was behind the aircraft versus just before the break. |
| M-14 | 3 | engine-out sidestep landing | Tried later deployment of gear & landing flaps. |
| M-15 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | same as before |
| M-16 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | More sensitive to wind |
| M-18 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Same reason as previously stated. [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light [sic] sensation. Airplane feels heavier.] |
| M-19 | 3 | engine cut at V1; engine cut at VR | Both, rudder inputs were NOT STABLE - Had to keep varying. |
| NM-01 | 3 | engine cut at V1 | Yaw and skid indicator: The skid was too sensitive therefore I had to disregard. |
| NM-01 | 3 | engine cut at VR | Its movement and use only trend movement of the yaw and skid indicator. |
| NM-04 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | As before, more active with aileron than rudder. (Id use more rudder, aileron as required in airplane, other sims). |
| NM-06 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Rudder to [sic] sensitive. |
| NM-11 | 3 | engine cut at V1; engine cut at VR | Both, I was thinking "be very easy with the rudder" |
| NM-14 | 3 | engine cut at V1; engine cut at VR | During V1 and VR cut it seems like the plane became uncoordinated very quickly. On initial application of the rudder it seemed to be too much, so I momentarily released rudder pressure and then had to reapply the same rudder. |
| NM-16 | 3 | engine cut at VR | Initial cross control after engine failure. In a/c - aileron first/ then rudder. |
| NM-17 | 3 | engine cut at VR | Without seat of pants cues correct the integration of instrument info was more difficult. [experimenter comment: motion was on during this phase] |
| NM-18 | 3 | engine cut at V1 | Overcontrolled initially. |
| NM-18 | 3 | engine-out sidestep landing | More bumps needed (Turb) |
| NM-18 | 3 | engine-out straight-in approach/landing | Still didn’t notice WShear. |
| NM-19 | 3 | engine-out sidestep landing | Maneuvering seems easier - more responsive. |
| NM-20 | 3 | engine cut at V1; engine cut at VR | Somewhat easier in the A/C Seat of pants yaw |

COMMENTS ON HANDLING QUALITIES

| PF | Questionnaire | Control | Comment |
| --- | --- | --- | --- |
| M-02 | 1 | pitch control; yaw control; altitude control; overall handling qualities | The overall sensitivity of the sim makes the handling qualities moderately worse |
| M-03 | 1 | pitch control; overall handling qualities | Pitch seems a little erratic in turns, felt a pitch up and down when initiating a turn. Altitude- felt it a little harder to maintain altitude in the sim. Pitch caused more airspeed change than I expected. Overall - I think the sim is more sensitive than the airplane in pitch. |
| M-04 | 1 | pitch control; bank angle control; yaw control; heading control; airspeed control; overall handling qualities | Difficult to assess because most of sim flying was with eng-out configuration. Airspeed in simulator does not appear to react as quickly as in airplane. |
| M-07 | 1 | pitch control; bank angle control; altitude control; heading control; airspeed control; overall handling qualities | Simulator easier to hold a specific airspeed/heading (seemed to drift off less). |
| M-08 | 1 | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | Slightly more sensitive. |
| M-09 | 1 | pitch control; yaw control; altitude control; overall handling qualities | Pitch, yaw, altitude control are all stiffer and less responsive with a slight lag between input and output. |
| M-10 | 1 | altitude control | Altitude control was very similar, but did seem to be a little easier (when my instrument cross check was up to speed.) |
| M-13 | 1 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control; overall handling qualities | In performing tasks, seems similar to airplane |
| M-14 | 1 | pitch control; yaw control; altitude control; overall handling qualities | No significant change, just enough to feel different. |
| M-15 | 1 | yaw control; overall handling qualities | Same rudder input made handling difficult. |
| M-18 | 1 | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | See previous comment [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light sensation. Airplane feels heavier. (This answer apply [sic] to other questions too).] |
| M-19 | 1 | pitch control; yaw control; overall handling qualities | It appeared that the rudder inputs kept changing - it could have been me, but I thought I didn’t change anything but I had to change the rudder input. |
| M-20 | 1 | altitude control | There is less somatic feel (visual & seat of pants) for small deviations in the sim, than there is in the acft. |
| NM-02 | 1 | altitude control | Pitch steering bars occasionally give erroneous commands - ie. Trying to keep level flight: I was allowed to deviate with no correcting commands |
| NM-03 | 1 | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | On subject approaches, raw data localizer control seemed moderately worse (Could be [my] scan). |
| NM-04 | 1 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control; overall handling qualities | "Slightly" worse overall should be emphasized. |
| NM-06 | 1 | pitch control; yaw control; overall handling qualities | This sim is to [sic] quick to move - It will not stay in trim. |
| NM-07 | 1 | bank angle control; yaw control; altitude control; overall handling qualities | Felt almost no motion |
| NM-08 | 1 | pitch control | Too sensitive. Airplane tends to hold an established vertical rate. |
| NM-13 | 1 | bank angle control | Less stable. |
| NM-14 | 1 | yaw control; overall handling qualities | Again the yaw was much different. Also part of the problem might be that without the motion, you lose a large source of sensory information. |
| NM-15 | 1 | pitch control; bank angle control; yaw control; overall handling qualities | Pitch/Bank/Yaw: More sensitive than the a/c (less stable). Overall: a bit unstable. |
| NM-16 | 1 | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | Lack of motion feeback [sic] makes performing tasks require greater concentration than the airplane. The simulator tends to seem less stable than the airplane. That may be as much a function of pilot over control due to lack of sensory input (ie. motion/sound) |
| NM-17 | 1 | pitch control; yaw control; overall handling qualities | Again, the roll and pitch controls are mushier requiring over imput [sic] and subsequent correction to the over imput [sic]. |
| NM-18 | 1 | yaw control | Yaw seemed more controllable than last ACFT once warmed up on this machine. |
| NM-19 | 1 | pitch control; bank angle control; yaw control; altitude control; heading control | Yaw seems closer to sim than A/C. The sim handles well - maybe overall slightly better than A/C. The A/C somewhat sluggish handling qualities may make pilots a little too complacent regarding control usage in crosswinds, etc. |
| NM-20 | 1 | yaw control; heading control; overall handling qualities | The sim is a little harder to control heading because of yaw/rudder sensitivity + lack of seat of pants yaw feel. |
| NM-21 | 1 | pitch control; bank angle control; yaw control; altitude control; heading control; overall handling qualities | Motion off is disorienting and reduces feedback. My head was almost spinning once breaking out on the ILS |
| M-02 | 2 | pitch control; bank angle control; yaw control | Mainly because the sim feel causes or can cause over controling [sic] more than the aircraft. For example, simulator feels like "weak lateral stability" rather than "strong lateral stability". |
| M-03 | 2 | pitch control; bank angle control | Seems to be more sensitive than airplane. |
| M-04 | 2 | altitude control | Slightly worse |
| M-04 | 2 | airspeed control | Slightly worse - not as responsive to throttle inputs. |
| M-12 | 2 | bank angle control | Ailerons slightly more sensitive than airplane. |
| M-12 | 2 | yaw control | Rudder feels too sensitive. |
| M-13 | 2 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control | As previous, airplane seems to be more stable and "tighter" i.e. Seems to handle better |
| M-14 | 2 | pitch control; bank angle control; yaw control; airspeed control | Due to slightly lighter control loading/sensitivity |
| M-15 | 2 | pitch control; bank angle control; yaw control; altitude control; heading control | All are much more sensitive than the airplane. Much to [sic] rapid a response than the real plane. |
| M-16 | 2 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control | Not as stable of platform. Minor changes do a lot. |
| M-18 | 2 | pitch control; altitude control; heading control | The airplane is most stable. Sim tends to go away from alt, hdg more quicker. |
| NM-01 | 2 | bank angle control | Difficult did not want to stay in one place, ie. seemed to precess [pilot said it was inherently unstable unlike the company simulator which is more stable than the aircraft] |
| NM-01 | 2 | yaw control | Yaw indication moved around without input. In comparison the aircraft dampens response to controls and indicator. |
| NM-03 | 2 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control | "I think it should be slightly worse" |
| NM-04 | 2 | yaw control | Yaw control sensitivity made heading/ yaw control very tough at first. |
| NM-04 | 2 | heading control | Overall sim seems to handle like a much lighter airplane. |
| NM-05 | 2 | pitch control | To [sic] light. Normal weights would help. Say-875,000. |
| NM-05 | 2 | yaw control | To [sic] light. |
| NM-06 | 2 | bank angle control; heading control | The sim is overall more sensitive than the airplane |
| NM-15 | 2 | pitch control; bank angle control; yaw control; airspeed control | Axes control seems a bit "unstable". A/c tends to hold airspeed more precise than simulator. |
| NM-16 | 2 | pitch control; yaw control | The lack of motion is a distraction. It takes away from the sensation of flight. The simulator definitely lacks the stability of the a/c. The slightest force on the controls causes often unwanted attitude changes however slight. |
| NM-18 | 2 | yaw control | Too nice. I can't feel the tail move (skid) |
| NM-18 | 2 | airspeed control | Might be too easy. |
| NM-21 | 2 | heading control | Loc roll bar at capture was too sensitive and aggressive at Loc turnon [sic] |
| M-02 | 3 | pitch control; bank angle control; yaw control | Slightly "worse" may be the wrong word - I would say "different" |
| M-03 | 3 | pitch control; yaw control; overall handling qualities | Feel that the pitch and yaw are very sensitive. |
| M-04 | 3 | pitch control; bank angle control; altitude control; overall handling qualities | Again, just seems like I had to stay "on top" of the simulator more than the airplane - less stable. |
| M-06 | 3 | bank angle control | Just sensitive aileron. My slow cross-check. |
| M-07 | 3 | pitch control; bank angle control; altitude control; heading control; airspeed control; overall handling qualities | Simulator felt heavy and sloppy, not responding as well as before lunch, needed more attention, as well as trim to fly on speed/altitude. |
| M-09 | 3 | pitch control; bank angle control; yaw control; altitude control; overall handling qualities | Slight lag between input and airplane response. |
| M-10 | 3 | pitch control; bank angle control; altitude control; heading control; overall handling qualities | Once again, the sim seemed a little "stiffer" than aircraft and seemed to "bobble." |
| M-11 | 3 | yaw control; overall handling qualities | Yaw - I do a lot of yaw watching. Yaw seems to lag wrt my inputs, but it is sensitive. |
| M-12 | 3 | yaw control; airspeed control | Rudder slightly over sensitive. Airspeed easier to control than plane. |
| M-13 | 3 | bank angle control; yaw control; overall handling qualities | In relation to sensitivity, the simulator does seem to be more difficult/ challenging than the actual aircraft. |
| M-14 | 3 | pitch control; bank angle control; yaw control; altitude control; airspeed control; overall handling qualities | Again very minor excursions from baseline - Nothing significant. |
| M-15 | 3 | pitch control; yaw control; heading control; overall handling qualities | Same as before. |
| M-17 | 3 | pitch control; yaw control; airspeed control | Sim sentivity [sic] w/o kinesthetics |
| M-18 | 3 | pitch control; bank angle control; yaw control; altitude control; heading control; airspeed control; overall handling qualities | Same reason as previously stated. [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light [sic] sensation. Airplane feels heavier.] |
| M-19 | 3 | pitch control; bank angle control; yaw control; heading control; airspeed control; overall handling qualities | Simulator is less stable than the airplane in terms of heading, altitude & yaw - Maintaining inputs once they are put in. |
| M-20 | 3 | pitch control; bank angle control; heading control; overall handling qualities | The sim did not feel as crisp as the ACFT. Pitch, bank angle, and heading control (especially) felt mushy and imprecise. |
| NM-03 | 3 | pitch control; bank angle control; yaw control; altitude control; heading control; overall handling qualities | Overall stability ( stay where you put and trim it). Aircraft more stable. |
| NM-04 | 3 | pitch control; bank angle control; yaw control; altitude control; heading control; overall handling qualities | Sim handles like a lighter airplane. |
| NM-05 | 3 | yaw control | Rudder too touchy. |
| NM-06 | 3 | bank angle control; yaw control; overall handling qualities | I am having trouble with the rudder control in the sim. |
| NM-08 | 3 | pitch control | Pitch sensitive in simulator. |
| NM-10 | 3 | airspeed control | Airspeed control - seemed more difficult to fine tune. |
| NM-11 | 3 | pitch control; bank angle control; yaw control; altitude control; heading control; overall handling qualities | The sim did not respond with the same sense of mass/inertia as the 550,000 lb aircraft would. Felt more like the old 727 sims. |
| NM-13 | 3 | bank angle control; yaw control; airspeed control; overall handling qualities | Don’t feel as if--->After 3-4 hours in the sim, I have a "feel" for the sim. "Feels" like a/c very responsive to every input, but not overly sensitive. |
| NM-14 | 3 | pitch control; bank angle control; yaw control; heading control; overall handling qualities | It feels like the airplane handles better ie. more responsive, but this creates added workload to maintain a constant attitude, and altitude. Airspeed control was most similar to the airplane. |
| NM-16 | 3 | pitch control; yaw control; altitude control; overall handling qualities | The sensitivity of the controls and lack of stability make precision more difficult. |
| NM-17 | 3 | altitude control; heading control; overall handling qualities | Altitude and heading control were a bit more difficult to maintain--Probably due to turbulance [sic] rather than sim function. |
| NM-18 | 3 | yaw control; altitude control | Overall felt more sensitive. This may because of becoming accustomed to earlier feel. |
| NM-19 | 3 | yaw control; altitude control; overall handling qualities | See previous [Controls just seem to be slightly more effective than A/C.] |
| NM-21 | 3 | pitch control; yaw control; altitude control; overall handling qualities | Yaw seemed too touchy. Pitching down I didn't have the same sensation of less than 1g like in the airplane |

COMMENTS ON PERFORMANCE

| PF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- |
| M-02 | 1 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Simulators always have a different feel and cues to the aircrew cannot always be provided. The aircraft provides all those needed cues like sounds or actual motion. |
| M-03 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Straight in approach was off localizer farther with rudder trim out of position than I could feel in the airplane Eng out side step was again off localizer - didn’t have rudder trim set for the correction needed. |
| M-04 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | E/O approach - pilot issue vrs sim. |
| M-06 | 1 | engine cut at V1; engine-out straight-in approach/landing; | Raw data, coupled w/ the xtra cross-check usually results in a stagnated x check and more deviations, something not routinely flown or encouraged. So---it was less precise than I would prefer and w/ practice usually fly better. |
| M-07 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No experience, but feel I may have done slightly better due to "seat of the pants" feel. |
| M-08 | 1 | engine cut at VR | Could not see engine parameters on the upper EICAS to determine which engine had failed or what was going on with the primary instruments. |
| M-09 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Had difficulty coordinating aileron and rudder on engine cut at Vr. |
| M-10 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | While I hope my response would be similar (or perhaps better) in the aircraft, I have never actually experienced any of the above in the B747. |
| M-11 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Maybe I was getting used to sim flying. It takes a while to settle down & fly a simulator which is slightly more sensitive to my inputs. |
| M-13 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | As described before, the Non-LNAV/Non-VNAV takeoff was difficult for me i.e. VNAV & autothrottles do much on an engine failure takeoff. Also... didn’t expect the lack of flight directors. |
| M-14 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Engine cuts: have not performed in sim since mid-May, none in actual aircraft. Approaches: Reliance on F.D., removal of FD at critical phase of phase (along with) A.P. required recueing [sic] of mindset. |
| M-15 | 1 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Perceived rudder sensitivity made heading very difficult to hold-From there-speed & altitude deviations quickly followed. |
| M-16 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | Sensitivety [sic] played a roll [sic] but not used to raw data approaches which played a big roll [sic]. |
| M-17 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Power changes were more quick than my experience; therefore airspeed & pitch changes were rather abrupt and quickly materialized. This caused larger rudder & pitch adjustments - the former too light and quick - the latter too slow and heavy. |
| M-18 | 1 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | See previous comment [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light sensation. Airplane feels heavier. (This answer apply [sic] to other questions too).] |
| M-19 | 1 | engine cut at V1; engine cut at VR | The rudder input differences caused (I think) a little more bank control problems than in A/C - Might have been due to the amount of deflection of Ball in respect to the heading indicator. [drawing of triangle with bar below with something sticking out from it towards the triangle versus triangle with bar below closer to center of triangle] |
| NM-03 | 1 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | First engine out man performance is impacted by lack of normal prep and brief prior to initial take off. |
| NM-04 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | All these maneuvers have to be compared to other simulators, because I've never had any of above in the airplane. V1 cut - Wake-up call! Didn’t restabilize on runway before rotation. VR cut - I let out too much rudder after initial response. Both cuts are worst case (max. thrust / light gross weight) On V1 cut climb-out, I fell behind on climb profile clean-up due to "A/T inop". I should have briefed/reviewed this more thoroughly (not a routine task at [airline company]) On engine out straight-in, got behind on no FD, No A/T approach. [Airline company] has 4000 RVR/ 3/4 mi visibility requirement for such approaches. According to my SOP, I should have gone around. This should be briefed more thoroughly with BO32 test crews. |
| NM-06 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I would have crashed the airplane if I fly it like the sim. |
| NM-07 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Very little motion or no motion felt in sim. |
| NM-08 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Have not had actual V1 cut in airplane - [company] simulator only. |
| NM-10 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Honestly did not expect any of the event sets. Did not mental [sic] expect the unexpected so soon. 1. V1 cut- took me a bit to get a handle on the rudder. 2. VR cut- took me a bit to get the pitch under control. 3. Straight-in- took me sometime [sic] to get the raw data scan going. Did not expect FD to be turned off. Additionally, once I got visual, I was working lineup and lost the descent rate. As a result I got high and had to exceed 1000 fpm for landing. -Landed in touchdown zone but long at about 2700 down RWY. 4. |
| NM-10 | 1 | engine-out sidestep landing | Sidestep- I would hope this would be like the a/c. |
| NM-11 | 1 | engine cut at V1 | I think on the V1 cut I allowed more heading deviation from centerline than I would like. |
| NM-12 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | A little caught off guard with respect to the engine failures. Unfamiliarity and foreign setting contributed. |
| NM-13 | 1 | engine cut at VR; engine-out sidestep landing | Did not aggressively put enough rudder to maintain C/L. (VR) A/C req'd more initial control input to begin sidestep and then I failed to bring it back in line before overshooting R/W. |
| NM-14 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Harder to detect engine failures which slowed down the response times. No motion and sound contributed to the quality of performance. Also on the sidestep procedure we had a slight wind sheer [sic] situation which resulted in us remaining high. This was not expected by the weather reports. |
| NM-15 | 1 | engine cut at V1; engine cut at VR | V1/VR cut: Action in sim is much "faster" (ie. quick yaw after failure.) |
| NM-16 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | During straight approach, I felt I was chasing needles. Lack of motion sensation put me behind and I had to try to consciously speed up my scan. |
| NM-17 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The seat of the pants physical cues and 3-D visual cues on breakout give a better feel for correction of errors. These added two cues help me refine what my instruments are telling me. |
| NM-18 | 1 | engine-out straight-in approach/landing | EO ST IN APP [Engine out straight in approach]: MIS-SES DA on F/D out APP led to go around at 600ft. [from PNF: misunderstanding on MDA/DH (minimums) & started go around early] |
| NM-19 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Couldn’t seem to pick up cues - Visual seemed ok but feel was less than I expected (mainly yaw) for V1, VR cuts. Sidestep was ok but I didn’t get the usual cues from crosswind I'm used to--seemed that drift perception was subdued somewhat. |
| NM-20 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | With the nose up + few vis[ual] references the lack of yaw feel + extra sensitivity makes the VR cut harder in the sim. The V1 cut w/ center line info makes the yaw easier to solve on V1 cut + approaches |
| NM-21 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of motion and FD's off at no notice was surprising and created some difficulty. Also I use the flight path vector in the airplane for 3o glidepath assistance. |
| M-01 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I feel there are more clues in the aircraft into what is occurring. This fact helps reduce the work load as you don’t get so far off your a/s [airspeed], alt, G/s, & LOC. |
| M-02 | 3 | engine cut at V1; engine cut at VR | Behind the aircraft at first. |
| M-03 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Felt more visual clues in the airplane would help on flying the approach. Feel acceleration and turn forces better in the airplane. |
| M-04 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Felt the simulator required more constant attention than the airplane. If you looked away for a moment, the simulator rapidly became out of position. |
| M-06 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Slower cross check Could not find correct trim for rudder which caused me to drop items from my cross check then have to correct. |
| M-07 | 3 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Although I felt controls were slightly degraded/sloppy/heavy, I was experienced and could deal with problems better except for Vr cut - surprised me. |
| M-09 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Sims are harder to fly than airplane but I have never flown airplane with engine out. |
| M-10 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | As previously stated, I have never accomplished any of the above, but aircraft seems more stable. |
| M-11 | 3 | engine cut at V1; engine cut at VR | I think my trouble with V1 cut/ VR cut is pilot induced. Getting better w/ time in the sim. |
| M-12 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | I felt my performance was worse overall after the break. |
| M-13 | 3 | engine cut at V1; engine cut at VR | I felt very behind the airplane after lunch - somewhat "out of the loop" |
| M-14 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Definite impact of fatigue from jetlag (trans pacific crossing day prior) affecting problem recognition/solution time interval |
| M-15 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Sensitivity and lack of feedback in "seat of the pants" feel makes flying the sim much harder than the real airplane. |
| M-16 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Don't practice this type of flying. |
| M-17 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Scan needs & sim feel without kinesthics [sic] of a/c. |
| M-18 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | After the break and because [of] the lunch my performance felt I [sic] little worse. My concentration and scanning were different. Needed more time to concentrate. |
| M-19 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | My rudder control is better in airplane. My overall approaches are more stable. |
| NM-01 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I just completed my annual check with no problems. I flew much better then (15-Mar-02). Airspeed control is easier. But most of all, yaw control is easier in the aircraft or the [company] sim than the NASA sim. |
| NM-04 | 3 | engine cut at V1 | (Again, compared to other sims only.) V1 cut - First response was ok. But even slight rudder recorrections created excessive excursions in yaw, roll. |
| NM-04 | 3 | engine cut at VR | (Again, compared to other sims only.) VR cut - Same but I managed it better. [First response was ok. But even slight rudder recorrections created excessive excursions in yaw, roll.]. |
| NM-04 | 3 | engine-out straight-in approach/landing | (Again, compared to other sims only.) Straight-In App - Got away from me in close. Out of parameters from breakout to flare. |
| NM-04 | 3 | engine-out sidestep landing | (Again, compared to other sims only.) Side-Step - Got high on sidestep. |
| NM-06 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | [Slightly worse] because of lack of cues. |
| NM-10 | 3 | engine cut at V1; engine cut at VR | V1 and VR cut - Since I felt funky, I did not have a warm and fuzzy. I seemed to do well, but short of feeling funky, I expect I would have done better. |
| NM-10 | 3 | engine-out sidestep landing | Engine out sidestep landing - I got some deviations during the sidestep maneuver [sic] since my Flight Director was still on and not giving me good information. I had Tom turn it off and things settled down. |
| NM-13 | 3 | engine cut at VR; engine-out sidestep landing | Sim feels "heavier" - Control input is put in and sim is stable with little or no wandering. |
| NM-14 | 3 | engine cut at V1; engine-out straight-in approach/landing | The sim still feels a little too light and responsive. On application of the rudder during the V1 cut it takes a couple of moments to take effect. But overall, the sim is performing more like the plane [than this morning.] |
| NM-16 | 3 | engine cut at V1; engine cut at VR; engine-out sidestep landing | V1 cut easier due to heightened anticipation. V2 cut worse due to using rudder with aileron rather than aileron then rudder. Sidestep harder due to less visual cues and the lower level of stability of the simulator. |
| NM-17 | 3 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seat of the pants feel still lacking somewhat. Especially on VR cut and windshear scenario. Felt my body would give me cues to assist me in instrument interpretation. |
| NM-18 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | See [seem] to have lost accurate feel for acft. It will be interesting to see how my next acft flt goes. I'd be glad to follow up with my impressions once I fly again. |
| NM-19 | 3 | engine-out sidestep landing | Better cues seemingly visual and maybe instruments - i.e. more responsive trend arrow or faster response of A/S and/or Rate of climb. Beats me! |
| NM-20 | 3 | engine cut at V1; engine cut at VR | Was having harder time than training in solving yaw and keeping it solved. |

COMMENTS ON OTHER CUES

| PF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- |
| M-03 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | NOTE: The sim always feels different for me than the airplane in roll during a visual maneuver. It seems more sensitive |
| M-04 | 1 | engine-out straight-in approach/landing | Same comments as prev. [Again, difficult to compare. 90% of approaches in airplane performed w/ flt directors on.] |
| M-04 | 1 | engine cut at V1; engine cut at VR | Same comments as prev. [Not experienced in aircraft.] |
| M-05 | 1 | engine cut at V1 | 2nd V1 Cut ATIS & fog however I counted 3 lights [approximately] 600 ft RVR [runway visual range]. |
| M-07 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | ?No inflight experience with eng. failure- I imagine it would be slightly different in terms of feel and noise(?) |
| M-09 | 1 | engine cut at V1; engine cut at VR | Rudder not as effective. |
| M-09 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | Rudder response time delayed. |
| M-10 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Most all clues good, but can't replace actual [vibrations (illegible, pilot clarified to experimenter)] / sound. |
| M-12 | 1 | engine cut at V1; engine cut at VR | Too sensitive to rudder input |
| M-13 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Only other difference noted was the NAV display seemed "jumpy" |
| M-15 | 1 | engine cut at V1; engine cut at VR | Outside visual references are not good enough to give the same feel as airplane. |
| M-15 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | Ground visuals & lack of feel both laterally & horizontally make visual flying very difficult |
| M-17 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Remember that none of these have I actually experienced in the airplane. |
| M-18 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The noise level in sim are [sic] usually more pronounce [sic] and no [sic] that realistic. The 747-400 is a noisy airplane. It seems that the noise and feeling on all sim [sic] (767, A-320 etc) are not different from the 747. I think that should be something to compensate according to specific aircraft. |
| M-18 | 1 | engine cut at V1 | The noise cue are [sic] very different than airplane. |
| M-19 | 1 | engine cut at V1; engine cut at VR | Rudder indication "ball" [picture of triangle with band below, arrow to band] was very sensitive compared to [company] a/c [aircraft]. |
| NM-01 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Not as much motion visual cue's [sic] |
| NM-02 | 1 | engine cut at V1; engine cut at VR | I’m sure a V1 cut in the real airplane would offer better visual cues, ie) yaw: possibly a better visual reference as to what is going on. |
| NM-04 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Motion response to an [sic] control inputs were non-existant [sic], particularly on large scale events/ inputs. (Eng. failures, landing, rapid control inputs) |
| NM-05 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Same as other sims. Never had a V1 or Vr failure. |
| NM-06 | 1 | engine cut at V1 | Airplane will give cues (feel, noise.) Normal. |
| NM-06 | 1 | engine cut at VR | Airplane will give you cues (feel/noise) More cues in airplane. |
| NM-06 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | More stable in airplane. |
| NM-07 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Very little motion felt if any. |
| NM-10 | 1 | engine-out straight-in approach/landing | Not much depth perception so got high - landed long. Typical even in [company Boeing 747-]400 simulators. |
| NM-11 | 1 | engine cut at VR | No "G" changes, of course. I think yaw sensation in aircraft would be much stronger |
| NM-12 | 1 | engine cut at V1; engine cut at VR | More side vision cues [in airplane]. Other crew members |
| NM-14 | 1 | engine cut at VR | Easier [than V1] to detect because the pilot has transitioned his scan to inside the a/c. [Pilot said VR was still different than the airplane because of lack of motion and sound.] |
| NM-14 | 1 | engine cut at V1 | No feeling due to no motion in sim. The engine cut was silent and harder to detect. |
| NM-16 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Sensation |
| NM-17 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | 3D cues on breakout in low visibility are slightly better in the real aircraft. |
| NM-18 | 1 | engine cut at V1; engine cut at VR | Lack of good yaw sense made both manuevers (sic) less accurate. |
| NM-18 | 1 | engine-out straight-in approach/landing | Not much (air) feel. Bumps etc. |
| NM-19 | 1 | engine cut at V1; engine cut at VR | I expected greater yaw at eng failure |
| NM-19 | 1 | engine-out sidestep landing | Sim seemed to present cues faster (?) than real life situation. |
| NM-20 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of yaw feel |
| M-01 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | easier to feel what the aircraft is doing vs simulator |
| M-02 | 2 | engine-out sidestep landing | Microburst: I would have felt much faster the effect of microburst in throttle positions and quick attitude changes. |
| M-02 | 2 | engine-out straight-in approach/landing | Shifting winds: I would have felt much sooner the dynamics of constant shifting winds. |
| M-03 | 2 | engine-out sidestep landing | I have more visual & feel cues in the airplane |
| M-07 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I imagine it would be close to that experienced in the simulator. |
| M-09 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Note: I have never done any engine out in the airplane. |
| M-10 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Sims do a pretty good job, but the sounds and vibrations are slightly diferent [sic]. |
| M-13 | 2 | engine cut at V1; engine cut at VR | As previous, visual system seemed to add real life distractions |
| M-14 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Slight difference in visual maneuvers primarily relating to visual cues (or lack thereof) normally associated with actual aircraft. |
| M-15 | 2 | engine cut at V1; engine cut at VR | Outside visual doesn't give exact visual cues on takeoff |
| M-15 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | No feel for sink rate or lateral movement |
| M-16 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Sensitivity & wind |
| M-18 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | as previously stated on the previous survey [The noise level in sim are [sic] usually more pronounce [sic] and no [sic] that realistic. The 747-400 is a noisy airplane. It seems that the noise and feeling on all sim [sic] (767, A-320 etc) are not different from the 747. I think that should be something to compensate according to specific aircraft.] |
| M-19 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PFD refresh rate is too slow. |
| M-19 | 2 | engine cut at V1; engine cut at VR | Rudder response. |
| NM-01 | 2 | engine cut at V1; engine cut at VR | There seemed to be less motion |
| NM-01 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | I was not sure the motion was on |
| NM-02 | 2 | engine cut at V1; engine cut at VR | PROBABLY BETTER YAW feel in aircraft when you would lose an engine? |
| NM-04 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Again motion was ineffective as a cue for any maneuver. |
| NM-05 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No ground feel. Only indicaton [sic] of landing is spoiler. |
| NM-05 | 2 | engine cut at V1; engine cut at VR | No feel. |
| NM-06 | 2 | engine cut at V1; engine cut at VR | No external cues - No noise. No feeling. The only thing that’s telling me what the aircraft is doing is the flight instruments. |
| NM-06 | 2 | engine-out straight-in approach/landing | No feel at touchdown. |
| NM-07 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | No Motion Felt |
| NM-08 | 2 | engine cut at V1; engine cut at VR | Did not feel yaw |
| NM-10 | 2 | engine cut at V1 | Engine cut at V1: At [airline company] we train with "noise". Specifically an engine failure noise at the failure time. At [airline company] we use engine seizure so we here [sic] the noise. Additionally the weight is lighter than normal training but I am getting a feel. Also we do not use the screens as debriefing aids but I found them very helpful. |
| NM-10 | 2 | engine cut at VR | Engine cut at V2-"Noise" primary difference. |
| NM-11 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | For both [landings], simulator balloons when flaps selected from 10 to 20. Also pitches up a little. I think the aircraft actually noses over on this configuration change. |
| NM-12 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In general there are additional visual cues in respect to side vision (additional windows). |
| NM-14 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all situations there were less clues or cues to help identify the malfunction. -(Yaw- lack of feeling, when in the side-step procedure the windsheer [sic] is very smooth and you dont [sic] notice the airspeed green arrow increasing right away. What you first notice is the glideslope falling away. "lack of descent." |
| NM-16 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all cases, small changes in attitude are difficult to detect by feel in the simulator like they can be in the aircraft. Sound in the a/c is also a help. You can hear very subtle changes in air noise in the a/c. You can also feel changes in speed in the aircraft. |
| NM-17 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | 3D cues in a real environment add into the mix for better control and corrections. |
| NM-18 | 2 | engine cut at V1; engine cut at VR | Cant [sic] feel the bumps on runway. Also yaw was not perceptible. |
| NM-18 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | The motion was not perceptible during many of these manuevers [sic]. |
| NM-18 | 2 | engine-out sidestep landing | Windshear was not noticeable and certainly did not require evasive action. (More Turb.) |
| NM-18 | 2 | engine-out straight-in approach/landing | Cant [sic] feel the bumps in the air. (Turb) |
| NM-19 | 2 | engine-out sidestep landing | Windshear cues seemed more rapidly displayed on instruments. |
| NM-20 | 2 | engine cut at V1; engine cut at VR | Lack of seat of pants yaw. |
| NM-21 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Lack of motion required more focus |
| M-01 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | There seems to be more clues as to what is occurring in the aircraft vs. the simulator |
| M-03 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Transitioning to visual difficult in the sim with roll and pitch more sensitive. |
| M-06 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Wind noise seems louder than in airplane. |
| M-07 | 3 | engine cut at V1; engine cut at VR | I imagine different yaw & noise cues for both |
| M-09 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I have never flown airplane with engine out and never sidestepped. Yaw can not be felt in sim, wind noise is different. There is a lag between control input and sim response. |
| M-10 | 3 | engine cut at V1; engine cut at VR | Cues are not exactltly [sic] same - - Good cues just different |
| M-10 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Seemed like the acft was on the tip of a rod & seemed to "bobble" on occasion. |
| M-13 | 3 | engine cut at VR | Visual in simulator makes it seem more like the airplane. |
| M-14 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Outside visual cues as mentioned before. [Slight difference in visual maneuvers primarily relating to visual cues (or lack thereof) normally associated with actual aircraft.] |
| M-15 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | same as before |
| M-18 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Same reason as previously stated. [In these sim you tend to overcompasate [sic] more than the airplane because sim is more light [sic] sensation. Airplane feels heavier.] But it seems that the noise of the engines sounded more pronounce [sic]. |
| NM-01 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Except for visual cues. |
| NM-02 | 3 | engine cut at V1; engine cut at VR | Engine cuts - hard to feel the yaw. |
| NM-04 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Can only compare to other sims. Never did any of these maneuvers in airplane. Exagerated [sic] yaw sensitivity resulted in excessive movement cues (transitory). |
| NM-05 | 3 | engine cut at V1; engine cut at VR | Unable to simulate exact motion of aircraft. |
| NM-06 | 3 | engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | I would have cues in the airplane [like] seat of the pants. |
| NM-06 | 3 | engine cut at V1 | I think the sim is acting quicker than the airplane. |
| NM-07 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Motion appeared to be on and functioning properly this session |
| NM-11 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | The reaction to the shear was significant. The sim seemed to lurch/pitch |
| NM-12 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Other aural cues could contribute. We have 1000 ft calls, 500 ft calls, 100/50/20 calls. |
| NM-13 | 3 | engine-out sidestep landing | Windshear on sidestep, if it is a "minimal" shear then sims [sic] is somewhat effective. However I feel the sim overcompensates for a shear that req's very little throttle or control input to correct shear |
| NM-14 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | With the addition of simulator motion there were more cues to help identify the malfunctions. It was helpful in all of the sequences. However the sim was still a little more tame than the airplane. |
| NM-16 | 3 | engine cut at V1 | Yaw easier to detect quickly in a/c. |
| NM-16 | 3 | engine cut at VR | Fewer engine sounds than a/c. |
| NM-17 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Wheel touchdown feel was better so I was better able to judge my flare on the 2nd approach and maintained better directional control throughout landing roll. |
| NM-17 | 3 | engine cut at VR | Seat of the pants cues were off. |
| NM-18 | 3 | engine-out straight-in approach/landing | More bumps! & turb |
| NM-18 | 3 | engine cut at V1 | Inputs seemed exaggerated. |
| NM-18 | 3 | engine-out sidestep landing | Seems pitch sensitive. |
| NM-19 | 3 | engine-out sidestep landing | More stable, more maneuverable, but cues must contribute – don’t know if it is visual or instrument response. |
| NM-20 | 3 | engine cut at V1 | Amount of rudder less. |
| NM-20 | 3 | engine cut at VR | Yaw solution was harder. |

COMMENTS ON GAINING PROFICIENCY

| PF | Comment |
| --- | --- |
| M-01 | About the same. The fact NASA doesn’t follow all of [company] procedures changes the way I do things somewhat in the NASA simulator. |
| M-02 | Gaining proficiency was about the same as the time in the simulator is increased. Both simulators take time to adjust to, so therefore, it reflects how much time a pilot has been in the simulator. |
| M-03 | Felt a little distracted by my inability to compensate for changes in wind etc which made tracking localizer more difficult. |
| M-04 | The conditions in the final sim period, more duplicate the performance of the previous experience with the [company] simulators, whereas earlier periods the NASA sim seemed much superior to the [company] sim experiences. |
| M-05 | I feel they are the same. |
| M-06 | No doubt about it. The less distracting it is to compare "airplane vs. simulator" hadling [sic] and the more closely the sims become to the plane the more practice (proficiency) one can attain out of the time spent in the sim. This simulator generally flies better than my last 400 simulator. |
| M-07 | Before lunch, I felt the simulator was very close to [company] sims. After lunch, it felt like old technology, or purposely degraded stability. |
| M-08 | Note w/o FD\ Auto-pilot is not SOP. Therefore, I had to relearn my scan!! Once that was accomplished no problem. |
| M-09 | The simulator here and at [airline company] seemed identical to me. |
| M-10 | I think it is an excellent simulator to gain proficiency on. |
| M-11 | I feel I was gaining proficiency the same as I do in other sims. |
| M-12 | They are both so close to the same I would judge them equal. |
| M-13 | Training of quick repitition [sic] helped a great deal - lunch break did not. |
| M-14 | Overall, more repetitions equals greater success. However, this was somewhat temporary by general feeling of fatigue (as discussed in previous critiques) which continued to progress as sessions went on |
| M-15 | Pretty close to [company] sim - Perhaps rudder and elevator were a bit more sensitive than normal. |
| M-16 | Seemed to improve with time. |
| M-17 | Proficiency increase seemed fast at first then more rapid later. |
| M-18 | There is not a significant difference between the two to make a comment. |
| M-19 | It took a little longer for me to gain proficiency in the NASA sim than the [company] sim. |
| M-20 | None. |
| NM-01 | This sim view very much like the 767 [company] sim. I used strategies from that sim to gain proficiency here. |
| NM-02 | Same |
| NM-03 | Once you are familiar with simulator, proficiency can be gained normally. |
| NM-04 | Well, I'm working harder to meet the parameters. So I'll do better elsewhere, but I still was rough on the yaw/heading control. It's harder to get proficient in this sim. |
| NM-05 | Repitions, (sic) and time only way I know to become proficient. |
| NM-06 | The proficiency gain in the NASA sim was about the same as in the [company] sim. |
| NM-07 | Able to gain proficiency faster flying with the motion on. Less mental workload. Reduced reliance on instruments. |
| NM-08 | The NASA simulator and the [company] simulator are very, very similar. I used the same techniques in both. |
| NM-10 | The debrief screens used in the morning period were helpful in understanding how to improve performance. |
| NM-11 | I felt I could gain proficiency during each session. It was a matter of "learning" the sim., which is what everyone does during annual/semi-annual training. |
| NM-12 | I was able to gain proficiency in this simulator as well as my previous simulators. |
| NM-13 | With this last set up, no proficiency could be gained. Just a handful to fly it. Could generate no learning experience. Felt like ---->you didn’t know if the sim was re-creating manual flying hazards or whether it was a sim glitch. |
| NM-14 | This simulator felt similar to my previous simulator experiences. Small corrections had the predicted and desired result. The small corrections didn’t have an aggressive unwanted result. |
| NM-15 | Same |
| NM-16 | The last session was a bit unproductive as the motion felt unusual. The upside was that I gained confidence in my ability to ignore sensations which conflicted with my instrument indications. |
| NM-17 | The obvious closeness of control sensitivity and response to the aircraft will definitely aid in gaining faster proficiency in the aircraft. |
| NM-18 | Just like gaining the feel for any new acft. Fortunately, all Boeings fly similarly. I’ve flown B707, 737, 777, 747. I felt I could gain proficiency at a normal rate. |
| NM-19 | As I said previously, things just seemed easier in the NASA sim. But this is a no risk environment and much of the perceived "easiness" might by psychological. |
| NM-20 | Can tell no differences between the two. |
| NM-21 | No real difference with motion on. |

FINAL COMMENTS ACCEPTIBILITY

| PF | Comment |
| --- | --- |
| M-01 | Fine simulator. |
| M-02 | As far as simulators I feel they are well above average to use as a training device. Even though the aircraft and simulator will always be slightly different it serves the purpose. However, if the pitch trim and rudder control and sensitivity could be improved that would be a great help. |
| M-03 | Felt it is more sensitive once it goes into roll it almost feels like its hitting wind shear because the pitch changes so much. |
| M-04 | Again, same thing. Earlier periods with NASA sim seem much better than the final NASA sim. |
| M-05 | Very good. |
| M-06 | Overall acceptability is above average. I would feel comfortable taking my annual evaluation in this simulator any day. |
| M-07 | Due to my perceived degrading of stability, I would find it difficult to do much more than work at flying the simulator. I was becoming more comfortable, but never could relax. |
| M-08 | Great training aid. |
| M-09 | Excellent sim. |
| M-10 | Good sim. |
| M-11 | I think it was fine to teach me procedures and practice emergency procedures. My only gripe is spatial/ visual disorientation if I make too many corrections - inputs at once. |
| M-12 | As good as present state of the art can produce. |
| M-13 | As before, as good as any except - Nav display and engine instruments a little "jumpy". Visual system - very good. |
| M-14 | Very comparable to most sims in [company] inventory. |
| M-15 | A little more difficult to fly than the [company] sim do [sic] to increased sensitivity + waketurb + "burble" incorrect feel + design |
| M-16 | Very good sim & instructors. |
| M-17 | At the end better than the beginning At the end - acceptable. |
| M-18 | It is an excellent simulator. |
| M-19 | FINE - It was ok for a simulator and training tool. I would like better rudder feel for engine out work. |
| M-20 | Great sim. |
| NM-01 | As good as any I have flown. Although I would take a check ride in the [company] sim if I could choose. |
| NM-02 | Great simulator. |
| NM-03 | Overall totally acceptable - Some minor adjustments as discussed might be beneficial. |
| NM-04 | Overall, it is pretty close to the fleet except as noted earlier. |
| NM-05 | Very good simulator. Better with motion on, though |
| NM-06 | It is a good fresh sim. The rudder problem is [sic] had [pilot's writing is illegible] problem. |
| NM-07 | Very similar if not the same as [company] sims. Very acceptable for training. |
| NM-08 | Increase volume on nose gear at landing and rollout. Decrease pitch sensitivity slightly. |
| NM-10 | Simulator overall was completely acceptable. |
| NM-11 | Sim is acceptable. |
| NM-12 | Completely acceptable as an excellent flight training aid. |
| NM-13 | Morning - excellent. - Afternoon - call maintenance. [maintenance was called, extensive testing on the motion found nothing wrong] |
| NM-14 | This was the best sim session of the day. |
| NM-15 | "Excellent" |
| NM-16 | Other than the slightly unusual feel of the motion, the NASA sim was on par with other sims I've flown. All are acceptable for preparing fo [sic] initial operating flights in the a/c. |
| NM-17 | Marked improvement over existing sims. |
| NM-18 | Seemed "OK" but not real similar in the roll and yaw axis (Oversensitive yaw). Yaw was most inaccurate. Sometimes it felt like there was no yaw damper. Roll was not as sensitive as expected with the flaps down > 20. |
| NM-19 | Certainly as acceptable as any other sim I've used. (With comments previously stated concerning slightly better stability, better cues, and somewhat greater control sensitivity. |
| NM-20 | This sim is very acceptable as to training. |

FINAL COMMENTS PHYSICAL COMFORT

| PF | Comment |
| --- | --- |
| M-01 | Pretty much the same. |
| M-02 | Same. |
| M-03 | No difference. |
| M-04 | The last period seemed about the same and perhap [sic] a bit worse than the previous [company] sim - However, the earlier periods in the NASA sim were much more comfortable with regard to nausia [sic], vertigo, motion, etc. |
| M-05 | Same. |
| M-06 | Physical comfort was fine. No symptoms noted. I could get clues, however, to when I had failed to use proper coordinated control inputs. |
| M-07 | Seemed as comfortable - airflow, noise, headsets, visuals, instruments etc., all seemed about the same comfort level. |
| M-08 | None. |
| M-09 | See above [The simulator here and the one at [airline company] seemed identical to me]. NASA sim seems to have better air conditioning than [company simulator]. |
| M-10 | Well, since the last sim was a little more stable, there were occasions that I felt mild discomfort, but nothing degrading. |
| M-11 | It seemed warm to me, but getting in the "hot seat" always makes one warm and sweaty. The sim was the same in this respect. |
| M-12 | Same as above [they are both so close to the same I would judge them equal.] |
| M-13 | Physical comfort good - I like using day mode with the lights turned up. |
| M-14 | No comments. |
| M-15 | Same except rudder/ yaw control loading seemed excessive. |
| M-16 | About the same - good visual. |
| M-17 | The same. |
| M-18 | Physical comfort is not that difference between the two simulator. |
| M-19 | Ok. |
| M-20 | Very similar feel except for better visual in the clouds (as previously noted) |
| NM-01 | The NASA sim was cleaner. |
| NM-02 | Same. |
| NM-03 | Generally seems to require a little more effort physically to maintain a given profile. |
| NM-04 | With the motion dialed up, the excessive yaw sensitivity leads to some pretty big motion transients, which I believe are exagerated [sic]. This could create some discomfort. |
| NM-05 | Same as other sims. |
| NM-06 | I am dizzy and my body feels weak. I think I would be the same in any sim after that workout. |
| NM-07 | Same - Very comfortable to me. |
| NM-08 | Very comfortable/ same as [company] simulator. |
| NM-10 | The first afternoon period I felt wacked out - wierd [sic] - funky. Other sessions in the morning nothing to note. The last afternoon period was not noticeable. |
| NM-11 | Comfort was good. Never used my sweatshirt or got hot. |
| NM-12 | Same as the previous simulators I have flown. No worse or better. |
| NM-13 | Sim felt like it "free flowed" a lot more. Could make for some uneasy stomachs. |
| NM-14 | The sims felt identical. |
| NM-15 | Same |
| NM-16 | The last session was the most disorienting, however, not overwhelming. Otherwise, the NASA sim had the same comfort level as previous sims that I have flown. |
| NM-17 | The reduction in sim disorientation is a marked plus. The more comfortable one is with the realism of the training environment the better he will acquire and retain what he learns. |
| NM-18 | I felt comfortable by the final set. It is rather squarrozy compared to the aircraft but certainly manageable. |
| NM-19 | See Above [As I said previously, things just seemed easier in the NASA sim. But this is a no risk environment and much of the perceived "easiness" might by psychological.] |
| NM-20 | They are equal. |
| NM-21 | Same when the motion is on. |

FINAL COMMENTS CONTROL FEEL, SENSITIVITY, OTHER CUES

| PF | Comment |
| --- | --- |
| M-01 | The aircraft is easier to fly as there are more clues as to what is occurring. The simulator did a funny pitch at 1,000 AGL several times. The simulator is fairly realistic though and if you fly the simulator well you can fly the aircraft even better most of the time. JBC: With respect to other clues, the pilot also added that there were more in the aircraft, e.g., engine noise. |
| M-02 | Overall by phase IV you forget the experience per say of the actual aircraft and concentrate on the control feel and sensitivity of the simulator. So, these elements were normal. |
| M-03 | Felt sensitivity made it hard to correct for changes in yaw and pitch. It would be easier in the airplane to adjust changes in wind etc. |
| M-04 | The final sim period, the feel, sensitivity felt worse than the earlier periods and worse than the airplane - significantly worse, expecially [sic] with regards to the pitch & aileron and throttle. Also, the control loading on the rudders [sic] seem too heavy. |
| M-05 | No further comments. |
| M-06 | Most sims I have ever flown never fly the same as the airplane. They are generally most sensitive in roll and rudder response to inputs. Pitch trim was normal. I feel that the "air noise" is louder in this simulator compared to the airplane for the same parameters and flight conditions |
| M-07 | Perceived stability degradation in second half seemed to heighten workload to just fly the simulator. Not many brain cells left for working the engine problem etc. After t/o and climbout, the sim seemed to "bump" as if in mild turbulence and then seemed to start "wandering" becoming sloppy and harder to control. |
| M-08 | Less visual cues, therefore more oscillation in turns, eng failures etc. Overall, good instrument cues for testing control sensitivity as it compared to airplane performance. |
| M-09 | Pitch, yaw and roll are all harder to fly precisely than the airplane. All 3 plus the elevator trim seem to lag more than the airplane. Speed stability is more sensitive than the airplane. If you are level with power and speed stable and then enter a slight climb or descent, speed increases or decreases more rapidly than it would on the airplane. All controls feel somewhat heavier than the airplane. |
| M-10 | The aircraft is more stable than the sim, but I think one learns more from an unstable platform. The visual on this sim is one of the best I've seen. - Good feel for flair [sic] alt & rate of decent [sic]. The airplane speed and heading control is better. One can usually look away for a second or two without losing control (no, it really wasn't that bad!) For a light aircraft, the engines didn't seem to respond as in the real acft/ [sic]. |
| M-11 | I find the simulator (as in all simulators) to be very sensitive and very slightly lagging behind my inputs. I think if you can fly the sim well, you can fly the airplane better. I [sic] always takes me a little while to get used to the sim. It's always a humbling experience (not necessarily a bad thing). I think the airplane is easier to fly, generally. |
| M-12 | To me a simulator never feels exactly like the airplane. That means that to a great extent flying a simulator well means very quickly [determining] what the differences are. From that point on the problem is how to make the sim do what you want it to do. |
| M-13 | Overall, compared to the airplane & other simulators I have been in, this simulator is as good as any in representing the airplane. |
| M-14 | In general, control feel / sensitivity / loading felt slightly lighter than actual aircraft in all scenarios. Only exception was last session pitch trim requirements and pitch input requirements slightly higher. (In other words - Overall control pressure was more sensitive in nature than aircraft). |
| M-15 | Simulator vs the airplane - Controls are way too sensitive. The false feeling burbles on the turns were not realistic- windshear example was not realistic with airplane experience- having no fly by the seat of your pants feel adds to difficulty in flying visuals - also yaw control loading seemed way over sensitive when moving rudders [sic] quickly |
| M-16 | I feel I did better the last session got use to the sim & inputs - more relaxed. |
| M-17 | Feel and sensitivity seem light and quick respectively (especially yaw) but either became more similar to what I’m used to, or I got more adept. |
| M-18 | This last session the simulator feel a little more heavier. But sensitivity is a more pronounce in the sim then in the airplane. Noise level seemed to be less than before. |
| M-19 | Sim - Slop in the yoke. You can move the yoke a little before getting some reaction - In airplane you get instant reaction and no dead spots (or slop). Noise is good. |
| M-20 | Sim behaved like aircraft as near as I could tell. |
| NM-01 | I think the simulator motion input was increased on the last 2 periods. ELV [elevator] feel was difficult to estimate. The trim made no noise when running. |
| NM-02 | Simulator is a little rough sometimes when you make aggressive inputs-the airplane is not quite as rough Throttles were a little sensitive - - maybe aircraft (simulator was light) Elevator was still a little heavy in light turbulence |
| NM-03 | Feel in all axes of control seem slightly lighter than normal. Control sensitivity in pitch + roll seem slightly higher than normal, but this may be explained by lighter gross weights used in the scenario. Control sensitivity in yaw is much higher than normal. Based on control movements (rudder or aileron through adverse yaw), trim effects or asymetric [sic] thrust. It was very difficult to make subtle changes without over controlling, even with practice. Motion cues varied throughout the day, with motion cues being imperceptible in first 2 sessions. Overall fidelity of sim is directly proportional to motion. |
| NM-04 | Feel in all axes of control seemed slightly lighter than norm. Control sensitivity in pitch and roll seemed slightly higher than normal. But this may be explained by lighter gross weights used in the scenario. Control sensitivity in yaw is much higher than normal. Based on control movements (rudder or aileron through adverse yaw), trim effects or asymmetric thrusts. It was very difficult to make subtle changes without over controlling. Even with practice. Motion cues varied throughout the day, with motion cues being imperceptible in 1st 2 sessions. Overall fidelity of sim is directly proportional to motion. |
| NM-05 | Rudder still to sensitive, others are acceptable, far better than a few years back, but improvements are coming along. Again if you can fly the sim the airplane is a piece of cake. |
| NM-06 | The control feel in the NASA sim is [?] than the [company] airpliain [sic]. |
| NM-07 | Same as aircraft. |
| NM-08 | Overall feel of sim is very similar to the airplane. I found it somewhat more sensitive in pitch than the airplane. Visual system is very good |
| NM-10 | The last period seemed a bit more pitch sensitive. In the afternoon I could hear and feel the landings whereas in the morning period I did not. I did not feel as funky in the very last event set. The noise was more noticeable/audible in the afternoon set. |
| NM-11 | Simulator does not seem to decel when configuring for landing like the a/c does. In the a/c very little power corrections are needed from level altitude/cvean, Vzf +20 [?] to GS intercept/landing config. on glideslope. Final approach/flair [sic] seemed correct. On last session sim. would seem to pitch up or down while turning for no apparent reason. |
| NM-12 | Compared to the airplane the simulator felt like most simulators relating to the airplane. More sensitivity, in the yaw (rudder) and the ailerons, especially. Pitch was good. Throttle response good. |
| NM-13 | Overly sensitive, inputs were made and it felt like, little effect at first then inputs were overexaggerated later, sim felt very light and was constantly fighting it to fly it. From rudders, to trim everything. |
| NM-14 | This felt the most like the airplane. The cues provided helped identify the malfunctions. The controls felt heavy as they do in the airplane. Trimming is done more to releive [sic] control pressure than to maintain desired attitude. Without proper trimming the sim and plane feel very heavy making it uncomfortable. |
| NM-15 | Simulator felt "sensitive" on controls (unstable about all three axes), otherwise similar to simulators at my company. |
| NM-16 | In the last session during the take off phase, the control sensitivity seemed particularly high. I felt as though it was difficult not to overcontrol the aircraft. The control feel was reasonably normal. The rudder feel may have been a little light. |
| NM-17 | Rudder control seemed stiffer in this last segment. |
| NM-18 | Wow, not sure now what's real and what's not! The last ses seemed fairly familiar. |
| NM-19 | Throttles in sim read about 1.20 EPR in same position throttles in A/C read 1.10 EPR. The NASA sim generally seems more responsive than [company] sims. In retrospect the control forces seem about the same but sensitivity is increased. The slip indicator is much more sensitive than [company] sims and A/C [aircraft]. Things (maneuvers) seem easier to accomplish in NASA sim. (I like the viz better, also). |
| NM-20 | The same as previous surveys the rudder seems sensitive and control feel for rudder is slightly light. Pitch seems on except for short final. |
| NM-21 | Felt several small pitch oscillates while hand flying turning to final at about 20 degrees of bank. Rudder seemed a little too sensitive, made the slip indicator dance around a lot. |

FINAL COMMENTS HANDLING QUALITIES, CONTROL STRATEGY

| PF | PNF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- | --- |
| M-03 | PNF-1 | 2 | engine-out sidestep landing | Very experienced. Above [ratings] is based on that. |
| M-06 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Seems to have better than average instrument cross check. |
| M-07 | PNF-1 | 2 | engine cut at VR; overall gain of proficiency | Wrong rudder on 2nd VR Cut. Overall gain average harder on average based on VR cuts |
| M-08 | PNF-1 | 2 | engine cut at V1 | Gained proficiency as average except V1 cut which was much better improvement. |
| M-09 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Gained proficiency slightly easier, scan pattern increased. |
| M-10 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Big improvement over first attempt. Seems to have good instrument scan. |
| M-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seems to have a bit more problem with rudder control on engine failures on take off. Instrumt [sic] scan on approaches is better than average. Above average approaches & landings. |
| M-12 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. began to get tired during last half of session. |
| M-13 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good x [cross] scan. |
| M-14 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good understanding of flight director use. I think PF became tired during final sequence & slightly overcontrol loc intercept, but a good job. |
| M-15 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying ability (instrument scan) allowed for above average improvement. |
| M-16 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has trouble with raw data approaches. Did not seem to be aware of wind direction/ velocity read-out on ND. |
| M-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good scan and basic skills. One straight-in approach did not go too well but others were good. |
| M-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with good basic skills & scan to build on. |
| NM-02 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check, particularly for getting as little flying as he does. |
| NM-05 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Average for experienced pilot. |
| NM-06 | PNF-2 | 2 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | PF slow to increase scan pattern, therefore overcorrected & chased information. |
| NM-08 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Approach speeds are high without correction. |
| NM-10 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is a current sim instructor. |
| NM-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR | Gain in proficiency on engine cuts came as much from explaining/understanding F/D & what it commands for speed as flight practice. Good improvement in heading control with practice.(engine cuts) |
| NM-13 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good instrument scan & good basic skills. |
| NM-14 | PNF-1 | 2 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall gain in proficiency. Crashed on 1st V1 cut. But got to average level after that. All approaches became above average, except last straight in approach. |
| NM-15 | PNF-2 | 2 | engine-out straight-in approach/landing | On ILS P.F. slightly slow on wind change on appch. |
| NM-16 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good scan pattern. |
| NM-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | On one VR cut simulator seemed to turn left for no apparent reason, before engine failure, sim was frozen, all others normal. |
| NM-18 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills and instrument scas [sic]. |
| NM-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with, allowed good gain in prof. particularly with engine failures. |
| NM-21 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is an instructor in simul. |
| M-03 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Coming back after lunch seems to be hard. Seems to take time to get back up to speed. |
| M-06 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | In first engine cut and approach (VR & straight in) gain in proficiency was a bit below normal. Second circuit was average. |
| M-07 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Take offs about the same as start - (Approaches/Landings better) Used correct rudder inputs but a bit late. |
| M-08 | PNF-1 | 3 | engine cut at V1 | Regressed on Engine Failure at V1. |
| M-10 | PNF-1 | 3 | engine cut at V1; engine cut at VR; | First after lunch, heading control on take offs with engine failures not as good as practice session - approaches were average |
| M-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good improvement in engine cuts. Continues to improve approaches. |
| M-12 | PNF-2 | 3 | engine-out straight-in approach/landing | PF slightly over controlled pitch on raw data ILS (after lunch). |
| M-14 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF seems to be a little tired, possible jet lag. |
| M-15 | PNF-1 | 3 | engine cut at VR | Engine cut at VR seemed to be a bit of a surprise. |
| M-16 | PNF-1 | 3 | engine-out straight-in approach/landing; overall gain of proficiency | Straight in approach is getting better but would still be a go around under normal conditions. |
| M-17 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good inst. scan & basic abilities. |
| M-18 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF had slight lunch break letdown. |
| M-19 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with above average skills. |
| M-20 | PNF-2 | 3 | engine-out straight-in approach/landing | PF had slight let down on ILS approach (lunch). |
| NM-02 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skill in the begining [sic]. |
| NM-05 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check & is a bit further ahead of the aircraft than average. |
| NM-06 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Proficiency increaced [sic] at a normal rate from proficiency during training phase. |
| NM-08 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall improvement. |
| NM-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has gained proficiency easier than average - better than average basic skills. |
| NM-13 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Improvement after the break better than average. Good basic flying skills & scan. |
| NM-14 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Engine failures acceptable, approaches good - PF seems to have good instrument scan. |
| NM-16 | PNF-2 | 3 | engine cut at VR | P.F. seem to over react to motion on VR cut. Improved quickly. |
| NM-17 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Engine cut at V1 was better than VR cut. VR cut was almost crash. Not having motion washed out took PF by surprise. Speed on straight in approach was about 20 kts high--Side step approach was almost normal with speed about 10 kts high. Also on VR engine cut, believe PF initially applied wrong rudder |
| NM-18 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills & scan. |
| NM-19 | PNF-1 | 3 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | VR cut was first take off - after that, PF got the "feel" of simulator somewhat better. |
| M-03 | PNF-1 | 4 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Seemed to do better in the morning. |
| M-06 | PNF-1 | 4 | engine cut at VR | Engine cut at Vr made harder by use of wrong rudder at engine failure. After recovery, average performance. |
| M-07 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | Takeoffs average this time. Approaches above average. |
| M-09 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. has good scan & flying background. |
| M-11 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | V1/ VR Cuts improved as average. Approaches improved better than average due good instrument scan. |
| M-12 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was somewhat tired due to more raw data flying than normal. |
| M-13 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF may have become a little bored or tired during last two sessions. |
| M-14 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was tired. (jet lag?) |
| M-18 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF flew this session without using rudder trim therefore tended to slightly overcontrol. |
| M-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skills starting. |
| NM-02 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Pilot started from good level of proficiency. Gained proficiency as instrument flying basics were already good. |
| NM-05 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | As before, good basic instrument cross-check makes improvement easier. |
| NM-08 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good gain in proficiency. Good basic flying ability - good scan. |
| NM-11 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills allowing better than average progress. |
| NM-13 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good basic skills, & instrument scan. Backslid a little on straight in approach as speed got a little low. |
| NM-14 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Oscilation [sic] in roll much improved from previous. Seems to have good basic skills & be ahead of the aircraft. |
| NM-15 | PNF-2 | 4 | engine cut at V1; engine cut at VR | P.F. tends to allow a/c to drift off LOC/G.S. after visual contact with-out FLT DIR. |
| NM-16 | PNF-2 | 4 | engine cut at VR | P.F. still over controls on VR cut. |
| NM-17 | PNF-1 | 4 | engine-out sidestep landing | Speed control on straight-in landing was about the only problem this time. |
| NM-18 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic skills better than average instrument scan. |
| NM-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with. |
| NM-20 | PNF-2 | 4 | engine-out straight-in approach/landing; | PF overcontrol with full motion |
| NM-21 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. is siml [simulator] instru [instructor]. |

FINAL COMMENTS GAINING PROFICIENCY

| PF | PNF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- | --- |
| M-03 | PNF-1 | 2 | engine-out sidestep landing | Very experienced. Above [ratings] is based on that. |
| M-06 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Seems to have better than average instrument cross check. |
| M-07 | PNF-1 | 2 | engine cut at VR; overall gain of proficiency | Wrong rudder on 2nd VR Cut. Overall gain average harder on average based on VR cuts |
| M-08 | PNF-1 | 2 | engine cut at V1 | Gained proficiency as average except V1 cut which was much better improvement. |
| M-09 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Gained proficiency slightly easier, scan pattern increased. |
| M-10 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Big improvement over first attempt. Seems to have good instrument scan. |
| M-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seems to have a bit more problem with rudder control on engine failures on take off. Instrumt [sic] scan on approaches is better than average. Above average approaches & landings. |
| M-12 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. began to get tired during last half of session. |
| M-13 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good x [cross] scan. |
| M-14 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good understanding of flight director use. I think PF became tired during final sequence & slightly overcontrol loc intercept, but a good job. |
| M-15 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying ability (instrument scan) allowed for above average improvement. |
| M-16 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has trouble with raw data approaches. Did not seem to be aware of wind direction/ velocity read-out on ND. |
| M-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good scan and basic skills. One straight-in approach did not go too well but others were good. |
| M-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with good basic skills & scan to build on. |
| NM-02 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check, particularly for getting as little flying as he does. |
| NM-05 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Average for experienced pilot. |
| NM-06 | PNF-2 | 2 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | PF slow to increase scan pattern, therefore overcorrected & chased information. |
| NM-08 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Approach speeds are high without correction. |
| NM-10 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is a current sim instructor. |
| NM-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR | Gain in proficiency on engine cuts came as much from explaining/understanding F/D & what it commands for speed as flight practice. Good improvement in heading control with practice.(engine cuts) |
| NM-13 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good instrument scan & good basic skills. |
| NM-14 | PNF-1 | 2 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall gain in proficiency. Crashed on 1st V1 cut. But got to average level after that. All approaches became above average, except last straight in approach. |
| NM-15 | PNF-2 | 2 | engine-out straight-in approach/landing | On ILS P.F. slightly slow on wind change on appch. |
| NM-16 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good scan pattern. |
| NM-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | On one VR cut simulator seemed to turn left for no apparent reason, before engine failure, sim was frozen, all others normal. |
| NM-18 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills and instrument scas [sic]. |
| NM-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with, allowed good gain in prof. particularly with engine failures. |
| NM-21 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is an instructor in simul. |
| M-03 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Coming back after lunch seems to be hard. Seems to take time to get back up to speed. |
| M-06 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | In first engine cut and approach (VR & straight in) gain in proficiency was a bit below normal. Second circuit was average. |
| M-07 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Take offs about the same as start - (Approaches/Landings better) Used correct rudder inputs but a bit late. |
| M-08 | PNF-1 | 3 | engine cut at V1 | Regressed on Engine Failure at V1. |
| M-10 | PNF-1 | 3 | engine cut at V1; engine cut at VR; | First after lunch, heading control on take offs with engine failures not as good as practice session - approaches were average |
| M-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good improvement in engine cuts. Continues to improve approaches. |
| M-12 | PNF-2 | 3 | engine-out straight-in approach/landing | PF slightly over controlled pitch on raw data ILS (after lunch). |
| M-14 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF seems to be a little tired, possible jet lag. |
| M-15 | PNF-1 | 3 | engine cut at VR | Engine cut at VR seemed to be a bit of a surprise. |
| M-16 | PNF-1 | 3 | engine-out straight-in approach/landing; overall gain of proficiency | Straight in approach is getting better but would still be a go around under normal conditions. |
| M-17 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good inst. scan & basic abilities. |
| M-18 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF had slight lunch break letdown. |
| M-19 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with above average skills. |
| M-20 | PNF-2 | 3 | engine-out straight-in approach/landing | PF had slight let down on ILS approach (lunch). |
| NM-02 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skill in the begining [sic]. |
| NM-05 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check & is a bit further ahead of the aircraft than average. |
| NM-06 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Proficiency increaced [sic] at a normal rate from proficiency during training phase. |
| NM-08 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall improvement. |
| NM-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has gained proficiency easier than average - better than average basic skills. |
| NM-13 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Improvement after the break better than average. Good basic flying skills & scan. |
| NM-14 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Engine failures acceptable, approaches good - PF seems to have good instrument scan. |
| NM-16 | PNF-2 | 3 | engine cut at VR | P.F. seem to over react to motion on VR cut. Improved quickly. |
| NM-17 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Engine cut at V1 was better than VR cut. VR cut was almost crash. Not having motion washed out took PF by surprise. Speed on straight in approach was about 20 kts high--Side step approach was almost normal with speed about 10 kts high. Also on VR engine cut, believe PF initially applied wrong rudder |
| NM-18 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills & scan. |
| NM-19 | PNF-1 | 3 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | VR cut was first take off - after that, PF got the "feel" of simulator somewhat better. |
| M-03 | PNF-1 | 4 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Seemed to do better in the morning. |
| M-06 | PNF-1 | 4 | engine cut at VR | Engine cut at Vr made harder by use of wrong rudder at engine failure. After recovery, average performance. |
| M-07 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | Takeoffs average this time. Approaches above average. |
| M-09 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. has good scan & flying background. |
| M-11 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | V1/ VR Cuts improved as average. Approaches improved better than average due good instrument scan. |
| M-12 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was somewhat tired due to more raw data flying than normal. |
| M-13 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF may have become a little bored or tired during last two sessions. |
| M-14 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was tired. (jet lag?) |
| M-18 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF flew this session without using rudder trim therefore tended to slightly overcontrol. |
| M-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skills starting. |
| NM-02 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Pilot started from good level of proficiency. Gained proficiency as instrument flying basics were already good. |
| NM-05 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | As before, good basic instrument cross-check makes improvement easier. |
| NM-08 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good gain in proficiency. Good basic flying ability - good scan. |
| NM-11 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills allowing better than average progress. |
| NM-13 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good basic skills, & instrument scan. Backslid a little on straight in approach as speed got a little low. |
| NM-14 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Oscilation [sic] in roll much improved from previous. Seems to have good basic skills & be ahead of the aircraft. |
| NM-15 | PNF-2 | 4 | engine cut at V1; engine cut at VR | P.F. tends to allow a/c to drift off LOC/G.S. after visual contact with-out FLT DIR. |
| NM-16 | PNF-2 | 4 | engine cut at VR | P.F. still over controls on VR cut. |
| NM-17 | PNF-1 | 4 | engine-out sidestep landing | Speed control on straight-in landing was about the only problem this time. |
| NM-18 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic skills better than average instrument scan. |
| NM-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with. |
| NM-20 | PNF-2 | 4 | engine-out straight-in approach/landing; | PF overcontrol with full motion |
| NM-21 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. is siml [simulator] instru [instructor]. |

FINAL COMMENTS MISCELLANEOUS

| PF | Comment |
| --- | --- |
| M-02 | FYI: Loc capture: The PFD was given correct loc information. However, when I put in a "wind correction course" that should have corrected course destination, I noticed that on the "ND" it actually parallels the course with no intercept heading at all. When I figured this out, I made the proper heading correction to stay on the loc. course. Due to the cross-wind problem. VR Cut: During Phase IV I thought the aircraft yawed to the right for a left engine out, but actually it yawed left for a right engine out. As a result, I applied the wrong rudder which causes the aircraft unusual attitude. |
| M-03 | Enjoyed the practice on approaches. Thought the engine out feeling was very close to the airplane reaction would be. Thought tracking localizer more difficult and hard to control. |
| M-04 | Scenarios are so challenging and require so much attention to be focused on the mission that it is difficult to be cognizant of the items we are asked to evaluate. Also, not knowing in advance what items we are going to be commenting on, it is hard to reconstitute in your mind how those items (components) performed. |
| M-07 | Great facilities - Everyone is ready and works hard to make it an enjoyable, productive experience for the pilot - - Thanks! |
| M-08 | Turn the lights up on the upper EICAS instruments. |
| M-10 | Not knowing the full scope of the experiment, I'm not sure of other aspects. I know I appreciated the opportunity to fly a 747 sim for several hours. The folks conducting the experiment were very professional and assisted greatly in my being comfortable with the experience. |
| M-11 | I’m not sure what you are doing exactly, except making me sweat (HA!) Actually I would like to hear about it and also debrief how I did. Thanks for the opportunity to fly the simulator. I love the practice that I don't get in the airplane. Would like to do it again. Also, its hard to remember what the last sim I flew was like so its hard to compare unless I just flew it. |
| M-12 | My one missed approach felt like I was encountering a strong wind shear, which resulted in great increases in both airspeed and altitude |
| M-13 | Lunch break killed my performance [pilot drew an unhappy face] |
| M-14 | As sim technology continues to progress and improve, most noticeable absent feature is ground rush nominal to actual aircraft operations. Especially side windows. |
| M-16 | Maybe start off using the F/D a little more at first - at least one approach. |
| M-17 | Felt like I was flat footed at outset (Literally & figuratively!) |
| M-18 | The experiment is very intensive. Even though you do same maneuvers over and over. It is very hard to become comfortable with the maneuvers even though you know what is going to happen. It is a well thought experiment. Congratulations.-------------- |
| M-20 | The NASA and [company] sims behavior in the V2 cut is something I've often questioned. Based on my experience in the Boeing KC-135 and actual V2 cuts, the simulators seem to require a much faster and more aggressive response in order to maintain sim control. I find it difficult to believe the aircraft would behave similarly. I have not had an actual engine failure in the 747 so it is hard for me to say. However, compared to an actual failure of an engine in a KC-135, the simulator "wraps up" tighter and faster than I would expect. |
| NM-02 | Always treated great here! |
| NM-04 | On in-briefing, emphasize that you don’t want us flying to company Ops - Specs (Visibility requirements) or SOPs (use of VNAV/VNAV)on takeoff, autothrottle use, flight director use etc). At [airline company], no VNAV takeoff are not done unless a system degrade requires it. In that case, Id be reviewing that profile carefully. |
| NM-05 | I hope you get lots of useful data. |
| NM-06 | We should have this type of workout at [airline company] for our P.I. CR. |
| NM-07 | Good workout - Feel more proficient now by a great deal. Thank you very much for this opportunity. |
| NM-08 | Performance plots are helpful in bringing attention to areas that are out of limits ie) bank angle. The learning curve to improve instrument scan from raw data vs. flight director, auto throttle takes 6 to 9 approaches and landings. Some discussion of EPR (power) settings before flying would speed up the learning process. |
| NM-10 | Very professionally executed from start to finish. Including the rental car/hotel arrangements. I feel that my professional abilities have been greatly expanded. Since this is a performance based profession, it is important to challenge yourself and grow professionally - That objective was accomplished today in this experiment. |
| NM-12 | Nice group of people hosting the study. Thank you! |
| NM-13 | Enjoyable. |
| NM-14 | I enjoyed the atmosphere[sic]. I hope I was helpful. |
| NM-16 | Without knowing the research goals of the testing, I have no comments on the experiment. A good dusting of the cobwebs for me though. |
| NM-17 | Questions on questionnaires are a bit ambiguous could be a bit clearer. I finally caught on what was really being asked in the second or third set of questions. Specifically with regard to the sensitivety [sic] and control issues. |
| NM-18 | Nice study. I must say that overall I feel less certain now about how the aircraft feels. I look forward to flying the airplane again to further evaluate this study. Id be happy to follow up once I fly again. Email: [email address] Thxs ws |
| NM-19 | Sorry too tired to think! Very interesting maneuvers. I appreciated the opportunity to repeat maneuvers and see feedback. The feedback wasn't always what I expected. Thanks |

PNF COMMENTS ON MOTION

| PF | PNF | Questionnaire | Question | Subquestion | Comment |
| --- | --- | --- | --- | --- | --- |
| NM-10 | PNF-2 | 3 | control performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. somewhat surprised of control feel with motion on, so initially overcontroled [sic], but improved quickley [sic]. |
| NM-15 | PNF-2 | 3 | control performance | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. slighly [sic] overcontroled [sic] with motion on intiality [sic], but improved quickly. |
| NM-16 | PNF-2 | 3 | control strategy and technique | engine cut at VR | Seem to over react to motion after lunch |
| NM-16 | PNF-2 | 3 | gaining proficiency | engine cut at VR | P.F. seem [sic] to over react to motion on VR cut Improved quickley [sic]. |
| NM-17 | PNF-1 | 3 | gaining proficiency | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Engine cut at V1 was better than VR cut. VR cut was almost crash. Not having motion washed out took PF by surprise. Speed on straight in approach was about 20 kts high--Side step approach was almost normal with speed about 10 kts high. Also on VR engine cut, believe PF initially applied wrong rudder |
| NM-20 | PNF-2 | 3 | control strategy and technique | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all mavn. [maneuvers] P.F. tended to overcontrol due to full motion. |
| NM-20 | PNF-2 | 4 | gaining proficiency | engine-out straight-in approach/landing; | PF overcontrol with full motion |
| NM-21 | PNF-2 | 3 | control strategy and technique | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF slightly overcontroled [sic] while getting feel with motion on. |

PNF COMMENTS ON PF PERFORMANCE

| PF | PNF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- | --- |
| M-01 | PNF-2 | 1 | engine-out straight-in approach/landing | Almost average on PIA |
| M-02 | PNF-2 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF Scan pattern very proficient. |
| M-03 | PNF-1 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Level is average I would expect for first attempt. |
| M-04 | PNF-2 | 1 | engine cut at V1 | Aborted after V1 |
| M-10 | PNF-1 | 1 | engine-out straight-in approach/landing | Got loc full off on straight in approach. |
| M-15 | PNF-1 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Average for first period. |
| NM-06 | PNF-2 | 1 | engine cut at VR; engine-out straight-in approach/landing | PF overcontrol due to slow scan pattern while flying raw data. |
| NM-14 | PNF-1 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Average for first attempt. |
| NM-17 | PNF-1 | 1 | engine-out straight-in approach/landing | Lost scan on straight in approach towards the end (under 1000' AGL). |
| NM-18 | PNF-1 | 1 | engine-out straight-in approach/landing | Misunderstanding on MDA/DH and started go around early. Average up to that point. |
| M-03 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Average for experienced pilot in this aircraft. |
| M-06 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Refer to previous page [Seems to have better than average instrument cross check] good instrument cross-check. |
| M-17 | PNF-1 | 2 | engine-out straight-in approach/landing | Straight in approaches except for one was good the other two were better than average. |
| M-18 | PNF-2 | 2 | engine cut at V1; engine cut at VR | PF would have done better on eng cut but he antisipated [sic] which eng would fail & sometime [sic] put in incorrect rudder slightly. |
| NM-06 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | See note Qu # 1 [PF slow to increase scan pattern, therefore overcorrected & chased information.] |
| NM-08 | PNF-1 | 2 | engine cut at V1; engine cut at VR | Average approach except speeds remain high. |
| NM-14 | PNF-1 | 2 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing | First V1 cut-crashed. Became average level after that. Achieved above average level on approaches - Did backslide a bit on last straight in approach. |
| NM-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Scan seems a bit slow at times. |
| M-02 | PNF-2 | 3 | engine cut at VR | PF not mentally prepare [sic] for T.O. |
| M-03 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | Comments same as previous page. [Coming back after lunch seems to be hard. Seems to take time to get back up to speed.] |
| M-06 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | Learning took place between first & second circuits. |
| M-07 | PNF-1 | 3 | engine cut at VR | A bit late on rudder input on Vr cut. |
| M-08 | PNF-1 | 3 | engine cut at V1 | Regressed on V1 engine failure |
| M-12 | PNF-2 | 3 | engine-out straight-in approach/landing | See previous comment [PF slightly over controlled pitch on raw data ILS (after lunch).] |
| M-18 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF slight over control, due to getting behind on scan, due to lunch break. |
| NM-04 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. experienced after lunch lull |
| NM-06 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF still tends to overcontrol. |
| NM-10 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. somewhat surprised of control feel with motion on, so initially overcontroled [sic], but improved quickley [sic]. |
| NM-15 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. slighly [sic] overcontroled [sic] with motion on intiality [sic], but improved quickly. |
| NM-17 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing; | Engine failure at VR - Aircraft generally out of control until at 3500' and 270 deg heading. Believe wrong rudder applied at first. On approaches, speed control lacking about 20 kts high on straight-in & 10 kts on side step. |
| M-02 | PNF-2 | 4 | engine cut at VR | 2nd Vr Cut OK |
| M-03 | PNF-1 | 4 | engine cut at VR; engine-out straight-in approach/landing | Did well before lunch. |
| M-06 | PNF-1 | 4 | engine cut at VR | Use of wrong rudder at engine cut made performance below average. |
| NM-02 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | See previous comments [Pilot started from good level of proficiency. Gained proficiency as instrument flying basics were already good]. |
| NM-05 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | Raw data approaches better than average, pilot ahead, seems to be reacting to wind data & not just to needle displacement. |
| NM-17 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Once again, speed control on approach was the main problem. |

PNF COMMENTS ON PF’S STRATEGY

| PF | PNF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- | --- |
| M-06 | PNF-1 | 1 | engine-out sidestep landing | Used quite a bit more rudder trim, than necessary. |
| M-08 | PNF-1 | 1 | engine cut at V1 | Crashed |
| M-08 | PNF-1 | 1 | engine-out straight-in approach/landing | Got behind a/c - scan pattern slow. |
| M-10 | PNF-1 | 1 | engine cut at V1; engine cut at VR | Doesn’t use rudder trim. |
| M-10 | PNF-1 | 1 | engine-out straight-in approach/landing | Didn’t use wind information. |
| M-13 | PNF-2 | 1 | engine cut at V1; engine cut at VR | PF turns A/C to 270 degrees before cleaning up flaps with eng failure. |
| M-15 | PNF-1 | 1 | engine-out straight-in approach/landing | Didn’t use normal amount of rudder trim. |
| M-16 | PNF-1 | 1 | engine-out straight-in approach/landing | Didn't seem to use NAV display wind indication. |
| NM-08 | PNF-1 | 1 | engine cut at V1 | Aborted |
| NM-11 | PNF-1 | 1 | engine cut at V1; engine cut at VR | Out of 1400' MSL accelerated & cleaned up aircraft as one would but looked through F/D so speeds will show high at this point. |
| NM-13 | PNF-1 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | same as average on first attempt |
| NM-14 | PNF-1 | 1 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing | Did not use rudder trim until side step approach. |
| NM-18 | PNF-1 | 1 | engine-out straight-in approach/landing | Started GA early due to misunderstanding of minimums. Average up to that point. |
| NM-19 | PNF-1 | 1 | engine-out straight-in approach/landing; engine-out sidestep landing | Good scan - raw data approaches better than average. |
| NM-20 | PNF-2 | 1 | engine cut at VR | PF turned autopilot on early without advising PNF. A/C was 2000MSL so I let it continue. |
| M-03 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Techniques (overall) were standard. |
| M-07 | PNF-1 | 2 | engine cut at VR | Wrong rudder on 2nd Vr cut - otherwise average performance. |
| M-08 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Instrument scan seems a little slower than the average that I have seen. |
| M-10 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Doesn’t use rudder trim very much. |
| M-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR | Technique on engine cuts - seemed to be behind the aircraft & over controlled to catch up. |
| M-12 | PNF-2 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | PF uses inboard REV only after landing (technique only). |
| M-14 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF uses rudder trim quite a bit, slightly more & quicker than the average PF. |
| M-16 | PNF-1 | 2 | engine-out straight-in approach/landing | Did not correct for wind chased LOC needle with big corrections. |
| M-20 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. flys [sic] with zero rudder trim & uses manual input. On appch P.F. flys [sic] with differential throtte [sic] position (i.e. outboad [sic] operating eng at idle). |
| NM-02 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Strategy same as average but cross check better than average resulting in above average performance. |
| NM-03 | PNF-2 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | P.F. controls speed using inboard throttles only, leaves outboard at approach power after landing, through landing roll |
| NM-06 | PNF-2 | 2 | engine cut at VR | PF initial rudder input wrong direction all 3 T.O. s |
| NM-06 | PNF-2 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | A/C in landing config outside Charr |
| NM-08 | PNF-1 | 2 | engine-out sidestep landing | Leaves approach speed high-otherwise average to above average |
| NM-16 | PNF-2 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | PF sets desired target speed below ref speed for current flap setting. PF uses ref + 10kt for app speed. So is constantly fast on final app. |
| NM-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Tech. & strat. same. PF just further ahead of a/craft than average. |
| M-03 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | See comments on first page [Coming back after lunch seems to be hard. Seems to take time to get back up to speed.] Pilot was not out ahead of the airplane & had trouble catching up. |
| M-05 | PNF-2 | 3 | engine cut at V1; engine cut at VR | P.F. climbed to 3500, began left turn to 270 degrees, then started flap retraction. |
| M-07 | PNF-1 | 3 | engine cut at VR | A bit late on rudder input. |
| M-08 | PNF-1 | 3 | engine cut at V1 | Slow to recognize & correct. |
| M-10 | PNF-1 | 3 | engine-out straight-in approach/landing | Had good outboard engine reduced to lower power than inboard engines. |
| M-12 | PNF-2 | 3 | engine-out straight-in approach/landing | see previous [PF slightly over controlled pitch on raw data ILS (after lunch)] |
| M-13 | PNF-2 | 3 | engine cut at V1; engine cut at VR | PF appeared to try to antisapate [sic] eng failing, therefore slightly overcontrold [sic]. |
| M-16 | PNF-1 | 3 | engine-out straight-in approach/landing | Behind the aircraft with wind corrections. Large heading changes but getting better. |
| M-18 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | See previous comments. [PF slight over control, due to getting behind on scan, due to lunch break.] |
| M-20 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF flys [sic] with split throttle thrust engine inop and uses no rudder trim. |
| NM-01 | PNF-2 | 3 | engine cut at VR | Not mentally prepared for T.O. |
| NM-03 | PNF-2 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | See Questionnaire #2 concerning Throttle usage on Approach + Landing [P.F. controls speed using inboard throttles only, leaves outboard at approach power after landing, through landing roll]. |
| NM-06 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Cver controling [sic] all phases |
| NM-07 | PNF-2 | 3 | engine cut at V1 | P.F. tends to use minimum rudder trim |
| NM-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Normal technique with better than average precision. |
| NM-14 | PNF-1 | 3 | engine-out straight-in approach/landing | Seemed average except did not use rudder trim. |
| NM-16 | PNF-2 | 3 | engine cut at VR | Seem to over react to motion after lunch |
| NM-17 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF scan is slow |
| NM-17 | PNF-1 | 3 | engine cut at VR | Believe wrong rudder applied initially and took a long time to recover. |
| NM-20 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | In all mavn. [maneuvers] P.F. tended to overcontrol due to full motion. |
| NM-21 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | PF slightly overcontroled [sic] while getting feel with motion on. |
| M-03 | PNF-1 | 4 | engine cut at VR; engine-out straight-in approach/landing | Strategy and technique involved overcorrecting indicating pilot was behind the aircraft during VR cut and straight in approach. |
| M-06 | PNF-1 | 4 | engine cut at VR | Initial use of wrong rudder. |
| M-11 | PNF-1 | 4 | engine cut at V1; engine cut at VR | Speed control will seem high as PF cleaned up airplane starting acceleration at 800' AGL. |
| M-18 | PNF-2 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | See previous comments. [PF flew this session without using rudder trim therefore tended to slightly overcontrol.] |
| M-19 | PNF-1 | 4 | engine-out sidestep landing | Seemed to anticipate wind shear & compensated more aggressively than one would expect in a real situation. |
| M-20 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | see previous comments [PF flys [sic] with split throttle thrust engine inop and uses no rudder trim.] |
| NM-02 | PNF-1 | 4 | engine cut at V1 | Same strategy - Well done. |
| NM-03 | PNF-2 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | see Quest. #2 [P.F. controls speed using inboard throttles only, leaves outboard at approach power after landing, through landing roll] |
| NM-06 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Still over controls |
| NM-07 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. used minimum rudder trim while flying. |
| NM-11 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Normal technique/strategy, better than average precision. |
| NM-14 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | Only small thing - Uses very little rudder trim with No. one engine shut down but a normal amount with No. four. |
| NM-21 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | P.F. hurried flt and tended to overcontrol, jerky flt controls to do so. |

PNF COMMENTS ON PF’S WORKLOAD

| PF | PNF | Questionnaire | Comment |
| --- | --- | --- | --- |
| M-06 | PNF-1 | 1 | On last approach -(sidestep)-had quite a bit more rudder trim than necessary which increased his workload. |
| M-07 | PNF-1 | 1 | Seemed a bit higher than average with rudder inputs. Not enough rudder at first, then over-did trim. |
| M-08 | PNF-1 | 1 | A bit higher than normal as instrument scan is a bit slow on some manuvers [sic]. |
| M-10 | PNF-1 | 1 | Seemed a bit behind the airplane - Overcontrol in the begining [sic] - this improved on second takeoff/approach. |
| M-15 | PNF-1 | 1 | seemed a bit behind the aircraft with rudder inputs requiring more work with ailerons. |
| M-16 | PNF-1 | 1 | At this point, seems to be using larger than normal control inputs to achieve LOC/GS alignment. |
| M-19 | PNF-1 | 1 | Good basic flying skills and instrument scan. Makes the job look easy. |
| NM-02 | PNF-1 | 1 | Good Cross Check |
| NM-03 | PNF-2 | 1 | PF has flown siml. quite a lot. Is an instructor. I think. |
| NM-05 | PNF-1 | 1 | Approaches better or looked easier than average - good cross check. |
| NM-11 | PNF-1 | 1 | Good instrument scan allows PF to make approaches seem easy. |
| NM-15 | PNF-2 | 1 | Workload only slightly higher due to PF becoming accustom [sic] to slight differences in data display (ie Flt Dir). |
| NM-19 | PNF-1 | 1 | Good basic skills & instrument scan - makes the job look easy, particularly on raw data approaches. |
| M-03 | PNF-1 | 2 | Experienced pilot ahead of the airplane so he doesn’t seem to work too hard. |
| M-04 | PNF-2 | 2 | P.F. appeared to begin to tire near end of secession [sic] |
| M-06 | PNF-1 | 2 | Good scan allowed him to seem like he was not working too hard. |
| M-08 | PNF-1 | 2 | Slow instrument scan makes him seem to work a bit harder than average. |
| M-10 | PNF-1 | 2 | Control inputs could be a bit smoother at times but generally average. |
| M-11 | PNF-1 | 2 | Slightly higher applies to engine cuts, on approaches, workload was lower was lower [sic] than average. |
| M-12 | PNF-2 | 2 | Workload increased in latter part on session due to fatigue setting in. |
| M-13 | PNF-2 | 2 | see previous comment [PF has good x scan] |
| M-15 | PNF-1 | 2 | Improved rudder control over first period. |
| M-16 | PNF-1 | 2 | A lot more control input, particularly in pitch, on approaches. |
| M-17 | PNF-1 | 2 | PF is ahead of the aircraft with good basic skills and instrument scan. Makes the job look easy. |
| M-19 | PNF-1 | 2 | Good scan, makes the job look easy. |
| NM-02 | PNF-1 | 2 | Good instrument cross check allowed him to be ahead of the aircraft. |
| NM-05 | PNF-1 | 2 | Average during training maneuvers. |
| NM-11 | PNF-1 | 2 | Good instrument scan & trimming allows PF to make things look easy. |
| NM-13 | PNF-1 | 2 | Good basic skills & scan make job look easier. |
| NM-14 | PNF-1 | 2 | Seems not to have to work to [sic] hard, particularly on approaches. Seems to be ahead of the aircraft due to good basic skills & instrument scan. |
| NM-16 | PNF-2 | 2 | See previous comments |
| NM-17 | PNF-1 | 2 | Scan is a little slow at times so PF has to work a bit harder to catch up. |
| NM-18 | PNF-1 | 2 | PF is ahead of aircraft - good instrument scan. |
| NM-19 | PNF-1 | 2 | PF ahead of the aircraft, makes the job seem easy. |
| NM-21 | PNF-2 | 2 | PF is simul instructor. |
| M-03 | PNF-1 | 3 | Higher physical workload due to being behind the airplane. |
| M-06 | PNF-1 | 3 | Work load on the first circuit was higher. Second was average, learned from first attempt. |
| M-07 | PNF-1 | 3 | same as average except on Vr cut - Late rudder application created more work |
| M-08 | PNF-1 | 3 | Slower than average instrument scan causes increased workload. |
| M-10 | PNF-1 | 3 | A little rough at times. |
| M-11 | PNF-1 | 3 | On approaches seems to make them look a bit easier than average due to good scan. |
| M-16 | PNF-1 | 3 | This is improving but still using large pitch inputs on short final. |
| M-17 | PNF-1 | 3 | Pilot has good, basic skills is ahead of the airplane making job look easy. |
| M-19 | PNF-1 | 3 | Above average skills, makes job look easy. |
| NM-02 | PNF-1 | 3 | Still the pilot has a good instrument cross check which puts him ahead of the aircraft & seems to be less workload. |
| NM-05 | PNF-1 | 3 | Good instrument cross check allows pilot to be ahead of the airplane. This makes for less apparent work load. |
| NM-08 | PNF-1 | 3 | Pilot seems ahead of the simulator, probably better than average instrument scan. |
| NM-11 | PNF-1 | 3 | Good basic skills allow PF to make operation look easy in all phases. |
| NM-13 | PNF-1 | 3 | Good basic skills - Job appears to be done with less work. Pilot well "ahead" of the aircraft. |
| NM-14 | PNF-1 | 3 | PF seems to be oscillating in roll control. In part this seemed to be due to not using rudder trim on first approach. On second approach used rudder trim but oscillation did not go away fully, but improved. |
| NM-17 | PNF-1 | 3 | Scan is slow. Speed control on approaches is lacking. Overall, PF is behind the aircraft & working hard to catch up. |
| NM-18 | PNF-1 | 3 | PF ahead of the aircraft due to a good instrument scan. |
| NM-19 | PNF-1 | 3 | Lower than average workload on the whole except for the first take off (VR Cut). |
| M-03 | PNF-1 | 4 | At times higher workload as pilot overcorrected and got behind the aircraft. |
| M-06 | PNF-1 | 4 | About average but worked rudder a bit more than normal, particularly in turns. |
| M-07 | PNF-1 | 4 | Approach work load a bit better than average. |
| M-08 | PNF-1 | 4 | Instrument scan improved sufficiently to be about average. |
| M-10 | PNF-1 | 4 | Was a bit rough at times, but average. |
| M-11 | PNF-1 | 4 | A little higher workload on takeoffs & lower on approaches. |
| M-12 | PNF-2 | 4 | see previous comment [PF I think was somewhat tired due to more raw data flying than normal.] |
| M-14 | PNF-2 | 4 | PF maybe tired (jet lag). |
| M-15 | PNF-1 | 4 | Good basic skills/ instrument helps PF stay ahead. |
| M-17 | PNF-1 | 4 | As before, the job looked easy due to good basic skills. |
| M-19 | PNF-1 | 4 | PF was ahead of the aircraft making the job look easy. |
| NM-02 | PNF-1 | 4 | Lower due better than average level of proficiency. |
| NM-05 | PNF-1 | 4 | Pilot didn’t seem to have to work as hard as average to achieve improvement on approaches. About average though on engine cuts. |
| NM-08 | PNF-1 | 4 | Good scan keeps him ahead of simulator and makes flying look easy. |
| NM-11 | PNF-1 | 4 | As before, good basic skills allow PF to make the job look easy. |
| NM-13 | PNF-1 | 4 | Did not appear to work as hard as some, good basic skills generally out "ahead" of the airplane. |
| NM-14 | PNF-1 | 4 | Now seems to be lower workload - PF seems to have better "feel" of aircraft in roll. |
| NM-17 | PNF-1 | 4 | Slower than average instrument scan makes work for PF. |
| NM-18 | PNF-1 | 4 | Good basic skills and instrument scan - makes it look easy. |
| NM-19 | PNF-1 | 4 | PF's good scan helped him stay ahead of the sim. Makes for lighter workload. |
| NM-21 | PNF-2 | 4 | See previous. [PF hurried flt and tended to overcontrol. Jerky flight controls to do so.] |

PNF COMMENTS ON PF’S GAINING PROFICIENCY

| PF | PNF | Questionnaire | Maneuver | Comment |
| --- | --- | --- | --- | --- |
| M-03 | PNF-1 | 2 | engine-out sidestep landing | Very experienced. Above [ratings] is based on that. |
| M-06 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Seems to have better than average instrument cross check. |
| M-07 | PNF-1 | 2 | engine cut at VR; overall gain of proficiency | Wrong rudder on 2nd VR Cut. Overall gain average harder on average based on VR cuts |
| M-08 | PNF-1 | 2 | engine cut at V1 | Gained proficiency as average except V1 cut which was much better improvement. |
| M-09 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Gained proficiency slightly easier, scan pattern increased. |
| M-10 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Big improvement over first attempt. Seems to have good instrument scan. |
| M-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing | Seems to have a bit more problem with rudder control on engine failures on take off. Instrumt [sic] scan on approaches is better than average. Above average approaches & landings. |
| M-12 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. began to get tired during last half of session. |
| M-13 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good x [cross] scan. |
| M-14 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good understanding of flight director use. I think PF became tired during final sequence & slightly overcontrol loc intercept, but a good job. |
| M-15 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying ability (instrument scan) allowed for above average improvement. |
| M-16 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has trouble with raw data approaches. Did not seem to be aware of wind direction/ velocity read-out on ND. |
| M-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good scan and basic skills. One straight-in approach did not go too well but others were good. |
| M-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with good basic skills & scan to build on. |
| NM-02 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check, particularly for getting as little flying as he does. |
| NM-05 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Average for experienced pilot. |
| NM-06 | PNF-2 | 2 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | PF slow to increase scan pattern, therefore overcorrected & chased information. |
| NM-08 | PNF-1 | 2 | engine-out straight-in approach/landing; engine-out sidestep landing | Approach speeds are high without correction. |
| NM-10 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is a current sim instructor. |
| NM-11 | PNF-1 | 2 | engine cut at V1; engine cut at VR | Gain in proficiency on engine cuts came as much from explaining/understanding F/D & what it commands for speed as flight practice. Good improvement in heading control with practice.(engine cuts) |
| NM-13 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good instrument scan & good basic skills. |
| NM-14 | PNF-1 | 2 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall gain in proficiency. Crashed on 1st V1 cut. But got to average level after that. All approaches became above average, except last straight in approach. |
| NM-15 | PNF-2 | 2 | engine-out straight-in approach/landing | On ILS P.F. slightly slow on wind change on appch. |
| NM-16 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF has good scan pattern. |
| NM-17 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | On one VR cut simulator seemed to turn left for no apparent reason, before engine failure, sim was frozen, all others normal. |
| NM-18 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills and instrument scas [sic]. |
| NM-19 | PNF-1 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with, allowed good gain in prof. particularly with engine failures. |
| NM-21 | PNF-2 | 2 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF is an instructor in simul. |
| M-03 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Coming back after lunch seems to be hard. Seems to take time to get back up to speed. |
| M-06 | PNF-1 | 3 | engine cut at VR; engine-out straight-in approach/landing | In first engine cut and approach (VR & straight in) gain in proficiency was a bit below normal. Second circuit was average. |
| M-07 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Take offs about the same as start - (Approaches/Landings better) Used correct rudder inputs but a bit late. |
| M-08 | PNF-1 | 3 | engine cut at V1 | Regressed on Engine Failure at V1. |
| M-10 | PNF-1 | 3 | engine cut at V1; engine cut at VR; | First after lunch, heading control on take offs with engine failures not as good as practice session - approaches were average |
| M-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good improvement in engine cuts. Continues to improve approaches. |
| M-12 | PNF-2 | 3 | engine-out straight-in approach/landing | PF slightly over controlled pitch on raw data ILS (after lunch). |
| M-14 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF seems to be a little tired, possible jet lag. |
| M-15 | PNF-1 | 3 | engine cut at VR | Engine cut at VR seemed to be a bit of a surprise. |
| M-16 | PNF-1 | 3 | engine-out straight-in approach/landing; overall gain of proficiency | Straight in approach is getting better but would still be a go around under normal conditions. |
| M-17 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good inst. scan & basic abilities. |
| M-18 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF had slight lunch break letdown. |
| M-19 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF started with above average skills. |
| M-20 | PNF-2 | 3 | engine-out straight-in approach/landing | PF had slight let down on ILS approach (lunch). |
| NM-02 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skill in the begining [sic]. |
| NM-05 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has good cross check & is a bit further ahead of the aircraft than average. |
| NM-06 | PNF-2 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Proficiency increaced [sic] at a normal rate from proficiency during training phase. |
| NM-08 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good overall improvement. |
| NM-11 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Has gained proficiency easier than average - better than average basic skills. |
| NM-13 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Improvement after the break better than average. Good basic flying skills & scan. |
| NM-14 | PNF-1 | 3 | engine-out straight-in approach/landing; engine-out sidestep landing | Engine failures acceptable, approaches good - PF seems to have good instrument scan. |
| NM-16 | PNF-2 | 3 | engine cut at VR | P.F. seem to over react to motion on VR cut. Improved quickly. |
| NM-17 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Engine cut at V1 was better than VR cut. VR cut was almost crash. Not having motion washed out took PF by surprise. Speed on straight in approach was about 20 kts high--Side step approach was almost normal with speed about 10 kts high. Also on VR engine cut, believe PF initially applied wrong rudder |
| NM-18 | PNF-1 | 3 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills & scan. |
| NM-19 | PNF-1 | 3 | engine cut at V1; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | VR cut was first take off - after that, PF got the "feel" of simulator somewhat better. |
| M-03 | PNF-1 | 4 | engine cut at VR; engine-out straight-in approach/landing; overall gain of proficiency | Seemed to do better in the morning. |
| M-06 | PNF-1 | 4 | engine cut at VR | Engine cut at Vr made harder by use of wrong rudder at engine failure. After recovery, average performance. |
| M-07 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | Takeoffs average this time. Approaches above average. |
| M-09 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. has good scan & flying background. |
| M-11 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing | V1/ VR Cuts improved as average. Approaches improved better than average due good instrument scan. |
| M-12 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was somewhat tired due to more raw data flying than normal. |
| M-13 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF may have become a little bored or tired during last two sessions. |
| M-14 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF I think was tired. (jet lag?) |
| M-18 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | PF flew this session without using rudder trim therefore tended to slightly overcontrol. |
| M-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Above average skills starting. |
| NM-02 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Pilot started from good level of proficiency. Gained proficiency as instrument flying basics were already good. |
| NM-05 | PNF-1 | 4 | engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | As before, good basic instrument cross-check makes improvement easier. |
| NM-08 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good gain in proficiency. Good basic flying ability - good scan. |
| NM-11 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic flying skills allowing better than average progress. |
| NM-13 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out sidestep landing; overall gain of proficiency | Good basic skills, & instrument scan. Backslid a little on straight in approach as speed got a little low. |
| NM-14 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Oscilation [sic] in roll much improved from previous. Seems to have good basic skills & be ahead of the aircraft. |
| NM-15 | PNF-2 | 4 | engine cut at V1; engine cut at VR | P.F. tends to allow a/c to drift off LOC/G.S. after visual contact with-out FLT DIR. |
| NM-16 | PNF-2 | 4 | engine cut at VR | P.F. still over controls on VR cut. |
| NM-17 | PNF-1 | 4 | engine-out sidestep landing | Speed control on straight-in landing was about the only problem this time. |
| NM-18 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good basic skills better than average instrument scan. |
| NM-19 | PNF-1 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | Good scan and skills to start with. |
| NM-20 | PNF-2 | 4 | engine-out straight-in approach/landing; | PF overcontrol with full motion |
| NM-21 | PNF-2 | 4 | engine cut at V1; engine cut at VR; engine-out straight-in approach/landing; engine-out sidestep landing; overall gain of proficiency | P.F. is siml [simulator] instru [instructor]. teh |

# Footnotes

Preliminary results of this study have been published in Bürki-Cohen, Go, Chung, Schroeder, Jacobs, and Longridge (2003) and Go, Bürki- Cohen, Chung, Schroeder, Saillant, Jacobs, and Longridge (2003)

Please note that in the questionnaires, the V2 cut was described as a VR cut.

Although wheel reaction time was not included in these analyses, earlier analyses had not found any differences in wheel reaction times between the two groups for Evaluation (F(1,35)=1.45, p=.237) or Quasi-Transfer Testing (F(1,32)=.07, p=.803) (see Bürki-Cohen et al., 2001).

Note that the scales from 1 to 7 in the questionnaires, where 4 was labeled as equivalent to the airplane, were transformed to scales from –3 to +3 with 0 meaning equivalent to the airplane.

Unlike in Second Study, the number of training runs was not equal among the pilots in the First Study as they needed only to reach the company standard (I/E grade of 3) to end the training. Comparisons for improvement were therefore done differently than in the Second Study.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

Note that pilot NM-09 was excluded from all analyses because it was discovered only after his participation that he was not currently qualified on the B747-400 airplane. He was replaced by NM-21.

# Text boxes

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

ILS/DME Rwy 36L  354º    111.9      IBXN

ILS           Rwy 36R  354º    110.55    IFJN

DFW Twr 			124.15

REGIONAL  DEP		118.55

REGIONAL APP		118.42

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

ILS/DME Rwy 36L  354º    111.9      IBXN

ILS           Rwy 36R  354º    110.55    IFJN

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

ILS/DME Rwy 36L  354º    111.9      IBXN

ILS           Rwy 36R  354º    110.55    IFJN

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

DFW Twr 			124.15

REGIONAL DEP		118.55

REGIONAL APP		118.42

ILS/DME Rwy 36L  354º    111.9      IBXN

ILS           Rwy 36R  354º    110.55    IFJN