Preservation Note 8

Accessibility for Disabled Persons: Building Hardware

Doors and Windows

August-91

Special Function Hardware-08780

--------------------------------------------------------------------------------

Include the following guidelines in all scopes of work for design projects involving handicapped accessibility to elevator, fire alarm, or other hardware mounted in stone, unpainted wood, unpainted metal, or other ornamental wall finishes:

--------------------------------------------------------------------------------

V. Special Considerations

Protection of Ornamental Materials: Special care shall be taken to avoid penetration into stone, unpainted wood, unpainted metal, ceramic materials, ornamental plaster, decorative painting, and other ornamental finishes. Use the following rules of thumb for the placement of hardware in ornamental wall finishes:

1. If the existing hardware is located within 54 inches from the floor, for side reach accessibility, and within 49 inches from the floor, for front reach accessibility,* retain the existing hardware in place. If new hardware is required, install it in place of the existing hardware to avoid cutting a new hole in the wall. Specify new hardware finishes matching the original hardware. Consult the Regional Historic Preservation Officer to determine if salvaging the original hardware is required.

Notify the Regional Historic Preservation Officer in writing if retaining existing hardware in place will require a waiver from the handicapped access code. State the code requirement and the allowance (inches from required height) needed to reuse the existing hardware. The preservation staff member reviewing the project will prepare the waiver request for submission to the GSA Administrator.

2. If the existing hardware is located above 54 inches from the floor, for side reach accessibility, or above 49 inches from the floor, for front reach accessibility, retain the existing hardware in place. Cut the wall the minimum extent necessary to install new, handicapped accessible hardware separately. Install the new hardware (matching original hardware's finish) at a location five to ten feet away from the existing hardware. When this is not possible, align new and old hardware vertically.

Do not install new and old hardware together on an enlarged backplate. Do not remove old hardware and cover hole with an enlarged backplate. The intent is to minimize cutting into the ornamental wall material."

*Based on wheelchair maneuverability at the hardware location (function of corridor width, etc.)