TYPICAL SPENT FUEL TRANSPORTATION CASKS

Generic Truck Cask for Spent Fuel

Typical Specifications

Gross Weight (including fuel):  50,000 pounds (25 tons)

Cask Diameter:  4 feet

Overall Diameter (including Impact Limiters):  6 feet

Overall Length (including Impact Limiters):  20 feet

Capacity:  Up to 4 PWR or 9 BWR fuel assemblies

Generic Rail Cask for Spent Fuel

Typical Specifications

Gross Weight (including fuel):  250,000 pounds (125 tons)

Cask Diameter:  8 feet

Overall Diameter (including Impact Limiters): 11 feet

Overall Length (including Impact Limiters):  25 feet

Capacity: Up to 26 PWR or 61 BWR fuel assemblies