## Slide 1
Reduced Vertical Separation Minimum (RVSM) Monitoring Requirements
U.S. Domestic Implementation
Federal Aviation
Administration
Date: April 25, 2011
Notes: Good Day and Welcome to the presentation on the US Reduced Vertical Separation Minimum, or RVSM, Monitoring Program. This presentation will cover the US Domestic Implementation of RVSM Monitoring Requirements. This briefing has been developed to provide an overview or refresher on the Initial and Continuing Monitoring Requirements for RVSM. RVSM was implemented in US Domestic Airspace from Flight Level 290 to Flight Level 410, inclusive, in 2005. Let's get started with the presentation.

## Slide 2: Presentation Outline
RVSM Monitoring
Changes to RVSM Monitoring Standards
Current and revised FAA Policy
Effective Date
Monitoring Requirements
1
RVSM Minimum Monitoring Requirements
North American Approvals Registry and Monitoring Organization (NAARMO)
RVSM Approvals Database
Frequently Asked Questions
Monitoring Program
2
References
Points of Contact
Useful Web Links
Regional Monitoring Agencies
GMU/GMS Monitoring Procedures
AGHME Monitoring Procedures
Other Monitoring Procedures
FAA Monitoring Process
General Information
3
Notes: This presentation will consist of a brief review of the RVSM Monitoring Requirements, changes to RVSM Monitoring Standards, current FAA Policy on Monitoring, the Revised FAA Policy, the effective date associated with implementation of the revised policy, Minimum Monitoring Standards, what the NAARMO is and how it operates, the RVSM Approvals Data Base, operator options for monitoring, and Frequently Asked Questions with regard to monitoring. Additional information sources will also be reviewed at the conclusion of the presentation.

## Slide 3
RVSM System Performance Monitoring was implemented in conjunction with the establishment of RVSM Airspace to ensure that the implementation and continued operation of RVSM meets safety objectives.
Monitoring of Height-Keeping Performance is an integral part of global RVSM safety and is implemented on a regional basis
In accordance with International standards and State regulations all RVSM operators will participate in a monitoring program
Reduced Vertical Separation Minimum (RVSM) Monitoring
>
>
>
Notes: RVSM System Performance Monitoring was implemented in conjunction with the establishment of RVSM Airspace to ensure that the implementation and continued operation of RVSM meets safety objectives. Monitoring of Height-Keeping Performance is an integral part of global RVSM safety and is implemented on a regional basis. In accordance with International standards and State regulations all RVSM operators will participate in a monitoring program.

## Slide 4: Changes to RVSM Monitoring Standards
18 November 2010, ICAO change to Annex 6, Operation of Aircraft, Parts I & II, became applicable:
  Operators, that have been issued an U.S. RVSM approval, shall ensure that a minimum of two airplanes of each [RVSM] aircraft type grouping of the operator have their height-keeping performance monitored, at least once every two years or within intervals of 1,000 flight hours per airplane, whichever period is longer. If an operator aircraft type grouping consists of a single airplane, monitoring of that airplane shall be accomplished within the specified period
The Federal Aviation Administration will implement the standard above for RVSM Monitoring
ICAO Annex 6 Revision
Notes: On November 18, 2010, changes to ICAO Annex 6 Parts I and II, with regard to RVSM monitoring became applicable. Operators, that have been issued a US RVSM approval, shall ensure that a minimum of 2 airplanes of each RVSM aircraft type grouping of the operator have their height-keeping performance monitored, at least once every 2 years or within intervals of 1,000 flight hours per airplane, whichever period is longer. If an operator aircraft type grouping consists of a single airplane, monitoring of that airplane shall be accomplished within the specified period. The FAA will implement the ICAO standard for RVSM monitoring.

## Slide 5: Current and Revised FAA Policy
All U.S. Operators wishing to operate in RVSM airspace shall be authorized and shall participate in a monitoring program
Initial Monitoring - Operators have up until six months after they receive RVSM Authority or until six months after the start of RVSM operations, whichever occurs later, to comply with RVSM monitoring requirements and
Continuing Requirement - Operators that have been issued an U.S. RVSM authorization will be required to conduct monitoring every two years or within intervals of 1,000 flight hours per aircraft, whichever period is longer
The minimum number of aircraft in an operator’s fleet that must be monitored is established on an RVSM aircraft category basis and requirements can be found in the regional minimum monitoring tables maintained (in North America) by the North American Approvals Registry and monitoring Organization (NAARMO)
Revised FAA Policy
All U.S. Operators wishing to operate in RVSM airspace shall be authorized and shall participate in a monitoring program
Initial Requirement - Operators have up until six months after they receive RVSM Authority or until six months after the start of RVSM operations, whichever occurs later, to comply with RVSM monitoring requirements
The minimum number of aircraft in an operator’s fleet that must be monitored is established on an RVSM aircraft category basis and requirements can be found in the regional minimum monitoring tables maintained (in North America) by the North American Approvals Registry and monitoring Organization (NAARMO)
2
Current FAA Policy
1
Notes: The current FAA Policy is outlined in the left column of the slide. All U.S. Operators wishing to operate in RVSM airspace shall be authorized and shall participate in a monitoring program. Operators have up until six months after they receive RVSM Authority or until six months after the start of RVSM operations, whichever occurs later, to comply with RVSM monitoring requirements. The minimum number of aircraft in an operators fleet that must be monitored is:
1) Established on an RVSM aircraft category basis and
2) Requirements for this minimum number can be found in the regional minimum monitoring tables maintained by the North American Approvals Registry and Monitoring Organization (NAARMO).
The Revised FAA Policy, outlined in the right column of the slide, includes a continuing requirement for monitoring. The Continuing Requirement is as follows: Operators that have been issued an U.S. RVSM authorization will be required to conduct monitoring every two years or within intervals of 1,000 flight hours per aircraft, whichever period is longer.

## Slide 6: Effective Date
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
2010
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
2012
2011
The new ICAO Standards became effective
18 November 2010
Current FAA Policy
The FAA will revise the RVSM Monitoring Policy applicable on 18 May 2011
Current FAA Policy
Operators will have until 18 November 2012 to comply
Current FAA Policy
Notes: The new ICAO standards became effective November 18, 2010. The FAA will revise the monitoring policy applicable on May 18, 2011. Operators will have until November 18, 2012 to comply with the requirement.

## Slide 7: RVSM Monitoring Requirements
Table 1 from the (North American) RVSM Minimum Monitoring Requirements Chart establishes the minimum number of airframes from each fleet of an operator to be monitored. This table will be updated when data collected indicates a need for change. The latest version of the chart can be found on the NAARMO website and also on the FAA RVSM webpage in the “Monitoring Requirements / Procedures” section.
Aircraft status for monitoring - Aircraft engineering work that is required for the aircraft to receive RVSM airworthiness approval must be completed prior to the aircraft being monitored. Any exception to this rule needs to be coordinated with FAA Flight Standards (AFS-400).
Applicability of monitoring from other regions - Monitoring data obtained in conjunction with RVSM monitoring programs from other regions can be used to meet regional monitoring requirements.
Monitoring prior to the issue of RVSM Operational approval is not a requirement - Operators should submit monitoring plans to their applicable Flight Standards District Office (FSDO), Certificate Management Office (CMO) or Certificate-Holding District Office (CHDO) to NAARMO to show how they intend to meet the requirements specified in Table1. Monitoring will be carried out in accordance with this table.
Monitoring Requirements - 1
Notes: Table 1 from the NAARMO RVSM Monitoring Requirements Chart establishes the minimum number of airframes from each fleet of an operator to be monitored. This table will be updated when data collected indicates a need for change. We will review Table 1 in a moment.
Other monitoring requirements include the following:
1. All aircraft engineering work that is required for the aircraft to receive RVSM airworthiness approval must be completed prior to monitoring.
2. Monitoring data from other Regions can be used to meet regional monitoring requirements, and finally
Monitoring PRIOR to the issue of RVSM Operational Approval is not a requirements.

## Slide 8: RVSM Monitoring Requirements
Aircraft groups not listed in table 1 - Contact NAARMO for clarification if an aircraft group is not listed in Table 1 or for clarification of other monitoring related issues. An aircraft group not listed in Table 1 will probably be subject to Category 2 or Category 3 monitoring requirements.
Table of monitoring groups - Table 2 shows the aircraft types and series that are grouped together for operator monitoring purposes.
Trailing cone data - Altimetry System Error estimations developed using Trailing Cone data collected during RVSM certification flights can be used to fulfill monitoring requirements. It must be documented, however, that aircraft RVSM systems were in the approved RVSM configuration for the flight.
Monitoring of airframes that are RVSM compliant on delivery - If an operator adds new RVSM compliant airframes of a type for which it already has RVSM operational approval and has completed monitoring requirements for the type in accordance with the attached table, the new airframes are not required to be monitored. If an operator adds new RVSM compliant airframes of an aircraft type for which it has not previously received RVSM operational approval, then the operator should complete monitoring in accordance with the attached table.
Monitoring Requirements - 2
Notes: If an aircraft type or group is not listed in Table 1, contact NAARMO for clarification. Table 2, also from the NAARMO RVSM Monitoring Requirements Chart, shows the aircraft types and series that are grouped together for monitoring purposes. We will review Tables 2 in a moment as well.
It should be noted that if an operator adds new RVSM compliant airframes of a type for which it already has RVSM operational approval, the new airframes are NOT required to be monitored.

## Slide 9: RVSM Monitoring Requirements
Monitoring Requirements - 3
MONITORING IS REQUIRED IN ACCORDANCE WITH THIS TABLE Note: Monitoring prior to the issue of RVSM approval is not a requirement |  |  | 
Category |  | Aircraft Group | Minimum Operator Monitoring For Each Aircraft Group
1 | GROUP APPROVED: INDICATES COMPLIANCE WITH THE RVSM MASPS | A124, A300, A306, A310-GE, A310-PW, A318, A320, A330, A340, A345, A346, A3ST, AVRO, B712, B727, B737CL, B737C, B737NX, B747CL, B74S, B744-5, B744-10, B752, B753, B767, B764, B772, B773, BD100, CL600, CL604, CL605, C17, C525, C560, C56X, C650, C680, C750, CARJ, CRJ7, CRJ9, DC10, E135-145, E170-190, F100, F900, FA10, GALX, GLEX, GLF4, GLF5, H25B-800, J328, KC135, LJ40, LJ45, LJ60, MD10, MD11, MD80, MD90, 1, T154 | Two airframes from each fleet of an operator to be monitored
2 | GROUP APPROVED: INSUFFICIENT ON APPROVED AIRCRAFT | Other group aircraft other than those listed above including: A148, A380, AC95, AN72, ASTR, ASTR-SPX, B701, B703, B703-E3, B731, B732, BD700, BE20, BE30, BE40, B744-LCF, B748, C130, C500, C25A, C25B, C25C, C441, C5, C510, C550-552, C550-B, C550-II, C550-, D328, DC85, DC86-87, DC93, DC95, E120, E50P, EA50, F2TH, F70, FA20, FA50, FA7X, G150, GLF2, GLF2B, GLF3, H25B-700, H25B-750, H25C, HA4T, IL62, IL76, IL86, IL96, L101, L29B-2, L29B-731, LJ31, LJ35-36, LJ55, MU30, P180, PC12, SB20, 1, 2, T134, T204, T334, TBM, WW24, YK42 | 60% of airframes (round up if fractional) from each fleet of an operator or individual monitoring
3 | Non-Group | Non-group approved aircraft | 100% of aircraft shall be monitored
Table 1: Monitoring Requirements Table
Notes: Table 1 from the NAARMO Minimum Monitoring Requirements Chart is presented here and establishes the minimum number of airframes from each fleet of an operator that must be monitored. There are 3 Categories for Monitoring. Category 1) Group approved indicates compliance with the RVSM MASPS, Category 2) Group Approved with insufficient data on approved aircraft, and Category 3) Non-group approved aircraft. The latest version of the chart can be found on the NAARMO website and the FAA RVSM website.

## Slide 10: RVSM Monitoring Requirements
Monitoring Requirements - 4
Example from Table 2: Monitoring groups for aircraft certified under group approval requirements
Monitoring Group | A/C ICAO | A/C Type | A/C Series
A124 | A124 | AN-124 RUSLAN | ALL SERIES
A148 | A148 | AN-148 | 100
A300 | A30B | A300 | B2-100, B2-200, B4-100, B4-100F, B4-120, B4-200, B4-200F, B4-220, B4-220F, C4-200
A306 | A306 | A300 | 600, 600F, 600R, 620, 620R, 620RF
A310-GE | A310 | A310 | 200, 200F, 300, 300F
A310-PW | A310 | A310 | 220, 220F,320
A318 | A318 | A318 | ALL SERIES
A320 | A319 A320 A321 | A319 A320 A321 | CJ , 110, 130 110, 210, 230 110, 130, 210, 230
A330 | A332 A333 | A330 A330 | 200, 220, 240 300, 320, 340
A340 | A342 A343 | A340 A340 | 210 310
A345 | A345 | A340 | 500, 540
A346 | A346 | A340 | 600, 640
A380 | A388 | A380 | 800, 840, 860
A3ST | A3ST | A300 | 600R ST BELUGA
Notes: For RVSM, a monitoring group is considered to be a group of aircraft that have similar height-keeping characteristics. This can be an aircraft type or a series of aircraft within an aircraft type. For example, the Airbus 310 with GE engines is defined as a monitoring group, and within this group are the 200, 200F, 300, and 300F series within that aircraft type. In contrast the A318 contains all series for that model or aircraft type.

## Slide 11: North American Approvals Registry and Monitoring Organization
Regional Monitoring Agencies (RMAs) were established to support implementation and continued safe use of RVSM airspace
Through bi-lateral agreements with Canada and Mexico, the FAA has established the North American Approvals Registry and Monitoring Organization (NAARMO)
Resides at FAA William J. Hughes Technical Center managed by the Separations Analysis Team (AJP-7B1)
Background
Functions
Functions of NAARMO Include:
  Continuous monitoring for RVSM aircraft height keeping performance
  Development and maintenance of North American RVSM Approvals Data Base
  Scrutiny of RVSM approval status and aircraft using North American RVSM airspace
  Coordination with the International Civil Aviation Organization (ICAO) and other RMAs in regards to the minimum monitoring requirements
Notes: Regional Monitoring Agencies, or RMAs, were established to support RVSM implementation and continued safe use of RVSM. Through bi-lateral agreements with Canada and Mexico, the United States established the NAARMO. Again, NAARMO stands for the North American Approvals Registry and Monitoring Organization. The NAARMO resides at the FAA William J Hughes Technical Center and is managed by the Separations Standards Analysis Team.
Key functions of the NAARMO are:
1. Continuous monitoring for RVSM aircraft height keeping performance
Development and maintenance of the North American RVSM Approvals Data Base
Scrutiny of RVSM approval status
Coordination with ICAO and other RMAs about minimum monitoring requirements

## Slide 12: US RVSM Approvals Database
NAARMO manages the U.S. RVSM Approvals Data Base
An Operator with a Valid US RVSM Authorization is authorized to fly in any RVSM airspace in the world
Operators can view status of RVSM approvals and last valid monitoring date
NAARMO shares data with other RMAs
The abridged version of the approval data base can be found on the NAARMO website or linked from the FAA RVSM Webpage Note: If your aircraft does not appear in the database, it is not an indication of an unsuccessful AGHME monitoring. Please contact NAARMO for further assistance.
Monitoring Requirements - 2
Notes: The NAARMO manages the United States RVSM Approvals data base. An Operator with a valid US RVSM Authorization is authorized to fly in any RVSM airspace in the world. Operators can view the status of RVSM approvals and the last valid monitoring date on the NAARMO website or the FAA RVSM webpage. It should be noted that if your aircraft does not appear in the database, it is not an indication of an unsuccessful monitoring attempt. If this occurs contact NAARMO for further assistance.

## Slide 13
GMS-based Monitoring Unit
Operators can choose to fly with a portable GPS-based Monitoring Unit (GMU) on their aircraft .
AGHME
In North America operators may choose to fly over one of the ground-based height monitoring units in the Aircraft Geometric Height Measurement Element (AGHME) constellation
Ground-based Height Monitoring Units (HMUs)
Operators may choose to fly over other ground-based height monitoring units outside of North America (Europe, Strumble)
>
>
>
Options for Participating in Monitoring Programs
Note: For international operators, the selected monitoring method should be approved by their respective State authority.
Notes: There are 3 options for operators to participate in the monitoring program.
They are:
-1) Arrange to have the portable GPS-based monitoring unit, or GMU, on board for a monitoring flight
-2) Fly over one of the ground based Aircraft Geometric Height Measurement Elements, or AGHMEs in North America, or
-3) Fly over other ground based height monitoring units or HMUs outside North America

## Slide 14
Question: Documents and Guidance - Where can documents explaining monitoring systems, operator requirements and procedures be found?
All of the documents referred to in this list of Monitoring FAQ’s are posted on the RVSM Documentation Webpage in the “Monitoring Requirements and Procedures” section.
Q:
Frequently Asked Questions
Question: Number of Aircraft to be Monitored - How many aircraft from an operator’s fleet are required to be monitored?
In general, operators are only required to have a portion of their fleets monitored. Monitoring requirements are published in the North American Minimum Monitoring Requirements Charts posted under “Monitoring Requirements and Procedures”.
Q:
Question: Monitoring Groups - What are monitoring groups and where are they listed?
Monitoring groups are listed on the Minimum Monitoring Requirements charts. For monitoring purposes, aircraft types can be placed in a single monitoring group. For example, the A319, A320 and A321 are categorized as a single monitoring group.
Q:
Question: 1000 hour Requirement - If I fly my RVSM approved aircraft less than 1000 flight hours in 2 years. Am I required to have it monitored within the 2 year period.
No. The policy states that aircraft will be monitored every two years or 1000 flight hours, whichever is longer. However, if your aircraft has not had a valid monitoring in the last 2 years you may be contacted by your local Flight Standards District Office and asked to provide data that shows you have flown less than 1000 hours in the 2-year period.
Q:
Notes: A number of frequently asked questions are reviewed on the next 2 slides with regard to RVSM Monitoring. This slide addresses general RVSM monitoring questions such as where to locate documents and reference material for RVSM monitoring, how many aircraft need to be monitored, monitoring groups, and the how the 1000 hour requirement is implemented. The questions will be updated as received and posted to the RVSM website.

## Slide 15
Question: MMR Chart - If I purchase an aircraft of the same model and type series, for which I already hold a valid RVSM authorization, does it have to be monitored?
It depends. NOTE 9 of the RVSM MMR Chart states: If an operator adds new RVSM compliant airframes of a type for which it already has RVSM operational approval and has completed monitoring requirements for the type in accordance with the attached table, the new airframes are not required to be monitored. If an operator adds new RVSM compliant airframes of an aircraft type for which it has NOT previously received RVSM operational approval, then the operator should complete monitoring in accordance with the attached table.
Example 1 - You own a fleet of three Gulfstream 5’s (GLF5) that have a valid monitoring in the last two years. You purchase of a fourth Gulfstream 5, it would not require monitoring because you already meet the minimum requirement of two airframes. A GLF5 is a group approved aircraft in category 1. This is specified in Table 1 of the Minimum Monitoring Chart.
Example 2 - You own a fleet of three Gulfstream 3’s (GLF3) and 2 of the aircraft have a valid monitoring in the last two years. You purchase two more GLF3’s, At least one would require monitoring to meet the 60% requirement (3-aircraft) within 6 months. A GLF3 is a group approved aircraft in category 2. This is specified in Table 1 of the Minimum Monitoring Chart.
Note: airframes must be RVSM compliant upon delivery
Q:
Frequently Asked Questions
Question: MMR Chart - I just purchased a fleet of 4 Boeing 767’s and applied for an U.S. RVSM operational authorization. How many must be monitored and when?
In accordance with FAA Policy and Note 2 of the RVSM MMR CHART, operators must show a plan for meeting applicable monitoring requirements. Initial monitoring of two airframes (for MMR chart category 1) should be completed as soon as possible but not later than 6 months after the issue of RVSM operational authority. A minimum of two airframes (MMR chart category 1) shall have a valid monitoring every two years or 1000 flight hours whichever period is longer.
Q:
Notes: This slide reviews the Minimum Monitoring Requirements Chart. The first question and examples address operators adding to existing fleets and how to determine the minimum requirements for monitoring for a Category 1 and Category 2 aircraft group. The second question addresses an operator purchasing a new fleet of 767s. These examples along with the MMR Chart and Notes should be studied following the briefing. If a question arise with regard to the Minimum Monitoring Requirements, the NAARMO should be contacted.

## Slide 16: General Information
Notes: We will now present some general information on RVSM Monitoring including Reference Material, Points of Contact, Useful weblinks, Regional Monitoring Agencies, GMU and GMS Monitoring Procedures, AGHME Monitoring Procedures, Other Monitoring Procedures, and the FAA monitoring Process.

## Slide 17: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Useful References
14 CFR Part 91.180, Operations within airspace designated as Reduced Vertical Separation Minimum airspace
14 CFR Appendix G to Part 91, Operations in Reduced Vertical Separation Minimum airspace
14 CFR Part 91.706, Operation within airspace designed as Reduced Vertical Separation
FAA Advisory Circular (AC) 91-85, Reduced Vertical Separation Minimum (RVSM) Authorizations
ICAO ANNEX 6, Parts I and II (7.27 and 2.5.27 respectively), Operation of Aircraft
ICAO ANNEX 11, 3.3.5.1-3.3.5.2, Air Traffic Services
ICAO Document 9574, Manual on Implementation of a 300 m (1000 ft) Vertical Separation Minimum Between FL 290 and FL 410 Inclusive
Notes: Useful Reference Material that can be found on the RVSM WEBSITE include the following:
-CFR Part 91.180, 91.706 and Appendix G to Part 91 for Operations within RVSM Airspace
-FAA Advisory Circular 91-85, RVSM Authorizations
-Sections and Parts of ICAO Annex 6 and 11 that refer to RVSM Operation of Aircraft and RVSM Air Traffic Services are listed
And ICAO Document 9574, the Manual on RVSM Implementation between FL 290 and 410, inclusive

## Slide 18: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Points of Contact
Name | Organization | Telephone | Email
Madison Walton | RVSM Lead, FAA Flight Standards, AFS-470 | (202) 385-4596 | Madison.Walton@faa.gov
Trent Bigler | RVSM Regulations, FAA Flight Standards, AFS-470 | (202) 385-4504 | Trent.Bigler@faa.gov
Stephanie Beritsky | FAA Support, AJP-7B1 Separations and Standards Group, CSSI, Inc. | (609) 485-7851 | Stephanie.ctr.Beritsky@faa.gov
Stephen Smoot | FAA Support, AFS-470 Flight Standards, CSSI, Inc. | (202) 863-0865 | ssmoot@cssiinc.com
NAARMO | Operations Coordinator, FAA Technical Center | (609) 485-5678 | NAARMO@faa.gov
GMU Monitoring | CSSI, Inc. | (202) 863-2398 | Monitor@cssiinc.com
GMS Monitoring | ARINC, Inc. | (410) 573-3007 | RVSMOps@arinc.com
Notes: US RVSM Points of Contact are presented here. The program is managed by the Flight Standards Service, Flight Technology and Procedures Division at FAA Headquarters. The US RVSM Approvals Data Base and monitoring program is managed by the FAA Technical Center. CSSI is responsible for all aspects of program support at FAA Headquarters and at the FAA Technical Center. And finally contacts are provided for GMU and GMS Monitoring.

## Slide 19: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Useful Web Links
FAA RVSM Webpage: http://www.faa.gov/about/office_org/headquarters_offices/ato/service_units/enroute/rvsm/
NAARMO Webpage: http://www.faa.gov/air_traffic/separation_standards/naarmo
AGHME: http://www.faa.gov/air_traffic/separation_standards/aghme/
GMU Monitoring: monitor@cssiinc.com
GMS Monitoring: rvsmops@arinc.com
Europe RVSM: http://www.ecacnav.com/RVSM
Notes: Useful web links are listed here. These web links will provide quick and direct access to guidance and information needed during the RVSM approval and monitoring process. Links are provided for the FAA RVSM Webpage, NAARMO Webpage, AGHME site, GMU and GMS monitoring sites, and the European RVSM website.

## Slide 20: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Regional Monitoring Web Site Links
AFI Regional Monitoring Agency (ARMA): http://www.atns.co.za
Australian Airspace Monitoring Agency (AAMA): http://www.airservicesaustralia.com/organisations/aama/
Caribbean and South American Regions Monitoring Agency (CARSAMA): http://www.cgna.gov.br/CARSAMMA/siteUSA/inicial.htm
China Regional Monitoring Agency: http://www.chinarma.cn
EUROCONTROL Regional Monitoring Agency: http://www.ecacnav.com/rvsm
Monitoring Agency for Asia Region (MAAR): http://www.aerothai.co.th/maar/
Middle East Regional Monitoring Agency (MIDRMA): http://www.midrma.com/
North American Approvals Registry and Monitoring Organization (NAARMO): http://www.faa.gov/air_traffic/separation_standards/naarmo/
North Atlantic Central Monitoring Agency (NAT CMA): natcma@nats.co.uk
Pacific Approval Registry and Monitoring Organization (PARMO): http://www.faa.gov/air_traffic/separation_standards/parmo/
Notes: Contact information is provided for each of the Regional Monitoring Agencies around the world. Included are the RMAs for Africa, Australia, the Caribbean/South America or CARSAM, China, Europe, Asia, the Middle East, North America, the North Atlantic, and the Pacific.

## Slide 21: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Monitoring Process
Operator Applies for RVSM Authorization in accordance with AC 91-85
CMO, CHDO, FSDO Evaluates Application and if approved issues OpSpec, MSpec or LOA (PTRS Updated)
U.S. Operator conducts initial monitoring with in six months in accordance with FAA Policy
NAARMO updates Approval Database
RVSM airspace continuously monitored and database maintained
Operator ensures a valid monitoring flight (IAW MMR Chart) is conducted every two years or 1000 flight hours whichever is longer
Operator shows valid reason for delinquency or acceptable plan to re-establish currency
FAA Verification of two year requirement through sampling against Approvals Database
If Operator falls out of compliance the CMO, SHDO or FSDO will be notified

## Slide 22: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
GMU Monitoring Procedures for US Operators
The FAA has agreements with ARINC Inc. and CSSI Inc. under which the FAA provides these private-sector firms with GPS-based Monitoring Units, receiving in turn from them accurate aircraft geometric height estimates. It should be noted that monitoring services provided to operators are in accordance with fee schedules established by these firms
ARINC, Inc. GMS Operations: Tel +1 410-266-4707 Fax +1 410-573-3007 rvsmops@arinc.com ARINC.com
CSSI, Inc. GMU Operations Coordinator: Tel +1 202-554-1050 or 866-GMU-8111 Fax +1 202-863-2398 monitor@cssiinc.com RVSM-Monitoring.com
Contact Information:
The aircraft is determined to be RVSM-compliant. (RVSM modifications/ inspections completed, as required)
FSDO/ CMO determination of aircraft RVSM-compliance and PTRS action may occur before or after monitoring is completed. For example, an aircraft service center may complete monitoring when RVSM-compliance work is completed before the operator takes possession of the aircraft
Operator contacts GMS Support Contractor to plan monitoring flight
Operator schedules and conducts flight with GMS Support Contractor
GMS Support Contractor provides Operator with status updates for flight data
NAARMO Updates US Approvals Database to reflect results/date of monitoring flight
Operator completes monitoring application and submits to the US GMS Coordinator and appropriate GMS Support Contractor
Monitoring Flight Activity
Monitoring schedule provided by GMS support contractor
- RVSM Technician conducts GMU flight data on operator aircraft
- RVSM Technician submits post-flight FIF to WJHTC
- GPS data files are post-processed by GMS Support Contractor
- Processed data files are submitted by GMS Support Contractor to WJHTC for final ASE calculation

## Slide 23: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Cleveland
Ottawa
Wichita
Phoenix
Oregon
Lethbridge
Atlantic City
Operational
Planned
AGHME Monitoring Procedures for US Operators
Ensure that the aircraft is in RVSM approved configuration.
Obtain acceptance of an RVSM monitoring plan from the relevant State RVSM approving official.
Complete the “US Operator Application For RVSM Monitoring” posted on this page. Email the form to naarmo@faa.gov with "AGHME Monitoring Application" and the aircraft registration number in the subject line or fax it to 609-485-5078
Choose an AGHME constellation for monitoring (see the “AGHME Locations” section for choices).
Flight plan on a route through the AGHME coverage area, at a flight level between 290 and 410, inclusive. There are no special monitoring routings; do not ask ATC for any special treatment to accommodate AGHME measurement.
Ensure that the flight plan provides for straight level-flight operation through the AGHME coverage area.
Prior to departure, verify the status of appropriate AGHME monitoring constellation on the “AGHME Locations” link
In flight, do not ask ATC for any special handling or treatment to accommodate the flight for AGHME monitoring purposes. AGHME monitoring is not an ATC responsibility.
Notes: If an operator chooses to fly over one of the AGHMEs in North America, the steps presented here should be followed. After coordination with the appropriate officials and the application process, the operator must flight plan on a route at an RVSM Flight level through the AGHME coverage area.
This chart also shows where in North America the AGHMEs are located: In Canada there are 2 operational systems in Lethbridge and Ottawa, and the US there are 4 operational systems in Atlantic City, Cleveland, Wichita, and Phoenix with an additional element planned for Oregon.

## Slide 24: General Information
Other HMU Procedures
AGHME Procedures
GMU
Procedures
Monitoring Process
RMA Information
Useful Web Links
Points of Contact
References
Other HMU Procedures
For Procedures on how to use HMU’s in Europe contact: EUROCONTROL http://www.ecacnav.com/RVSM
For Procedures on how to use the HMU in Strumble contact: NAT Central Monitoring Agency Via email at natcma@nats.co.uk
Notes: Information on where to obtain guidance for use of the HMUs in Europe and in the United Kingdom is presented here. EUROCONTROL is the point of contact for the European HMUs and the NAT Central Monitoring Agency is the point of contact for the HMU at Strumble.

## Slide 25: CONCLUSION FAA RVSM Webpage: http://www.faa.gov/about/office_org/headquarters_offices/ato/service_units/enroute/rvsm/
Thank you for your attention and have a wonderful day!
Notes: This concludes the presentation on the US Domestic Implementation of RVSM Monitoring Requirements. If you remember one thing, remember that all of the information presented here along with a great deal more can be found on the FAA RVSM Website. The website is now updated with specific information regarding the RVSM Monitoring Program and can be accessed through the link listed here. If questions arise during the monitoring process, use the Point of Contacts list to get assistance. Thank you for your attention and have a wonderful day.