|  | U.S. Department of Transportation Federal Aviation Administration Washington, D.C. |
| --- | --- |
| Master Minimum Equipment List |
| Revision: 9 |
| Date: DRAFT |
| Falcon 900 |
| Dassault Aviation |
| Mystere Falcon 900, Falcon 900B, Falcon 900C |
| John K. Pinnow, Chairman |
| Flight Operations Evaluation Board (FOEB) |
| Federal Aviation Administration Flight Standards Division Seattle Aircraft Evaluation Group, SEA-AEG 1601 Lind Ave. S.W. Renton, WA 98057-3356 |
| Telephone: | (425) 917-6600 |
| FAX: | (425) 917-6638 |

Table of Contents

ATA	SYSTEM	PAGE

--	Cover Page	I

--	Table of Contents	II

--	Control Page	III, IV, V

--	Highlights of Change	VI

--	Definitions	VII

--	Preamble	VIII

21	Air Conditioning	21-1, THRU 10

22	Auto Flight	22-1, THRU 3

23	Communications	23-1, THRU 9

24	Electrical Power	24-1, THRU 3

25	Equipment/Furnishings	25-1, THRU 10

26	Fire Protection	26-1, 2

27	Flight Controls	27-1, THRU 5

28	Fuel	28-1, THRU 7

29	Hydraulic Power	29-1, 2

30	Ice and Rain Protection	30-1, THRU 4

31	Indicating/Recording Systems	31-1, THRU 3

32	Landing Gear	32-1, THRU 3

33	Lights	33-1, THRU 3

34	Navigation	34-1, THRU 25

35	Oxygen	35-1

36	Pneumatic	36-1, THRU 2

38	Water/Waste	38-1

46	Information Systems	46-1, 2

49	Airborne Auxiliary Power	49-1

52	Doors	52-1, 2

73	Engine Fuel & Control	73-1, 2

74	Ignition	74-1

77	Engine Indicating	77-1, 2

78	Engine Exhaust	78-1, 2

79	Engine Oil	79-1

80	Starting	80-1

Cover Page	I	9	DRAFT

Table of Contents	II	9	DRAFT

Control Page	III	9	DRAFT

Highlights of Change	VI	9	DRAFT

Definitions	VII	9	DRAFT

Preamble	VIII	9	DRAFT

ATA 21	21-1	9	DRAFT

21-2	9	DRAFT

21-3	9	DRAFT

21-4	9	DRAFT

21-5	9	DRAFT

21-6	9	DRAFT

21-7	9	DRAFT

21-8	9	DRAFT

21-9	9	DRAFT

21-10	9	DRAFT

ATA 22	22-1	9	DRAFT

22-2	9	DRAFT

22-3	9	DRAFT

ATA 23	23-1	9	DRAFT

23-2	9	DRAFT

23-3	9	DRAFT

23-4	9	DRAFT

23-5	9	DRAFT

23-6	9	DRAFT

23-7	9	DRAFT

23-8	9	DRAFT

23-9	9	DRAFT

ATA 24	24-1	9	DRAFT

24-2	9	DRAFT

24-3	9	DRAFT

ATA 25	25-1	9	DRAFT

25-2	9	DRAFT

25-3	9	DRAFT

25-4	9	DRAFT

25-5	9	DRAFT

25-6	9	DRAFT

25-7	9	DRAFT

25-8	9	DRAFT

25-9	9	DRAFT

25-10	9	DRAFT

ATA 26	26-1	9	DRAFT

26-2	9	DRAFT

ATA 27	27-1	9	DRAFT

27-2                9	DRAFT

27-3	9                      DRAFT

27-4	9	DRAFT

27-5	9	DRAFT

ATA 28	28-1	9	DRAFT

28-2	9	DRAFT

28-3	9	DRAFT

28-4	9	DRAFT

28-5	9	DRAFT

28-6	9	DRAFT

28-7	9	DRAFT

ATA 29	29-1	9	DRAFT

29-2	9	DRAFT

ATA 30	30-1	9	DRAFT

30-2	9	DRAFT

30-3	9	DRAFT

30-4	9	DRAFT

ATA 31	31-1	9	DRAFT

31-2	9	DRAFT

31-3	9	DRAFT

ATA 32	32-1	9	DRAFT

32-2	9	DRAFT

32-3	9	DRAFT

ATA 33	33-1	9	DRAFT

33-2	9	DRAFT

33-3	9	DRAFT

ATA 34	34-1	9	DRAFT

34-2	9	DRAFT

34-3	9	DRAFT

34-4	9	DRAFT

34-5	9	DRAFT

34-6	9	DRAFT

34-7	9	DRAFT

34-8	9	DRAFT

34-9	9	DRAFT

34-10	9	DRAFT

34-11	9	DRAFT

34-12	9	DRAFT

34-13	9	DRAFT

34-14	9	DRAFT

34-15	9	DRAFT

34-16	9	DRAFT

34-17	9	DRAFT

34-18	9	DRAFT

34-19	9	DRAFT

34-20	9	DRAFT

34-21	9	DRAFT

34-22	9	DRAFT

34-23	9	DRAFT

34-24	9	DRAFT

34-25	9	DRAFT

ATA 35	35-1	9	DRAFT

ATA 36	36-1	9	DRAFT

36-2	9	DRAFT

ATA 38	38-1	9	DRAFT

ATA 46	46-1	9	DRAFT

46-2	9	DRAFT

ATA 49	49-1	9	DRAFT

ATA 52	52-1	9	DRAFT

52-2	9	DRAFT

ATA 73	73-1	9	DRAFT

73-2	9	DRAFT

ATA 74	74-1	9	DRAFT

ATA 77	77-1	9	DRAFT

77-2	9	DRAFT

ATA 78	78-1	9	DRAFT

78-2	9	DRAFT

ATA 79	79-1	9	DRAFT

ATA 80	80-1	9	DRAFT

Highlights of Change

General Changes

-     Wording "operates normally" and "check to be operative" are re-worded as "is    operative / verified operative"

-    Wording "flight days" are re-worded as "consecutive calendar days"

-     Reference to item xx is added when if required

-    When the flight is conducted in unpressurized configuration, (O) and the check of EFIS Fans are added.

-    "Warning Light" are replaced by "Caution Light" for amber light displays

-    (O) or (M) is changed / added / deleted according to the OPER or MAINT procedure  to perform and the need of the crew to go out the cockpit

-    Various rewordings

-    Complete revision to all pages of MMEL. This is to accommodate the new format where all pages of an ATA chapter are changed when there are any changes anywhere in the chapter.

Major Changes

ATA 24: 	10.	Loadshed override

ATA 25: 	2. 	Pilot’s seat headreat

3. 	Copilot's seat headrest

19. 	Galley to Cabin Sliding Door

ATA26: 	2. 	APU Compartment Extinguisher System

3. 	Baggage Compartment Extinguisher System

ATA 28: 	9. 	XTK2 system

ATA 30:  	5. 	Windshield Wipers in non-rest position

17. 	Ice Detection System

ATA 34: 	3. 	Stby Magnetic Compass Lighting is added

17. 	Navigation Databases Data Loader

55. 	Incidence Meter

ATA 38: 	1. 	Rear Toilet Drain Valve

ATA 49: 	1. 	APU

ATA 52: 	6. & 7. Baggage Compartment External Door Reducing Gear Motor

Policy Letter 39, 56, 72, 79, 93, 106, 117, 120, 129 Updated or Incorporated

For the Master Minimum Equipment List, Definitions addendum, refer to the current FAA Policy Letter PL-25, “Policy Concerning MMEL Definitions”, as well as, the current FAA Policy Letter PL-70, “Definitions Required in MELs”, as found on the Flight Standards Information Management System “FSIMS” website.

FSIMS - Policy Letters

For the Master Minimum Equipment List, Preamble addendum, refer to the current FAA Policy Letter PL-34, “MMEL and MEL Preamble”, for operations under 14 CFR Parts 121, 125, 129, and 135, and FAA Policy Letter PL-36, “FAR Part 91 MEL Approval & Preamble”, for operations under 14 CFR Part 91, as found on the Flight Standards Information Management System “FSIMS” website.

FSIMS - Policy Letters

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Automatic Pressure Controller 21-81-00 | C | 1 | 0 | (O) May be inoperative provided: UP-DN manual controller and Dump mode are verified operative before each flight, Cabin visual and audio warnings are verified operative, and UP-DN manual controller is set to the RH part of the white arc for take-off. | ¦ ¦ ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | UP-DN Manual Controller 21-81-00 | C | 1 | 0 | (O) May be inoperative provided: Automatic pressure control system is verified operative, DUMP mode is verified operative before first flight of the day, and Manual controller is aligned with the green index mark. | ¦ ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Outflow Pressurization Valves 21-81-00 |  |  |  |  |  |
|  | Electropneumatic Outflow Valve | C | 1 | 0 | (O) May be inoperative provided aircraft is operated at or below 14,000 ft MSL. |  |
|  | Pneumatic Outflow Valve | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | Triple Cabin Indicator 21-81-00 |  |  |  |  |  |
|  | Cabin Altitude Indication | C | 1 | 0 | (O) May be inoperative provided: Cabin differential pressure indicator is verified operative, and A chart to convert cabin pressure differential to cabin altitude is provided to the crew. | ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 4. | Triple Cabin Indicator 21-81-00 (Cont'd) |  |  |  |  |  |
|  | Cabin Differential Pressure Indication | C | 1 | 0 | (O) May be inoperative provided: Cabin altitude indicator is verified operative, and A chart to convert cabin altitude to cabin differential pressure is provided to the crew. | ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | Cabin Vertical Speed | C | 1 | 0 | (O) May be inoperative provided: Cabin pressure differential indicator is operative, and Automatic cabin pressure control is operative. | ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Cabin Aural Warning (Cabin Altitude) 21-81-00 | C | 1 | 0 | (O) May be inoperative provided: CABIN warning light is verified operative, and Cabin altitude remains at or below 10,000 feet. | ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | CABIN Light/Aural Warning Test Circuit 21-81-00 | C | 1 | 0 | (M)(O) May be inoperative provided operation of CABIN light and aural warning are verified operative. | ¦ |
|  | CABIN Warning Light 21-81-00 |  |  |  |  |  |
|  | MF 900, 900B only | C | 1 | 0 | (M)(O) May be inoperative provided: Aural warning feature is operative, Visual inspection before departure verifies that main entrance door is closed and latched, and forward toilet service door (if installed) is closed, Cabin altitude remains at or below 10,000 ft., and Warning light is deactivated if it operates continuously. | ¦ ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 7. | CABIN Warning Light 21-81-00 (Cont’d) |  |  |  |  |  |
|  | F900C Only | C | 1 | 0 | (M)(O) May be inoperative provided: CABIN aural warning is operative, and Cabin altitude remains at or below 8,000 feet. | ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | CABIN and CREW Air Conditioning Bleed Control Valves 21-00-00 | C | 2 | 1 | (M)(O) One may be inoperative closed provided: Remaining valve is operative, Airplane remains at or below FL 410, and Air supply interconnect remains open. | ¦ |
|  |  | C | 2 | 0 | (O) Both AUTO position may be inoperative provided: OFF position is selected for take-off, ON position is selected at the end of the second segment climb profile, Air flow/pressurization is monitored, and Cabin altitude light and audio are operative. | ¦ ¦ ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Environmental Control Unit (ECU) 21-20-00 | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |
|  | Automatic Temperature Control System 21-50-00 | C | 2 | 1 | (O) One may be inoperative provided the associated manual mode is verified operative. | ¦ ¦ |
|  |  |  |  |  | NOTE: If necessary, turn off associated air conditioning valve. |  |
|  |  | C | 2 | 0 | (O) May be inoperative in the automatic mode provided both manual modes are verified operative. | ¦ ¦ |
|  | CABIN Temperature Remote Control Selector 21-50-00 | C | 1 | 0 | May be inoperative provided the cockpit control for the cabin is operative. | ¦ |
|  | Temperature Control Valve Position Indicators 21-50-00 | C | 2 | 0 |  |  |
|  | Cabin Temperature Indicator 21-50-00 | C | 1 | 0 |  |  |
|  | Gasper PRV Supply Valve 21-40-00 | C | 1 | 0 | (O) May be inoperative provided EFIS Fans are verified operative. | ¦ ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Air Supply Conditioning Tie Control Lever 21-30-00 | C | 1 | 0 | May be inoperative provided cabin and crew air conditioning bleed control valves are operative. | ¦ |
|  | Baggage Compartment Supply Valve 21-60-00 | C | 1 | 0 | (M) May be inoperative closed. | ¦ |
|  |  | C | 1 | 0 | (M) May be inoperative open provided the CREW air conditioning control valve is verified operative. | ¦ ¦ |
|  | Baggage Compartment Isolating Valve 21-60-00 |  |  |  |  |  |
|  | MF900 & F900B | C | 1 | 0 | (O)(M) May be inoperative provided: Valve is secured in the closed position, BAG ACCESS light is out, Baggage compartment distribution valve is verified operative, Crew air conditioning valve is operative, Baggage compartment remains empty and is placarded “DO NOT OPEN IN FLIGHT”, and AFM limitations are applied. | ¦ ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 17. | Baggage Compartment Isolating Valve 21-60-00 (Cont'd) |  |  |  |  |  |
| 2) | F900C Only | C | 1 | 0 | (M)(O) May be inoperative in closed position (BAG ISOL light on) provided: Valve is secured in the closed position, MESSAGE* caution light is operative, No BAG ACCESS message is displayed on the EID, Baggage compartment distribution valve is verified operative, Crew air conditioning valve is operative, Baggage compartment remains empty and is placarded “DO NOT OPEN IN FLIGHT”, and AFM limitations are applied. | ¦ ¦ ¦ ¦ ¦ ¦ |
|  | EFIS Cooling Systems 21-70-00 |  |  |  |  |  |
|  | MF900 & F900B | C | 2 | 1 | (M) One may be inoperative provided all EFIS components are properly cooled by the cold air supply system. |  |
|  | F900C Only | C | 5 | 4 | (M) One may be inoperative provided the cold air supply system is verified to provide an adequate airflow to the EFIS. |  |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Nose Cone Supply Valve 21-85-00 | C | 1 | 0 | (M) May be inoperative OPEN. |  |
|  |  | C | 1 | 0 | (M) May be inoperative CLOSED provided: NOSE CONE OVHT warning system is verified operative, and Nose cone blower is verified operative. | ¦ ¦ ¦ |
|  | Nose Cone Blower 21-85-00 | C | 1 | 0 | (M) May be inoperative provided: NOSE CONE OVHT warning system is verified operative, and Nose cone supply valve is verified operative. | ¦ ¦ ¦ |
|  | Pilot Gaspers 21-40-00 | C | 2 | 0 | (M) May be inoperative provided at least one gasper outlet remains open. |  |
| *** | Flood Duct Systems | C | 2 | 0 |  |  |
|  | ECU OVHT Caution Light | C | 1 | 0 | May be inoperative provided the ECU (item 21-9) is considered inoperative. | ¦ |

| 21 | AIR CONDITIONING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | ECU Turbo Fan | A | 1 | 0 | (M)(O) May be inoperative provided: Air conditioning remains OFF on ground and in flight when IAS is below 310 Kt, EFIS fans are verified operative, Air conditioning is switched ON in flight only when IAS is above 310 Kt, Cabin and crew air conditioning bleed control valves are verified operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | ECU A/I Switch Light (With Mod 1779 or SB F900-131) | C | 1 | 0 | (M) May be inoperative provided the emergency anti-ice electric valve is verified open. |  |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Flight is conducted in an unpressurized configuration, and EFIS fans are verified operative | ¦ ¦ |

| 22 | AUTO FLIGHT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Autopilot System 22-00-00 | B | - | 0 | Except where enroute operations require its use, may be inoperative provided approach minimums do not require its use. |  |
|  |  | C | - | 1 |  |  |
|  | AP, FD, YD Functions | C | 2 | 0 | NOTE: Any mode which is operative may be used. | ¦ |
| 2) | Mach Trim Function | C | 2 | 1 |  |  |
|  |  | C | 2 | 0 | May be inoperative provided speed remains at or below M .80. |  |
| 2. | Autopilot Disengage Switches 22-00-00 | C | 2 | 1 | One may be inoperative provided: Autopilot is not used below 1,500 feet AGL, and Approach minimus do not require the use of the autopilot. | ¦ ¦ ¦ ¦ ¦ |
|  |  | B | 2 | 0 | May be inoperative provided autopilot is not used. | ¦ |
| 3. | Autopilot Control Panel 22-00-00 | B | 1 | 0 | Except where enroute operations require its use, may be inoperative provided speed remains at or below M .80. |  |
| 4. | Advisory Display Units (ID-802) 22-00-00 (Except F900C) | C | - | 1 |  |  |

| 22 | AUTO FLIGHT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 5. | Manual AP Computer Transfer Functions 22-00-00 | C | - | 0 | (O) May be inoperative provided the green CPL arrows are in view in both EADI’s. |  |
| 6. | Autopilot Disconnect Light 22-00-00 |  |  |  |  |  |
|  | MF900 & F900B | C | 1 | 0 | (O) May be inoperative provided: ID-802 ADU is operative, AP disconnect is indicated by a AP DISENGAGED amber flashing message, and Warning light is deactivated if it operates continuously. | ¦ |
| 2) | Warning Label (PFD) (900C Only) | C | 1 | 0 | (O) May be inoperative provided Master Warning and AUTOPILOT aural warning are verified operative. | ¦ |
| 7. | MISTRIM Light 22-00-00 | C | 1 | 0 | (O) May be inoperative provided the ID-802 ADU is operative. | ¦ |
| 8. | Yaw Damper 22-00-00 | C | 1 | 0 |  |  |
| 9. | Go-Around Buttons | C | 2 | 1 | (O) Copilot’s button may be inoperative provided Captain’s button is operative. | ¦ |
|  |  | C | 2 | 0 | May be inoperative provided autopilot or flight director is not used below 1,500 feet AGL. |  |

| 22 | AUTO FLIGHT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 10. | Integrated Avionics Computer (IAC) (F900C Only) | A | 3 | 2 | (O) No. 1 IAC may be inoperative provided repairs are made within three consecutive calendar days. | ¦ ¦ |
| 11. | Pitch Servomotor | B | 1 | 0 | May be inoperative provided autopilot (item 22-1) is considered inoperative and not used. | ¦ |
| 12. | Roll Servomotor | B | 1 | 0 | May be inoperative provided autopilot (item 22-1) is considered inoperative and not used. | ¦ |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Communication Systems (VHF, UHF) | D | - | - | Any in excess of those required by CFR may be inoperative provided it is not powered by the Emergency AC Bus, Emergency DC Bus, Battery Bus, Battery Direct Bus, or the DC Transfer Bus and not required for emergency procedures. | ¦ |
|  | VHF Comm Control Panels |  |  |  |  |  |
|  | Frequency Transfer Light | C | - | 0 |  |  |
|  | Frequency Transfer Switch | C | - | 0 |  |  |
|  | Frequency Transfer Knob | C | - | 2 |  |  |
|  | Frequency Indication | C | - | 2 |  |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Passenger Address System (PA) |  |  |  |  |  |
|  | Passenger Configuration | B | 1 | 0 | (O) May be inoperative provided: Alternate, normal and emergency procedures and/or operating restrictions are established and used, and Flight attendant alerting system (audio and visual) is operative. | ¦ |
|  |  |  |  |  | NOTE: Any station function(s) that is operative may be used. | ¦ ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided: PA not required by FAR, and Alternate, normal and emergency procedures and/or operating restrictions are established and used. |  |
|  |  |  |  |  | NOTE: Any station function(s) that is operative may be used. | ¦ ¦ |
|  | Lavatory Speakers | C | - | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 1 | 0 | May be inoperative provided procedures do not require its use. |  |
|  |  |  |  |  | (Continued) |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Passenger Address System (PA) (Cont’d) |  |  |  |  |  |
|  | Cargo Configuration |  |  |  |  |  |
|  | Lavatory Speakers | C | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 1 | 0 | May be inoperative provided procedures do not require its use. |  |
|  | Flight Deck Speaker Systems 23-50-00 | C | 2 | 0 | May be inoperative provided: Procedures do not require their use, and Headsets are installed and are operative. | ¦¦ |
|  | Microphones 23-50-00 | C | - | 2 | May be inoperative provided one microphone is operative at each pilot’s station. | ¦ |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Cockpit Voice Recorder System (CVR) |  |  |  |  |  |
|  | With FDR Installed | A | 1 | 0 | May be inoperative provided: Flight Data Recorder (FDR) is operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ |
|  | Without FDR Installed | A | 1 | 0 | May be inoperative provided repairs are made within three consecutive calendar days. | ¦ |
|  | For an operator other than a holder of an air carrier or commercial operator certificate. | A | 1 | 0 | May be inoperative provided repairs are made in accordance with applicable FARs. |  |
| *** | Selective Call System (SELCAL) 23-92-01 | C | - | 0 | May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |
|  | Channels | C | - | 0 | (O)May be inoperative provided alternate procedures are established and used. | ¦ |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Static Dischargers 23-60-00 | C | 17 | 15 | Two may be damaged or missing provided they are not located in the same area. |  |
|  | Ground Service Interphone System (Flight Deck to Ground) |  |  |  | Deleted, relief incorporated into Item 23-23, Revision 6. |  |
| *** | Air Phone |  |  |  | Moved to Item 25-5, Revision 1. |  |
| *** | Automatic Cabin Briefer | D | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  | Avionics Master Switches | C | 2 | 1 | (M) Pilot’s side may be inoperative provided it has failed in the “ON” position only. |  |
| *** | FMS Master Switch (Except F900C) | C | - | 1 |  |  |
|  | Standby Battery Pack for Comm/ATC |  |  |  | Moved to ATA 24. |  |
|  | Emergency Locator Transmitter (ELT) 25-96-01 |  |  |  | Moved to ATA 25. |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Boom Microphones |  |  |  |  |  |
|  | Cockpit Voice Recorder Equipped to Record Boom Microphones per FAR 121.359(g), 135.151(d), or 125.227(e). | A | - | 0 | May be inoperative provided: Flight data recorder (FDR) is operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ |
| *** | Cockpit Voice Recorder Not Equipped to Record Boom Microphone | D | - | 0 | Any in excess of those required by FAR may be inoperative. |  |
|  | Audio Selector Panels 23-50-00 | D | - | - | Any in excess of those required for flight deck crewmembers (including official observer in forward observer’s seat) may be inoperative. |  |
|  | Headsets 23-50-00 | C | 2 | 1 | One pilot’s headset may be inoperative provided cockpit speakers are operative. | ¦ |
| *** | Airborne Flight Information System (AFIS) (VHF SAT) | C | 1 | 0 | May be inoperative provided alternate procedures are established and used. |  |
| *** | SATCOM | C | - | 0 | May be inoperative provided alternate procedures are established and used. |  |
| *** | ACARS | C | - | 0 | May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Radio Tuning Unit (RTU) | C | 2 | 1 | (O) One may be inoperative provided: FMS is equipped to allow tuning of radios, and Radio tuning function of the FMS is operative. | ¦ |
| 22. | High Frequency (HF) Communication System | D | - | - | (O) Any in excess of those required by FAR may be inoperative. |  |
|  |  | C | - | 1 | (O) May be inoperative while conducting operations that require two LRCS provided: SATCOM Voice or Data Link (High or Low Gain) is operative, Alternate procedures are established and used, SATCOM Voice coverage is available over the intended route of flight, and If SATCOM Voice is to be used over the intended route of flight, SATCOM Voice short codes (INMARSAT) or direct dial commercial numbers (IRIDIUM) must be available. If not available, prior coordination with appropriate ATS (FIR) facility is required. NOTE: SATCOM Voice is to be used only as a backup to normal HF communications. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Crewmember Interphone System(s) |  |  |  |  |  |
|  | Passenger Configuration |  |  |  |  |  |
|  | Flight Deck to Cabin, Cabin to Flight Deck Functions | B | - | - | (O) May be inoperative provided: Flight deck to cabin and cabin to flight deck interphone functions are operative on at least fifty percent of the cabin handsets, and Alternate communications procedures between the affected flight attendants station(s) are established and used. | ¦ |
|  |  |  |  |  | NOTE: Any station function(s) that is operative may be used. | ¦ ¦ |
|  | Flight Deck to Ground Function |  |  |  |  |  |
| 1) | Large Turbojet Powered Airplanes Operating under Part 121 | C | 1 | 0 | (O) Flight interphone flight deck to ground/ground to flight deck function may be inoperative provided: Alternate procedures are established and used, and Nose gear/forward fuselage service interphone jack is operative. | ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 23 | COMMUNICATIONS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 23. | Crewmember Interphone System(s) (Cont’d) |  |  |  |  |  |
| 1) | Passenger Configuration (Cont'd) |  |  |  |  |  |
| b) | Flight Deck to Ground Function (Cont'd) |  |  |  |  |  |
|  | Large Turbojet Powered Airplanes Operating under Part 121 (Cont'd) | C | 1 | 0 | (O) Service interphone flight deck to ground/ground to flight deck function may be inoperative provided: Alternate procedures are established and used, and Nose gear/forward fuselage flight interphone jack is operative. | ¦ |
|  |  | B | - | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  | All Other Aircraft/Operations | C | - | 0 | (O) May be inoperative provided procedures are established and used. |  |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |

| 24 | ELECTRICAL POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Batteries 24-31-00 |  |  |  | Deleted, Rev. 3. |  |
| 2. | Battery Blower 24-31-00 | C | 1 | 0 | (O) May be inoperative provided HOT BAT warning system is operative. |  |
| 3. | BAT 1 and BAT 2 Caution Lights 24-31-00 | B | 2 | 1 | (O) One may be inoperative provided: Voltage and charging current of each battery are verified operative before each takeoff, Voltmeter and ammeter of the associated DC generating system and battery overheat sensing system are closely monitored during flight, and It is verified that the associated battery is tied to the bus. | ¦ ¦ ¦ |
| 4. | Battery Temperature Indicating Systems (Digital Or Analog) 24-31-00 |  |  |  |  |  |
| 1) | TEMP Indication | C | 2 | 1 | (O) One may be inoperative provided associated battery warning lights are operative. | ¦ ¦ |
| 2) | Warm (Amber) and Red Hot Light (2 Light system) | C | 2 | 1 | (O) One may be inoperative provided both temperature indicators are operative. | ¦ ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 24 | ELECTRICAL POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 4. | Battery Temperature Indicating Systems (Digital Or Analog) 24-31-00 (Cont'd) |  |  |  |  |  |
| 3) | Warm (Amber) and Red Hot Light (4 Light system) | C | 4 | 3 | (O) One may be inoperative provided both temperature indicators are operative. | ¦ ¦ ¦ |
| 5. | GEN Caution Lights 24-32-00 | C | 3 | 2 | (O) One may be inoperative provided: Voltmeter and ammeter of the associated DC generating system are operative, Engine start is manually discontinued at 50% N2, and Generator output current is closely monitored during flight. | ¦ |
| 6. | DC Voltmeters | C | 2 | 1 | (O) One may be inoperative provided: Ammeter of the associated generating system is operative, and Bus TIED and generator caution lights are operative. | ¦ ¦ ¦ ¦ ¦ |
| 7. | Generators | B | 3 | 2 | (O) Either GEN 1 or GEN 3 may be inoperative provided: Bus tie system is verified operative, and AFM load shedding procedures are considered. | ¦ ¦ ¦ ¦ ¦ |
| 8. | BUS TIED Caution Light | C | 1 | 0 | (O) May be inoperative provided the bus tie circuit and voltmeters are verified operative. | ¦ ¦ |

| 24 | ELECTRICAL POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | AUX Battery System | D | 1 | 0 |  |  |
| 10. *** | Load Shed Override Function (M3468) | D | 1 | 0 | (M) May be inoperative provided: Optional Galley Loads are not used, and Associated Galley circuit breakers (blue ring) are pulled and collared. | ¦ ¦ ¦ ¦ ¦ ¦ |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Crewmember Shoulder Harness 25-10-00 |  |  |  | Deleted, Rev. 1. |  |
| 2. | Pilot’s Seat |  |  |  |  |  |
|  | Vertical Adjustment | C | 2 | 0 | (M)(O) May be inoperative provided: Seat is secured at the individual crewmember’s requirements, Fore-aft adjustment is operative, and Associated circuit breakers are pulled and collared. | ¦ |
| 2) | Armrests | C | 4 | 0 | (M)(O) May be inoperative provided: Affected armrest is in the up position or removed, and Seat is acceptable to the affected crewmember. |  |
| 3) | Recline Adjustment | C | 2 | 0 | (M)(O) May be inoperative provided: Seat is secured at a position acceptable to the affected crewmember, and Seat is able to move full Fore and Aft on its track. |  |
| 4) | Headrests | C | 2 | 0 | (O) Headrest fairing may be damaged provided: Headrest structure is verified adequate, and It is acceptable to the affected crewmember. | ¦ ¦ ¦ ¦ ¦ ¦ |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 3. | Passenger Seats | D | - | - | May be inoperative provided: Seat does not block an Emergency Exit, Seat does not restrict any passenger from access to the main aircraft aisle, and The affected seat(s) are blocked and placarded DO NOT OCCUPY. NOTE 1: A seat with an inoperative seat belt is considered inoperative. NOTE 2: Inoperative seats do not affect the required number of Flight Attendants. NOTE 3: Affected seat(s) may include the seat(s) behind and/or adjacent outboard seats. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
| *** | Recline Mechanism | D | - | - | (M) May be inoperative and seat occupied provided seat back is secured in the full upright position. | ¦ ¦ ¦ |
|  |  | D | - | - | May be inoperative and seat occupied provided seat back is immovable in full upright position. | ¦ ¦ ¦ |
| 2) | Under seat Baggage Restraining Bars | C | - | - | (O) May be inoperative provided: Baggage is not stowed under seat with inoperative restraining bar, Associated seat is placarded DO NOT STOW BAGGAGE UNDER THIS SEAT, and Procedures are established to alert Cabin Crew of inoperative restraining bar. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 3) | Armrest |  |  |  |  |  |
|  | a) Armrest with Recline Mechanism | D | - | - | (M) May be inoperative or missing and seat occupied provided: Armrest does not block an Emergency Exit, Armrest does not restrict any passenger from access to the main aircraft aisle, and If armrest is missing, seat is secured in the full upright position. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | b) Armrest without Recline Mechanism | D | - | - | May be inoperative or missing and seat occupied provided: Armrest does not block an Emergency Exit, and b) Armrest does not restrict any passenger from access to the main aircraft aisle. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
| 4) | Seat Belt Air Bag Restraint Systems |  |  |  |  | ¦ ¦ |
|  | a) Seat Belt Air Bags Required By CFR | D | - | - | May be inoperative provided affected seat is blocked and placarded DO NOT OCCUPY. | ¦ ¦ ¦ |
|  | b) Seat Belt Air Bags Not Required By CFR | D | - | - | May be inoperative or disconnected provided seat belt operates normally. | ¦ ¦ |
| 5) *** | Electrical/Electronic Systems Components | C | - | - | (M) May be inoperative and seat occupied provided associated component(s) is deactivated. | ¦ ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 3. | Passenger Seats (Cont'd) |  |  |  |  |  |
| 6) | Swivel Mechanism | C | - | - | May be inoperative and seat occupied provided: Associated seat does not block an emergency exit, Associated seat does not restrict any passenger from access to main aisle, and Associated seat is locked in the take-off position for take-off and landing. | ¦ ¦ ¦ ¦ |
|  |  |  |  |  | NOTE 1: A seat with an inoperative safety belt is considered inoperative. |  |
|  |  |  |  |  | NOTE 2: The affected seat(s) may include the seat behind and its adjacent outboard seat(s). |  |
|  |  |  |  |  | NOTE 3: Inoperative seat(s) do not affect the required number of flight attendants. |  |
| 7) | Headrests | D | - | - | May be inoperative provided associated passenger seat is in take-off position. | ¦ ¦ |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 4. | Passenger Convenience/NEF Items |  |  |  |  |  |
|  |  |  |  |  | Deleted, Rev. 9 | ¦ |
| *** | Non–Essential Equipment & Furnishings (NEF) |  | - | 0 | May be inoperative, damaged or missing provided that the item(s) is deferred in accordance with the operator’s NEF deferral program. The NEF program, procedures and processes are outlined in the operators (insert name) Manual. (M) and (O) procedures, if required, must be available to the flight crew and included in the operator’s appropriate document. |  |
|  |  |  |  |  | NOTE: Exterior lavatory door ash trays are not considered NEF items. |  |
| 5. *** | Air Phone | D | - | 0 |  |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 6. | Forward Observer Seat (Including Associated Equipment) | A | 1 | 0 | May be inoperative provided: A passenger seat in the passenger cabin is made available to an FAA inspector for the performance of official duties, and Repairs are made within two consecutive calendar days. | ¦ |
|  |  | A | 1 | 0 | May be inoperative provided: Required minimum safety equipment (safety belt and oxygen) is available, Seat is acceptable to an FAA inspector for the performance of official duties, and Repairs are made within two consecutive calendar days. | ¦ |
|  |  |  |  |  | NOTE 1: These provisos are intended to provide for occupancy of the above seat by an FAA inspector when the minimum safety equipment (oxygen and safety belt) is functional and the inspector determines the conditions to be acceptable. NOTE 2: The pilot-in-command will determine if the minimum safety equipment is functionally for other persons authorized to occupy any observer seat. NOTE 3: When not occupied, the observer seat must be stowed so as to not impede egress from the cockpit. |  |
|  |  |  |  |  | (Continued) |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 6. | Forward Observer Seat (Including Associated Equipment) (Cont'd) |  |  |  |  |  |
|  | For an operator other than a holder of an air carrier or commercial operator certificate. | D | - | 0 | NOTE: The pilot-in-command will determine if the minimum safety equipment is functionally for other persons authorized to occupy any observer seat. | ¦ ¦ ¦ ¦ ¦ |
| 7. | Emergency Locator Transmitter (ELT) |  |  |  |  |  |
|  | Survival Type ELTs | D | - | - | Any in excess of those required by FAR may be inoperative or missing. |  |
|  | Fixed ELTs | A | - | 0 | (M) May be inoperative provided: a) System is deactivated, and b) Repairs are made within 90 consecutive days. | ¦ ¦ ¦ ¦ |
|  |  | A | - | 0 | May be missing provided repairs are made within 90 consecutive days. | ¦ ¦ |
|  |  | D | - | - | (M) Any in excess of those required by FAR may be inoperative provided system is deactiviated. | ¦ ¦ ¦ |
|  |  | D | - | - | Any in excess of those required by FAR may be inoperative or missing. |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 8. | Lavatory Door Ashtrays |  |  |  |  |  |
|  | Airplanes With More Than One Lavatory Door Ashtray Installed | A | - | - | One may be missing provided it is replaced within 10 consecutive calendar days. | ¦ |
|  | Airplanes With Only One Lavatory Door Ashtray Installed | A | 1 | 0 | May be missing provided it is replaced within 3 consecutive calendar days. | ¦ |
| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| 9. *** | Security Systems | D | 1 | 0 |  |  |
| 10. *** | Cockpit Smoke Vision System (CSVS) (STC # SA00892LA) | D | - | 0 | May be inoperative or missing. | ¦ ¦ |
| 11. | Aircraft Ladders | C | 3 | 0 | (M) May be inoperative or removed. |  |
| 12. | Exterior Baggage Door | C | 1 | 0 | (M) May be inoperative provided Door is verified closed and secure prior to each departure. |  |
| 13. | Baggage Compartment Shelves |  |  |  |  |  |
| 1) | Shelf Stowage Straps | D | 2 | 0 | May be inoperative or removed provided the shelves remain in the down position. |  |
| 2) | Shelf Support Straps | D | 4 | 0 | May be inoperative or removed provided the shelves remains in the stowed (up) position and are not used. |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 14. | Overwater Equipment (Flotation Devices/Rafts) | D | - | - | Any in excess of those required by FAR may be inoperative or missing. |  |
| 15. | Crewmember Flashlight Holder Assemblies (Including Flashlight) | C | - | - | May be inoperative or missing provided crewmember has a flashlight of equivalent characteristics readily available. |  |
| 16. | Automatic External Defibrillator (AED) and/or Associated Equipment | A | - | 0 | (O) May be incomplete, missing or inoperative provided: a) AED is resealed in a manner that will identify it as a unit that can not be mistaken for a fully serviceable unit, and b) Repairs or replacements are made with-in 3 flight cycles. |  |
|  |  | D | - | - | Any in excess of those required by FAR may be incomplete, missing, or inoperative. |  |

| 25 | EQUIPMENT/ FURNISHINGS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 17. | Emergency Medical Kit (EMK) and/or Associated Equipment |  |  |  |  |  |
|  |  | A | - | 0 | (O) May be incomplete, missing or inoperative provided: EMK is resealed in a manner that will identify it as a unit that can not be mistaken for a fully serviceable unit, and Repairs or replacements are made within 3 flight cycles. |  |
|  |  | D | - | - | Any in excess of those required by FAR may be incomplete, missing, or inoperative. |  |
| 18. | First Aid Kit (FAK) and/or Associated Equipment | A | - | - | (O) If more than one is required by FAR, only one of the required first aid kits may be incomplete, missing or inoperative provided: FAK is resealed in a manner that will identify it as a unit that can not be mistaken for a fully serviceable unit, and Repairs or replacements are made within 3 flight cycles |  |
|  |  | D | - | - | Any in excess of those required by FAR may be incomplete, missing, or inoperative |  |
| 19. *** | Galley-to-Cabin Sliding Door ("Pocket" door) | D | 1 | 0 | (M) May be inoperative provided the door is secured in open position using an acceptable means. | ¦ ¦ ¦ |

| 26 | FIRE PROTECTION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | APU Fire Warning System 26-10-00 | D | 1 | 0 | (M) May be inoperative provided APU is considered inoperative (item 49-1) and not used. | ¦ |
| 2. | APU Fire Extinguisher System 26-20-00 | C | 1 | 0 | (M) May be inoperative provided: APU is not used, and Fire extinguisher pressure is verified adequate. | ¦ ¦ ¦ ¦ ¦ |
|  |  | C | 1 | 0 | May be inoperative provided APU is not used, and Baggage compartment remains empty | ¦ ¦ ¦ ¦ |
| 3. | Baggage Compartment |  |  |  |  | ¦ |
|  | Smoke Detector | C | 1 | 0 | May be inoperative provided: No supplemental electronic equipment or avionic are installed, and Only non-combustible materials are carried. | ¦ |
|  | Fire Extinguisher System | C | 1 | 0 | May be inoperative provided: Baggage compartment remains empty, and Fire extinguisher pressure is verified adequate. | ¦ ¦ ¦ ¦ ¦ |
|  |  | C | 1 | 0 | May be inoperative provided: Baggage compartment remains empty, and APU is not used. | ¦ ¦ ¦ ¦ |
| 26 | FIRE PROTECTION |  |  |  |  |  |
| 4. *** | Lavatory Smoke Detection System | C | - | 0 | (O) May be inoperative provided an alternate procedure is established and used to detect smoke in the Lavatory. |  |
| 5. | Hand Fire Extinguishers | D | - | - | Any in excess of those required by FAR may be inoperative or missing provided: The inoperative fire extinguisher is tagged inoperative, removed from the installed location, and placed out of sight so it cannot be mistaken for a functional unit, and Required distribution is maintained. |  |

| 27 | FLIGHT CONTROLS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Aileron Trim Control System | C | 1 | 0 | (M)(O) May be inoperative provided: Roll Trim is verified in neutral position, Aileron emergency operation is verified operative before each flight, Rudder trim system is verified operative, TRIM AILERON circuit breaker is pulled and collared, Fuel quantity indicators are operative, and Fuel imbalance between number 1 and number 3 tank system is limited to 500 lbs. or less. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | AILERON Trim Position Indicator | C | 1 | 0 | (M)(O) May be inoperative provided: Aileron trim control system verified is operative, Roll Trim is verified in neutral position, and Aileron control surfaces are verified to be in the same position. | ¦ |
|  | Arthur Q Units 27-10-00, 27-30-00 |  |  |  |  |  |
|  | Aileron | C | 1 | 0 | (M)(O) May be inoperative provided: Roll control forces are verified to be in low speed configuration before each departure, AIL FEEL circuit breaker is pulled and collared, and AFM limitations are observed. |  |
|  |  |  |  |  | (Continued) |  |

| 27 | FLIGHT CONTROLS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 3. | Arthur Q Units 27-10-00, 27-30-00 (Cont’d) |  |  |  |  |  |
|  | Elevator | B | 1 | 0 | (M)(O) May be inoperative provided: PITCH FEEL circuit breaker is pulled and collared, Arthur Bellcrank low speed position is verified prior to each departure, Airspeed does not exceed 220 KIAS/ .74 Mach, and AFM limitations are observed. |  |
|  | Rudder Trim System |  |  |  | Deleted, Rev. 1. |  |
|  | Rudder Trim Position Indicator 27-20-00 | C | 1 | 0 | (O) May be inoperative provided: Rudder trim control system is verified operative, and Rudder is visually verified to be in the neutral position with yaw damper off before departure. | ¦ ¦ ¦ |
|  | Horizontal Stabilizer Position Indicator 27-40-00 | C | 1 | 0 | (O) May be inoperative provided: Horizontal stabilizer system is operative, Stabilizer is visually verified and set between the two takeoff reference marks, and T/O CONFIG warning system is verified operative. | ¦ ¦ ¦ ¦ |

| 27 | FLIGHT CONTROLS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | PITCH FEEL Caution Light 27-30-00 | B | 1 | 0 | (M)(O) May be inoperative provided: Arthur Bellcrank low speed position is verified before each departure, Airspeed does not exceed 220 KIAS/. 74 Mach, and AFM limitations are observed. |  |
|  | Stabilizer Trim Audio Warning 27-40-00 | B | 1 | 0 | (O) May be inoperative provided: Horizontal Stabilizer trim is operative, T/O CONFIG warning system is verified operative, Horizontal Stabilizer position indicator is operative, and Autopilot is not used. | ¦ ¦ ¦ ¦ ¦ |
|  | Slat/Flap Configuration Panel 27-80-00 |  |  |  |  |  |
|  | Green Light | B | 1 | 0 | (O) May be inoperative provided: Position of the slats and the slat control are verified in agreement before each departure. T/O CONFIG warning system is verified operative, Wing anti-ice lights are operative, and Red (In Transit) Light is operative. | ¦ ¦ ¦ ¦ ¦ |
|  | Red Light | C | 1 | 0 | (O) May be inoperative provided speed remains at or below 200 KIAS. |  |

| 27 | FLIGHT CONTROLS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | STALL Test 27-30-00 | A | 2 | 1 | (O) One may be inoperative provided: Emergency slats control is verified operative before each departure, An airspeed greater than 1.3 Vs is maintained whenever the slats are retracted, Slats are extended with the normal control at speeds below 200 KIAS, Slat configuration panel is operative, AUTO SLATS caution light is operative, and Repairs are made within two consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | AUTO SLATS Caution Light 27-80-00 | C | 1 | 0 | (M) May be inoperative provided: Airspeed does not exceed 270 KIAS, Slats are extended with normal control at speeds below 200 KIAS, and Slat configuration panel is operative. | ¦ ¦ ¦ |
|  | T/O CONFIG Warning Light | C | 1 | 0 | (O) May be inoperative provided aural warning is verified operative. | ¦ |
|  | FLAP ASYM Caution Light 27-50-00 | C | 1 | 0 | (M)(O) May be inoperative provided: Flap asymmetry protection system is verified operative, and Flap symmetry is verified before each departure. | ¦ ¦ |

| 27 | FLIGHT CONTROLS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | AIRBRAKE Amber Light 27-60-00 | B | 1 | 0 | (M)(O) May be inoperative provided: Airbrakes are verified operative, Airbrakes are visually verified in the retracted position for each departure, STALL tests are verified operative, and T/O CONFIG warning system (light and aural) is verified operative. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | Rudder Pedal Adjustments | C | 2 | 0 | (M)(O) May be inoperative provided: Adjustments can be secured in a position that suits individual pilot(s) requirements, and Position of pedal(s) permits normal full flight control movement. |  |
|  | AIL FEEL Caution Light | C | 1 | 0 | (M)(O) May be inoperative provided: Roll control forces are verified to be in the low speed configuration before each departure, and AFM limitations are observed. | ¦ ¦ ¦ |
|  | AIL ZERO Caution Light | B | 1 | 0 | (O) May be inoperative provided it is verified before each departure that left and right ailerons are in same position when aileron trim is set to zero. |  |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | LEVEL Lights (Except F900C) 28-50-00 | C | 3 | 0 | (O) May be inoperative provided: Fuel quantity indicating system is operative, and LO FUEL caution lights are verified operative. | ¦ ¦ ¦ ¦ |
| 2. | LO FUEL Caution Lights 28-50-00 |  |  |  |  | ¦ |
|  | F900C Only | B | 3 | 2 | (O) One may be inoperative provided: Fuel quantity indicating system is operative, and LVL Messages on EID is verified operative. | ¦ ¦ ¦ ¦ ¦ |
|  | MF900 and F900B | B | 3 | 2 | (O) May be inoperative provided: Fuel quantity indicating system is operative, and LEVEL Lights are verified operative. | ¦ ¦ ¦ ¦ |
| 3. *** | Fuel Temperature Indication 28-50-00 | C | 1 | 0 | (O) May be inoperative provided: Boost pumps, transfer systems and engine Crossfeed are operative, and Operations are conducted at a TAT no colder than 13 degrees below the fuel freeze point. | ¦ ¦ |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 4. | Pressure Fueling System 28-60-00 | C | 1 | 0 | (O) May be inoperative OFF provided cockpit FUELING caution light is operative and extinguished. | ¦ ¦ |
|  | Vent Valves | C | 2 | 0 | (M) May be inoperative provided: Affected vent valve(s) is (are) manually opened prior to refueling and manually closed after refueling, If STOP FUELING red indicator light remains lighted after opening of the vent valves, gravity refueling is used, and Cockpit FUELING caution light is operative and extinguishes after closing sequence. | ¦ ¦ |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 5. | Booster Pumps 28-20-00 |  |  |  |  |  |
|  | Side Engine Booster Pump | C | 2 | 1 | (M)(O) One may be inoperative provided: Both center engine booster pumps are operative, Associated C/B is pulled and collared, Crossfeed system is used at engine start, Wing tank pressurization is verified with engines running (pressure gauge in rear compartment), Crossfeed system is selected on above 1500 ft AGL, Procedures to correct fuel imbalance is applied, and Operations are limited to 17000 ft MSL if JP4 or Jet B fuel is utilized or flight level 310 if Jet A or Jet 1A fuel is used. | ¦ |
|  |  |  |  |  | (Continued) |  |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 5. | Booster Pumps 28-20-00 (Cont'd) |  |  |  |  |  |
|  | Center Engine | C | 2 | 1 | (M)(O) One may be inoperative provided: Both side engine booster pumps are operative, Associated C/B is pulled and collared, Fuel tank pressurization is verified with engines running, Associated fuel quantity indicator is operative, Procedures to correct fuel imbalance is applied, and Operations are limited to 17000 ft MSL if JP4 or Jet B fuel is utilized or flight level 310 if Jet A or Jet 1A fuel is used. | ¦ ¦ ¦ ¦ |
| 6. | Wing Interconnection System (XTK 1-3) | C | 1 | 0 | (M) May be inoperative provided: Fuel X-feed system is operative, and Valve is verified closed. | ¦ ¦ |
| 7. | Fuel Quantity Indicators (Except F900C) | C | 3 | 2 | (M)(O) One indicator may be inoperative provided: Fuel quantity is determined by other acceptable means, Associated fuel level indicator (1,000 lbs.) light and LO fuel (250 lbs.) caution light are verified operative, and All other fuel components are operative. | ¦ ¦ ¦ ¦ ¦ |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 8. *** | Gross Weight Counter System | C | 1 | 0 |  |  |
| 9. *** | Front-To-Rear Tank Fuel Transfer System (XTK2) (Except F900C) |  |  |  |  |  |
|  | Automatic System | C | 1 | 0 | (M)(O) May be inoperative provided the OPEN/CLOSED electrical control is verified operative. |  |
|  |  | C | 1 | 0 | (M)(O) May be inoperative provided: Transfer valve XTK-2 is secured in open position, Fuel moment charts for aircraft without transfer valve XTK-2 is used for weight and balance computation, "XTK-2 OPEN" and "XTK-2 CLOSED" caution lights are disregarded, and Front fuel tank continuous consumption is monitored during flight. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
| 2) | OPEN/CLOSED Electrical Control System | C | 1 | 0 | (M)(O) May be inoperative provided manual control in the cabin is verified operative. | ¦ |
| 3) | XTK2 OPEN and XTK2 CLOSED caution Lights | C | 2 | 0 | (M)(O) May be inoperative provided fuel transfer from front to rear tank is monitored on fuel quantity indicators. | ¦ |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 10. | LVL Message (F900C Only) | C | 3 | 0 | (M) May be inoperative provided: Fuel quantity indicating system is operative, and LO FUEL caution lights are verified operative. | ¦ ¦ ¦ ¦ |
| 11. | Number 1 and Number 3 Tank Quantity Indicating System (EID) (F900C Only) | C | 2 | 1 | (M)(O) Indicating system for either Number 1 or Number 3 Tank may be inoperative provided: Fuel quantity is determined by other acceptable means, Fuel flow/fuel used indicators are operative, LVL message on EID is verified operative, LO FUEL caution lights are verified operative, and Partial fueling selector is not used. | ¦ ¦ ¦ ¦ ¦ ¦ |
| 12. | FUELING Caution Light | C | 1 | 0 | (M) May be inoperative provided it is verified: Both fueling panel access doors are closed, Fuel tanks pressurization is verified with engines running, Defueling valve is closed, and The DEFUELING switch remains in the OFF position. | ¦ ¦ |

| 28 | FUEL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 13. | XBP 1-3 System | C | 1 | 0 | (M)(O) May be inoperative closed provided: Both side engine boost pumps are operative, 1-2 and 2-3 crossfeed systems are verified operative, Fuel tank pressurization is verified with engines running, and Fuel quantity indications are operative. | ¦ ¦ ¦ ¦ |
| 14 | XBP 1-2 and 2-3 Valves | C | 2 | 1 | (M)(O) One may be inoperative closed provided: Both center boost pumps are operative, Remaining crossfeed system is operative, Fuel tank pressurization is verified with engine running, and Procedure to correct fuel imbalance is applied. | ¦ ¦ ¦ ¦ ¦ |

| 29 | HYDRAULIC POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | HYDR#.. PUMP.. Caution Lights (Except F900C) 29-10-00 | C | 3 | 2 | (O) One may be inoperative provided: Associated hydraulic pressure indicator is verified operative, Engine to be started first is the one whose PUMP light is inoperative, so as to check the amount of pressure delivered by the pump, and Standby hydraulic pump is verified operative before engine start. | ¦ ¦ ¦ |
|  | Hydraulic Pressure Indicators (System 1 or 2) (Except F900C) 29-10-00 | C | 2 | 1 | (O) One may be inoperative provided: All PUMP caution lights of associated system are verified operative, and Standby hydraulic pump is verified operative before each take-off. | ¦ ¦ ¦ ¦ |
|  | Hydraulic Reservoir 1 or 2 Fluid Quantity Indicators 29-10-00 | C | 2 | 0 | (M) May be inoperative provided fluid quantity is visually verified to be adequate before each takeoff. | ¦ |
|  | STBY PUMP Caution Light 29-20-00 | C | 1 | 0 | (M)(O) May be inoperative provided: Standby hydraulic pump is verified operative before engine start, and Selector handle is secured in position 2. | ¦ ¦ |
|  | No 1 System Accumulator 29-10-00 | C | 1 | 0 |  |  |

| 29 | HYDRAULIC POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Accumulator Pressure Indicators 29-10-00 | C | 4 | 0 | (M) May be inoperative provided an alternate procedure to verify accumulator pressure is established and used. |  |
|  | HYDR#.. PUMP.. Caution Lights (F900C Only) | C | 3 | 2 | (O) One may be inoperative provided: Associated hydraulic system pressure indicator is verified operative and is monitored during flight, and Standby hydraulic pump is verified operative before engine start. | ¦ ¦ ¦ ¦ ¦ |
|  | #1 System Hydraulic Pressure Indicator (F900C Only) | C | 1 | 0 | (M) May be inoperative provided HYDR #1 PUMP 1 and HYDR #1 PUMP 3 caution lights are verified operative. | ¦ ¦ |
|  | #2 System Hydraulic Pressure Indicator (F900C Only) | C | 1 | 0 | (M)(O) May be inoperative provided: HYDR #2 PUMP 2 caution light is verified operative, and Standby hydraulic pump is verified operative before engine start. | ¦ ¦ ¦ ¦ |

| 30 | ICE AND RAIN PROTECTION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Wing Anti-Ice System 30-10-00 | C | 1 | 0 | (M)(O) May be inoperative provided: Airplane is not operated in known or forecast icing conditions, and Wing anti-ice valve is verified in the closed position. |  |
|  | Engines and S-Duct Anti-Icing Systems 30-20-00, 30-20-10, 30-20-20 | B | 3 | 2 | (M)(O) May be inoperative provided: Airplane is not operated in known or forecast icing conditions, and Inoperative system is deactivated off. |  |
|  | Windshield Heating Systems 30-40-10 | C | 2 | 1 | (O) One may be inoperative provided: Windshield Defogging System is operative, and Airplane is not operated in known or forecast icing conditions. | ¦ ¦ |
|  | Side and Rear Flight Deck Windows Heating System 30-40-10 | C | 1 | 0 |  |  |
| 30 | ICE AND RAIN PROTECTION |  |  |  |  |  |
|  | Windshield Wipers 30-40-30 | C | 2 | 0 | (O) May be inoperative or missing provided the airplane is not operated in precipitation within 5 nautical miles of the airport of takeoff or intended landing. | ¦ |
|  |  | B | 2 | 1 | (M) One may be inoperative in non-rest position provided: Airplane is not operated in precipitation within five nautical miles of the airport of take-off or intended landing, Pilot flying is on the non-affected side, Airplane is operated with a maximum speed of 215 kt, and Associated breaker is pulled and collared. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  | Pitot Heating System (Pilot and Copilot) 30-30-00 | B | 2 | 1 | (O) One may be inoperative provided flight is conducted in day VMC flight conditions only. |  |
|  | Stand-by Pitot Probe Heating System 30-30-00 |  |  |  | Deleted, Rev. 4. |  |
|  | Static Port Heating Systems 30-30-00 | C | 2 | 1 | One may be inoperative provided the airplane is not operated in known or forecast icing conditions. |  |

| 30 | ICE AND RAIN PROTECTION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Angle of Attack Sensor Heating Systems 30-30-00 | C | 2 | 1 | (M) One may be inoperative provided: Airplane is not operated in known or forecast icing conditions, and Sensor asymmetry warning system (AUTOSLATS caution light) is verified operative. | ¦ ¦ |
|  | Pitot/Angle of Attack Systems Heat Indicator Lights (L. PITOT, R. PITOT, STBY PITOT, L. AOA, or R. AOA) 30-30-00 (Except F900C) | B | 5 | 4 | (O) One may be inoperative provided: Associated heater element is verified operative, and Airplane is not operated in known or forecast icing conditions. | ¦ ¦ |
|  | TAT Probe Heating System | B | 1 | 0 | (O) May be inoperative provided airplane is not operated in known or forecast icing conditions. |  |
|  | XFR Caution (Windshield) | C | 1 | 0 | (M) May be inoperative provided the temperature controller, controller transfer system and heating networks are verified operative. | ¦ |

| 30 | ICE AND RAIN PROTECTION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | ANTI-ICE Caution Light (F900C Only) | C | 1 | 0 | (O) May be inoperative provided Anti-Ice overhead panel amber lights is operative and are monitored during flight. | ¦ |
|  | PROBE HEATING Caution Light (F900C Only) | B | 1 | 0 | (M)(O) May be inoperative provided: All heaters are verified operative for each departure, and Airplane is not operated in known or forecast icing conditions. | ¦ |
|  | Windshield DE-FOG System | C | 2 | 0 | May be inoperative provided windshield heating systems are operative. | ¦ |
| *** | Brake Heating System (With SB F-900-32) | C | 1 | 0 | (M)(O) May be inoperative provided: Brake Heating Valves are secured in closed position, and Brake Heating System (wing brake position) is not used. |  |
| 17. *** | Ice Detection System (M3257) | C | 1 | 0 |  | ¦ ¦ |

| 31 | INDICATING/ RECORDING SYSTEMS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Flight Data Recorder (FDR) System | C | - | - | Any in excess of those required by FAR may be inoperative. | ¦ |
|  |  | A | - | 0 | May be inoperative provided: Cockpit Voice Recorder (CVR) is operative, Airplane is not dispatched from a designated airport as listed in the operator’s MEL unless: The FDR failure occurs after pushback but prior to take-off, or The FDR repairs was attempted but was not successful. In those cases where repair is attempted but not successful, the aircraft may be dispatched on a flight or series of flights until the next designated airport where repair must be accomplished prior to dispatch, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ |
|  | FDR Recording Parameters Required by FAR. | A | - | - | May be inoperative provided: Cockpit Voice Recorder (CVR) is operative, and Repairs are made within 20 consecutive calendar days. | ¦ ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 31 | INDICATING/ RECORDING SYSTEMS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Flight Data Recorder (FDR) System (Cont'd) |  |  |  |  |  |
|  | FDR Recording Parameters Not Required by FAR. | A | - | - | May be inoperative provided repairs are made prior to the completion of the next heavy maintenance visit. |  |
|  | For an operator other than a holder of an air carrier or commercial operator certificate. | C | - | 1 | Any in excess of those required by FAR may be inoperative. |  |
|  |  | A | - | 0 | May be inoperative provided repairs are made in accordance with FARs. |  |
|  | Clocks | C | - | 1 | One may be inoperative at either the pilot’s or copilot’s station. |  |
|  | TAS Indication | C | 2 | 0 |  |  |
|  | Data Acquisition Units (DAU) (F900C Only) |  |  |  |  |  |
|  | Channels | A | 4 | 3 | (M)(O) One channel may be inoperative provided: Engine oil temperature indication is verified operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ |

| 31 | INDICATING/ RECORDING SYSTEMS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | SAT TAT Indication | C | 2 | 1 |  |  |
| *** | Quick Access Recorder (QAR) (M3352) |  | 1 | 0 | May be inoperative provided the DFDR (item 31-1) is considered inoperative. |  |
|  | MF900 & F900B | C | 1 | 0 | May be inoperative provided no Digital Flight Data Recorder (DFDR) System or Flight Data Acquisition Unit (FDAU) fault is reported on the Data Entry Control Panel (DECP). |  |
|  | F900C Only | C | 1 | 0 | May be inoperative provided: No Digital Flight Data Recorder (DFDR), or Flight Data Acquisition Unit (FDAU) failure is displayed on the Data Entry Control Panel (DECP), and No DFDR fault is reported on the Engine Instrument Display (EID). |  |

| 32 | LANDING GEAR |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Landing Gear Selector Flashing Light 32-40-00 | C | 1 | 0 | (O) May be inoperative provided gear position indicators and warning voice are verified operative. | ¦ ¦ |
|  | “Gear” Voice Warning System 32-40-00 |  |  |  | Deleted Rev. 2. |  |
|  | Emergency/Park Brake 32-50-00 |  |  |  | Deleted Rev. 4. |  |
|  | System 2 “PARK BRAKE” Label (on EID) (F900C Only) | C | 1 | 0 | (O) May be inoperative provided the T/O CONFIG Warning system is verified operative. | ¦ |

| 32 | LANDING GEAR |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Antiskid System (Includes Annunciator Lights) |  |  |  |  |  |
|  | Dry Runways | C | 1 | 0 | (O) May be inoperative provided operations are conducted in accordance with the Performance Data of the AFM. |  |
|  | Wet Runways (No standing water present in area of takeoff ground roll, no snow, no icy runway conditions) | C | 1 | 0 | (O) May be inoperative provided: Operations are limited to utilization of PFCO or grooved runway, Thrust Reversers are operative, Acceptable Performance Data from an analysis of the Accelerate Stop Capability on Wet Runway Surfaces is developed and used, The cross wind component for both departure and arrival runways is forecast to be 15 knots or less, Acceptable Performance Data Report is referenced in the Operator’s Minimum Equipment List (MEL) by Report Name, Number, Revision Number, and Acceptance Data, Performance Data Report assumes that reverse thrust action is terminated at 60 knots, and Wet runway landing conditions are conducted in accordance with available landing performance data in the AFM. | ¦ |

| 32 | LANDING GEAR |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Nose Wheel Steering System | A | 1 | 0 | (M)(O) May be inoperative provided: Nose wheel is verified free to caster, Anti-Skid is operative, Airplane is not operated to or from an airport with standing water or contamination of the runways, Operations are limited to crosswinds of 10 KTS or less, and Repairs are made within two consecutive calendar days. | ¦ ¦ ¦ |
|  | BRAKE ACCU Caution Light (F900C Only) | C | 1 | 0 | (M) May be inoperative provided the park brake accumulator pressure is verified adequate once each flight day. |  |

| 33 | LIGHTS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Cockpit and Instrument Panel Lighting System 33-11-00 | C | - | - | Individual lights may be inoperative or missing provided remaining lights are: Not on emergency bus. Sufficient to clearly illuminate all required instruments, controls, and other devices for which it is provided, Positioned so that direct rays are shielded from flight crew member’s eyes, and Lighting configuration and intensity is acceptable to the flight crew, | ¦ ¦ ¦ |
|  | Passenger Cabin Normal Lighting System | C | - | - | Individual lights may be inoperative or missing provided: Adjacent light is operative, and Inoperative lights do not exceed 50 percent of the total installed. | ¦ ¦ ¦ |
|  | Passenger Notice System (“No Smoking/Fasten Seat Belt” Signs) 33-20-00 | C | - | - | (O) “No Smoking/Fasten Seat Belt” signs may be inoperative and the associated passenger seat(s) may occupied provided: An acceptable procedure is used to notify passengers when seat belts must be fastened or smoking is prohibited. | ¦ |
|  | Aft Compartment Lighting System 33-30-00 | C | 1 | 0 |  |  |

| 33 | LIGHTS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Baggage Compartment Lighting System (Interior/Exterior) 33-30-00 | C | 1 | 0 |  |  |
|  | Landing Lights 33-40-00 | C | 2 | 1 | One may be inoperative for night operations provided taxi light is operative. | ¦ ¦ |
|  |  | C | 2 | 0 | May be inoperative for day operations. |  |
| 1) | Pulse Light System (Aircraft with S/N ≥ 165 | C | 1 | 0 |  | ¦ ¦ |
|  | Taxi Light 33-40-00 | C | 1 | 0 | (O) May be inoperative for night operations provided both landing lights are operative. | ¦ |
|  |  | C | 1 | 0 | May be inoperative for day operations. |  |
|  | Position Lights System 33-40-00 |  |  |  |  |  |
|  | Without M2718 or SB F900-257 | C | 3 | 0 | May be inoperative for day operations. |  |
|  | With M2718 or SB F900-257 | C | 5 | 3 | May be inoperative provided at least one light is operative at each position. |  |
|  |  | C | 5 | 0 | May be inoperative for day operations. |  |

| 33 | LIGHTS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Anti-Collision Lights 33-40-00 | B | 2 | 0 | (O) May be inoperative provided strobe light system is installed and is operative. | ¦ |
|  | Wing Ice Detection Lights 33-40-00 | C | 2 | 0 | May be inoperative provided: a) Aircraft is not operated in known or forecast icing conditions at night, and Ground deicing procedures do not require their use. | ¦ ¦ ¦ ¦ ¦ ¦ |
|  |  | C | 2 | 1 | One may be inoperative provided: a) The left light is operative for single pilot operations, and b) Ground deicing procedures do not require their use. | ¦ ¦ ¦ ¦ ¦ |
|  | Exterior Emergency Lighting System 33-50-00 | C | 1 | 0 | May be inoperative for day operations. |  |
| *** | Logo Light System 33-40-00 | D | 1 | 0 |  |  |
|  | Strobe Light System 33-40-00 | C | 1 | 0 |  |  |
| *** | Pulse Light System | D | 1 | 0 |  |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Standby Pneumatic Altimeter (Except for Aircraft with Honeywell Primus Epic Control Display System for Retrofit) | C | - | 1 |  |  |
| 2. | Standby Attitude Indicator (Except for Aircraft with Honeywell Primus Epic Control Display System for Retrofit) | C | - | 0 | May be inoperative provided not required by FAR. |  |
|  |  | B | - | 0 | May be inoperative provided: Operations are conducted in Day VMC only, Operations are not conducted into know or forecast over-the-top conditions. |  |
| *** |  | D | - | - | Optional Heading or VOR/ILS information on Standby Attitude Indicator may be inoperative provided all corresponding normal systems are operative. |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 3. | Standby Magnetic Compass | B | 1 | 0 | (O) May be inoperative provided: Any combination of three gyro (or INS (IRU)) stabilized compass systems are operative. |  |
|  |  | B | 1 | 0 | (O) May be inoperative provided: Any combination of two gyro stabilized compass systems are operative, and Airplane is operated with dual independent navigation capability and under positive radar control by ATC during the en-route flight phase. |  |
|  |  | C | 1 | 0 | (O) May be inoperative for flights that are entirely within areas of magnetic unreliability provided at least two stabilized directional gyro systems are installed, are operative and used in conjunction with approved free gyro navigation techniques. |  |
| 1) | Compass Lighting | B | 1 | 0 | May be inoperative provided Non-Stabilized Magnetic (Standby) Compass (item 34-3) is considered inoperative. | ¦ ¦ ¦ |
|  |  | C | 1 | 0 | May be inoperative for daylight operations. | ¦ ¦ |
| 4. | VMO/MMO Aural Warning 34-15-00 | B | 2 | 1 | May be inoperative provided: Both Mach/airspeed indicators are operative, and VMO/MMO AFM limitations are observed. | ¦ ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 5. | Altitude Alerter/ Preselector System | A | 1 | 0 | (O) Except where enroute operations require their use, may be inoperative provided: Autopilot with altitude hold is operative, and altitude capture is operative. Enroute operations, ie RVSM, do not require its use. Airplane does not depart from a designated airport (as listed in the operator’s MEL) where repair or replacement can be made, and Repairs are made within three flight days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  |  | C | - | 1 |  | ¦ |
| 6. | VHF Navigation System (VOR/ILS) | C | - | - | As required by FAR. | ¦ |
| 7. | Distance Measuring Equipment (DME) 34-52-00 | D | - | - | Any in excess of those required by FAR may be inoperative. | ¦ |
| 8. | Weather Radar | C | - | - | As required by FAR. | ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required |  |  |  |  | ¦ |
|  | Class A |  |  |  |  | ¦ |
|  | GPWS | A | 1 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Repairs are made within two consecutive calendar days. | ¦ ¦ |
| (1) | Modes 1 Thru 4 | A | 4 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Repairs are made within two consecutive calendar days. | ¦ |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required (Cont'd) |  |  |  |  |  |
| 1) | Class A (Cont'd) |  |  |  |  |  |
| a) | GPWS (Cont'd) |  |  |  |  |  |
| (2) | Test Mode | A | 1 | 0 | May be inoperative provided: GPWS is considered inoperative, and Repairs are made within two consecutive calendar days. | ¦ |
|  | Glideslope Deviation(s) (Mode 5) | C | - | 1 |  |  |
|  |  | B | - | 0 |  |  |
|  | Advisory Callouts | B | - | 0 | (O) May be inoperative provided alternate procedures are established and used |  |
|  |  | C | - | 0 | (O) May be inoperative provided: Advisory callout not required by FAR, and Alternate procedures are established and used |  |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required (Cont'd) |  |  |  |  |  |
| 1) | Class A (Cont'd) |  |  |  |  |  |
| a) | GPWS (Cont'd) |  |  |  |  |  |
| *** | Windshear Mode (Reactive) | B | 1 | 0 | (O) May be inoperative provided Alternate procedures are established and used. | ¦ |
|  |  |  |  |  | NOTE: Operator's alternate procedures should include reviewing windshear avoidance and windshear recovery procedures. |  |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Windshear Detection and Avoidance System (Predictive) is operative. | ¦ ¦ |
| b) | Terrain System -Forward Looking Terrain Avoidance (FLTA) And Premature Descent Alert (PDA) Functions | B | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used | ¦ |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required (Cont'd) |  |  |  |  |  |
| 1) | Class A (Cont'd) |  |  |  |  |  |
| c) | Terrain Displays | C | - | 1 |  | ¦ |
|  |  | B | - | 0 |  |  |
| d) *** | Runway Awareness & Advisory System (RAAS) | C | 1 | 0 |  | ¦ |
|  | Class B |  |  |  |  |  |
|  | GPWS | A | 1 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Repairs are made within two consecutive calendar days. | ¦ |
|  | Modes 1 & 3 | A | 2 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Repairs are made within two consecutive consecutive days. | ¦ |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required (Cont'd) |  |  |  |  |  |
| 2) | Class B (Cont'd) |  |  |  |  |  |
| a) | GPWS (Cont'd) |  |  |  |  |  |
|  | Test Mode | A | 1 | 0 | May be inoperative provided: GPWS is considered inoperative, and Repairs are made within two consecutive calendar days. | ¦ |
| *** | Modes 2, 4 & 5 | C | 3 | 0 |  |  |
|  | Advisory Callouts | B | - | 0 | (O) May be inoperative provided alternate procedures are established and used |  |
|  |  | C | - | 0 | (O) May be inoperative provided: Advisory callout not required by FAR, and Alternate procedures are established and used |  |
|  | Windshear Mode (Reactive) | C | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 9. | TAWS Equipment Required (Cont'd) |  |  |  |  |  |
| 2) | Class B (Cont'd) |  |  |  |  |  |
| b) | Terrain System - Forward Looking Terrain Avoidance (FLTA) And Premature Descent Alert (PDA) Functions | B | 1 | 0 |  | ¦ |
| c) *** | Terrain Displays | C | - | 0 |  | ¦ |
| d) *** | Runway Awareness & Advisory System (RAAS) | C | 1 | 0 |  | ¦ |
|  | Class C |  |  |  |  | ¦ |
| *** | TAWS/GPWS | C | 1 | 0 | (O)May be inoperative provided alternate procedures are established and used. | ¦ |
|  |  |  |  |  | NOTE: Any mode that operative may be used. | ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 10. | Radio Altimeter System 34-42-00 | A | - | 0 | (M)(O) May be inoperative provided: Dispatch deviation for GPWS is observed, Approach minimums or operating procedures do not require its use, and Repairs are made within three consecutive calendar days. | ¦ ¦ |
| 11. | ATC Transponder and Automatic Altitude Reporting Systems | B | - | 0 | May be inoperative provided: Enroute operations do not require its use, and Prior to flight, approval is obtained from ATC facilities having jurisdiction over the planned route of flight. | ¦ |
|  |  | D | - | 1 | Any in excess of those required by FAR may be inoperative. |  |
| 12. | Radio Compass (ADF) System 34-53-00 | D | - | - | Any in excess of those required by FAR may be inoperative. | ¦ |
| 13. | VLF/OMEGA System 34-95-01 |  |  |  | Moved to item 34-45, Rev. 2. | ¦ |
| 14. *** | RMIs 34-23-00 | C | 2 | 1 |  | ¦ |
| 15. | Microwave Landing System (MLS) | C | - | - | As required by FAR. | ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 16. | Marker Beacon Receiver 34-32-00 | C | - | - | May be inoperative provided approach minimums do not require its use. | ¦ |
| 17. | Flight Management System (FMS) |  |  |  |  | ¦ |
|  | Without Lasertrack Installed | C | - | 1 | (O) Except where enroute/terminal operations require its use, one may be inoperative. |  |
| 2) *** | With Lasertrack Installed | C | - | 0 | (O) Except where enroute/terminal operations require its use, may be inoperative provided IRS is initialized by Lasertrack. |  |
| 3) | Navigation Databases | C | - | 0 | (O) May be out of currency provided: Current Aeronautical Charts are used to verify Navigation Fixes prior to dispatch, Procedures are established and used to verify status and suitability or Navigation Facilities used to define route of flight, and Approach Navigation Radios are manually tuned and identified. |  |
| 4) | Navigation Databases Data Loader | C | 1 | 0 | May be inoperative provided the time limits of the Navigation Databases are not exceed. | ¦ ¦ |
|  |  |  | 1 | 0 | May be inoperative provided the Navigation Databases (item 34-17.3) are considered out of currency. | ¦ ¦ ¦ |
| 34 | NAVIGATION |  |  |  |  |  |
| 18. | Attitude and Heading System (IRS) | D | - | 2 | Any in excess of the two required to independently power the Captain’s and First Officer’s system may be inoperative. | ¦ |
| 19. | EADI Annunciators/Displays (Except F900C and aircraft with Honeywell Primus Epic Control Display System for Retrofit) 34-01-00 |  |  |  |  | ¦ |
|  | Fast/Slow Indications | C | 2 | 0 | (M) May be inoperative provided indications are removed by an acceptable procedure. |  |
|  | Flight Director | C | 2 | 0 | May be inoperative provided approach minimums do not require their use. |  |
|  | Radio Altitude |  |  |  | Moved to ATA 34, Item 11. |  |
|  | Excess Deviation | C | 2 | 0 | May be inoperative provided approach minimums do not require their use. |  |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 19. | EADI Annunciators/Displays (Except F900C and aircraft with Honeywell Primus Epic Control Display System for Retrofit) 34-01-00 (Cont'd) |  |  |  |  |  |
|  | Speed Trend | C | 2 | 0 | (M) May be inoperative provided trend information is removed from display. |  |
|  | Mach Indication | C | 2 | 1 | (M) May be inoperative provided Mach information is removed from affected display. |  |
|  | Accel/Decel Indication | C | 2 | 0 | May be inoperative provided information is removed from affected display. |  |
|  | DH Indication | C | 2 | 0 | May be inoperative provided approach minimums do not require its use. |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 20. | EHSI Annunciations/Display (Except F900C and a/c with Honeywell Primus Epic Control Display System for Retrofit) 34-01-00 |  |  |  |  |  |
|  | Selected Heading | C | 2 | 1 |  |  |
|  | Selected Course | C | 2 | 1 | (O) May be inoperative provided navigation procedures do not require its use. |  |
|  | Bearing Pointers | C | 4 | 0 | May be inoperative provided associated RMI(s) is operative. | ¦ |
|  | DME Display | C | 2 | 0 | As required by FAR. |  |
|  | Groundspeed/Time To Go | C | 2 | 0 |  |  |
|  | ARC Mode | C | 2 | 0 | NOTE: Weather radar requirements must be considered if both ARC modes are inoperative. |  |
|  | Elapsed Time | C | 2 | 0 |  |  |
|  | Wind Speed Vector | C | 2 | 0 |  |  |
|  | True Air Speed (TAS) | C | 2 | 0 |  |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 21. | Symbol Generators 34-01-00 | C | - | 2 | One may be inoperative provided each pilot’s EFIS is driven by an independent symbol generator unit which is operative. | ¦ |
| 22. | Multifunction/Radar Display (MFD) (Except F900C) 34-90-01 | C | 1 | - | (O) May be inoperative provided: Procedures do not require its use, and When required, at least one radar display is operative. | ¦ |
| 23. | IRS NO AIR Caution Light 34-20-00 | C | - | - | (M) May be inoperative provided: Filter is checked for cleanliness, and Cooling fan is operative. | ¦ |
|  |  | C | - | - | May be inoperative provided IRS is considered inoperative. |  |
| 24. | Instrument Comparator System | C | - | 0 | May be inoperative provided approach minimums do not require its use. |  |
| 25. | Glide Slope Receiver | C | - | 0 | Moved to ATA 34, item 7, |  |
| 26. | LORAN System |  |  |  | Moved to item 34-45, Rev 2. |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 27. *** | Navigation Data Bank (NDB) | C | - | 0 | (O) May be out of currency provided: Current Aeronautical Charts are used to verify Navigation Fixes prior to dispatch, Procedures are established and used to verify status and suitability of Navigation Facilities used to define route of flight, and Approach Navigation Radios are manually tuned and identified. |  |
| 28. *** | Storm Scope/Lightning Sensor | C | - | 0 |  |  |
| 29. | Wind Shear Detection System | C | - | 0 | Move to ATA 34, Item 10, REV. 4. |  |
| 30. | NAV/COM Preselect Tuning Functions | C | - | - | May be inoperative provided direct tuning mode is installed and is operative for each associated unit. | ¦ |
| 31. | Voice Advisory/Flight Profile Advisory System | C | - | 0 | Moved to ATA 34, item 10, REV. 4. |  |
| 32. | NAV/COM/ADF/ Transponder Memory Channels | C | - | 0 | May be inoperative provided manual tuning is operative. | ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 33. | NAV/COM/ADF/ Transponder Digital Frequency Selector/LCD/LED Display Units | C | - | - | One or either pilot’s side may be inoperative provided: Manual remote tune or dual FMS/CDU capability is operative, and All digital Frequency Selector/LCD/LED display units on opposite pilot side is operative. | ¦ ¦¦ |
| 34. | IRS (Compass) Transfer System | C | - | 0 | May be inoperative provided the compass information remains in the normal (onside) selection. |  |
| 35. | Radar Auto Standby | C | 1 | 0 |  |  |
| 36. | Radar NAV Display | C | 1 | 0 | Moved to ATA 34, item 23, REV. 4. |  |
| 37. | Airborne Flight Information System | C | 1 | 0 | Moved to ATA 23. |  |
| 38. | Flight Director Systems | C | 2 | 0 | Moved to ATA 34, item 20, REV. 4. |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 39. | Traffic Alert and Collision Avoidance System |  |  |  |  |  |
|  | TCAS I | B | - | 0 | (M) May be inoperative provided: System is deactivated and secured, and Enroute or approach procedures do not require its use. |  |
|  |  | C | - | 0 | (M) May be inoperative provided: Not required by FAR, System is deactivated and secured, and Enroute or approach procedures do not require its use. |  |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 39. | Traffic Alert and Collision Avoidance System (Cont'd) |  |  |  |  |  |
|  | TCAS II | B | - | 0 | (M) May be inoperative provided: System is deactivated and secured, and Enroute or approach procedures do not require its use. |  |
|  |  | C | - | 0 | (M) May be inoperative provided: Not required by FAR, System is deactivated and secured, and Enroute or approach procedures do not require its use. |  |
| *** | Combined Traffic Alert (TA) and Resolution Advisory (RA) Dual Display System(s) | C | 2 | 1 | May be inoperative on the non-flying pilot’s side provided: TA and RA visual display is operative on the flying pilot’s side, and TA and RA audio function is operative on the flying pilot’s side. |  |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 39. | Traffic Alert and Collision Avoidance System (Cont'd) |  |  |  |  |  |
| 2) | TCAS II (Cont'd) |  |  |  |  |  |
| *** | Resolution Advisory (RA) Display System(s) | C | 2 | 1 | May be inoperative on the non-flying pilot side. |  |
|  |  | C | - | 0 | (O) May be inoperative provided: All Traffic Alert (TA) visual display and audio functions are operative TA Only Mode is selected by the crew, and Enroute or approach procedures do not require its use. |  |
|  | Traffic Alert (TA) Display System(s) | C | - | 0 | (O) May be inoperative provided: RA visual display and audio functions are operative, and Enroute or approach procedures do not require its use. |  |
|  | Audio Functions | B | 1 | 0 | May be inoperative provided enroute or approach procedures do not require use of TCAS. |  |
|  | Airspace Selection Function | C | - | 0 |  |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 40. | Standby Airspeed Indicator (Pneumatic) (Except for aircraft with Primus Epic Control Display System for Retrofit) | C | - | 1 |  |  |
| 41. *** | Global Positioning System (GPS) | C | - | - | Moved to ATA 34, item 45. |  |
| 42. | Vertical Speed Indicators | B | 2 | 1 | May be inoperative for day VMC. |  |
| 43. *** | Traffic Collision Avoidance Device (TCAD) | C | - | 0 | (M)(O) May be inoperative provided system is deactivated. |  |
| 44. *** | Long Range Navigation Systems (IRS, GPS, LORAN, Lasertrack, Etc.) | C | - | 0 | Except where enroute operations require its use, may be inoperative. | ¦ |
| 45. | Turn and Bank Indicators |  |  |  |  |  |
| *** | Rate or Turn Indicators | C | 2 | 1 |  |  |
|  |  | C | 2 | 0 | May be inoperative provided Standby Horizon indicator is operative. | ¦ |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 46. | Display Controller Panels (DCP) (F900C Only) | A | 2 | 1 | (M) Co-pilot position may be inoperative provided: Reversion Switch Panels (RSP) are operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ |
| 47. | Reversion Switch Panels (RSP) (F900C Only) | B | 2 | 1 | (O) One may be inoperative provided: Both Display Controller Panels (DSP) are operative, and No reversion is selected. |  |
| 48. | Fault Warning Computer (F900C Only) | B | 3 | 2 |  |  |
| 49. *** | Analog Airspeed Indicators | B | 2 | 0 | May be inoperative provided digital airspeed indicator on affected side is operative. | ¦ ¦ |
| 50. | Low Speed Cue (AOA) (F900C Only) | B | 2 | 1 | (O) One may be inoperative provided stall warning system is verified operative before each departure. | ¦ |
| 51. *** | Co-Pilot Emergency Power and Standby Instrument System |  |  |  |  |  |
|  | Air Speed Indicator | C | 1 | 0 | May be inoperative provided Captain’s standby airspeed is operative. |  |
|  | Altimeter | C | 1 | 0 | May be inoperative provided Captain’s standby altimeter is operative. |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 53. | Electronic Flight Instrument System (EFIS) Displays (F900C Only) | A | 5 | 4 | (M)(O) Copilot’s ND #2 may be inoperative provided: Reversion Switch Panels (RSP) are verified operative, Display Controller Panels (DCP) are operative, Symbol Generators (SG) are operative, Standby instruments are operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  |  |  |  |  | NOTE 1: In case of a second ND failure in flight, TCAS and EGPWS situation awareness are not available. |  |
|  |  |  |  |  | NOTE 2: In case of a second ND failure in flight, FMS ND flight plan depictions are not available; FMS flight plan legs displayed on FMS CDU’s remains functional including FD/AP coupling. |  |
| 54. | Honeywell Primus Epic Control Display System for Retrofit |  |  |  |  |  |
|  | Multifunction Display Controller | A | 2 | 1 | (M) One position may be inoperative provided: Reversion Switch Panels (RSP) are operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ |
|  |  |  |  |  | (Continued) |  |

| 34 | NAVIGATION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 54. | Honeywell Primus Epic Control Display System for Retrofit (Cont'd) |  |  |  |  |  |
|  | Reversion Switch Panels (RSP) | B | 2 | 1 | (O) One may be inoperative provided: Both Display Controller Panels (DSP) are operative, and No reversion is selected. | ¦ |
|  | Remote Instrument Controller | A | 2 | 1 | One Remote Instrument Controller may be inoperative provided the Altitude Alerter/ Preselector System (item 34-6) is operative. |  |
|  | Display Units (DU's) | A | 4 | 3 | (M)(O) One Inboard DU may be inoperative provided: Reversion Switch Panels (RSP) are verified operative, Display Controller Panels (DCP) are operative, Symbol Generators (SG) are operative, Standby instruments are operative, Multifunction display controllers are operative, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  |  |  |  |  | NOTE 1: In case of a second ND failure in flight, TCAS traffic information is not available. |  |
| 34 | NAVIGATION |  |  |  |  |  |
| 55. *** | Incidence Meter (M0051) | D | 1 | 0 | (M) May be inoperative provided associated circuit breakers are pulled and collared. | ¦ ¦ ¦ |

| 35 | OXYGEN |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Passenger Oxygen System 35-20-00 | C | 1 | - | (M)(O) Automatic presentation system may be inoperative provided: Manual deployment is operative, and Flight is conducted at or below FL250. | ¦ |
|  |  | C | 1 | - | (M)(O) One or more passenger service units may be inoperative without flight altitude restrictions provided: Associated seats are placarded and blocked to prevent occupancy, and Units are operative at all usable lavatory and flight attendant locations. | ¦ |
|  |  | C | 1 | 0 | (O) May be inoperative provided flight altitude remains at or below 10,000 feet. |  |
|  | Cargo Only Configuration | D | 1 | 0 |  |  |
|  | First Aid Oxygen 35-20-00 | C | - | - | As required by FAR. |  |
|  | Portable Oxygen System 35-30-00 | D | - | - | Any in excess of those required by FAR may be inoperative. |  |

| 36 | PNEUMATIC |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | HP1, Bleed Valve 36-00-00 | C | 1 | 0 | (O) May be inoperative closed provided: PRV2 and PRV3 Valves are operative, and Airplane is not operated in known or forecast icing conditions. | ¦ ¦ |
|  | Pressure Regulating Valves (PRV2 or PRV3) 36-00-00 | C | 2 | 1 | (M)(O) One may be inoperative closed provided: HP1 Valve is operative, and Airplane is not operated in known or forecast icing conditions. | ¦ ¦ |
|  | Isolation Valve 36-00-00 | C | 1 | 0 | (M)(O) May be inoperative closed provided airplane is not operated in known or forecast icing conditions. | ¦ |
|  | ISOL Rotary Switch | C | 1 | 0 | (M)(O) May be inoperative provided; Rotary switch remains in ISOL position, ISOLATION valve is verified in the closed position, and Airplane is not operated in known or forecast icing conditions. |  |
|  | ISOL Indicator Light (Overhead Panel) | C | 1 | 0 | (M)(O) May be inoperative provided: ISOL rotary switch remains in ISOL position, ISOLATION valve is verified in the closed position, and Airplane is not operated in known or forecast icing conditions. | ¦ |

| 36 | PNEUMATIC |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | APU BLEED AIR Valve | C | 1 | 0 | (M)(O) May be inoperative provided: Valve is verified in the closed position, and APU is used for electrical power only. |  |
|  | APU BLEED AIR Switch | C | 1 | 0 | (M)(O) May be inoperative provided: Switch remains in OFF position, APU BLEED AIR valve is verified in the closed position, and APU is used for electrical power only. |  |
|  | BLEED APU Caution Light | C | 1 | 0 | (M)(O) May be inoperative provided; APU BLEED AIR switch remains in OFF position, APU BLEED AIR valve is verified in the closed position, and APU is used for electrical power only. |  |

| 38 | WATER/WASTE |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1. | Rear Toilet Drain Valve | A | 1 | 0 | May be inoperative in closed position provided repairs are made before next toilet drain pan draining operation. | ¦ ¦ ¦ |
|  |  | A | 1 | 0 | (M)(O) May be inoperative in open position provided: Flight is conducted in a unpressurized configuration, Placard is installed on toilet door with "DO NOT USE TOILET" inscription, Draining port plug is verified to be in locked position, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
|  |  | A | 1 | 0 | (M)(O) May be inoperative provided: After manually operating the drain valve in closed position, it is checked there is no water leak at the drain valve, and Repairs are made within three consecutive calendar days. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ |

| 46 | NEW TECHNOLOGY |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| *** | Electronic Flight Bag Systems (EFBs) |  |  |  |  |  |
| *** | Class 3 EFBs | C | - | - | (O) May be inoperative provided: alternate procedures are established and used. |  |
|  |  |  |  |  | NOTE: Any function, program or document which is operative may be used. | ¦ |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |
| *** | Data Connectivity (Class 2) | C | - | - | (O) May be inoperative provided: alternate procedures are established and used. |  |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |
| *** | Power Connection (Class 1 and 2) | C | - | - | (O) May be inoperative provided: alternate procedures are established and used. |  |
|  |  | D | - | 0 | May be inoperative provided procedures do not require its use. |  |
|  |  |  |  |  | (Continued) |  |

| 46 | NEW TECHNOLOGY |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 1. *** | Electronic Flight Bag Systems (EFBs) (Cont'd) |  |  |  |  |  |
| *** | Mounting Device (Class 2) | C | - | 0 | (M)(O) May be inoperative provided: Associated EFB and hardware is secured by an alternate means or removed from the aircraft, and Alternate procedures are established and used. |  |
|  |  | D | - | 0 | (M) May be inoperative provided: Associated EFB and hardware is secured by an alternate means or removed from the aircraft, and procedures do not require its use. |  |

| 49 | AIRBORNE AUXILIARY POWER |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Auxiliary Power Unit (APU) | C | 1 | 0 | (O) May be inoperative provided procedures do not require its use. | ¦ ¦ |
|  |  | D | 1 | 0 | (M) May be inoperative provided APU is secured or removed. | ¦ |
|  | APU Computer | D | 1 | 0 | (M) May be inoperative provided APU (item 49-1) is considered inoperative and not used. | ¦ |
|  | N1 Indicator | C | 1 | 0 | (M)(O) May be inoperative provided APU computer and T5 indicator are operative. | ¦ |
|  | T5 Indicator | D | 1 | 0 | (M) May be inoperative provided APU (item 49-1) is considered inoperative and not used. | ¦ |
|  | APU OIL Pressure Indicator Light | C | 1 | 0 | (M) May be inoperative provided APU computer is operative. | ¦ |
|  |  | C | 1 | 0 | (M) May be inoperative provided APU oil level is verified once each flight day. | ¦ |
|  |  | D | 1 | 0 | (M) May be inoperative provided APU (item 49-1) is considered inoperative and not used. | ¦ |
|  | APU GEN Indicator Light | C | 1 | 0 | (O) May be inoperative provided Bus Power is verified operative. | ¦ |

| 52 | DOORS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Door Warning Lights (Bag Access, Cabin and Rear Doors) (Except F900C) 52-70-00 | C | 3 | 0 | (O) May be inoperative provided: It is verified before takeoff that each of the doors is closed and latched, A steady RED light must be deactivated, and A steady altitude warning (aural) feature is operative. | ¦ |
| 2 | Fueling Door Light 28-60-00 | C | 1 | 0 | (M)(O) May be inoperative provided: It is verified before takeoff that both fueling panel access doors are closed, Fuel tanks are properly pressurized, Pressure gauge in rear compartment and vent outlets in wing roots are verified with engines running, and Defueling valve inside the fuel compartment between frame 19 and 20 closed. | ¦ |
| 3. | DOORS* Warning Light System (F900C Only) | C | 1 | 0 | (M)(O) May be inoperative provided before each departure: Main entry door is verified closed and latched, External baggage compartment access door is verified closed and latched, and Internal baggage compartment access door is verified closed and latched and placarded “DO NOT OPEN IN FLIGHT”. |  |

| 52 | DOORS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 4. | SERVICE DOORS* Caution Light (F900C Only) | C | 1 | 0 | (O) May be inoperative provided before each departure it is visually verified: Rear compartment door is closed and latched, and Forward toilet service door is closed and latched. | ¦ |
| 5. *** | Electric Main Entrance Door Motor System (Post M2716) (F900C Only) | C | 1 | 0 | (M) May be inoperative provided Door is verified to manually open and close freely. |  |
| 6. | Baggage Compartment External Door Reducing Gear Motor (Except F900C) | C | 1 | 0 | (M) May be inoperative provided: Baggage compartment external door is closed manually, Baggage compartment external door is verified latched and locked before each flight, and REAR DOORS caution light is extinguished. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |
| 7 | Baggage Compartment External Door Reducing Gear Motor (F900C only) | C | 1 | 0 | (M) May be inoperative provided: Baggage compartment external door is closed manually, Baggage compartment external door is verified latched and locked before each flight, and DOORS* warning light is extinguished. | ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ ¦ |

| 73 | ENGINE FUEL & CONTROL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Fuel Flowmeters (Except F900C) 73-60-00 | B | 3 | 2 | (O) One may be inoperative provided: All remaining engine instruments are operative, ITT, N1 and N2 indicators are compared with those of the other engines, and Fuel Used counter and Total Fuel Used/GW meter are not used. | ¦ |
|  | Fuel Used Indicators (Except F900C) 73-60-00 | C | 3 | 2 | One may be inoperative provided the instantaneous fuel flow meter and associated fuel quantity indicators are operative. | ¦¦ |
|  | Engine Sync. System 73-20-00 |  |  |  | Deleted Rev. 2. |  |

| 73 | ENGINE FUEL & CONTROL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Engine Computer 73-20-00 |  |  |  |  |  |
|  | Automatic Mode | C | 3 | 2 | (M)(O) Automatic mode of one computer may be inoperative provided: Test to verify correct operation of the Overspeed protection system of the corresponding engine is performed as indicated in AFM annex 8 or annex 8A (as applicable), Airplane is operated in accordance with AFM annex 8 or annex 8A (as applicable), No other dispatched inoperative item or configuration deviation concerning power plant or performance exists, Airplane is not operated in known or forecast icing conditions, and Associated ENG Computer is operated in manual mode, and Thrust Reverser is deactivated and secured in the stowed position if ENG Computer 2 is operated in manual mode. | ¦ ¦ ¦¦¦¦ |
|  | CMPTR Caution Light | C | 3 | 2 | (O) One may be inoperative provided the associated Engine Computer (item 73-1) is considered inoperative in automatic mode. | ¦ |

| 74 | IGNITION |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Ignition Indicator Lights (Except F900C) 74-00-00 | C | 3 | 2 | (M) One may be inoperative provided automatic ignition system is verified operative. | ¦ ¦ ¦ |
|  | Automatic Ignition Systems (AOA Activated) 74-00-00 | C | 2 | 1 | (M)(O) One may be inoperative provided: Manual ignition is verified operative, and AIR START position is selected for all critical stages of flight (take-off, approach, turbulence). | ¦ ¦ |
|  | Ignition Selector Switches 74-00-00 | C | 3 | 2 | (O) One GRD START position may be inoperative provided: Associated engine AIR START position is operative, and Switch is returned to GRD START position after each ground start. | ¦ |
|  | IGN Labels (EID) (F900C Only) | C | 3 | 2 | (M) One may be inoperative provided ignition system is verified operative. | ¦ |
|  | Ignitor Plugs | C | 6 | 5 | One may be inoperative provided all Engine computers are operative in auto mode. | ¦ |

| 77 | ENGINE INDICATING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | N1 Indicators 77-10-00 |  |  |  |  |  |
|  | Digital Readout(s) | C | 3 | 0 |  |  |
|  | N2 Indicators 77-10-00 | C | 3 | 2 | (O) One may be inoperative provided N1 and Fuel Flow indicators for the associated engine are operative. | ¦ |
|  | ITT Indicators 77-20-00 |  |  |  |  |  |
|  | Digital Readout(s) | C | 3 | 0 |  |  |
|  | Fuel Flow Indications (F900C Only) | B | 3 | 2 | One may be inoperative provided all other engine indications and the associated fuel quantity indication system are operative. | ¦ |
|  | Fuel Used Indications (F900C Only) | C | 3 | 2 | One may be inoperative provided the associated Fuel Flow and Fuel Quantity Indications are operative. | ¦ |

| 77 | ENGINE INDICATING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | EID Indications (F900C Only) |  |  |  |  |  |
|  | N1 Indications | C | 3 | 2 | (O) One may be inoperative provided: N2, ITT and fuel flow indications are operative, Associated DEEC is operative in AUTO mode, and Both DAUs are operative. | ¦ ¦ ¦ |
|  | ITT Indications | C | 3 | 2 | (O) One may be inoperative provided: N1, N2 and fuel flow indications are operative, Associated DEEC is operative in AUTO mode, and Both DAUs are operative. | ¦ ¦ ¦ |
|  | N2 Indications | C | 3 | 2 | (O) One may be inoperative provided: Both DAUs are operative, N1, ITT and fuel flow indications are operative, Associated DEEC is operative in AUTO mode, and During starting, the power lever is moved to idle at the first indication of N1. | ¦ ¦ ¦ |
|  | Oil Pressure Indications | C | 3 | 2 | One may be inoperative provided the associated OIL low pressure warning light and oil temperature indication are operative. | ¦ ¦ |

| 78 | ENGINE EXHAUST |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | DEPLOYED Indicator Light (Except F900C) 78-00-00 | C | 1 | 0 | May be inoperative provided Thrust Reverser system (item 78-2) is considered inoperative. | ¦¦ ¦ |
|  | Thrust Reverser System 78-00-00 | C | 1 | 0 | (M)(O) May be inoperative provided: No damage to the thrust reverser system exists which would adversely affect operation of the airplane, Reverser is deactivated and secured in the stowed position by use of the two safety pins, All braking systems are operative, and A reverser unlock light that remains illuminated must be deactivated. | ¦¦ |
|  | Transit Indicator Light (Except F900C) | C | 1 | 0 | May be inoperative provided Thrust Reverser system (item 78-2) is considered inoperative. | ¦¦ ¦ |

| 78 | ENGINE EXHAUST |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | REV UNLOCK Warning Light (Except F900C) | C | 1 | 0 | May be inoperative provided thrust reverser system (item 78-2) is considered inoperative. | ¦¦ |
|  | DEPLOY Label (EID) (F900C Only) | C | 1 | 0 | May be inoperative provided Thrust Reverser system (item 78-2) is considered inoperative. | ¦¦ ¦ |
|  | TRANS Label (EID) (F900C Only) | C | 1 | 0 | May be inoperative provided Thrust Reverser system (item 78-2) is considered inoperative. | ¦¦ ¦ |
|  | THRUST REVERSER Warning Light | C | 1 | 0 | May be inoperative provided Thrust Reverser system (item 78-2) is considered inoperative. | ¦¦ ¦ |

| 79 | ENGINE OIL |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | OIL 1, 2, and 3 Warning Lights (Oil Pressure and Chip Detectors) 79-30-00 | C | 3 | 2 | (M)(O) One may be inoperative provided; It is verified that the malfunction is in the warning system, Associated magnetic plugs are checked for evidence of metal chips or clogging before the first flight of each day, Oil pressure and oil temperature indicators are monitored closely during flight, and A steady light must be deactivated. |  |
|  | Oil Quantity Indicator 79-40-00 | C | 1 | 0 | (M) May be inoperative provided engine oil levels are verified adequate before each departure. | ¦ |

| 80 | STARTING |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Automatic Starter Cutout Feature 80-00-00 | C | 3 | 2 | (O) One may be inoperative provided starter is disengaged manually at 50% N2 during engine start. |  |