MEL-GC59.doc
       PL-84

       SUBJECT: RVSM OPERATIONS


 ------------------------------ MMEL GLOBAL CHANGE-----------------------------

	PL-84 is designated as GC-59

             This GC is an approved addendum to all existing MMEL
             documents.  The operator may seek use of the specific relief
             contained in the policy letter by revising the Minimum
             Equipment List (MEL).  In doing so, the sample proviso stating
             the relief in the policy letter must be copied verbatim in the
             operator's MEL.  Approval of the revised MEL is gained
             utilizing established procedure, through the assigned
             Principal Operations Inspector (POI).

 ===========================================================================

    PL-84, Revision 1                          August 15, 1997

    SUBJECT:    Master Minimum Equipment List (MMEL) for
                Reduced Vertical Separation Minimum (RVSM)
                Operations

    MMEL CODE: 34 (NAVIGATION)

    REFERENCE: Former Policy Letter 84, dated July 18, 1996,
	               signed by David R. Harrington.

    FROM:      Manager, Air Transportation Division, AFS-200

    TO:        All Region Flight Standards Division Managers
               All Aircraft Evaluation Group Managers

    REPLY TO
    ATTN OF:   Manager, Program Management Branch, AFS-260

    PURPOSE:
    This policy letter provides MMEL requirements for RVSM
    Operations.

    DISCUSSION:
    This policy was formerly contained in Policy Letter 84,
    dated July 18, 1996.  Revision 1 contains reformatting, but
    the policy is unchanged.

    Since the 1950's, 1,000 foot vertical separation has been
    applied up to Flight Level (FL) 290 and 2,000 foot vertical
    separation has been applied above FL 290.  The RVSM program
    enables 1,000 foot vertical separation to be applied between
    FL 290 and FL 410 based on FAA approval of operator's aircraft
    altitude-keeping capability, continuing airworthiness and
    operations programs.  The following systems are required to
    be installed on aircraft to be approved to conduct RVSM
    operations:  two (2) independent altitude measurement
    systems (as defined in FAA Interim Guidance 91-RVSM,
    paragraph 8a), one (1) secondary surveillance radar (SSR)
    reporting transponder, one (1) altitude alerting system, and
    one (1) automatic altitude control system.  In addition,
    there is an operational requirement for certain systems to
    be operating at entry into airspace where RVSM is applied.
    They are: two (2) independent altitude measurement systems,
    one (1) altitude alert system, and one automatic altitude
    control system.

    POLICY:
    The FOPB has determined that the MMEL's for aircraft
    approved to operate in RVSM airspace should reflect dispatch
    requirements for certain aircraft systems that provide
    altitude-keeping capability.  Accordingly, the following
    requirements must be addressed:

    Two (2) independent altitude measurement systems comprised
    of the following elements:

         -Cross coupled static source system provided with ice
         protection if located in areas subject to ice accretion

         -Equipment for measuring static pressure sensed by the
         static source, converting it to pressure altitude, and
         displaying pressure altitude to the flightcrew

         -Equipment for providing a digitally coded signal
         corresponding to the displayed pressure altitude, for
         automatic altitude reporting purposes

         -Static source error correction (SSEC), if required to
         meet RVSM altimetry system error requirements

         -Equipment to provide reference signals for automatic
         altitude control and alerting systems

    One (1) SSR altitude reporting transponder

    One (1) altitude alert system

    One (1) automatic altitude control system capable of
    automatically controlling the aircraft to a referenced
    pressure altitude

    Above guidance and generic equipment requirements reflect
    the operational environment as it currently exists, and are
    applicable to all aircraft dispatching into airspace where
    RVSM is applied.  FOEB chairmen may need to assess specific
    aircraft and systems independently where unique design
    features and/or service history identify the need to address
    "other" unspecified equipment requirements, e.g.,
    operational limitations on the B-747 classic that may
    mandate the use of autothrottles to preclude unacceptable
    mach excursions which can induce altimetry system errors.

    EXAMPLE:

    Altitude Alerting   A    -    0    	(0)Except where enroute
    System                            	operations require
                                          		its use, may be
	                                          inoperative provided:
                                          
				a) Autopilot with
               	                              altitude hold
                             	                is operative, and

	                                          b) Repairs are made
               	                              within three flight
                             	                days.