TC4 ER-2 Science Flight: July 29, 2007

Flight Report

Flight Scientists: P. Newman, S. Platnick

Sortie: 07-9024

Pilot:	Denis Steele

Takeoff (SJO):	1142 UTC (5:42 AM local)

Landing (SJO):	1827 UTC (12:27 PM local)

Duration: 6:40

Objectives:

• To investigate marine stratus microphysical and radiative properties near the equator in support of Terra/CloudSat.

• Underfly Terra with ER-2/DC-8, ER-2 aligned with track, for radiometric and retrieval comparisons with MODIS.

• To investigate volcanic SO2 emissions in support of OMI

Satellite Coordination:

The Terra overpass occurs at approximately 1557 UTC (a heading of 192.05̊). The image below shows the Terra overpass as the blue (courtesy, Douglas Spangenberg, LaRC). The Aqua, Cloudsat/CALIPSO, Aura overpasses occur 1853, 1854, and 1909 UTC respectively near the equator near Ecuador.  The TRMM overpass is also close to Costa Rica, but occurs prior to the ER-2 launch at 1142 UTC.

Flight Plan Summary (see RTMM maps):

Takeoff was at 1142 UTC.  The ER-2 initially flies S over the Pacific towards a region where  marine stratus is expected (waypoint 3 on the map) and along the jetway available to the DC-8.  Visible imagery showed the Sc desk to be farther south along the jetway than the original plan.  ER-2 flew tracks from Amero to Valem, Valem to 83W (along same line) and back to Valem, Valem to 82.5W (same line), then turned to a 12° heading on the Terra track. Following the Terra overpass, the ER-2 return to MROC.

blue line: ER-2 flight track

cyan line: ER-2, original waypoints

red line: DC-8 flight track

Terra track: gray line

GOES VIS image

MODIS Terra QuickLook Imagery

White clouds indicate liquid water, strong coral/redish color clouds indicate ice, slightly redish clouds might indicate larger water droplets and/or ice particles.

ER-2 Science Instrument Payload and Status:

| Instrument | Status | Notes |
| --- | --- | --- |
| CPL Cloud Physics Lidar | G |  |
| CRS Cloud Radar System | G |  |
| EDOP ER-2 Doppler Radar | G |  |
| AMPR Advanced Microwave Precipitation Radiometer | G |  |
| CoSSIR Compact Scanning Sub-mm wave Imaging Radiometer | G | 380 GHz channels disconnected, some intermittent noise on one of the 640 GHz dual-pol channels |
| MASTER MODIS/ASTER Airborne Simulator | G | 7 µm channel dead |
| S-HIS Scanning High Resolution Interferometer | G |  |
| IR Radiometer Broadband flux radiometer (nadir & zenith) | G |  |
| SSFR Solar Spectral Flux Radiometer (nadir & zenith) | G |  |
| MVIS video camera | G |  |
| MTP Microwave Temperature Profiler | G |  |

## G = good; P = partial data collected; F = failure, no data